GENERIC FIDO DRIVER INTERFACE
	Updatewd 29 Jan 86
	T. Jennings 12 July 1985

	FIDO_GEN.EXE is a "generic" Fido for otherwise unsupported
	machines. It will not work until you write a device driver
	or terminate-stay-resident program to provide the following
	functions. The format of this driver will remain independent
	of the Fido version; once written it will work with all
	future Fido versions.

	All IO is done through an IBM PC like Interrupt 14 hex. Many
	calls are directly compatible, but you will have to extend
	it to support the added features. Note that FIDO_GEN will
	NOT run on an IBM PC as is.

	The interface is very consistent; AX and DX are used for
	all functions.

	It is possible to use an entirely polled IO system for
	Fido; Fido does "typeahead" in the higher level software,
	so everything but ASCII Upload will work fine polled, and
	even that may work OK on most machines. Interrupt character
	input is very desireable. Interrupt output is not needed
	at all, unless you wish to run under a multi-tasker such
	as Multilink.

	Please note that I cannot help you write drivers, nor will
	I help you debug them. You are on your own! Extensive
	assembly language experience is needed, and a good degree
	of familiarity with your hardware, so please do not
	underestimate the difficulty of this task.

	Assumptions here are that you can run MSDOS or PCDOS
	version 2 or 3; Fido does not support ANY other operating
	system.

	Either a device driver or a terminate-stay-resident type
	structure for your driver set is reccomended. Device drivers
	obviously go in your CONFIG.SYS on the boot disk; term stay
	res programs should be put in AUTOEXEC.BAT, to be run only 
	ONCE. Every time you run a term stay res, it consumes more
	memory, unless special provision is made in your program
	to detect whether it was previously loaded. Keep in mind that
	in normal operation, Fido is run more than once, ie. you may
	Control-C Fido to copy files, run in Test Mode, etc.

	On the subject of Test Mode, an important note: Fido does not
	make ANY HARDWARE DEPENDENT CALLS in /T test mode. This means
	that ANY version of Fido will work on ANY other machine in
	test mode. You must run it without /T specified in order to
	get it to use your drivers. Test mode is useless as a test of
	your drivers. It means nothing.

	It is probably a good idea to test each and every single 
	function before attempting to use Fido with your driver set;
	I repeat, I cannot help you with your drivers in any way.


	The following is the function call used internally to Fido
	to access the drivers you write. This is provided for your
	information only. 

	val= int14(ah,al,dx);

	int val;		/* integer return value */

	int ah;			/* command byte, 0 - N */
	int al;			/* argument */
	int dx;			/* I/O device, ie. channel */


	For all calls, DX is the IO device from the /1, /2, etc
	command line switch. This can be used or ignored as desired.
	It will be valid for all calls at all times.

	AH is the command type; 0 - 3 are very similar to IBM PC
	INT 14 calls. 4 and up are extentions to support further
	functions. (Note that the IBM version of Fido does NOT
	use INT 14.)

	For all calls, your driver MUST preserve all segment
	registers, plus BP and SP. All other registers can be
	modified. Interrupts should be left ENABLED after 
	returning. There is adequate stack space to do almost
	anything you need; there should be at least a kilobyte
	of stack space.


AH = 0:	Set baud rate

	This command is almost identical to the IBM PC equivalent
	call. The upper three bits indicate the baud rate; the
	lower ones indicate parity (always none) and stop bits 
	(always 1). You can always assume that NO PARITY and ONE
	STOP BIT are used throughout Fido.

		Baud	Value
		 300	043h
		1200	083h
		2400	0a3h
		9600	0e3h

	The sample driver strips off all but the upper three
	bits. You can do this in your driver also, but Fido
	will always pass the byte patterns as defined above.



AH = 1:	Write a character to the serial port

	Output the character in AL to the serial port. Wait for 
	output ready as necessary.



AH = 2:	Read a character from the serial port

	Return one character from the serial port in AL. Wait for 
	one if necessary.


AH = 3:	Return status

	This command returns various status bits back to Fido in AH
	and AL. There are three status bits you must return in this
	call; two have predetermined values, and the other you can
	assign to any other bit, as it is tested with the command
	line /V value. (See below) These are bit patterns, not
	numeric values; you can (and will) have more than one bit
	set at a time.

	AH:	20h		TBE	Transmit Buffer Empty
		01h		RDA	Receive Data Available

	TBE means the transmitter is ready to accept a character.
	RDA means there is a character from the modem waiting.

	The other bit the the Carrier Detect (CD) bit. This can be
	returned in either AH or AL. The command line switch /V
	defines the mask bit used to test this port. For example,

		128/V

	Defines the CD mask bit to be 128, or 0080h. This is ANDed
	with the value returned by the STATUS call, and if the 
	result is true (bit is set) then Fido assumes the modem is
	connected.

	For making this test, Fido treats AH and AL as a 16 bit
	integer, in the usual fashion: AH is the most signifigant
	and AL the least.  Therefore, 32768/V tests the MSB in
	AH, and 1/V test the LSB in AL. You can't use 8192/V 
	or 256/V, since those are TBE and RDA, respectively.

	Unused bits may take on any value as you see fit.



AH = 4:	One time initialization

	Perform any necessary one time initialization here. Fido 
	will make this call only ONCE before any IO is done to 
	the serial port. 

	After this function is called, DTR should be high. This
	is important, as Fido will not raise DTR explicitly for
	the first call.


AH = 5:	One time UN initialization

	Do one time un-initialization; this is called ONCE, just
	before Fido exits to DOS. Remove any interrupt structures
	or whatever were installed by AH = 0. NO OTHER call will be
	mode to the IO drivers after this call.

	It is general practice when exiting Fido to leave the 
	DTR line low so that the modem is disabled when Fido 
	is not running. Fido lowers DTR before calling this
	function and exiting, but you might want to make sure that
	this function does not raise it again inadvertantly.



AH = 6:	Raise/Lower Data Terminal Ready

	This function controls the state of the DTR line output to
	the modem, usually on Pin 20. AL = 0 means lower DTR; 
	AL = 1 means raise it true. True enables the modem; false
	disables it.

	No other functions in your drivers should change the state
	of the DTR line, except AH = 4 and AH = 5. See the note
	in AH = 5 about exiting Fido.

AH = 7:	Return Timer Tick parameters

	This function is used to tell Fido about the timer tick
	to be used for marking time. This is an extremely critical
	function, and luckily, fairly simple. The hard part will
	be getting the information.

	AH = 4 is called before this call, so you can use that to
	start any timer running if necessary; if you do, use AH = 5
	to remove it.

	AH = 7 returns three numbers:

		AL = 	Timer Tick Interrupt Number	0 - 255
		AH =	Ticks Per Second
		DX = 	Timer Tick Rate, Milliseconds

	Note that this function merely returns fixed values to
	Fido; Fido will do all the work of operating the timer
	interrupt, and pass control to the original interrupt
	service routine. The following information is given
	as background only.

	Fido's timer tick is done very simply by inserting itself
	in series with the interrupt numbe you specify in AL. When
	Fido has done its timer counter incrementing, it chains
	via a long jump to the original interrupt vector, thereby
	preserving the original interrupt vector. Fido does not 
	defer the interrupt by more than a few hundred microseconds,
	so there are no problems with interrupt acknowledges
	regardless of the interrupt system type. The DEC Rainbow,
	for instance, has a low tolerance for interrupt deferrment;
	it has hardware to check for interrupt loss, and the screen
	refresh depends on a repeatable clock; Fido's timer tick
	method presents no problem.

	The reason for both ticks per second and milliseconds per
	tick is that frequently the timer is at an inconvenient rate;
	the IBM PC for example is approx. 55 mS, which does not make
	for easy counting. (Note that if you work it out, the
	sample drive as supplied is very inaccurate. Oh well.)

	Fido counts both milliseconds and hours minutes seconds; these
	two parameters let you choose values that will result in the 
	highest accuracy. It is not necessary to have extreme accuracy.

	Fido does its millisecond counting by adding the number you
	return in DX to a 32 bit counter in memory; it is used for
	XMODEM, etc timeouts, and does not need to be highly accurate;
	10% is fine, but try for the most accurate possible.

	Hour minute second counting is done with the number your return
	in AH; every (AH) timer tick Fido increments the seconds counter.
	This value should be as accurate as is possible, since this is
	what controls each users time limit on the system.