To assist third-party programmers, this file documents how TriBBS's
TTPROT.EXE protocol driver is called.

IMPORTANT: TTPROT.EXE can only be used with either TriBBS or a related
TriBBS utility or door.  Any other use is a violation of United States
Copyright laws.

TTPROT.EXE is called as follows:

TTPROT port baud rts/cts protocol filename

Where:

port            is the serial port to be used.  The valid range is 1 to 4.

baud            is the baud rate to be used.  The valid range is 300 to
                57600.

rts/cts         indicates whether or not to use RTS/CTS hardware flow
                control.  Y if RTS/CTS flow control is to be used.
                Otherwise, N if RTS/CTS flow control isn't to be used.

protocol        XU      to send a file using Xmodem
                1U      to send a file using Xmodem-1K
                YU      to send one or more files using Ymodem
                GU      to send one or more files using Ymodem-G
                ZU      to send one or more files using Zmodem
                XD      to receive a file using Xmodem
                1D      to receive a file using Xmodem-1K
                YD      to receive one or more files using Ymodem
                GD      to receive one or more files using Ymodem-G
                ZD      to receive one or more files using Zmodem

filename        is the name of a the file to be sent or received.  With a
                batch upload or download, the filename can be preceded with
                an @ to indicate that the file is an ASCII text file that 
                lists the name of the files to be sent or received.