X00 Utility (XU)

                         Copyright 1990,  by Raymond L. Gwinn
                                 12469 Cavalier Drive
                              Woodbridge, Virginia 22192

                                 All Rights Reserved








                                                                          i















                                     INTRODUCTION

          XU  is  a   utility  program  intended  to  support   the  Serial
          Input/Output (SIO) device driver X00.

          XU  combines  several individual  utilities that  were previously
          distributed  with X00.  XU  gives the user  the ability to change
          most of the X00 command line  options that were specified in  the
          CONFIG.SYS file,  or when  X00 was  installed as  a TSR.   Future
          versions of XU will provide additional functions such as port/IRQ
          re-mapping.

          Use this program at your  own risk.  No warranties  or guarantees
          are given or implied.

          You  may  enter as  many  commands as  you  wish in  a  single XU
          execution.   The  only limitation  is the  length of  DOS command
          lines.

          All references in this manual to the 16550A apply to the 16550AF,
          16550AFN,  16C551 aka  16551,  and 16C552  aka  16552.   See  the
          appendix  in X00USER.DOC  for a  discussion on  the  various chip
          types.








                                                                         ii

                                  TABLE OF CONTENTS


          INTRODUCTION  . . . . . . . . . . . . . . . . . . . . . . . .   i

          BOOT  . . . . . . . . . . . . . . . . . . . . . . . . . . . .   1

          CAPTURE . . . . . . . . . . . . . . . . . . . . . . . . . . .   2

          FIFO  . . . . . . . . . . . . . . . . . . . . . . . . . . . .   3

          DTR . . . . . . . . . . . . . . . . . . . . . . . . . . . . .   4

          DV  . . . . . . . . . . . . . . . . . . . . . . . . . . . . .   5

          LOCK  . . . . . . . . . . . . . . . . . . . . . . . . . . . .   6
               Valid baud rates . . . . . . . . . . . . . . . . . . . .   6
               Valid parity . . . . . . . . . . . . . . . . . . . . . .   6
               data bits per character  . . . . . . . . . . . . . . . .   6
               stop bits  . . . . . . . . . . . . . . . . . . . . . . .   7

          NASTY . . . . . . . . . . . . . . . . . . . . . . . . . . . .   8

          PORT  . . . . . . . . . . . . . . . . . . . . . . . . . . . .   9

          SET . . . . . . . . . . . . . . . . . . . . . . . . . . . .    10

          STATUS or S . . . . . . . . . . . . . . . . . . . . . . . .    11

          USEBIOS . . . . . . . . . . . . . . . . . . . . . . . . . .    12

          WATCHCD . . . . . . . . . . . . . . . . . . . . . . . . . .    13








                                                                          1



















                                         BOOT

          This function should cause a warm boot.  The BOOT functions works
          in  most environments, including  DESQview on most  systems.  The
          BOOT function will not work on some 386 systems running protected
          mode software.

          An example of the usage is:

                                       XU BOOT

          One appropriate place  to use this  function is  in a batch  file
          that  is controlling  an  automated system  like  a  BBS.   If  a
          condition is detected that is considered by the user to be severe
          enough, the BOOT command can be issued to restart the system.








                                                                          2




                                       CAPTURE

          X00 is a  FOSSIL serial I/O device driver.   A FOSSIL is normally
          entered (called)  using an 80x86  INT 14h.   This means  that the
          vector  (pointer)  for interrupt  14h must  point  to X00.   Some
          programs will alter the  interrupt 14h vector (pointer).   If the
          INT 14h vector is changed, X00 may not function properly.

          Application  programmers please note that the  INT 14h vector can
          be  avoided  by using  the HLLAPI  routines  included in  the X00
          distribution file.

          The  CAPTURE function is provided to instruct X00 to take control
          of, or to release the INT 14h vector.

          Examples of usage are:

                                   XU CAPTURE:ON

                                   XU CAPTURE:OFF

                                   XU CAPTURE

          CAPTURE:ON  means  that  X00  will take/re-take  the  vector  for
          interrupt  14h.   That  is,  X00  will make  the  INT 14h  vector
          (pointer) point to the X00 function dispatcher.  The value of the
          old INT  14h vector  is saved.   X00  does not save  the INT  14h
          vector if it already points to X00.

          CAPTURE:OFF  means that  X00 is  to release  the INT  14h vector.
          When X00 is initialized,  or when a CAPTURE:ON is issued, the INT
          14h  vector  is saved.   The  CAPTURE:OFF  function tells  X00 to
          restore the  last INT  14h vector  that it saved.   It  should be
          noted  that the  last  INT  14h  vector that  X00  saved  is  not
          necessary the correct vector.  An explanation is beyond the scope
          of  this  document.    CAPTURE:OFF  will  also  disable the  BIOS
          emulator.   CAPTURE:OFF  does  not deactivate  any FOSSIL  active
          ports.

          If  you  are having  problems with  a  FOSSIL aware  program, try
          CAPTURE:ON  just  prior to  executing the  program.   If  you are
          having problems  with a communications program that is not FOSSIL
          aware, try CAPTURE:OFF just prior to executing the program.

          This function takes effect immediately upon execution.








                                                                          3






                                         FIFO

          This function is  provided to give the  user control of FIFOs  in
          the  SIO  chip.   At  this  time the  only  FIFOed  chip that  is
          supported is the 16550A  and later versions.  Other  FIFOed chips
          are being worked on and will be supported in the future.

          Some early PS/2  systems had 16550 (non A) chips  installed.  X00
          will identify the non A versions (and tell you that you have one)
          but it will  not use the FIFOs.   The FIFOs of the  16550 (non A)
          are not reliable.

          If  the SIO  chip is  not a  FIFOed device,  this command  has no
          effect.

          Examples of usage are:

                                   XU FIFO:15

                                   XU FIFO:8

                                   XU FIFO:OFF

          X00  defaults to  8 for a  16550A.   If an invalid  FIFO value is
          specified, the default value will be substituted.

          When  a number  parameter is  given, it  specifies the  number of
          characters that can be loaded  into the transmit FIFO of  the SIO
          chip.  The receive FIFO is always set at the maximum.

          The  FIFO:OFF  command disables  both  the  receive and  transmit
          FIFOs.

          I have seen problems with the 16550A when the  FIFO is set to the
          maximum of 16.   The problems go away with the FIFO  value set to
          15.  If you are seeing an occasional error during file transfers,
          try lowering the FIFO value.

          This  command will  not take  effect for  ports that  are already
          FOSSIL  active.  Once the port is reactivated, the specified FIFO
          parameters will take effect.








                                                                          4



















                                         DTR

          This function is provided to turn on  and or off DTR for a  given
          port.

          Examples of usage are:

                                   XU DTR:0:ON
                                   XU DTR:0:OFF
                                   XU DTR:0:OFF DTR:0:ON

          In the third  example note that DTR is first  turned off and then
          back  on in the  same execution of  XU.  Some  modems may require
          that  DTR  be  off  for  a  given  period  of  time  before being
          recognized as  a valid off.  If this  is the case for your modem,
          turning DTR off, then on in the same execution may not work.








                                                                          5










                                          DV

          This  function  is provided  to  support  software running  under
          DESQview.  Normally DESQview will provide a  full time slice to a
          program whether it is doing anything productive or not.  However,
          DESQview provides a method,  called PAUSE, that allows  a program
          to end its current time slice.

          Examples of usage are:

                                   XU DV:ON

                                   XU DV:OFF

          When the DV option is enabled (DV:ON) X00 will make a guess as to
          whether  the program is doing anything  productive.  For example,
          if the program is simply waiting for the next character and there
          is no character  available, then  time can be  made available  to
          another program running under DESQview.   DV:OFF will disable the
          releasing of time to other programs.

          As stated  above, X00  tries  to guess  if the  program is  doing
          something productive.  In some cases for some programs, the guess
          is  going to be wrong.  That  is, X00 will incorrectly assume the
          program is, in effect, idle when it  is not.  In such cases, your
          application program may  slow down considerably.  The  only thing
          you can do to correct this is to issue a DV:OFF command.

          As time goes on, I believe X00's guesses will get better.  So, if
          you  have problems with DV:ON, try it  again with new releases of
          X00.

          This function takes effect immediately upon execution.








                                                                          6




                                         LOCK

          Some modems allow  or require a fixed baud rate from the computer
          to the modem.  This function is intended to support those modems.
          Note  that  LOCK does  not set  the  specified parameters  in the
          hardware  when   issued.    See  the  following  SET  command  to
          immediately set the operational characteristics  of a port.  This
          function locks  the operational  characteristics only for  FOSSIL
          aware programs  and programs using  the BIOS emulator.   Programs
          that  perform direct I/O to  the serial I/O  registers can change
          the operational characteristics.

          Examples of usage are:

                                   XU LOCK:0:19200

                                   XU LOCK:0:19200:8N1

                                   XU LOCK:0:OFF

                                   XU LOCK:0:7E1

                                   XU LOCK:0:OFF:7S1

          The command  LOCK:0:19200 will cause  the computer to  modem baud
          rate (for logical port 0, usually COM1) to be 19200  baud even if
          the application program requests that the baud rate be changed to
          another value.  RTS/CTS  hardware handshaking is implied (forced)
          when a locked baud rate is specified.

          Valid baud rates for  locking are: 75, 110, 134.5, 150, 300, 600,
          1200,  1800, 2000,  2400, 3600, 4800,  7200, 9600,  19200, 28800,
          38400, 57600, and 115200.

          Valid  parity etc settings can  be made up  of any combination of
          the following first second and third characters.

                    First     Second    Third
                      5         N         1
                      6         E         2
                      7         M
                      8         O
                                S

          The first number specifies the number of data bits per character.








                                                                          7


          The second character specifies the parity as follows:

               N = None
               E = Even
               M = Mark (always 1)
               O = Odd
               S = Space (always 0)

          The third character specifies  the number of  stop bits, 1 or  2.
          If 5 data bits are specified, 2 really means 1.5 stop bits.

          The  command LOCK:0:OFF turns the  locking off for  both baud and
          parity for port 0 off.  Request from  the application program for
          baud rate changes will be honored.

          If the indicated port (0 in the above examples) is FOSSIL active,
          the locking or  unlocking will not take effect until  the port is
          reactivated.

          Note that a single OFF parameter ie XU LOCK:0:OFF will reset  all
          locked parameters on the specified port.  If you wish to turn off
          only one of the locked parameters, use a command similar to this:
          XU LOCK:0:19200:OFF








                                                                          8















                                        NASTY

          This  function is not very nice to  other programs.  It will also
          slow down processing when it is  in effect.  NASTY should only be
          turned on if you can not get your program to work any other  way.
          There is  also a good chance  that this option will  lock up your
          system randomly.

          This option will cause  X00 to alter memory of programs that have
          taken interrupt vectors  away from X00.  This may  allow the user
          to achieve desired results in a hostile program environment.

          Examples of usage are:

                                   XU NASTY:ON

                                   XU NASTY:OFF

          Again, use this function only if it is absolutely necessary.  The
          potential for subtle and major problems is not worth it if you do
          not need the NASTY feature.

          This function takes effect immediately upon execution.








                                                                          9







                                         PORT

          This function  allows the user  to make a  port FOSSIL  active or
          inactive.    This  function  is provided  to  (attempt  to)  make
          programs that are not FOSSIL  aware use the FOSSIL.   Thus, these
          programs gain the advantages of interrupt driven serial I/O.

          Examples of usage are:

                                   XU PORT:0:ON

                                   XU PORT:0:OFF

          The command PORT:0:ON  will make  the indicated port  (0 in  this
          case)  FOSSIL active.  This means that interrupts will be enabled
          for the port and I/O will be buffered.

          The command PORT:0:OFF will restore  the indicated port to normal
          operation.   The  OFF command  is also  useful for  poorly tested
          programs  that unintentionally  leaves the  FOSSIL hot  when they
          terminate.

          Several of  the alpha testers of  XU seemed compelled to  issue a
          PORT:0:ON  command prior to running a  FOSSIL aware program, like
          BINKLEY or OPUS, with mixed results.  There is no need to turn on
          the  port  for  FOSSIL aware  programs.   In  fact  it  may cause
          problems if you do.

          You should  not use XU to  activate or deactivate a  port that is
          currently being used by a program.  For example, do not use XU in
          one  DESQview window  to activate  or deactivate  a port  that is
          being  used by a program in another window.  Random problems will
          result if you do.

          Remember,  this function is intended to get programs that are NOT
          FOSSIL  aware to  use  the FOSSIL.    You must  not activate  and
          deactivate ports for FOSSIL aware programs.

          This function takes effect immediately upon execution.








                                                                         10



















                                         SET

          The syntax for  the SET command is identical  to the LOCK command
          above.   This command is  use to immediately  set the operational
          characteristics of a serial I/O port.  This command does not lock
          the settings.  An application program using INT 14h is allowed to
          change the operational characteristics.

          Examples of usage are:

                                   XU SET:0:19200

                                   XU SET:1:1200:8N2

                                   XU SET:0:115200








                                                                         11
























                                     STATUS or S

          This command will display the current operational characteristics
          of X00 and the serial I/O ports that X00 knows about.
           








                                                                         12








                                       USEBIOS

          This function is  provided to maintain  compatibility with  older
          versions of X00.

          Out of self  defense, I found it necessary to  include a BIOS INT
          14h emulator  in X00.   The emulator processes  INT 14h  calls to
          serial  I/O  ports that  are not  FOSSIL  active.   This function
          allows the user to enable and disable the emulator.

          Examples of usage are:

                                   XU USEBIOS:ON

                                   XU USEBIOS:OFF

          The USEBIOS:ON command  tells X00 to pass  calls to the BIOS  INT
          14h processor.  That is, it disables the X00 BIOS emulator.

          The  USEBIOS:OFF command tells X00  to use the  BIOS emulator for
          INT 14h calls to FOSSIL inactive  ports.  That is, it enables the
          X00 BIOS emulator.

          Many  DOOR  type  programs would  not  work  with  X00 until  the
          emulator was added.  By default, X00 uses the emulator.

          If a  program normally uses  BIOS INT 14h  (and it will  not work
          with a FOSSIL),  you will probably see improved  performance when
          the  BIOS emulator  is  used.   Especially if  you have  a 16550A
          installed.

          The  emulator provides X00 with  a fixed frame  of reference with
          respect to the serial I/O ports.   The emulator should be enabled
          (default or USEBIOS:OFF) for the vast majority of programs.

          This function takes effect immediately upon execution.








                                                                         13
















                                       WATCHCD

          This  function is  provided to  enable and  disable a  monitor of
          carrier detect.

          A description for  the need of this function  is beyond the scope
          of this document.  The reason is obvious to those who need it.

          Examples of usage are:

                                   XU WATCHCD:0:ON

                                   XU WATCHCD:0:OFF

          The WATCHCD:0:ON command enables the monitor.  If carrier for the
          specified  port (0 in the  above examples) goes  away, the system
          will be booted.

          The WATCHCD:0:OFF command disables the monitor.

          This function takes effect immediately upon execution.








                                                                         14

                                        INDEX

          16550 (non A) . . . . . . . . . . . . . . . . . . . . . . . . . 3
          16550A  . . . . . . . . . . . . . . . . . . . . . . . .  i, 3, 12
          16550AF . . . . . . . . . . . . . . . . . . . . . . . . . . . . i
          16550AFN  . . . . . . . . . . . . . . . . . . . . . . . . . . . i
          16C551 aka 16551  . . . . . . . . . . . . . . . . . . . . . . . i
          16C552 aka 16552  . . . . . . . . . . . . . . . . . . . . . . . i
          BOOT  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 1
          CAPTURE . . . . . . . . . . . . . . . . . . . . . . . . . . . . 2
          Data bits per character . . . . . . . . . . . . . . . . . . . . 6
          DTR . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 4
          DV  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 5
          FIFO  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 3
          FOSSIL  . . . . . . . . . . . . . . . . . . . . 2, 3, 6, 7, 9, 12
          INTRODUCTION  . . . . . . . . . . . . . . . . . . . . . . . . . i
          LOCK  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 6
               data bits per character  . . . . . . . . . . . . . . . . . 6
               parity . . . . . . . . . . . . . . . . . . . . . . . .  6, 7
               stop bits  . . . . . . . . . . . . . . . . . . . . . . . . 7
               Valid baud rates . . . . . . . . . . . . . . . . . . . . . 6
          NASTY . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 8
          Parity  . . . . . . . . . . . . . . . . . . . . . . . . . .  6, 7
          PORT  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 9
          RTS/CTS hardware handshaking  . . . . . . . . . . . . . . . . . 6
          SET . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  10
          STATUS or S . . . . . . . . . . . . . . . . . . . . . . . . .  11
          Stop bits . . . . . . . . . . . . . . . . . . . . . . . . . . . 7
          TABLE OF CONTENTS . . . . . . . . . . . . . . . . . . . . . .  ii
          USEBIOS . . . . . . . . . . . . . . . . . . . . . . . . . . .  12
          WATCHCD . . . . . . . . . . . . . . . . . . . . . . . . . . .  13