A Quick Reference


			   CONEX VERSION 6.2D

		       Mon  06-14-1993	10:35:35


		  Copyright (C) 1991-93 Erhard Hilbig



CONEX (Latin connection) is used to communicate between IBM personal
computer and a mainframe or between two IBM PCs.

These are the highlights of the program:

 -  The IBM PC can be used as terminal via COM1 - COM4, via Interrupt 14,
    DECNET LAT, FTP TCP/IP and B&W TCP/IP at a mainframe.

 -  Parameters like baudrate (50-115200), parity, full/half duplex,
    xon/xoff or hardware handshake can be set in CONEX.

 -  Files can be transferred without protocol, e.g., to save a session to
    disk.

 -  Several DOS commands can be used inside CONEX, such as "dir", "cd",
    "del" or a DOS shell can be entered.

 -  All incoming characters can be sent to a printer.

 -  You can transfer files to and from the mainframe via KERMIT
    protocol using long packets and sliding windows.

 -  Tektronix 4010/4014 and DEC VT100 - VT320 can be emulated. The
    crosshair in GIN mode can be moved by a mouse.

 -  Graphical output can be displayed on a HPGL plotter or transferred to
    other programs.

 -  Up to 10 pages of screen output can be scrolled back to screen and
    edited.

 -  All keys including the numerical keypad can be programmed.

 -  Incoming characters from the port can be remapped by the user.

 -  The configuration of CONEX can be saved to an ASCII file, which can
    be protected by a password or CONEX can be patched by itself.

 -  Several sessions, especially net sessions, can be opened concurrently.

 -  CONEX is completely written in assembler and therefore very quick
    and small. The only file necessary to run CONEX is "conex.exe".



			ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
			³  How to start CONEX  ³
			ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Simply start CONEX version 6.2d with

		conex [<host name>|<number>] [<options>]

parameters
----------

<host name>   - connect to name of host in a network
		(must have been set with Alt-I before!)
<host number> - enter session 0 - 9 (default: 0)


options
-------

/i<filename> - load different ini file (default: conex.ini)



			   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
			   ³  DOS Commands  ³
			   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

DOS commands can be executed nearly at any time using the alternate keys.



=> <Alt-D> - list Directory

   When asked for "Dir mask:" you can enter filenames using wild cards ?
   and *, e.g. you get all files ending with .asm if you enter "*.asm".
   You can scroll the filenames using the cursor keys.

   If you are to enter a filename e.g. with <Alt-E> or <S> in kermit
   mode, you can switch to this screen with <Page up>/<Page down>. Multiple
   files may then be selected with the keys <Ins> or <Del> or a single
   file simply with <Return>.



=> <Alt-C> - Change to another drive/directory

   You can change to a new drive by adding "<drive>:" to your pathname.



=> <Alt-E> - Erase file

   Wild cards cannot be used when entering the filename, but you can
   switch to a selection menu with <Page up>/<Page down>.



=> <Alt-X> - eXecute DOS commands

   Any valid DOS commands can be executed. But if you want to enter the
   DOS shell completely give <Return>. You return to CONEX with "exit".



			 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
			 ³  Port Parameters  ³
			 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

=> <Alt-I> - Initialize connection

   The following parameters can be modified

   Host:       name of the host to which you are connected. It is only
	       important if you are working on a network with LAT,
	       PC/TCP or BW/TCP. Changing this parameter will
	       automatically close the old session.

   Port:       Com, interrupt 14, LAT, PC/TCP or BW/TCP

   Bits/parity:7 space, 7 even, 7 odd, 7 mark, 8 odd, 8 even, 8 none

   Duplex:     half - all entered characters are immediately displayed.
	       full - the host echoes all received characters.

   more ...:   This allows you to change more parameters which are less
	       important. These are:

   Prompt:     You can enter part of the prompt of the connected machine
	       here. When you enter "return" in "edit mode" all
	       characters following this prompt are transmitted.

   Answer:     This string is transmitted, if the host sends ENQ
	       (decimal 5).


			  COM PORT and INT 14
			 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   Portnumber: 1, 2, 3, 4
		  COM1 ... COM4 if they exist. COM3 and COM4 can only be
		  used if they are defined in BIOS, otherwise you have
		  to set IO-ports and interrupts for these ports in
		  conex.ini. (See tech.ref for more details)

   Baudrate:   50, 75, 150, 200, 300, 600, 1200, 1800, 2400, 3600, 4800,
	       9600, 19200, 38400, 57600, 115200 bits/second
		  Shows the speed at which characters are
		  transmitted.

   Stopbits:   1, 2 - Number of stop bits that follow the end of a
		  character on a serial line. Normally this has not much
		  influence on the transmission.

   Handshake:  none	- no handshake
	       hardware - Characters are only transmitted if pins CTS or
			  DSR are set.
	       xon/xoff - XOFF=^S stops transmission
			  XON=^Q starts transmission again


			   PC/TCP and BW/TCP
			  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   Telnet port: Default port is 23, some hosts use different ports for
		special purposes.

   Telnet timeout: How long do we wait for an answer during initial
	       connection in milliseconds? This value may be increased
	       for long distance connections.


   Some networks offer interrupt 14 as a link.

   LAT (Local Area Transport) is used to connect PC and mainframe via
   DECNET. A resident program called "lat" must be loaded before using
   this option. LAT is contained in DECnet-DOS which is available from
   DEC (Digital Equipment Corporation). This software has been tested
   with DECnet-DOS version 2.1.

   With PC/TCP you can make a telnet connection on ethernet. The PC/TCP
   kernel ("ethdrv") from FTP Software Inc. must be loaded before, it is
   not public domain. The program has been tested with version 2.04, 2.05
   and 2.1. PC/TCP is a registered trademark of

      FTP software, Inc.		   anonymous file server
      26 Princess Street		   vax.ftp.com (128.127.2.100)
      Wakefield, MA 01880
      (617) 246-0900

   BW/TCP has the same features as PC/TCP. The internet number can be
   entered directly as hostname or the hostname can be resolved with a
   host file. Enter its location in <Alt-Y>. Hostname resolution with a
   name server is not supported.

   BW/TCP is a product from Beame & Whiteside Software Ltd.

      Beame & Whiteside Software Ltd	   Tel + Fax:
      P.O. BOX 8130			   (416) 648 6556
      Dundos, Ontario
      CANADA
      L9H 5E7


=> <Alt-S> - Save all current parameters or Patch conex

   The parameters are normally written to the file "conex.ini" and are
   automatically read again when you start CONEX. If you select a
   different name as save file you have to activate it with the command
   line option "/i<filename>".

   The following parameters are saved: port parameters (<Alt-I>), packet
   parameters (kermit mode <I>-command), VT320-emulation (<Alt-M>), graphics
   enabled (<Alt-G>), plot parameters (<Alt-P>) and status line (<Alt-L>) in
   the different sessions 0 ... 9 and the keyboard macros. The save file
   is an ASCII file which can be altered by a normal editor, see
   "tech.ref" for more details. It can also be encrypted with a
   password especially to protect the keyboard macros.

   Replacing the ini-file by the exe-filename (normally "conex.exe") will
   save parameters to conex.exe itself. Afterwards the INI-file is not
   automatically read, lest you force CONEX to read it with the /i-option.
   Password protection is not supported then.


=> <Alt-0> ... <Alt-9> - change to another session

   Up to 10 different network sessions can be opened concurrently
   depending on the limit of the resident network software. Port and
   kermit parameter can be set differently in each session, the screen
   is saved and restored, too. These sessions can be directly selected
   with <Alt-0> to <Alt-9>.


=> <Alt-N> - change to another session with host Name

   All sessions are listed and can be selected with the cursor keys.
   Open sessions in a network are marked with an arrow.



=> <Alt-B> - send Break

   Sends a break over the serial line (short break), if <Alt-B> is
   pressed twice, the signals RTS and DTR are dropped for a short time
   (long break). These commands are normally used to interrupt the
   connection between mainframe and PC. In the networks NOVELL, DECNET
   or TELNET a break is sent according to network standards.



			ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
			³  Terminal Emulation  ³
			ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


The PC can be used as a normal terminal. The following modes can be
selected with function keys:



=> <F7> - normal mode

   All input characters are immediately sent to the mainframe.



=> <F8> - edit mode, scroll back

   In this mode the screen can be scrolled back and modified with the
   cursor keys (<Home>, <End>, <Left>, <Right>, <Up>, <Down>, <Page up>,
   <Page down>, <Del>, <Ins>, <Ctrl-End> = delete to end of line). You
   can scroll back up to 10 screen pages. You can enter this mode with
   <Shift-Cursor keys>, too.

   With <Return> the cursor line is sent to the mainframe and CONEX is
   switched back to normal mode. If a prompt has been defined with
   <Alt-I> for this session it is stripped off. With <Esc> or <F7> you
   return to normal mode without transmitting anything.



=> <F9> - kermit mode

   Kermit must be started on the mainframe to transfer files. (see below)



=> <Alt-M> - change eMulation, character set

   The following DEC terminals can be emulated: VT100, VT102, VT220,
   VT320. Actually these different emulations only differ in the
   response to the terminal identification, nearly all ESC sequences of
   a VT320 terminal are interpreted and the keyboard is set up
   accordingly.

   The keyboard corresponds to a DEC terminal like this:

		       Dec VT 100/200/300 series

			     function keys
  ÚÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³	F6     ³     F7     ³	 F8	 ³    F9      ³    F10	    ³
  ³ <Shift-F6> ³ <Shift-F7> ³ <Shift-F8> ³ <Shift-F9> ³ <Shift-F10> ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  ÚÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³	F11    ³     F12    ³	 F13	 ³    F14     ³    Help     ³
  ³  <Alt-F1>  ³  <Alt-F2>  ³  <Alt-F3>  ³  <Alt-F4>  ³  <Alt-F5>   ³
  ³	       ³	    ³		 ³	      ³    <F11>    ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  ÚÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³	Do     ³     F17    ³	 F18	 ³    F19     ³     F20     ³
  ³  <Alt-F6>  ³  <Alt-F7>  ³  <Alt-F8>  ³  <Alt-F9>  ³  <Alt-F10>  ³
  ³    <F12>   ³	    ³		 ³	      ³ 	    ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

	     edit keys			       numerical keypad
 ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ¿	ÚÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿
 ³   Find   ³  Insert  ³  Remove    ³	³ PF1  ³ PF2  ³ PF3  ³	PF4  ³
 ³	    ³	Here   ³	    ³	³ <F1> ³ <F2> ³ <F3> ³ <F4>  ³
 ³   <End>  ³	<Ins>  ³  <Del>     ³	ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
 ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄ´	³  7   ³  8   ³  9   ³	 -   ³
 ³  Select  ³ Previous ³   Next     ³	³ <7>  ³ <8>  ³ <9>  ³	<->  ³
 ³	    ³ Screen   ³  Screen    ³	ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
 ³  <Home>  ³ <Pageup> ³ <Pagedown> ³	³  4   ³  5   ³  6   ³	 ,   ³
 ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÙ	³ <4>  ³ <5>  ³ <6>  ³	<*>  ³
					ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
					³  1   ³  2   ³  3   ³	     ³
					³ <1>  ³ <2>  ³ <3>  ³	     ³
					ÃÄÄÄÄÄÄÁÄÄÄÄÄÄÅÄÄÄÄÄÄ´ Enter ³
					³     0       ³  .   ³	<+>  ³
					³    <0>      ³ <.>  ³	     ³
					ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ


   In 8 bit mode codes between 128-159 have special meanings and
   the above function keys send 8 bit codes. 8 bit can only be selected
   with VT220 or VT320.

   Character set 1 (characters 33-127) and character set 2 (characters
   160-255) can be selected from ASCII, UK, graphic, German,
   multinational and user. The user character set is defined in
   CONEX.INI.

   <Alt-M> always resets VT320 emulation to default values.


=> <Alt-L> - change status Line

   You can select from the following items:

	1. normal status line,
	2. empty status line,
	3. status line with column numbers,
	4. no status line.

   The selection can be saved with <Alt-S>.


=> <Alt-H> - Help

   This gives a list of all possible commands in CONEX, of modified
   keys and last not least my address. Keys which have been replaced by
   a single key are marked with an arrow.
   Pressing a function key or Alt-combination will execute this command,
   normal keys quit the help screen.



=> <F10> - quit CONEX

   DTR and RTS can be dropped when you leave the program. If you changed
   any important parameters you are asked to save them. Network
   connections are always closed.



=> <Ctrl-Backspace> = DEL, <Ctrl-Return> = LF

   An unknown fact is that DEL (127) and LF (10) can be
   produced this way. Another way is to redefine keys using <Alt-K> or
   define <Backspace> in <Alt-M>.



=> <Ctrl-Num Lock> or <Pause>

   Stop output to screen, any other key resumes output to screen again.
   This command is executed by the normal keyboard device driver.



			  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
			  ³  Graphic Screen  ³
			  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

The program can switch automatically into graphic mode when it
receives a graphic command and behave as a tectronix 4010 or 4014. The
following graphic cards are supported: hercules, CGA, EGA and VGA.
The graphic card is automatically detected on entry to CONEX.

This mode is only used to view graphics, so it is not as comfortable as
normal text mode. Some keys like Alt combinations will not work any more
in this mode.


=> <F5> - enter graphic mode

   Switch into graphic mode manually. The last graphic picture will be
   restored.


=> <Alt-G> - enter Graphic mode automatically

   When a graphic command GS, FS, US or ESC ENQ, ESC FF, ESC SUB is
   received CONEX will automatically switch into graphic mode. You can
   switch back to normal by pressing <F7>.

   In GIN mode the crosshair can be moved using the cursor keys; the
   shift key speeds up this movement. If a Microsoft compatible mouse is
   connected and the mouse driver loaded you can move the crosshair with
   the mouse as well.



=> <Alt-P> - write a Plot file

   The graphics can be written to a file in HPGL format and plotted on a
   HPGL compatible plotter later on. Pagewidth, margins and velocity of
   the pen can be selected as well. Plots use the original resolution of
   a Tektronix 4014 screen.


			ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
			³  Writing Key Macros  ³
			ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



=> <Alt-K> - write Key macro

   Enter key

   All keys can be programmed, if they are detected by BIOS (Int 11h)
   calls. Press <F4> and the key you want to redefine. Simple ASCII
   characters must be entered without <F4>, otherwise you will get an
   error message.

   There also exist some virtual keys þIN0 ... þIN9, which must be
   entered using <F4>, <I>, <N>, #. When a new connection is opened the
   corresponding macro IN# is automatically started. On com ports a new
   connection is determined from the presence of DTR and CTS.


   Macro

   Characters in a macro are sent out at a rate of 10 characters/sec.
   Function, Alt and Control keys must be entered by <F4><key>.

   The following combinations have special meanings in macros:

   ®W#¯
	Wait for # seconds. # = 1...9

   ®R<string1> ³ <string2> ³ ...¯
	Wait until the mainframe sends <string1> or <string2> or ... The
	strings must be seperated with key <F3>= "³".

   ®D#1 ³ #2 ³ ...¯
	Dial telephone number #1, if it is occupied try next number #2
	... The special string sent before or after the phone number
	must be set with Alt-Y, especially prefix (string before
	number), suffix (string after number) and connect|fail (answer
	of mainframe if connected or connection failed).

   - Function keys <F1>="®", <F2>="¯", <F3>="³" can be used to enter
     special characters in macros.
   - A memory region of 10000 bytes is reserved for keyboard macros.
   - During the execution of a macro inputs from the keyboard can be
     done, only ESC stops the macro.


   Label

   <Alt-H> lists the labels of all defined user keys. During the
   execution of a macro this label is also displayed in the status line.
   Labels are ignored if you replace a key by a single key.


=> <Alt-Y> - configuration of CONEX

   page length
     If > 0, page numbers are printed at the top with <Ctrl-print screen>

   prefix dialing
     This string goes before the phone number

   suffix dialing
     This string comes after the phone number

   connect³fail
     First string is the answer from the modem when connected successfully
     all other strings which are seperated by ³ mean connection failed.
     If a connection could not be established, the next number is dialed.

   host name (BW)
     Name of host table, only used with BW/TCP

   default port
     When the program is started in a network with "conex <host>" and a
     session <host> has not been defined, this port is taken by default.
     When set to "automatic", the networks LAT, PC/TCP, BW/TCP and
     Netbios can be detected.



	      ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
	      ³  Transfer of Files without any Protocol  ³
	      ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


=> <Alt-W> - Write file

   Use this command to save all incoming characters to a file either to
   remember what you were doing or to transfer files. The transfer may
   be interrupted with the <Alt-W>.



=> <Alt-R> - Read file

   The file is transferred to the mainframe as it is, especially CR and
   LF at the end of line are sent. The transfer can be interrupted with
   <Alt-R>.



=> <Ctrl-Print Screen> - print incoming characters

   All incoming characters are transferred to the printer. If a page
   length is defined with <Alt-Y>, the printed pages will be numbered.
   Pressing <Control-Print Screen> twice produces a form feed and page
   numbering begins anew.



		  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
		  ³  Transfer Files in Kermit Mode  ³
		  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

You must start kermit on the mainframe and enter "server", "receive" or
"send", then press <F9> to enter local kermit mode to start the file
transfer.



=> <I> -Init parameters

   ASCII/binary file type - Binary files (files with characters over 127)
      should be transferred with file type binary. The mainframe must be
      set to this mode, too, normally with "set file_type binary".
      Sometimes binary files can also be transferred with "parity none",
      which is quicker.

   packet length - length of a transmitted packet including packet
	number, type and checksum. (default 2000) Values above 94 are
	ignored if the host does not support large packets.

   window size - Size of a window. (default 1) Values different from 1
	are ignored if the host does not support windowing.

	- If you want to speed up the transmission rate

	  enlarge packet size <-- reliable connection
	  enlarge window size <-- unreliable connection

	  Enlarging both packet and window size does not make much sense.

   type of checksum - CONEX supports 3 kinds of checksums, which consist
	of 1, 2 or 3 bytes. (default 1) It might be a good idea to
	select a more exact checksum with large packet sizes and
	unreliable connections.

   more... - Change more parameters, which are less important.


   padding character - characters sent before any packets to synchronize
	transmission. (normally not necessary)

   quote control character - control character are quoted with this
	character, Control-A is coded as '#A'. (default #)

   quote 8-bit character - characters whose 8th bit is set are quoted
	with this character, hex A8 is coded as &H. (default &)

   Repeating - repeated characters are compressed in a packet.

   repeat character - 8 characters 'HHHHHHHH' is shortened to 3
	characters ~'H, 8 is coded as '. (default ~)

   packet terminator - Every packet is terminated with this character.
	(default = CR)

   Max number of retries - number of trials to resend a packet, which
      has been refused by the mainframe. (default 5)

   Time out in secs - If the PC did not answer for the specified time
      the last packet is resend. (default 5)



=> <S> - Send files

   Multiple files seperated with blanks and "wild cards" can be entered.
   If you want to select from a file list, press <page up>/<page down>
   and select with <Ins> or <Del>.



=> <R> - Receive files

   This command is used to get files from the mainframe. If this file
   already exists on the PC the old one is renamed to ".bak".

   If the sender has already been told the name of the file ("send
   foo"), simply press return when asked for "receive file". It is also
   possible to enter "wild cards" which are understood by kermit at the
   mainframe.



=> <O> - lOg packets to disk

   If log is on, all sent and received packets are written to the file
   "conex.log". This feature is mainly used to trace down any bugs.


=> <F> - Finish server on the mainframe

   Kermit on the mainframe is terminated and CONEX changes back to
   normal mode.



=> <L> - Logout on the mainframe

   Like "finish" but terminate session, too.



=> cursor keys

   Scroll the messages at the bottom of the screen.



=> <C> - Change directory on the mainframe

   This and the following commands only work, if kermit on the
   mainframe supports generic commands.



=> <D> - list Directory on the mainframe



=> <E> - Erase file on the mainframe



=> <N> - reName file on the mainframe



=> <U> - query disk Usage



=> <M> - send a short Message



=> <Q> - Query server status



=> During a file transfer the following commands can be used.

   <Esc> - interrupts transmission completely. This should be the last
	   resort if nothing else works.

   <^F>  - interrupts the transfer of current file, the transmission
	   proceeds with the next file.

   <^G>  - interrupts file transfer completely.

   <CR>  - resend last packet, if transmission stopped


			 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
			 ³  error characters  ³
			 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Some characters, which are output to screen, have special meanings:

Blinking character  - Parity or Framing error: A bad character was received.
		      Alter bits/parity, if all characters are blinking.

rubout (dec 178)    - Overrun error at COM port. Too many characters have
		      been received at the port.

up arrow (dec 24)   - Sender time out: Characters could not be sent out.
		      In a network environment the connection is
		      interrupted.

down arrow (dec 25) - Receiver time out: Characters could not be received
		      from remote host. The connection is interrupted.


			  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
			  ³ Tips and Tricks ³
			  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

Redefine Backspace to DEL
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

This is what you should do

1. Enter macro definition: <Alt-K>
2. Select key to redefine: <F4> <Backspace> <Return>
3. Delete old definition: <Delete> several times
4. Insert new definition: <Ctrl-Backspace> <Return>




Redefine enhanced IBM numerical keypad to look like DEC VT100/VT220 keypad
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The positions of the EDIT keys on a VT220 keyboard are not the same as
on the IBM keyboard.

	 Dec VT 200/300 series		      PC AT extended keyboard
   ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄ¿	ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄ¿
   ³   Find   ³  Insert  ³  Remove  ³	³ Insert   ³  Home    ³  Page	 ³
   ³	      ³   Here	 ³	    ³	³	   ³	      ³   Up	 ³
   ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄ´	ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄ´
   ³  Select  ³ Previous ³   Next   ³	³ Delete   ³   End    ³  Page	 ³
   ³	      ³ Screen	 ³  Screen  ³	³	   ³	      ³  Down	 ³
   ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÙ	ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÙ

If this is what you want redefine them as follows

directly in conex.ini		      using <Alt-K>

"þINS",,"þEND"!              <F4><Insert>   -->  <F4><End>
"þHOM",,"þINS"!              <F4><Home>     -->  <F4><Insert>
"þPUP",,"þDEL"!              <F4><Page up>  -->  <F4><Delete>
"þDEL",,"þHOM"!              <F4><Delete>   -->  <F4><Home>
"þEND",,"þPUP"!              <F4><End>      -->  <F4><Page up>
   - more -
!

Sorry, some keys on the numeric keypad, like </>, <Enter> cannot be
redefined in this version. Coming in 6.3!


			     ÕÍÍÍÍÍÍÍÍÍÍÍÍ¸
			     ³	Problems  ³
			     ÔÍÍÍÍÍÍÍÍÍÍÍÍ¾

1. Interrupt numbers >7 on COM have not been tested.
2. VT320 emulation is not yet complete. If you encounter any problems
   contact me, so I can enhance the implementation.


			   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
			   ³  Past history ³
			   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

6.0   1st Public Domain Version in comp.binaries.ibm.pc

6.1   default COM3/4 Interrupt = 4 and 3
      COM3/4 Interrupt + IO address configurable
      up to 4 LAT sessions
      ESC FF, ESC SUB, ESC ENQ automatically switch into graphic mode (Alt-G)
      support extended keyboard (esp. F11, F12)
      rotate interrupts configurable in conex.ini
      format of CONEX.INI changed!!!
      dial sequences are saved in CONEX.INI
      start initial macro at 1st opening of a session (<Alt-K>, þIN#)
      characters from port can be remapped (<Alt-M>, character set: user)
      conex can be patched (<Alt-S>, file name: conex.exe)
      support B&W TCP/IP (<Alt-P>)
      ESC stops macros only in normal or graphics mode
      alphabetically sorted output in directory listing
      alphabetically sorted output of macros in help screen
      multinational supplement character set implemented
      ESC ENQ supported in graphics mode
      hercules graphic screen increased to 720 X 360 pixels

6.2   default setting changed to bits/parity: 8 none, emulation: VT320-7
      single key replacement is shown with <Alt-H>
      support sliding windows/long packets in kermit file transfer
      default kermit packet size = 2000 bytes (long packet)
      "ESC [" switches back from graphic mode to text mode
      Cursor type changes according to insert/overwrite mode
      Numbers can be entered directly in windows
      <Shift-TAB> can be programmed
      support printer command under VT... emulation
      features from VT320 emulation
      support UART 16550A FIFO
      Answerback message implemented (<Alt-I>, more=yes)
      support line drawing patterns in Tek mode (ESC `, ..., ESC e)
      "ESC [ ? 38 h" switches into graphic mode
      Characters in Tektronix mode are transmitted to HPGL file
      telnet port and timeout made configurable (<Alt-I>)


			   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
			   ³  Future plans  ³
			   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

- NETBIOS support
- enhance macro language
- more rows, columns on EGA/VGA card
- FTP file transfer
- direct access to packet drivers
- emulate tektronix 4105
- support other file transfer protocols esp. z-modem



			      ÕÍÍÍÍÍÍÍÍÍÍ¸
			      ³  Author  ³
			      ÔÍÍÍÍÍÍÍÍÍÍ¾

	Erhard Hilbig
	Hochschulrechenzentrum
	Universitaet-Gesamthochschule Paderborn
	Postfach 1621
	W-4790 Paderborn (Germany)

	e-mail: zahilb@pbhrzt.uni-paderborn.de
		zahilb@hrz.nw.uni-paderborn.de
	phone: +49 5251/60-2433 	  room: N2-316
	FAX:   +49 5251/60-2519


      This program has been developed by me and can be distributed
     freely. There is also a more detailed documentation in German
     available, which is written in LaTeX. You can have it as LaTeX
	DVI file or as a print file, which must be output using
			"copy conex.lst prn/b".

    If you find any bugs or have an idea how to improve the program,
			   send me a message!