****************************************************************************
 *                                                                          *
 *       DDDD   IIIIII    A    LL     TTTTTT  OOOO   NN   NN EEEEEE         *
 *       DDDDD  IIIIII   AAA   LL     TTTTTT OOOOOO  NN   NN EEEEEE         *
 *       DD  DD   II    AA AA  LL       TT   OO  OO  NNN  NN EE             *
 *       DD  DD   II   AA   AA LL       TT   OO  OO  NN N NN EEEE           *
 *       DD  DD   II   AAAAAAA LL       TT   OO  OO  NN  NNN EE             *
 *       DDDDD  IIIIII AA   AA LLLLLL   TT   OOOOOO  NN   NN EEEEEE         *
 *       DDDD   IIIIII AA   AA LLLLLL   TT    OOOO   NN   NN EEEEEE         *
 *                                                                          *
 *           95LX System Manager Compliant (DTMF) Phone Dialer              *
 *               (c) Ivo Steklac, Toronto, Ontario CANADA                   *
 *                               March 1992                                 *
 *                                                                          *
 ****************************************************************************


DialTone - The HP 95LX Phone Dialer
------------------------------------------------------------------------------

DialTone  is  the  one  simple  utility  that HP/Lotus omitted from the 95LX's
repertoire of built-in applications.  DialTone dials any number stored in your
phone book(s)  by generating  the proper  Dual Tone  Multifrequency (DTMF), or
Touchtone, tones which by playing them into the microphone end of a  telephone
receiver.

Anyone having  seen an  Atari Portfolio  or any  other electronic phone dialer
already knows  that a  Touchtone phone  can be  dialed in  this manner.   This
telephony feature is possible because the DTMF tones are contained within  the
telephone voice  band (0.3-3.0kHz).   The  circuitry within  your phone simply
generates these tones and applies them directly to the phone line.

When I first uncrated my 95LX and tore through the manual (yech!)  I found, to
my disappointment, that this marvel of technology did not have the  capability
of generating DTMF tones.   After hearing its  beeps and moans I  surmised the
unit used a piezo  electric beeper for tone  generation and I gave  up hope of
ever endowing  the device  with this  capability.   Several months later David
Marsh was kind enough to write  and release into the public domain  SND.EXE, a
program that  played digitized  sounds (including  speech) through  the 95LX's
built-in digital to analog converter (DAC) and piezo speaker.

My spirits lifted.  Not only was  this little beauty a pocketable PC -  it was
an improvement on  the original design.   At this  point I conducted  a little
religious ceremony in honor of the "hardware weenies" (to implore a  favourite
of Everet Kaser, who I'm sure is using the praiseworthy connotation of  weenie
as defined in The New Hackers Dictionary) at Corvalis.  After pestering  David
for the source code and clogging  his mail basket with questions about  how to
generate proper sounds I managed to write DialTone.


What is it and what does it do?
------------------------------------------------------------------------------

DialTone is both a  System Manager compliant program  and a DOS program.   The
DOS program is used to calculate the DTMF tones and store them in a data  file
for the  System Manager  version.   The DOS  version also  allows you  to dial
manually entered phone  numbers.  The  System Manager version,  using the data
file created by the DOS version, dials either manually entered phone  numbers,
or phone numbers extracted from the contents of the clipboard.  Obviously this
feature supports pasting phone numbers copied from SYSMGR phone books.

There are several reasons  for having 2 programs.   To generate the  DTMF data
file I needed floating point math which is generally unavailable under  SYSMGR
by any reasonable means (yes I know  both Lotus 123 & HP Calc employ  floating
point math, but I have it  under good authority that they implement  their own
libraries  which  are  inaccessible).    Also  once the Touchtone data file is
created, and fine  tuned, it becomes  a waste of  valuable memory to  drag the
creation code along.


Installation
------------------------------------------------------------------------------

DialTone consists of the following files:

                    DIALTONE.DOC - this file
                    DIALTONE.EXE - DOS setup & config file
                    DIALTONE.EXM - SYSMGR phone dialer
                    DIALTONE.DAT - sample data file
                    DIALTONE.ENV - generated by DIALTONE.EXM

The executable  files, DIALTONE.EXE  and DIALTONE.EXM,  can be  copied to  any
drive and  directory.   According to  95LX fashion,  however, the  data files,
DIALTONE.DAT and DIALTONE.ENV, must reside in "C:\_DAT".  Note the environment
file, DIALTONE.ENV, is created by the SYSMGR version in "C:\_DAT".

You may use  PKLITE to compress  DIALTONE.EXE while you  experiment with phone
dialing, but you must not compress DIALTONE.EXM.


Setup & Configuration - DIALTONE.EXE
------------------------------------------------------------------------------

The DOS program "DIALTONE.EXE" is invoked from the command line with the "new"
argument to create the  "DIALTONE.DAT" DTMF data file.   In creating the  data
file, the following questions must be answered:

                    1. Sampling frequency (in Hz)
                    2. Cumulative frequency error (in %)
                    3. Tone duration (in # of samples)
                    4. Inter-digit pause (in ms.)

The sampling frequency is the rate  at which the program quantizes sine  waves
to generate the primary DTMF tone data.  Frequencies between 23,000 and 24,000
Hertz have worked best for me, although differences between 95LX's and various
phones  may  account  for  other  values  working  better.    Determining  the
appropriate frequency takes a bit of experimentation.  Surprisingly, the  best
method is put a phone against one ear and the 95LX against the other (hold  it
a ways out though - it can be LOUD).

The cumulative frequency error is a percentage figure that denotes a threshold
for the tone generation algorithm.  It is a measure of how close the generated
tone is  to a  pure tone.   Obviously  the lower  the threshold the better the
tonal accuracy.   The telephone specification  can tolerate 1.5%  error.  I've
used figures in the range of 0.20% to 0.50% successfully.  These lower  values
take into account the inherent errors in the piezo electric speaker and in the
free air transmission of the  tones.  Note that the  size of the data file  is
directly proportional to the error threshold.  The smaller the threshold,  the
larger the data file - so  again experimentation will probably yield the  best
results.    To  keep  things  reasonable  DIALTONE.EXE will terminate, without
generating DIALTONE.DAT, if any  one tone exceeds 500  bytes in length.   This
limits the tone file to a maximum of 4,500 bytes.

The tone duration  is given in  samples and denotes  how long each  individual
tone will sound.  The telephone specification calls for a minimum duration  of
50  ms.    In  practice  I've  found  that  the  95LX  must generate tones for
significantly longer than this for them to be recognized.  Durations of  4000
or more samples should  be sufficient.  Note  that the duration does  not have
any impact on the length of the data file.

The last parameter, the inter-digit pause, denotes the duration in ms. of  the
pause that is inserted between subsequent digits.  The telephone specification
calls for a minimum of 50 ms.   In practice I've found that 75 ms. has  worked
well.

The key to determining proper values for these parameters is  experimentation.
Try different phones, home  and work.  I've  found that new electronic  phones
are best, the  older traditional phones  with the carbon  microphones are very
particular.  From these observations it became obvious why HP did not  include
a DTMF dialer in the 95LX - it is simply not possible to provide it in a  form
that "works right out of the box".  If you don't mind fooling around a bit you
can get it to work, if you can't tolerate this kind of hacking, then  DialTone
is not your kind of application.

To assist  the experimentation  effort DIALTONE.EXE  allows you  to dial phone
numbers manually.  This mode is entered after the tone data file is generated,
if the program was invoked with the "new" command line argument, or as soon as
the the program is invoked if  an existing DIALTONE.DAT file is found  and the
"new" keyword  is left  out.   In this  mode the  program excepts phone number
strings similar to those  used in the Hayes  AT command set.   All numbers 0-9
are signaled,  while number  separators such  as "()-"  are ignored.   The ","
provides a pause  for PBX systems.   The pause  is equivalent to  20 times the
inter-digit pause.   In addition to  these, the program  excepts the following
single character commands:

               "x":  exits the program
               "r":  redials the last number
               "l":  same as "r", only closer to the Enter key
               "d":  modifies the tone duration
               "p":  modifies the inter-digit pause

A final few words about DIALTONE.EXE; the program only runs on an HP 95LX, and
is by no means a robust application.  By this I mean it uses "scanf" and other
such user hostile 'C'  standard library calls -  so be careful, please!   Once
you have the data file configured  you can remove DIALTONE.EXE from your  95LX
to conserve precious RAM.


System Manager Phone Dialer - DIALTONE.EXM
------------------------------------------------------------------------------

The  System  Manager  (SYSMGR)  compliant  program  "DIALTONE.EXM"  makes  use
"DIALTONE.DAT" to dial either manually entered phone numbers, or phone numbers
extracted from the SYSMGR Phone Book application.  As with any other  external
SYSMGR  application   a  reference   to  DialTone   must  placed   within  the
C:\_DAT\APNAME.LST application loader name list file.  To invoke DialTone from
the  C:\_DAT\  subdirectory  with  the  {ALT-Phone} hotkey place the following
entry into APNAME.LST (without the quotes):

        "C:\_DAT\DIALTONE.EXM,B700,DialTone"

To register DialTone with SYSMGR save the APNAME.LST file and reboot your 95LX
(make sure to save any open files first), then press {ALT-Phone} to  activate.
After a brief plea for support you'll be presented with the following  opening
screen:

                  +----------------------------------------+
   Application -> |DialTone v1.0      YY-MM-DD hh:mm:ss xm | <- Date/Time in
   Status Line -> |                                        |    your format
                  |========================================|
                  |                                        |
                  |                                        |
        Screen -> | DDD  III   A   L   TTT  OO  N   N EEEE |
        Filler    | D  D  I   A A  L    T  O  O NN  N E    |
                  | D  D  I  A   A L    T  O  O N N N EEE  |
                  | D  D  I  AAAAA L    T  O  O N  NN E    |
                  | DDD  III A   A LLLL T   OO  N   N EEEE |
                  |                                        |
                  |  (c) 1992 Ivo Steklac, Toronto CANADA  |
                  |                                        |
                  |                                        |
  Function Key -> |   Paste    LDC                     Quit|
  Definitions  -> |Dial    PBX                             |
                  +----------------------------------------+

DialTone attempts to follow  the 95LX style of  applications with only one  or
two slight deviations, the most notable being that there is no help, and that
you  can  exit  the  application  using  a  function  key  rather  than a menu
selection.    The  visible  function  keys  provide the majority of DialTone's
functions.

Function key F1 allows  manual entry of a  phone number for dialing;  function
key F2 dials  a phone number  copied from a  Phone Book entry  by means of the
clipboard; function keys F3  and F4 are toggles  that enable, or disable,  the
PBX and  LDC dialing  prefixes; and  function key  F10 removes the application
from memory.  After dialing a number  using either F1 or F2, function key  F9,
redial,  becomes  available  to  enable  you  to  redial the last number.  The
following list summarizes the function keys:

                     F1 : manual dial
                     F2 : paste from clipboard & dial
                     F3 : enable/disable PBX dial prefix
                     F4 : enable/disable LDC dial prefix
                     F9 : redial last number
                     F10: quit application

Function keys F3  & F4 require  a little more  explanation.  If  you work in a
office where you must dial 9 to get an outside line, or you've been in a hotel
where you must dial 8 or 9  to get an outside line, you've experience  using a
PBX, or  personal branch  exchange.   In such  situations you  must prefix the
phone number  you wish  to dial  with a  "9," or  a "8,"  (remember the  comma
provides the necessary delay  for the 95LX to  allow the PBX to  switch to the
outside line before it continues with the rest of the dial string).   Function
key F3 toggles the PBX prefix on and off.  Similarly automatic long  distance
code handling (explained  below) is toggled  with function key  F4.  The  PBX
and long distance code prefixes can be set from DialTone's menu.

Pressing the 95LX MENU key brings up the following screen:

                  +----------------------------------------+
          Menu -> |PBX Prefix  Local LDC  Home LDC  Quit   |
     Edit Line -> |                                        |
                  |========================================|
        Status -> |Current DialTone Settings:              |
                  |                                        |
                  |->PBX Prefix := 9,                      | <- default values
                  |->Local LDC  := 416                     |
                  |->Home LDC   := 416                     |
                  |                                        |
                  |                                        |
                  |                                        |
                  |                                        |
                  |                                        |
                  |                                        |
                  |                                        |
                  |                                        |
                  +----------------------------------------+

The menu behaves  like all other  95LX menus.   The right and  left arrow keys
navigate the menu, ENTER, or the first letter of an option selects the option,
and ESC,  or the  Quit option,  exits the  menu.   The screen  also shows  the
current settings for the  three menu options.   Shown above are their  default
settings prior  to any  modification.   The local  and home  LDC, like the PBX
prefix, are dialing prefixes for long distance codes.  The home LDC represents
the long distance code  of your home town,  the local LDC represents  the long
distance  code  of  the  town  you're  currently  in.  Each option accepts ten
characters, but only recognizes "0-9" and the "," as valid dialing characters.
For clarity DO NOT include any parenthesis, "()", in the LDC prefix codes.

Selecting an option  replaces the menu  with a prompt  message followed by  an
edit line containing the current setting.  Any change is reflected immediately
in  the   status  area   of  the   screen.     The  settings   are  stored  in
C:\_DAT\DIALTONE.ENV according to  95LX convention.   The environment file  is
saved (or created if it does not exist) only upon exiting DialTone (F10).

DialTone employs the following rules when dialing a phone number extracted
from a Phone Book entry (via the clipboard) when LDC prefixes are enabled:

1. If the local LDC is not the same as the home LDC and the phone number to be
   dialed does not have any LDC, DialTone prefixes the phone number with the
   home LDC. The assumption is that you're away from home and dialing a home
   phone number, so you need to include the long distance code.
2. If the LDC of the phone number to be dialed is the same as the local LDC,
   the LDC is removed from the phone number. The assumption is that you're
   presently in the town to which an LDC would apply if you were at home.
3. Any phone number with a LDC is prefixed with "1-" prior to dialing.
4. If the PBX prefix is enabled all phone numbers are prefixed with this
   prefix prior to dialing (the PBX prefix, prefixes the LDC prefix).

   NOTE: These rules do not apply to manually entered phone numbers (ie. those
         entered via F1).

The  LDC  and  PBX  prefix  handling  also  assumes some basic rules have been
applied in the creation of your Phone Book.  These are:

1. All local phone numbers entered in the Phone Book MUST NOT BE proceeded by
   any long distance codes, or other dialing prefixes (such as "9,").
2. All non-local phone numbers entered in the Phone Book MUST BE proceeded by
   the appropriate long distance code bracketed by parenthesis, ie. in the
   form "(xxx)", but MUST NOT BE proceed with a "1-" prefix.
3. Any numbers not conforming to 1. and 2. above will not be correctly handled
   by DialTone, thus it is suggested to disable LDC prefix handling for these
   numbers (overseas numbers for example that require longer dial prefixes are
   not currently supported).
4. Only phone numbers from the 30 character Number field of Phone Book entries
   are currently supported (any numbers found within the address field area
   are ignored). Note only the first phone number from this field is
   extracted.

Finally to enable quick dialing from a SYSMGR Phone Book, it is recommended
that the following keyboard macro be defined using SYSMGR Setup:

        "{F2}{Alt-PHONE}{F2}{PHONE}"

The macro can be bound to any unused  function key (I use F10).  Once set,  it
allows quick  dialing of  the currently  highlighted Phone  Book entry  without
leaving the Phone Book  (well, in principle only,  in actuality you leave  but
come right back to where you left).  Note, if you do not bind DialTone to  the
ALT-PHONE hotkey,  substitute whatever  binding you  used in  the above  macro
definition.


The Bottom Line
------------------------------------------------------------------------------

DialTone (EXE & EXM) and its documentation are copyright (c)1992 Ivo  Steklac,
all rights reserved.  They may not be circulated in any incomplete or modified
form, nor sold for profit, without written permission of the author.

Version  1.0  of  DialTone  is  hereby  released  as  user supported freeware.
DialTone is fully  functional with only  a slightly annoying  plea for support
preceeding  each  invokation  (initial  launching,  and  at  each  SYSMGR task
switch).    If  you  find  DialTone  useful,  and  would  like  to support the
development of 95LX software, please register it.  Single user registration is
a very reasonable $10 US ($15 CDN).  All registered users will receive:

1. A disk copy of DialTone (specify 3 1/2" or 5 1/4" disk) and a certificate
   of registration.
2. One free upgrade to the next released version of DialTone.
3. 50% discounts on all subsequent releases of DialTone or any other 95LX
   software written by the author.

-----------------------------------cut here-----------------------------------

                          DialTone v1.0 Registration

Please send all registrations along with a cheque or money order for
$10 US or $15 CDN to:

Ivo Steklac
205 Wynford Drive #2503
Toronto, Ontario
CANADA
M4G 3X1


Name           :
                -------------------------------------------------------------:
Address        :
                -------------------------------------------------------------:
City           :
                -------------------------------------------------------------:
Country        :
                -------------------------------------------------------------:
Postal/ZIP Code:
                -------------------------------------------------------------:
                        +-+           +-+
Disk Size      : 3 1/2" | | or 5 1/4" | |
                        +-+           +-+

-----------------------------------cut here-----------------------------------


Disclaimer
------------------------------------------------------------------------------

You undertake to use DialTone at your  own risk.  The author does not  warrant
the  suitability  of  DialTone  for  any  particular  purpose,  and assumes no
liability for damages of any kind resulting from its use.

Ivo Steklac
CompuServe [70404, 1073]
Canada Remote Systems (CRS)