HamComm
                                  Version 2.1

                                June 11th 1992




                                W. F. Schroeder

                                    DL5YEC















 
 


         HamComm 2.1                Manual              June 11th 1992
 
 


         1.  Introduction

         HamComm  is  a program for ham radio communications.  Version
         2.1  supports  reception  and  transmission  of amateur radio
         teletype  and  Morse code signals.  A converter or modem chip
         is  not  required.   The  audio  output  of  the  receiver is
         connected  to  the  serial  port  of  any PC/XT/AT compatible
         computer  thru  a very simple and low-cost circuit.  Only one
         IC  is  needed  (Op-Amp  LM741  or similar) and a few diodes,
         capacitors  and  resistors.  The supply current is drawn from
         the  serial port.  For transmission the audio signal from the
         speaker  or  serial port is connected to the microphone input
         of   the  transmitter  thru  a  passive  R/C  filter.   Audio
         frequency generation and decoding, serial/parallel conversion
         and all other signal processing is done by the program.


         2.  License

         HamComm  2.1  is  not in the public domain.  The author keeps
         the copyright and all other rights.

         You are NOT allowed to:
          - make any modifications to the program
          - distribute the program without this file
          - take more than $10 for distribution including all costs

         You ARE allowed to:
          - use this program freely for any non-commercial purpose
          - make as many copies as you like and give them away

         If you like HamComm please send a contribution of $10
         or more to the following address:

                     Django Schroeder
                     Augsburger Weg 63
                     D-4790 Paderborn
                     Germany










 
                                     - 1 -


         HamComm 2.1                Manual              June 11th 1992
 
 


         3.  Exclusion of warranty

         Because  this  program is licensed free of charge, the author
         provides  absolutely  no warranty, to the extent permitted by
         applicable  state  law.   Except  when  otherwise  stated  in
         writing, the author and/or other parties provide this program
         "AS  IS"  without  warranty  of any kind, either expressed or
         implied,   including,   but   not  limited  to,  the  implied
         warranties  of  merchantability  and fitness for a particular
         purpose.   The  entire risk as to the quality and performance
         of  the  program  is  with  you.   Should  the  program prove
         defective,  you  assume  the cost of all necessary servicing,
         repair or correction.

         In no event unless required by applicable law will the author
         and/or  any  other  party  who may modify and/or redistribute
         this program be liable to you for damages, including any lost
         profits,   lost  monies,  or  other  special,  incidental  or
         consequential  damages arising out of the use or inability to
         use  (including but not limited to loss of data or data being
         rendered inaccurate or losses sustained by third parties or a
         failure  of  the  program to operate with any other programs)
         this   program,   even  if  you  have  been  advised  of  the
         possibility  of  such  damages, or for any claim by any other
         party.


         4.  System requirements

         HamComm  2.1  will  run  under  MS-DOS  3.x  or higher on any
         PC/XT/AT-compatible  computer  with  at  least  320KB of free
         memory.   A harddisk is not required.  Because of the size of
         the  program  file  there may be not enough space to copy all
         required  files onto a 360KB diskette.  On slow systems, e.g.
         8088  CPU, some functions may not work as expected or may not
         work at all.

         HamComm  will  automatically detect the type of video adapter
         in  use.  MDA, CGA, EGA, VGA and Hercules are supported.  The
         graphics  display  functions  are not available on MDAs since
         the  MDA  has  no graphics mode.  No attempt has been made to
         avoid screen flicker (snow) on cheap CGAs.

         HamComm  will probably not run under any kind of multitasking
         software like Desqview, Windows or OS/2 since it needs direct
         control  of  the  interrupt controller, timer chip and serial
         I/O hardware.

 
                                     - 2 -


         HamComm 2.1                Manual              June 11th 1992
 
 
         5.  Installation

         For   installation   on   a  harddisk  you  should  create  a
         subdirectory  HAMCOMM  and  CD to that directory.  HamComm is
         distributed  as  a  .ZIP or .EXE file.  To unpack a .ZIP file
         you  need  a program like UNZIP or PKUNZIP.  The .EXE version
         is  a  'self-extracting  archive' that contains all the files
         and  a build-in unpack program.  In both cases the files will
         be created in the current directory.

         Please read the files README, HC.CFG and CHANGES !


         6.  Startup

         To  start  HamComm  type  HC at the DOS prompt and hit ENTER.
         The  interface circuit is not needed if you just want to play
         with the program.

         HamComm  normally uses the currently selected video mode.  If
         you  have  an EGA or VGA card with an EGA/VGA monitor you can
         also  switch to 43 or 50 lines.  Try option -L43 to switch to
         43 lines on EGA/VGA cards or -L50 for 50 lines on VGA cards.

         Many  SuperVGA  cards  have special text modes e.g.  80x60 or
         132x44.   Activate  the desired mode before starting HamComm.
         Most  cards come with a utility program to do this.  Only the
         modes  where  the video display buffer starts at segment B800
         are supported.

         HamComm  assumes  that  the original PC display character set
         known as "codepage 437" is active.

         On  startup the program identifies the video card and monitor
         in  use  and  automatically  selects  the  graphics  mode for
         highest   resolution.    Some  program  functions  require  a
         graphics   mode   for  display  of  the  input  signal.   The
         identification  may  fail  because of compatibility problems.
         By selecting one of the following commandline options HamComm
         can be forced to use the specified mode:

                 Option  Mode      Resolution

                  -cga    6        640x200  2-color
                  -ega   10h       640x350 16-color
                  -vga   12h       640x480 16-color
                  -herc  Hercules  720x348  2-color



 
                                     - 3 -


         HamComm 2.1                Manual              June 11th 1992
 
 
         If  you  have  a computer with LCD display and readability is
         poor try the following DOS command before starting HamComm:

                 mode bw80

         The  'mode'  program is supplied with MS-DOS and is used here
         to switch to black and white mode.


         7.  Screen layout

         HamComm has an SAA-like user interface with pull-down menues,
         dialog  boxes and online helptexts.  The menue bar at the top
         of  the  screen  is  always visible if the program is in text
         mode.   The  bottom  line has information about the currently
         selected menue item.

         Every  name  on  the  menue  bar has a highlighted character.
         Press  and hold the ALT key and type that character to select
         the  corresponding  menue.   The cursor-left and cursor-right
         keys  can  now  be used to switch to the previous/next menue.
         Use the cursor-up and cursor-down keys to move to the desired
         function and hit the ENTER key.

         Every  menue  line  also has a highlighted character.  Typing
         that character (without the ALT key) will get you directly to
         the corresponding function.

         Some  frequently  used  menue  entries  have been assigned to
         function  keys.   The  F8 key for example activates the SCOPE
         function.

         The ESC key can be used any time to abort menue selection.


         8.  Help system

         The  ALT-H and F1 keys both start the help system.  The ALT-H
         key  displays  general  information about the program, the F1
         key displays a help text specific to the current situation.










 
                                     - 4 -


         HamComm 2.1                Manual              June 11th 1992
 
 


         9.  Interface schematics

         The  interface  schematics  are  included  in the online help
         texts.

         1. Start the program,
         2. Hit ALT-H to start the help subsystem,
         3. Hit the letter 'O' to select topic 'Overview',
         4. Hit the TAB key to select topic 'Converter' and hit return,
         5. Scroll the help text using the cursor-up/cursor-down keys
            and read the text.

         Hit ESC to leave the help system.


         10.  Receive circuit

         The  operational amplifier (OpAmp) is used to bring the audio
         signal  from  the  receiver  up  to  RS232 level.  The supply
         current  is  drawn  from  the  DTR and RTS pins of the serial
         port.   The  four  diodes  (1N4148 or similar) of the receive
         circuit form a standard bridge rectifier.  The 1uF capacitors
         are used for buffering.

         The  input  signal amplitude should be at least 100mVpp.  The
         100nF  capacitor  removes  any DC bias.  Since the OpAmp runs
         with  maximum gain there will be a (more or less) rectangular
         waveform  at  its  output.  It should have an amplitude of at
         least +/-5V to reliably drive the RS232 input.

         The  operational  amplifier  LM741  was choosen because it is
         inexpensive   and  widely  available.   However  with  todays
         technology its electrical characteristics are not impressive.
         An LF356 or TL071 for example is much faster and has a higher
         input  resistance.   If  you  want  to substitute a different
         opamp  type,  keep  in  mind  that  the  serial port can only
         deliver a supply current of a few milliamperes.











 
                                     - 5 -


         HamComm 2.1                Manual              June 11th 1992
 
 


         11.  PTT circuit

         The  RTS  output  of the COM port is not only used to provide
         the  supply  current  for  the  opamp,  but  also  to key the
         transmitter.   A Diode is used to protect the base of the PTT
         transistor  against the negative voltage of the RTS output in
         receive  mode.   The  resistor  is required to limit the base
         current.   In  transmit  mode  the  RTS  and  DTR pins change
         polarity.   RTS  is now positive and the transistor pulls the
         PTT  line  to  ground.   This circuit has been tested with an
         FT747, FT757GXII and a TS440S.  On some old rigs there may be
         a  high voltage on the PTT line.  The required current to key
         the  transmitter may also be too high for a small transistor,
         so better check BEFORE connecting it to the computer.


         12.  Transmit circuit

         AFSK  tone  signals  for  transmission  are  available at two
         places:

                 1. at the speaker connector
                 2. at the serial port.

         With  many  motherboards one side of the speaker is connected
         to  the  +5Volt  supply  thru  a  resistor, the other side is
         pulled  to ground by a transistor.  In contrast to most other
         areas  of  the  PC's hardware there is no standard design for
         the  speaker  output, so there may be variations.  In general
         one  side of the speaker will be near ground or +5Volt, while
         the  other side has a square-wave signal.  This signal is fed
         to two R/C filters to smooth it out.  The microphone input is
         very sensitive so a variable resistor is used for attenuation
         and a capacitor to remove any DC.

         If  you don't want to make any modifications to the PC or the
         speaker  output  is  not accessible, you can also get an AFSK
         signal from the TxD pin of the COM port.  The frequencies are
         not  as  accurate  as  at  the  speaker output and will often
         deviate  by  5  to  10Hz, but this usually gives no problems.
         The  signal  level  at the TxD pin is much higher than at the
         speaker  output, so you probably have to change the component
         values for the R/C filter and the attenuator a bit.





 
                                     - 6 -


         HamComm 2.1                Manual              June 11th 1992
 
 
         13.  External converter

         An  option  "External Converter" is available on the "Keying"
         menue.  It can also be controlled by the ALT-F9/ALT-F10 keys.
         If  this  option  is  enabled,  a  mark/space  signal from an
         external  converter  or modem chip is expected at the CTS pin
         of  the  COM  port.  Please note that the normal interface is
         still  required.   There  will  be  no reception if it is not
         connected  or doesn't get the audio signal from the receiver.
         Connect  the  input  of  the  converter  and the input of the
         HamComm interface in parallel to the receiver output.

         Filter   converter   for   RTTY   are  normally  designed  to
         differentiate  between two tones.  For CW reception a kind of
         tone decoder is required that can tell the tone from noise.


         14.  External AFSK

         AFSK  tones  for  transmission  are normally available at the
         speaker  output or the TxD pin of the COM port.  If you don't
         want  to  use those signals for whatever reason, you can find
         an  FSK  signal  at  the  DTR  pin of the COM port.  For RTTY
         transmission  DTR  is  negative for 'mark' state and positive
         for  'space' state.  In CW mode DTR is negative for 'no-tone'
         and  positive  for  'tone'.   During  reception DTR is always
         positive.

         Note  that in receive mode the RTS pin is negative and always
         positive  during  transmissions.  It can thus be used to gate
         the DTR signal for keying a transmitter in CW mode.

         If  you attach any additional components to these pins please
         keep  in  mind  that the DTR/RTS signals supply the power for
         the OpAmp.


         15.  Signal decoding

         The  amplified  audio  signal  is  connected to the DSR modem
         status  input  of  the  serial port where every zero crossing
         generates  an interrupt.  HamComm determines the time between
         successive interrupts using the PCs timer chip and calculates
         the   corresponding   tone   frequency.   Due  to  the  timer
         resolution  of  about  one  microsecond  the  result is quite
         accurate  and  constitutes  the  base  for all further signal
         processing.



 
                                     - 7 -


         HamComm 2.1                Manual              June 11th 1992
 
 
         For  RTTY  decoding  the  tone  is  compared to the currently
         selected  center  frequency to decide wether this is a 'mark'
         or  'space'  signal.  The mark/space signal is sampled at the
         proper time according to the current baud rate collecting all
         bits of a character.

         For  CW  decoding  the  program has to differentiate the tone
         from noise.  To be regarded a valid signal the tone has to be
         between  the  currently selected mark/space frequencies for a
         certain  amount  of  time.   The program maintains a floating
         average  of  the  length  of the dots and dashes to adjust to
         varying speeds.

         When  the character is complete it is converted to ASCII code
         and displayed in the RX window.


         16.  Macro keys

         A  macro  key  can  be  used  to replay a previously recorded
         sequence  of  keystrokes.   The  digits on the top row of the
         keyboard  are  used  as  macro  keys  while  the  ALT  key is
         depressed.    They  are  normally  located  right  above  the
         QWERTY...   row.   Do not confuse these keys with the numeric
         keypad!

         In  the  beginning  there  are  no keystrokes assigned to the
         macro  keys, so pressing ALT-1, ALT-2...ALT-9 or ALT-0 has no
         effect.   To  start  recording,  select item 'Macro recorder'
         from  the  FILE  menue.  A message box will appear confirming
         that  recording has been started.  When the ENTER key is hit,
         the  message  box  will  go  away  and  from now on up to 250
         keystrokes  will be recorded along with normal processing.  A
         blinking  "! RECORDING !" message is shown at the lower right
         corner of the screen to remind you that the recorder is still
         active.

         Now hit one of the macro keys to stop recording and to assign
         the  keystroke  sequence to that key.  This also replaces any
         previous  assignment.   A  message box will appear to confirm
         that  macro  recording  has terminated.  Every time the macro
         key  is  hit the recorded keystroke sequence will be replayed
         just like it had been typed again.

         To  terminate  recording  without changing any macro key just
         select 'Macro recorder' again from the FILE menue.  A message
         box  will  appear  to  confirm  that macro recording has been
         canceled.


 
                                     - 8 -


         HamComm 2.1                Manual              June 11th 1992
 
 
         To  clear  a  macro  key start recording in the usual way and
         directly  after  that  hit the key to clear.  This will erase
         any  previous  recording assigned to that macro key.  Again a
         message box will confirm the result.


         17.  Macro files

         Macro  definitions  can be saved to a file by selecting "Save
         macros"  from the FILE menue.  The usual file select box pops
         up  with  a suggested .MAC file type.  All recorded keystroke
         sequences will be saved to the selected file.

         To load a .MAC file select "Load macros" from the FILE menue.
         All  macro  definitions  found  in  the selected file will be
         added to or replace the current assignments.  Macro keys that
         didn't  hold any keystrokes at the time the file was written,
         will not be changed when the file is loaded.

         There  is  also  a  way  to automatically load your favourite
         macros  definitions.  When HamComm is started it searches for
         the   default   macro  file  HC.MAC,  first  in  the  current
         directory, then in every directory along the PATH.


         18.  Scope function

         In  RX  mode  the tone decoder routine calculates the current
         signal  frequency for use by other parts of the program.  The
         SCOPE  function  uses  this  value  to display a graph of the
         input  frequency  vs.   time.   This  is the blue line on the
         SCOPE screen.

         The tone decoder also maintains a floating average frequency.
         The  effect  is very similar to a low-pass filter and is used
         for  noise  reduction.  The result is displayed at the top of
         the screen as a red line.

         The  solid  green  line  marks  the currently selected center
         frequency  and the dotted lines above and below show the mark
         and  space  tones.  For RTTY reception the center line should
         be  in  the  middle between the mark and space tones.  For CW
         reception  the signal should match the center frequency.  All
         signals  outside  the  area  marked  by  the dotted lines are
         ignored.





 
                                     - 9 -


         HamComm 2.1                Manual              June 11th 1992
 
 
         The display can be controlled with the following keys:

                       F1  display help screen
                      F10  activate menue bar
                      ESC  same as F10
                      '+'  toggle display of decoded signal
                      '*'  toggle grid display
                      'B'  toggle position of red line
                     HOME  reset sample rate to 1ms
                    PG-UP  sample rate faster
                  PG-DOWN  sample rate slower
                    ENTER  hold display immediately

         The  right  mouse  button holds the display at the end of the
         current sweep.  The left mouse button activates the menue bar
         just like F10.

         The  red  line  (input  signal  after  low-pass)  is normally
         displayed  at the top of the screen to not interfere with the
         blue  line.   In its second position it will overlay the blue
         line to compare the two signals.

         Display  of  the decoded signal is normally disabled.  It can
         be found at the bottom of the screen and shows the mark/space
         states for RTTY and tone/no-tone states for CW reception.

         With  some  practice it is quite easy to determine the signal
         you  are  listening  to  by  watching the SCOPE display.  CW,
         AMTOR   ARQ  and  FEC,  Packet  Radio  and  RTTY  show  their
         characteristic  patterns and you can also watch unstable VFOs
         sweeping slowly across the band.


         19.  Spectrum function

         On  entry  to the Spectrum function a graphics mode according
         to the video card and monitor in use is activated.

         Every  millisecond  the  current  input frequency is checked.
         For  every  frequency  there  is  a  counter and the one that
         corresponds  to  the  current  frequency is incremented.  All
         counter  values  are  displayed  as  vertical lines with each
         sweep  from  left to right.  The higher the count, the longer
         the  line.   What  you see on the screen is therefore not the
         true  audio spectrum but the result at the output of the tone
         decoder  routine.   An  opamp  and  a few lines of code can't
         substitute a real spectrum analyzer.



 
                                    - 10 -


         HamComm 2.1                Manual              June 11th 1992
 
 
         When set to 1Hz per pixel SPECTRUM has the best resolution of
         all display functions.  For example, the actual shift used by
         an RTTY station can be determined quite accurately.

         The display can be controlled with the following keys:

                       F1  display help screen
                      F10  activate menue bar
                      ESC  same as F10
                      '-'  toggle raw/filtered data
                      '+'  toggle 'shaddow' (color displays only)
                      '*'  toggle dot/line mode
                     HOME  reset, start at 200Hz, 3Hz per pixel
                    PG-UP  zoom in
                  PG-DOWN  zoom out
                     LEFT  lower frequencies
                    RIGHT  higher frequencies
                    SPACE  clear display
                    ENTER  hold display

         The  right  mouse  button holds the display at the end of the
         current sweep.  The left mouse button activates the menue bar
         just like F10.

         If  you  have a slow PC then don't use the SPECTRUM function,
         you  might  get  frustrated.   There  simply isn't enough CPU
         power  to keep the display in motion.  AT class maschines and
         real fast XTs should be ok.

         The   SPECTRUM   function   has   been   found  to  be  quite
         entertaining, especially with a color display.  Next time you
         got  visitors  in  your  shack who don't know what's going on
         just  start  this  function,  turn  the  lights low and sweep
         across a crowded band.
















 
                                    - 11 -


         HamComm 2.1                                 Table of Contents
 
 
                               Table of Contents


         1 Introduction  ........................................... 1
         2 License ................................................. 1
         3 Exclusion of warranty ................................... 2
         4 System requirements ..................................... 2
         5 Installation  ........................................... 3
         6 Startup ................................................. 3
         7 Screen layout ........................................... 4
         8 Help system ............................................. 4
         9 Interface schematics  ................................... 5
         10 Receive circuit  ....................................... 5
         11 PTT circuit  ........................................... 6
         12 Transmit circuit ....................................... 6
         13 External converter ..................................... 7
         14 External AFSK  ......................................... 7
         15 Signal decoding  ....................................... 7
         16 Macro keys ............................................. 8
         17 Macro files  ........................................... 9
         18 Scope function ......................................... 9
         19 Spectrum function  .................................... 10




























 
                                       i


         HamComm 2.1                                             Index
 
 
         AFSK output................6
         CGA........................2
         Converter, external........7
         Converter..................5
         CW.........................8
         Desqview...................2
         EGA........................3
         ESC........................4
         Exclusion of warranty......2
         External AFSK..............7
         external converter.........7
         F1.........................4
         Floppy.....................2
         Function keys..............4
         Harddisk...................2
         Help system................4
         Installation...............3
         Interface schematics.......5
         Introduction...............1
         Laptop.....................4
         LCD........................4
         License....................1
         Macro files................9
         Macro keys.................8
         Menue bar..................4
         Multitasking...............2
         Operational Amplifier......5
         PTT circuit................6
         Receive circuit............5
         RTTY.......................8
         Scope function.............9
         Screen layout..............4
         Selection..................4
         Signal decoding............7
         Speaker....................6
         Spectrum function.........10
         Startup....................3
         SuperVGA...................3
         System requirements........2
         Transmit circuit...........6
         VGA........................3
         Video adapter..............2
         Windows....................2
         XT.........................2






 
                                       i