+=================================================+                +=================================================+
                |      PibTerm Script Language Reference Guide    |                |      PibTerm Script Language Reference Guide    |
                +=================================================+                +=================================================+
                                          
                                          
                                          
                                          
                                          
            
            
            
            
            
            
            
            
            
            
            
            
            
            
            
                  Copyright (c) February, 1988 by Philip R. Burns                  Copyright (c) February, 1988 by Philip R. Burns






            
            Using Script Files ....................................    1            Using Script Files ....................................    1
                Compatibility With Old Scripts ....................    1
            Executing a Script File ...............................    1            Executing a Script File ...............................    1
                From the PibTerm command line .....................    1
                From <ALT>G .......................................    2
                User-defined command ..............................    2
                Compiling Scripts .................................    2
                Limitations on Script Size ........................    2
                Script Library PIBTERM.SCL ........................    2
                    Search Order For Scripts ......................    3
                Terminating Execution Of A Script .................    4
                Automatic Script Generation -- The Learn Facility .    4
            Script File Commands ..................................    4            Script File Commands ..................................    4
                General Syntax of Script Commands .................    9
                Script Variable Names .............................    9
                    Declaring variables ...........................   10
                    Saving variable values after script ends ......   10
            Detailed Description of Script Commands ...............   11            Detailed Description of Script Commands ...............   11
                AddCommand -- Add User-Defined Command ............   11
                Addlf -- Add Line Feeds ...........................   14
                Alarm -- Issues Five Beeps ........................   14
                Break -- Send Break ...............................   14
                Call -- Call Internal Script Procedure ............   14
                Capture -- Capture Session To Disk ................   14
                Case -- Case Selector For DoCase ..................   15
                ChDir -- Change Current Directory or Drive ........   15
                Clear -- Clear Screen .............................   15
                Close -- Close File ...............................   16
                ClrEol -- Clear Display To End Of Line ............   16
                ComDrain -- Drain Serial Port Output Buffer .......   16
                ComFlush -- Flush Serial Port Buffers .............   16
                CopyFile -- Copy File .............................   17
                Delay -- Delay Execution For Specified Interval ...   17
                DelLine -- Delete Current Line On Screen ..........   18
                Dial --- Dial A Number ............................   18
                DirFirst -- Find First Matching File ..............   18
                DirNext -- Find Next Matching File ................   20
                DoCase -- Do Case Statement .......................   22
                Dos -- Execute DOS Command ........................   23
                Echo --- Toggle Local Echo ........................   24
                EditFile -- Invoke File Editor ....................   24
                Else -- Part Of IF Statement ......................   24
                EndCase -- Ends Case Block ........................   25
                EndDoCase -- Ends DoCase Statement ................   25
                EndIf --- Ends An IF Statement ....................   25
                EndProc -- Ends a Script Procedure ................   25
                EndWhile -- Ends a WHILE block ....................   25
                EraseFile -- Erase (Delete) A File ................   25
                Execute -- Execute One Script From Another ........   25
                Exit -- Terminate Script Execution ................   27
                ExitAll -- Exit Nested Scripts ....................   27
                For -- Start FOR Loop .............................   28
                FreeSpace -- Find Free Space On Drive .............   28






                GetDir -- Get Current Directory And Drive .........   29
                GetParam -- Get Value of PibTerm Parameter ........   29
                GetVar -- Get Value of Script Variable ............   30
                GoToXY -- Move To Specified Screen Position .......   31
                Hangup -- Hang Up The Phone .......................   32
                Host -- Enter Host Mode ...........................   32
                If -- Conditionally Execute Statements ............   32
                    Conditions allowed in IF statements ...........   32
                Import -- Import Variable To Execute Script .......   33
                Input -- Get Input From Keyboard ..................   34
                InsLine -- Insert Line At Cursor ..................   35
                Key -- Set Function Key Values ....................   35
                KeyDef -- Define Function Key Value ...............   36
                KeyFlush -- Flush KeyBoard ........................   37
                KeySend -- Send Function Key Value To Remote ......   37
                Log -- Toggle Printer Logging .....................   38
                Menu -- Display Pop-Up Menu .......................   38
                Message -- Display Message On Screen ..............   39
                Mute -- Toggle Mute Mode ..........................   39
                Open -- Open File .................................   39
                Param -- Set Program Parameter ....................   40
                PrintFile -- Print A FIle .........................   41
                Procedure -- Define Script Procedure ..............   41
                Quit -- Quit PibTerm execution ....................   44
                Read -- Read Character From A File ................   44
                Readln -- Read Line From File .....................   45
                Receive -- Receive File From Remote System ........   46
                Redial -- Redial Last Number Dialed ...............   48
                Repeat -- Repeat Block Of Statements ..............   48
                Reset -- Reset Script Execution To Start Of Script    49
                RInput -- Receive Input From Remote System ........   49
                ScreenDump -- Dump Screen To File .................   50
                Send -- Send File To Remote System ................   50
                Set -- Assign Value To Script Variable ............   52
                SetParam -- Set Value Of PibTerm Parameter ........   55
                SetVar -- Set Value of PibTerm Parameter ..........   56
                SText -- Send Text To Remote System ...............   57
                Suspend -- Suspend Execution Of Script ............   57
                Text -- send text to remote system ................   58
                Translate -- Read In Translate Table ..............   58
                Until -- Ends Repeat Block ........................   58
                ViewFile -- Invoke File Viewer ....................   58
                Wait -- Wait For Time Of Day ......................   59
                WaitCount -- Wait For Number Of Characters ........   59
                WaitList -- Wait For List Of Strings ..............   60
                WaitQuiet -- Wait For Quiet Line ..................   61
                WaitString -- Wait For String From Remote .........   61
                WaitTime -- Set Wait Time .........................   62
                When -- Wait For String And Respond ...............   62
                WhenDrop -- Take Action On Carrier Drop ...........   63
                WhereXY -- Return Current Cursor Position .........   63
                While -- Execute Statements While Condition True ..   64
                Write -- Write Characters To File .................   64
                Writeln -- Write Line To File .....................   65






                WriteLog -- Write String To Log Files .............   65
            Using Script Commands in Command Line Mode ............   65            Using Script Commands in Command Line Mode ............   65
                Command mode key definition .......................   65
                Script Commands Legal In Command Line Mode ........   66
            Sample Scripts ........................................   67            Sample Scripts ........................................   67
                CDC/NOS login script ..............................   67
                VAX/VMS login script ..............................   68
                IBM CMS login script ..............................   69
                LUIS login script .................................   71
                OPUS login script .................................   72
                RBBS login script .................................   73
                IBBS login script .................................   73
                CompuServe login script ...........................   74
                Using A Password File .............................   75
                PC Board login script using password file .........   78
                Reading A New Configuration File ..................   80
            Defining Scripts For External Transfer Protocols ......   81            Defining Scripts For External Transfer Protocols ......   81
                SENDMLIN.SCR for sending files with MegaLink ......   84
                RECMLINK.SCR for receiving files with MegaLink ....   86
                SENDZMOD.SCR for sending files with Zmodem ........   87
                RECZMOD.SCR for receiving files with Zmodem .......   89
            






            
            Using Script Files            Using Script Files
            
            PibTerm provides  an extensive  script file  facility  which
            allows you to create a file containing a set of instructions
            for PibTerm to execute. The instructions can include dialing
            up a  remote system, performing file transfers,  waiting for
            a specific time before initiating an event, and many others.
            Scripts allow  PibTerm to  run in   unattended mode and take
            advantage of  off-hours  rates  on  host  computer  systems.
            Scripts automate such chores as logging into remote systems.
            And,  scripts  provide  you  with  the  tools  you  need  to
            customize PibTerm by adding new commands or replacing built-
            in commands with those of your own devising.
            
            
            Compatibility With Old Scripts            Compatibility With Old Scripts
            
            The script  language starting with PibTerm v4.0 represents a
            considerable upgrade  of the  script language  available  in
            previous  versions.    Most  of  the  script  commands  have
            changed, mainly  to support  script variables.  When writing
            new scripts  you should  use the  new syntax and facilities.
            However,  scripts  written  using  the  old  pre-version-4.0
            script language  SHOULD continue  to work  with just  a  few
            minor changes.   If an old script does not execute correctly
            with PibTerm  v4.0 (or  a later  version), try rewriting the
            part of  the old  script that  fails using  the  new  script
            syntax.   Most of  the incompatibilities  arise  because  of
            script variables, which are new in PibTerm v4.0, and because
            of minor  changes in  things  like  file  transfer  protocol
            abbreviations.
            
            
            Executing a Script File            Executing a Script File
            
            There are three ways to execute a script file.  The first is
            to enter  the file  name of  a script  file on  the  PibTerm
            command line itself at the DOS prompt:
            
                 PIBTERM /s=script.SCR
            
            where script.SCR is the name of a script file.  You need not                  script.SCR                                            
            explicitly give  the .SCR,  it is  understood  if  no  other                                 .SCR                                   
            extension is provided.
            
            When PibTerm  begins execution,  it will take its input from
            the script file.  You may still type keyboard entries if you
            desire, and  there are some script commands which explicitly
            request keyboard  input.   This  provides  quite  a  bit  of
            flexibility  in   case  something   goes  wrong  during  the
            execution of  a script  and you  are present  to repair  the
            damage.
            



            PibTerm Script Language Reference Guide              Page 2            PibTerm Script Language Reference Guide              Page 2


            If no  script file  name appears  on the PibTerm invocation,
            PibTerm looks  for the  file  PIBTERM.SCR  and  executes  it                                          PIBTERM.SCR                   
            automatically if  found.   This is  useful if  you  want  to
            execute a  fixed set  of commands  each time  you  start  up
            PibTerm.
            
            The second  way to  execute a  script file is to hit <ALT>G.
            You will  be prompted  for the  name of  the script  file to
            execute.  Again, you need only provide the first part of the
            file name; .SCR is understood.
            
            If you  hit the  Enter key, a directory of available scripts                             Enter                                      
            appears. You  can choose  to execute one  by using the arrow
            keys to  move to the desired script and hitting the Enter or                                                                Enter   
            Return key.            Return     
            
            The third  way to  execute a  script is  through the  use of
            user-defined commands.   PibTerm  allows you  to  execute  a
            subset of  script commands  using a  command-line mode.  You
            can also  define your  own commands  as  extensions  to  the
            script language;  these are implemented as scripts which are
            automatically invoked  when the  command you defined is used
            in command-line mode.  We will discuss user-defined commands
            in more detail later on.
            
            
            Compiling Scripts            Compiling Scripts
            
            Before  executing  a  script  file,  PibTerm  scans  it  and
            converts it  to an in-memory list of commands.  This process
            is called  compiling  the  script.  During  the  compilation                       compiling                                        
            process, you  will be informed if any script command line is
            syntactically bad.  PibTerm stops scanning at the first line
            in error.  Any erroneous  script statement  prevents PibTerm
            from executing the script.
            
            
            Limitations on Script Size            Limitations on Script Size
            
            The size  of a  script is limited by the available memory to
            hold the  "compiled" script  code. If  there is  not  enough
            memory for  the  script,  it  will  not  be  executed.    No
            individual script can compile to more than 32767 bytes; this
            should not  pose   any problems,  since long  scripts can be
            broken up into a series of shorter scripts which  can invoke
            each other using the EXECUTE script command.                                 EXECUTE                
            
            
            Script Library PIBTERM.SCL            Script Library PIBTERM.SCL
            
            The  file  PIBTERM.SCL  provides  a  simple  script  library                       PIBTERM.SCL                                      
            facility. Versions  of PibTerm  prior to  v4.0 required that
            each script  be stored  in a separate file. This resulted in
            considerable wasted  disk space,  since even  a tiny  script



            PibTerm Script Language Reference Guide              Page 3            PibTerm Script Language Reference Guide              Page 3


            took up  a large  block of disk space.  The file PIBTERM.SCL
            may contain  many scripts;   since  it it is one large file,
            disk space is more efficiently used.
            
            PIBTERM.SCL is  a straightforward  ASCII  text  file.    The
            scripts contained  in it  follow one  right after the other,
            separated by a line beginning (in column one) with two equal
            signs and  the name  of the script.  For example, if we have
            three  scripts,   named  WINKEN,   BLINKEN,  and  NOD,  then
            PIBTERM.SCL would look like this:
            
            
                 ==WINKEN
                      -- text of winken.scr
                 ==BLINKEN
                      -- text of blinken.scr
                 ==NOD
                      -- text of nod.scr
            
                 ^
                 |
                 column 1
            
            Script entries  will be  searched for  sequentially in  this
            file. Thus,  you should place the most commonly used scripts
            at the front of PIBTERM.SCL.
            
            PIBTERM.SCL  must  reside  in  the  main  PibTerm  directory
            (pointed to by SET PIBTERM=).
            
            You may  place the  primary script  file to  be executed  in
            PIBTERM.SCL instead of creating a separate PIBTERM.SCR file.
            For this to work, the following conditions must hold:
            
                 1.   No PIBTERM.SCR exists.
            
                 2.   ==PIBTERM    is  the FIRST LINE (and therefore the
                      first script) in PIBTERM.SCL.
            
            This execution order is taken regardless of any script order
            configuration settings (see next section).
            
            
            Search Order For Scripts            Search Order For Scripts
            
            The new  parameter SF=  provides the  name of  the directory
            containing the  (separate file)  scripts to be executed.  If
            SF is  the null  string, then the current directory is used.
            SF= can be set from the <ALT>P P)aths menu.
            
            Scripts may executed from separate files or from the library
            file PIBTERM.SCL.   The  new parameter SO= defines the order
            in which a search for a script is performed:
            



            PibTerm Script Language Reference Guide              Page 4            PibTerm Script Language Reference Guide              Page 4


                 SO=0:     SF= directory, then PIBTERM.SCL  (default)
                 SO=1:     PIBTERM.SCL then SF=
                 SO=2:     SF= only  (ignore PIBTERM.SCL)
                 SO=3:     PIBTERM.SCL only  (ignore SF= and any scripts
                           contained there)
            
            
            Terminating Execution Of A Script            Terminating Execution Of A Script
            
            To stop  executing a  script, use  the <ALT>X command.  If a
            script is  executing, you  will be prompted as to whether or
            not you want to stop executing the script.  If you then want
            to exit PibTerm, type <ALT>X again.
            
            You can  also use  the EXIT  and EXITALL  script commands to                                   EXIT      EXITALL                    
            terminate a  script from  within a  script, or  from command
            line mode.
            
            
            Automatic Script Generation -- The Learn Facility            Automatic Script Generation -- The Learn Facility
            
            If you  hit Enter  after striking  <ALT>G, you are presented
            with a  list of  scripts available  for execution as well as
            several other  facilities.   One of  these is  the "Learn  a
            script."   This option  opens a  file to receive a specially
            edited transcript of the communications session in which the
            local and  remote input  and  output  are  transformed  into
            script commands.   This allows PibTerm to "learn" a sequence
            of script commands which you can edit and use again later.
            
            When you start a learn script sequence, you are prompted for
            the maximum  number of  characters to  be generated  in  any
            WAITSTRING and also for the maximum number of lines (defined
            by a  string of  characters ended  with  CR  or  LF)  to  be
            generated in  any WAITSTRING.  Usually choosing the defaults
            of 30 characters and 1 line produces good results.
            
            You usually need to touch up the generated script  manually.
            
            See the  "Guide to  PibTerm" for  more details on learning a
            script.
            
            
            Script File Commands            Script File Commands
            
            Script file  commands consist  of an  initial  command  word
            possibly followed by zero or more arguments.  Blank lines or
            lines beginning  with an  "*" may be used as comments.  Many
            of the  commands perform  similar functions  to the  regular
            <Alt>letter keyboard entries described in the PibTerm Guide.
            
            Here is  a complete  list of  PibTerm script commands with a
            brief description  of the  purpose  of  each.    A  detailed
            description of each command will be given later.



            PibTerm Script Language Reference Guide              Page 5            PibTerm Script Language Reference Guide              Page 5


            
            AddCommand     adds a user-defined command to PibTerm script            AddCommand                                                  
                           language
            
            AddLF          adds line feeds to carriage returns.            AddLF                                              
            
            Alarm          issues five beeps            Alarm                           
            
            Break          issues a break sequence (like <ALT>B).            Break                                                
            
            Call           calls internal script procedure            Call                                          
            
            Capture        toggles session  capture  to  specified  file            Capture                                                     
                           (like <ALT>O).
            
            Case           selection block header for DOCASE statement            Case                                                      
            
            ChDir          changes current directory            ChDir                                   
            
            Clear          clears the screen (like <ALT>C).            Clear                                          
            
            Close          closes specified file            Close                               
            
            ClrEol         clears display  from cursor to end of line on            ClrEol                                                      
                           screen
            
            ComDrain       drains serial port output ring buffer            ComDrain                                            
            
            ComFlush       flushes ring buffers for serial port            ComFlush                                           
            
            CopyFile       copies one file to another            CopyFile                                 
            
            Declare        provides name,  type, and  initial value  for            Declare                                                     
                           script variable
            
            Delay          delays PibTerm execution for specified length            Delay                                                       
                           of time.
            
            DelLine        deletes current line in screen display            DelLine                                              
            
            Dial           dial a  number in the dialing directory (like            Dial                                                        
                           <ALT>D).
            
            DirFirst       finds  first   file   matching   a   wildcard            DirFirst                                                    
                           specification
            
            DirNext        finds subsequent  files matching  a  wildcard            DirNext                                                     
                           specification
            
            DoCase         starts multiway selection statement            DoCase                                            
            
            Dos            executes a  specified DOS  command  (somewhat            Dos                                                         
                           like <ALT>J).
            



            PibTerm Script Language Reference Guide              Page 6            PibTerm Script Language Reference Guide              Page 6


            Echo           toggles local echo (like <ALT>E).            Echo                                            
            
            
            EditFile       invokes the currently defined editor (usually            EditFile                                                    
                           the built-in PibTerm editor)
            
            Else           FALSE branch of an IF statement.            Else                                           
            
            EndCase        ends a Case block            EndCase                         
            
            EndDoCase      ends a DoCase statement            EndDoCase                             
            
            EndFor         ends FOR loop            EndFor                      
            
            EndIf          ends an IF statement.            EndIf                               
            
            EndProc        ends an internal script procedure            EndProc                                         
            
            EndWhile       ends a WHILE statement.            EndWhile                              
            
            EraseFile      erases (deletes) a file            EraseFile                             
            
            Execute        executes another script            Execute                               
            
            Exit           stop executing the script.            Exit                                     
            
            ExitAll        exits nested scripts            ExitAll                            
            
            For            starts For loop            For                           
            
            FreeSpace      finds free space on drive            FreeSpace                               
            
            GetDir         gets current drive and directory            GetDir                                         
            
            GetParam       gets value of a PibTerm parameter            GetParam                                        
            
            GetVar         gets value of a PibTerm variable            GetVar                                         
            
            GoToXY         positions   cursor    at   specified   screen            GoToXY                                                      
                           coordinates
            
            HangUp         hangs up the phone (like <ALT>H).            HangUp                                          
            
            Host           enters Host mode (like <ALT>W).            Host                                          
            
            If             test   for   several   different   types   of            If                                                          
                           conditions; Else  is also available and Endif
                           terminates an IF block.
            
            Import         declares variable  passed  to  nested  script            Import                                                      
                           invoked using Execute
            
            InsLine        inserts line  at current  cursor position  on            InsLine                                                     
                           screen



            PibTerm Script Language Reference Guide              Page 7            PibTerm Script Language Reference Guide              Page 7


            
            Input          prompt for input from local user.            Input                                           
            
            Key            sets function  keys from specified file (like            Key                                                         
                           <ALT>K "Read definitions from a file").
            
            KeyFlush       flushes current keyboard buffer            KeyFlush                                      
            
            KeySend        sends specified  function key's definition to            KeySend                                                     
                           remote system.
            
            Log            toggles  session  logging  on  printer  (like            Log                                                         
                           <ALT>L).
            
            Menu           displays pop-up menu            Menu                               
            
            Message        display message  on PC's  screen; message  is            Message                                                     
                           not sent to remote system.
            
            Mute           toggles mute mode (like <ALT>M).            Mute                                           
            
            Open           opens a file            Open                       
            
            Param          sets program parameters            Param                                 
            
            PrintFile      starts printing  of  a  file  using  built-in            PrintFile                                                   
                           PibTerm spooling facility
            
            Procedure      defines start of internal script procedure            Procedure                                                
            
            Read           reads characters from a file            Read                                       
            
            Readln         reads a line from a file            Readln                                 
            
            Receive        receives a  file from  a remote  system (like            Receive                                                     
                           <ALT>R).
            
            Redial         redials the  last phone  number entered (like            Redial                                                      
                           <ALT>Q).
            
            Repeat         begins block  of statements  to be repeatedly            Repeat                                                      
                           executed until  condition on  matching  UNTIL
                           statement is true.
            
            Reset          starts executing  script from  the  beginning            Reset                                                       
                           again.
            
            Return         returns from  internal  script  procedure  to            Return                                                      
                           calling procedure
            
            RInput         prompt for input from remote system.            RInput                                             
            
            Send           sends a file to a remote system, like <ALT>S.            Send                                                        
            



            PibTerm Script Language Reference Guide              Page 8            PibTerm Script Language Reference Guide              Page 8


            Set            sets value of a script variable            Set                                           
            
            SetParam       sets value of a PibTerm parameter            SetParam                                        
            
            SetVar         sets value of a script variable            SetVar                                        
            
            SText          send text  to remote  system,  and  interpret            SText                                                       
                           embedded   characters   like   function   key
                           characters.
            
            Suspend        suspends  script   execution  for   specified            Suspend                                                     
                           length of time (PibTerm continues executing).
            
            Text           send   text    to   remote   system   without            Text                                                        
                           interpretation.
            
            Translate      reads in a translation table (like <ALT>T).            Translate                                                 
            
            Until          terminates   REPEAT    block   and   provides            Until                                                       
                           termination condition.
            
            ViewFile       invokes   currently   defined   file   viewer            ViewFile                                                    
                           (usually built-in PibTerm file viewer)
            
            Wait           stops PibTerm  execution  until  a  specified            Wait                                                        
                           time (in  HH:MM:SS form) is reached, at which
                           time execution proceeds.
            
            WaitCount      waits for  specified number  of characters to            WaitCount                                                   
                           appear from remote system
            
            WaitList       waits for  any one  of a  list of  strings to            WaitList                                                    
                           appear from remote system
            
            WaitQuiet      waits for serial port input to quiesce            WaitQuiet                                            
            
            WaitString     waits for  a given  string to appear from the            WaitString                                                  
                           remote system (only done once).
            
            WaitTime       sets wait time for other wait commands            WaitTime                                             
            
            When           waits for  a given  string to appear from the            When                                                        
                           remote system,  and then  sends  a  specified
                           response string  (done as  often as  required
                           string appears).
            
            WhenDrop       specifies action to take when carrier drops            WhenDrop                                                  
            
            WhereXY        returns current cursor position on screen            WhereXY                                                 
            
            While          begins block  of statements  to be repeatedly            While                                                       
                           executed as  long as  specified condition  is
                           true.   A While  block is  terminated  by  an
                           EndWhile statement.



            PibTerm Script Language Reference Guide              Page 9            PibTerm Script Language Reference Guide              Page 9


            
            Write          writes characters to a file            Write                                     
            
            Writeln        writes a line to a file            Writeln                               
            
            WriteLog       writes text to log/capture files            WriteLog                                       
            
            
            General Syntax of Script Commands            General Syntax of Script Commands
            
            Here are some general comments about script command syntax:
            
            1.   Command names  may be  entered in  any case;  "CLEAR" =
                 "Clear" = "ClEaR".
            
            2.   Each command must fit on a single input line.  There is
                 no provision for multi-line commands.
            
            3.   When quoted  strings are  called for,  either single or
                 double quotes  may be  used.   To insert a quote into a
                 string in  which that  same quote  is being used as the
                 string delimiter,  write  two  adjacent  quotes.    For
                 example, the string
            
                      Here's a string
            
                 can be written as:
                 
                      'Here''s a string'.
            
            4.   Quoted strings  cannot span  a line.   Unclosed  quotes
                 cause an error.
            
            
            Script Variable Names            Script Variable Names
            
            The PibTerm  script language  includes variables  as well as
            commands. Script  variable names may be up to ten characters
            long, and  may contain letters and digits.  Case is ignored.
            The first character must be a letter.
            
            Examples:
            
                 Abc
                 c34
                 ABC  (same as Abc)
                 thelongone
            
            



            PibTerm Script Language Reference Guide              Page 10            PibTerm Script Language Reference Guide              Page 10


            Declaring variables            Declaring variables
            
            You may  declare script  variables using  the Declare script                                                          Declare       
            command. ALL  script variables  MUST  appear  in  a  Declare
            command.  Each Declare defines only one variable.
            
            The syntax of a Declare statement is:
            
                 DECLARE name type S3
            
            where name is the variable name,  type is the variable type,                  name                        type                      
            and S3  is the  initial value  of the  variable.   S3 may be
            either a string variable or a string constant.
            
            Note that  neither the  name nor  the type  is  enclosed  in
            quotes.
            
            Case is not important in variable names.
            
            The following types are available:
            
            INTEGER   An integer  value from  -2147483648 to  2147483647            INTEGER                                                     
                      (beginning with  PibTerm v4.1  -- in PibTerm v4.0,
                      values were limited to the range -32768 to 32767).
            
            STRING    A variable  length  string  of  maximum  size  255            STRING                                                      
                      characters.
            
            Examples:
            
                 DECLARE Abc String  'ABC'
            
                      --   a string of maximum length 255 with initial   
                           value ABC
            
                 DECLARE c  Integer
            
                      --   'c' is an integer with initial value 0
            
            When no  initial value  is provided  a  string  variable  is
            assigned the  null string as a value when it is declared.  A
            numeric variables  is set  to zero  if no  initial value  if
            provided.
            
            ABC, Abc,  AbC, etc.  are all  the same variable name.  Case
            doesn't matter in variable names.
            
            
            Saving variable values after script ends            Saving variable values after script ends
            
            Variables disappear  when the  last script  in  a  stack  of
            nested scripts  is finished executing.  If you want to carry
            over the  variable  values  from  one  script  execution  to
            another, you  can use  the text  file  facilities  to  store



            PibTerm Script Language Reference Guide              Page 11            PibTerm Script Language Reference Guide              Page 11


            information on  MS DOS  files  between  script  invocations.
            Alternatively, you  can store  variable values  in  (unused)
            function  keys  (see  the  KeyDef  script  command  and  the                                       KeyDef                           
            KeyString function in the Set script command).            KeyString                 Set                 
            
            Each script  gets it  own set  of variables.  It is possible
            for one  script to invoke another, and for those two scripts
            to share  variables.  This is done using the Import facility
            described later.
            
            
            Detailed Description of Script Commands            Detailed Description of Script Commands
            
            The following  sections  detail  each  script  command.  The
            examples for some commands use other commands which will not
            be described  until later.   You may need to make two passes
            through these  descriptions in order to fully understand the
            examples.
            
            In what  follows, any  variable name  beginning with  a  'S'
            indicates a  string variable  or constant,  and any variable
            starting with 'I' indicates an integer variable or constant.
            (Note:   It is  assumed that  variables have  been  properly
            declared using the DECLARE statement.)
            
            
            AddCommand -- Add User-Defined Command            AddCommand -- Add User-Defined Command
            
            PibTerm allows you to define up to one hundred new commands.
            This is  primarily useful  when PibTerm  is  being  used  in
            command key mode.
            
            The script  command AddCommand  adds a  new command.  It has                                AddCommand                              
            the syntax:
            
                 AddCommand Sname Script
            
            Sname is  the name  of the command to be added, which may be            Sname                                                       
            up eight characters long.
            
            Script is  the name  of the  script to  be invoked  when the            Script                                                      
            command is  encountered either  in a script or (more likely)
            when entered in command key mode.
            
            Both Sname  and Script  may be  either string  variables  or                 Sname      Script                                      
            string constants.
            
            The best  way to set up a list of commands to be added is to
            place  all   the  AddCommand   definitions  in  the  default
            PIBTERM.SCR which  will be automatically executed at startup
            time.
            
            If you  write a  command with  the same  name as an existing
            PibTerm script  command, then your version will override the                                                       will override    



            PibTerm Script Language Reference Guide              Page 12            PibTerm Script Language Reference Guide              Page 12


            built-in command.  You may still want access to the built-in
            command -- for example, if you're writing a spiffy front-end
            for a  built-in command.   To  request the  original command
            name, precede it by a '$'.                                  '$'.
            
            For example,  suppose you  write a  new RECEIVE command, but                                                    RECEIVE             
            you still want access to the original RECEIVE.  Then you can                                                  RECEIVE               
            write $RECEIVE  where you  want the  reference to  be to the                  $RECEIVE                                              
            original built-in RECEIVE command.                              RECEIVE         
            
            To illustrate how to add a command, suppose that you want to
            define an EMULATE command for PibTerm. Also suppose that the
            script containing the code to perform the EMULATE command is
            in the script file EMULATE.SCR.  Then you could write:                               EMULATE.SCR                        
            
                 AddCommand 'Emulate' 'Emulate.scr'
            
            Now if you enter a command like:
            
                 Emulate VT100
            
            then control  is passed  to 'Emulate.scr'  to  process  that
            input line.  When the  script gains control, all of the text
            following the  command name  'Emulate' itself is stored as a
            parameter line.   The contents of that parameter line can be
            accessed using  the ParamLine  command,  or  pieces  may  be
            broken  out   using  the   ParamCount  and  ParamStr  string
            functions.     ParamCount  and  ParamStr  operate  like  the
            standard Turbo  Pascal functions  of the  same name,  except
            that they  operate on the command line text, not the PibTerm
            parameter text:   ParamCount  counts the  number of  (blank-
            delimited) command line entries, and ParamStr(i) returns the
            ith command-line entry.
            
            To make  this  clearer,  here  is  the  text  for  a  sample
            EMULATE.SCR script:
            
                 *******************************************************************
                 *                                                                 *
                 *  Emulate.scr --- Command processor to set terminal emulation.   *
                 *                  Use ADDCOMMAND 'Emulate' 'Emulate.scr' to      *
                 *                  activate this function.                        *
                 *                                                                 *
                 *  Use:                                                           *
                 *                                                                 *
                 *    Emulate terminalname                                         *
                 *                                                                 *
                 *       terminalname -- name of terminal (e.g., VT100) to         *
                 *                       emulate.                                  *
                 *                                                                 *
                 *******************************************************************
                 *
                 Declare TermName String
                 *



            PibTerm Script Language Reference Guide              Page 13            PibTerm Script Language Reference Guide              Page 13


                 *   Pick up terminal name from command line text.
                 *
                 IF ( ParamCount > 0 ) THEN
                    Set TermName = UpperCase( ParamStr( 1 ) )
                 ELSE
                    Set TermName = ' '
                 ENDIF
                 *
                 *   Set terminal type depending upon name.
                 *
                 DOCASE TermName OF
                    CASE 'DUMB'
                       Message "Dumb terminal chosen."
                       SetParam   'te' '0'
                    ENDCASE
                    CASE 'VT52'
                       Message "VT52 terminal chosen."
                       SetParam   'te' '1'
                    ENDCASE
                    CASE 'ANSI'
                       Message "ANSI/BBS terminal chosen."
                       SetParam   'te' '2'
                    ENDCASE
                    CASE 'VT100'
                       Message "VT100 terminal chosen."
                       SetParam   'te' '3'
                    ENDCASE
                    CASE 'GOSSIP'
                       Message "Gossip mode chosen."
                       SetParam   'te' '4'
                    ENDCASE
                    CASE 'TEK4010'
                       Message "Tek 4010 terminal chosen."
                       SetParam   'te' '6'
                    ENDCASE
                    CASE 'ADM3A'
                       Message "ADM3a terminal chosen."
                       SetParam   'te' '7'
                    ENDCASE
                    CASE 'ADM5'
                       Message "ADM5 terminal chosen."
                       SetParam   'te' '8'
                    ENDCASE
                    CASE 'TV925'
                       Message "Televideo 925 terminal chosen."
                       SetParam   'te' '10'
                    ENDCASE
                    CASE ELSE
                       Message "Bogus terminal choice!"
                    ENDCASE
                 ENDDOCASE
            
            



            PibTerm Script Language Reference Guide              Page 14            PibTerm Script Language Reference Guide              Page 14


            AddLF -- Add Line Feeds            AddLF -- Add Line Feeds
            
            AddLF toggles  the addition  of a line feed to each carriage            AddLF                                                       
            return received from the remote system.  This is useful when
            accessing remote  systems that  expect a  carriage return to
            also act  as a  line feed.  Not many system do that anymore.
            However, occasionally  a  system  accessed  using  FTP  over
            ArpaNet doesn't  send the  <CR><LF> sequence,  just <CR>, so
            AddLF is a handy way to rectify that problem.
            
            
            Alarm -- Issues Five Beeps            Alarm -- Issues Five Beeps
            
            Alarm issues five beeps as long as mute mode is turned off.            Alarm                                                      
            
            
            Break -- Send Break            Break -- Send Break
            
            Break issues  a break  signal over  the communications port.            Break                                                       
            This is  exactly the same as hitting the <ALT>B.  The length
            of the break signal is controlled by the BL= parameter.
            
            
            Call -- Call Internal Script Procedure            Call -- Call Internal Script Procedure
            
            Call  invokes   an  internal  script  procedure.    See  the            Call                                                        
            Procedure command below for more details.            Procedure                                
            
            
            Capture -- Capture Session To Disk            Capture -- Capture Session To Disk
            
            Capture toggles  session capture  to a  specified file.  The            Capture                                                     
            syntax of the capture command is:
            
                 Capture Sname Scaptype
            
            Sname is the name of the file to capture to.            Sname                                       
            
            Scaptype indicates  the type  of capture  to  be  performed.            Scaptype                                                    
            "E" specifies   an  edited  capture  and  "U"  specifies  an
            unedited capture.  An edited  capture displays  the lines as
            they appear  on the  screen.   An  unedited  capture  writes
            characters as they arrive from the remote system.
            
            For example,  to initiate  edited session  capture  to  file
            "GETIT.DAT", use the script command:
            
                 Capture "GETIT.DAT" "E"
            
            If the  script variable  'Sname' contains  "GETIT.DAT",  you
            could also write:
            
                 Capture Sname "E"
            



            PibTerm Script Language Reference Guide              Page 15            PibTerm Script Language Reference Guide              Page 15


            To turn  off capture  later in  the same  script, just enter
            Capture with no argument:
            
                 Capture
            
            Be careful  -- if  you enter  Capture with no arguments, and
            you have  not previously  requested session  capturing, then
            PibTerm will  issue a  prompt for  the capture file name, if
            PibTerm is  running in  attended mode. The intent here is to
            provide flexibility  when running a script in attended mode;
            but if you're not careful, you may find an unattended script
            gets hung  up waiting  for the  capture file name entry.  In
            unattended mode, the spurious Capture is ignored.
            
            
            Case -- Case Selector For DoCase            Case -- Case Selector For DoCase
            
            Case marks  the start  of a  Case/EndCase block  in a DoCase            Case                                                        
            statement.   See the DoCase statement definition for further                                 DoCase                                 
            details.
            
            
            ChDir -- Change Current Directory or Drive            ChDir -- Change Current Directory or Drive
            
            ChDir changes  the current  logged directory  and/or  drive.            ChDir                                                       
            The syntax is:
            
                 CHDIR   Sdir
            
            Sdir is  either a string variable or constant containing the            Sdir                                                        
            name of the new directory, drive, or both in standard MS DOS
            directory format.
            
            Examples:
            
                 ChDir 'c:\modem'
                 Set mydir = 'b:\bogus'
                 ChDir mydir
            
                 ChDir 'b:'
                 Set mydrive = 'b:'
                 ChDir mydrive
            
            
            Clear -- Clear Screen            Clear -- Clear Screen
            
            Clear clears  the screen (except for the status line).  This            Clear                                                       
            is just like the <ALT>C keyboard command.
            
            



            PibTerm Script Language Reference Guide              Page 16            PibTerm Script Language Reference Guide              Page 16


            Close -- Close File            Close -- Close File
            
            Close closes  a file  opened using  the script  command Open            Close                                                   Open
            (see below).  The syntax is:
            
               CLOSE  Ifile
            
            IFile is the index of the file to be closed.            IFile                                       
            
                 *
                 Declare MyFile Integer
                 *
                 Close 1
                 Set Myfile = 3
                 Close Myfile
            
            
            ClrEol -- Clear Display To End Of Line            ClrEol -- Clear Display To End Of Line
            
            ClrEol clears  the display beginning with the current cursor            ClrEol                                                      
            position and  continuing to  the end  of  the  line  on  the
            screen.
            
            
            ComDrain -- Drain Serial Port Output Buffer            ComDrain -- Drain Serial Port Output Buffer
            
            ComDrain waits  a specified number of seconds for the serial            ComDrain                                                    
            port output buffer to empty.  The syntax is:
            
                 ComDrain IWaitSecs
            
            where "IWaitSecs"  is the  number of seconds to wait for the                   IWaitSecs                                            
            buffer to  become empty.   Execution of the script continues
            with the next statement when either the buffer is drained or
            the number of seconds to wait is exceeded.
            
            
            ComFlush -- Flush Serial Port Buffers            ComFlush -- Flush Serial Port Buffers
            
            ComFlush flushes  or drains  the serial  port  buffers.  The
            syntax is:
            
                 ComFlush Sflushtyp
            
            where "Sflushtyp"  is a  string constant  or variable  which                   Sflushtyp                                            
            indicates which serial port buffers are to be flushed:
            
                 'I'       Flush input buffer only
                 'O'       Flush output buffer only
                 'B'       Flush both buffers
            
            If no  Sflushtyp appears,  both the input and output buffers                   Sflushtyp                                            
            are flushed.
            



            PibTerm Script Language Reference Guide              Page 17            PibTerm Script Language Reference Guide              Page 17


            The input  buffer is  flushed by  throwing away  the current
            contents of  the buffer -- i.e., any character received from
            the remote  system but  not yet  processed by PibTerm -- and
            then waiting for the port to become briefly inactive.
            
            The output  buffer is  flushed by throwing away the contents
            of the  buffer, i.e.,  any characters  waiting to be sent to
            the remote system.
            
            
            CopyFile --- Copy File            CopyFile --- Copy File
            
            CopyFile copies one file (of any type) to another.  The copy            CopyFile                                                    
            proceeds byte-by-byte and is not limited to text files.  The
            syntax is:
            
                 COPYFILE  Sorig Scopy
            
            Sorig is the original file to be copied.            Sorig                                   
            Scopy is the resultant copy.            Scopy                       
            
            
            Delay -- Delay Execute for Specified Interval            Delay -- Delay Execute for Specified Interval
            
            Delay delays PibTerm execution for the number of tenths of a            Delay                                                       
            second specified by the argument.  The syntax is:
            
                 Delay Idelay
            
            For example,
            
                 Delay  10
            
            delays PibTerm  execution for one second (ten tenths = one).
            To delay execution for half a second, enter:
            
                 Delay 5
            
            If the  script variable  Delaytime contains  a 5,  then  you
            could write:
            
                 Declare DelayTime Integer
                 Set DelayTime = 5
                 Delay Delaytime
            
            to delay execution for half a second.
            
            Delay differs from the Suspend command described below.  The            Delay                  Suspend                              
            Suspend  command   only  halts  SCRIPT  processing  for  the
            specified  length   of  time.     Delay  halts  ALL  PibTerm
            processing (except  the asynchronous  reception of  incoming
            characters).
            
            



            PibTerm Script Language Reference Guide              Page 18            PibTerm Script Language Reference Guide              Page 18


            DelLine -- Delete Current Line On Screen            DelLine -- Delete Current Line On Screen
            
            DelLine deletes  the display line on which the cursor rests.            DelLine                                                     
            All lines  below the  deleted line  (except the status line)
            are scrolled up.
            
            
            Dial -- Dial A Number            Dial -- Dial A Number
            
            Dial dials  a number  in the PibTerm dialing directory, just            Dial                                                        
            like <ALT>D.  The number  to be dialed can be specified as a
            string variable or string constant. The syntax for Dial is:
            
                 DIAL    Sdial NOSCRIPT
            
            SDial specifies the entry to be dialed.            SDial                                  
            NOSCRIPT (written  without quote  marks) indicates  that the            NOSCRIPT                                                    
            automatic invocation  of the  associated dialing  script, if
            any, is to be suppressed.
            
            For example, to dial directory entry 3, use the command:
            
                 Dial "3"
            
            You can add the dialing prefix characters if you wish:
            
                 Dial "-3"
            
            You can  also request  a manual dial by prefixing the entire
            number with an M:
            
                 Dial "M1234567"
            
            If the  string variable  EntryNum contains "-3" then you can
            write:
            
                 Dial EntryNum
            
            If you  don't want  the associated  script for entry 3 to be
            invoked, then write:
            
                 Dial EntryNum NOSCRIPT
            
            
            DirFirst -- Find First Matching File            DirFirst -- Find First Matching File
            
            DirFirst, combined  with DirNext  (described below),  allows            DirFirst                 DirNext                            
            you to  search DOS  directories for  file names  matching  a
            wildcard specification.  The syntax of DirFirst is:
            
                 DirFirst Spec Srchattr Sname Sattr Sdate Stime Size
            



            PibTerm Script Language Reference Guide              Page 19            PibTerm Script Language Reference Guide              Page 19


            Spec is  a string  containing the wildcard specification for            Spec                                                        
            the search.   Only files matching this specification will be
            selected.  Here are some examples of legal wildcards:
            
                 *.*                 All files.
                 c:\bogus\*.pas      All  files  in  subdirectory  *.pas
                                     with the extension '.pas'.
                 myfile.dat               Only the file 'myfile.dat'.
                 
            
            Srchattr is  a string  which specifies which file attributes            Srchattr                                                    
            should be  searched for.   Only files matching the specified
            attributes will be selected.  Here are the various attribute
            letters and meanings:
            
                 A    Archive bit set
                 D    Directory
                 H    Hidden
                 N    Normal file
                 R    Read-only
                 S    System
                 V    Volume label
            
            You may  combine attributes.   Specifying  a null string for
            SrchAttr means  the same  thing  as  combining  ALL  of  the            SrchAttr                                                    
            attributes.  Here are some examples:
            
                 "N"  Select normal files only
                 "HS" Select hidden system files only
                 "V"  Select volume label only
                 ""   Select ALL files
            
            Refer to  your DOS  manual  for  details  about  these  file
            attributes.
            
            Sname gets  the name of the first file (if any) matching the            Sname                                                       
            given specification and attributes.  If no files match, then
            Sname will be an empty string.            Sname                         
            
            Sattr gets  the attributes  associated with  the file  as  a            Sattr                                                       
            string.   The attribute  string  is  composed  of  the  same
            letters described  above for  the Srchattr  parameter.  Note                                              Srchattr                  
            that there  may be  MORE attributes for a particular file in
            Sattr than in Srchattr.            Sattr         Srchattr 
            
            Sdate gets  the creation  date of the file as a string.  The            Sdate                                                       
            date  format  is  controlled  by  the  setting  of  the  DF=
            parameter (see the PibTerm Parameter Reference Manual).
            
            Stime gets  the creation  time of the file as a string.  The            Stime                                                       
            time format is controlled by the TF= parameter.
            
            Size gets the size of the file in bytes as a string.            Size                                                
            



            PibTerm Script Language Reference Guide              Page 20            PibTerm Script Language Reference Guide              Page 20


            Here is an example in which DirFirst is used to retrieve and
            display the  volume label  of the  current logged drive (DOS
            3.0 and above only):
            
            
                 Declare VolID String
                 Declare Drive String
                 Declare Dir String
                 Declare Attr String
                 Declare Date String
                 Declare Time String
                 Declare Size String
                 *
                 *                             Get current drive/dir
                 *
                 GetDir Drive Dir
                 *
                 *                             Append colon to drive
                 *
                 Set Drive = CONCAT( Drive , ':' )
                 *
                 *                             Look for volume label
                 *
                 DirFirst Drive "V" VolID Attr Date Time Size
                 *
                 *                             Display if found
                 *
                 IF ( VolID <> '' ) THEN
                      Set VolID = CONCAT( 'Volume: ', VolID )
                      Set VolID = CONCAT( CONCAT( VolID , '   Created: ' ), Date )
                      Set VolID = CONCAT( CONCAT( VolID , ' ' ), Time )
                      Writeln
                      Writeln VolID
                 ELSE
                      Writeln
                      Writeln "Volume label not found."
                 ENDIF
            
            
            DirNext -- Find Next Matching File            DirNext -- Find Next Matching File
            
            DirNext  returns   further   files   matching   a   wildcard            DirNext                                                     
            specification provided by a previously executed DirFirst.
            
            The syntax of DirNext is:
            
                 DirNext   Sname Sattr Sdate Stime Size
            
            where Sname  through Size  have the  same  meanings  as  for                  Sname          Size                                   
            DirFirst above.
            
            Here is  a script  which prompts for a file specification to
            be searched for, and then lists the matching files and sizes
            on the display:



            PibTerm Script Language Reference Guide              Page 21            PibTerm Script Language Reference Guide              Page 21


            
            *                                   Wildcard for files
             Declare FSpec String
            *                                   Attributes for search
             Declare FAttr String
            *                                   File name
             Declare FileName String
            *                                   File attributes
             Declare FileAttr String
            *                                   File creation date
             Declare FileDate String
            *                                   File creation time
             Declare FileTime String
            *                                   File size in bytes
             Declare FileSize String
            *                                   Report line
             Declare ReportLine String
            *                                   Counts files found
             Declare TotalFiles Integer
            *
            *                                   Get file spec to search for
            *
             Writeln
             Input "Enter file spec to search for: " FSpec
             Writeln
            *
            *                                   If file spec null, quit.
            *
             IF ( FSpec = '' ) THEN
                Exit
             ENDIF
            *
            *                                   Search for first file.
            *
             DirFirst FSpec "" FileName FileAttr FileDate FileTime FileSize
            *
            *                                   No first file -- report that
            *                                   and quit.
            *
             IF ( ( FileName = '' ) OR ( IOResult <> 0 ) ) THEN
                Writeln
                Writeln "No files found."
                Writeln
                Exit
             ENDIF
            *                                   Set files found to 0.
             Set TotalFiles = 0
            *
            *                                   Begin loop over rest of files.
            *
             WHILE ( LENGTH( FileName ) <> 0 ) DO
            *
            *                                   Increment file count
            *



            PibTerm Script Language Reference Guide              Page 22            PibTerm Script Language Reference Guide              Page 22


                Set TotalFiles = TotalFiles + 1
            *
            *                                   Display file stuff
            *
                Set FileName = CONCAT( FileName , DUPL( ' ' , 14 - LENGTH( FileName ) ) )
                Set FileSize = CONCAT( DUPL( ' ' , 12 - LENGTH( FileSize ) ) , FileSize )
                Set FileSize = CONCAT( FileSize , ' ' )
                Set FileDate = CONCAT( FileDate , ' ' )
                Set FileTime = CONCAT( FileTime , ' ' )
            *
                Set ReportLine = CONCAT( CONCAT( FileName , FileSize ), FileDate )
                Set ReportLine = CONCAT( CONCAT( ReportLine , FileTime ), FileAttr )
            *
                Writeln ReportLine
            *                                   Get next file
            *
                DirNext FileName FileAttr FileDate FileTime FileSize
            *
             ENDWHILE
            *                                   Display final count of files
            *
             Set ReportLine = CONCAT( 'Total files found: ', STRING( TotalFiles ) )
            *
             Writeln
             Writeln ReportLine
            
            
            DoCase -- Do Case Statement            DoCase -- Do Case Statement
            
            The DoCase  statement starts  a  multiway  selection  block.                DoCase                                                  
            The syntax of DoCase is as follows:
            
                 DOCASE var
                    CASE value1
                       ...
                    ENDCASE
                    CASE value2
                       ...
                    ENDCASE
                       ...
                    CASE ELSE
                       ...
                    ENDCASE
                 ENDDOCASE
            
            'var' can  be  either  an  integer  or  a  string  variable.
            'value1', 'value2',  etc. are the case-selection values.  If
            the value  of 'var'  matches one  of the  'value(n)' values,
            then  the   statements  following  that  CASE  value(n)  are
            executed.     CASE  ELSE  provides  a  means  for  executing
            statements if  the  value  of  'var'  matched  none  of  the
            'value(n)' values.
            



            PibTerm Script Language Reference Guide              Page 23            PibTerm Script Language Reference Guide              Page 23


            DoCase provides a convenient alternative to a long series of
            nested IF statements.
            
            Examples:
            
                 DECLARE  I  Integer
                 DECLARE  S  String
                  ...
                 DOCASE I
                    CASE 1
                      ...
                    ENDCASE
                    CASE 2
                      ...
                    ENDCASE
                    CASE 3
                      ...
                    ENDCASE
                    CASE ELSE
                      ...
                    ENDCASE
                 ENDDOCASE
            
                 DOCASE S
                    CASE 'VT100'
                      ...
                    ENDCASE
                    CASE 'VT52'
                      ...
                    ENDCASE
                    CASE 'ANSI'
                      ...
                    ENDCASE
                    CASE ELSE
                      ...
                    ENDCASE
                 ENDDOCASE
            
            For another  example, see  the definition of the EMULATE.SCR
            script in the description of the AddCommand command above.
            
            
            Dos -- Execute DOS Command            Dos -- Execute DOS Command
            
            Dos executes  a  specified  DOS  command  --  somewhat  like            Dos                                                         
            <ALT>J, but only for a single command.  The syntax is:
            
                 Dos Sdos
            
            Sdos specifies the DOS command to be executed.            Sdos                                          
            
            For example, to execute a DIR command, enter:
            
                 Dos "DIR"



            PibTerm Script Language Reference Guide              Page 24            PibTerm Script Language Reference Guide              Page 24


            
            If the  script variable  'Doscom' contains  'DIR' you  could
            write:
            
                 Dos Doscom
            
            To jump to a new copy of DOS, write:
            
                 Dos ""
            
            Dos automatically  returns to  PibTerm after  executing  the            Dos                                                         
            single  specified  MS  DOS  command,  unless  the  specified
            command is  null.  In that case, Dos  invokes a new level of                                             Dos                        
            the MS  DOS command  processor, and  you will  have to enter
            EXIT to return to PibTerm.  This is the same behavior as for
            the <ALT>J command.
            
            
            Echo -- Toggle Local Echo            Echo -- Toggle Local Echo
            
            Echo toggles  local echo  mode, just like the keyboard entry            Echo                                                        
            <ALT>E. In  local echo  mode, PibTerm displays characters as
            you type  them, and  doesn't wait  for the  remote system to
            echo them back.
            
            
            EditFile -- Invoke File Editor            EditFile -- Invoke File Editor
            
            EditFile invokes  the currently  defined editor specified by
            the EN=  parameter.   If the  value of EN= is null, then the
            built-in PibTerm  editor is  invoked.  Otherwise, the string
            specified as  the value of EN= is executed as a DOS command,
            after making  any required  file name  substitution (see the
            description of  the EN=  parameter in the "PibTerm Parameter
            Reference Manual" for details).
            
            The syntax of EditFile is:
            
                 EditFile  Sname
            
            Sname specifies the name of the file to be edited.            Sname                                             
            
            For example,  to invoke  the editor  for file "BOGUSCO.DAT",
            you could write:
            
                 EditFile "Bogusco.dat"
            
            
            Else -- Part Of IF Statement            Else -- Part Of IF Statement
            
            Else is described as part of the If command below.            Else                                              
            
            



            PibTerm Script Language Reference Guide              Page 25            PibTerm Script Language Reference Guide              Page 25


            EndCase -- Ends Case Block            EndCase -- Ends Case Block
            
            EndCase is described as part of the DoCase command above.            EndCase                                                  
            
            
            EndDoCase -- Ends DoCase Statement            EndDoCase -- Ends DoCase Statement
            
            EndDoCase is described as part of the DoCase command above.            EndDoCase                                                  
            
            
            EndIf -- Ends an IF Statement            EndIf -- Ends an IF Statement
            
            EndIf is described as part of the 'If' command below.            EndIf                                                
            
            
            EndProc -- Ends a Script Procedure            EndProc -- Ends a Script Procedure
            
            EndProc is described as part of the Procedure command below.            EndProc                                                     
            
            
            EndWhile -- Ends a WHILE Block            EndWhile -- Ends a WHILE Block
            
            EndWhile is  described as  part  of  the  'While'  statement            EndWhile                                                    
            below.
            
            
            EraseFile -- Erase (Delete) A File            EraseFile -- Erase (Delete) A File
            
            EraseFile erases (deletes) a file.  The syntax is:            EraseFile                                         
            
                 EraseFile Sname
            
            Sname specifies the name of the file to be erased.            Sname                                             
            
            For example,  to erase  the file  "BOGUSCO.DAT",  you  could
            write the following script command:
            
                 EraseFile "Bogusco.dat"
            
            This is equivalent to issuing the DOS command:
            
                 ERASE BOGUSCO.DAT
            
            
            Execute -- Execute One Script From Another            Execute -- Execute One Script From Another
            
            Scripts may  invoke  other  scripts.    The  Execute  script                                                         Execute        
            command provides the necessary mechanism.  The syntax of the
            Execute command is:
            
                 Execute Sname <Arguments>
            
            Sname is the name of the script to be invoked.            Sname                                         
            



            PibTerm Script Language Reference Guide              Page 26            PibTerm Script Language Reference Guide              Page 26


            <Arguments> is  a list  of variables  or constants  (but NOT            <Arguments                                                  
            expressions) to  be passed  as  arguments  to  the  executed
            script.   This is essentially the same format as for calling
            an internal  script procedure  (see Call), except that Sname                                                Call               Sname
            here refers to  an external script.
            
            Here is a script which invokes three other scripts:
            
                 DECLARE I Integer
                 DECLARE S String
                 DECLARE name String 'Other2'
                 ...
                 Message " "
                 Message "We will now invoke three scripts."
                 Message " "
                 Execute 'OTHER1' 23 'VT100' S
                 Execute name I
                 Execute 'OTHER3'
            
            The three scripts OTHER1, OTHER2, and OTHER3 will be invoked
            and executed.
            
            The TYPE  of the arguments passed is NOT CHECKED by PibTerm.
            If you  make a  mistake, you  may get  bizarre results.  The
            NUMBER of  arguments IS checked, and the invoked script will
            NOT  be  executed  if  the  wrong  number  of  arguments  is
            provided.
            
            Arguments are  passed to  a nested  script using  the Import                                                                  Import
            script statement.  See the definition of Import for details.
            
            The <ALT>X  command exits  one level  of script nesting at a
            time.  You may need to repeat it several times to get out of
            all the  scripts.  The script command Exitall will also take                                                  Exitall               
            you out of all scripts, regardless of nesting depth.
            
            Here is  an extended example of an executed script.  Suppose
            we want  to construct a script to prompt a remote caller and
            handle  sending   of  files.    The  script  will  take  two
            arguments, the  file name of the file(s) to be send, and the
            transfer protocol.  If either or both aren't specified, then
            the executed  script will  prompt for them.  We'll call this
            script SENDIT:
            
                 IMPORT  Filename String
                 IMPORT  Protocol String
                 *
                 DECLARE Temp     String
                 *
                 *        Check if file name provided.  Prompt if missing.
                 *
                       WHILE( LENGTH(FileName) = 0 ) DO
                          RInput  "Enter name of file to transfer: " Filename
                       ENDWHILE



            PibTerm Script Language Reference Guide              Page 27            PibTerm Script Language Reference Guide              Page 27


                 *
                 *        Check if file exists.  If not, quit.
                 *
                       IF ( NOT FILEEXISTS( Filename ) ) THEN
                          SET Temp = CONCAT( CONCAT( "The file ", Filename ), " does not exist.|")
                          SText Temp
                          Quit
                       ENDIF
                 *
                 *        Check if protocol provided.  Prompt if missing.
                 *
                       WHILE( LENGTH( Protocol ) = 0 ) DO
                          RInput  "Enter protocol to use:          " Protocol
                       ENDIF
                 *
                 *        Check if protocol is legitimate; send file if so.
                 *
                       IF POS( Protocol , 'X,XC,Y,YB,TE' ) > 0 THEN
                          Send Filename Protocol
                       ELSE
                          SText   "Invalid protocol name.|"
                       ENDIF
                 
            We could invoke this script as:
                 
                      SENDIT  '' ''
            
            This would prompt the remote caller for the file name and
            transfer type.
            
            
            Exit -- Terminate Script Execution            Exit -- Terminate Script Execution
            
            Exit  terminates   execution  of   the  script.      PibTerm            Exit                                                        
            automatically inserts an Exit at the end of a script, so you                                     Exit                               
            need not  provide it  there.   Exit is  most useful when you
            want to  stop script  execution somewhere in the middle of a
            script.
            
            Exit only  stops the current script.  If you are in a nested
            script, control is returned to the invoking script.  To exit
            all scripts, use the ExitAll command instead.
            
            Note that terminating a script does NOT terminate processing
            of any defined 'When' string.  See the section on the 'When'
            script command below for further details.
            
            
            ExitAll -- Exit Nested Scripts            ExitAll -- Exit Nested Scripts
            
            ExitAll stops  executing the  current script,  regardless of            ExitAll                                                     
            the nesting  depth.    All  higher-level  scripts  are  also
            stopped.
            



            PibTerm Script Language Reference Guide              Page 28            PibTerm Script Language Reference Guide              Page 28


            
            For -- Start FOR Loop            For -- Start FOR Loop
            
            A For loop has the form:              For                   
            
                 FOR index = start-expression TO     end-expression DO
                     ...
                     other statements
                     ...
                 ENDFOR
                                   -or-
            
                 FOR index = start-expression DOWNTO end-expression DO
                     ...
                     other statements
                     ...
                 ENDFOR
            
            'index' is  an integer  variable name;    'start-expression'
            gives the  initial loop  value;   'end-expression' gives the
            final loop value. 'TO' specifies an ascending loop; 'DOWNTO'
            specifies a descending loop. The increment is always 1.
            
            Examples:
            
               DECLARE I Integer
                  ...
            
               FOR I = 1 TO 10 DO
                  ...
               ENDFOR
            
               FOR I = 10 DOWNTO 1 DO
                  ...
               ENDFOR
            
               FOR I := ( J * 10 - I ) TO ( K - 32 ) DO
                  ...
               ENDFOR
            
            
            FreeSpace -- Find Free Space On Drive            FreeSpace -- Find Free Space On Drive
            
            FreeSpace finds the number of bytes of space which are still            FreeSpace                                                   
            unused on a drive.  The syntax is:
            
                 FreeSpace Sdrive Sfree
            
            Sdrive specifies  the drive  for which  the  free  space  is            Sdrive                                                      
            desired.
            
            Sfree gets the free space as a string.            Sfree                                 
            



            PibTerm Script Language Reference Guide              Page 29            PibTerm Script Language Reference Guide              Page 29


            For example,  to find  the number  of free bytes on drive C:
            write:
            
                 Declare Size String
                 FreeSpace "C:" Size
                 Writeln Size
            
            
            GetDir -- Get Current Directory And Drive            GetDir -- Get Current Directory And Drive
            
            GetDir retrieves  the currently  logged  drive  and  MS  DOS            GetDir                                                      
            subdirectory.  The syntax is:
            
                 GETDIR  Sdrive Sdir
            
            Sdrive is a string variable which receives the current drive            Sdrive                                                      
            letter (without a trailing colon).
            
            Sdir  is  a  string  variable  which  receives  the  current            Sdir                                                        
            subdirectory, without initial or trailing slashes.
            
            Example:
            
            Suppose  that   the  current  path  is  "c:\bogus".    After
            executing the following script statements:
            
                 Declare drive string
                 Declare drive dir
                 GetDir drive dir
            
            The resulting values are:
            
                 drive     contains C                 drive               
                 dir       contains BOGUS                 dir                     
            
            
            GetParam -- Get Value of PibTerm Parameter            GetParam -- Get Value of PibTerm Parameter
            
            GetParam retrieves  the current value of a PibTerm parameter            GetParam                                                    
            variable.  The syntax is:
            
               GetParam  Spname  Svalue
            
            Spname is  the two-character  name of  the parameter  to  be            Spname                                                      
            retrieved.   Spname can  be  either  a  string  variable  or
            constant.
            
            Svalue is  the current value of that parameter.  Svalue must            Svalue                                                      
            be a string variable.
            
            See the  "PibTerm Parameters Reference Guide" for a complete
            list of the parameter names and types.
            



            PibTerm Script Language Reference Guide              Page 30            PibTerm Script Language Reference Guide              Page 30


            Parameters whose values are integers are converted to string
            form for  storage in  Svalue.   Parameters whose  values are                                  Svalue                                
            boolean are  converted to "1" for a true value and "0" for a
            false value.
            
            Requesting a  non-existent parameter  name results in Svalue                                                                  Svalue
            being set to an empty string.
            
            To avoid  excessive code overlay swaps, try to keep a series
            of GetParam statements together in your script.
            
            Example:
            
            Suppose that  the current baud rate is 2400; that PibTerm is
            NOT  set   for  hard-wired   access;  and   that  the  modem
            initialization string  is "ATZ".   Then  after executing the
            following script statements:
            
            *
                 Declare ModemInit String
                 Declare BaudRate  String
                 Declare HardWired String
                 Declare PName     String
                 *
                 *          Get modem initialization string (string)
                 *
                 GetParam  'mi' ModemInit
                 *
                 *          Get baud rate (integer variable)
                 *
                 Set       PName  = 'ba'
                 GetParam  PName BaudRate
                 *
                 *          Get hardwired status
                 *
                 GetParam  'hw' HardWired
            
            the resulting values are (all strings):
            
                 ModemInit      ATZ
                 BaudRate       2400
                 HardWired      0
            
            
            GetVar -- Get Value of Script Variable            GetVar -- Get Value of Script Variable
            
            GetVar retrieves  the current  value of a script variable by            GetVar                                                      
            name.  The syntax is:
            
                 GetVar Sname Stype Svalue
            
            Sname is the name of the variable whose value is wanted.            Sname                                                   
            



            PibTerm Script Language Reference Guide              Page 31            PibTerm Script Language Reference Guide              Page 31


            Stype  returns   the  type   ("INTEGER",  "STRING")  of  the            Stype                                                       
            variable.
            
            Svalue returns  the current value of the variable, converted            Svalue                                                      
            to a string value if necessary. The most current instance of
            the variable  name is  returned.   That means  in  a  nested
            script or  script procedure,  the value from the most recent
            definition of the variable is used.
            
            If the  given variable  name  doesn't  exist,  the  type  is
            returned as  "UNDEFINED" and  the value  is returned  as  an
            empty string.
            
            GetVar is  useful when  you  don't  know  the  name  of  the
            variable for  which you  want a  value until  the script  is
            being executed.   If  you do  know the name of the variable,
            you should  use the  Set  command  instead,  which  is  more                                 Set                                    
            efficient.
            
            As an  example, suppose  that the  variable VARA is a string                                                        VARA            
            variable with  the current  value "bogus value".  Then after
            executing the following script statements:
            
                 Declare vtype string
                 Declare vval  string
                 Declare vname string
                      ...
                 GetVar 'VARA' vtype vval
                 SET vname = 'VARA'
                 GetVar vname vtype vval
            
            the resulting values are:
            
                 vname     VARA
                 vtype     STRING
                 vval      bogus value
            
            
            GoToXY -- Move To Specified Screen Position            GoToXY -- Move To Specified Screen Position
            
            GoToXY positions the cursor to a specified row and column on            GoToXY                                                      
            the screen.  The syntax is:
            
                 GoToXY IX IY
            
            IX is  the new  column position,  and  IY  is  the  new  row            IX                                     IY                   
            position.
            
            Examples:
            
            
                 *
                 *                Move to column 1, row 12
                 *



            PibTerm Script Language Reference Guide              Page 32            PibTerm Script Language Reference Guide              Page 32


                 GoToXY  1 12
                 *
                 *                Move to column 2, row 23
                 *
                 Set I1 = 2
                 Set I2 = 23
                 GoToXY  I1 I2
                 
            
            
            Hangup -- Hang Up The Phone            Hangup -- Hang Up The Phone
            
            Hangup hangs  up the  phone, just  like the  keyboard  entry            Hangup                                                      
            <ALT>H.
            
            
            Host -- Enter Host Mode            Host -- Enter Host Mode
            
            Host causes  PibTerm to  enter  Host  mode,  just  like  the            Host                                                        
            keyboard command  <ALT>W.   In this mode PibTerm acts like a
            mini-BBS (bulletin  board system).  Remote callers  can dial
            your system and transfers files and leave messages.  See the
            section on  PibTerm host  mode in the "PibTerm User's Guide"
            for more details.
            
            
            If -- Conditionally Execute Statements            If -- Conditionally Execute Statements
            
            If allows  testing of  several different types of conditions            If                                                          
            and conditionally  executing  a  block  of  statements.  The
            general form of the 'If' statement in PibTerm is:
            
               IF  ( condition ) THEN
                 < script statements executed if condition is TRUE >
               ELSE
                 < script statements executed of condition is FALSE >
               ENDIF
            
            The Else  part is  optional and  need not be specified.  You                Else                                                    
            MUST specify  the Endif.   IF statements can be nested up to                              Endif                                     
            64 levels deep.
            
            The "( condition )" must be an expression which evaluates to
            either zero  (false) or  non-zero (true).    Basically,  the
            "condition" is  of the  form "v1  OP v2" where v1 and v2 are                                                           v1     v2    
            script variables  or  functions,  and  OP  is  a  relational                                                   OP                   
            operator. The  available functions  are described  under the
            Set command below. The available relational operators are:            Set                                                       
            
                 =, <, >, <>, <=, >=, NOT, AND, OR, XOR
            
            Examples:
            
                 IF ( a = b ) THEN



            PibTerm Script Language Reference Guide              Page 33            PibTerm Script Language Reference Guide              Page 33


                      ...
                 ENDIF
            
                 IF ( a <> 'Where''s the beef?' ) THEN
                 ...
                 ENDIF
            
                 IF ( c <= 25 ) THEN
                 ...
                 ENDIF
            
                 IF ( NOT ( a = b ) ) THEN
                 ...
                 ENDIF
            
            Compound conditions are allowed, for example:
            
                 IF ( ( a = b ) AND ( NOT CONNECTED ) ) THEN
                 ...
                 ENDIF
            
            String  comparisons   use  the  ASCII  character  set  as  a
            collating sequence.
            
            These same conditional expressions can be used in all of the
            other conditional commands like WHILE, UNTIL, and so on.
            
            
            Import -- Import Variable To Executed Script            Import -- Import Variable To Executed Script
            
            A script invoked using the Execute script statement needs to                                       Execute                          
            indicate which  variables are  being passed  to it.  This is
            done using the IMPORT command, which has the syntax:
            
                 Import varname type
            
            Imported variables may be used just like Declared variables.
            You can  also Declare  variables which  will be local to the
            Executed script.            Execute         
            
            Here is the same main script as given in the Execute command
            description:
            
                 DECLARE I Integer
                 DECLARE S String
                 DECLARE name String 'Other2'
                 ...
                 Message " "
                 Message "We will now invoke three scripts."
                 Message " "
                 Execute 'OTHER1' 23 'VT100' S
                 Execute name I
                 Execute 'OTHER3'
            



            PibTerm Script Language Reference Guide              Page 34            PibTerm Script Language Reference Guide              Page 34


            
            The first three statements of script OTHER1 above might look
            like this:
            
                 IMPORT N        Integer
                 IMPORT TermType String
                 IMPORT Message  String
                    ...
                 
            
            The Import statements connect the variables N, TermType, and
            Message in  the script OTHER1 with the variables passed from
            the main  script, which may have quite different names.  For
            example:
            
                 Execute 'other1' 23 'vt100' S
                 
            results in the following matchups:
            
                 N         <-- 23
                 TermType  <-- 'VT100'
                 Message   <-- S
            
            As with internal script procedures, you may alter the values
            of IMPORTed  variables and the new values ARE passed back to
            the invoking  script IF  the  corresponding  argument  is  a
            variable.   Changes in  constants are NOT passed back to the
            invoking script.
            
            
            Input -- Get Input From Keyboard            Input -- Get Input From Keyboard
            
            Input prompts  for and  reads characters  from the keyboard.            Input                                                       
            The syntax is:
            
                 Input Sprompt Sinput
            
            Sprompt contains  the prompt  string, which  may be the null            Sprompt                                                     
            string, in which case no prompt is issued.
            
            Sinput  receives   the  characters  typed  up  to  (but  not            Sinput                                                      
            including) the terminating carriage return.
            



            PibTerm Script Language Reference Guide              Page 35            PibTerm Script Language Reference Guide              Page 35


            Example:
            
                 *
                 *           Read letter into variable answer
                 *
                 Declare answer string
                 Declare prompt string
                 *
                 Input 'Enter letter: ' answer
                 *
                 *           Read letter into variable answer.
                 *
                 Set prompt = 'Enter letter: '
                 Input prompt answer
            
            
            InsLine -- Insert Line At Cursor            InsLine -- Insert Line At Cursor
            
            InsLine inserts  a blank  line in  the display following the            InsLine                                                     
            line on  which the  cursor  rests.    All  lines  below  the
            inserted line  (except the  status line)  are scrolled down,
            and the last line is scrolled off the screen.
            
            
            Key -- Set Function Key Values            Key -- Set Function Key Values
            
            Key reads  function keys  from a  specified file,  like  the            Key                                                         
            <ALT>K keyboard  entry "Read  definitions from  a file". The
            syntax is:
            
                 Key Skeyfile
            
            Skeyfile is  the name  of the  file containing  the keyboard            Skeyfile                                                    
            definitions.
            
            Example:
            
            In the following script segment:
            
                 *
                 *          Read keyboard definition from file "mydefs.fnc"
                 *
                 Declare KeyFile String
                 *
                 Key "mydefs"
                 *
                 Set KeyFile = "mydefs"
                 Key KeyFile
                 *
                 Set KeyFile = "mydefs.fnc"
                 Key KeyFile



            PibTerm Script Language Reference Guide              Page 36            PibTerm Script Language Reference Guide              Page 36


                 
                 
            all three  Key statements  read key  definitions  from  file                       Key                                              
            "mydefs.fnc" -- the ".fnc" is understood.
                 
            
            KeyDef -- Define Function Key Value            KeyDef -- Define Function Key Value
            
            KeyDef defines a string to be sent to the remote system when            KeyDef                                                      
            a function  key is struck.  This is like the <ALT>K "D)efine
            key" command. The syntax is:
            
                 KeyDef Skeyname Skeytext
            
            Skeyname is the name of the key to be defined.            Skeyname                                      
            
            Skeytext is the text string to be assigned to the key.            Skeytext                                              
            
            The following key names are used with KeyDef:
            
                 F1 through F12 (for function key F1 through F12)                 F1         F12                                  
                 A1 through A12 (for <ALT>F1 though <ALT>F12);                 A1         A12                               
                 C1 through C12 (for <CTRL>F1 through <CTRL>F12);                 C1         C12                                  
                 S1 through S12 (for <SHIFT>F1 through <SHIFT>F12).                 S1         S12                                    
            
                 N1 through N0  (for <ALT>1 through <ALT>0 on top row                 N1         N0                                       
                                of the keyboard);
                 N-             (for <ALT>- on the top keyboard row)                 N-                                                 
                 N+             (for <ALT>+ on the top keyboard row)                 N+                                                 
            
                 K0 through K9  (for keypad 0 through 9)                 K0         K9                          
                 K.             (for keypad . or DEL key)                 K.                                      
                 K+             (for keypad + )                 K+                            
                 K-             (for keypad - )                 K-                            
                 K*             (for keypad * )                 K*                            
                 K/             (for keypad / )                 K/                            
                 KE             (for keypad enter)                 KE                               
                 AK versions    (for <ALT>keypad 0 through 9, etc.)                 AK                                                
                 CK versions    (for <CTRL>keypad 0 through 9, etc.)                 CK                                                 
            
                 PS             (for PrtSc)                 PS                        
                 APS            (for <ALT>PrtSc)                 APS                            
                 CPS            (for <CTRL>PrtSc)                 CPS                             
            
                 AEN            (for <ALT>Enter)                 AEN                            
            
                 BS             (for Backspace)                 BS                            
                 CBS            (for <CTRL>Backspace)                 CBS                                 
                 ABS            (for <ALT>BackSpace)                 ABS                                
            
                 XU             (for separate cursor pad up arrow)                 XU                                               
                 XD             (for separate cursor pad down arrow)                 XD                                                 
                 XL             (for separate cursor pad left arrow)                 XL                                                 
                 XR             (for separate cursor pad right arrow)                 XR                                                  



            PibTerm Script Language Reference Guide              Page 37            PibTerm Script Language Reference Guide              Page 37


                 AX versions    (for <ALT>separate cursor pad keys)                 AX                                                
                 CX versions    (for <CTRL>separate cursor pad keys)                 CX                                                 
            
                 XI             (for separate position pad Insert)                 XI                                               
                 XH             (for separate position pad Home)                 XH                                             
                 XPU            (for separate position pad PageUp)                 XPU                                              
                 XDE            (for separate position pad Delete)                 XDE                                              
                 XE             (for separate position pad End)                 XE                                            
                 XPD            (for separate position pad PageDown)                 XPD                                                
                 AX versions    (for <ALT>separate position pad keys)                 AX                                                  
                 CX versions    (for <CTRL>separate position pad keys)                 CX                                                   
            
            Not all  keys exist  on all  keyboards.   However,  you  can
            always assign  values to keys that don't exist on individual
            keyboards anyway.
            
            Examples:
            
                 *
                 Declare KeyName String
                 Declare KeyDef  String
                 *
                 Key 'F1' 'DIR *.*|'
                 *
                 Set KeyName = 'F1'
                 Set KeyDef  = 'DIR *.*|'
                 KeyDef Keyname KeyDef
                 KeyDef 'F1' Keydef
                 KeyDef KeyName 'DIR *.*|'
            
            
            KeyFlush -- Flush Keyboard            KeyFlush -- Flush Keyboard
            
            KeyFlush flushes all pending characters from the keyboard.            KeyFlush                                                  
            
            
            KeySend -- Send Function Key Value To Remote            KeySend -- Send Function Key Value To Remote
            
            KeySend sends  the specified  key's definition to the remote            KeySend                                                     
            system.  The syntax is:
            
                 KeySend Skeyname
            
            Skeyname provides  the name  of the  key to  be sent.    The            Skeyname                                                    
            allowed values  for Skeyname  are the same as for the KeyDef                                Skeyname                          KeyDef
            command above.
            
            Example:
            
                 *           Send the text associated with function key F1
                 *           to the remote system
                 *
                 KeySend "F1"
            



            PibTerm Script Language Reference Guide              Page 38            PibTerm Script Language Reference Guide              Page 38


            
            Log -- Toggle Printer Logging            Log -- Toggle Printer Logging
            
            Log toggles  session logging  on printer,  like the keyboard            Log                                                         
            entry <ALT>L.  You should ensure that your printer is turned
            on before  using <ALT>L.  When logging  is active,  all  the
            output from the remote system is echoed on your printer.
            
            
            Menu -- Display Pop-Up Menu            Menu -- Display Pop-Up Menu
            
            Menu displays  a pop-up  menu on the screen similar to those            Menu                                                        
            used internally by PibTerm.  The syntax is:
            
                 MENU Ires Irow Icol Ideflt Stitle Sitem1 Sitem2 ...
            
            Ires is  the index of the menu item chosen (or -1 if the ESC            Ires                                                     ESC
            key it struck).
            
            Irow and Icol indicate the position to display the top left-            Irow and Icol                                               
            hand corner  of the  position menu.   Irow  and Icol  may be                                                  Irow      Icol        
            either integer variables or constants.
            
            Ideflt is  the index of the default choice and may be either            Ideflt                                                      
            an integer variable or constant.
            
            Stitle is the menu title and may be either a string variable            Stitle                                                      
            or constant.
            
            Sitem1, Sitem2,  etc. provide  the text  for the  menu  line            Sitem1, Sitem2                                              
            entries and may be either string variables or constants.
            
            The resulting menu is displayed over the current contents of
            the screen. The keypad arrow keys/mouse/first character of a
            menu item  can be used to choose a value from the menu, just
            like with standard PibTerm menus.
            
            Example:
            
            Here is  a menu definition which requests that a pop-up menu
            with the  title "Select  baud rate"  be placed  at  position
            (column=10, row=11)  on the  screen.   There are to be three
            possible values,  300, 1200,  and  2400.    2400  is  to  be
            highlighted as the default value.
            
                 Declare MyBaud Integer
                 Menu MyBaud 10 11 3 "Select baud rate: " "300" "1200" "2400"
            
            If the  returned value  of MyBaud is 1, then 300 was chosen;
            if MyBaud  is 2,  then 1200  was chosen; if MyBaud is 3 then
            2400 was chosen.  If MyBaud is <= 0, then no choice was made
            (the ESC key was hit).
            
            



            PibTerm Script Language Reference Guide              Page 39            PibTerm Script Language Reference Guide              Page 39


            Message -- Display Message On Screen            Message -- Display Message On Screen
            
            Message displays text on the screen.  The syntax is:            Message                                             
            
                 Message String
            
            where String  is the  text to  be displayed.   String may be                  String                                   String       
            either a string variable or string constant.
            
            The text is NOT sent to the remote system.
            
            Example:
            
                 Message "Here is a sample message."
            
            The message  text cannot  span more than a single line.  You
            may enter as many 'Message' statements in a row as you want,
            if you wish to have more than one line of text appear.
            
            There is  an important difference in the function of Message                                                                 Message
            and Writeln  0.   Message passes  the characters through the                Writeln  0    Message                                   
            current terminal  emulator display mechanism, so that escape
            sequences will  be processed.    This  allows  you  to  take
            advantage of  interesting effects possible when using escape
            sequences.   Writeln 0  writes the characters to the display                         Writeln 0                                      
            directly,  without   regard  for   the  particular  terminal
            emulation  begin   used.    Escape  sequences  will  not  be                                                                 not    
            processed.
            
            
            Mute -- Toggle Mute Mode            Mute -- Toggle Mute Mode
            
            Mute toggles  mute mode, like the keyboard entry <ALT>M.  In            Mute                                                        
            mute mode,  no sounds  like bells or music are issued.  This
            is ideal  for those late-night sessions when you want to log
            in to  those remote systems that play the entire top 40 rock
            hits before  they allow  you to do anything useful, and also
            for those  systems which  beep at  you  every  time  you  do
            ANYTHING at all.
            
            
            Open -- Open File            Open -- Open File
            
            Open make a text file accessible for processing in a script.            Open                                                        
            The syntax is:
            
                 Open Ifile Sname Stype
            
            Ifile is  the "handle"  (1 through 10) to be assigned to the            Ifile                                                       
            file, and may be either an integer variable or constant.
            
            Sname is  the name of the file (which may include a complete            Sname                                                       
            DOS path).
            



            PibTerm Script Language Reference Guide              Page 40            PibTerm Script Language Reference Guide              Page 40


            Stype provides the access method for the file:            Stype                                         
            
                 'I'  Input          File to be read
                 'O'  Output    File to written/overwritten
                 'A'  Append    File to be added to at end of file
            
            A file  opened  with  OPEN  should  be  closed  with  CLOSE.                                  OPEN                            CLOSE 
            All opened  files are  automatically  closed  when  the  top
            script level  is exited.   Files  ARE global  across  nested
            scripts.
            
            A handle  of 0 is reserved for keyboard/screen input/output.
            You need not (and cannot) explicitly open handle 0.
            
            To read  from a  file, use  the  script  commands  Read  and                                                               Read     
            Readln.  To write to a file, use Write and Writeln.  See the            Readln                           Write     Writeln          
            definitions of  those  commands  for  details.    To  switch
            between reading  and writing  a file,  you need to CLOSE the                                                               CLOSE    
            file and re-open it.
            
            Examples:
            
                 *
                 Declare handle   integer
                 Declare filename string
                 Declare opentype string
                 *
                 Open 1 'bogus.txt' 'input'
                 *
                 Set handle = 2
                 Set filename = 'c:\mybogus\bogus2.txt'
                 Set opentype = 'output'
                 *
                 Open handle filename opentype
                 
            
            Param -- Set Program Parameter            Param -- Set Program Parameter
            
            Param sets  Pibterm program  parameters.  The syntax follows            Param                                                       
            that used  in the  PIBTERM.CNF file.   You  specify the two-
            letter name  of the parameter to change, then an equal sign,
            and then  the value  to be  assigned to that parameter.  The
            parameter names  and values  are described  in the  "PibTerm
            Parameters Reference Guide."
            
            Param is  an old  script command,  left over  from  previous            Param                                                       
            PibTerm versions,  and  included  for  compatibility.    You
            should use the SetParam command instead in new scripts.                           SetParam                                
            
            For example, to change the terminal emulation to VT100 mode,
            write:
            
                 Param te=3
            



            PibTerm Script Language Reference Guide              Page 41            PibTerm Script Language Reference Guide              Page 41


            To change the baud rate to 1200 baud, write:
            
                 Param ba=1200
            
            
            PrintFile -- Print A File            PrintFile -- Print A File
            
            PrintFile starts  printing a specified file using the built-            PrintFile                                                   
            in PibTerm  print spooler.   PibTerm   overlaps the printing
            with other  duties like reading keyboard input or displaying
            output received from the remote system.
            
            The syntax for PrintFile is:
            
                 PrintFile Sname
            
            Sname specifies the name of the file to be printed.            Sname                                              
            
            To start printing a file called "BOGUSCO.LIS", write:
            
                 PrintFile "Bogusco.lis"
            
            To  stop  the  print  operation  before  the  file  finishes
            printing, write:
            
                 PrintFile ""
            
            
            Procedure -- Define Script Procedure            Procedure -- Define Script Procedure
            
            Procedure marks the start of an internal script procedure. A            Procedure                                                   
            script procedure  is like  a script within a script. You can
            declare an internal script procedure as follows:
            
                 PROCEDURE name args
                      -- statements ---
                 ENDPROC
            
            Here name  is the  name of the procedure, and args is a list                 name                                     args          
            of arguments  and types  for the procedure.  A procedure may
            reference any  variables previously  defined by higher level
            procedures or  the main  script as  well  as  the  variables
            defined by its arguments. Local variables -- declared within
            the procedure -- are also allowed.
            
            A procedure definition must precede its first use.
            
            The EndProc  acts as  a return.  You may also explicitly use                EndProc                                                 
            the Return statement.                Return           
            
            You invoke a procedure using the CALL statement:                                             CALL           
            
                 Call name arguments
            



            PibTerm Script Language Reference Guide              Page 42            PibTerm Script Language Reference Guide              Page 42


            Here name  is the  name of  the procedure, and arguments are                 name                                      arguments    
            the procedure  arguments.   The arguments must match in type
            and number  with those  declared on  the  PROCEDURE  command                                                      PROCEDURE         
            defining the  called procedure.  (If not,  a syntax error is
            reported.)  The arguments may be variables or constants, but
            NOT expressions.     Arguments which  ARE variables  may  be
            changed in  the called procedures if desired. Constants will
            NOT be  changed, even  if an assignment to the corresponding
            procedure argument is made in the body of the procedure.
            
            IT IS  EXTREMELY IMPORTANT  TO DECLARE  ALL GLOBAL VARIABLES            IT IS  EXTREMELY IMPORTANT  TO DECLARE  ALL GLOBAL VARIABLES
            BEFORE  DEFINING   ANY  PROCEDURES,   whether  or   not  the            BEFORE  DEFINING   ANY  PROCEDURES,                         
            procedures use variables. Likewise, all IMPORTs must precede
            any procedure definitions.
            
            Here is  a sample  script with  two procedures,  neither  of
            which takes an argument:
            
                 *
                 *   Here is the first procedure.
                 *
                 PROCEDURE One
                    Message " "
                    Message "Script ONE was called."
                    Message " "
                 ENDPROC
                 *
                 *   Here is the second procedure.
                 *
                 PROCEDURE Two
                    Message " "
                    Message "Script TWO was called."
                    Message " "
                 ENDPROC
                 *
                 *   Begin "mainline" script.  This is where script execution
                 *   actually begins.
                 *
                 Call One
                 Call Two
                 
            Here is  a sample script with procedures with sub-procedures
            and arguments:
            
                 Declare A String
                 Declare B Integer
                 Declare S String
                 *
                 PROCEDURE Sub1 Mya String, MyB Integer
                 *
                 Declare MyC String
                 *
                    PROCEDURE Sub1a Mya String
                       Message "Entered procedure Sub1a"



            PibTerm Script Language Reference Guide              Page 43            PibTerm Script Language Reference Guide              Page 43


                       Set MyC = CONCAT( CONCAT( 'Value of A = <', MyA ), '>' )
                       Message MyC
                       Set MyA = 'BOGUS A!!!!!'
                    ENDPROC
                 *
                    PROCEDURE Sub2a MyB Integer
                       Set MyC = CONCAT( 'Value of B = ', String( MyB ) )
                       Message MyC
                    ENDPROC
                 *
                    Call Sub1a Mya
                    Call Sub2a Myb
                 *
                 *
                 ENDPROC
                 *
                 PROCEDURE Sub2 MyB Integer
                 *
                    Declare MyC String
                 *
                    Message "Entered script Sub2"
                    Set MyC = CONCAT( 'Value of B = ', String( MyB ) )
                    Message MyC
                 *
                    Set MyB = 10
                 *
                 ENDPROC
                 *
                 PROCEDURE Sub3 MyA String
                 *
                    Declare MyC String
                 *
                    Message "Entered script Sub3"
                    Set MyC = CONCAT( CONCAT( 'Value of A = <', MyA ), '>' )
                    Message MyC
                 *
                 ENDPROC
                 *==============================================================
                 *                   M A I N   P R O G R A M                   *
                 *==============================================================
                 *
                 Set A = 'Here is parameter A'
                 Set B = 50
                 *
                 Set S = CONCAT( CONCAT( 'A:<' , A ), '>' )
                 Message S
                 *
                 Set S = CONCAT( CONCAT( 'B:<' , STRING( B ) ), '>' )
                 Message S
                 *
                 Message A
                 Message "Calling procedure Sub1 ..."
                 *
                 Call sub1 A B



            PibTerm Script Language Reference Guide              Page 44            PibTerm Script Language Reference Guide              Page 44


                 *
                 Message "Back to main"
                 Set S = CONCAT( CONCAT( 'New value of A is <', A ), '>' )
                 Message S
                 *
                 Message "Calling procedure Sub2 ..."
                 *
                 Call sub2 B
                 *
                 Message "Back to main"
                 Set S = CONCAT( 'New value of B is ', String( B ) )
                 Message S
                 *
                 Message "Calling procedure Sub3 ..."
                 *
                 Call sub3 A
                 *
                 Message "Back to main"
                 
            
            Procedure Sub1a  above changes  the value  of MyA,  which in                      Sub1a                               MyA           
            turn changes  the value  of variable  A in  the main  script                                                  A                     
            body.  What if the call to Sub1 had been                                       Sub1         
            
                 Call sub1 'Hi there!' B
            
            instead?  Would the value of 'Hi there!' somehow be changed?
            
            No, PibTerm  recognizes that  a request to change a constant
            has been  made and IGNORES it.  The change WILL be in effect
            during the  lifetime of Sub1/Sub1a, but the changed value is
            NOT passed back to the main script body.
            
            
            Quit -- Quit PibTerm execution            Quit -- Quit PibTerm execution
            
            
            Quit terminates  execution of  PibTerm and  returns to  DOS.            Quit                                                        
            The effect  of Quit is similar to typing <ALT>X, except that                           Quit                                         
            all current  scripts are  exited, and  no prompt  is  issued
            asking if execution should actually be terminated.
            
            Quit is  useful in writing scripts for unattended operation,            Quit                                                        
            so that  PibTerm can  be invoked  as one  command in a batch
            file, and  then the batch file can continue after PibTerm is
            exited.
            
            
            Read -- Read Characters From A File            Read -- Read Characters From A File
            
            Read reads characters from a file which has been opened with            Read                                                        
            the Open script command.  The syntax is:                Open                                
            
                 READ Ifile Sdata Ichars



            PibTerm Script Language Reference Guide              Page 45            PibTerm Script Language Reference Guide              Page 45


            
            Ifile is the file handle for the file from the Open command.            Ifile                                                       
            Ichars provides the number of characters to be read.            Ichars                                              
            Sdata is the string of characters as read from the file.            Sdata                                                   
            
            Both Ifile  and Ichars can be integer variables.  Sdata must                 Ifile      Ichars                            Sdata     
            be a string variable.
            
            The file  must have  been opened  for input;  see  the  Open                                                                    Open
            command for details.
            
            You can  specify file  handle 0  -- or  omit the file handle
            altogether -- to read from the keyboard.
            
            You can test for end-of-file using the EOF function (see the                                                   EOF                  
            description  in  the  Set  command).  End-of-file  is  never                                  Set                                   
            returned for the keyboard.
            
            You can test for an I/O error using the IOResult function                                                    IOResult         
            (see the Set command for details).                     Set                      
            
            
            Example:
            
                 Declare mychars string
                 *                         Open the file
                 Open 1 "myfile.dat" "I"
                 *                         Read ten characters from file
                 READ 1 mychars 10
                 *                         Check for an error
                 *
                 IF ( IOResult <> 0 ) THEN
                    Message "I/O error reading handle 1"
                 ENDIF
            
            Another example:
            
            Suppose you want to read one character from the keyboard
            without requiring that a carriage return be entered
            afterwards.  That can be done by writing a read statement
            for one character as follows:
            
                 *
                 Declare Ch String
                 *
                 Read Ch 1
            
            
            Readln -- Read Line From File            Readln -- Read Line From File
            
            Readln reads  a line  of text  from a file previously opened            Readln                                                      
            using the Open script command. The syntax is:                      Open                               
            
                 READLN Ifile Sdata



            PibTerm Script Language Reference Guide              Page 46            PibTerm Script Language Reference Guide              Page 46


            
            Ifile is the file handle to read from.            Ifile                                 
            Sdata stores  the characters read from the file, and must be            Sdata                                                       
            a string  variable. If  no characters  are  read,  Sdata  is                                                               Sdata    
            returned as an empty string.
            
            A line  is defined  as a  series of  up to to 255 character,
            terminated by  Ascii characters  ^M^J (carriage  return  and
            line feed).   The terminating ^M^J characters are not stored
            as part of the string S1.
            
            The file  must have  been opened  for input;  see  the  Open
            command for details.
            
            You can  specify file  handle 0  -- or  omit the file handle
            altogether -- to read from the keyboard.
            
            You can test for end-of-file using the EOF function (see the                                                   EOF                  
            description  in  the  Set  command).  End-of-file  is  never                                  Set                                   
            returned for the keyboard.
            
            You can  test for  an I/O  error using the IOResult function                                                       IOResult         
            (see the Set command for details).                     Set                      
            
            Example:
            
            
                 Declare mychars string
                 *                         Open the file
                 Open 1 "myfile.dat" "I"
                 *                         Read line from file
                 READLN 1 mychars
                 *                         Check for an error
                 *
                 IF ( IOResult <> 0 ) THEN
                    Message "I/O error reading handle 1"
                 ENDIF
            
            
            Receive -- Receive File From Remote System            Receive -- Receive File From Remote System
            
            Receive is used to receive a file from a remote system, like            Receive                                                     
            the keyboard command <ALT>R.  The syntax is:
            
                 Receive Sname Sprotocol
            
            Sname is  the name  of the  file to  be received.    It  may            Sname                                                       
            contain a wildcard specification for batch protocols.
            
            Sprotocol contains the abbreviation for the protocol name to            Sprotocol                                                   
            be used for the transfer.
            
            The protocol names are:
            



            PibTerm Script Language Reference Guide              Page 47            PibTerm Script Language Reference Guide              Page 47


                 AS   --   Ascii
                 XK   --   Xmodem CheckSum
                 XC   --   Xmodem CRC
                 X1   --   Xmodem 1K
                 XG   --   Xmodem 1K G
                 YB   --   Ymodem Batch
                 YG   --   Ymodem G Batch
                 TE   --   Telink
                 MK   --   Modem7 Batch Checksum
                 M7   --   Modem7 Batch CRC
                 KE   --   Kermit
            
            If you  have added  any user-defined  protocols, then  their
            abbreviations  can   also  be   used.     For  example,  you
            customarily use ZM as an abbreviation for Zmodem.                            ZM                               
            
            To receive the file YUMYUM.PAS using Xmodem 1K, write:
            
                 Receive "yumyum.pas" "X1"
            
            To receive a batch of files using Ymodem, write:
            
                 Receive "" "YB"
            
            The file names are automatically provided by the sender with
            Ymodem, so  you don't  have to  specify  the  name  --  just
            provide a  null filename  as shown above.  This is generally
            true of other batch protocols as well.
            
            Note that  "Receive" only  sets up PibTerm to receive a file
            - it  does NOT  initiate a  transfer from the remote system.
            You will need to issue a command to the remote system to get
            it to  start a  transfer so  that Pibterm  can  receive  the
            file(s).   For example,  if you  are connected  to the  file
            section of  an RBBS  system, you  might enter  the following
            sequence of statements to download a file you know you want:
            
                 *
                 *     Request that file "goodstuf.lbr" be sent to me.
                 *
                 Stext "s;goodstuf.lbr;x|"
                 Receive "goodstuf.lbr" x
                 
            
            There  are   a  number  of  remote  Kermit  server  commands
            implemented, available  from the  Kermit receive  file menu.
            You can  also indicate that you want a remote server command
            in a  script, by  requesting a Kermit download and using '/'
            followed by the text of the remote server command.
            
            Examples:
            
                 *
                 *                          Send FINISH command to server



            PibTerm Script Language Reference Guide              Page 48            PibTerm Script Language Reference Guide              Page 48


                 *
                 Receive '/FINISH'    "Ke"
                 *
                 *                          Send "display directory" command
                 *
                 Receive '/DIRECTORY' "Ke"
                 *
                 *                          Send "type file BOGUS" command
                 *
                 Receive '/TYPE BOGUS' "Ke"
                 *
                 *                          Send "change directory" command
                 *
                 Receive '/CWD Sys$login' "Ke"
            
            It may  seem backwards to use RECEIVE rather than SEND here,
            but it  turns out to be more convenient, since the output of
            these commands  is sent  to PibTerm as file (to be displayed
            on the screen) using the Kermit protocol.
            
            
            Redial -- Redial Last Number Dialed            Redial -- Redial Last Number Dialed
            
            Redial redials  the last  phone  number  entered,  like  the            Redial                                                      
            keyboard command  <ALT>Q.   However, you can specify a phone
            number in  quotes on  the 'Redial'  command and PibTerm will
            redial that  phone number until a connection is established.
            For example,  to repeatedly  dial phone  directory  entry  3
            until a connection is established, write:
            
               Redial "3"
            
            
            Repeat -- Repeat Block Of Statements            Repeat -- Repeat Block Of Statements
            
            Repeat  begins  a  block  of  statements  to  be  repeatedly            Repeat                                                      
            executed until  the condition  on a matching UNTIL statement
            is true.
            
            Examples:
            
            Here is  a loop  which sends a carriage return to the remote
            system once every two seconds and looks to see if the string
            "Username:" has arrived.  The loop exits when "Username:" is
            found.
                 
                 Repeat
                    Stext '|'
                    Waitstring "Username:" 2
                 Until ( WaitFound )
            
            
            Here is a "repeat forever" loop that will never complete:
            



            PibTerm Script Language Reference Guide              Page 49            PibTerm Script Language Reference Guide              Page 49


                 Repeat
                      .    
                      .
                 Until ( 0 )
                                          
            You can  stop such  a loop  from  the  keyboard  by  hitting
            <ALT>X, or  by using the Exit/ExitAll script commands inside                                     Exit/ExitAll                       
            the Repeat/Until loop.
            
            Other testable  conditions  are  described  under  the  "If"
            statement above.
            
            
            Reset -- Reset Script Execute To Start Of Script            Reset -- Reset Script Execute To Start Of Script
            
            Reset starts executing the current script from the beginning            Reset                                                       
            of the script again.  Reset has no arguments.
            
            
            RInput -- Receive Input From Remote System            RInput -- Receive Input From Remote System
            
            RInput prompts for input from the remote system.  The syntax            RInput                                                      
            is:
            
                 RInput Sprompt Secho Sanswer
            
            Sprompt is  the prompt  string, which  will be  sent to  the            Sprompt                                                     
            remote  system   as  an   indication  that  input  is  being
            requested.  The prompt string can be empty, in which case no
            prompt to the remote system will be issued.
            
            Secho indicates  if the  remote system's response characters            Secho                                                       
            are to  be echoed by the actual character value or a '.' for
            security purposes.
            
            Sanswer is  the response from the remote system, and must be            Sanswer                                                     
            specified as a string variable.
            
            Setting Sechor  = 'Echo'  causes the actual character values                    Sechor                                              
            received from the remote system to be echoed.  Setting Secho                                                                   Secho
            = 'Noecho'  causes '.'  to be  used to  echo each character.
            This is useful when echoing passwords.
            
            Examples:
            



            PibTerm Script Language Reference Guide              Page 50            PibTerm Script Language Reference Guide              Page 50


                 *                 Read response from remote system into
                 *                 variable, echoing the characters as
                 *                 sent.
                 
                 Declare Response String
                 Declare Prompt   String
                 Declare Echo     String
                 *
                 RInput 'Enter letter: ' 'ECHO' Response
                 *
                 *                 Now read response and echo using '.'s.
                 *
                 Set Prompt = 'Enter letter: '
                 Set Echo   = 'NOECHO'
                 RInput Prompt Echo Response
            
            
            ScreenDump -- Dump Screen To File            ScreenDump -- Dump Screen To File
            
            ScreenDump writes the current screen contents (text only) to            ScreenDump                                                  
            a file, like the <ALT>U keyboard command.  The syntax is:
            
                 SCREENDUMP Sname
            
            Sname contains the file name to receive the screen dump.            Sname                                                   
            
            Examples:
            
                 Declare DumpFile String
                 ScreenDump 'bozo.dat'
                 Set DumpFile = 'bozo.dat'
                 ScreenDump DumpFile
            
            
            Send -- Send File To Remote System            Send -- Send File To Remote System
            
            Send sends  a file  to a  remote system,  like the  keyboard            Send                                                        
            command <ALT>S.  The syntax is:
            
                 Send Sname Sprotocol
            
            Sname is  the name  of the  file to  be sent,  and can  be a            Sname                                                       
            wildcard specification for batch protocol transfers.
            
            Sprotocol is  the protocol  abbreviation.   (See the Receive            Sprotocol                                            Receive
            command for a list of protocol abbreviations.)
            
            For example,  to send  the file  "yumyum.lbr"  to  a  remote
            system using Xmodem-CRC, write:
            
                 Send "yumyum.lbr" "xc"
            
            To send  all files  ending in  .PAS using Telink to a remote
            system, write:



            PibTerm Script Language Reference Guide              Page 51            PibTerm Script Language Reference Guide              Page 51


            
                 Send "*.pas" "te"
            
            'Send' only  causes PibTerm  to begin  sending files  to the
            remote system.   You  must have  previously  instructed  the
            remote system  to be  ready  to  receive  the  files.    For
            example, if you are connected to the file section of an RBBS
            system, you  could send  the file  "yumyum.lbr" using Xmodem
            with the commands:
            
                 SText "r;yumyum.lbr;x|"
                 Suspend 400
                 Send "yumyum.lbr" "x"
            
            The Suspend  is included  to ensure  we don't start the send                Suspend                                                 
            procedure before RBBS is ready.
            
            Kermit transfers  are particularly easy if the remote system
            can run  Kermit in  server mode.   Just  run Kermit  on  the
            remote system,  put it  into server  mode,  and  issue  Send
            commands to  your heart's  content.   For example, to send a
            bunch of files to a Vax system running Kermit under VMS, you
            could write:
            
                 *
                 *     Wait for VMS command prompt
                 *
                  WaitString "$"
                 *
                 *     Start up Kermit
                 *
                  SText "Kermit|"
                 *
                 *     Wait for Kermit's prompt, then send command
                 *     to put Kermit in server mode.
                 *
                  Waitstring ">"
                  SText "Server|"
                 *
                 *     Wait for blurb about server mode to go by, then
                 *     send a bunch of files, then receive a file.
                 *
                  Suspend 500
                  Send "*.pas" "ke"
                  Send "*.doc" "ke"
                 *
                  Receive "newstuf.doc" "ke"
                 *
                 *     Take remote Kermit out of server mode.
                 *
                  Receive "/finish" "ke"
                 *
                 *     Tell remote Kermit to stop executing.
                 *



            PibTerm Script Language Reference Guide              Page 52            PibTerm Script Language Reference Guide              Page 52


                  SText "exit|"
                 
            
            
            Set -- Assign Value To Script Variable            Set -- Assign Value To Script Variable
            
            The Set  command may  be used  to assign  values  to  script                Set                                                     
            variables. The Set command has the form:
            
                 Set varname = expression
            
            where 'varname'  is the  name of the variable to be set, and
            'expression' is the value.
            
            You may  omit Set  if you  like, since  a script line of the                          Set                                           
            form
                 
                 varname = expression
            
            is assumed to be a Set statement.                               Set           
            
            The allowable expressions are:
            
            1.   a string  constant enclosed  in  quotes  for  a  string
                 variable, e.g.,
            
                      SET Abc = 'Here''s a string'
            
            2.   an integer constant for an integer variable, e.g.,
            
                      SET c = 123
            
            3.   another variable
            
                      SET Abc = Yum
            
            4.   a special function, which may be one of the following:
            
                 ATTENDED            returns a value of 1 if the session                 ATTENDED                                               
                                     is in  attended mode (AM=1) or 0 if
                                     the session  is in  unattended mode
                                     (AM=0).
                 
                 CHR( n )            returns   a    1-character   string                 CHR( n )                                               
                                     containing  the   Ascii   character
                                     whose ordinal is given by 'n'.  For
                                     example, CHR(65)  = 'A'.  If 'n' is
                                     not in  the range  0  through  255,
                                     then a null string is returned.
                 
                 CONCAT( s1 , s2 )   concatenates strings 's1' and 's2'.                 CONCAT( s1 , s2 )                                      
                 



            PibTerm Script Language Reference Guide              Page 53            PibTerm Script Language Reference Guide              Page 53


                 CONNECTED           returns a  value of  1 if  a remote                 CONNECTED                                              
                                     connection has  been made or 0 if a
                                     remote connection doesn't exist.
                 
                 DUPL( S1, n )       returns string with first character                 DUPL( S1, n )                                          
                                     in S1 duplicated n times.
                 
                 DATE                returns  date   as  a   string   in                 DATE                                                   
                                     YY/MM/DD format.
                 
                 DIALED              returns the dialing entry number if                 DIALED                                                 
                                     this script was executed because it
                                     was attached to a dialing directory
                                     entry, or 0 (or -1) otherwise.
                 
                 DIALENTRY( n )      returns the  n-th dialing directory                 DIALENTRY( n )                                         
                                     entry as a string.  This string can
                                     be  broken  up  into  fields  using
                                     other string  functions. The format
                                     of   the   dialing   directory   is
                                     described in  the PibTerm parameter
                                     reference guide.    If  an  invalid
                                     entry  number   is  given,  a  null
                                     string is returned.
                 
                 ENHKEYBD            returns 1  if an  enhanced  101-key                 ENHKEYBD                                               
                                     keyboard is in use, 0 otherwise.
                 
                 EOF( I1 )           returns  1   if  file  attached  to                 EOF( I1 )                                              
                                     handle specified by I1 is at end of
                                     file,  0   otherwise.     (See  the
                                     description  below   of  the   OPEN
                                     script command for details.)
                 
                 FILEEXISTS( S1 )    returns a  value of  1 if  the file                 FILEEXISTS( S1 )                                       
                                     named in  'S1' exists, or '0' if it
                                     doesn't exist.
                 
                 INDEX( s1 , s2 )    position of  string 's1'  in string                 INDEX( s1 , s2 )                                       
                                     's2' or zero if not found
                 
                 IORESULT            returns system  code from  last I/O                 IORESULT                                               
                                     operation.       Should   be   used
                                     following READ,  WRITE, OPEN,  etc.
                                     commands to check whether operation
                                     proceeded properly.  0 always means
                                     operation completely successfully.
                 
                 KEYSTRING( s )      returns  the  function  key  string                 KEYSTRING( s )                                         
                                     attached to  the key name specified
                                     by the  value  of  "s".    See  the
                                     description of  the  KeyDef  script
                                     command for legitimate names to use
                                     in "s".



            PibTerm Script Language Reference Guide              Page 54            PibTerm Script Language Reference Guide              Page 54


                 
                 LENGTH( s )         current length  of string  variable                 LENGTH( s )                                            
                                     's'.
                 
                 LTRIM( S1 )         trims leading  blanks  from  string                 LTRIM( S1 )                                            
                                     S1.
                 
                 NUMBER( s1 , n )    if  's1'   can  be   converted   to                 NUMBER( s1 , n )                                       
                                     integer, then  the  integer  value,
                                     else zero.   If  the conversion was
                                     done,  N   is  0,  else  N  is  the
                                     character position  in  's1'  which
                                     caused the conversion to fail.
                 
                 ORD( s1, n )        returns the  Ascii ordinal  of  the                 ORD( s1, n )                                           
                                     nth character  in  the  string  s1.
                                     For example,  ORD( 'A', 1 ) returns
                                     65.   If 'n'  is  less  than  1  or
                                     greater than  the length of 's1', 0
                                     is returned.
                 
                 PARAMLINE           returns  current   parameter   line                 PARAMLINE                                              
                                     contents (for  use  when  executing
                                     script tied to added user command).
                 
                 PARAMCOUNT          returns number  of  blank-delimited                 PARAMCOUNT                                             
                                     parameters  appearing   in  current
                                     parameter   line   (as   given   by
                                     PARAMLINE).
                 
                 PARAMSTR( I1 )      returns I1-th  parameter in current                 PARAMSTR( I1 )                                         
                                     parameter   line   (as   given   by
                                     PARAMLINE).
                 
                 READCTRL( s1 )      reads  a   string  containing   the                 READCTRL( s1 )                                         
                                     special control  character  markers
                                     used for  function key definitions,
                                     with each  instance of  the  marked
                                     characters  converted   to   actual
                                     control characters.   For  example,
                                     "ReadCtrl( ^C )" where "^C" are the
                                     two ascii  characters with ordinals
                                     94 and  67,  is  converted  to  the
                                     single control  character  ^C  with                                                                ^C      
                                     ascii ordinal 3.
                 
                 STRING( n )         value  of   integer   constant   or                 STRING( n )                                            
                                     variable 'n' converted to string
                 
                 SUBSTR( s1, b, l )  substring of  's1' for  length 'l',                 SUBSTR( s1, b, l )                                     
                                     starting at position 'n'.
                 
                 TIME                returns time  of day as a string in                 TIME                                                   
                                     24 hour HH:MM:SS format.



            PibTerm Script Language Reference Guide              Page 55            PibTerm Script Language Reference Guide              Page 55


                 
                 TRIM( S1 )          trims trailing  blanks from  string                 TRIM( S1 )                                             
                                     S1.
                 
                 UPPERCASE( S1 )     returns  contents   of   S1   after                 UPPERCASE( S1 )                                        
                                     converting  lower-case   to   upper
                                     case.
                 
                 WAITFOUND           returns 1  if preceding  WAITSTRING                 WAITFOUND                                              
                                     or WAITLIST  was  successful,  else
                                     returns 0.
                 
                 WRITECTRL( s1 )     returns  a   string  in  which  any                 WRITECTRL( s1 )                                        
                                     instances  in   's1'   of   control
                                     characters  are  converted  to  '^'
                                     prefix form, etc.
                 
            5.   A complex  expression containing  variables, constants,
                 operators, parentheses, and function calls.
            
            Note that  no SET  statement can  exceed one input line. You
            can break  up complicated  expressions into  a series of SET
            statements if you need to.
            
            A short example:
            
                 DECLARE a String
                 DECLARE b String
                 DECLARE c Integer
                 DECLARE d Integer
                 SET a = 'HERE IS A LINE OF TEXT WITH 123 in it'
                 SET d = POS( '1' , a )
                 SET b = Substr( a, d, 3 )
                 SET c = NUMBER( b , d )
                 
            At this point, the value of 'c' is 123.
            
            The last four lines could also be written:
            
                 SET a = 'HERE IS A LINE OF TEXT WITH 123 in it'
                 SET c = NUMBER( Substr( a, d, 3 ) , POS( '1' , a ) )
            
            Here is a more complicated arithmetic assignment:
            
                 SET c = ( ( c * 24 ) / D ) + 13
            
            
            SetParam -- Set Value Of PibTerm Parameter            SetParam -- Set Value Of PibTerm Parameter
            
            SetParam sets  a PibTerm parameter to a specified value. The
            syntax is:
            
                 SetParam  Spname  Spval
            



            PibTerm Script Language Reference Guide              Page 56            PibTerm Script Language Reference Guide              Page 56


            Spname is the name of the parameter.            Spname                              
            Spval is the new parameter value.            Spval                            
            
            If a  PibTerm parameter is of boolean type, enter "1" to set
            the parameter  value to  True, or enter "0" to set the value
            to False.  (See the "Parameter Language Reference Manual" to
            determine the type for each PibTerm parameter.)
            
            To increase  the efficiency  of processing  several SetParam
            statements, try  to place  them one right after the other if
            possible.  This avoids extra code module swaps during script
            execution.
            
            Examples:
            
            
                 Declare Name String
                 Declare Rate String
                 Declare True String
                 *                           Set terminal type to VT100
                 SetParam "te" "3"
                 
                 *                           Change baud rate to 1200
                 Set Rate = "1200"
                 Set Name = "ba"
                 SetParam name rate
                 *
                 *                           Set hardwired mode
                 *
                 Set True = "1"
                 SetParam "hw" True
            
            
            SetVar -- Set Value of PibTerm Parameter            SetVar -- Set Value of PibTerm Parameter
            
            
            SetVar sets  the  most  recent  instantiation  of  a  script            SetVar                                                      
            variable to a specified value.  The syntax is:
            
                 SETVAR Svname Sval
            
            Svname provides the name of the variable to be set.            Svname                                             
            Sval is the new value for the variable.            Sval                                   
            
            SetVar has  a different  purpose than  the Set command.  The                                                       Set              
            Set command  is translated  into internal code at the time a
            script is  compiled.    You  cannot  therefore  use  Set  to
            reference a  variable whose  name you  don't know  until the
            script is  being executed.   With  SetVar, you  can assign a
            value to  a variable  whose name  you don't  know until  the
            execution time  of the  script. Note  that  SetVar  is  MUCH
            slower than using a Set command;  use Set if possible. Also,



            PibTerm Script Language Reference Guide              Page 57            PibTerm Script Language Reference Guide              Page 57


            SetVar doesn't allow an expression as a value, although this
            isn't a real problem: you can use a Set command to build the
            value of the Sval parameter to SetVar.                         Sval                     
            
            Examples:
            
                 Declare vtype string
                 Declare vval  string
                 Declare vname string
                 Declare I     Integer
                 ...
                 SetVar 'VARA' 'Hi there'
                 SET vname = 'VARA'
                 SET vval  = 'Hi there'
                 SetVar vname vval
                 SetVar 'I' '10'
                 
            
            SText -- Send Text To Remote System            SText -- Send Text To Remote System
            
            SText sends text to the remote system. The syntax is:            SText                                                
            
                 SText String
            
            String contains the text to be sent.            String                              
            
            The special  characters used  in function  keys for carriage
            returns, marking  control characters, and delays may be used
            in SText  as well.   (See the section on the <ALT>K keyboard
            command in  the PibTerm  Guide for  details on these special
            characters.)
            
            You've already  seen a number of examples of SText in action
            in the description of other commands.
            
            
            Suspend -- Suspend Execution Of Script            Suspend -- Suspend Execution Of Script
            
            Suspend suspends script execution for a given length of time            Suspend                                                     
            (PibTerm continues executing).  The syntax is:
            
                 Suspend Itime
            
            Itime is  the length  of time  in hundredths  of a second to            Itime                                                       
            suspend the script execution.
            
            For example,  to stop  script  processing  for  one  second,
            enter:
            
                 Suspend 100
            
            To stop script processing for half a second, enter:
            
                 Suspend 50



            PibTerm Script Language Reference Guide              Page 58            PibTerm Script Language Reference Guide              Page 58


            
            Suspend differs  from the Delay script command in that Delay                                      Delay                             
            stops EVERYTHING  except the reception of remote characters,
            while Suspend  only stops  the execution of script commands.
            Note,  however,  that  WaitString  and  When  searches  will
            continue during  the suspension  period.  That makes Suspend
            useful in writing conditional loops with recalcitrant remote
            systems that may require a variable number of, say, carriage
            returns before the remote system wakes up.
            
            
            Text -- Send Text To Remote System            Text -- Send Text To Remote System
            
            Text sends  text to  the remote  system, WITHOUT any special            Text                                                        
            interpretation (e.g., unlike SText).  The syntax is:
            
                 Text String
            
            String provides  the text to be sent.  No special processing            String                                                      
            is performed on the text, unlike the SText command.
            
            
            Translate -- Read In Translate Table            Translate -- Read In Translate Table
            
            Translate reads  in a  translation table  from a  file, just            Translate                                                   
            like the "read file" option of <ALT>T.  The syntax is:
            
                 Translate Sname
            
            Sname is  the file  name from  which to read the translation            Sname                                                       
            table.
            
            For example,  to read  a table  from the file "Striphi.tra",
            write:
            
                 Translate "striphi"
            
            The ".tra" is assumed.
            
            
            Until -- End Repeat Block            Until -- End Repeat Block
            
            See the Repeat statement above.                    Repeat                 
            
            
            ViewFile -- Invoke File Viewer            ViewFile -- Invoke File Viewer
            
            ViewFile invokes  the  file  viewer  specified  by  the  LN=
            parameter.   If the  value of LN= is null, then the built-in
            PibTerm file  viewer is  invoked.    Otherwise,  the  string
            specified as  the value of LN= is executed as a DOS command,
            after making  any required  file name  substitution (see the



            PibTerm Script Language Reference Guide              Page 59            PibTerm Script Language Reference Guide              Page 59


            description of  the LN=  parameter in the "PibTerm Parameter
            Reference Manual" for details).
            
            The syntax of ViewFile is:
            
                 ViewFile  Sname
            
            Sname specifies the name of the file to be viewed.            Sname                                             
            
            For  example,   to  invoke   the   viewer   for   the   file
            "BOGUSCO.DAT", you could write:
            
                 ViewFile "Bogusco.dat"
            
            
            Wait -- Wait For Time Of Day            Wait -- Wait For Time Of Day
            
            Wait stops PibTerm execution until a given time (in HH:MM:SS            Wait                                                        
            form) is  reached, at  which time  execution proceeds.   The
            syntax is:
            
                 Wait Stime
            
            Stime provides the time to wait for in HH:MM:SS format.
            
            For example, to stop PibTerm execution until 1 AM, write:
            
                 Wait "01:00:00"
            
            The wait command only works within a given 24 hour period.
            
            
            WaitCount -- Wait For Number Of Characters            WaitCount -- Wait For Number Of Characters
            
            WaitCount causes PibTerm to wait until a specified count of
            characters has arrived from the remote system, regardless of
            what characters they are.  The syntax is:
            
                 WAITCOUNT Icount
            
            Icount is the number of characters to wait for.            Icount                                         
            
            Note that  NUL characters  (Ascii  0)  are  NOT  counted  if                       NUL                                              
            received.
            
            Example:
            



            PibTerm Script Language Reference Guide              Page 60            PibTerm Script Language Reference Guide              Page 60


                 *                   Wait for 5 characters to be received
                 Declare count integer
                 *
                 Set count = 5
                 *
                 WaitCount 5
                 WaitCount count
            
            
            WaitList -- Wait For List Of Strings            WaitList -- Wait For List Of Strings
            
            WaitList waits  for any  of up  to twenty  strings to appear            WaitList                                                    
            from the remote system.  The syntax is:
            
                 WaitList Index Swait1 Swait2 Swait3 ...
            
            Index is  the index  of the  string found.  Index must be an            Index                                       Index           
            integer variable.   If  none of  the strings  is found, then
            Index is returned as 0.            Index                  
            
            Swait1, Swait2,  etc. are  the strings  to be waited for.  I            Swait1, Swait2                                              
            must be an integer variable.
            
            If Index  is returned  as 0,  then none  of the  strings was               Index                                                    
            found in  the wait  time.   The wait  time is  set using the
            WaitTime command (which see).            WaitTime                     
            
            The WaitFound  function (see  the Set  command) can  also be                WaitFound                     Set                       
            used to  determine if  any of  the strings was found, but it
            doesn't indicate which.
            
            WaitList is  similar  to  WaitString,  but  WaitString  only                                      WaitString                        
            allows one  string to  be waited  on.   However,  WaitString
            executes faster than a WaitList with one string specified.
            
            Example:
            
                  Declare Index Integer
                  Declare Str1 'CONNECT'
                  Declare Str2 'NO CARRIER'
                  Declare Str3 'BUSY'
                  WaitList Index Str1 Str2 Str3 'VOICE'
                  IF ( Index > 0 ) THEN
                 *
                 *            process string found
                 *
                              ...
                  ELSE
                 *
                 *            process string not found
                 *
                              ...
                  ENDIF
            



            PibTerm Script Language Reference Guide              Page 61            PibTerm Script Language Reference Guide              Page 61


            
            WaitQuiet -- Wait For Quiet Line            WaitQuiet -- Wait For Quiet Line
            
            WaitQuiet waits until the communications line has been
            "quiet" -- no characters have been received -- for a
            specified length of time.  The syntax is:
            
                 WAITQUIET Itime
            
            Itime specifies the number of tenths of a second to wait for            Itime                                                       
            the communications line to be quiet.
            
            Example:
            
                 *                Wait for 1/2 (5/10) second for quiet line
                 *
                  Declare Time Integer
                 *
                  Set Time = 5
                 *
                  WaitQuiet 5
                  WaitQuiet Time
            
            
            WaitString -- Wait For String From Remote            WaitString -- Wait For String From Remote
            
            WaitString causes  Pibterm to  wait for  a given  string  to            WaitString                                                  
            appear from the remote system. The syntax is:
            
                 WaitString Swait Itime
            
            Swait is the string to be waited on.            Swait                               
            
            Itime is  the number  of seconds  to wait  for the string to            Itime                                                       
            appear.   If Itime  is not  specified, then the current wait                         Itime                                          
            time is  whatever was  specified  by  a  preceding  WaitTime                                                                WaitTime
            command.   If no previous WaitTime command was given, then a
            wait time of 30 seconds is used.
            
            If the  string does  not appear  within the  specified  time
            period,  then   execution  proceeds  with  the  next  script
            command.   WaitString can be combined with the Repeat/Until,
            While/EndWhile, and  If/Else/Endif script statements to good
            effect, since  the WaitFound (see the Set command) condition                               WaitFound          Set                   
            is TRUE  (=1) if  the specified  string appeared,  and FALSE
            (=0) if it didn't appear.
            
            To wait until the string 'Username:' appears, write:
            
                 WaitString 'Username:'
            
            PibTerm waits  30 seconds for 'Username:' to appear.  If you
            want it to wait for, say 60 seconds, write:
            



            PibTerm Script Language Reference Guide              Page 62            PibTerm Script Language Reference Guide              Page 62


                 WaitString 'Username:' 60
            
            You can wait for a single character:
            
                 WaitString ">"
            
            WaitString slows  down PibTerm's  execution somewhat, so you            WaitString                                                  
            should not be surprised if the output from the remote system
            is displayed more slowly than usual.
            
            
            WaitTime -- Set Wait Time            WaitTime -- Set Wait Time
            
            
            WaitTime  specifies   the  time   allotted  for   successful            WaitTime                                                    
            completion of  a WaitString  or WaitList  command.   (For an
            individual WaitString,  this time  can be  overridden on the
            WaitString command itself.) The syntax is:
            
                 WAITTIME Itime
            
            Itime is  the time  in seconds  to wait.   30 seconds is the            Itime                                                       
            default wait time.
            
            Examples:
            
                 Declare waiting Integer
                 WaitTime 25
                 Set waiting = 40
                 WaitTime waiting
            
            
            When -- Wait For String And Respond            When -- Wait For String And Respond
            
            When waits  for a  given string  to appear  from the  remote            When                                                        
            system --  like WaitString  -- and  then sends  a  specified
            response string.   The syntax is:
            
                 When Swait Ssend
            
            Swait is  the string  to wait for, and Ssend is the response            Swait                                  Ssend                
            string.   Both may  be either  string  constants  or  string
            variables.
            
            When searching  stays active  until you  deactivate it using            When                                                        
            <ALT>X, even after the script itself has finished executing.
            Hence, to  stop a script, you can enter <ALT>X, but the WHEN
            keeps on  going.   You can  enter another <ALT>X to stop the
            WHEN.  A third <ALT>X takes you out of PibTerm entirely.
            
            When slows  down PibTerm's execution somewhat, so you should            When                                                        
            not be  surprised if the output from the remote system seems
            to be displayed more slowly than usual.
            



            PibTerm Script Language Reference Guide              Page 63            PibTerm Script Language Reference Guide              Page 63


            Examples:
            
                 Declare Whenwait String
                 Declare Whensend String
                 *
                 WHEN 'Username: ' 'MYUSERID|'
                 *
                 Set Whenwait = 'Username: '
                 Set Whensend = 'MYUSERID|'
                 *
                 WHEN Whenwait Whensend
            
            
            WhenDrop -- Take Action On Carrier Drop            WhenDrop -- Take Action On Carrier Drop
            
            WhenDrop specifies  a string  to be sent to the modem when a            WhenDrop                                                    
            carrier drop is detected. The syntax is:
            
                 WHENDROP Ssend
            
            Ssend is  the string  to be  sent out  the port to the modem            Ssend                                                       
            when the carrier drops.
            
            WhenDrop is useful for resetting a modem when a carrier drop
            occurs.  Since Ssend  may contain an Execute PibTerm command                           Ssend                 Execute                
            function, this allows you to deal with many conditions on  a
            carrier drop.   This WhenDrop condition can co-exist with an
            ordinary When condition.                     When           
            
            Example:
            
                 WhenDrop "@G@/WEDIED^M/"
            
            
            This says  that when  the carrier drop occurs, PibTerm is to
            execute the script "WEDIED.SCR". (@G --> <ALT>G, @/WEDIED^M/
            -->  WEDIED   followed  by  CHR(CR),  so  script  WEDIED  is
            executed.)
            
            
            WhereXY -- Return Current Cursor Position            WhereXY -- Return Current Cursor Position
            
            WhereXY returns  the current  row and column position of the            WhereXY                                                     
            cursor on the screen.  The syntax is:
            
                 WhereXY Icolumn Irow
            
            Icolumn receives  the column  position and Irow receives the            Icolumn                                    Irow             
            row position.  Both must be integer variables.
            
            



            PibTerm Script Language Reference Guide              Page 64            PibTerm Script Language Reference Guide              Page 64


            While -- Execute Statements While Condition True            While -- Execute Statements While Condition True
            
            While begins a block of statements to be repeatedly executed            While                                                       
            as long as the specified condition on the While statement is
            true. A  While block is terminated by an EndWhile statement.                                                     EndWhile           
            The form  of  the  condition  for  the  While  statement  is
            identical to that for the Until and If statements.                                      Until     If            
            
            For example, to execute a block of script statements as long
            as PibTerm is connected to a remote system, write:
            
                 While ( Connected ) Do
                      .
                      .
                      .
                 EndWhile
            
            
            See the  Set statement  for details on Connected, and the If                     Set                           Connected          If
            statement for details on conditions.
            
            
            Write -- Write Characters To File            Write -- Write Characters To File
            
            Write writes  characters to  a file  prepared  by  the  Open            Write                                                   Open
            command. The syntax is:
            
                 WRITE Ifile Sdata
            
            where Ifile is the file handle of the file, and Sdata is the                  Ifile                                     Sdata       
            string of characters to be written.
            
            A handle  of 0  refers to the screen.  A missing file handle
            also refers to the screen.
            
            You can  use the  IOResult function to check for errors (see                              IOResult                                  
            the Set command).                Set          
            
            Examples:
            
                  Declare handle integer
                  Declare HiString String
                 *
                  Open 1 "bogusco.dat" "O"
                 *
                  WRITE 1 'Hi there!'
                 *
                  Set HiString = 'Hi there!'
                  Set handle = 1
                 *
                  WRITE handle HiString
            
            



            PibTerm Script Language Reference Guide              Page 65            PibTerm Script Language Reference Guide              Page 65


            Writeln -- Write Line To File            Writeln -- Write Line To File
            
            Writeln writes  a string to a file, terminated by a carriage            Writeln                                                     
            return and linefeed.  The syntax is:
            
                 WRITELN Ifile Sdata
            
            Ifile is  the file  handle and  Sdata is  the string  to  be            Ifile                           Sdata                       
            written.   Ifile may  be either  an integer  or  an  integer                       Ifile                                            
            constant.   Sdata  may  be  either  a  string  or  a  string                        Sdata                                           
            constant.   Sdata should NOT have the ^M^J (carriage return-                        Sdata                                           
            linefeed) specified  as part  of the string; those are added
            automatically.
            
            A file  handle of  0 refers  to the  screen.  A missing file
            handle also refers to the screen.
            
            Examples:
                 
                  Declare handle integer
                  Declare HiString String
                 *
                  WRITELN 1 'Hi there!'
                 *
                  Set HiString = 'Hi there!'
                  Set handle = 1
                 *
                  WRITELN handle HiString
                 *
                  WRITELN 0 'This appears on screen.'
                  WRITELN 'This also appears on screen.'
                 
            
            WriteLog -- Write String To Log Files            WriteLog -- Write String To Log Files
            
            WriteLog writes  the contents  of a  string to  all  of  the            WriteLog                                                    
            active log  files.   These include  the review  buffer,  the
            capture file,  the PIBTERM.LOG  log file, and the printer --
            whichever are  in use  (if any).    The  string  is  written
            preceded by  the current  date and  time in standard PibTerm
            logging format.
            
            The syntax is:
            
                 WRITELOG Slog
            
            Slog is  the string  to be  written.   Slog can  be either a            Slog                                   Slog                 
            string variable or a string constant.
            
            
            Using Script Commands in Command Line Mode            Using Script Commands in Command Line Mode
            
            You can  enter a  script command  from the  keyboard.   This
            allows you to use PibTerm in a command-driven fashion if you



            PibTerm Script Language Reference Guide              Page 66            PibTerm Script Language Reference Guide              Page 66


            dislike the  menus.   To do  this you  need to  define a key
            which will invoke command mode.  This is done at the <ALT>P,
            O)dds and ends, b) command key definition submenu.  You will
            be asked  to hit  the key which will be subsequently used to
            invoke command  mode.    This  key  must  be  one  of  those
            available for definition at <ALT>K.
            
            There is  NO DEFAULT  value for  the command line key, i.e.,
            PibTerm does not provide command line mode by default.
            
            Hitting the command key causes the status line (usually line
            25) of  the display to show 'Command: '.  You may then enter
            a script command which will be immediately executed.
            
            For example, you might enter the command
            
                 Dial "1"
            
            to dial the first number in the dialing directory, or
            
                 SetParam "pa" "N"
            
            to set no parity.
            
            If the  command is  incorrectly entered, an error message is
            printed on the status line.
            
            You may  add  your  own  user-defined  commands.    See  the
            description of  the  AddCommand  script  command  above  for                                 AddCommand                             
            details.
            
            
            Script Commands Legal In Command Line Mode            Script Commands Legal In Command Line Mode
            
            The following subset of script commands can be used sensibly
            in command line mode:
            
                 Addlf     Alarm     Break     Capture   ChDir     
                 Clear     ComDrain  ComFlush  CopyFile  Delay     
                 Dial      Dos       Echo      EditFile  EraseFile 
                 Execute   Exit      ExitAll   FreeSpace GetDir    
                 GetParam  Hangup    Host      Input     Key       
                 KeyDef    KeyFlush  KeySend   Log       Message   
                 Mute      Param     PrintFile Quit      Receive   
                 Redial    RInput    ScreenDump          Send      
                 SetParam  SText     Suspend   Text      Translate 
                 ViewFile  Wait      WaitCount WaitList  WaitQuiet 
                 WaitString          WaitTime  When      WhenDrop  
                 WriteLog
                 
            
            Some of  the other  commands may  be  accepted,  but  aren't
            probably useful  in command line mode.  Some of the commands
            (like IF, REPEAT, etc.) will NOT be accepted at all.



            PibTerm Script Language Reference Guide              Page 67            PibTerm Script Language Reference Guide              Page 67


            
            
            Sample Scripts            Sample Scripts
            
            The script  language in  PibTerm is  complicated enough that
            some extended examples are useful in showing how scripts can
            be constructed  for common  login sequences.   You  can also
            find some  script examples  in the "Guide to Using PibTerm."
            There are  also a  number of sample scripts (including those
            shown  here)   provided  as  part  of  the  PibTerm  release
            materials (look for the files ending in ".SCR").
            
            Notice how similar all of the login scripts are.  You should
            be able  to modify  one of  these  (or  one  of  the  others
            provided as  part of  the  PibTerm  release  materials)  for
            nearly any type of mainframe, mini, or remote bulletin board
            system you wish to access.
            
            
            CDC/NOS login script            CDC/NOS login script
            
            Here is a script for automatically logging on to the CDC NOS
            mainframe system  at ACNS.   Other  CDC sites will generally
            require a different sequence:
            
            
            ***************************************************************************
            *       N O S . S C R --- Script for connecting to Cyber NOS system       *
            ***************************************************************************
            *                                                                         *
            *    Script:  Nos.Scr                                                     *
            *                                                                         *
            *    Purpose: Connects to Cyber NOS system.  Designed for use as          *
            *             attached script in dialing directory.                       *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "Nos"                                                     *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       Change the values of "username" and "password" to those of        *
            *       your own NOS account.                                             *
            *                                                                         *
            ***************************************************************************
            *
            *                                  Send CRs to wake up autobaud
             Repeat
            *
                SText "|"
            *                                  Wait on parity message, indicating
            *                                  baud rate/parity detected
                WaitString "arity" 4
            *



            PibTerm Script Language Reference Guide              Page 68            PibTerm Script Language Reference Guide              Page 68


             Until ( WaitFound OR ( NOT Connected ) )
            *
            *                                  If carrier dropped, quit script.
             If ( NOT Connected ) Then
                Exit
             Endif
            *                                  Now wait for "operating system" prompt
             WaitString "ting system"
            *                                  If carrier dropped, quit script.
             If ( NOT Connected ) Then
                Exit
             Endif
            *                                  Indicate to CDCNET that we want
            *                                  a NOS session.  For NOS/VE, we
            *                                  would send "CREC VE" instead.
             WaitQuiet 20
             SText "crec nos|"
            *                                  Wait for username prompt
             WaitString "USER NAME:"
            *                                  Send user name -- ENTER YOURS HERE.
             SText "username|"
            *                                  Wait for password prompt
             WaitString "PASSWORD:"
            *                                  Send password -- ENTER YOURS HERE.
             SText "password|"
            *                                  Wait for bulletins, etc. to pass.
             WaitQuiet 30
            *                                  Set VT100 emulation in PibTerm.
             SetParam 'VC' '0'
             SetParam 'AK' '0'
            *                                  Load NOS function keys.
             Key 'cdcnos.fnc'
            *                                  Set backspace if not already set.
             SetParam 'BS' '^H'
             SetParam 'DE' ''
            *                                  Set VT100 emulation on NOS.
             SText "SETTERM,VT100|"
            
            
            VAX/VMS login script            VAX/VMS login script
            
            Here is  a script  to log  on to  a Vax system running under
            VMS, like the Vax 785 at ACNS:
            
            
            ***************************************************************************
            *        V A X . S C R --- Script for connecting to Vax VMS system        *
            ***************************************************************************
            *                                                                         *
            *    Script:  Vax.Scr                                                     *
            *                                                                         *
            *    Purpose: Connects to Vax VMS system.  Designed for use as            *
            *             attached script in dialing directory.                       *
            *                                                                         *



            PibTerm Script Language Reference Guide              Page 69            PibTerm Script Language Reference Guide              Page 69


            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "Vax"                                                     *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       Change the values of "username" and "password" to those of        *
            *       your own Vax account.                                             *
            *                                                                         *
            ***************************************************************************
            *
            *                                  Wake up Vax's autobaud.
             Repeat
            *
                SText "|"
            *                                  Wait for "Username" prompt.
                WaitString "Username:" 2
            *
             UNTIL ( WaitFound OR ( NOT Connected ) )
            *
            *                                  Quit if carrier dropped.
             IF ( NOT Connected ) THEN
                Exit
             ENDIF
            *                                  Send user name -- PUT YOURS HERE.
             SText "username|"
            *                                  Wait for password prompt.
             WaitString "Password:"
            *                                  Send password -- PUT YOURS HERE.
             SText "password|"
            *
            *                                  Set VT100 emulation
             SetParam 'VC' '0'
             SetParam 'AK' '0'
            *
             WaitString "$ "
             SText "SET TERM/VT100|"
            *                                  Load Vax function keys
             IF ( EnhKeybd = 1 ) THEN
                Key 'decvaxe.fnc'
             ELSE
                Key 'decvax.fnc'
             ENDIF
            *                                  Set backspace if not already set.
             SetParam 'DE' '^H'
             SetParam 'BS' ''
            
            
            IBM CMS login script            IBM CMS login script
            
            Here is a script to log on to an IBM CMS system, through an
            7171 (or equivalent) front-end:
            
            



            PibTerm Script Language Reference Guide              Page 70            PibTerm Script Language Reference Guide              Page 70


            ***************************************************************************
            *       I B M . S C R --- Script for connecting to IBM CMS system         *
            ***************************************************************************
            *                                                                         *
            *    Script:  Ibm.Scr                                                     *
            *                                                                         *
            *    Purpose: Connects to IBM CMS system with a 7171 front end.           *
            *             Designed for use as attached script in dialing directory.   *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "Ibm"                                                     *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       Change the values of "username" and "password" to those of        *
            *       your own Ibm account.                                             *
            *                                                                         *
            ***************************************************************************
            *
            *                                  Wake up 7171 front-end
             Repeat
            *
                SText "|"
            *                                  Wait for "Username" prompt.
                WaitString "TYPE:" 2
            *
             Until ( WaitFound OR ( NOT Connected ) )
            *
            *                                  Quit if carrier dropped.
             IF ( NOT Connected ) THEN
                Exit
             ENDIF
            *                                  Send terminal type of VT100
             SText "vt100|"
            *                                  Set VT100 emulation in PibTerm
             SetParam 'VC' '0'
             SetParam 'AK' '0'
            *                                  Load CMS function keys
             IF ( EnhKeybd = 1 ) THEN
                Key      'ibmcmse.fnc'
             ELSE
                Key      'ibmcms.fnc'
             ENDIF
            *                                  Load backspace if not already done
             SetParam 'BS' '^[[OD'
             SetParam 'DE' '^[[OD'
            *                                  Wait for intro screen to finish.
             WaitQuiet 30
            *                                  Issue login -- put your own account
            *                                  and password here.
            *
             SText "|"
             WaitQuiet 10



            PibTerm Script Language Reference Guide              Page 71            PibTerm Script Language Reference Guide              Page 71


            *
             SText "login username password|"
            *
            
            
            LUIS login script            LUIS login script
            
            Here is  a script  for logging  in to the LUIS system.  LUIS
            runs under  IBM CMS,  but there  is no  account and password
            required.
            
            
            ***************************************************************************
            *       L U I S . S C R --- Script for connecting to Luis system          *
            ***************************************************************************
            *                                                                         *
            *    Script:  Luis.Scr                                                    *
            *                                                                         *
            *    Purpose: Connects to Luis system.  Designed for use as               *
            *             attached script in dialing directory.                       *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "Luis"                                                    *
            *                                                                         *
            ***************************************************************************
            *
            *                                  Wake up protocol converter.
             Repeat
            *
                SText "|"
            *                                  Wait for "Username" prompt.
                WaitString "TYPE:" 2
            *
             UNTIL ( WaitFound OR ( NOT Connected ) )
            *
            *                                  Quit if carrier dropped.
             IF ( NOT Connected ) THEN
                Exit
             ENDIF
            *                                  Send terminal type of VT100.
             SText "vt100|"
            *                                  Wait until an intro stuff clears.
             WaitQuiet 20
            *                                  Send CR to get Luis screen.
             SText "|"
            *
            *                                  Set VT100 emulation
             SetParam 'VC' '0'
             SetParam 'AK' '0'
            *                                  Load CMS function keys
             SetParam 'BS' '^[[OD'
             SetParam 'DE' '^[[OD'
            *



            PibTerm Script Language Reference Guide              Page 72            PibTerm Script Language Reference Guide              Page 72


             IF ( EnhKeybd = 1 ) THEN
                Key      'ibmcmse.fnc'
             ELSE
                Key      'ibmcms.fnc'
             ENDIF
            *
            
            
            OPUS login script            OPUS login script
            
            Here is  a script  to log on to an OPUS system.  This is the
            bulletin   board   software   currently   running   on   the
            Northwestern IBM PC bulletin board system.
            
            
            ***************************************************************************
            *        O P U S . S C R --- Script for logging into OPUS BBS system      *
            ***************************************************************************
            *                                                                         *
            *    Script:  Opus.Scr                                                    *
            *                                                                         *
            *    Purpose: Connects to OPUS system.  Designed for use as               *
            *             attached script in dialing directory.                       *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "Opus"                                                    *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       Change the values of "firstname", "lastname", and "password"      *
            *       to those of your own OPUS account.                                *
            *                                                                         *
            ***************************************************************************
            *
            *                                  Wait for name prompt.
             Waitstring "Your FIRST name:" 2
            *                                  Carrier dropped -- quit.
             If ( NOT Connected ) Then
                Exit
             EndIf
            *                                  Didn't get "FIRST name" prompt -- quit.
             If ( NOT WaitFound ) Then
                Exit
             Endif
            *
            *                                  Send first name, last name.
            *                                  PUT YOURS HERE.
            *
             SText   "firstname lastname|"
            *
            *                                  Reply "y" to validation prompt
            *
             Waitstring "Y,n"



            PibTerm Script Language Reference Guide              Page 73            PibTerm Script Language Reference Guide              Page 73


             Stext "y|"
            *
            *                                 Wait for password prompt and then
            *                                 send password.
            *                                 PUT YOURS HERE.
            *
             Waitstring "assword:"
             Stext "password|"
            
            
            RBBS login script            RBBS login script
            
            Here is  a script  to log on to an RBBS system.  This script
            may need  modification for  an individual RBBS system, since
            there can  be a  great deal  of variation as regards initial
            welcome messages and so on.
            
            
            ***************************************************************************
            *        R B B S . S C R --- Script for logging into RBBS BBS system      *
            ***************************************************************************
            *                                                                         *
            *    Script:  Rbbs.Scr                                                    *
            *                                                                         *
            *    Purpose: Connects to RBBS system.  Designed for use as               *
            *             attached script in dialing directory.                       *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "Rbbs"                                                    *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       Change the values of "firstname", "lastname", and "password"      *
            *       to those of your own RBBS account.                                *
            *                                                                         *
            ***************************************************************************
            *
            *                                  Wait for name prompt.
             WaitString "ame:"
            *                                  Send first name, last name, and password.
            *                                  PUT YOURS HERE.
            *
             SText   "firstname;lastname;password|"
            
            
            IBBS login script            IBBS login script
            
            Here is  a script  to log  on to  an IBBS  system like  Gene
            Plantz's system in Chicago:
            
            
            ***************************************************************************
            *        I B B S . S C R --- Script for logging into IBBS BBS system      *



            PibTerm Script Language Reference Guide              Page 74            PibTerm Script Language Reference Guide              Page 74


            ***************************************************************************
            *                                                                         *
            *    Script:  Ibbs.Scr                                                    *
            *                                                                         *
            *    Purpose: Connects to IBBS system.  Designed for use as               *
            *             attached script in dialing directory.                       *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "IBBS"                                                    *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       Change the values of "IDnnnn" and "password" to your own.         *
            *                                                                         *
            ***************************************************************************
            *
            *                                  Wait for name request
            *
             Waitstring "FIRST Name"
            *                                  Quit if not connected.
             If ( NOT Connected ) Then
                Exit
             Endif
            *                                  Send ID number and password.
            *                                  Also request message reading from
            *                                  last previous message.
            *                                  PUT YOUR ID/PASSWORD HERE.
            *
             WaitQuiet 10
             Stext   "IDnnnn;password;m;r;*|"
            *
            
            
            CompuServe Login Script            CompuServe Login Script
            
            Here is a sample script to log on to CompuServe.
            
            
            ***************************************************************************
            *        C I S . S C R --- Script for connecting to CompuServe            *
            ***************************************************************************
            *                                                                         *
            *    Script:  Cis.Scr                                                     *
            *                                                                         *
            *    Purpose: Connects to CompuServe.                                     *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "Cis"                                                     *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       Change the values of "user,id" and "password" to those of         *



            PibTerm Script Language Reference Guide              Page 75            PibTerm Script Language Reference Guide              Page 75


            *       your own CIS account.                                             *
            *                                                                         *
            ***************************************************************************
            *
            *                                  Wait a few seconds for network to activate
             Suspend 300
            *                                  Wake up CompuServe
             SText "^C"
            *                                  Wait for userid prompt
             WaitString "User"
            *                                  Send userid -- PUT YOURS HERE
             SText "user,id|"
            *                                  Wait for password prompt
             WaitString "Password:"
            *                                  Send password -- PUT YOURS HERE
             SText "password|"
            *                                  Wait for main prompt
             WaitString " !"
            *                                  Turn on CompuServe B protocol
             SetParam "BP" "1"
            *
            
            
            Using A Password File            Using A Password File
            
            PibTerm does  not store  the passwords for remote systems in
            the dialing  directory, for security purposes.  However, you
            may want  to keep  a file  of passwords  for remote  systems
            anyway, in  order to  better automate your scripts for those
            systems.   You can use the script facilities and text editor
            in PibTerm to maintain a password file.
            
            For example, if you regularly dial into a dozen different PC
            Board systems, you could write separate very similar scripts
            for  each   system  with   your  unique   ID  and  password.
            Alternatively, you  could write  one general  script and get
            the password for a particular system from a password file.
            
            Following is  a script  GETPASS.SCR which can be EXECUTEd by                                                             EXECUTE    
            another script to retrieve passwords from the password file.
            The initial  comments in  this script detail how to create a
            password file.
            
            
            ***************************************************************************
            *       G E T P A S S . S C R  --- Get password for remote system         *
            ***************************************************************************
            *
            *                                  Dialing entry to get password for
             Import DEntry Integer
            *                                  Name of dialed system to return to caller
             Import SysName String
            *                                  Password to return to calling script
             Import PassWord String



            PibTerm Script Language Reference Guide              Page 76            PibTerm Script Language Reference Guide              Page 76


            *
            ***************************************************************************
            *                                                                         *
            *    Script:  GetPass.Scr                                                 *
            *                                                                         *
            *    Purpose: Returns entry in password file corresponding to             *
            *             given dialing entry.                                        *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute 'GetPass'  DialEnt SysName PassWord                       *
            *                                                                         *
            *          DialEnt  --- Number of entry to get password for               *
            *          SysName  --- Name of System for entry 'DialEnt'                *
            *          PassWord --- Password for entry 'DialEnt'                      *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       PibTerm does not store passwords for systems to be dialed in the  *
            *       dialing directory.  This is for security reasons.  However,       *
            *       you may find it convenient to maintain a file of passwords for    *
            *       each system on your own.  You can do this with the built-in       *
            *       PibTerm editor, for example.                                      *
            *                                                                         *
            *       This script provides a mechanism for accessing your password      *
            *       file from another script invoked as the result of a PibTerm       *
            *       request.  Your dialing script just needs to invoke this script    *
            *       as indicated above.                                               *
            *                                                                         *
            *       Using a password file allows you to write one script which can    *
            *       handle the signon sequence for a number of remote systems.  For   *
            *       example, you can write a generic routine to log into PC Board     *
            *       systems.  Then you can attach this generic script to the dialing  *
            *       entries for all the PC Board systems you call.  The major         *
            *       difference will be the password, and using GETPASS.SCR allows you *
            *       to handle that difference rather easily.                          *
            *                                                                         *
            *       The password file is assumed to be called 'c:\pibterm\mypass.dat' *
            *       but you can change that to whatever name you like.  The format    *
            *       of the password file is simple:  for each entry in the dialing    *
            *       directory, place the system's name, followed by a colon (:),      *
            *       followed by the system's password on the matching line            *
            *       number in the password file.  Hence, if your dialing directory    *
            *       (PIBTERM.FON) has 25 entries, then your password file should also *
            *       have 25 lines.  Each line has the name and password corresponding *
            *       to one dialing entry.  For example, the 10th line in the password *
            *       file should have the name and password for the 10th entry in the  *
            *       dialing directory                                                 *
            *                                                                         *
            *       A non-existent password is returned as a null string.             *
            *                                                                         *
            *       While you won't stop a dedicated "hacker" from finding it, you    *
            *       may want to assign a "hidden" file attribute to your password     *
            *       file.  The GetPass script will still be able to read it, but      *



            PibTerm Script Language Reference Guide              Page 77            PibTerm Script Language Reference Guide              Page 77


            *       casual "perusers" of your hard disk won't find it in a standard   *
            *       DIR listing.                                                      *
            *                                                                         *
            ***************************************************************************
            *
            *                                  Current entry in password file
             Declare IEntry Integer
            *                                  Return null password in case of error
             PassWord = ''
            *                                  Ditto for System Name
             SysName  = ''
            *                                  Make sure dialing # is reasonable
             IF ( DEntry <= 0 ) THEN
                EXIT
             ENDIF
            *                                  Open password file.
            *                                  Change name to whatever you want.
            *
             Open 1 'c:\pibterm\MyPass.dat' 'Input'
            *
            *                                  Check that open went OK -- if not,
            *                                  return to caller.
             IF ( IOResult <> 0 ) THEN
                EXIT
             ENDIF
            *                                  Skip down to correct entry
            *
             FOR IEntry = 1 TO ( DEntry - 1 ) DO
                Readln 1 SysName
                IF ( IOResult <> 0 ) THEN
                   SysName = ''
                   CLOSE 1
                   EXIT
                ENDIF
             ENDFOR
            *                                 Read correct entry
             Readln 1 SysName
            *
             IF ( IOResult <> 0 ) THEN
                SysName = ''
                CLOSE 1
                EXIT
             ENDIF
            *                                  Close password file
             Close 1
            *                                  Parse out system name and password
            *                                   System Name begins line, then a colon (:),
            *                                   and then the password
             Set IEntry = Index(':', SysName)
             If ( IEntry = 0 ) then
                SysName = ''
                Exit
             EndIf
             Set Password = Trim( LTrim( SubStr(SysName, IEntry+1, Length(SysName)-IEntry)))



            PibTerm Script Language Reference Guide              Page 78            PibTerm Script Language Reference Guide              Page 78


             Set SysName  = Trim( LTrim( SubStr(SysName, 1, IEntry-1)))
            *
            
            
            PC Board Login Script Using Password File            PC Board Login Script Using Password File
            
            As an  example of how to use the GETPASS.SCR script, here is
            a generalized  PC Board  login script  written by Richard P.
            Byrne:
            
            
            *
               Declare  SysName     String
               Declare  PassWord    String
               Declare  DialEnt     Integer
               Declare  StrIdx      Integer
               Declare  TimeOut     Integer  10
               Declare  LoopCount   Integer   0
               Declare  CaptStatus  String  'OFF'
            *
            ******************************************************************************
            *                                                                            *
            *   Script:     PCBOARD.SCR                                                  *
            *                                                                            *
            *   Purpose:    Automated logon for PCBoard bulletin board systems.          *
            *                                                                            *
            *   Invocation: This script is meant to be invoked from the dialing          *
            *               directory.                                                   *
            *                                                                            *
            *   Remarks:    Creates a file called PCB_NEWS.TXT that will contain the     *
            *               first screenful of News displayed by the system (if any).    *
            *                                                                            *
            *               This script calls the GETPASS script to return the name      *
            *               of the system being accessed plus the password for that      *
            *               system.                                                      *
            *                                                                            *
            ******************************************************************************
            *
            *                             Get entry number of system dialed
               Set DialEnt = Dialed
            *                             Wait for the "graphics" prompt
            *
               WaitString '=no?' TimeOut
               If (WaitFound) then
            *                             Use graphics for this call
                  SText 'Y Q|'
            
            *                             Get name of system + password from Mypass.Dat file
            *
                  Execute 'getpass' DialEnt SysName PassWord
            *
            *                             Format Password for use by combining
            *                             with logon id (ie. first & last name)
            *



            PibTerm Script Language Reference Guide              Page 79            PibTerm Script Language Reference Guide              Page 79


                  Set PassWord = CONCAT('FirstName LastName ', PassWord)
                  Set PassWord = CONCAT( PassWord , '|' )
            *
            *                             Format System Name for log file entry
            *
                  Set SysName  = CONCAT('Captured News Items for ', SysName)
            *
            *                             Turn on capture in case there's news
            *
                  Capture 'C:\pcbdir\PCB_News.Txt' 'E'
            *
            *                             Set capture file status flag to
            *                             indicate an open log file
            *
                  Set CaptStatus = 'ON'
            *
            *                             Write system name to log file
            *
                  WriteLog '========================================================'
                  WriteLog SysName
                  WriteLog '========================================================'
            
            *                             Send logon id and password
                  SText PassWord
            
            *                             Set WaitTime to one second
                  WaitTime 1
            *                             Loop until we get to main command prompt
                  Repeat
                     WaitList StrIdx 'continue?' '=no?' '(NS)?' '=yes?' 'Command?'
                     Set LoopCount = LoopCount + 1
                     DoCase StrIdx
                        Case 1
            *                             Answer the "Press (Enter) to continue?"
            *                             prompt
                           SText '|'
            *                             And re-initialize our "dead-man"
            *                             loop counter
            *
                           Set LoopCount = 0
                        EndCase
                        Case 2
            *                             Conference "auto-joined" ...
            *                             Answer the "view others" prompt
                           SText '|'
            *                             And re-initialize our "dead-man"
            *                             loop counter
            *
                           Set LoopCount = 0
                        EndCase
                        Case 3
            *                             Answer the "More: (Y), (N), (NS)?"
            *                             prompt
                           SText 'N|'



            PibTerm Script Language Reference Guide              Page 80            PibTerm Script Language Reference Guide              Page 80


            *                             And re-initialize our "dead-man"
            *                             loop counter
            *
                           Set LoopCount = 0
                        EndCase
                        Case 4
            *                             Turn off capture and scan all
            *                             message bases for mail
            *
                           If ( CaptStatus = 'ON' ) Then
                              Capture
                              Set CaptStatus = 'OFF'
                           EndIf
                           SText 'A NS|'
                           Set LoopCount = 0
                        EndCase
                     EndDoCase
                  Until (StrIdx = 5) or (LoopCount = TimeOut)
            
               EndIf
            *
            *                             If the capture file is still on (?),
            *                             then turn it off
            *
               If ( CaptStatus = 'ON' ) Then
                  Capture
               EndIf
            *                             That's all folks!
            
            
            Reading A New Configuration File            Reading A New Configuration File
            
            The PibTerm  script language  doesn't provide a direct means
            of  reading   in  a   parameter  configuration   file   like
            PIBTERM.CNF.   Reading in  a new  configuration file  can be
            very useful  if  you  want  to  change  a  large  number  of
            parameters at  once.   However, you can use the input/output
            facilities of PibTerm to read a new configuration file.
            
            Here is  a script  which can  be EXECUTEd by another script,                                             EXECUTE                    
            and which will read and process a configuration file.
            
            
            ***************************************************************************
            *       R E A D C O N F . S C R --- Read configuration file               *
            ***************************************************************************
            *
            *                                  Name of configuration file to be read
             Import ConfName String
            *
            ***************************************************************************
            *                                                                         *
            *    Script:  ReadConf.Scr                                                *
            *                                                                         *



            PibTerm Script Language Reference Guide              Page 81            PibTerm Script Language Reference Guide              Page 81


            *    Purpose: Reads a configuration file and resets PibTerm parameters.   *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "ReadConf" ConfName                                       *
            *                                                                         *
            *          ConfName --- Configuration file to read                        *
            *                                                                         *
            *          Example:    Execute "ReadConf" "Bogusco.Cnf"                   *
            *                                                                         *
            ***************************************************************************
            *
            *                                  Configuration line
             Declare ConfLine String
            *                                  Configuration parameter name
             Declare ConfName String
            *                                  Configuration parameter value
             Declare ConfValue String
            *                                  Open configuration file.
            *
             Open 1 ConfName "Input"
            *
            *                                  Check that open went OK -- if not,
            *                                  return to caller.
             IF ( IOResult <> 0 ) THEN
                EXIT
             ENDIF
            *                                  Begin loop over configuration file.
             REPEAT
            *                                  Read line from configuration file.
                Readln 1 ConfLine
            *                                  Parse into parameter name and value.
            *
                ConfName  = Substr( ConfLine, 1, 2 )
                ConfValue = Substr( ConfLine, 4, 255 )
            *
            *                                  Set parameter value.
                SetParam ConfName ConfValue
            *
             UNTIL ( EOF( 1 ) )
            *                                  Close configuration file
             Close 1
            
            
            Defining Scripts For External Transfer Protocols            Defining Scripts For External Transfer Protocols
            
            As indicated  in the  "Guide to  PibTerm", it is possible to
            hook external  file transfer  protocols into  PibTerm  using
            either batch  files or  scripts.   The  "Guide  to  PibTerm"
            describes the procedure for using batch files.  This section
            discusses  the   use  of   scripts,  which   provides   more
            flexibility  but   requires  considerably  more  programming
            expertise.
            



            PibTerm Script Language Reference Guide              Page 82            PibTerm Script Language Reference Guide              Page 82


            This section  presents scripts  for use  with MLINK.COM, the
            module written  by Paul Meiners that implements the MegaLink
            protocol.   The discussion on adding external file transfers
            to PibTerm  in  the  "Guide  to  PibTerm"    also  uses  the
            MLINK.COM program  as an  example, so  you should  have  the
            "Guide" handy for comparison.
            
            Let's begin by recapitulating the parameters expected by the
            external protocol  module.   In the  case of  MegaLink,  the
            MLINK.COM program takes argument of the form:
            
                 MLINK PORT n SPEED s RM download_directory
                 MLINK PORT n SPEED s SM
            
            where 'n' is the communications port number, 's' is the baud
            rate  of  the  connection,  RM  indicates  files  are  being
            received,  SM   indicates  files   are   being   sent,   and
            'download_directory' is  the name  of the  PibTerm  download
            directory.
            
            For example,  to receive files at 2400 baud over port 1, the
            MLINK.COM invocation should be:
            
                 MLINK PORT 1 SPEED 2400 RM C:\DOWNLOAD
            
            assuming   that    the   PibTerm   download   directory   is
            'C:\DOWNLOAD', while  to send files over port 2 at 1200 baud
            the MLINK.COM invocation should be:
            
                 MLINK PORT 2 SPEED 1200 SM
            
            In general,  a script  to receive  a file  or files contains
            statements to do the following:
            
                 1.   Save the  current drive/directory  using  the  new
                      GETDIR script command.
                 
                 2.   Move to  the select  download directory (parameter
                      DD= in  terminal mode  or HD=  in host mode) using
                      the CHDIR  script  command,  unless  the  external
                      protocol  module  has  a  way  of  specifying  the
                      download directory name.
                 
                 3.   Pick up the file name to be transferred (parameter
                      FN=) using the GETPARAM script command.
                 
                 4.   Pick  up  any  other  information  needed  by  the
                      external protocol handler, such as the port (PO=),
                      baud rate  (BA=), etc.,  again using  the GETPARAM
                      command.
                 
                 5.   Construct the  DOS command  to invoke the external
                      handler module, including the program name and all
                      of its  parameters.  This will involve a series of



            PibTerm Script Language Reference Guide              Page 83            PibTerm Script Language Reference Guide              Page 83


                      SET statements  to CONCAT  the various  parameters
                      together.
                 
                 6.   Execute  the   external  handler   using  the  DOS
                      command.
                 
                 7.   Return to  the original  drive/directory using the
                      CHDIR command.
                 
            A script  to send  files is  similar.  In terminal mode, you
            don't need  to specify a directory from which to send files.
            In host  mode, you  should specify  the host  mode  download
            directory (HD=)  and restrict  files  to  be  sent  to  that
            subdirectory. The  easiest way  to  do  that  is  to  simply
            prepend the  host mode  directory to  the file specification
            provided by  the user  (from  FN=).    If  a  non-super-user
            requests some  other path,  the script  should strip  it, or
            just not allow the transfer.
            
            When sending  files, or  receiving files  with  a  non-batch
            protocol, you  need to know the file name(s) of the files to
            be transferred.  PibTerm will  have already prompted for the
            name.   You gain  access to  the file specification provided
            using  the  new  FN=  pseudo-parameter.  FN=  is  a  pseudo-
            parameter because  it isn't  written to  PIBTERM.CNF (and is
            ignored if  read from  there), but  it can be accessed using
            the script  command 'GetParam'  just like  a real parameter.
            The value  returned by  FN is  the file  specification  last
            entered to  PibTerm.   You can look at SENDMLIN.SCR (appears
            below) to see how to use FN=.
            
            If you  allow the protocol to execute in host mode, then you
            also need  to check  within your script whether the protocol
            has been  invoked from host mode or from terminal mode.  The
            new pseudo-parameter HP= provides this information:
            
                 HP=      -- in terminal mode (HP is a blank)
                 HP=N     -- in host mode, user is a normal user
                 HP=S     -- in host mode, user is a super-user
            
            Like FN=,  HP= is  not written to PIBTERM.CNF and is ignored
            if present in that file.
            
            NOTE:     For security  reasons in  host  mode,  when  using
                      external protocols,  make sure  that the  external
                      driver has either
            
                           (1)  a mechanism  for restricting  the  files
                           sent or received to the current directory, or
            
                           (2)  a   mechanism    for   specifying    the
                           directories from which files are sent or into
                           which files are received.
            



            PibTerm Script Language Reference Guide              Page 84            PibTerm Script Language Reference Guide              Page 84


                      Otherwise, non-super-users  could use  an external
                      protocol  to   transfer  files   you  don't   want
                      transferred, and  which wouldn't be allowed by the
                      internal PibTerm  transfer facilities  because  of
                      the XferList  (PIBTERM.XFR) checking.  No XferList                                     PIBTERM.XFR                        
                      checking is available for external protocols.
            
            
            Example: SENDMLIN.SCR for sending files with MegaLink            Example: SENDMLIN.SCR for sending files with MegaLink
            
            Here is the script SENDMLIN.SCR for interfacing MLINK.COM to
            PibTerm for purposes of sending files to a remote system:
            
            
            ***************************************************************************
            *    S E N D M L I N . S C R --- Script interfacing MLINK to PibTerm      *
            ***************************************************************************
            *                                                                         *
            *    Script:  SendMLin.Scr                                                *
            *                                                                         *
            *    Purpose: Interfaces external Megalink driver program MLINK.COM       *
            *             to PibTerm for sending files.                               *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "SendMLin"                                                *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       This script is designed to be automatically invoked by the        *
            *       <ALT>S command when MegaLink has been defined as an external      *
            *       protocol at <ALT>P, F)ile transfer, k) external file transfers.   *
            *                                                                         *
            ***************************************************************************
            *                                                                         *
            *                                  File spec for files to transfer
               Declare FileSpec String
            *                                  Baud rate for transfer
               Declare BaudRate String
            *                                  Comm port number
               Declare Port     String
            *                                  Build MLink invocation line in this
               Declare Mlink    String
            *                                  Host mode flag
               Declare HostMode String
            *                                  Upload directory
               Declare UpDir String
            *
            **************************************************************************
            *       StripPath --- procedure to strip path from file name             *
            **************************************************************************
            *
               PROCEDURE StripPath
            *



            PibTerm Script Language Reference Guide              Page 85            PibTerm Script Language Reference Guide              Page 85


                  Declare I  Integer
                  Declare L  Integer
                  Declare Ch String
            *
                  IF ( ( INDEX( '\' , FileSpec ) <> 0 ) OR ( INDEX( ':' , FileSpec ) <> 0 ) ) THEN
            *
                     L = LENGTH( FileSpec )
                     I = L
            *
                     REPEAT
                        I  = I - 1
                        Ch = Substr( FileSpec, I, 1 )
                     UNTIL ( ( Ch = '\' ) OR ( Ch = ':' ) )
            *
                     FileSpec = SUBSTR( FileSpec,  I + 1 , L - I )
            *
                  ENDIF
            *
               ENDPROC   StripPath
            *
            **************************************************************************
            *                       SendMLin -- Main Routine                         *
            **************************************************************************
            *
            *                                  Find out if we're in host mode
            *
               GetParam 'HP' HostMode
            *                                  Get port number
               GetParam 'PO' Port
            *                                  Get baud rate
               GetParam 'BA' BaudRate
            *                                  Get file spec
               GetParam 'FN' FileSpec
            *                                  Get host mode directory, and
            *                                  prepend to file spec, after
            *                                  stripping any other directory spec.
               IF ( HostMode = 'N' ) THEN
                  GetParam 'HD' UpDir
                  Call StripPath
                  Set FileSpec = CONCAT( UpDir , FileSpec )
               ENDIF
            *                                  Build MLink invocation line
            *
               Set Mlink = CONCAT( 'MLink port ' , Port )
               Set Mlink = CONCAT( CONCAT( Mlink , ' speed '  ), BaudRate )
               Set Mlink = CONCAT( CONCAT( Mlink , ' SM ' ), FileSpec )
            *
            *                                  Echo built line to screen
               Writeln " "
               Writeln "Invoking MLink as follows:"
               Writeln Mlink
               Writeln " "
            *                                  Echo Mlink line to capture file
            *



            PibTerm Script Language Reference Guide              Page 86            PibTerm Script Language Reference Guide              Page 86


               Writelog "Invoking MLink as follows:"
               Writelog Mlink
            *                                  Call MLink
               Dos Mlink
            *
            
            
            Example: RECLINK.SCR for receiving files with MegaLink            Example: RECLINK.SCR for receiving files with MegaLink
            
            Here is the script RECMLINK.SCR for interfacing MLINK.COM to
            PibTerm for  purposes  of  receiving  files  from  a  remote
            system:
            
            
            ***************************************************************************
            *       R E C M L I N K . S C R --- Script interfacing MLINK to PibTerm   *
            ***************************************************************************
            *                                                                         *
            *    Script:  RecMLink.Scr                                                *
            *                                                                         *
            *    Purpose: Interfaces external Megalink driver program MLINK.COM       *
            *             to PibTerm for receiving files.                             *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "RecMLink"                                                *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       This script is designed to be automatically invoked by the        *
            *       <ALT>R command when MegaLink has been defined as an external      *
            *       protocol at <ALT>P, F)ile transfer, k) external file transfers.   *
            *                                                                         *
            ***************************************************************************
            *                                                                         *
            *                                  Baud rate for transfer
               Declare BaudRate String
            *                                  Comm port number
               Declare Port     String
            *                                  Build Mlink invocation line in this
               Declare MLink    String
            *                                  Download directory
               Declare DownDir  String
            *                                  Length of download directory
               Declare L        Integer
            *                                  Host mode flag
               Declare HostMode String
            *                                  Find out if we're in host mode
            *
               GetParam 'HP' HostMode
            *                                  Get download directory.
            *                                  If in host mode, use host mode upload
            *                                  directory.
            *



            PibTerm Script Language Reference Guide              Page 87            PibTerm Script Language Reference Guide              Page 87


               IF ( HostMode = ' ' ) THEN
                  GetParam 'DD' DownDir
               ELSE
                  GetParam 'HU' DownDir
               ENDIF
            *                                  Get port number
               GetParam 'PO' Port
            *                                  Get baud rate
               GetParam 'BA' BaudRate
            *                                  Strip final '\' if any from download dir
               Set L = LENGTH( DownDir )
            *
               IF ( Substr( DownDir, L, 1 ) = '\' ) THEN
                  Set DownDir = Substr( DownDir, 1, L - 1 )
               ENDIF
            *                                  Build Mlink invocation line
            *
               Set MLink = CONCAT( 'Mlink port ' , Port )
               Set MLink = CONCAT( CONCAT( MLink , ' speed ' ), BaudRate )
               Set MLink = CONCAT( CONCAT( MLink , ' rm ') , DownDir )
            *
            *                                  Echo MLink line to screen
               Writeln " "
               Writeln "Invoking MLink as follows:"
               Writeln MLink
               Writeln " "
            *                                  Echo MLink line to capture file
            *
               Writelog "Invoking MLink as follows:"
               Writelog MLink
            *                                  Call MLink
               Dos MLink
            *
            
            
            Example: SENDZMOD.SCR for sending files with Zmodem            Example: SENDZMOD.SCR for sending files with Zmodem
            
            The PibTerm  release materials  already include a definition
            of Zmodem  as an  external file  transfer protocol using the
            batch files RECZMOD.BAT and SENDZMOD.BAT to invoke DSZ.COM.                        RECZMOD.BAT     SENDZMOD.BAT                   
            
            As an  alternative, the  following presents send and receive
            scripts for use with DSZ.COM.
            
            Here the  script SENDZMOD.SCR  for  interfacing  DSZ.COM  to
            PibTerm for purposes of sending files to a remote system:
            
            
            ***************************************************************************
            *       S E N D Z M O D . S C R --- Script interfacing DSZ to PibTerm     *
            ***************************************************************************
            *                                                                         *
            *    Script:  SendZMod.Scr                                                *
            *                                                                         *



            PibTerm Script Language Reference Guide              Page 88            PibTerm Script Language Reference Guide              Page 88


            *    Purpose: Interfaces external Zmodem driver program DSZ.COM           *
            *             to PibTerm for sending files.                               *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "SendZmod"                                                *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       This script is designed to be automatically invoked by the        *
            *       <ALT>R command when Zmodem has been defined as an external        *
            *       protocol at <ALT>P, F)ile transfer, k) external file transfers.   *
            *                                                                         *
            ***************************************************************************
            *                                                                         *
            *                                  File spec for files to transfer
               Declare  FileSpec String
            *                                  Baud rate for transfer
               Declare BaudRate String
            *                                  Comm port number
               Declare Port     String
            *                                  Zmodem block size
               Declare Block    String
            *                                  Build DSZ invocation line in this
               Declare Zmodem   String
            *                                  'restrict ' for host mode, else null
               Declare Restrict String
            *                                  Host mode flag
               Declare HostMode String
            *                                  Saves drive/directory we're in now
               Declare CurDrive String
               Declare CurDir   String
            *                                  Host mode download directory =
            *                                  directory remote callers can download from.
               Declare UpDir    String
            *                                  Length of directory name
               Declare L        Integer
            *                                  Get port number
               GetParam 'PO' Port
            *                                  Get baud rate
               GetParam 'BA' BaudRate
            *                                  Get Zmodem block size
               GetParam 'ZB' Block
               Set Block = '50'
            *                                  Get file spec
               GetParam 'FN' FileSpec
            *                                  Get host mode flag
               GetParam 'HP' HostMode
            *                                  Get directory we're in now
               GetDir CurDrive CurDir
            *                                  If host mode, move to host mode
            *                                  download directory and set restrict.
               Set Restrict = ''
            *



            PibTerm Script Language Reference Guide              Page 89            PibTerm Script Language Reference Guide              Page 89


               IF ( HostMode <> ' ' ) THEN
            *
                  GetParam 'HD' UpDir
            *                                  Strip final '\' if any from download dir
                  Set L = LENGTH( UpDir )
            *
                  IF ( Substr( UpDir, L, 1 ) = '\' ) THEN
                     Set UpDir = Substr( UpDir, 1, L - 1 )
                  ENDIF
            *                                  Move to download dir
                  ChDir UpDir
            *                                  Set restrict if not super-user
                  IF ( HostMode <> 'S' ) THEN
                     Set Restrict = 'restrict '
                  ENDIF
            *
               ENDIF
            *                                  Build DSZ invocation line
            *
               Set Zmodem = CONCAT( 'DSZ port ' , Port )
               Set Zmodem = CONCAT( CONCAT( Zmodem , ' speed '  ), BaudRate )
               Set Zmodem = CONCAT( CONCAT( Zmodem , ' d z pL' ), Block )
               Set Zmodem = CONCAT( CONCAT( CONCAT( Zmodem , Restrict ), ' sz ' ), FileSpec )
            *
            *                                  Echo built line to screen
               Writeln " "
               Writeln "Invoking DSZ as follows:"
               Writeln Zmodem
               Writeln " "
            *                                  Echo Zmodem line to capture file
            *
               Writelog "Invoking DSZ as follows:"
               Writelog Zmodem
            *                                  Call DSZ
               Dos Zmodem
            *                                  Return to original directory if host mode
               IF ( HostMode <> ' ' ) THEN
                  Set CurDir = CONCAT( CONCAT( CurDrive , ':\' ), CurDir )
                  Chdir CurDir
               ENDIF
            
            
            Example: RECZMOD.SCR for receiving files with Zmodem            Example: RECZMOD.SCR for receiving files with Zmodem
            
            Here is  the script  RECZMOD.SCR for  interfacing DSZ.COM to
            PibTerm for purposes of sending files to a remote system:
            
            
            ***************************************************************************
            *       R E C Z M O D . S C R --- Script interfacing DSZ to PibTerm       *
            ***************************************************************************
            *                                                                         *
            *    Script:  RecZMod.Scr                                                 *
            *                                                                         *



            PibTerm Script Language Reference Guide              Page 90            PibTerm Script Language Reference Guide              Page 90


            *    Purpose: Interfaces external Zmodem driver program DSZ.COM           *
            *             to PibTerm for receiving files.                             *
            *                                                                         *
            *    Invocation:                                                          *
            *                                                                         *
            *       Execute "RecZmod"                                                 *
            *                                                                         *
            *    Remarks:                                                             *
            *                                                                         *
            *       This script is designed to be automatically invoked by the        *
            *       <ALT>R command when Zmodem has been defined as an external        *
            *       protocol at <ALT>P, F)ile transfer, k) external file transfers.   *
            *                                                                         *
            ***************************************************************************
            *                                                                         *
            *                                  Baud rate for transfer
               Declare BaudRate String
            *                                  Comm port number
               Declare Port     String
            *                                  Build DSZ invocation line in this
               Declare Zmodem   String
            *                                  Saves drive/directory we're in now
               Declare CurDrive String
               Declare CurDir   String
            *                                  Download directory
               Declare DownDir  String
            *                                  Length of download directory
               Declare L        Integer
            *                                  Host mode flag
               Declare HostMode String
            *                                  "Restrict" for host mode, else null
               Declare Restrict String
            *                                  Get directory we're in now
               GetDir CurDrive CurDir
            *                                  Get port number
               GetParam 'PO' Port
            *                                  Get baud rate
               GetParam 'BA' BaudRate
            *                                  Find out if we're in host mode
            *
               GetParam 'HP' HostMode
            *                                  Get download directory.
            *                                  If in host mode, use host mode upload
            *                                  directory.
            *
               Set Restrict = ''
            *
               IF ( HostMode = ' ' ) THEN
                  GetParam 'DD' DownDir
               ELSE
                  GetParam 'HU' DownDir
                  IF ( HostMode = 'N' ) THEN
                     Set Restrict = 'restrict '
                  ENDIF



            PibTerm Script Language Reference Guide              Page 91            PibTerm Script Language Reference Guide              Page 91


               ENDIF
            *                                  Strip final '\' if any from download dir
               Set L = LENGTH( DownDir )
            *
               IF ( Substr( DownDir, L, 1 ) = '\' ) THEN
                  Set DownDir = Substr( DownDir, 1, L - 1 )
               ENDIF
            *                                  Move to download directory
               Chdir     DownDir
            *                                  Build DSZ invocation line
            *
               Set Zmodem = CONCAT( 'DSZ port ' , Port )
               Set Zmodem = CONCAT( CONCAT( Zmodem , ' speed ' ), BaudRate )
               Set Zmodem = CONCAT( CONCAT( CONCAT( Zmodem , ' d ' ), Restrict ), 'rz -y')
            *
            *                                  Echo Zmodem line to screen
               Writeln " "
               Writeln "Invoking DSZ as follows:"
               Writeln Zmodem
               Writeln " "
            *                                  Echo Zmodem line to capture file
               Writelog "Invoking DSZ as follows:"
               Writelog Zmodem
            *                                  Call DSZ
               Dos Zmodem
            *                                  Return to original directory
            *
               Set CurDir = CONCAT( CONCAT( CurDrive , ':\' ), CurDir )
            *
               Chdir CurDir