MX5 Extended FOSSIL Functions (Int 14h)
(Also see FOSSIL.DOC for complete list of supported functions.)

AH = 0E0h (MX5 Extended FOSSIL Functions)
AL = Subfunction as Follows:

-------------------------------------------------------------
00h		Return MNP Status Block
-------------------------------------------------------------

Purpose:	Returns MNP related information.


On Entry	Register Contents
--------	-----------------
AH		E0h
AL		00h
DX		Port (0-3)

On Return	Register Contents
---------	-----------------
ES:BX		pointer to a structure as follows:

		mnp_active	db	?	;0=no, 1=yes
		level		db	?	;MNP level (2,4,5)
		series_id	db	?	;from other MNP entity
		tot_tx		dd	?	;total packets
		dup_tx		dd	?	;number of duplicates
		max_tx		dd	?	;max speed
		tot_rx		dd	?	;total packets
		dup_rx		dd	?	;number of duplicates
		max_rx		dd	?	;max speed

-------------------------------------------------------------
01h		Get/Set MNP Level
-------------------------------------------------------------

Purpose:	Gets or Sets the Maximum MNP level.

On Entry	Register Contents
--------	-----------------
AH		E0h
AL		01h
BL		MNP Level
		00h; None
		02h; Level 2
		04h; Level 4
		05h; Level 5 (default)
BH		00h; Get MNP Level
		01h; Set MNP Level
DX		Port (0-3)

On Return	Register Contents
---------	-----------------
BL		MNP Level (see BL above)

-------------------------------------------------------------
02h		Get/Set MNP Orig/Ans Mode
-------------------------------------------------------------

Purpose:	Gets or Sets Originate or Answer mode for
		an MNP connection.

On Entry	Register Contents
--------	-----------------
AH		E0h
AL		02h
BL		Orig/Ans Mode
		00h; Orig Mode (default)
		01h; Answer Mode
BH		00h; Get Mode
		01h; Set Mode
DX		Port (0-3)

On Return	Register Contents
---------	-----------------
BL		Mode (see BL above)

-------------------------------------------------------------
03h		Get/Set MNP Wait Tics
-------------------------------------------------------------

Purpose:	Gets or Sets number of tics (55 msecs/tic)
		after Carrier Detect raises until an MNP
		connection is attempted.

On Entry	Register Contents
--------	-----------------
AH		E0h
AL		03h
BL		MNP Wait Tics (default=14)
BH		0h; Get MNP Wait Tics
		1h; Set MNP Wait Tics
DX		Port (0-3)

On Return	Register Contents
---------	-----------------
BL		MNP Wait Tics (see BL above)

-------------------------------------------------------------
04h		Get/Set MNP Connect Sound Level
-------------------------------------------------------------

Purpose:	Gets or Sets wether MX5 will "play"
		a tune after an MNP connection.  If an
		MNP connection is successful, 3 high
		beeps are played.  If the MNP connection
		is not successful, a high/low beep is
		played.

On Entry	Register Contents
--------	-----------------
AH		E0h
AL		03h
BL		MNP Sound
		00h; Sounds are not played
		01h; Sounds are played (default)
BH		00h; Get Sound state
		01h; Set Sound state
DX		Port (0-3)

On Return	Register Contents
---------	-----------------
BL		MNP Sound state (see BL above)

-------------------------------------------------------------
05h		Remove MX5 from Memory
-------------------------------------------------------------

Purpose:	Requests MX5 to remove itself from memory.
		MX5 will de-initalize the current com port
		(hanging up if online), restore all hooked
		interupt vectors, and return it's MCB
		address so it may be freed.

**** Note:	Place the value returned in BX into ES and
****		call DOS function 49h to release MX5's MCB
****		(see example below).

On Entry	Register Contents
--------	-----------------
AH		E0h
AL		05h

On Return	Register Contents
---------	-----------------
BX		MCB segment address or 0 if unsuccessful


Example:	mov	ah,0e0h		;tell MX5 to uninstall
		mov	al,5
		int	14h
		cmp	bx,0
		je	cant_uninstall	;jump if unsuccessful
		mov	es,bx
		mov	ah,49h		;free MX5's memory
		int	21h

-------------------------------------------------------------
06h		Return MX5 Version Number
-------------------------------------------------------------

Purpose:	Returns the major and minor version of MX5

On Entry	Register Contents
--------	-----------------
AH		E0h
AL		06h
BX		00h

On Return	Register Contents
---------	-----------------
AH		Major version number
AL		Minor version number
BX		"MX" (4D58h)

Example:	mov	ah,0e0h		;see if MX5 is installed
		mov	al,6
		int	14h
		cmp	bx,'MX'
		jne	not_installed	;jump if MX5 not installed

-------------------------------------------------------------
07h		Wait CX Tics
-------------------------------------------------------------

Purpose:	Waits the number of tics specified in CX

On Entry	Register Contents
--------	-----------------
AH		E0h
AL		07h
CX		Tics to Wait

On Return	Register Contents
---------	-----------------
nothing