SanyCOMM - A FOSSIL Driver For The Sanyo MBC-55x


Written by Paul Kelly
Copyright 1987 by Paul A. Kelly,  ALL RIGHTS RESERVED

     This code is may be used and distributed in its unmodified form for ANY
NONCOMMERCIAL USE WHATEVER.  Modified versions of this software are NOT to
be distributed without the express written consent of the author.  You are
not allowed to sell or otherwise make money from the use of this software
without specific license from the author.

         Paul A. Kelly
         20 Forbes Road
         Trafford, PA  15085

     You may contact the author with bug reports or suggestions for improvement
via FidoNet mail at Net 129 Node 11 - First Sanyo Opus - for non-commercial
purposes only.

     If you wish to distribute this driver with a commercial communications 
package,  just write.  I will be glad to authorize free usage of this
type,  as long as no extra money is charged above the regular price of
package.  I wish to keep track of this kind of usage so that regular
updates can be distributed.

     This program implements the Fido/Opus/SEAdog Standard Inferface Layer
(FOSSIL) functions for the the Sanyo MBC-55x.  It is a complete implementation
of the FOSSIL driver as defined by version 5 of the FOSSIL specification.

     This driver implements all 27 functions defined in the current FOSSIL
spec.  It also implements the user appendage functions (the extended 
dispatcher).

     The current version of this driver ignores the port number passed in DL.

     SanyCOMM is upwardly compatible with the Sanyo MBC-55x BIOS,  int 14h,  
functions 0 - 4.  FOSSIL function 4 is a superset of int 14h,  function 4.

     SanyCOMM is now an installable device driver.  Put SanyCOMM.SYS in your
root directory and add the following statement to your CONFIG.SYS file:

  Device=SanyCOMM.SYS

     SanyCOMM completely replaces the standard Sanyo driver for devices AUX
and COM1,  and adds a device named FOSSIL$.  All i/o to these devices 
automatically is routed through the FOSSIL driver,  including redirected
console i/o.

     SanyCOMM has been tested fully in production use with BinkleyTerm 1.30,
Opus 1.10.ii/gamma,  and SEAdog v4.1.  It has also been fully tested for
proper operation with GT-PowerComm v13.00F.  The driver uses a 4k receive
buffer and a 1k transmit buffer.


                                                           Paul Kelly
                                                           01/30/88