Visual Zmodem
                 High-Quality External Protocol Driver
                 Copyright (C) 1992, by Jon R. Rickher
                          All Rights Reserved

                              DESCRIPTION
                             =============

Visual Zmodem is not merely a Zmodem driver. It also supports Xmodem CRC,
Xmodem Checksum, Xmodem 1K, Xmodem 1kG, Ymodem, Ymodem 1kG, and Kermit, as
well as Zmodem and ZmodemSprint (Zmodem with 8k blocks).

VZ is mostly compatible with Omen Technology's DSZ, but looks better and
does a few things (WWIV-status monitoring, Kermit, ZIP commenting or un-
commenting, and virus scanning [with MacAfee's SCAN.EXE]) that neither DSZ nor
GSZ support.

VZ is meant to provide BBS systems or communications programs without ZModem
or Kermit with those options, and to provide all BBS systems and
communications with a better-looking display during transfers, while using
memory economically. In addition, using VZ when downloading files should
help prevent the spread of viruses; since it's all automatic, you don't
have to worry about putting off your virus-scanning and then later forgetting
to do it at all and thereby letting a virus slip through the cracks.



                       USE WITH WWIVNET SOFTWARE
                      ===========================

Right now it is possible to use VZ with the WWIVnet software by renaming it
to DSZ.EXE and making sure you have 120k free RAM for network callouts. In
the future (in the next release of the WWIVnet software) VZ will be directly
supported and will not need to be renamed.


                          ZIP (UN)COMMENTING
                         ====================

Zip Commenting is enabled with the -a option. If the received file is a valid
ZIP file, and a file called VZ.CMT exists in the current directory, then
this will be used for the ZIP comment. If no such file exists then any ZIP
comment will be automatically stripped.


                        AUTOMATIC VIRUS SCANNING
                       ==========================

To use the virus-scanning on received files, SCAN.EXE must be in your path.
In addition, for each archive type you wish to be automatically extracted
and scanned, you will need to have in your path the appropriate archive
extractor. VZ looks for the following:

                    Archive     VZ will look for
                    -------     ----------------
                      ZIP       PKUNZIP.EXE
                      ARC       PKXARC.COM
                      ARJ       ARJ.EXE
                      LZH       LHA.EXE
                      PAK       PAK.EXE

All other files will be scanned as a single file with no extraction if the
file's extension does not match one of the above. Of course, the -v option
must be used. VZ maintains a file called VZSCAN.LOG that shows the results
of the scanning. If a virus is detected there will be an alarm, and the file
will be deleted.

                         SYSTEM REQUIREMENTS
                        =====================

Visual Zmodem should work on any IBM or IBM compatible computer with a serial
port, including IBM PS/2's, that has at least 256K of memory and a Hercules
or CGA monitor or better. VZ works best on '286-class machines or better that
have at least 512k of expanded memory.

Memory requirements vary somewhat. If you do not enable ZmodemSprint then
VZ requires about 120K of memory. Enabling ZmodemSprint adds another 32k
to the memory requirment. Enabling the virus-scanning boosts the memory
requirement more than anything, because the new PKUNZIP itself requires
185k of memory. Both VZ and PKUNZIP make use of expanded memory (EMS) and
will run better on machines equipped with it.


                               REGISTRATION
                              ==============

VZ is not public domain. It is ShareWare. The evaluation period is one month.
If you find that you are using it after one month has gone by then you are
obligated to delete all but the original archive that contained VZ, or
register it. Registration is a measely $10. If your integrity isn't worth
$10...well, most peoples' integrity *is* worth more than that and I hope
you're one of them. Using VZ without registering also does damage to the
ShareWare concept in general, so please don't abuse or in the end everyone
ends up losing. Really, with this low of a price, there's no excuse for
not registering.

VZ may be distributed freely, so long as it is distributed only in its
original archive and so long as this archive is left unmodified. If you
charge a fee for handling costs (disk, whatever), then this fee may be no
more than $5 for a disk containg VZ.

Registrations may be mailed to:

   Jon R. Rickher
   c/o The Fellowship
   7035 Ethel
   St. Louis, MO 63117

This does *not* get a disk mailed to you. Rather, this will give you access
to the latest registered VZ files when you get an account on The Fellowship.
The phone number for The Fellowship is 314-644-5777. If you wish a disk mailed
to you then include an extra $5 (a total of $15). This includes international
orders. This $5 only gets you *one* mailing, however. Additional upgrades
for registered users may be downloaded or you may send another $5 along with
name and registration number for an additional mailing.

Note that I do *not* intend to have a zillion different releases coming out
with a new one every four days. I will only release new versions that are
*significantly* changed and improved.


                            THE DISPLAY WINDOWS
                           =====================

The display is easy to understand - there is one window for the current file
being transferred. When sending file(s), if the protocol supports batch
transfers, there is also a batch status window. If you use the -w option
(see below) then there will also be a WWIV status window if CHAIN.TXT is in
the current directory. You may toggle from active window to another window
(making it the "active" window) with the TAB or SHIFT-TAB keys. Windows may
be moved around with the cursor keys (although no window may be moved off
the screen). Windows may be tiled and may overlap. For performance reasons
(it takes time to do some of the windowing), it is best to leave the File
Status window the active window, but you can play around.


                      PARAMETER DESCRIPTIONS, DETAILED
                     ==================================

Running VZ.EXE from a DOS prompt with no parameters shows a simple summary of
available options. These are detailed as follows:

   --------------------------------------------------------------------------

   port <portnum>        Use serial communications port number <portnum>

   Example               VZ port 3 sz *.*
   Default               port 1
   Note                  Only the standard base addresses are supported at
                           this time. PS/2's use different addresses than
                           "normal" computers. The -2 option (see below)
                           can compensate for computers that are inaccurately
                           reported as being PS/2 machines.

   --------------------------------------------------------------------------

   portx base,IRQ        Specify a new base address and IRQ number for the
                           port defined by the "port portnum" parameter.

   Example               vz port 2 portx $2e8,3 sz *.*
   Default               N/A (uses "standard" base addresses and IRQ's for
                           com ports - almost always works)
   Note                  This parameter sequence is only necessary if your
                           serial port is set to use a nonstandard base
                           address and/or IRQ.

   --------------------------------------------------------------------------

   speed <bpsrate>       Use <bpsrate> when communicating with the chosen
                           serial port

   Example               VZ speed 2400 sz *.*
   Default               Whatever speed the computer is currently using to
                           communicate with the chosen serial port.
   Note                  This option is very rarely necessary. Unless you're
                           *sure* you need to change the BPS rate from its
                           current status, it is best to omit this option.

   --------------------------------------------------------------------------

   restrict              Disallows pathnames, and any filename containing
                           a "/" or "\".

   Example               VZ restrict rz
   Default               Off
   Note                  This option is rarely needed.

   --------------------------------------------------------------------------

   est <speed>           Estimate transfer efficiency based on a modem-to-
                           modem speed of <speed>.

   Example               VZ est 9600 sz *.PAS
   Default               Estimate based on DTE-DCE speed (speed with which
                           the computer is communicating with the serial
                           port).
   Note                  If you have the serial port "locked" then this
                           option is useful for reporting transfer efficiency
                           accurately. To maintain DSZ commandline-
                           compatiblility if the <speed> parameter is 0, then
                           VZ will look ahead one extra parameter.

   --------------------------------------------------------------------------

   -a                    Toggles ZIPfile (un)commenting.

   Example               VZ port 4 -a rz C:\DLOADS
   Default               Off
   Note                  If a file called VZ.CMT exists in the current
                           directory then this will be used for the ZIP
                           comment if this option is enabled. If this
                           option is enabled and no such file exists then
                           ZIP comments will be stripped from incoming
                           files. Very handy for BBSes that do not desire
                           ZIP comments or wish to have a ZIP comment of
                           their own. Registered version only.

   --------------------------------------------------------------------------

   -d                    Toggles carrier detect monitoring on/off.

   Example               VZ -d sz *.*
   Default               On
   Note                  Some modems improperly report their carrier detect
                           status. This option will toggle the automatic
                           carrier detect checking and may be useful when
                           using such modems.

   --------------------------------------------------------------------------

   -e                    Toggles exploding windows on/off.

   Example               VZ -e port 2 sz *.TXT
   Default               Off

   --------------------------------------------------------------------------

   -f                    Toggles 16550A[FN] UART buffering.

   Example               VZ -f port 1 est 2400 rz
   Default               On
   Note                  The UART type is autodetected by default and the
                           16550 UART is used with a trigger level of 14.

   --------------------------------------------------------------------------

   -n                    Toggles on or off only writing newer files.

   Example               VZ -n port 4 rz
   Default               On
   Note                  If this option is on (default) then only newer
                           files with the same name will be written.

   --------------------------------------------------------------------------

   -r                    Toggles on or off Zmodem crash recovery (resume).

   Example               VZ -r rz *.PAS
   Default               On
   Note                  This allows an interrupted file transfer to be
                           resumed after an interruption.

   --------------------------------------------------------------------------

   -s                    Toggles on or off "squeaky" windows.

   Example               VZ -s port 2 sz *.ZIP
   Default               Off
   Note                  This option causes a sound when windows are opened
                            or closed. An aesthetic thing only.

   --------------------------------------------------------------------------

   -v                    Toggles on or off automatic virus-scanning.

   Example               VZ port 2 -v rz
   Default               Off
   Note                  Only the registered version has this option. A status
                           log called VZSCAN.LOG is kept (in the current
                           directory) that shows which files were scanned and
                           which contained viruses or were "clean". Infected
                           files are deleted if this option is toggled on.
                           MacAfee's SCAN.EXE must be in the current directory
                           or exist on your PATH for this option to function.

   --------------------------------------------------------------------------

   -w                    Toggles on or off WWIV status viewing.

   Example               VZ -w port 2 rz
   Default               Off
   Note                  This option, when enabled, causes VZ to look in the
                            current directory for a file called CHAIN.TXT.
                            If this file exists then it is read and some
                            information about the current user is shown on
                            the screen, and that user's time left online is
                            tracked by VZ. If it expires then any transfer is
                            aborted. This can prevent bad line conditions
                            from causing a caller to "hog" the line for
                            excessive amounts of time.

   --------------------------------------------------------------------------

   -2                    Toggles on or off automatic PS/2 detection.

   Example               VZ -2 rz
   Default               On
   Note                  The default (on) will always properly detect if
                           VZ is running on a PS/2 machine (and all base
                           addresses and IRQ numbers will be adjusted
                           accordingly). However, some standard AT machines
                           improperly report themselves as PS/2's, which
                           could cause a port address or IRQ conflict. If
                           this is a problem, then this option will solve it.

   --------------------------------------------------------------------------

   -8                    Toggles on or off ZmodemSprint.

   Example               VZ -8 sz *.ARJ
   Default               Off
   Note                  This option can increase overall throughput by
                           using 8k blocks with Zmodem transfers. Although
                           this is not part of the defined Zmodem standard,
                           some other Zmodem implementations do support
                           large-block Zmodem transfers, so it is supported
                           here as well. Do not use this option, though,
                           unless you are sure the other side can handle
                           it, or there will be errors. Registered version
                           only.

   --------------------------------------------------------------------------

   on                    Use CTS/RTS flow control

   Example               VZ on sz *.zip
   Default               CTS/RTS is enabled by default if the connect speed
                           is greater than 2400 bps, otherwise XON/XOFF
                           is enabled.

   --------------------------------------------------------------------------

   off                   Turn off all flow control

   Example               VZ off rz
   Default               Flow control is XON/XOFF for connect rates of 2400
                           or slower or CTS/RTS if the connect rate is
                           higher by default. This option overrides the
                           defaults and turns off all flow control.

   --------------------------------------------------------------------------

   both                  Turn on XON/XOFF and CTS/RTS flow control

   Example               VZ both sz *.pak
   Default               See description for "off".

   --------------------------------------------------------------------------

   slow                  Use CTS/RTS flow control but lower the RTS signal
                           during disk access. This should allow systems with
                           unusually slow hard drives or floppy drives,
                           or systems multitasking heavily, to eradicate
                           some or all data input errors during a transfer.

   --------------------------------------------------------------------------
   Transferring Files, Protocol and Direction Selection:

   sz             Send Zmodem
   rz             Receive Zmodem

   sb             Send Ymodem
   rb             Receive Ymodem

   sx             Send Xmodem
   rx             Receive Xmodem

   sb -g          Send Ymodem 1kG
   rb -g          Receive Ymodem 1kG

   sx -k          Send Xmodem 1k
   rx -k          Receive Xmodem 1k

   sx -g          Send Xmodem 1kG
   rx -g          Receive Xmodem 1kG

   --------------------------------------------------------------------------

   Transferring Files, Filename Selection:

   The last parameter of the commandline should be either a filemask (eg,
   "C:\*.*" or a filename or (if you're receiving, and the protocol
   allows it [Ymodem, Kermit, Zmodem]) no filemask or filename at all.

   In addition, when receiving you may simply specify a directory and
   all transferred files will be placed there.

   For protocols that support batch transfers you may also specify a file
   list if you precede the name of the file list with the "@" symbol (eg,
   "VZ port 3 -es sz @C:\DLOADS\FILES.LST"). Any files listed in this
   listfile, if they exist, will be sent. Note that files in this list
   must not contain DOS wildcards.

   --------------------------------------------------------------------------

   Example complex send commandline:

   VZ port 2 est 9600 -waves28 sz @C:\WWIV\FILES.DL

   This commandline would use port 2 with the standard base address and IRQ
   for a non-PS/2 system, estimating transfer times based on a 9600 bps speed,
   with WWIV status, exploding windows, "squeaky" windows, no PS/2 detection,
   and 8K Zmodem blocks - sending all files that actually exist that are
   listed in the file C:\WWIV\FILES.DL. If a file called VZ.CMT exists in
   the current directory, this would be used as a zip comment for received
   files, else zip comments would be stripped from incoming ZIP files. All
   received files (if this were a receive commandline) would also be scanned
   for viruses using MacAfee's SCAN.EXE utility and infected files would
   be deleted.

   --------------------------------------------------------------------------

   Included batch files:

   Name             Description
   -------------    ---------------------------------------------------------
   VZS.BAT          Standard batch file for using VZ within Telix, sending
   VZR.BAT          Standard batch file for using VZ within Telix, receiving
   VZS8.BAT         Batch file for using VZ with 8k Zmodem within Telix,
                      sending
   VZR8.BAT         Batch file for using VZ with 8k Zmodem within Telix,
                      receiving

   Edit the batch files to reflect your communications port. You can also
   specify a download directory for the receive batch files, and disable
   the virus-scanning, zip-commenting, exploding windows, and squeaky windows
   by removing the appropriate option.

   --------------------------------------------------------------------------