SET COMBASE=nnnn
       Specifies the I/O port base for the active COM port in decimal
       format. COM1 is usually 1016, COM2 is usually 760.

     SET COMIRQ=n
       Specifies the IRQ level for the active COM port in decimal
       format.  COM1 usually uses IRQ 4 and COM2 uses IRQ 3.

   For com ports other than the normal COM1 and COM2, you will need insert
   the following statements in your BOARD.BAT file:

        SET COMBASE=nnnn    ;port base I/O address (decimal)
        SET COMIRQ=n        ;port IRQ setting

   Use these SET statements in conjunction with the com port setting
   that's in your PCBOARD.DAT file, if your running PCBoard 14.x.