GEnie Aladdin Script Language
                               User's Guide

     If you are familiar with Aladdin, you may want to write your own
  scripts to perform functions that Aladdin does not do for you now. You
  can use scripts to access specific areas on GEnie. Aladdin's script
  language is quite simple to use. As in any programming language, you
  will need to know the commands that you can use and the proper way to
  invoke them.

     You will find many pre-written scripts available in the Aladdin
  Software Libraries and Bulletin Board on GEnie. If you have a problem
  while writing a script and this manual does not answer a question, ask
  for help in the Aladdin Bulletin Board. Users are willing to offer their
  help with writing your scripts.


  GENERAL SCRIPT LANGUAGE GUIDELINES

  The following general guidelines and rules apply to all scripts,

  - You may only have one command per line.

  - Command words must be separated by at least one <TAB> or space
    character.

  - The language is not case-sensitive. Command words can be any
    combination of upper- and lower-case characters.

  - If a line does not contain any commands it must either be blank or
    have a semicolon ";" or a colon ":" as the first non-blank
    character. If the line begins with a colon then the line is
    considered to be a label or place-marker within the script that can
    be referred to with the GOTO or CALL commands. If the line begins
    with a semi-colon then the line is a comment and is ignored during
    script execution.

  - Any text remaining in a line after the formal command is ignored.
    This makes for easy commenting of script commands without having to
    worry about special delimiting characters.

  - In the descriptions of the commands, {string} refers to any sequence
    of characters surrounded by a pair of delimiters. A delimiter is any
    single character. If the left-hand delimiter is anything other than
    the (, [, {, <, " or ` characters, then the right-hand delimiter
    must be the same as the left-hand delimiter. If one of these five
    characters is used as a left- hand delimiter, then the right-hand
    delimiter must be the corresponding ), ], }, >, " or ',
    respectively. The text within the delimiters must not contain the
    right delimiter character.

  - In a {string}, the symbols "^A" through "^Z" are converted into the
    corresponding control characters Ctrl-A through Ctrl-Z.

  - All occurrences of the characters %0 through %9 in any script are
    replaced with the corresponding user-defined string equivalent.
    User-defined strings 0 through 9 are created using the SETSTRING,
    GETKEY or GETSTRING commands. If you want to use the % character
    followed by a digit in your scripts without it being replaced for a
    user-defined string, use the %% combination instead. For example, %0
    refers to user-defined string number 0, but %%0 defines a string
    with the characters % and 0.


  COMMANDS AND THEIR USES

     The Aladdin script commands are explained in alphabetical order. An
  example of each command is provided to get you started. Included is a
  list of related commands, if any. In the descriptions of the commands,
  the following notations are used:

     {filename} - is any valid DOS filename may be used, including drive
                  and/or directory information.

         {path} - is any valid drive and/or directory.

       {string} - is any sequence of characters surrounded by a pair of
                  delimiters. (see above)

       {prompt} - is any single character without delimiters.

        {label} - is any sequence of characters beginning with a colon (:)
                  and not containing spaces or tabs.

  {script name} - is any sequence of characters up to 31 characters long.

         {time} - is a time in HH:MM:SS 24-hour format.

      {seconds} - is a number representing a duration of time, optionally
                  includes a decimal point.

          {day} - is SUN, MON, TUE, WED, THU, FRI, or SAT.

         {page} - is a GEnie product page number.

        {digit} - is a character 0 through 9.  Some digits cannot be used
                  in some commands.

    {A | B | C} - is option A or B or C.

                   ---------------------------------

  Command: ALARM
  Arguments:  None
  Description:   Causes Aladdin to issue a series of beeps that will
                 continue until a key is pressed.

  Example: LOG ON
           IF SUCCESS
              BEEP
           ELSE
              NOTE "Log on not successful. Press any key to continue."
              ALARM
           ENDIF

  Related commands: BEEP

                   ---------------------------------

  Command: ASCII
  Arguments:  UPLOAD {filename}
  Description:   UPLOAD tells Aladdin to send the ASCII file you specify
                 from your PC to GEnie at this point in the script. You can
                 send the file to a Bulletin Board, Software Library, or
                 another user through GE Mail. You must move to the area in
                 GEnie where you want the file sent before you transfer
                 edthe file.

                 NOTE: You may need to perform special steps before you can
                 transfer the file. For example, when sending a file in a
                 GE Mail message or Bulletin Board reply, you must type *UP
                 at a line-number prompt. You will see "READY FOR INPUT" on
                 the screen, then you can continue with ASCII UPLOAD.

  Example: LOG ONTO "110;1"
           SENDCOMMAND "SET 9"
           SENDLINE "REP 2"
           WAITFOR "1>"
           SENDLINE "*UP"
           WAITFOR "READY FOR INPUT"
           ASCII UPLOAD "MSG.TXT"
           SEND "^C"
           WAITFOR ">"
           SENDCOMMAND "*S"

  Related commands: CAPTURE, XMODEM, ZMODEM

                   ---------------------------------

  Command: BEEP
  Arguments:  None
  Description:   Causes Aladdin to sound one short beep.

  Example: LOG ON
           IF SUCCESS
              BEEP
           ELSE
              ALARM
           ENDIF

  Related commands: ALARM

                   ---------------------------------

  Command: CALL, RETURN
  Arguments:  {label}
  Description:   CALL temporarily transfers execution of the script to
                 another point in the script. The {label} argument
                 references a line within the script which begins with a
                 colon ":" character and is immediately followed by a
                 label name. A label can be any sequence of characters
                 not containing spaces or tabs. When Aladdin finds a
                 RETURN, it will resume processing in the script with
                 the line following the CALL command.

  Example: CALL Step1
           CALL Step2
           GOTO EndofScript
           :Step1
           CLEAR
           RETURN
           :Step2
           NOTE "This is Step 2"
           RETURN
           :EndofScript
           ENDSCRIPT

  Related commands: GOTO

                   ---------------------------------

  Command: CAPTURE
  Arguments:  {filename}
  Description:   CAPTURE tells Aladdin to write any information it
                 receives from, or sends to, GEnie to a file on your
                 disk. You must specify the name of this file in the
                 argument. If the capture file already exists, the
                 incoming text will be appended to the end of the
                 existing file. If a capture file is already open either
                 because of a previous CAPTURE command or by the use of
                 the "A" option in the Terminal Mode menu, the current
                 capture file will be closed before the new one is
                 opened. The capture stops when Aladdin finds the
                 command ENDCAPTURE in the script.

  Example: LOG ONTO "8003"
           SENDLINE "6"
           ERASEFILE "holidays.txt"
           CAPTURE "holidays.txt"
           WAITFORPROMPT
           ENDCAPTURE

  Related commands: ENDCAPTURE, ERASEFILE, IF EXIST, SNAPSHOT

                   ---------------------------------

  Command: CLEAR
  Arguments:  None
  Description:   Causes Aladdin to blank out or clear the terminal mode
                 screen.

  Example: CLEAR
           NOTE "The screen should be blank,"
           NOTE "except for these three lines"
           NOTE "of text."

  Related commands: None

                   ---------------------------------

  Command: COMMANDMODE
  Arguments:  {ON | OFF}
  Description:   Tells Aladdin if you want to see the GEnie menus or not
                 during the script. If you issue a COMMANDMODE ON
                 command, Aladdin will always attempt to switch GEnie
                 into command mode anytime that it sees an "Enter #"
                 prompt. If instead you issue a COMMANDMODE OFF command,
                 Aladdin will not try to make the switch.

  Example: LOG ONTO "8005"
           COMMANDMODE ON
           WAITFORPROMPT
           NOTE "This is a prompt in COMMANDMODE"
           COMMANDMODE OFF
           IF CURRENTLINEHAS "Enter #"
           ELSE
             SENDLINE "C"
           ENDIF
           NOTE "This is a normal menu."

  Related commands: None

                   ---------------------------------

  Command: ECHO
  Arguments:  {ON | OFF}
  Description:   If the ECHO is ON, Aladdin will show you every command
                 it issues during the script. If the ECHO is OFF, you
                 will only see information that is transmitted across
                 the modem. The default is for ECHO ON, and this is
                 useful if you are trying to track down a problem in a
                 script.

  Example: SCRIPT 8 GEnie Demo Script
           ECHO OFF
           .
           .
           .

  Related commands: None

                   ---------------------------------

  Command: ENDCAPTURE
  Arguments:  None
  Description:  Ends a CAPTURE

  Example: LOG ONTO "8003"
           SENDLINE "14"
           ERASEFILE "holidays.txt"
           CAPTURE "holidays.txt"
           WAITFORPROMPT
           ENDCAPTURE

  Related commands: CAPTURE

                   ---------------------------------

  Command: ENDSCRIPT
  Arguments:  None
  Description:   Shows Aladdin when the script is finished. Every script
                 MUST have the ENDSCRIPT command at the end.

  Example: SCRIPT Short script
           CLEAR
           NOTE "We are testing a quick script."
           ENDSCRIPT

  Related commands: SCRIPT

                   ---------------------------------

  Command: ERASEFILE
  Arguments:  {filename}
  Description:   Tells Aladdin to find a file name you specify and erase
                 it from the disk.

  Example: IF EXIST "LOAN.TXT"
             ERASEFILE "LOAN.TXT"
           ENDIF
           SENDLINE "M8008;2"
           CAPTURE "LOAN.TXT"
           WAITFORPROMPT
           ENDCAPTURE

  Related commands: SNAPSHOT, CAPTURE, IF EXIST

                   ---------------------------------

  Command: EXITALADDIN
  Arguments:  None
  Description:   Ends current script, exits Aladdin and returns you
                 to your DOS prompt.

  Example: SCRIPT 5 Morning News
           WAITUNTIL 05:00
           LOG ONTO "8013"
           SENDLINE "1"
           ERASEFILE "WORLDNWS.TXT"
           WAITFOR "WORLD NEWS SUMMARIES"
           CAPTURE "WORLDNWS.TXT"
           WAITFORPROMPT
           ENDCAPTURE
           SENDLINE "1,2,3,4,5"
           WAITFOR "=START="
           CAPTURE "WORLDNWS.TXT"
           WAITFOR "WORLD NEWS SUMMARIES"
           ENDCAPTURE
           WAITFORPROMPT
           SENDCOMMAND "P"
           LOG OFF
           EXITALADDIN
           ENDSCRIPT

  Related commands: none

                   ---------------------------------

  Command: GETKEY
  Arguments:  {digit}
  Description:   Aladdin will wait until a single character is entered
                 from the keyboard when it sees this command, it will then
                 save the value of that key in a user-defined string (0 -
                 9). You may not have more than 10 strings in use at a
                 given time.

  Example: NOTE "Do you wish to Continue (Y/N)?"
           GETKEY 1
           IF STRING 1 IS "N"
              GOTO ENDOFSCRIPT
           ENDIF
           NOTE "Continuing with script"
           :EndofScript
           ENDSCRIPT

  Related commands: GETSTRING, SETSTRING, IF STRING

                   ---------------------------------

  Command: GETSTRING
  Arguments:  {digit}
  Description:   This command works almost the same as the GETKEY
                 command except it will store a string of characters
                 instead of just one character.

  Example: NOTE "Enter your nick-name?"
           GETSTRING 1
           IF STRING 1 IS ""
           ELSE
             NOTE {You entered "%1".}
           ENDIF

  Related commands: GETKEY, SETSTRING, IF STRING

                   ---------------------------------

  Command: GOTO
  Arguments:  {label}
  Description:   Transfers execution of the script to another point in
                 the script designated by the {label}. The {label} works
                 the same as in the CALL command.

  Example: NOTE "Do you wish to Continue (Y/N)?"
           GETSTRING 1
           IF STRING 1 IS "N"
              GOTO ENDOFSCRIPT
           ENDIF
           NOTE "Continuing script..."
           :EndofScript
           ENDSCRIPT

  Related commands: CALL, RETURN

                   ---------------------------------

  Command: HANGUP
  Arguments:  None
  Description:   Tells Aladdin to disconnect the modem from the phone
                 line immediately. It is not the same as LOG OFF.

  Example: IF ONLINE
             HANGUP
           ELSE
              ENDSCRIPT

  Related commands: LOG

                   ---------------------------------

  Command: HHH
  Arguments:  {ON | OFF}
  Description:  OFF tell Aladdin not to send out three H's to get U#= login
                prompt. This is useful when creating an alternate log on
                script to access GEnie in places where the HHH is not need
                to get the U#= prompt.

  Example:  Script 3 Japan Logon Script
            ;GEnie Japan(NEC) C & C VAN Net
            ECHO OFF
            HHH OFF
            SENDLINE "ATZ"
            WAITFOR "OK"
            PAUSE 1
            SENDLINE "ATDT phone #"
            WAITFOR "CONNECT"
            PAUSE 7
            SENDLINE "VANGENIE"
            ENDSCRIPT

  Related commands: None

                   ---------------------------------

  Command: HIDE
  Arguments:  {ON | OFF}
  Description:   If HIDE is ON, any text received from the remote system
                 will be displayed with the word "SECRET", repeating
                 over and over again for all text received. This is good
                 for masking passwords, etc.

  Example: WAITFOR "U#="
           HIDE ON
           SENDLINE "XAA12345,ABCDEFGH"
           PAUSE 1
           HIDE OFF

  Related commands: None

                   ---------------------------------

  Command: IF, ELSE, ENDIF
  Description: The IF command provides the Aladdin Script Language with a
               feature which is critical to any programming language, the
               ability to make simple decisions and take courses of action
               based on the state or result of a condition. The IF command
               does just that. The syntax of the IF command is:

                           IF {condition}
                           ...
                           ELSE
                           ...
                           ENDIF

               The {condition} argument can be one of the following
               keywords:

               SUCCESS                              DATAWAITING
               ONLINE                               KEYWAITING
               CURRENTLINEHAS {string}              EXIST {filename}
               STRING {digit} {IS | HAS} {string}   DAYOFWEEK IS {day}
               MAILWAITING                          MAILFOUND


               Each one of these conditions is evaluated as a TRUE or
               FALSE result. If the condition returns a TRUE result, the
               statements within the IF command and the first ENDIF
               encountered in the script will be executed. If the
               condition argument returns a FALSE result and there is no
               ELSE command between the IF command and the next ENDIF
               command, the statements are ignored and execution continues
               on the first line after the ENDIF command. We will cover
               each one of the conditions separately in the next few pages
               of this manual and present examples for each possible
               condition argument as well. All IF commands must have a
               matching ENDIF command.

               The ELSE optional command tells Aladdin that if the
               condition evaluated in the IF command is evaluated to a
               FALSE result, execution of the script will jump to the
               first line immediately after the ELSE command and continue
               from that point. If the condition is evaluated as a TRUE
               result, Aladdin will execute the statements immediately
               after the IF command. When it gets to the ELSE command, all
               statements up to the next ENDIF command are ignored, and
               execution continues on the next line immediately after the
               ENDIF command. The ELSE command basically extends Aladdin's
               decision-making powers from a simple "if this condition is
               TRUE do this" to a more complete "if this condition is TRUE
               do this; if it is FALSE, do this instead".

               The ENDIF command marks the end of a block of instructions
               related to the previous IF command. Again, all IF commands
               must have a matching ENDIF command. IF commands may be
               nested, which means that you can have IF commands within
               other IF commands.


  Command: IF CURRENTLINEHAS
  Arguments:  {string}
  Description:   Tells Aladdin to check the last line that it received
                 from GEnie for a specific {string} of text. The
                 comparison performed by Aladdin is case-sensitive,
                 which means that you must specify the string you are
                 looking for in the exact combination of upper- and
                 lower-case characters that you want to match.

  Example: IF CURRENTLINEHAS "Enter #"
           ELSE
             SENDLINE "C"
           ENDIF

  Related commands: All IF Commands

                   ---------------------------------

  Command: IF DATAWAITING
  Arguments:  None
  Description:   Checks to see if there is any data still in the buffer
                 that GEnie has sent but Aladdin has not yet processed.

  Example: SNAPSHOT "PICTURE.PIC"
           IF DATAWAITING
              SENDLINE " "
              WAITFORPROMPT
           ENDIF

  Related commands: All IF Commands

                   ---------------------------------

  Command: IF DAYOFWEEK IS
  Arguments:  {day}
  Description:   You may have a script that you run once a week and do
                 not want to run it on the wrong day. This tells Aladdin
                 to check what day it is, before it continues. Remember:
                 the date on your PC's DOS clock must be correct for
                 this to work properly.

  Example: IF DAYOFWEEK IS SAT
              LOG ON
           ELSE
              GOTO ENDOFSCRIPT
           ENDIF
           IF MAILFOUND
              BEEP
           ELSE
              LOG OFF
           ENDIF
           :ENDOFSCRIPT
           ENDSCRIPT

  Related commands: All IF Commands

                   ---------------------------------

  Command: IF EXIST
  Arguments:  {filename}
  Description:   Tells Aladdin to check your disk and see if a file
                 specified by the name in the {filename} is already stored
                 on your PC.

  Example: SETSTRING 2 "CONTRACT.TXT"
           SENDLINE "M8005;2"
           IF EXIST "%2"
              ERASEFILE "%2"
           ENDIF

  Related commands: All IF Commands

                   ---------------------------------

  Command: IF KEYWAITING
  Arguments:  None
  Description:   Tells Aladdin to check the keyboard buffer on your PC
                 and see if there are any keystrokes stored that have
                 not been processed.

  Example: KEYWAITING ON
           NOTE "Press any key to exit this script."
           CAPTURE "SCPTFILE.TXT"
           IF KEYWAITING
              ENDCAPTURE
              GOTO ENDOFSCRIPT
           ENDIF

  Related commands: All IF Commands, KEYWAITING, MONITOR

                   ---------------------------------

  Command: IF MAILFOUND
  Arguments:  None
  Description:  It then allows you to specify what to do if Aladdin has
                retrieved mail. Aladdin will only retrieve if the "Always
                pick up mail" option is set to YES.

  Example: LOG ON
           PERFORM 1
           IF MAILFOUND
             BEEP
             BEEP
             BEEP
           ENDIF
           ENDSCRIPT

  Related commands: All IF Commands

                   ---------------------------------

  Command: IF MAILWAITING
  Arguments:  None
  Description:  It then allows you to specify what to do if there is unread
                mail waiting. Note that Aladdin will always check for mail
                when it logs on to GEnie as a result of using the LOG ON or
                LOG ONTO commands.

  Example: LOG ON
           IF MAILWAITING
             BEEP
             BEEP
             BEEP
           ENDIF
           PERFORM 1
           ENDSCRIPT

  Related commands: All IF Commands

                   ---------------------------------

  Command: IF ONLINE
  Arguments:  None
  Description:   Tells Aladdin to see if the modem has a Carrier
                 Detected or not.

  Example: IF ONLINE
              SENDCOMMAND "M8004;2"
           ELSE
              LOG ON
           ENDIF

  Related commands: All IF Commands

                   ---------------------------------

  Command: IF STRING
  Arguments:  {digit} {HAS | IS} {string}
  Description:   If this is used with the HAS option, Aladdin will check to
                 see if a specific {string} occurs within the specified
                 user-defined string (0 - 9). If it is used with the IS
                 option, Aladdin will check to see if the specified
                 user-defined string (0 - 9) matches a specific {string}.
                 The comparison performed by Aladdin is case-sensitive,
                 which means that you must specify the string you are
                 looking for in the exact combination of upper- and
                 lower-case characters that you want to match.

   Example: NOTE "Do you wish to Continue (YES/NO)?"
            GETSTRING 1
            IF STRING 1 HAS "y"
              SETSTRING "Y"
            ENDIF
            IF STRING 1 HAS "Y"
              NOTE "Continuing..."
            ELSE
               GOTO ENDOFSCRIPT
            ENDIF
            PERFORM 1
            :EndofScript
            ENDSCRIPT

  Related commands: All IF Commands, GETSTRING, SETSTRING

                   ---------------------------------

  Command: IF SUCCESS
  Arguments:  None
  Description:   Tells Aladdin to make sure the last command was
                 executed properly before it continues.

  Example: LOG ON
           IF SUCCESS
              NOTE "You are now online!"
           ELSE
              NOTE "You did not get online!"
           ENDIF

  Related commands: All IF Commands

                   ---------------------------------

  Command: KEYWAITING
  Arguments:  {ON | OFF}
  Description:   Determines whether Aladdin should check the keyboard
                 buffer for its usual special keys such as F5-Stay
                 Online and ESC-Exit Script. The KEYWAITING condition
                 defaults to check for these special keys during the
                 execution of any script unless the script has the
                 command KEYWAITING ON, which will place any key pressed
                 during the script at the end of the buffer. To process
                 this keypress, the script would also have to invoke the
                 command IF KEYWAITING.

  Example: KEYWAITING ON
           NOTE "Press any key to exit this script."
           CAPTURE "SCPTFILE.TXT"
           IF KEYWAITING
           ENDCAPTURE
              GOTO ENDOFSCRIPT
           ENDIF

  Related commands: IF KEYWAITING, MONITOR

                   ---------------------------------

  Command: LOG
  Arguments:  {ON | ONTO {page} | OFF}
  Description:   LOG ON will call GEnie and go to the TOP Menu. LOG OFF
                 tells Aladdin to enter the BYE command at a GEnie prompt
                 and finish the session. LOG ONTO will log you on to GEnie
                 and take you directly to a GEnie page number and,
                 optionally, a selection within that page number. If you
                 are already logged on to GEnie, Aladdin issues an "M"
                 command, instead, to move to that page and optional
                 selection number.

  Example: LOG ONTO "200"
           IF MAILFOUND
              SENDLINE "2"
              CAPTURE "MAIL.TXT"
              WAITFORPROMPT
              ENDCAPTURE
           ELSE
              LOG OFF
           ENDIF
           ENDSCRIPT

  Related commands: HANGUP

                   ---------------------------------

  Command: MONITOR
  Arguments:  None
  Description:   Tells Aladdin to display each character on the screen
                 as it is received from GEnie.

  Example: KEYWAITING ON
           MONITOR
           IF KEYWAITING
           GOTO ENDOFSCRIPT
           ENDIF

  Related commands: none

                   ---------------------------------

  Command: NOTE
  Arguments:  {string}
  Description:   Causes Aladdin to display your message on the screen
                 without interfering with the process of the script.

  Example: LOG ON
           IF SUCCESS
              NOTE "You are now online!"
           ELSE
              NOTE "You did not get online!"
           ENDIF

  Related commands: None

                   ---------------------------------

  Command: PAUSE
  Arguments:  {seconds}
  Description:   Causes Aladdin to wait for a specified period of
                 seconds, or fraction of a second, before it processes
                 the next command.

  Example: IF STRING 1 IS "N"
              NOTE "We will not run the Loan Demo!"
              PAUSE 1.5
              GOTO ENDOFSCRIPT
           ELSE
              GOTO CONTINUE
           ENDIF
           :CONTINUE

  Related commands: None

                   ---------------------------------

  Command: PERFORM
  Arguments:  {digit}
  Description:   Tells Aladdin to run another script you have created,
                 come back to this script, and continue from the line
                 following the PERFORM command. Scripts 1 and 2 are the
                 Aladdin Automatic passes; while Scripts 3 through 9
                 would be user defined.

  Example: IF STRING 1 IS "Y"
              NOTE "We will run the Loan Demo."
              PAUSE 1
              PERFORM 4
           ELSE
              GOTO ENDOFSCRIPT
           NOTE "We are back in the GEnie Demo."
           :ENDOFSCRIPT

  Related commands: SCRIPT, CALL, RETURN, GOTO

                   ---------------------------------

  Command: QUOTES
  Arguments:  {ON | OFF}
  Description:   If you use QUOTES ON, Aladdin will change any single
                 quotation mark (') GEnie sends to double quotation
                 marks ("). This is for use with the NewsGrid Service.
                 The default is QUOTES OFF, which means Aladdin will not
                 change any of the quotation marks that it receives.

  Example: SENDLINE "M8013;3"
           WAITFORPROMPT
           SENDLINE "1,2"
           QUOTES ON
           CAPTURE "NEWS.TXT"
           WAITFORPROMPT
           ENDCAPTURE
           QUOTES OFF

  Related commands: None

                   ---------------------------------

  Command: SCRIPT
  Arguments:  {digit} {script name}
  Description:   All scripts must have a number and name as the first
                 line of the script, just as they must all have
                 ENDSCRIPT as the last line. Scripts 1 and 2 are the
                 Aladdin Automatic passes; you can create up to seven
                 more. You should give the script a name, which will
                 appear on the Aladdin Main Menu. This name maybe up
                 to 31 characters long.

  Example: SCRIPT 3 GEnie Super Script
           ECHO OFF
           LOG ON
           .
           .
           .
           ENDSCRIPT

  Related commands: SCRIPT, PERFORM

                   ---------------------------------

  Command: SEND
  Arguments:  {string}
  Description:   Causes Aladdin to send a {string} but not to send a
                 Carriage Return at the end of the line.

  Example: SCRIPT 7 Retrieve Closing Quotes
            LOG ONTO "8008"
            SEND "1^M"
            WAITFOR "ious?"
            SEND "3^M"
            WAITFOR "nd?"
            SEND "FFIDX,"
            SEND "ELFNX,"
            SEND "GESSX,"
            SEND "UNCMX^M"
            CAPTURE "quotes.txt"
            WAITFOR "nd?"
            ENDCAPTURE
            SEND "^M"
            WAITFOR "ious?"
            SENDCOMMAND "P"
            LOG OFF
           ENDSCRIPT

  Related commands: SENDCOMMAND, SENDLINE, SENDSPECIALCOMMAND

                   ---------------------------------

  Command: SENDCOMMAND
  Arguments:  {string}
  Description:   Tells Aladdin to send a {string}, with a Carriage Return,
                 then wait for the next standard GEnie prompt before it
                 processes the next command in the script.

  Example: LOG ONTO "8008;2"
           ERASEFILE "LOAN.TXT"
           SENDCOMMAND "2"
           SENDCOMMAND "P"
           .
           .
           ENDSCRIPT

  Related commands: SEND, SENDLINE, SENDSPECIALCOMMAND

                   ---------------------------------

  Command: SENDLINE
  Arguments:  {string}
  Description:   This works the same as the SEND command, except it
                 sends a Carriage Return at the end of the {string}.

  Example: SCRIPT 7 Retrieve Closing Quotes
            LOG ONTO "8008"
            SENDLINE "1"
            WAITFOR "ious?"
            SENDLINE "3"
            WAITFOR "nd?"
            SENDLINE "FFIDX,ELFNX,GESSX,UNCMX"
            CAPTURE "quotes.txt"
            WAITFOR "nd?"
            ENDCAPTURE
            SENDLINE ""
            WAITFOR "ious?"
            SENDCOMMAND "P"
            LOG OFF
           ENDSCRIPT

  Related commands: SEND, SENDCOMMAND, SENDSPECIALCOMMAND

                   ---------------------------------

  Command: SENDSPECIALCOMMAND
  Arguments:  {string} {prompt}
  Description:   This works the same as the SENDCOMMAND, except it
                 allows you to specify the prompt you want to wait for.
                 This could be used in GE Mail or EAASY SABRE where the
                 standard GEnie prompt is not used.

  Example: NOTE "This will bring you to the"
           NOTE "AMERICAN AIRLINES EAASY SABRE"
           NOTE "Where SENDSPECIALCOMMAND can be"
           NOTE "of great use. This is a GEnie"
           NOTE "*Basic Service"
           SENDLINE "M8760;3"
           SENDSPECIALCOMMAND "Y" >
           SENDSPECIALCOMMAND "/EXI" >

  Related commands: SEND, SENDLINE, SENDCOMMAND

                   ---------------------------------

  Command: SETSTRING
  Arguments: {digit} {string}
  Description:   This forces the user-defined string (0 - 9) to contain a
                 specific {string}. It is similar to the GETSTRING
                 command, but it does not ask for the value during the
                 script execution. You may not have more than 10 strings
                 in use at a given time.

  Example: SETSTRING 2 "CONTRACT.TXT"
           LOG ONTO "8017"
           IF EXIST "%2"
              ERASEFILE "%2"
           ENDIF
           SENDLINE "6"
           CAPTURE "%2"
           WAITFORPROMPT
           ENDCAPTURE

  Related commands: GETKEY, GETSTRING

                   ---------------------------------

  Command: SNAPSHOT
  Arguments:  {filename}
  Description:  Takes a "picture" of the screen at the moment the
                command is issued and stores it into a file. If the
                file already exists, it will be erased and replaced
                with a new file.

  Example: SENDCOMMAND "1"
           SENDCOMMAND "A"
           SNAPSHOT "LOAN.TXT"
           SENDCOMMAND "N"

  Related commands: CAPTURE, ENDCAPTURE, ERASEFILE

                   ---------------------------------

  Command: SUCCESS
  Arguments:  {TRUE | FALSE}
  Description:   Sets the state of the SUCCESS condition to a TRUE
                 or FALSE state.

  Example: SUCCESS FALSE
           IF SUCCESS
             NOTE "This line will never show"
           ELSE
             NOTE "This line will always display"
           ENDIF

  Related commands: IF SUCCESS

                   ---------------------------------

  Command: WAITFOR
  Arguments:  {string}
  Description:   Tells Aladdin to watch incoming text for a specific
                 {string} and not to continue until it is found.

  Example: SENDLINE "M8010;4"
           CAPTURE "EDUCATE.TXT"
           WAITFOR "GEnie*Basic"
           ENDCAPTURE

  Related commands: WAITFORDATA, WAITFORKEYPRESS, WAITFORPROMPT,
  WAITUNTIL

                   ---------------------------------

  Command: WAITFORDATA
  Arguments:  {START | STOP}
  Description:   Tells Aladdin not to process any more commands until
                 data either STARTs or STOPs coming from GEnie.

  Example: SCRIPT 5 Get NewsGrid Custom Clippings
           LOG ONTO "340;3"
           SENDCOMMAND "10"
           SENDCOMMAND "2"
           IF CURRENTLINEHAS "V"
             SENDLINE "V"
             WAITFORDATA START
             ERASEFILE "newsgrid.nws"
             WAITFOR "Matched"
             CAPTURE "newsgrid.nws"
             WAITFOR "NewsGrid Headline"
             ENDCAPTURE
             WAITRORPROMPT
           ENDIF
           SENDCOMMAND "P"
           ENDSCRIPT

  Related commands: WAITFOR, WAITFORKEYPRESS, WAITFORPROMPT, WAITUNTIL

                   ---------------------------------

  Command: WAITFORKEYPRESS
  Arguments:  None
  Description:   Tells Aladdin to stop what it is doing until a key is
                 pressed.

  Example: CLEAR
           NOTE "WE ARE ABOUT TO LOG ONTO GENIE."
           NOTE "PRESS ANY KEY TO CONTINUE"
           WAITFORKEYPRESS
           LOG ON

  Related commands: WAITFOR, WAITFORKEYPRESS, WAITFORPROMPT, WAITUNTIL

                   ---------------------------------

  Command: WAITFORPROMPT
  Arguments:  None
  Description:   Tells Aladdin not to process the next command until it
                 receives a standard GEnie prompt.

  Example: SETSTRING 2 "CONTRACT.TXT"
           LOG ONTO "8017"
           IF EXIST "%2"
              ERASEFILE "%2"
           ENDIF
           SENDLINE "6"
           CAPTURE "%2"
           WAITFORPROMPT
           ENDCAPTURE

  Related commands: WAITFOR, WAITFORDATA, WAITFORKEYPRESS, WAITUNTIL

                   ---------------------------------

  Command: WAITUNTIL
  Arguments:  {time}
  Description:   Tells Aladdin to wait until a specific time of day
                 before it continues the script. Time must be entered
                 in 24-hour format. For this to work properly, your
                 DOS clock must be set correctly.

  Example: SCRIPT 5 Non-Primetime Script
           ECHO OFF
           WAITUNTIL 18:01
           PERFORM 1
           EXITALADDIN
           ENDSCRIPT

  Related commands: WAITFOR, WAITFORDATA, WAITFORKEYPRESS, WAITFORPROMPT

                   ---------------------------------

  Command: XMODEM
  Arguments:  {UPLOAD {filename} | DOWNLOAD {filename}}
  Description:   UPLOAD tells Aladdin to send the file you specify from
                 your PC to GEnie at this point in the script. DOWNLOAD
                 tells Aladdin to begin receiving a file from GEnie and
                 place it on your PC with the filename you specify here.

  Example: SENDCOMMAND "COMMANDS.TXT"
           SENDCOMMAND "D"
           SENDLINE "1"
           NOTE " "
           NOTE "THIS IS AN XMODEM DOWNLOAD!!!!"
           WAITFOR "receive"
           PAUSE .5
           XMODEM DOWNLOAD "COMMANDS.TXT"
           WAITFORPROMPT
           SENDCOMMAND "N"

  Related commands: ASCII, ZMODEM

                   ---------------------------------

  Command: ZMODEM
  Arguments:  DOWNLOAD {path}
  Description:   ZMODEM tells Aladdin to begin receiving a file from
                 GEnie and place it on your PC in the path you specify
                 here. Unlike XMODEM, ZMODEM is able to do batch file
                 transfers. If an optional {path} is used, it requires
                 a trailing backslash (\).

  Example: SENDCOMMAND "1075;4"
           SENDCOMMAND "6"
           SENDCOMMAND "MANUAL.TXT,COMMANDS.TXT"
           NOTE "This is a ZMODEM download."
           SENDCOMMAND "D"
           SENDCOMMAND "4"
           WAITFOR "receive"
           ZMODEM DOWNLOAD "C:\NEWFILES\"
           WAITFORPROMPT
           SENDCOMMAND "N"

   Related commands: ASCII, XMODEM

                   ---------------------------------

 Aladdin Script Language Command Summary:

  Script structure commands
  -------------------------
   SCRIPT {digit} {title}
     The first line in any script
   GOTO {label}
     Script processing continues at {label}
   CALL {label}
     Processing continues at {label} (see RETURN)
   RETURN
     Processing continues after previous CALL
   PERFORM {digit}
     Perform a user script or auto pass 1 or 2
   ENDSCRIPT
     Processing continues after previous PERFORM
   EXITALADDIN
     End current script and terminate execution
     of Aladdin, exiting to DOS.

 IF...ELSE...ENDIF
 -----------------
  IF ONLINE
    Continues if modem is on-line
  IF CURRENTLINEHAS {string}
    Continues if current line has string
  IF STRING {digit} IS {string}
    Continues if user string matches specified string
  IF STRING {digit} HAS {string}
    Continues if user string contains specified string
  IF DATAWAITING
    Continues if information is waiting to be received
  IF KEYWAITING
    Continues if key has been pressed (see KEYWAITING)
  IF EXIST {filename}
    Continues if the specified file exists
  IF DAYOFWEEK IS {day}
    Continues if today is specified day of week
  IF MAILWAITING
    Continues if there is unread mail waiting
  IF MAILFOUND
    Continues if Aladdin has retrieved mail
  ELSE
    Processing continues here if IF statement is false
  ENDIF
    Processing continues here if IF statement is false and
    there is no ELSE.  Each IF must have a matching ENDIF
  IF SUCCESS
    Continues if previous command was successful
  SUCCESS TRUE
  SUCCESS FALSE
    Forces the result of IF SUCCESS


 Display control
 ---------------
  ECHO ON
    Displays script command while processing
  ECHO OFF
    Hides script commands while processing
  CLEAR
    Clears the screen
  NOTE {string}
    Display the specified message
  HIDE ON
    Causes modem information to be displayed as SECRET...
  HIDE OFF
    Causes modem information to appear as normal
  MONITOR
    Displays one character from the modem
  BEEP
    Emit a short beep
  ALARM
    Sound an alarm until a key is pressed


 Delay commands
 --------------
  PAUSE {seconds}
    Pause of specified number of seconds
  WAITUNTIL {time}
    Suspends script processing until specified
    time.


 File commands
 -------------
  ERASEFILE {filename}
    Erase the specified file
  CAPTURE {filename}
    Save incoming modem text in specified file
  ENDCAPTURE
    Close CAPTURE file and stop saving text
  SNAPSHOT
    Save the screen image as a text file
  XMODEM DOWNLOAD {filename}
  ZMODEM DOWNLOAD {path}
    Download a file
  XMODEM UPLOAD {filename}
    Upload a file
  ASCII UPLOAD {filename}
    Send the contents of an ASCII text file

 GEnie commands
 --------------
  LOG ON
    Log onto GEnie TOP menu (page 1)
  LOG ONTO {page}
    Log onto specified GEnie page
  LOG OFF
    Send BYE and disconnect
  COMMANDMODE ON
    Automatically enter command mode when prompt is found
  COMMANDMODE OFF
    Do not automatically enter command mode
  QUOTES ON
    Convert '' into " in all messages
  QUOTES OFF
    Do not convert ''
  HHH ON
    Send out three H's to get U#= login prompt (default)
  HHH OFF
    Do not send out three H's to get U#= login prompt


 Terminal commands
 -----------------
  HANGUP
    Disconnect the modem
  SEND {string}
    Send the specified string
  SENDLINE {string}
    Send the specified string followed by a carriage return
  SENDCOMMAND {string}
    Send the string and a carriage return and wait for next prompt
  SENDSPECIALCOMMAND {string} {prompt}
    Send the string and a carriage return and wait for special prompt
  WAITFOR {string}
    Wait until specified string appears in text from GEnie
  WAITFORPROMPT
    Wait for your prompt character to appear followed by a pause
  WAITFORDATA START
    Wait until any character is received by the modem
  WAITFORDATA STOP
    Wait until characters stop arriving at the modem


 Keyboard and strings
 --------------------
  KEYWAITING ON
  KEYWAITING OFF
    Enables and disables the use of WAITFORKEYPRESS and IF KEYWAITING
  WAITFORKEYPRESS
    Stop script processing until a key is pressed
  GETKEY {digit}
    Obtains a keypress and stores the resulting key in the user string
  GETSTRING {digit}
    Obtains a string from the keyboard
  SETSTRING {digit} {string}
    Set a user string as specified

                   ---------------------------------

               JIM.LUBIN - August 1992 - for GEnie PC Aladdin