ÛÛÛÛÛÛ        Û     Û
                                Û    Û        Û     Û
                                Û             Û     Û
                                Û             Û  Û  Û
                                Û             Û  Û  Û
                                Û    Û        Û  Û  Û
                                ÛÛÛÛÛÛ        ÛÛÛÛÛÛÛ
          
                                    Version 1.04
                                  20 September 1991
          
                                         by
                                    Larry Winslow
                                        W0NFU
                                 1520 E. Verlea Dr.
                                     Tempe, Az.
          
          
                                     Disclaimer
          
          There always has to be a disclaimer. This program has been written
          to the best of my abilities - I've been programming computers for
          27 years now so I should be pretty good at it. The program has been
          extensively tested and has been found to cause no damage to files,
          memory resident programs, or the computer itself. I assume no
          liability if some condition arises which I have not tested for.
          
          
                                    A brief note
          
          This program is not free. If, after using it for a few weeks, you
          find the program a benefit in your shack, a $10 contribution is
          expected. Otherwise, you are expected to remove it and all of its
          support files from your system. In return for your contribution, I
          will provide support either via mail correspondence or phone call
          (as long as you pay for the long distance charges).
          
          
                                  Brief Description
          
          "CW" is a versatile program which allows a PC to receive and send
          Morse code for the Amateur Radio operator. Some of the more
          significant features of "CW" are:
          
               - Automatic tracking of received CW speed.
          
               - User adjustment of parameters defining the length of the   
                 space after a character and after a word.
          
               - User adjustment of a programmatic filter to eliminate false
                 signals.
          
               - Code transmit speed can be either locked to the speed of the




                 received code speed or user adjustable.
          
               - Type ahead buffer of 4096 characters allowing user to enter
                 data to be sent in response to that being received.
          
               - Ten user defined messages which can be sent.
          
               - User definition of user call which can be sent with single
                 key stroke.
          
               - Maintenance of 2 receive parameters allowing the tracking of
                 multiple users.
          
               - User definition of user QTH which can be sent with a single
                 key stroke.
          
               - Random code generator for practice.
          
               - Received data can be captured to user defined file and/or to
                 the printer.
          
               - User defined input file which can be sent.
          
               - Help screen available with simple keystroke.
          
               - Full featured Iambic keyer with dit and dah memory.
          
          
          
                                Hardware Requirements
          
          The program requires at least 128k of available memory and 1 serial
          communication port which will operate at 9600 baud. The program has
          been successfully test on XT clones, AT clones and 16mhz 386SX
          systems. The timing function has been designed such that it is
          totally independent of the characteristics of the machine that it
          is executing on. The only machine that it has failed to function
          properly was a very old, true "Big Blue" XT with only a 4.77mhz
          clock and that was with a very busy TSR executing; without the TSR,
          the program functioned properly
          
          
          
                                Detailed Description
          
          My interest in a computer interface for CW was prompted by the
          article "ROBO-COPY" by Michael Hansen WB9DYI in the October 1990
          issue of 73 magazine. The program described in the article does an
          excellent job of copying CW but there was no provision for sending
          code. Therefore, after obtaining the source file and a file
          describing the code receive algorithm from the 73 BBS, I rewrote
          the program. The original was written in C but my skills in C are
          limited. Therefore, I wrote my program in QuickBasic 4.5 including
          the transmit functionality. My receive algorithm is identical to
          that in the C program.




          
          The algorithm is described as "The Mean Machine". This name is not
          used in a slang manner but rather the method of tracking the
          incoming code. I quote Michael Hansen's description of the
          algorithm.
          
          "Before we start writing the program, we have to decide on the
          algorithm (method) to be used to time the dits and dahs. How does
          the computer decide that a "mark" (Mark is the presence of a
          signal, either dit or dah - space is absence of the signal) falls
          into the dit or dah category?
          
          A good approach to try would be to calculate the average of some
          number of marks. The average, or as it is call by statisticians,
          the arithmetic mean, is calculated by adding up a number of related
          values then dividing that sum by the number of values. The ARRL
          tells us that proper Morse timing is that a dah is three times as
          long as a dit. This means that the calculated mark average should
          be 2 dits, assuming equal numbers of dits and dahs. As you can see
          in the figure below, this average is an excellent point of
          reference for sorting marks into dits and dahs.
          
          
          
          
          
          
          
                    WPM = 2.4/(average of Marks in milliseconds)
                           therefore, 20wpm => mark of 60ms.
          
                                                      Average
                                               DIT       |       DAH
                                       |________|________|________|
          Time in milliseconds         0ms     60ms     120ms    180ms
          Deviation from mean                    < -60ms >< +60ms >
          
                                         Time values for 20 wpm cw
          
          The important factor here is the number of marks used to calculate
          the average (mean). If that number is too small the average will
          become easily skewed by uneven occurrences of either dits or dahs.
          An example of this skew can be seen in the phrase "1000 watt"; it
          contains 24 dahs but only 3 dits. In this example the average would
          quickly converge to the length (time) of a dah.
          
          If we select a very large number (>250) of samples for the
          averaging calculation, we can effectively "swamp out" all but the
          most absurd of the "pathological" patterns that would significantly
          skew the average. An additional benefit to having a large number of
          samples in the average would be better noise immunity should an
          errant value enter the calculation due to QRM or QRN.
          
          A scheme based on a large sample average would work well if all cw
          operators could standardize on a fixed baud rate, much like the way




          the asynchronous serial protocols work. Unfortunately, the real
          world of cw is anything but standard when it comes to transmission
          speed. CW speed not only varies from operator to operator, but it
          also changes if the operator fatigues or desires to emphasize
          certain portions of the transmission such as signal reports, QTH,
          etc.
          
          There are two major disadvantages to the large sample average. The
          larger the number of samples used in an average, the less
          responsive to change it becomes. When a big change in transmission
          rate is encountered, such a system requires an infusion of many
          dozens of new mark values before it would have an accurate enough
          average to operate properly. During this time, much of the QSO
          would have been lost in a sea of garbled characters. Large sample
          averages are also computationally intensive, restricting their use
          with only the fastest machines.
          
                                  The MEAN Machine.
          
          ROBO-COPY's algorithm uses a smaller number of samples, 32,
          allowing it to "sync up" rapidly to varying transmission rates. The
          trick is to manage the entries that are used in the calculation of
          the average. First, the errant mark values due to noise are reduced
          by the sampling filter that qualifies each mark as it happens. Then
          a pre-screening function insures that skew is minimized by
          disallowing more than 3 successive marks of the same length, plus
          or minus 12.5%, from being entered into the average calculation.
          
          Another type of statistical operation used in ROBO-COPY is the mean
          deviation. It is used to detect large changes in the transmission
          speed and adjust for dah to dit rations that aren't 3:1. The mean
          deviation is the difference between the average and the current
          mark value. A record of the past 32 deviations from average is
          maintained. The above figure shows that under normal circumstances
          the mean deviation of the dit and dah are of equal value but have
          different signs. If you add all 32 mean deviations together the
          dits and dahs will cancel each other out and the sum will be near
          or at zero for "normal" copy.
          
          If the speed of the incoming code should change rapidly however,
          like when you change frequency from a 13 wpm QSO to a 50 wpm QSO,
          the mean deviation really "kicks in". When the value of the mean
          deviation exceeds 25% of the average value, the average is "opened-
          up" so that any mark will be included in the calculation of the new
          average. The program temporarily suspends the pre-screening of
          entries into the average in an effort to purge the average of the
          out-of-date values it contains. After the mean deviation recedes
          back below 25% of the average value the program will again start
          the pre-screening process using the new average as the basis for
          qualifications.
          
          Because of these algorithms, ROBO-COY is responsive to changing
          copy conditions, yet stable without being computational
          cumbersome."
          




          As each mark is completed, the program then starts measuring the
          length of the space following it. If the length of the space is
          less than or equal to the value of letter space value, then the
          space is considered to be part of the current character and the
          program starts measuring the length of the next mark. If not, then
          the character is considered to be complete and is output to the
          "receive" window of the screen. The timing of the space continues
          and if it reaches the value of word space, a word is considered
          complete and a space is output to the receive window of the screen.
          The program then waits for the beginning of the next mark. The
          default values of the letter space is initially 2.5 times the dit
          length. The default value of the word space is initially 6.7 times
          a dit length. Both of these two values can be changed with function
          keys.
          
          
          
                                    The Interface
          
          The program uses either COM1 or COM2 to interface to the radio
          equipment and to provide timing of the CW received or sent. Because
          a comm-port is used, the signals must conform to the RS-232
          definition which is normally a -12v to +12v swing. Naturally, the
          radio equipment does not normally provide the proper signals and
          therefore some type of interface must be developed.
          
          The interface to the "key" input of the rig is simple. Wire a diode
          from the DTR pin of the  comm-port connector to a very small reed
          relay (a good one would be one of the 16 pin DIP types) and then
          back to the GND pin of the connector. The polarity of the diode
          would be with the cathode connected to the connector.
          
                          |\  |     |----------|
              DTR   o-----|  \|-----|  relay   |--------+
                          | / |     |----------|        |
                                                        |
              GND   o-----------------------------------+
          
          The contacts of the relay can then be used to key the rig.
          
          However, the interface for the receive side is not quite so simple.
          The October 1990 issue of 73 magazine, which contains the original
          article describing ROBO-COPY, includes a somewhat simple interface
          which does function although it is not very effective.
          
          Back in the early 70s, I received the diagram of an interface
          circuit which is impressive in its performance. It is so effective
          in digging into the incoming signal and extracting the cw present
          that I added a small audio amplifier so that I could use it just as
          a simple audio filter. It has recovered a cw signal from the
          receiver even when it could not be heard with headphones on.
          Unfortunately, I misplaced the diagram when I moved from
          Minneapolis to Phoenix in 1980 - if you've ever moved, you will
          understand how easy this is to happen. I will have to reverse
          engineer the device before it can be provided to the users of CW.




          Please forward a SASE envelope to me and I will furnish you with
          the schematic as soon as possible.
          
          There are two different types of connectors which can be used on a
          PC - DB-9 and DB-25. The following table list only the pins which
          are of interest to the user.
          
                          DB-9 pin     DB-25 pin   usage
          
            Ring Indicator   9            22       input from receiver
            Data Term Rdy    4            20       "key" signal to rig
            GND              5             7       ground
            Clear to Send    8             5       Dit paddle
            Carrier Detect   1             8       Dah paddle
          
          
          
                                  Electronic keyer
          
          The user can also wire his keyer paddle such that the program will
          act as full-featured electronic keyer. This includes iambic action
          plus dit and dash memories. For this feature to be active, the user
          must include a line in the parameter file of "KEYER=YES". I have
          found that a simple 1488 EIA interface chip (used for some of the
          other required signals) with the paddle connections to the inputs
          of the chip provided a very satisfactory method of interfacing the
          keyer paddle to the program.
          
          
          
                                   Parameter file
          
          When the program is started, it reads in a file (which defaults to
          the file CW.MSG) which contains parameters defining the user and
          also up to 10 "canned" messages. Each record of the file begins
          with a keyword followed by the data associated with that keyword.
          
               Keyword       Associated data
          
               MSGn=         Where "n" can be 0 thru 9 defining 10 "canned"
                             messages. The content of those messages can be
                             any valid cw characters. One feature that can be
                             taken advantage of is the inclusion of #
                             followed by a "C", "Q", "N" or "I" - the pair
                             will be replaced with the users Call, the users
                             Qth, a program maintained Number, or Increment
                             that number.
          
               GMT=          Value necessary to adjust local time to GMT/UCT.
                             Negative values are represented by a leading -.
          
               PORT=         Hex value of the comm-port to be used. If this
                             parameter is not present, the program will
                             default to comm-port 1. Comm-port is "2F8".
          




               CALL=         User call sign.
          
               QTH=          User Qth.
          
               TONE=         Frequency of the monitor. If this parameter is
                             not present, the program defaults to 800hz.
          
               SPEED=        The transmit speed to be used initially. If this
                             parameter is not present, the program defaults
                             to 20 wpm.
          
               KEYER=        This must be "YES" for the electronic keyer
                             feature to be available.
          
          
          
          
          
                                  Program start-up
          
          The program is launched with the command:
          
               CW [filename]
          
          This will start the program executing and if "filename" is
          included, that file will be read in place of the default file of  
          "CW.MSG" (see description of the contents of this file above).
          
          First, the program will announce itself, wait three seconds [this
          can be shortened by pressing the <space> key], and then the normal
          screen is brought up. The normal screen consists of 4 areas: (1)
          the status line, (2) the receive area, (3) the keyboard area, and
          (4) the sending area.
          
          The information contained on the status line consists of:
          
               a) The state of the program - either RCVE or XMIT
               b) The current value of the receiving speed.
               c) The current value of the transmitting speed - this can have
                  a value of "LK" which indicates that the transmitting speed
                  locked to the receiving speed (see Alt-L later).
               d) The count of the number of characters currently in the    
                  keyboard buffer (to a maximum of 2048 characters).
               e) The state of the digital filter.
               f) The "letter" space to dit ratio.
               g) The "word" space to dit ratio.
               h) The monitor frequency.
               i) The local and GMT/UCT time.
          
          This is followed by the window for the data received by the program
          - while receiving, if the program detects a character which is
          invalid, it will be replaced with a @. The name of the receive
          window will flash when there is either printer or file capturing of
          received data. Also, the upper right corner of the shows which of
          the two sets of receive (see alt-U in special keys) is currently




          active.
          Next comes the window where the keyboard data is display that the
          user has entered for transmitting. And the final area is to show
          the user what is being sent.
          
          Just a brief warning. Do not have a "background" program such as
          print or a TSR running which can actively steal CPU cycles from the
          program. This will severely alter the timing mechanisms of the
          program.
          
          
                                   Operating Tips
          
          When the program is interpreting the incoming signal, it makes
          every attempt to properly decode the signal. However, because there
          is an infinite number of different "fists", it becomes almost
          impossible to adjust for each different operator. Frequently the
          user of the program must provide assistance so that the program can
          function as the user desires. This assistance if provide thru the
          F1, F2, F3 and F4 function keys.
          
          F1 and F2 should be used when the characters are translated into Ts
          and Es - for example, "C" becomes "TETE" - or when characters are
          combined - such as "AM" becomes "J". These two keys adjust the
          length of the space between elements of a character. Too long and
          the "AM" becomes "J" and too short results in the "TETE". As you
          use F1 and F2, the effect is reflected by the "Ltr=" value on the
          status line of the screen. The value reflects the "dit" time that
          represents the inter-letter space.
          
          The second assistance is thru the F3 and F4 keys. These keys are
          used to help the program determine the end of letters in a word. If
          the word "help" is shown as "h e l p" then the F3 key should be
          used. And if "help me" is show as "helpme" then F4 should be used.
          As with F1 and F2, when you use F3 and F4, the effect is reflected
          by the "Word=" value on the status line of the screen. The value
          represents the "dit" time that reflects the between-word space.
          
          During the development of the program, it quickly became apparent
          that without these function keys, the program would never be able
          to cope with the variety of "fists". Use them properly and the
          program is fully capable of showing even poor code on the screen.
          
          It is not unusual for the Rx speed on the status line to change a
          bit either up or down when the program is copying code solidly.
          This is caused by the program recalculating the receive code speed
          at the end of each dit or dah. The program should continue to copy
          the incoming code with no problem. On the other hand, if the speed
          should change by large values, this is an indication that the input
          signal is not properly tuned in such that the interface provides a
          solid signal to the computer -- another cause can be static
          crashes.
          
          
          



                                   "Special Keys"
          
          The program will respond to some keys other than as data to be
          sent. A brief explanation of these special keys can be obtained by
          entering Alt-H while the program is executing. The following is a
          more detailed description of each key.
          
               ESC       This key will toggle the program between receive and
                         transmit modes. The left end of the status line will
                         show the current mode. Additionally if in transmit
                         mode, the name of the Sending window will blink.
          
               F1        Adjust length of letter spacing down by .1 times of
                         the current dit length. This key should be pressed
                         when the received code is shown as is not separated
                         into individual characters properly. For example,
                         "is" is interpreted as "5".
          
               F2        Adjust length of letter spacing up by .1 times of
                         the current dit length. This key should be pressed
                         when the received code is shown as a string of Es
                         and Ts. For example, "B" would be shown as "TEEE".
          
               F3        When the spaces between words are missing, press
                         this key. This adjusts the length of the "space"
                         between words down by .1 times the current dit
                         length.
          
               F4        When every letter is separated by a space, use this
                         key. Each press of the key, adjust the length of the
                         "space" between words up by .1 times the current dit
                         length.
          
               F5        Decreases the send speed by 1 wpm.
          
           alt-F5        Decreases the send speed by 5 wpm.
          
               F6        Increases the send speed by 1 wpm.
          
           alt-F6        Increases the send speed by 5 wpm.
          
               F7        Clear the receive window of the screen
               
               F8        Clear the keyboard window of the screen. Note that
                         this will also change the "Buff" entry of the status
                         line to zero.
          
               F9        Toggle the digital filter. There are 4 settings of
                         the filter.  "Low" which limit the maximum received
                         code speed to 75 wpm but the program will be
                         sensitive to "noise". "Med" will limit the maximum
                         speed to 37 wpm but makes the program less sensitive
                         to noise. "Hi" limits the speed to 18 wpm but makes
                         the program even more insensitive to noise. And
                         finally, "Off" which removes limits from the maximum




                         speed but also makes the program very sensitive to
                         noise.
          
               F10       This will reset all program receive timing
                         parameters to their default values.
          
               alt-B     This will toggle the monitor on and off. The current
                         state can be seen on the status line.
          
               alt-H     A brief description of each special key will be
                         shown. The display can be terminated prematurely by
                         pressing the "ESC" key.
          
               alt-I     The user will prompted of the name of a file to be
                         read and treated as if the data were keyboard input
                         for transmission. The file will be read until end-
                         of-file is reached or until the user presses alt-I
                         a second time. When the file is closed, the user
                         will be notified with a brief message on the screen.
          
               alt-L     This key will lock (or unlock) the transmit code
                         speed to the value of the receiving code speed. A
                         brief message is shown the screen. Also, the TxSpeed
                         of the status line will reflect the current value.
          
               alt-M     This will display the value of the Call, Qth, and
                         the 10 canned messages.
          
               alt-N     Allows the user to initialize the value of "number"
          
               alt-O     This provides the user with the writing of the
                         received CW to a file. The user will be prompted for
                         the file name. The program always opens the file in
                         "append" mode. The file will remain open until alt-O
                         is pressed a second time or until the program
                         terminates. Note that any special cw characters such
                         as "BT" will be shown in brackets - for example,
                         [BT] - also, once a minute the date and time will be
                         written to the file again surrounded with brackets.
          
               alt-P     This function is identical to the alt-O described 
                         above except that the output is to the user printer.
          
               alt-Q     Terminate program.
          
               alt-R     This will cause the program to generate 63 groups of
                         5 characters of random code. It can be used for code
                         practice.
          
               alt-S     If the user is curious, this key will show the
                         current state of the mean-deviation and mark tables.
                         It is present for program debugging.
          
               alt-T     Allows the user to adjust the frequency of the
                         monitor.


          
               alt-U     The program has the ability to maintain its receive
                         algorithm values for 2 different signals. This key
                         will flip the program from one signal to the other.
                         This can be useful when you are in a QSO with two 
                         people are not sending identical code. Without this
                         functionality, there would be the possibility of a
                         brief period time when the program would receive
                         "garbage" while it synched up with the other signal.
          
               alt-0     Send message 0.
          
               alt-1     Send message 1.
                 .
                 .
                 .
               alt-9     Send message 9.
          
               Insert    Send cw character AS
          
               Home      Send cw character KN
          
               PgUp      Send cw character AR
          
               PgDn      Send cw character SK
          
               End       Send cw character SN
          
               Delete    Send cw character BK and switch program to receive
                         mode.
          
               <enter>   Send cw character BT
          
               UpArrow   Send call
          
               DnArrow   Send Qth
          
               RtArrow   Send "number"
          
               LtArrow   Increment "number" by 1.
          
               !         Send cw character AA
          
               #         Send cw character KA
          
               $         Send cw character IQ
          
               %         Send cw character AK
          
          Any character which is not in the above list nor represents a valid
          CW character will result in a Beep.
          
          

          
                                 And there is more!
          
          I have an ICOM IC-765 and have developed a computer interface to
          it. I then combined this interface with the CW program. This allows
          me to first tune the rig with my computer and then with the simple
          pressing of the F12 key, I'm in the CW program. Another press of
          F12 returns me back to the interface program. If you are interested
          in this software and have an ICOM CT-17 CI-V interface (I can
          provide you with the diagram of a $12 replacement for the $97.50
          that ICOM wants for the CT-17), send me a 5.25 floppy along with a
          shareware fee of $20. This interface has proven very effective in
          controlling my IC-765 and recognizing when I manually assume
          control of it. Based upon the documentation provided to me by ICOM,
          the program should be equally effective in controlling other ICOM
          HF rigs. 
          
          
          
          
                                        Change history
           
          Rev: 1.01 -- 25 July 1991
                  Initial release
          
          Rev: 1.02 -- 31 August 1991
                  Implemented calibration function.
                  Changed initial value calculations using results 
                       of calibration function.
                  Blanks and special characters weren't showing adjusted 
                       buffer count.
                  Initial filter value was getting changed down to "low".
                  Changed Welcome screen to reflect new rev number.
                  Corrected Alt-I function - it was not working.
                  Corrected TellClose - in case current line not at 
                       announcement.
                  Changed OpenWindow to center message
                  TxLock wasn t functioning
          
          Rev: 1.03 -- 15 September 1991
                  The help function (Alt-H) was inadvertantly changed such 
                  that it wouldn't function at all.
          
          Rev: 1.04 -- 20 September 1991
                  Corrected Farnsworth spacing - it was too short.
                  Show Farnsworth speed on send area border when active.

          
          
          
                                          Future changes
          
                  I'm currently working on a mouse interface for as many 
                  keyboard type functions as possible.
          
                  Any and all suggestions are solicitied. In fact, many of 
                  the current features were the result of suggestions from 
                  hams here in the Phoenix area. If you have an idea, let 
                  me know.