A
2CB
















          Radio Teletype Program
          For The IBM Personal Computer
          Version 1.2G
          



          10-04-1986


          Glenn E. Welman - KF4NB

          3301 Pastern Ct.
          Lexington, Ky 40513
          
          
          (C) Copyright Welman Software 1983, 1984, 1985, 1986




                              IBM PC RTTY Ver 1.2G 

          INTRODUCTION



          This program runs on the IBM Personal Computer and
          interfaces to your Amateur Radio equipment through the
          Asynchronous Communications adapter.  I wrote the program
          to be as flexible as possible hoping that it will be
          useable with any Terminal Unit (TU) and radio combination.
          I have attempted to provide enough information to help you
          make your system operational.  The program will work on the
          IBM PCjr with one minor limitation which is explained
          further on in this document.  I suspect that the program
          will also work on the IBM Portable PC, most PC clones and
          possibly the IBM PC AT, even though I have not had the
          opportunity to test the program on those machines.

          I intend for the program to be distributed by hams, rather
          than retailers.  I suggest the following.



          DISTRIBUTION GUIDELINES


              Please share (copy) the program with others who are
              interested in RTTY.

              Do not sell or barter the program to anyone. (That's my
              right!)

              When you pass along the program, include only the
              original unmodified version.

              Send a SASE along with your current version number and
              I will let you know if any known problems have been
              fixed by a later version.

              Don't remove these guidelines from the program or
              document.

              If you find the program of value, a small contribution
              for my effort will be appreciated ($25 suggested).












          Introduction                                               1


                              IBM PC RTTY Ver 1.2G 

          SUMMARY OF VERSION 1.2 CHANGES


          þ   Capability to clear the transmit buffer.

          þ   Capability to save the transmit buffer, clear it and
              later restore it.

          þ   Up to 10 filenames can be specified for easy loading
              into the transmit buffer from diskette.

          þ   The screen can now be used in color instead of white
              only.  The colors can be modified to your own taste.

          þ   The program can now handle any oscillator frequency
              input to the 8250 Async chip.  (e.g. The PCjr's
              frequency is different from the PC.)

          þ   There are now separate baud rates for Baudot and ASCII
              modes.  Additional baud rates can be user specified for
              extended flexibility.

          þ   Several enhancements have been added for our European
              friends

              -   The European date format is supported. (e.g.
                  15.Nov.1984)

              -   100 and 200 baud rates are now in the default ASCII
                  set.

              -   The column for the warning beep is 56 and there is
                  an automatic CR/LF at column 64.  These values can
                  be changed and the automatic CR/LF turned off.

              -   The Baudot character set is modified to support the
                  European standard.

          þ   Several characters have been defined to support unique
              ASCII to Baudot conversions for MARS usage.

          þ   The ASCII to Baudot and Baudot to ASCII conversion
              tables can be modified at program startup time to
              support unique conversions.

          þ   The title screen will now go away after 10 seconds or
              after the first keystroke.

          þ   The default time type can be specified in the
              "PARMS.RTY" file and no prompting will occur.

          þ   The operation of the DTR and RTS outputs can be user
              specified for transmit and receive.


          Introduction                                               2


                              IBM PC RTTY Ver 1.2G 

          þ   The number of ASCII data bits, parity bits and stop
              bits can now be specified.

          þ   SELCAL has been implemented for unattended monitoring
              operations.

          þ   A simple QSO logging capability has been added.




          SUMMARY OF VERSION 1.2A CHANGES


          þ   Added MARS keyword support to the PARMS.RTY file
              processor.




          SUMMARY OF VERSION 1.2B CHANGES


          þ   Redefined some MARS special characters for ASCII to
              Baudot translation.

          þ   Fixed a bug, in ASCII mode "+" would be sent 12 times,
              now it is sent only once.

          þ   Enhanced the setting of baud rates in the PARMS.RTY
              file.  You can now specify the rates positionally (you
              define the order).




          SUMMARY OF VERSION 1.2C CHANGES


          þ   Fixed bug when a transmit file with blank lines was
              sent, two line feeds were sent for each blank line.

          þ   Fixed a bug in receive mode, with unshift on space
              turned on, the program assumed an automatic unshift
              with CRs and LFs.

          þ   Provided a method to make the program start up in the
              ASCII mode.

          þ   Added the capability to specify the parms filename on
              the command line.

          þ   Provide some special support for packet radio users.


          Introduction                                               3


                              IBM PC RTTY Ver 1.2G 

          þ   Enhanced the MARS support to include the automatic
              sending of 12 letters functions when "NNNN" is sent.




          SUMMARY OF VERSION 1.2D CHANGES


          þ   Made a change to the handling of blank lines.  Changed
              the default to always send carriage return and line
              feed for blank lines.  If you only want line feeds for
              blank lines then specify "BLLF" in the parameter file.




          SUMMARY OF VERSION 1.2E CHANGES


          þ   Fixed the scroll routine to handle foreground and
              background colors.

          þ   Changed the program to allow a greater range of
              foreground and background colors.

          þ   Added the capability to specify the SELCAL end string
              and added an alternate string capability.

          þ   Provided the ability to start the program in the ART
              mode and/or in the unshift-on-space mode.

          þ   Added the capability to inhibit the bell (beeps) in the
              ART mode.

          þ   Added some enhancements for packet operation.  Packet
              starts up in the transmit mode.  You can specify a
              string to send the current time and date to your TNC.
              You can inhibit sending of the time and date on
              power-up and send it later with the use of the alt-D
              character.  You can let the system send a note that you
              are not around and then save data to a file for stored
              messages.

          þ   I put the scrolling routine assembler source code in
              the BAS file so there would be one less file to send
              and keep track of.








          Introduction                                               4


                              IBM PC RTTY Ver 1.2G 

          SUMMARY OF VERSION 1.2F CHANGES


          þ   Fixed a bug where the program would quit abruptly if
              SELCAL was turned on and the SELCAL ending sequence was
              received when the starting sequence had not been
              received.

          þ   Fixed a problem by making the program ignore null
              entries in the parms file.

          þ   Fixed a bug in the MARS option when "NNNN" is
              received.

          þ   Added the capability to vary the receive and transmit
              screen size.

          þ   Added the capability to customize the Date and Time
              stamp to your own liking.

          þ   Added the capability for the program to append the
              extension of "RTY" to the name of the parms file given
              when RTTY is invoked.

          þ   Added the ability to specify the UTC time difference in
              the parms file instead of being prompted for it.

          þ   Added the capability to send received data to both the
              printer and diskette with the SELCAL option.

          þ   Added the function when receiving data to a file for
              the program to save the file after every 15 lines of
              text.  This will keep you data loss to a minimum if you
              happen to lose power in the middle of a session or
              someone accidentally resets the entire system for you.

          þ   The program now figures out if you are running on a
              PCjr, and sets all of the correct parameters for you.




          SUMMARY OF VERSION 1.2G CHANGES


          þ   Fixed a bug in the MARS mode that occured when NNNN was
              received.

          þ   Added the alt-B key to toggle the enable/disable of the
              bell character in the ART mode.

          þ   Added several "alt-" key combinations to provide a
              means of sending control characters to the


          Introduction                                               5


                              IBM PC RTTY Ver 1.2G 

              communications port.  (All of the control keys which
              have special meaning to my program.)

          þ   Added several "alt-" keys to facilitate use of the
              Kantronics UTU.

          þ   Added a couple of new keywords to the PARMS file to
              make the program just a tad more flexible. (HAND and
              XMIT)

          þ   Changed the program logic for the handling of the DAY
              command for packet operation.  You now use a keyword to
              send the command when the program starts, rather than
              specifying not to send the command.  (Removed NPDT,
              added PKDT)

          þ   Replaced the RTTYU program with a program called RU.
              RU is one of my first attempts at C programming.  The
              main difference in RU is that it interprets carriage
              returns (CR) and line feed characters (LF) literally,
              instead of as a brand new line.


































          Introduction                                               6


                              IBM PC RTTY Ver 1.2G 

          PROGRAM OPERATION



          The program is started by placing the program diskette in
          the default drive (usually drive A:) and entering

          RTTY     or      RTTY filename


          In the above example, "filename" is the name of the
          parameter file to use instead of "PARMS.RTY".  This feature
          allows multiple runtime configuration files to be used for
          various operation modes.  This and other files should be
          personalized prior to running the program with your
          callsign and other pertinent information.  These files are
          identified further on in this document and may be changed
          with any text editor.  The program is primarily written in
          BASIC and compiled to achieve a useable operating speed.
          There is one subroutine written in Assembly Language to do
          things which I can't do well in BASIC.  Specifically, the
          routine scrolls the receive and transmit screens.

          The program takes advantage of the IBM Personal Computer's
          capabilities.  The interrupt capabilities of the
          Asynchronous Communications adapter and the keyboard allow
          many things to occur simultaneously without the loss of
          information.  The use of DOS files allows the storage and
          retrieval of a large supply of RTTY data.  I hope you find
          the program's many features useful.

          In version 1.2 I have tried to make the program a little
          more flexible.  The price that is paid for flexibility is a
          little more complexity in setup.  One of the changes is to
          allow the use of the program on the IBM PCjr.  The PCjr has
          a slightly different input frequency to the 8250 Async chip
          and it does not have DMA (direct memory access) during
          diskette operations.  The significance of no DMA is that
          data through the Asynchronous port will stop during any
          diskette accesses.  Specifically, if you are sending the
          received data to a diskette file, then about every 500
          characters there is a chance of missing one or more
          received characters.  During some tests which I performed
          with a 5200 character test file, 2 characters were dropped
          at 45.5 baud (BAUDOT mode), 8 characters were dropped at 74
          baud (BAUDOT) and 110 baud (ASCII), 28 characters were
          dropped at 300 baud (ASCII) and 35 characters were dropped
          at 1200 baud (ASCII).  Note that this is a hardware
          limitation as noted in the PCjr Technical Reference.
          Characters are only lost when received characters are
          placed in a diskette file, all other operations of the
          program are functional with no known problems.



          Program Operation                                          7


                              IBM PC RTTY Ver 1.2G 

          SYSTEM REQUIREMENTS


              An IBM Personal Computer with at least 128K bytes of
              memory and a minimum of one diskette drive or a true
              IBM PC compatible computer.

              An IBM Personal Computer Asynchronous Communications
              Adapter or equivalent.  Note that for the compiled
              BASIC program to work correctly, the Asynchronous
              adapter must use an 8250 UART chip mapped into the same
              I/O address space and interrupt level as the IBM PC
              version.

              IBM Personal Computer Disk Operating System (DOS)
              version 1.1 or later (or equivalent).

              A Terminal Unit (TU) for amateur radio teletype (RTTY)
              applications.  Or a packet terminal node controller
              (TNC) for packet radio operation.

              A radio receiver or transceiver capable of operating
              RTTY.
































          Program Operation                                          8


                              IBM PC RTTY Ver 1.2G 

          FEATURES


              The program will run under DOS 1.1 or later.

              The program will run on a monochrome display and both
              the 80X25 and the 40X25 mode on a color display.

              The program runs in a split screen mode with received
              data displayed on the top and the transmit buffer
              displayed on the bottom of the screen.  The number of
              lines used by the receive and transmit screens can be
              varied by using the RXLN keyword in the PARMS.RTY
              file.

              Run time information is displayed in the middle of the
              screen, such as current time, date and elapsed time
              since the last TTY ID was sent.

              Prompts for operator input are also displayed in the
              middle of the screen.

              The definition and status of the function keys is
              displayed at the bottom of the screen.

              Errors and informational messages are also reported at
              the bottom of the screen.

              In transmit mode the program sends CR, CR, LF, and
              letters at the end of a line.  This provides some
              degree of compatibility with the old mechanical
              teletype machines.

              The program supports both BAUDOT and ASCII RTTY modes.

              þ   Common BAUDOT rates of 60, 67, 75, and 100 WPM are
                  supported.  Those are baud rates of 45.5, 50, 56.9,
                  and 74.2 respectively.

              þ   Common ASCII baud rates of 100, 110, 200, 300, 400
                  and 1200 BAUD are supported.

              þ   Additional baud rates can be user specified in the
                  "PARMS.RTY" file up to a maximum of 10 rates on
                  both modes.

              The received input goes to the display and can be
              directed to the printer and/or a DOS file.  File
              compression is supported which can result in using less
              diskette/disk file space.

              While you are receiving, you can fill a 4000 character
              transmit buffer from the keyboard or DOS files.


          Program Operation                                          9


                              IBM PC RTTY Ver 1.2G 

              While the program is prompting you for information,
              received characters are placed into a 4000 character
              receive buffer.  If more than 4000 characters are
              received while the program is prompting you, a
              communications buffer overflow error will result.  The
              program will attempt to recover as much as possible.

              There are several predefined files which can be loaded
              into the transmit buffer with the stroke of a function
              key.  Up to 10 files can be user defined to be loaded
              into the transmit buffer with the use of the "Alt" and
              numeral keys.  Up to six files can be queued to be
              placed into the transmit buffer at any one time.

              A cursor is displayed at the current Transmit buffer
              location.  When the cursor reaches column 56, the
              program will sound a beep.  The user can define a new
              warning column and can specify an ending column with an
              automatic CR/LF insertion.

              The transmit buffer can be edited minimally by using
              the backspace key.  There is no full screen support.

              In the transmit mode, a date and time stamp can be sent
              over RTTY, as well as, a predefined RTTY ID field.

              There is a key defined to allow the storage of the
              callsign of the other station in the QSO.  The contents
              of this storage field will be placed at the beginning
              of the TTY ID when it is selected.  This buffer can be
              changed at any time.

              The transmit buffer is filled first by any transmit
              files, second by characters resulting from special
              keys, and finally from keyboard input.  The program
              will stop placing characters in the transmit buffer
              when it is full and will resume as characters are
              transmitted from the transmit buffer.

              A special Baudot mode can be selected for European
              usage.














          Program Operation                                         10


                              IBM PC RTTY Ver 1.2G 

              Some special characters have been defined for ASCII to
              Baudot translation for the MARS program.  These
              characters and their meanings are as follows

                  * causes a carriage return to be sent

                  = causes a line feed to be sent

                  + causes 12 letters characters to be sent

                  @ causes the bell character to be sent

                  \ causes the null character to be sent (&H00)

                  > causes the figures character to be sent

                  < causes the letters character to be sent

              Note that these characters may not operate correctly in
              the European mode.

              An additional MARS mode reduces the end-of-line
              function to CR, CR, LF and does not send a letters
              character automatically at the end-of-line or on the
              space character.

              SELCAL is now supported to automatically print or store
              received signals when a user specified sequence of
              characters is received.

              The transmit buffer can be cleared or stored for those
              times when you really want to send something other than
              what's in the buffer.

              A limited logging function can be executed with the use
              of a few keystrokes.  You will be prompted for
              pertinent information and it will be placed on
              diskette.

              When multiple blank lines are sent, the program only
              sends line feed characters to speed things up.
              Carriage returns are not sent for blank lines.

              Special support has been added for packet radio
              controller support.  I implemented a few things for use
              with my Kantronics Packet Communicator.  I believe that
              these are compatible with most TNCs on the market which
              follow the TAPR command structure.  There is a DAY
              command to set the clock in the TNC.  The program will
              also send a message when you are away from the
              keyboard.




          Program Operation                                         11


                              IBM PC RTTY Ver 1.2G 

          SPECIAL KEYS


              Backspace - Pressing the backspace key erases the last
              character entered into the transmit buffer and the
              cursor backs up.  If the last character was a line
              feed, the cursor backs up to the previous line and the
              character is displayed in reverse video.  When you
              backspace beyond the top line of the transmit screen,
              the previous line entered into the transmit buffer
              appears on the top line.  Lines prior to the line at
              the top of the screen are not visible.  Note that you
              cannot back up beyond the last character sent to the
              Asynchronous communications adapter.

              ENTER - Pressing the "ENTER" key at the end of a line
              causes a carriage return and line feed to be placed
              into the transmit buffer.

              Ctrl E - Ctrl E is a new added feature.  Typing a Ctrl
              E into the transmit buffer will cause the program to
              automatically return to the receive mode upon reading
              the Ctrl E from the transmit buffer.  Additional
              transmit buffer contents are retained but not
              transmitted until the XMIT mode is entered again.  This
              should be useful when you are transmitting a long file
              and you want to take a break and may not make it back
              in time to switch it over manually.

              Ctrl S - Pressing Ctrl S causes the program to prompt
              you for a line of characters which will be stored for
              later retrieval.  The information is kept in memory
              until the program is ended or another Ctrl S is
              entered.

              Ctrl R - This is the companion key of Ctrl S.  Pressing
              Ctrl R retrieves the stored line and places it in the
              transmit buffer.

              Ctrl W - Ctrl W is pressed to instruct the program to
              place only a carriage return in the transmit buffer.
              Pressing the "ENTER" key immediately after a Ctrl W
              will be ignored by the program.  Pressing a character
              key will result in an overprint condition.  The Ctrl W
              key will find primary application in sending RTTY art.
              This character is placed in the receive file for any
              carriage return.  An idea of what character may be
              displayed by various editors can be found in appendix C
              of the Technical Reference manual.

              Note that the absence of the Ctrl W/Ctrl T at the end
              of the line will result in the normal end of line
              processing which send CR, CR, LF and ltrs.


          Program Operation                                         12


                              IBM PC RTTY Ver 1.2G 

              Ctrl T - Ctrl T is the companion of the Ctrl W key and
              results in a single line feed being placed in the
              transmit buffer.  Pressing "ENTER" immediately after a
              Ctrl T will be ignored by the program.  The Ctrl T key
              will be used in RTTY art and may be used to replace a
              line feed erased by backspacing.  This character is
              placed in the receive file for any line feed.  An idea
              of what character may be displayed by various editors
              can be found in appendix C of the Technical Reference
              manual.

              Note that the absence of the Ctrl W/Ctrl T at the end
              of the line will result in the normal end of line
              processing which send CR, CR, LF and ltrs.

              Ctrl X - Ctrl X is provided to force the sending of the
              "Figures" character in Baudot mode only.  This key
              could be useful in send a SELCAL prefix.  This key will
              appear in the transmit buffer as a up arrow.

              Ctrl Y - Ctrl Y can be used to force the sending of the
              "(ltrs)" character in BAUDOT mode only.  This key can
              also be used in sending a SELCAL prefix.  This key will
              appear in the transmit buffer as a down arrow.

              Alt A - Alt A can be used to toggle between the Art
              mode and the No Art mode.  Art mode is for overstrike
              lines to darken (fill in) the print.  Note that
              multiple strikes are visible only on the printer, not
              on the display.  The No Art mode is used for noisy
              conditions (primarily text) where you want a CR/LF any
              time a CR or LF is received for maximum copy.  The
              status of the Art mode is included at the bottom of the
              screen in the receive mode.  Art mode is indicated by
              an "A" beside "RECV" and the No Art mode is indicated
              by an "N".  At program start the default is the No Art
              mode.  The "BELL" file on the diskette is an example of
              RTTY Art.

              Note that files which are received in the Art mode will
              have Ctrl-W and Ctrl-T characters in the file.  Files
              received in the no Art mode will not contain the Ctrl-W
              and Ctrl-T characters.

              Alt B - This key is used to toggle the enable/disable
              of the bell character (beep) in the ART mode.  This is
              extremely helpful when you are absolutely sick and
              tired of listening to incessant beeps.

              Alt C - This option can be used to clear the transmit
              buffer.  The buffer is cleared, all loading from
              diskette files is stopped, and you can start again with
              a clean slate.


          Program Operation                                         13


                              IBM PC RTTY Ver 1.2G 

              Alt D - This option will send the current time and date
              over the Asynchronous port in the format specified by
              the PDAT keyword.  The PDAT keyword is relatively free
              format to allow for different TNC implementations.  See
              the PARMS.RTY description for additional details.

              Alt T - This option saves the transmit buffer in a file
              named "TXBUFFER.RTY" and then clears the transmit
              buffer just like the "Alt C" option.  If the transmit
              buffer was previously saved (this session) it will
              first clear the transmit buffer and then load the file
              "TXBUFFER.RTY".  Note that once the file has been
              restored it will reset the flag indicating that the
              transmit buffer was previously saved.

              Alt S - Alt S is used to toggle the SELCAL (Selective
              Call) option on and off.  When the SELCAL option is
              turned on, you will be prompted to find out if you want
              to send the selected data to the printer, diskette or
              both.  A filename will be asked for when the diskette
              option is selected.  A message will appear at the
              bottom of the screen when the option is turned off.
              The character string to search for to start saving the
              data can be specified in the "PARMS.RTY" file.  Because
              there is no letters or figures character in ASCII, I
              have included the capability to specify a separate
              SELCAL ID for both the BAUDOT and ASCII mode.  SELCAL
              saving is terminated by the receipt of the sequence
              "NNNN" in the default mode.  You can use the ESEL and
              GESL keywords to specify your own unique SELCAL
              terminator.

              Alt L - This option will place information into a
              logging file with a filename of "LOG.RTY".  You will be
              prompted for the callsign of the station worked and for
              any other pertinent data.  You may want to include such
              things as signal reports, frequency, names and so on.
              The date, time and your data will be appended to the
              "LOG.RTY" file.

              Alt N - This option toggles the not-at-keys
              enable/disable flag.  The current status is displayed
              on the error line for approximately 5 seconds.  When
              turned on, the program will send the file "AWAY.MSG"
              when a string is received which matches the NKEY
              string.  All incoming data will be stored in the file
              "WHILE.OUT" or the already active received data file.
              This option is primarily for packet use.

              Alt 0-9 - This key sequence will load the file defined
              in the "PARMS.RTY" file corresponding to the file
              numbers 1 to 10.  If the filename has not been
              specified, then no action will be taken.


          Program Operation                                         14


                              IBM PC RTTY Ver 1.2G 

          Note that some of the special keys may be the same as the
          control keys for some TNCs.  The RTTY program will take
          action on the special key and will generally not pass any
          code over the Asynchronous lines.  To fix this problem, I
          have implemented the use of several alt-keys to send the
          control character codes directly through the Asynchronous
          adapter.  Note that the code will go immediately, not in
          sequence with anything in the transmit buffer.

              Alt E - This key will send the code for a cntl-E.

              Alt G - This key will send the code for a cntl-T.

              Alt H - This key will send the code for a cntl-S.

              Alt R - This key will send the code for a cntl-R.

              Alt W - This key will send the code for a cntl-W.

              Alt X - This key will send the code for a cntl-X.

              Alt Y - This key will send the code for a cntl-Y.

              Alt Z - This key will send the code for a cntl-C.

          I have also included some special alt-keys in an attempt to
          make the running of the program with the Kantronics UTU a
          little easier.  These alt-keys send a cntl-C followed by a
          command letter to the UTU.  These characters are placed
          sequentially into the transmit buffer.  To run the UTU, you
          should specify the PACK option in the PARMS.RTY input
          file.

              Alt I - This key sends cntl-C followed by R which
              selects receive mode.

              Alt J - This key sends cntl-C followed by S which
              selects shift change mode.

              Alt K - This key sends cntl-C followed by N which
              selects transmit mode.

              Alt M - This key sends cntl-C followed by X which
              selects command mode.

              Alt O - This key sends cntl-C followed by T which
              selects speed change mode.








          Program Operation                                         15


                              IBM PC RTTY Ver 1.2G 

          FUNCTION KEYS


          The ten function keys are used during program operation to
          direct the flow of information in the computer system.  The
          definition and status of the function keys is displayed at
          the bottom of the screen.  The function keys are defined as
          follows:



          General Function Keys


              F1  -  KEYS

                  This key toggles the definition of function keys 3
                  through 10 and changes the status line.

              F2  -  RECV/XMIT

                  This key toggles the program between receive mode
                  and transmit mode.  When the program begins, this
                  key defaults to RECV.  When the key is pressed to
                  go from XMIT to RECV, the program will wait until
                  the basic communication buffer is empty before
                  returning to the RECV mode.  BASIC buffers up to
                  128 characters independent of the program.  So
                  don't get too anxious if the transmitter doesn't
                  stop immediately.

                  There is a short delay of about one half a second
                  from the time the program turns the transmitter on
                  and the first data is sent.  This should give the
                  other station a chance to lock onto your signal.

                  Additionally, an A or N will appear with RECV to
                  indicate the current status of the Art mode (See
                  Alt A for additional information).
















          Program Operation                                         16


                              IBM PC RTTY Ver 1.2G 

          Function Key Set 1


              F3  -  RX FLE

                  Receive a File.  Pressing this key prompts you for
                  a filename in which to place the received
                  information.  The information is appended to the
                  file.  Pressing only "ENTER" results in no file
                  being opened.  Pressing this key while a file is
                  currently open will close the file.  Another
                  filename must be entered to continue saving data.
                  Entering the same name as an existing file will
                  result in that data being appended to the file.

                  When a filename is entered, you are asked if you
                  want the file to be saved as a compressed file.
                  Compressed files will take up less room on your DOS
                  diskette, but are not readily alterable in an
                  editor.  A utility is provided to decompress or
                  compress a file offline.

                  When a receive file is open, a reminder is
                  displayed on the middle status line of the screen.
                  The form of the display is "RX-filename".  The
                  program will close and then reopen the file after
                  every 15 lines of input.  This forces the computer
                  to update the file status and prevents the loss of
                  the entire file should you happen to lose power in
                  the middle of a session or if the computer managed
                  to get reset in the middle of a session.

              F4  -  UOS ON/UOS OF

                  This key toggles between "Unshift On Space" being
                  turned on and turned off.  This key only applies to
                  received data.  When "unshift on space" is on, the
                  program will shift back to "letters" mode any time
                  a space is received.

                  Independent of this key, the program will transmit
                  a "(ltrs)" character in the BAUDOT mode as required
                  with a space.  This makes the program compatible
                  with either type of teletype which may be in the
                  other station.  When the program begins, this key
                  defaults to UOS OF.

              F5  -  END

                  This key provides a means to terminate the program
                  gracefully.  You will be prompted for confirmation
                  of your request to quit.



          Program Operation                                         17


                              IBM PC RTTY Ver 1.2G 

              F6  -  PRT OF/PRT ON

                  This key toggles output to the printer on and off.
                  When PRT ON is displayed, all characters received
                  will also be printed on the matrix printer.  Bell
                  characters are not sent to the printer to keep down
                  the noise pollution.  When the program begins, this
                  key defaults to PRT OF.

              F7  -  Baud Rate Selector

                  This key toggles through the baud rates supported
                  by the program.  The status line is updated with
                  each change.  In Baudot mode, the baud rates of
                  45.5, 50.0, 56.9, and 74.2 correspond to character
                  rates of 60, 67, 75, and 100 words per minute (WPM)
                  respectively.  When the program begins, this key
                  defaults to 45.5.

                  For ASCII the baud rates of 100, 110, 200, 300,
                  400, and 1200 are supported.  When the ASCII mode
                  is selected this key defaults to 110 baud.

                  Up to 10 baud rates per mode are possible by adding
                  baud rates through the use of the BAUD and ASCI
                  options of the "PARMS.RTY" file.  The default rates
                  can also be changed.

              F8  -  BAUDOT/ASCII

                  This key toggles between Baudot and ASCII modes.
                  Any combination of baud rate and mode is
                  obtainable.  When the program begins, this key
                  defaults to BAUDOT unless specified otherwise in
                  the parms file.  Each time this key is pressed, the
                  baud rate selection will change to the first baud
                  rate for that mode, the default if 45.5 baud for
                  Baudot and 110 baud for ASCII.

              F9  -  NEW LN

                  This key provides the ability to force a CR/LF (new
                  line) in the middle of received text.  Such an
                  operation might be needed if the original CR/LF
                  were lost in the noise.

              F10 -  LTRS

                  This is the "letters" key.  During Baudot reception
                  it is occasionally desirable to force the receive
                  mode back into the "letters" mode.  This key
                  accomplishes that task.



          Program Operation                                         18


                              IBM PC RTTY Ver 1.2G 

          Function Key Set 2


              F3  -  TX FLE

                  Transmit a File.  Pressing this key allows the
                  contents of a DOS file to be placed into the
                  transmit buffer for transmission.  You will be
                  prompted for the filename of the file to transmit.
                  Pressing just "ENTER" will result in no file being
                  transmitted.  Entering the word "stop" will cause
                  the current file being processed to be closed.

                  The filename is placed in a buffer que which will
                  eventually be opened and read.  This allows for
                  placing several transmit files into the transmit
                  buffer in sequential order.  The filename of the
                  file currently being read is displayed on the
                  center display line.  The form of the display is
                  "TX-filename".

                  If an error is encountered in opening the file, an
                  error status is displayed for about five seconds at
                  the bottom of the screen and a beep is sounded.

                  Note that the program will not handle tab
                  characters.  The file should contain spaces to get
                  to the correct column.  For example, if the file is
                  created using the Personal Editor program, be sure
                  to use the "notabs" keyword when the file is
                  saved.

              F4  -  TX CQ

                  Transmit a CQ.  Pressing this key causes the file
                  "CQ.RTY" to be loaded into the transmit buffer.
                  This file is queued just like a transmit file and
                  is displayed on the middle status line of the
                  screen.  Note that you must personalize the
                  "CQ.RTY" file with your callsign and name.

              F5  -  RESET

                  This is the reset key.  Pressing this key will
                  close all transmit files, clear the screen and
                  start the program over.  There is no prompting to
                  make sure you mean it.  Note, BASIC sometimes
                  decides to clean up the string area at the most
                  inappropriate times.  When it does this, the system
                  may appear to lock up for several seconds (maybe
                  many), so try to be patient.




          Program Operation                                         19


                              IBM PC RTTY Ver 1.2G 

              F6  -  TX RYS

                  Transmit RYs.  Pressing this key will result in the
                  "RYS.RTY" file to be placed into the transmit file
                  que and eventually into the transmit buffer.  This
                  is handy for placing a bunch of RYs at the start of
                  your transmission, which gives the guy at the other
                  end a chance to lock back onto your signal.

              F7  -  PSE OF/PSE ON

                  Transmit Pause Off / Transmit Pause On.  This key
                  is used to temporarily stop the program from
                  sending any more characters out of the transmit
                  buffer.  This is useful for sending a steady
                  carrier signal for tuning purposes or whatever.  It
                  should be noted, that BASIC can buffer up to 128
                  characters.  These characters cannot be stopped
                  from being sent.  Thus, you may not be able to make
                  the program pause exactly where you want.  When the
                  program begins, this key defaults to PSE OF.

              F8  -  TTY ID

                  Teletype ID.  Pressing this key causes the contents
                  of the "TTYID.RTY" file to be placed into the
                  transmit buffer.  The contents of the QSO ID buffer
                  is placed at the beginning of the line.  Note that
                  this line of data is read from the file at the
                  beginning of the program and stored in program
                  memory.  Also note that the "TTYID.RTY" file must
                  be personalized with your name and callsign.  The
                  little block at the end of the TTYID when it is
                  placed in the buffer is used by the program to
                  reset the time since last ID.

              F9  -  QSO ID

                  This key prompts you for an entry of the current
                  QSO station id.  The data entered is placed at the
                  beginning of the TTY ID when that key is pressed.

              F10 -  DT&TM

                  Date and Time stamp.  This causes the current date
                  and time to be placed into the transmit buffer.
                  Note that the time sent is the time the key is
                  pressed, not the time the characters are actually
                  sent.






          Program Operation                                         20


                              IBM PC RTTY Ver 1.2G 

          PROGRAM FILES


          There are three files which the program expects to find on
          the default DOS drive.  If any of these files are absent
          when they are accessed, an error message will be
          displayed.  There is also an optional file which may be
          absent with no adverse effects.  There are also two files
          which will be created if absent and will be written to by
          the program.  The files are described below.



          Required Files


              TTYID.RTY - This file is required to have one line
              only.  The line contains the characters to be placed in
              the transmit buffer for your RTTY ID (e.g. DE KF4NB
              "GLENN" IN LEXINGTON, KY).  Note, you must personalize
              this file with your callsign, name, location and
              whatever.

              CQ.RTY - This file contains all the information you
              would like to send for a RTTY CQ.  Note, you must
              customize this file with your callsign, name, and
              location.  You may optionally change the format of the
              CQ.  This file may contain any number of lines.

              RYS.RTY - This file is simply a line of RYs which will
              be sent in response to a function key being pressed.
              This file could be changed in just about any way you
              desired.  Multiple lines are allowed.






















          Program Operation                                         21


                              IBM PC RTTY Ver 1.2G 

          Optional Files


              LOG.RTY - This file will be appended to by the "Alt L"
              command.  The information placed in the file is the
              date, time, Station ID worked and your comments.  If
              the file does not exist, a new file will be created.

              TXBUFFER.RTY - This file will be created or read by the
              "Alt T" command.  The transmit buffer will be dumped
              into the file on the first use of the "Alt T" command
              and the file will be reloaded into the transmit buffer
              on the second occurrence of the "Alt T" command.

              AWAY.MSG - This file will be sent when the not-at-keys
              string is received.  This is primarily intended for
              packet operation to allow you to tell someone to leave
              you a message when they connect.   All received input
              up until the time the end string is received
              (disconnect) will be placed into the file "WHILE.OUT".
              Both the start and stop strings can be user defined.

              PARMS.RTY - This file can have one or more of the
              following keywords on a single line separated by commas
              or on separate lines.  The first three or four
              characters of the words are compared and when a match
              is found, the pertinent information is obtained from
              the text string.  Any extra information between commas
              or at the end of the line is ignored.  Blank lines are
              ignored.  Commas can be imbedded in a keyword string by
              placing the entire keyword string in double quotes.
              For example, "DTTM=HH:MM Z  MONTH DD, YYYY".

              The filename can be overridden by specifying the
              alternate filename on the command line (e.g. RTTY
              ASCII.RTY).  The contents of the file may be any valid
              keywords for the PARMS.RTY file.  The program will
              automatically attempt to append the RTY extension, if
              it is unable to find the filename specified.  When an
              alternate filename is specified on the command line,
              the program will prompt for a new filename anytime
              during that session that the RESET key is used.

              As the file is processed, each parameter specification
              is displayed on the screen.  When the file has been
              processed, the program will wait approximately three
              seconds and then clear the screen and continue.  This
              waiting period can be bypassed by pressing any key.

              During processing of the file any parameters which are
              incorrectly specified will be displayed on the screen
              and the program will wait for you to press "Enter" to
              continue.


          Program Operation                                         22


                              IBM PC RTTY Ver 1.2G 

                  AGSL - This keyword is used to set the general
                  SELCAL search string for ASCII mode selection.  The
                  format is AGSL=QST.  Up to 10 characters can be
                  specified.  The default is "QST".

                  ALCR - This keyword can be specified to override
                  the default value put into the ASCII Line Control
                  Register of the 8250 Async chip.  This value will
                  determine format of the ASCII data.  It controls
                  the number of data bits, the number of stop bits,
                  use of the parity bit and the type of parity if
                  used.  The format of the option is ALCR=&H3E.  The
                  default value is &H3E, which sets the ASCII mode to
                  7 data bits, 2 stop bits and parity bit stuck low.
                  Further information on the possible values of this
                  parameter can be found in the Technical Reference
                  Manual.

                  ART  - This keyword allows you to start the RTTY
                  program in the ART mode.  If it is not specified
                  the program defaults to NoART mode.

                  ASCI - This keyword is used to add extra values to
                  the ASCII baud rate selection list.  The format is
                  ASCI=nnnn where "nnnn" is any baud rate number you
                  want to be able to run.  Up to 10 baud rates are
                  allowed.  A second form of the keyword allows you
                  to redefine the baud rate for any of the rates in
                  the list (even the default values).  The format is
                  ASCIxx=nnnn where "xx" is a number from 1 to 10 and
                  "nnnn" is the desired baud rate.  The number "xx"
                  must correspond to a previously defined rate or
                  just one more than the total number of rates
                  defined.

                  When the baud rate is specified, the program will
                  set the 8250 Async chip timer divisor rate to the
                  closest value to achieve the specified rate.  The
                  divisor rate of the 8250 is set to the integer
                  value of the crystal frequency divided by the baud
                  rate.  A total of four ASCII baud rates can be
                  specified.  Refer to the Technical Reference manual
                  for further information on divisor rates.

                  ASEL - This keyword is used to set the specific
                  SELCAL search string for ASCII mode selection.  The
                  format is ASEL=KF4NB.  Up to 10 characters can be
                  specified.  The default is "??????????".







          Program Operation                                         23


                              IBM PC RTTY Ver 1.2G 

                  ATCR - This keyword is used to turn on the
                  automatic carriage return and line feed (CR/LF)
                  option.  When this option is on, a CR/LF will be
                  added to the transmit data if the data reaches
                  column 64 or the column specified in the LLEN
                  option.  This option defaults to off.

                  BAUD - This keyword is used to add extra values to
                  the Baudot baud rate selection list.  The format is
                  BAUD=nnn.n where "nnn.n" is any baud rate number
                  you want to be able to run.  Note that the baud
                  rate is different from the words per minute rate.
                  Up to 10 baud rates are allowed.  A second form of
                  the keyword allows you to redefine the baud rate
                  for any of the rates in the list (even the default
                  values).  The format is BAUDxx=nnn.n where "xx" is
                  a number from 1 to 10 and "nnn.n" is the desired
                  baud rate.  The number "xx" must correspond to a
                  previously defined rate or just one more than the
                  total number of rates defined.

                  When the baud rate is specified, the program will
                  set the 8250 Async chip timer divisor rate to the
                  closest integer value to achieve the specified
                  rate.  The divisor rate of the 8250 is set to the
                  integer value of the crystal frequency divided by
                  the baud rate.  A total of six Baudot baud rates
                  can be specified.  Refer to the Technical Reference
                  manual for further information on divisor rates.

                  BDLW - This keyword provides the capability to
                  change the Baudot to ASCII conversion table of the
                  program.  The BDLW command is used to specify the
                  letters mode Baudot character to ASCII character
                  relationship.  The format of the command is
                  BDLWnn=xxxx.  Where "nn" is a number from 0 to 31
                  representing the 5 bit Baudot code and "xxxx" is
                  the value of the ASCII character.  For example,
                  "BDLW10=&H52" causes the receipt of a Baudot
                  character of 10 in the letters mode to be
                  translated to an ASCII character of &H52 which is
                  the correct representation of the letter "R".  Any
                  number of BDLW commands may be contained in the
                  file.











          Program Operation                                         24


                              IBM PC RTTY Ver 1.2G 

                  BDUP - This keyword provides the capability to
                  change the Baudot to ASCII conversion table of the
                  program.  The BDUP command is used to specify the
                  figures mode Baudot character to ASCII character
                  relationship.  The format of the command is
                  BDUPnn=xxxx.  Where "nn" is a number from 0 to 31
                  representing the 5 bit Baudot code and "xxxx" is
                  the value of the ASCII character.  For example,
                  "BDUP10=&H34" causes the receipt of a Baudot
                  character of 10 in the figures mode to be
                  translated to an ASCII character of &H34 which is
                  the correct representation of the number "4".  Any
                  number of BDUP commands may be contained in the
                  file.

                  BDOT - This keyword provides the capability to
                  change the ASCII to Baudot conversion table of the
                  program.  The BDOT command is used to specify the
                  ASCII character to Baudot character relationship.
                  Part of this command requires the capability to
                  specify if the Baudot character should be sent in
                  letters mode, figures mode or don't care mode.
                  This is accomplished by adding 64, 128 or 192
                  (decimal) respectively to the Baudot character.
                  This can also be represented by &H40, &H80, and
                  &HC0 (hexidecimal).  The format of the command is
                  BDOTnn=xxxx, where "nn" is the value of the ASCII
                  character and "xxxx" is the value of the Baudot
                  character with the added value for the proper
                  mode.  For example, "BDOT52=&H8A" causes an ASCII
                  character of 52 ("4") in the transmit buffer to be
                  sent as a "figures" followed by a Baudot 10.  Note
                  that if the figures mode was already valid then no
                  figures character would have been sent.  Any number
                  of BDOT commands may be contained in the file.

                  BGSL - This keyword is used to set the general
                  SELCAL search string for Baudot mode selection.
                  The format is BGSL=(ltrs)N(ltrs)N(ltrs)N where the
                  "(ltrs)" indicates the letters Baudot character.
                  Up to 10 characters can be specified.  The default
                  is "(ltrs)N(ltrs)N(ltrs)N".  Note that "(ltrs)" is
                  defined to be "Ctrl Y" and "(figs)" is defined to
                  be "Ctrl X" during program operation.

                  BLLF - This keyword is used to suppress the sending
                  of carriage returns when a blank line is
                  encountered.  Only line feeds will be sent for
                  blank lines when this option is used.






          Program Operation                                         25


                              IBM PC RTTY Ver 1.2G 

                  BSEL - This keyword is used to set the specific
                  SELCAL search string for Baudot mode selection.
                  The format is BSEL=(ltrs)KF4NB where the "(ltrs)"
                  indicates the letters Baudot character.  Up to 10
                  characters can be specified.  The default is
                  "??????????".  Note that "(ltrs)" is defined to be
                  "Ctrl Y" and "(figs)" is defined to be "Ctrl X"
                  during program operation.

                  COLO - This keyword is used to set the values for
                  the color characters for a color display.  The
                  colors can be further modified independently
                  through other options of the "PARMS.RTY" file.  Any
                  further changing must occur after the COLO
                  statement.  The default is to black and white
                  characters.

                  COM2 - This keyword will cause the program to use
                  the second asynchronous communications adapter for
                  RTTY.  The program default is the first adapter
                  (COM1).  This option may be useful if the first
                  adapter is primarily used for some other reason
                  such as a telephone modem or a serial printer.
                  This keyword must be used with a PCjr if an
                  internal modem option is installed.

                  COMM - This keyword specifies the base I/O address
                  of the 8250 chip (serial port).  The default is
                  COMM=&H3F8.  For the PCjr the parameter should be
                  specified as COMM=&H2F8.  If the PCjr also contains
                  the internal modem option, the COMM keyword must
                  come after the COM2 keyword in the PARMS.RTY file.
                  Note that beginning in version 1.2F, the program
                  recognizes that you are running on a PCjr and
                  correctly sets the proper COMM value to &H2F8.

                  DIDL - This keyword is provided for those folks who
                  like to send something (even null) while the
                  transmit buffer is empty.  Null characters are sent
                  about once per second while the transmit buffer is
                  empty.

                  DTR  - This keyword can be used to specify what
                  logic level the DTR (Data Terminal Ready) line out
                  of the Asynchronous adapter should be set to for
                  receive and transmit modes.  The format is DTR=xy,
                  where xy can be 00, 01, 10, or 11.  The number
                  corresponding to "x" is the logic level during
                  receive and the number corresponding to "y" is the
                  logic level during transmit.  "0" corresponds to a
                  low logic level and a "1" corresponds to a high
                  logic level.  The default is DTR=01.



          Program Operation                                         26


                              IBM PC RTTY Ver 1.2G 

                  DTTM - This keyword lets you specify the format of
                  the date and time stamp which can be sent using
                  function key F10.  The normal default is "HH:MM:SS
                  TMT MONTH DD, YYYY", where HH is hours, MM is
                  minutes, SS is seconds, TMT is the time type (e.g.
                  EST), MONTH is the month name, DD is the day of the
                  month and YYYY is the year.  The default time will
                  change if the MARS or the EURO keywords are
                  specified.  By using DTTM you can customize your
                  time stamp to anything you would like it to be.
                  The following keys will result in the indicated
                  substitution actions:


                      HH    -  hours as two decimal digits
                      MM    -  minutes as two decimal digits
                      SS    -  seconds as two decimal digits
                      TMT   -  time type as specified by TIME keyword
                      MO    -  month as two decimal digits
                      MON   -  month as a three letter abbreviation
                      MONTH -  month as the actual month name
                      YY    -  year as two decimal digits
                      YYYY  -  year as four decimal digits

                  Any other characters entered along with the keyword
                  will be displayed as they appear, no substitution.
                  The form of the keyword is DTTM=HH:MM:SS Z
                  MO/DD/YY.  If you want to imbed a comma within the
                  date and time stamp, then the entire keyword must
                  be placed within double quotes.  For example,
                  "DTTM=HH:MM:SS TMT   MONTH DD, YYYY".
























          Program Operation                                         27


                              IBM PC RTTY Ver 1.2G 

                  ECHO - This keyword causes each character sent to
                  the BASIC "COMn:" port to be displayed on the
                  receive portion of the screen.  This option is
                  provided for those who have TUs which do not place
                  the transmitted data back onto the receive line
                  coming back to the computer.  The program default
                  is no ECHO.

                  Note - BASIC has a 128 byte transmit buffer.  When
                  this keyword is active, the receive screen shows
                  the character when it is placed into the BASIC
                  buffer.  In other words, just because you see it on
                  the screen doesn't mean it has been sent yet!  The
                  program contains a check to make sure that the
                  Asynchronous adapter has finished before turning
                  off the transmitter.

                  If the receive buffer seems to be repeating
                  characters while in the transmit mode, then the
                  most likely problem is that you have specified echo
                  and your TU is also feeding back into the receive
                  input.  ECHO should be removed from the "PARMS.RTY"
                  file.

                  ERRB - This keyword is used to set the error line
                  background color.  The format is ERRB=7.  The
                  defaults are ERRB=7 for the monochrome mode and
                  ERRB=0 for the color mode.  Refer to the BASIC
                  manual for colors associated with possible values.

                  ERRF - This keyword is used to set the error line
                  foreground color.  The format is ERRF=0.  The
                  defaults are ERRF=0 for the monochrome and ERRF=12
                  for the color mode.  Refer to the BASIC manual for
                  colors associated with possible values.

                  ESEL - This keyword is used to set the specific
                  SELCAL search string for turning off SELCAL and/or
                  packet not-at-keys data storage.  The format is
                  ESEL=* DISCON.  UP to 10 characters are allowed.
                  The default is "NNNN".














          Program Operation                                         28


                              IBM PC RTTY Ver 1.2G 

                  EURO - This keyword is used to specify the European
                  mode.  The date and time stamp format is changed to
                  default to the form "HH:MM:SS TMT    DD.MON.YYYY",
                  where HH is hours, MM is minutes, SS is seconds,
                  TMT is the time type (e.g. EST), DD is the day, MON
                  is the three letter month name and YYYY is the
                  year.  The time format can be changed using the
                  DTTM keyword.  This EURO mode uses the automatic
                  CR/LF option and changes the Baudot to ASCII
                  conversion table to fit the European standards
                  instead of the U.S. standards.  The differences are
                  for figures mode only and are as follows

                       Baudot  European
                        code   character
                         05       '
                         09       #
                         11      bell
                         13       [
                         17       +
                         20       !
                         26       ]
                         30       =

                  Note that any parameter specifications using the
                  BDLW, BDUP or BDOT commands should occur after the
                  EURO command in the file.

                  FILE - This keyword is used to specify the names of
                  files to be transmitted with the use of the "Alt n"
                  keys, where "n" is one of the number keys at the
                  top of the QWERTY section of the keyboard.  The
                  format of the command is FILEnn=filename, where
                  "nn" is a number from 1 to 10 and filename is any
                  valid DOS filename.  For example, FILE1=PARMS.RTY
                  will cause the "PARMS.RTY" file to be loaded into
                  the transmit buffer when "Alt 1" is pressed.  Note
                  that "Alt 0" will cause FILE10 to be loaded.  Note
                  that the file must be in the current directory.

                  GESL - This keyword is used to set the general
                  SELCAL search string for turning off SELCAL and/or
                  packet not-at-keys data storage.  The format is
                  GESL=QUIT.  UP to 10 characters are allowed.  The
                  default is "NNNN".

                  HAND - This keyword is used to tell the program to
                  start the communications port expecting to use the
                  handshaking lines.  Refer to the "OPEN COM" command
                  in the BASIC manual for further information.





          Program Operation                                         29


                              IBM PC RTTY Ver 1.2G 

                  KEYB - This keyword is used to set the keys status
                  line background color.  The format is KEYB=7.  The
                  defaults are KEYB=7 for the monochrome mode and
                  KEYB=3 for the color mode.  Refer to the BASIC
                  manual for colors associated with possible values.

                  KEYF - This keyword is used to set the keys status
                  line foreground color.  The format is KEYF=0.  The
                  defaults are KEYF=0 for the monochrome and the
                  color mode.  Refer to the BASIC manual for colors
                  associated with possible values.

                  LLEN - Use this keyword to specify the column at
                  which you want the end of the line to be.  This is
                  used in conjunction with the ATCR command.  The
                  format is LLEN=nn, where nn is the column number of
                  the end of the line.  The default is 64.

                  LPT2 - This keyword forces the printer output to go
                  the second printer adapter (LPT2).  The default is
                  LPT1.

                  LPT3 - This keyword forces the printer output to go
                  to the third printer adapter (LPT3).  The default
                  is LPT1.

                  MARS - This keyword modifies the operation of the
                  program slightly for compatibility with the MARS
                  format rules.  Specifically, end-of-line processing
                  is set to CR, CR, and LF.  A letters character is
                  not sent automatically at the end of the line or
                  after the "space" character if a number preceded
                  it.  Also the bell character is represented by an
                  "@" in the receive file.  The letters character
                  after space can be reenabled by specifying
                  BDOT32=&H44 after the MARS keyword in the PARMS.RTY
                  file.  Twelve consecutive characters will be sent
                  after "NNNN" is transmitted.  The characters will
                  be the letters function or any alternate character
                  specified using the NCHR keyword.

                  MODE - This keyword can be used to make the program
                  start up in the ASCII mode.  The form of the
                  keyword is "MODE=A".  The normal default is to
                  start in the Baudot mode.

                  NCHR - This keyword is used in conjunction with the
                  MARS keyword to specify the character to send when
                  "NNNN" is sent.  The character will be sent twelve
                  times.  The form of the keyword is NCHR=nn, where
                  nn is the value of the character to be sent.  The
                  default is NCHR=60 which causes twelve letters
                  functions to be sent.


          Program Operation                                         30


                              IBM PC RTTY Ver 1.2G 

                  NKEY - This is the keyword to use to specify the
                  search string for the not-at-keys message during
                  packet operation.  When the string is found, all
                  received data up to the reception of the stop
                  search string will be saved in the file WHILE.OUT,
                  unless a receive file is currently open.  When this
                  string is received, the file AWAY.MSG is sent out
                  over the Asynchronous lines.  The format of the
                  keyword is NKEY=** CONNECT.  Up to 10 characters
                  are allowed.  The default is "* CONNECTE".

                  NOBP - This keyword is used to disable the bell
                  character (beep) on the PC while in the ART mode
                  only.  You may use the alt-B key to toggle the
                  enable/disable of the bell character.

                  PACK - This keyword is used to make the controller
                  compatible with packet radio TNCs and smart
                  terminal units.  The program is modified to send
                  only one CR at the end of the line instead of the
                  normal two CRs.  Also when backspace is used, the
                  program will send the backspace character to the
                  TNC for any character already sent up to the last
                  CR.  The program will also erase the characters on
                  the last line which have been sent.  The program
                  will come up in the transmit mode.  Most TNCs are
                  semi-full duplex, so there is no need to run in the
                  half duplex mode.  (You can send data at any time
                  without tying up the channel.)

                  PDAT - This keyword is used to specify the packet
                  time/date command format, which is sent by the use
                  of the alt-D key.  You can specify just about any
                  form you want with the exception of no imbedded
                  commas.  The format of the keyword is
                  "PDAT=MO-DD-YYYY AT HH:MM:SS EST".  Where the
                  program will substitute in the proper numbers from
                  the date and time commands.  The parameters to use
                  are YYYY for the full 4 digit year, YY for just the
                  last 2 digits of the year, MO for the month, DD for
                  the day of the month, HH for the hours digit, MM
                  for the minutes and SS for the seconds.  Any other
                  characters in the string will be sent as is with no
                  substitutions.  Any of the parameters can be left
                  out of the string.  The default is
                  "PDAT=DAY YYMODDHHMMSS".

                  PKDT - This keyword tells the program to send the
                  packet time/date over the asynchronous lines when
                  the program is just starting or has just been
                  reset.  To send the packet time/date, use the alt-D
                  key during normal program operation.



          Program Operation                                         31


                              IBM PC RTTY Ver 1.2G 

                  QB   - This keyword causes a bell character to be
                  sent any time a quote character is sent in the
                  transmit mode.  This is possibly useful in RTTY
                  ART, since some machines have the quote and the
                  bell reversed.  No action is taken in the receive
                  mode.  The default is no QB.

                  RTS - This keyword can be used to specify what
                  logic level the RTS (Request To Send) line out of
                  the Asynchronous adapter should be set to for
                  receive and transmit modes.  The format is RTS=xy,
                  where xy can be 00, 01, 10, or 11.  The number
                  corresponding to "x" is the logic level during
                  receive and the number corresponding to "y" is the
                  logic level during transmit.  "0" corresponds to a
                  low logic level and a "1" corresponds to a high
                  logic level.  The default is RTS=01.

                  RXB  - This keyword is used to set the receive
                  buffer background color.  The format is RXB=0.  The
                  defaults are RXB=0 for the monochrome and RXB=2 for
                  the color mode.  Refer to the BASIC manual for
                  colors associated with possible values.

                  RXF  - This keyword is used to set the receive
                  buffer foreground color.  The format is RXF=7.  The
                  defaults are RXF=7 for the monochrome mode and
                  RXF=14 for the color mode.  Refer to the BASIC
                  manual for colors associated with possible values.

                  RXLN - This keyword is used to change the number of
                  lines used for the receive data area of the screen
                  and the transmit data area of the screen.  The form
                  of the keyword is RXLN=n, where n is the number of
                  lines you would like to use for the receive data
                  area.  The number is value checked to be within the
                  range of 2 to 20 (19 in 40 column mode).  The
                  remaining lines will be used for the status line,
                  key definition line(s), error reporting lines and
                  for the transmit data area lines.  Increasing the
                  receive lines will decrease the transmit lines.
                  The default number of receive lines is 11.

                  SPLF - This keyword is used to suppress the sending
                  of line feeds over the communications link.  This
                  may prove useful when the program is used to send
                  data to a packet radio TNC which cannot handle the
                  CR/LF normally sent at the end of a line.







          Program Operation                                         32


                              IBM PC RTTY Ver 1.2G 

                  STSB - This keyword is used to set the status line
                  background color.  The format is STSB=7.  The
                  defaults are STSB=7 for the monochrome mode and
                  STSB=6 for the color mode.  Refer to the BASIC
                  manual for colors associated with possible values.

                  STSF - This keyword is used to set the status line
                  foreground color.  The format is STSF=0.  The
                  defaults are STSF=0 for the monochrome and the
                  color mode.  Refer to the BASIC manual for colors
                  associated with possible values.

                  TIME - This keyword is used to set the time-type at
                  program startup time.  When this keyword is used,
                  the program will assume that the time and date are
                  set according to the time-type and no prompting for
                  the time will be done at program startup time.
                  (Generally people always set their time the same
                  way every time.)  The format is TIME=EST.  If
                  TIME=? is used then prompting will occur.

                  TXB  - This keyword is used to set the transmit
                  buffer background color.  The format is TXB=0.  The
                  defaults are TXB=0 for the monochrome and TXB=1 the
                  color mode.  Refer to the BASIC manual for colors
                  associated with possible values.

                  TXF  - This keyword is used to set the transmit
                  buffer foreground color.  The format is TXF=7.  The
                  defaults are TXF=7 for the monochrome mode and
                  TXF=11 for the color mode.  Refer to the BASIC
                  manual for colors associated with possible values.

                  UOS  - This keyword will cause the program to begin
                  operation with the unshift-on-space option turned
                  on.  The default is to start with the option turned
                  off.

                  WARN - Use this keyword to specify the column at
                  which you want the program to beep at you in the
                  transmit buffer to warn you that you are
                  approaching the end of the line.  The format is
                  WARN=nn, where nn is the column number at which you
                  would like to be warned.  The default is 56.











          Program Operation                                         33


                              IBM PC RTTY Ver 1.2G 

                  XMIT - This keyword tells the program to start up
                  in the transmit mode.  This will be useful for
                  operating with smart terminal units and packet
                  units.  The PACK keyword automatically invokes this
                  option.

                  XTAL - This keyword is used to specify the crystal
                  input frequency to the 8250 Async chip.  The format
                  of the command is XTAL=1.8432.  For the IBM PCjr
                  XTAL is set to 1.78977.  Note that the complete
                  number must be given and that any inaccuracies will
                  affect the accuracy of the baud rate.  The default
                  is set to 1.8432 MHz.

                  ZULU - This keyword is used to specify that time is
                  to be sent in a military format.  The default time
                  format is "DDHHMMZ MON YY", where DD is the day, HH
                  is the hours, MM is the minutes, MON is the first
                  three letters of the month and YY is the last two
                  digits of the year.  If the time displayed on the
                  screen is anything other than "UTC", you will be
                  prompted at the start of the program for the amount
                  of time in hours to be added to the local time to
                  convert it to UTC time.  You can specify the
                  default time difference in the PARMS.RTY file and
                  you will not be prompted for the adder.  The form
                  of the keyword is ZULU=n where n is the number of
                  hours to add to the default time.  The time format
                  can be changed by using the DTTM keyword.  Anytime
                  the timestamp is placed in the transmit buffer, the
                  program will convert the displayed time to "UTC"
                  time, correcting for any overflow into the next
                  day, month and/or year.  Leap years are also taken
                  into account.  Additionally, when this keyword is
                  specified the timestamp will also be appended to
                  the end of your "TTY ID".



















          Program Operation                                         34


                              IBM PC RTTY Ver 1.2G 

          UTILITY PROGRAM


          A utility program has been provided to perform some of the
          normal program functions offline.  The utility is started
          by entering

              RU


          Note that this program replaces the former RTTYU program.
          The program allows you to view a file in the way that it
          would be sent by the RTTY program.  There is one exception,
          the RU program interprets CR and LF characters literally
          unless they come after the cntl-W () and cntl-T ()
          special characters produced by the art mode.  The RTTY
          program interprets the either of the CR or LF characters as
          a normal end of line condition and forces a CR and LF.

          The RU program also allows you to save the program to file
          with the CRs and LFs converted to the special characters
          for art mode.  The program supports compressing the file
          which is being saved and also is capable of reading a
          compressed file correctly.  This feature should be good for
          uncompressing a file so it can be edited or for compressing
          a file to save diskette space.

          The RU program also allows you to print the file on your
          primary printer.  The printed output will be the same form
          as you would expect on a normal RTTY hardcopy device.  Line
          feeds work as line feeds and CRs by no corresponding LF
          will cause a line overstrike.  The program also supports
          printing the picture in the normal printer character size
          or printing it in a smaller format.  The smaller printer
          format gives a slightly better aspect ratio (height to
          width ratio) and also serves to make the copy a little
          darker in comparison to the full size printout.

          The program will prompt you for information which is
          necessary for it to figure out what you want to do.  Here
          again as in other places, responding with anything other
          than a word starting with the letter "Y" will be taken to
          mean "NO".  When the file is completely processed you will
          be asked it you would like to process more files.











          Program Operation                                         35


                              IBM PC RTTY Ver 1.2G 

          BASIC COMPILING HELP






          COMPILING THE RTTY PROGRAM


          I am changing my stance on sending out the source code from
          my original position.  Originally, I intended only for the
          compiled program to be sent to the general public and the
          source code to stay under relatively tight control.  Well,
          as luck would have it, some well meaning soul took the
          liberty of placing "My source code" on the public access
          disk of CompuServe and Lord knows where else.  Well, if you
          can't lick 'em. . . join 'em!  This little episode along
          with some requests for help in getting it to run on some PC
          clones has helped change my mind.

          So much for the philosophical statements, now to the good
          stuff.  There is one assembly language routine which must
          be assembled.  This routine is a basic subroutine to scroll
          half screens.  It must be properly linked into the basic
          program before it will work.  If it isn't done correctly or
          the BASIC program is run in the interpretive mode, chances
          are the PC will lock up really well when the receive screen
          is full.  Because the execution speed of the interpretive
          mode is totally unacceptable (by my standards) I won't even
          try to explain how to link in the assembly language routine
          to the interpretive mode.  The following lines show how to
          compile the RTTY program and properly link the appropriate
          programs to end up with the executable RTTY file.


          BASCOM RTTY,,,/X/W/O/C:4096/S       (Assumes source in B: and
          LINK RTTY+RTTYSUBS+A:IBMCOM,,,A:      BASIC compiler in A:,
                                                B: is primary)
















          BASIC Compiling HELP                                      36


                              IBM PC RTTY Ver 1.2G 

          COMPILING THE RTTYU PROGRAM


          The RTTYU program is similarly compiled as follows


          BASCOM RTTYU,,,/E/O                 (Assumes source in B: and
          LINK RTTYU,,,A:                       BASIC compiler in A:,
                                                B: is primary)




          GETTING AND ASSEMBLING THE RTTYSUBS PROGRAM


          Starting with version 1.2E, the Assembly language for the
          Scrolling routine to support the half screens is included
          in the RTTY.BAS file.  In order to properly assemble the
          program, first of all copy the RTTY.BAS program to a file
          called RTTYSUBS.ASM.  Next using an editor of some flavor,
          preferably a full screen editor such as Personal Editor,
          remove the first several hundred lines of the basic program
          up to the start of the assembly code.  Next, remove the
          BASIC line numbers and the quote mark and leading blank
          characters from the remaining statements.  Once this has
          been accomplished, you can use the macro assembler to
          generate the object module necessary to link the Compiled
          BASIC RTTY program.


























          BASIC Compiling HELP                                      37


                              IBM PC RTTY Ver 1.2G 

          INTERFACE INFORMATION






          INTERFACE SIGNALS


          This program interfaces to the Amateur Radio equipment
          through the Asynchronous Communications adapter.  The
          specifications for the voltage levels are those for a
          standard RS-232C interface.  In particular, the standard
          specifies voltage levels of +12 volts and -12 volts to
          represent the logic states of the signal.  Further
          information can be obtained in the Technical Reference
          Manual.  The signals which the program uses are as
          follows.

              Pin  2 - Transmit Data (Tx data)   - characters to TU

              Pin  3 - Receive Data  (Rx data)   - characters from TU

              Pin  8 - Carrier Detect (CD)       - CW data in from TU

              Pin  4 - Request to Send (RTS)     - Transmitter
              control

              Pin 20 - Data Terminal Ready (DTR) - CW ID control

              Pin  7 - Ground (Gnd)              - reference level

          For Tx data and Rx data, mark is -12v and space is +12v.
          CD is tied to Rx data and is not required for RTTY,
          however, I included it for future use if I ever get around
          to writing a Morse receive routine.

          RTS and DTR are -12v in receive mode and +12v in normal
          transmit mode.

          Hopefully this is enough information to help you interface
          to your terminal unit.












          Interface Information                                     38


                              IBM PC RTTY Ver 1.2G 

          KANTRONICS 'THE INTERFACE' INFORMATION


          While I will give information here on how I interfaced the
          Kantronics TU to my system, I must add that it was a
          decision based on availability and price at the time of
          purchase more than anything else.  If you are trying to
          make a decision, check around and see what is available and
          what seems to work well.  While the Kantronics does well in
          many cases, it does seem to have difficulty with weak
          and/or fading signals.  The Kantronics interface does not
          provide an RS-232C level interface and also requires an
          external power supply.  Additionally, the RTTY transmit
          line requires a normal space condition for receive to
          operate correctly.  Based on these considerations, I
          designed a special RS-232C to Kantronics interface box.
          The schematic is included below.

          Since my original purchase of a TU, Kantronics has come out
          with some new models which seem to have addressed some of
          the above mentioned problems.  In particular, they have
          increased the sensitivity of the circuits and have provided
          an RS-232C level interface.  So remember, it pays to
          inquire before you purchase.

          Next, just a few words about the circuit.  The interface
          chips used are the same as those used in the IBM PC,
          namely, the 75150 line driver and the 75154 line receiver.
          The 1488 line driver and 1489 line receiver from Radio
          Shack could also be used but the pinouts are different.
          The 74LS00 is used to gate the Tx data signal with the
          transmitter control, to invert the RTTY transmit signal and
          to invert signals for the normal/reverse switch.  The
          circuitry needs +5v, +12v and -12v to run.  I used the
          7805, 7812 and the 7912 voltage regulators to get my
          voltages, but you can use your favorite regulator.  Just be
          sure to have enough filter capacitance on the input and
          enough heat sink on the regulators.  There is nothing worse
          than intermittent problems when things get hot and heavy.
          Also note, the signal ground from the asynchronous adapter,
          the special interface ground and the TU ground should all
          be tied together.

          Due to popular demand, I have also included a schematic
          using the 1488 and 1489 which should be readily available
          at Radio Shack.









          Interface Information                                     39


                              IBM PC RTTY Ver 1.2G 

          KANTRONICS RS-232C INTERFACE SCHEMATIC






                            +5v
                             ³
               ÚÄÄÄÄÄÄÄÄÄÄ¿  ³
              Ä´1         ÃÄ ³ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ CWID
              Ä´          ÃÄÄÙ ³
              Ä´          ÃÄ   ³              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ KEYIN
  DTR ÄÄÄÄÄÄÄÄÄ´          ÃÄÄÄÄÙ              ³  ÚÄÄÄÄÄÄÄÄÄÄ¿
  Tx data ÄÄÄÄÄ´          ÃÄÄÄÄ¿              ÃÄÄ´1         ÃÄ +5v
  RTS ÄÄÄÄÄÄÄÄÄ´          ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄ´          ÃÄÄÄÂÄÄÄÂÄÄ DECODE
              Ä´   75154  ÃÄ   ³              ÚÄÄ´          ÃÄÄÄÙ   ³
          Gnd Ä´          ÃÄÄ¿ ³              ÀÄÄ´          ÃÄÄÄÄÄ¿ ³
               ÀÄÄÄÄÄÄÄÄÄÄÙ  ³ ³         ÚÄÄÄÄÄÄÄ´          ÃÄÄÄ¿ ³ ³
            ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³         ³ÚÄÄÄÄÄÄ´  74LS00  ÃÄÄÄ´ ³ ³
            ³                  ³         ³³ Gnd Ä´          ÃÄ¿ ³ ³ ³
            ³                  ³         ³³      ÀÄÄÄÄÄÄÄÄÄÄÙ ³ ³ ³ ³
            ³                  ³         ³³                   ³ ³ ³ ³
            ³                  ³         ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ RTTY
            ³                  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿      ³ ³ ³ ³
        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³            /oÄÄÄÄÄÄÄÄÙ ³ ³
        ³   ³                         ³  ÀÄÄÄÄÄÄÄÄÄÄÄo|       ³   ³ ³
        ³   ³                         ³               |oÄÄÄÄÄÄÙ   ³ ³
        ³   ³  ÚÄÄÄÄÄÄÄÄÄÄ¿           ³               |           ³ ³
        ³   ÀÄÄ´1         ÃÄ +12v     ³               /oÄÄÄÄÄÄÄÄÄÄÄÄÙ
        ÃÄÄÄÄÄÄ´          ÃÄÄÄÄÄÄÄÄÄ¿ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄo            ³
        ÀÄÄÄÄÄÄ´   75150  ÃÄÄÄÄÄÄÄ¿ ³                  oÄÄÄÄÄÄÄÄÄÄÙ
          Gnd Ä´          ÃÄ -12v ³ ³
               ÀÄÄÄÄÄÄÄÄÄÄÙ       ³ ³           Normal/Reverse
                                  ³ ³           DPDT switch shown
  Rx data ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³           in normal position
  CD ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  Gnd ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ Gnd

  Computer                                                        Kantronics
  Interface                                                       Interface

                                             ³
  Note: Non-Intersections are indicated by  ÄÄÄ
                                             ³
        All grounds are connected together.

        An IBM Graphics Printer is required for this schematic
        to print correctly.


                        Kantronics RS-232C Interface



  Interface Information                                     40


                      IBM PC RTTY Ver 1.2G 



  DTR ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                                  ³
               ÚÄÄÄÄÄÄÄÄÄÄ¿ +5v   ³
  Tx data ÄÄÄÄÄ´1         ÃÄÄÙ    ³      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ CWID
              Ä´          ÃÄÄÄÄÄÄÄÙ      ³
        ÚÄÄÄÄÄÄ´          ÃÄ             ³    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ KEYIN
  RTS ÄÄÄÄÄÄÄÄÄ´          ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ    ³  ÚÄÄÄÄÄÄÄÄÄÄ¿
   ÚÄÄÄÄÙ     Ä´          ÃÄ                  ÃÄÄ´1         ÃÄ +5v
   ³    ÚÄÄÄÄÄÄ´   1489   ÃÄ     ÚÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄ´          ÃÄÄÄÂÄÄÄÂÄÄ DECODE
   ³    ³ Gnd Ä´          ÃÄ     ³            ÚÄÄ´          ÃÄÄÄÙ   ³
   ³    ³      ÀÄÄÄÄÄÄÄÄÄÄÙ      ³            ÀÄÄ´          ÃÄÄÄÄÄ¿ ³
   ³    ³                        ³       ÚÄÄÄÄÄÄÄ´          ÃÄÄÄ¿ ³ ³
   ³    ³                        ³       ³ÚÄÄÄÄÄÄ´  74LS00  ÃÄÄÄ´ ³ ³
   ³    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ       ³³ Gnd Ä´          ÃÄ¿ ³ ³ ³
   ³                                     ³³      ÀÄÄÄÄÄÄÄÄÄÄÙ ³ ³ ³ ³
   ³                                     ³³                   ³ ³ ³ ³
   ³                                     ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ RTTY
   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿      ³ ³ ³ ³
     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³            /oÄÄÄÄÄÄÄÄÙ ³ ³
     ³                                ³  ÀÄÄÄÄÄÄÄÄÄÄÄo|       ³   ³ ³
     ³                                ³               |oÄÄÄÄÄÄÙ   ³ ³
     ³         ÚÄÄÄÄÄÄÄÄÄÄ¿           ³               |           ³ ³
     ³   -12v Ä´1         ÃÄ +12v     ³               /oÄÄÄÄÄÄÄÄÄÄÄÄÙ
     ÀÄÄÄÄÄÄÄÄÄ´          ÃÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄo            ³
  Rx data ÄÄÄÄÄ´          ÃÄ                           oÄÄÄÄÄÄÄÄÄÄÙ
              Ä´          ÃÄÄÄÄÄ¿
              Ä´          ÃÄ    ³               Normal/Reverse
              Ä´   1488   ÃÄ    ³               DPDT switch shown
          Gnd Ä´          ÃÄ    ³               in normal position
               ÀÄÄÄÄÄÄÄÄÄÄÙ     ³
  CD ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  Gnd ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ Gnd

  Computer                                                        Kantronics
  Interface                                                       Interface

                                             ³
  Note: Non-Intersections are indicated by  ÄÄÄ
                                             ³
        All grounds are connected.

        An IBM Graphics Printer is required for this schematic
        to print correctly.



                        Kantronics RS-232C Interface






  Interface Information                                     41


                      IBM PC RTTY Ver 1.2G 

  A TERMINAL UNIT DESIGN COMPLIMENTS OF BOB AUSTIN, N4CLH







  W1GAFSK MODULATOR WITH XR-2206
  W0H

   ** ALL PARTS ARE AVAILABLE AT RADIO SHACK **

                                                        ÚÄÄÄÄ¿
             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´1 16Ã
  R1= 220    ³  AUDIO OUTÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´C5ÃÄÄÄÄÄÄÄÄÄÄÄ´    Ã
  R2= 33K    ³           ÚÄÄÄÄÄÄÄÄÄ´R8ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´    ÃÄÄ´R1ÃÄÄÄÄÄÄ¿
  R3= 20K    ³           ³              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´    ÃÄÄÄÄÄÄÄÄÄÄÄÄÙ
  R4= 20K    ³           ³              ³   ÚÄÄÄÄ´C3ÃÄÄÄ´    ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  R5= 33K    ³           ³    +12VÃÄÄÄÄÄ´   ÀÄÄÄÄÄÄÄÄÄÄÄ´    Ã               ³
  R6= 4.7K   ³           ³              ³       ÚÄÄÄÄÄÄÄ´    ÃÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³
  R7= 4.7K   ³           ³              ³       ³    ÚÄÄ´8  9ÃÄÄÄÄ¿       ³  ³
  R8= 50K    ³           ³              ³       Á    Á  ÀÄÄÄÄÙ    ÃÄÄTTL  ³  ³
             ³    ÚÄÄÄÄÄÄÅÄÄÄÄ´R7ÃÄÄÄÄÄÄÙ       R5   R2           ³   IN  ³  ³
  C1= 1uf    ³    ³      ³                      Â    Â            ³     + Á  ³
  C2= .001uf ³  + Á      Á                      Á    ³            Á       C1 ³
  C3= .01uf  ³    C4     R6                     R4   Á            C2      Â  ³
  C4= 10uf   ³    Â      Â                      Â    R3           Â       ³  ³
  C5= .1uf   ³    ³      ³                      ³    Â            ³       ³  ³
            ÂÅÂ  ÂÅÂ    ÂÅÂ                    ÂÅÂ  ÂÅÂ          ÂÅÂ     ÂÅÂÂÅÂ
  -----------------------------------------------------------------------------
  NOTES:
  C3 MUST BE STABLE CAPACITOR
  R3/R4 SHOULD BE MULTI-TURN POTS
  R8 VARIABLE POT TO ADJUST AUDIO OUTPUT
  C1/C4 ARE ELECTROLITIC

  SETUP:
  POWER TO PIN 4, ADJUST R3 FOR 2125 HZ AT AUDIO OUTPUT
  POWER TO PIN 4, GROUND PIN 9, ADJUST R4 FOR 2295 HZ AT AUDIO OUTPUT
  ADJUST R8 FOR DESIRED AUDIO OUTPUT LEVEL TO MICROPHONE CONNECTION
  NORMALLY LESS THAN 1 VOLT PEAK.
  NOTE**
  THE XR2211 WILL BLOW IF MORE THAT 2V PEAK  AUDIO IS APPLIED. IF YOU HOOK UP
  THE RELAY CIRCUIT TO ECHO XMIT BUFFER DO NOT ADJUST R8 FOR MORE THAN THE
  2V PEAK.









  Interface Information                                     42


                      IBM PC RTTY Ver 1.2G 


  From Bob Austin, N4CLH





  W1GAFSK DEMODULATOR USING XR-2211
  W0H

                                             ÚÄÄÄÄÄ¿
                        IN      +12VÃÄÄÄÄÄÄÄÄ´1  14ÃÄÄÄÄÄ´C6ÃÄÄÄÄ¿
                      AUDIO  ÃÄÄÄÄÄÄÄ´C11´ÄÄÄ´     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
          ÚÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³   ³   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     ÃÄÄÄÂÄ´R9ÃÄÄÄÄÁÄÄ´R10ÃÄÄÄÄ¿
          ³   ³   ³                          ´     ÃÄÄÄ³ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿     ³
          ³   ³   ³       TTL OUTÃÄÄÄÄÄÄÄÄÂÄÄ´     Ã   ÀÄÄÄÄÄÄÄÄÄ¿     ³     ³
          ³   ³   ³                       ÃÄÄ´7   8ÃÄÂÄÄ´R12ÃÄÄÄÄ´     ³     ³
          ³   ³   ³       +5VÃÄÄÄÄ´R15ÃÄÄÄ´  ÀÄÄÄÄÄÙ ³           ³     ³     ³
          ³   ³   ³                       ³          ³           ³     ³     ³
          ³   ³   ³                       ÀÄÄÄ´R13ÃÄÄ´           Á     Á     Á
          Á   Á   ³                                  ³           C7    C8    R11
         R14  C10 ³                                  Á           Â     Â     Â
          Â   Â   ³                                  C9          ³     ³     ³
          ³   ³   ³                                  Â           ³     ³     ³
         ÂÅÂ ÂÅÂ ÂÅÂ                                ÂÅÂ         ÂÅÂ   ÂÅÂ   ÂÅÂ
  -----------------------------------------------------------------------------




  R9 = 220K
  R10= 15K         NOTES: PINS 10 AND 11 DO NOT CONNECT
  R11= 20K               R11 IS MULTITURN POT
  R12= 100K              C6 MUST BE STABLE CAPACITOR
  R13= 470K              C9 IS FOR 110 ASCII/BAUDOT OR LESS
  R14= 470K                 I SWITCH TWO CAPS AT C9 FOR LOW SPEED AND HIGH
  R15= 10K                  SPEED USING .047 AND .0047(HIGH) 300 ASCII/BAUDOT

  C6 = .022        ADJUSTMENT:
  C7 = .0047                 POWER TO PIN 1, ADJUST R11 FOR CLEAN COPY
  C8 = .1                   (I USE A STRING OF *U FOR ADJUSTMENT AT 110 ASCII)
  C9 = .047
  C10= .05
  C11= .1










  Interface Information                                     43


                      IBM PC RTTY Ver 1.2G 

  From Bob Austin, N4CLH

  W1GTTL TO EIA INTERFACE
  W0H

  I LIKE TO USE A 7404 OR 74LS04 BETWEEN THE EIA LINE DRIVER/RECEIVER
  AND THE EXAR CHIPS TO LET ME USE SOME L E D'S FOR MARK AND SPACE.
  YOU MAY ELIMINATE THIS CIRCUIT AND CONNECT THE EXAR CHIPS TO THE
  LINE DRIVER/RECEIVER DIRECT.

                 TTL IN  FROM XR2211-PIN6
                   ÄÂÄ
                    ³        7404 OR 74LS04
                    ³         ÚÄÄÄÄÄ¿
             N ÚÄÄÄÄÁÄÄÄÄÄÄÄÄÄ´1  14ÃÄÄÄÄÄÄÄÄÄ´+5V
        ÚÄÄÄÄÄÄÄ S1        ÚÄÄ´     Ã
        ³    R ÀÄÂÄÄÄÄÄÄÄÄÄÁÄÄ´     Ã
        ³        ³         ÚÄÄ´     Ã
        ³        Á      ÚÄÄÁÄÄ´     Ã
        ³       R16     ³     ´     Ã
        ³        Â      Á   ÚÄ´7  8 Ã
        ³        ³     R17  ³ ÀÄÄÄÄÄÙ
        ³        Á      Â   ³                    S1= SPDT FOR NORMAL AND REVERSE
        ³        D1     ³   ³                        SIGNALS
        ³        Â      Á   ³                    R16= 390
        ³        ³      D2  ³                    R17= 390
        ³        ³      Â   ³                    D1=  LED  (MARK)
        ³       ÚÅ¿    ÚÅ¿ ÚÅ¿                   D2=  LED  (SPACE)
  ------³---------------------------------------------------------------------
        ³     1488 DRIVER
        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿               1489 RECEIVER
                                   ³
       +12V    -12V      EIA PIN6  ³          PIN4    PIN9  PIN2        +5V
        Â       Â            Â     ³            ÂEIA    Â    ÂEIA        Â
        ³       ÀÄÄÄÄÄ¿      ³     ³            ³       ³XR  ³           ³
        ³     ÚÄÄÄÄÄ¿ ³      ³     ³            ³       ³2206³           ³
        ÀÄÄÄÄÄ´1  14ÃÄÙ      ³     ³            ³       ³    ³  ÚÄÄÄÄÄ¿  ³
            ÄÄ´     ÃÄÄÄ¿    ³     ³            ³       ³    ÀÄÄ´1  14ÃÄÄÙ
            ÄÄ´     ÃÄÄÄÁÄÄÄÄ³ÄÄ¿  ³        ÚÄÄÄ³ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     Ã
            ÄÄ´     ÃÄÄÄÄÄÄÄÄÙ  ³  ³        ³   ³       ÀÄÄÄÄÄÄÄ´     Ã
            ÄÄ´     ÃÄÄÄ¿       ³  ³        ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     Ã
            ÄÄ´     ÃÄÄÄÁÄÄÄÄÄÄÄ³ÄÄÙ        ³      ÚÄÄÄÄÄÄÄÄÄÄÄÄ´     Ã
            ÚÄ´7  8 ÃÄÄÄÄ¿      ³           Á      ³      ÚÄÄÄÄÄ´     Ã
            ³ ÀÄÄÄÄÄÙ    ³      ³          C11     ³      ³   ÚÄ´7  8 Ã
            ³            ³      ³           Â      Á      Á   ³ ÀÄÄÄÄÄÙ
            ³  EIA   ÃÄÄÄÙ      ³           ³     C12    RELAY³
            ³  PIN3             ³           ³      Â     DRIVE³
           ÚÅ¿                 ÚÅ¿         ÚÅ¿    ÚÅ¿        ÚÅ¿


  C11= .1
  C12= .1



  Interface Information                                     44


                      IBM PC RTTY Ver 1.2G 


  From Bob Austin, N4CLH




  W1GPTT CIRCUIT
  W0H

  FOR THE RELAY TRANSISTOR, I USED A PNP 2N3906.
                          E
   PIN6              ÚÄÄÄÄÂÄÄ +5V
  1489 ÃÄÄÄÄÄÄ´R18ÃÄÄ´B   ³
  RCVR               ÀÄÄÄÄÁÄÄ RELAY COIL (OTHER END GND)
                          C
  R18= 470
  RELAY= DPDT 5VOLT MINIATURE.
  ** THERE ARE SEVERAL WAYS TO HOOK THE RELAY UP TO YOUR PTT.
  I COUPLED MY AUDIO OUTPUT TO THE AUDIO INPUT TO ECHO
  MY XMITTED BUFFER BACK TO ME.(THIS ALLOWS ME TO SEE BOTH XMIT AND
  RECEIVE IN MY SAVED FILES)
  IF YOU USE THE ECHO FUNCTION OF A RTTY PROGRAM YOU DO NOT HAVE TO
  HOOK THIS UP.. A SPST RELAY IS SUFFICIENT FOR PTT



  AUDIO HOOKUPS ON THE RELAY ARE MADE WITH COUPLING CAPS C5 AND C11 BETWEEN
  XR CHIPS AND RELAY.

  XR2206               COM ÚÄÄÄÄÄ¿COM
  AUDIO INPUT     ÃÄÄÄÄÄÄÄÄ´     ÃÄÄÄÄÄÄÄÄ´ PTT INPUT
  XR2211             N/OPEN³     ³ N/OPEN
  AUDIO OUTPUT    ÃÄÄÄÄÄÄÄÄ´     ÃÄÄÄÄÄÄÄÄÄÄÄ¿
                    N/CLOSE³     ³ N/CLOSE   ³
  RIG AUDIO OUT   ÃÄÄÄÄÄÄÄÄ´     ÃÄÄÄÄÄÄÄ    ³
  (SPKR)                   ÀÄÄÄÄÄÙ           ³
                                             ³
                                             ³
                                             ³
                                            ÚÅ¿



  W1G73's N4CLHW0H











  Interface Information                                     45
      ÚÅ¿



  W1G73's N4CLHW0H











  Inte