WELCOME TO THE SSTV AND FAX PROGRAM SSTVFAX VERSION ON5KN_16

						AUTHOR:ON5KN BBS @ON7RC-5
							BELGIUM

	THIS IS AN EXPERIMENTAL RECEIVE AND TRANSMIT PROGRAM WRITTEN IN
	ASSEMBLER AND TO USE ON ANY IBM COMPATIBLE UNDER MSDOS

	THE UPSET WAS MADE TO BE ABLE TO RECEIVE AND TRANSMIT SSTV AND
	FAX WITH A MINIMUM OF ADDITIONAL EXTERNAL HARDWARE

	FOR RECEPTION OF BOTH MODES YOU ONLY NEED A SIMPLE 741-IC
	TRANSMITTING TAKES PLACE VIA A LM324 AND A XR2206

	BOTH TRANSMIT AND RECEIVE HARDWARE ARE POWERSUPPLIED BY
	THE RS232 FROM THE PC

	THE SCHEMATICS ARE ADDED IN THE FILE SSTVFAX2.SCH WICH YOU
	SIMPLY CAN PRINT UNDER MSDOS ON	A GRAPHICS PRINTER
	USAGE: COPY SSTVFAX2.SCH PRN /B

	BE SURE TO MAKE THE CORRECT ADJUSTMENTS FOR THE TX-MODULE
	SYNCPULSES MUST BE 1200HZ
	FULL WHITE MUST BE BELOW OR EQUAL TO 2300HZ
	TO OBTAIN FULL WHITE SCREEN USE:
	IN RX-MODE CLEAR SCREEN TO BLACK WITH C,E OR V
	BRING TO KEY-MODE WITH K
	INVERT FULL BLACK SCREEN TO FULL WHITE WITH I

	SOME DYNAMIC ADJUSTMENT MAY BE NECESSARY TO FINE-ADJUST THE
	1200HZ PULSES (TRY ON A BLANK SCREEN)
	A 4-LEVEL GREYSCALE IS AUTOMATED ON BOTTOM OF EACH PICTURE

	SSTV CAN BE RECEIVED FROM ALL ACTUAL PRESENT MODES HOWEVER
	THE IMAGES WILL BE DISPLAYED IN GREY-LEVELS EVEN FOR COLOUR
	SENDED PICTURES
	TRANSMISSION OF SSTV IS POSSIBLE IN 16 GREY-LEVELS AND IN
	FOUR STANDARD MODES 8SEC, 16SEC, 32SEC,(NORMAL) AND 64SEC
	(IN DOUBLE MODE)

	FAX WILL BE RECEIVED IN 120 OR 90 LPM
	TRANSMISSION OF FAX WILL ALSO BE IN 120 OR 90 LPM AND AN
	OPTION PERMITS TO SEND EACH LINE TWICE (DOUBLE MODE)

	THE RECEPTION SCREEN CAN BE ONE OF THE CURRENT MODES EXCEPT
	S-VGA WICH IS NOT YET SUPPORTED

	SOME VIDEO CARDS MAY NOT BE COMPATIBLE

	IN SSTV BEST SYNC WILL BE OBTAINED WHEN RIGHT BOTTOM OF IMAGE
	IS POINTED WITH RIGHT MOUSE BUTTON

	START POINT OF IMAGE ON SCREEN CAN BE REDEFINED WITH MOUSE-
	POINTING AND LEFT MOUSE BUTTON

	ON SOME MODES OF COLOUR SSTV IT MAY BE INTERESTING TO USE
	DOUBLE COMPACTATION AND OR POINT RIGHT BOTTOM SYNCRO POINT
	AT END OF SCREEN

	ON RECEPTION OF 96 SEC OR MORE IMAGES USE OF "U" TO DISABLE
	VERTICAL SYNC UNTIL NEXT "T" AVOID SPURIOUS SYNC BY QRM

	AS TIMING IS CRITICAL ON SUCH AN APPLICATION THE POSSIBILITIES
	ARE FUNCTION OF THE SPEED OF YOUR PC AND TYPE OF SCREEN

	THE PROGRAM WAS WRITTEN ON  AT 286/12MC 640K VGA

	MAINLY CGA AND HERCULES MODES ARE NOT FULLY QUALIFIED BUT
	CAN GIVE ACCEPTABLE RESULTS IN RECEPTION

	A XT PC/4.7MC WILL NOT RESPECT THE TIMING STANDARDS IN TRANSMISSION

	ANOTHER FEATURE WICH EXPANDS THE POSSIBILITIES IS A STANDARD
	MOUSE WITH MOUSE-DRIVER

	THE PICTURES CAN BE STORED ON DISK AND VIDPIC.COM ALLOWS YOU
	TO PICK SCREENS FROM OTHER APPLICATIONS

	IF YOUR SYSTEM IS EQUIPED WITH A HAND-SCANNER YOU ARE ABLE
	TO CREATE YOUR OWN PICTURES AND PROCESS THEM WITHIN SSTVFAX
	MAKING SLOWSCAN AND FAX ON A REAL LOW-BUDGET WICH WAS THE
	MAIN TARGET OF THIS PACKAGE AND TO BRING THESE MODES OF
	RECEPTION AND TRANSMISSION AS A SIMPLE ADD TO THE BECOMING
	COMMON-USE-PC IN THE RADIO-AMATEUR WORLD

	TRY FIRST THE RECEPTION MODULE !
	IT IS EASY AND YOU WILL SEE THE ACTIVITIES ON HF AND VHF
	NEAR 14.230KHZ YOU ARE SURE TO SEE THEM FIRST

	ENJOY THIS FREE SOFTWARE PACKAGE AND LET ME KNOW WHAT YOU
	ARE THINKING ABOUT AND GIVE SOME SUGGESTIONS
	MAKE REFERENCE TO SSTVFAX2

	IF YOU MAKE A COPY FOR FURTHER DISTRIBUTION PLEASE LEAVE IT
	IN THE SELF-EXPLODING FORM SSTVFAX2.COM OR AT LEAST BE SURE
	THAT IT INCLUDES SSTVFAX2.TXT/SSTVFAX2.SCH/SSTVFAX.EXE/VIDPIC.COM
	AND THIS SSTVFAX2.DOC FILES

	LAST REMARK ... YOUR TIMER MAY BE DISTURBED AFTER RUNNING
	SSTVFAX JUST TILL ANOTHER START-UP OF YOUR PC

	HAVE A LOT OF FUN AND SEE YOU SOON ON THE BANDS
				73 ON5KN BBS @ON7RC-5 BELGIUM