;*************************************************************************
;**									**
;**			PDCLKSET					**
;**									**
;**									**
;**		Copyright (C) 1991 Jan.Engvald @ LDC.lu.se		**
;**									**
;** This program is free software; you can redistribute it and/or modify**
;** it under the terms of the GNU General Public License as published by**
;** the Free Software Foundation, version 1.				**
;**									**
;** This program is distributed in the hope that it will be useful,	**
;** but WITHOUT ANY WARRANTY; without even the implied warranty of	**
;** MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE.  See the	**
;** GNU General Public License for more details.			**
;**									**
;** You should have received a copy of the GNU General Public License	**
;** along with this program; if not, write to the Free Software 	**
;** Foundation, Inc., 675 Mass Ave, Cambridge, MA 02139, USA.		**
;**									**
;*************************************************************************
;**		USING PDCLKSET TO SET THE PC SOFTWARE CLOCK		**
;*************************************************************************
;**									**
;** PDCLKSET sets the time and date of the PC clock using a TIME server.**
;** To do so, the following information is required:			**
;**									**
;** - This clients unique IP number.					**
;** - The IP number of an UDP/IP time server (most Unix systems).	**
;** - The time zone offset from UTC (GMT) at this place.		**
;** - If daylight saving (summer) time is used, which algorithm to use. **
;**									**
;** All the above info can be supplied as arguments to PDCLKSET. If any **
;** of the first three are missing, it will send a BOOTP request to try **
;** to find the missing info. If you are not using BOOTP you probably	**
;** must use gateway and mask arguments too. Except for client IP number**
;** and network mask, arguments to PDCLKSET override BOOTP info.	**
;** Using a BOOTP server is highly recommended, freeware code exists	**
;** for Unix systems and MSDOS PCs.					**
;**									**
;** BOOTP can not supply which dst algorithm to use; also, zone offset	**
;** can't always be trusted. So, in practice, zone offset and dst algo- **
;** rithm (if applicable) are required arguments. On the other hand,	**
;** these parameters will stay the same all around the year, no need to **
;** change the setup.							**
;**									**
;** If PDCLKSET finds more than one time server (sum of arguments and	**
;** BOOTP fields) and the first one does not answer, it will try the	**
;** other servers. The same applies for gateways.			**
;**									**
;** It is very hard to get accurate info on all the dst algorithms used **
;** all over the world, so the one you choose, you should test out. Use **
;** the alter argument to add or subtract time and days, and check that **
;** the dst switch occurs correctly. When using the alter argument, the **
;** date and time is displayed as usual, but the PC clock is not set.	**
;** If you find any errors, mail me the correct info to my mail address **
;** below. If you want to, you can customize your own dst algorithm,	**
;** see detailed info below.						**
;**									**
;** PDCLKSET talks to the network card via a packet driver. If you have **
;** more than one packet driver, it will use the first one (lowest	**
;** packet interrupt number) unless you use the pktintno argument.	**
;** If you use a NDIS (LanManager) or ODI driver with your LAN card you	**
;** can still use PDCLKSET, just load DIS_PKT or ODIPKT on top of your	**
;** driver (available in pub/msdos/pktdrvr on many ftp archives).	**
;** I have only tested PDCLKSET with Ethernet or Ethernet simulating	**
;** packet drivers. I have one report that it works with S&K FDDI	**
;** interfaces, if so it should work for token ring too, but I've got	**
;** no confirmation on that.						**
;**									**
;** Running through remote bridges or slip links may require longer	**
;** than default timeouts. Add the number of extra seconds you need	**
;** with the argument LongerTimeout= time.				**
;**									**
;** If you want to omit the "End of pdclkset..." msg, add Flag=128 	**
;**									**
;** In AUTOEXEC.BAT you should first load the packet driver, then call	**
;** PDCLKSET. It is very small (14 kbyte) and executes fast, so you will**
;** not notice any delay. PDCLKSET is not memory resident and does not	**
;** use any CONFIG.SYS devices, so no memory is wasted. Use TERMIN.COM	**
;** if you want to unload the packet driver. See call syntax below.	**
;** Note: If you always log into a Novell server after a boot, you	**
;** don't need this program, the PC clock will be set from the server.	**
;** However, if you are the supervisor, use PDCLKSET+SRVTIME to set it	**
;** (available at msdos.ftp.sunet.se:pub/network/novelutl/srvtime).	**
;**									**
;*************************************************************************
;**		USING PDCLKSET TO SET A TIMEZONE VARIABLE		**
;*************************************************************************
;**									**
;** PDCLKSET can also assign the proper normal or dls timezone name to	**
;** an environment variable (TZ is used by most systems). Argument	**
;** "Zone= #" will assign numeric zones to TZ (like TZ=+0100). If you	**
;** want anything else, use the alternative syntax, e.g.		**
;** "Zone= tzone=MET,METDST" will set TZONE=MET or METDST.		**
;**									**
;*************************************************************************
;**		SYNTAX AND EXAMPLES FOR TIMESETTING			**
;*************************************************************************
;**									**
;**   (time is [- | +] [<hours>h] [<minutes>m] [<seconds>[s]] ) 	**
;**									**
;** pdclkset			(displays a usage message)	or	**
;**									**
;** pdclkset b[ootp]		(only if dst not used)	or		**
;**									**
;** pdclkset [o[ffset]=time]						**
;**									**
;**	     [d[aylightsave]=PAC | USA | CUB | CHIL | BRZ | GBR |	**
;**			     W_EU | M_EU | E_EU | LIBY | EGY | TURK |	**
;**			     ISR | IRAN | PRC | ROK | AUS | TASM |	**
;**			     NSW | LHI | NZE |				**
;**			     FrTime,FrWeekDay,FrDayOfYear,		**
;**			     ToTime,ToWday,ToDayOfYr,AddTime]		**
;**									**
;**	     [z[onename]= # | varible=normalname,dlsname		**
;**									**
;**	     [i[pnr]=n.n.n.n]  [t[imservers]=n.n.n.n[,n.n.n.n[,...]]]	**
;**									**
;**	     [m[ask]=n.n.n.n  g[ateways]=n.n.n.n[,n.n.n.n[,...]]]	**
;**									**
;**	     [p[ktintno]=hexnr]  [a[lter]=days,time]  [f[lags]=flagnr]	**
;**									**
;**	     [l[ongertimeout]=time]					**
;**									**
;**									**
;** All arguments to pdclkset must be on the same line, no continuation.**
;** For arguments to BAT files, use ":" instead of "=" and ";" instead	**
;** of "," .								**
;**									**
;** Valid flags for this mode:						**
;**   128 = half quiet (skip the End of pdclkset line if no errors)	**
;**									**
;** Examples:								**
;**									**
;** pdclkset o= -1h d=M_EU z=#	 (my IP nr and timeserver(s) from BOOTP)**
;**									**
;** pdclkset offs=6h dst=USA zonename= tz=CST,CDT  (sets TZ=CST or CDT) **
;**									**
;** pdclkset o=8h  d=PAC  ip=123.45.6.7  ts=123.45.6.8	(BOOTP not used)**
;**									**
;** pdclkset o=-9h30m t=1.2.3.4 i=2.3.4.5 g=2.3.4.1 m=255.255.255.0	**
;**									**
;**									**
;** Part of an AUTOEXEC.BAT file may look like this:			**
;**									**
;**	\net\smc_wd -w 0x7c 3 0x280 0xd000	(install packet driver) **
;**	\net\winpkt 0x7c			(install winpkt driver) **
;**	\net\pdclkset o=-1h d=M_EU z=#		(set PC clock and TZ)	**
;**									**
;** If you don't want to keep the paket drivers in memory, add the	**
;** following line:							**
;**									**
;**	\net\termin 0x7c			(remove packet drivers) **
;**									**
;** If you just need timesetting, use pdclksml instead of pdclkset.	**
;**									**
;*************************************************************************
;**		USING PDCLKSET FOR NETWORK TESTING (PING/ECHO)		**
;*************************************************************************
;**									**
;** There is also a buildt in ping client and server. If you just want	**
;** to enable the server, add a "flag=1" argument and the PDCLKSET	**
;** termination will be delayd and it responds to incoming pings until	**
;** you hit any key. If you want to send pings, use the echo argument.	**
;** When you then hit any key, it stops sending but still collects	**
;** responses. It terminates when hiting a second key (there may be a	**
;** delay to ensure all responses have arrived first). When pinging,	**
;** it displays real time statistics on delay and error rate (nice!).	**
;** PDCLKSET sets the hardware timer to enable millisecond accurate	**
;** timing; if your PC does not like this (e.g. SoftPC for Mac), add	**
;** argument "flag=16".							**
;**									**
;** A typical ping call look like:					**
;**									**
;**	pdclkset echo=ping.lu.se,34,256 				**
;**									**
;** The display will look like this:					**
;**									**
;** Calling nameserver(s)... got reply in  115 ms.			**
;**									**
;** Ping with packet size 34 and interval   256 ms to 130.235.128.100:	**
;**									**
;** ------ Packets ------ | --- Delay ms --- |	Packet	| Load | Time	**
;** transmit receive diff | this min avg max |	 loss	| kb/s |    s	**
;**	 187	 184	3.    87  27  36 517	1.6042 %     5	   41	**
;**									**
;**									**
;** You can use IP packet sizes from 34 to 1500. If you use a		**
;** negative size, it will sweep packet sizes from 34 up to abs(size)	**
;** and unless you hit ESC at termination an error size distribution	**
;** table is displayd. You can then see if packets are lost randomly or **
;** in bursts or if there is a pattern, like odd or big sizes. (Only	**
;** sizes 34 and up are used, but the number of out of sequence packets	**
;** are indicated in the size 22 position, the number of repeated	**
;** packets in the size 24 position and the number of lost packets are	**
;** in the size 26 position.) Using the minsize parameter you can sweep	**
;** a certain range, e g echo=host,-1500,128,1,1,1400 will sweep from	**
;** size 1400 up to size 1500 bytes.					**
;** While a few network errors only show up at a certain size, the	**
;** default 34-50 sweep is good in most cases and does not load links	**
;** unnecessarily. Sweeping is very effective for detecting queue	**
;** limits in routers and bridges, but then you should sweep up to at	**
;** least size 600 and with only a few milliseconds interval.		**
;**									**
;** The ping packet data is by default starting at 0x101 and incremented**
;** by one for each word in the packet. Using the optional data and inc **
;** fields you can fill with other values, like 0,0 or 0xffff,0 which	**
;** are useful for WAN modem link tests.				**
;**									**
;** Packets are transmitted at a constant rate depending on interval,	**
;** which can be from 0 and up to 28000. The interval unit is now 1.0	**
;** milliseconds (Note: ver 1.33 had 55 ms units!). To get a finer	**
;** interval grain, you may use a decimal point and one decimal digit.	**
;** This way you can get intervals from 0.0 up to 3500.0 ms, and the	**
;** inteval unit is rather close to 0.1 ms. As a safety for accidental	**
;** loading, if you wan't intervals less than 128 ms you must add a	**
;** Flag=1 argument. The default interval is 220 ms.			**
;**									**
;** When pinging in a wide area network environment, watch the load	**
;** figure not to overload slow links (showing the load caused by this	**
;** ping activity + server activity + broadcasts, and calibrated for	**
;** half duplex media such as Ethernet or LocalTalk). It requires just	**
;** a 20 MHz 386 to load an Ethernet to 9.9 Mb/s! The document		**
;** "Measured Capacity of an Ethernet: Myths and Reality" by Boggs,	**
;** Mogul and Kent, available at gatekeeper.dec.com in directory	**
;** pub/DEC/WRL/research-reports as file WRL-TR-88.4.ps.Z, is a good	**
;** source to read to understand how Ethernet behaves at such loads.	**
;**									**
;** The destination host must run IP and you can use its IP number or	**
;** its domain name if you have a name server.				**
;**									**
;** Diff is the difference between sent and received packets, and if	**
;** not zero either packets are lost or are in transit. If there are	**
;** network errors, watching how receive and diff increments tell you	**
;** how the errors are distributed in time (temporary total blocking or **
;** just random drops) down to tenths of a second (very useful!).	**
;** Blocking indicates serious errors, else it can be just high load.	**
;**									**
;** If there turns up a number between packets received and diff, it is **
;** the number of packets dropped due to no buffers available. This can	**
;** occur if the ping server is not as fast as the ping client and it	**
;** uses sub-millisecond intervals.					**
;**									**
;** If there turns up an apostrophe, double music note or dot after the	**
;** diff value, it indicates that packets have returned out of sequence	**
;** (may occur if there are multiple routes to the destination), been	**
;** duplicated or lost, respectively. Apostrophe + dot combine to	**
;** exclamation mark. You can see the number of each error in the	**
;** size 22/24/26 error distribution.					**
;**									**
;** The delay values are useful to characterize link loads. After a	**
;** while, the min value approaches the delay on an unloaded link. If	**
;** the average value is significantly higher, the link is loaded. If	**
;** the max value is significantly higher than the avg value, the load	**
;** is bursty. The "this" field shows the current delay.		**
;**									**
;** Packet loss is simply 100*diff/transmit, when you have stopped	**
;** pinging. During the pinging, however, there can be many packets in	**
;** transit giving a non-zero diff. So instead the packet loss is	**
;** computed using an intelligent algorithm that can compensate for	**
;** long turnaround delays and most out of sequence cases.		**
;**									**
;** If the host you are pinging don't drop packets (many do, a 386 with	**
;** PDCLKSET doesn't), the packet loss as a symptom of network health	**
;** is as follows:							**
;**									**
;**   0.01 % or less  : your network is most probably healthy. 		**
;**   0.01 % to 0.1 % : there are some minor faults but nobody will	**
;**			notice any delays.				**
;**   0.1 % to 1 %    : you will notice delays more or less often.	**
;**   1 % or more     : frequent delays, very annoying. 		**
;**									**
;** Some packet drivers, like smc_wd.com, give 0.0000 % lost packets on	**
;** a healthy network. This enables you to trace beginning component	**
;** degradation (oxidizing contacts, drifting IC circuits, etc) long	**
;** before they cause any trouble to real traffic.			**
;**									**
;** The display is updated five times a second. To avoid unpleasant	**
;** value flickering, when a packet is just sent, diff is temporarily	**
;** one less than it should be. When a packet has arrived it is back to **
;** normal. All values (except the "this" and the load values) are	**
;** accumulated or averaged during the complete time since pdclkset was **
;** last started. The time field tells you this elapsed time.		**
;**									**
;** Using udpecho= instead of echo= will send UDP echo instead of icmp	**
;** echo (ping) packets. Add flag=64 if you want UDP discard packets,	**
;** useful for saturated bottleneck throughput measurements.		**
;**									**
;** Argument f=1 will continue sending despite some send errors.	**
;**									**
;** If you don't run a BOOTP server, the i= (and n=) arguments are	**
;** needed and also m= and g= if any traffic goes through a router.	**
;**									**
;**									**
;** Syntax:								**
;**									**
;** pdclkset e[cho]= name | n.n.n.n [,size[,interval[,data,inc[,min]]]]	**
;**									**
;**	     [i[pnr]=n.n.n.n]  [n[ameservers]=n.n.n.n[,n.n.n.n[,...]]]	**
;**									**
;**	     [m[ask]=n.n.n.n  g[ateways]=n.n.n.n[,n.n.n.n[,...]]]	**
;**									**
;**	     [p[ktintno]=hexnr]  [f[lags]=flagnr]			**
;**									**
;**	     [l[ongertimeout]=time]					**
;**									**
;**	     u[dpecho]= name | n.n.n.n [,size[,intrvl[,data,inc[,min]]]]**
;**									**
;** Valid flags for server mode (no echo= or udpecho= argument):	**
;**	1 = Ping/Echo server (delay termination)			**
;**    16 = Not enough IBM compatible PC, use DOS interrupts		**
;**   128 = half quiet (skip the End of pdclkset line)			**
;**   512 = Stress the packet driver using upcall sends for ping serv	**
;**  4096 = Allow frame size up to 4096 (IP size 4082 bytes)		**
;**									**
;** Valid flags for client mode (echo= or udpecho= arguments):		**
;**	1 = Allow short (<128 ms) intervals; also continue despite errs **
;**    16 = Not enough IBM compatible PC, use DOS interrupts		**
;**   (32 = Use 0.1 ms interval unit instead of 1.0 ms)			**
;**    64 = For udpecho= argument, send discard instead of echo packets	**
;**   128 = half quiet (skip the End of pdclkset line)			**
;**   512 = Stress the packet driver using upcall sends for ping serv	**
;**  1024 = Stop if duplicated, lost or nonconsecutive packets seen	**
;**  4096 = Allow frame size up to 4096 (IP size 4082 bytes)		**
;**									**
;**									**
;** Examples:								**
;**									**
;** pdclkset  echo= nic.ddn.mil (ping client, auxilary info from BOOTP) **
;**									**
;** pdclkset  e= 1.2.3.4  i= 2.3.4.5  g= 2.3.4.1  m= 255.255.255.0	**
;**									**
;** pdclkset  echo= host.on.this.net  ip= 111.22.33.4  ns= 111.22.33.5	**
;**									**
;** pdclkset  udpecho= ping.lu.se		      (UDP echo client) **
;**									**
;** pdclkset  flags= 1			     (ping and UDP echo server) **
;**									**
;** pdclkset  flags= 1	ip= 2.3.4.5  g= 2.3.4.1  m= 255.255.255.0	**
;**									**
;*************************************************************************
;**		USING PDTBUILD TO GENERATE TABLES WITH ALL IP HOSTS	**
;*************************************************************************
;**									**
;** The PDTBUILD program, which is included in the ZIP package, looks	**
;** at all ARP broadcasts and generates a table with all the IP hosts	**
;** on this (sub)net. Each entry has IP number, Ethernet address and	**
;** host name, the latter which it asks a name server for. Two files	**
;** are generated, IPTBL.TXT and HWTBL.TXT, which are suitable as input **
;** to LANwatch or a LANalyzer or other monitors. It should preferably	**
;** be run for a complete day or longer. When started, if IPTBL.TXT	**
;** exists it will read it in and update with what it sees on the net.	**
;** It can handle up to 4094 hosts. Use BIGSORT for sorting (available	**
;** from oak.oakland.edu:pub/msdos/textutl)				**
;**									**
;** In the comment field, an A means authorative answer, N is non-	**
;** authorative answer from nameserver. 0 means host not registered	**
;** for reverse lookup (in-addr.arpa domain). - means name not found.	**
;** < and = denotes Ethernet duplicates for same IP address. >, = and + **
;** denotes IP duplicates for same Ethernetaddress (+ is used for a	**
;** gateway pdclkset know of). The last number on each line is how many **
;** ARP broadcasts we have seen from this address (so BIGSORT /R /+71	**
;** will sort the most used hosts first).				**
;**									**
;** You can speed up address collection by adding flag=8. This will	**
;** start ARP probing, a process that cycles through all IP addresses in**
;** the (sub)net and sends an ARP request for each address. The speed	**
;** is 9 ARP requests per second, slowing down to two per second when	**
;** nameserver requests are needed. It is rather successful in ignoring **
;** ARP replies from proxy ARP gateways (otherwise it would table a lot **
;** of fake hosts). Be careful with ARP probing, some programs (eg KA9Q	**
;** NET) may be hard to start when sprayed with ARP broadcasts.		**
;**									**
;** You can run echo (ping) in parallell with tablebuilding (and the	**
;** ARP probing), although the screen display is somewhat garbled. If	**
;** you don't ping, the display will show the accumulated number of ARP	**
;** broadcasts and the time of day; also the current ARP probe IP addr.	**
;**									**
;** If you don't run a BOOTP server, the i= and n= arguments are needed **
;** and also m= and g= if the nameserver is behind a router.		**
;**									**
;** The tblbuild code is a quick hack, undocumented, but works for me.	**
;** Pdtbuild includes all the functionality of pdclkset.		**
;**									**
;** Syntax:								**
;**									**
;** pdtbuild f[lags]=flagnr						**
;**									**
;**	     [i[pnr]=n.n.n.n]  [n[ameservers]=n.n.n.n[,n.n.n.n[,...]]]	**
;**									**
;**	     [m[ask]=n.n.n.n  g[ateways]=n.n.n.n[,n.n.n.n[,...]]]	**
;**									**
;**	     [p[ktintno]=hexnr]	 [l[ongertimeout]=time]			**
;**									**
;** Valid flags for table building mode:				**
;**	2 = Enable table building (required for this mode)		**
;**	4 = Use LANwatch table syntax instead of LANalyzer syntax	**
;**	8 = Use IP nr probing						**
;**    16 = Not enough IBM compatible PC, use DOS interrupts		**
;**   128 = half quiet (skip the End of pdclkset line)			**
;**   256 = Write fixed length IP numbers (good for sorting)		**
;**									**
;**									**
;** Examples:								**
;**									**
;** pdtbuild flags= 2  i=2.3.4.5  n=2.3.4.6   (LANalyzer table builder) **
;**									**
;** pdtbuild flags= 2  i=2.3.4.5  n=1.2.3.4  g=2.3.4.1	m=255.255.255.0 **
;**									**
;** pdtbuild flags= 2+4+256   (LANwatch table builder, sort compatible) **
;**									**
;** pdtbuild flags= 2+8 		  (table building with probing) **
;**									**
;*************************************************************************
;**		HISTORY 						**
;*************************************************************************
;**									**
;** Ver 0.85: Beta release.						**
;**									**
;** Ver 1.02: First official release.					**
;**	      Removed 386-only instructions. Numerous minor changes.	**
;**	      Corrected the Pacific daylight algorithm. 		**
;**									**
;** Ver 1.10: Selected release with support for one gateway.		**
;**									**
;** Ver 1.27: Major rewrite of the UDP/IP library to make it mostly RFC **
;**	      compliant. Multi gateway and multi timeserver support.	**
;**	      Fixed hangs on argument syntax errors.			**
;**	      Added comments and documentation to the code.		**
;**	      Added ping server and client function.			**
;**									**
;** Ver 1.28: Added fragment reassembly.				**
;**	      Added PDTBUILD application to automatically generate	**
;**	      hardware and IP tables by watching network traffic.	**
;**									**
;** Ver 1.29: Added SQID (Source Quench Introduced Delay)		**
;**	      All time compares changed to js/jns instead of jl/jge,	**
;**	      avoiding wrong handling once every hour.			**
;**									**
;** Ver 1.30: Added timezone environment variable handling (SET TZ=...).**
;**	      Timeserver not needed to ping or build tables.		**
;**									**
;** Ver 1.31: Ping delays now millisecond accurate.			**
;**									**
;** Ver 1.32: Corrected check on illegal ping packet size.		**
;**	      Ping display cleaned up and overhead reduced.		**
;**	      Corrected BufAlloc error when out of buffers.		**
;**									**
;** Ver 1.33: Fixed PDTBUILD error when not tablebuilding. Ping 	**
;**	      enhancements: Time server not needed, added elapsed ping	**
;**	      time field, send error messages displayed.		**
;**									**
;** Ver 1.34: Made a table for arg decode. Negative ping size will now	**
;**	      sweep from 28 up to abs(size). Also odd sizes work.	**
;**	      Added code in AdjTo16bits to avoid divide overflow.	**
;**									**
;** Ver 1.35: Made performance improvements. A 386SX with 16-bit WD	**
;**	      card can now handle 2000 pkts/s short packets (send +	**
;**	      receive) or load to 7 Mb/s (long packets). Echo interval	**
;**	      is now in units of milliseconds (actually 0.858 ms)	**
;**	      instead of 55 ms ticks. Added traffic load field in the	**
;**	      display. Added several debug checks.			**
;**									**
;** Ver 1.36: Made documentation changes for the above new features.	**
;**									**
;** Ver 1.37: Added domain name resolver for ping. Corrected a bug in	**
;**	      fragment reassembly. Changed length input to SendUdpPkt.	**
;**	      Found bug preventing inactivity timeout for remote hosts. **
;**									**
;** Ver 1.38: TblBuild redesigned to be able to detect both IP and	**
;**	      hardware address duplicates. Corrected a bug when out of	**
;**	      buffers trying to send unreachables.			**
;**									**
;** Ver 1.39: TblBuild enhanced with an active probe function to speed	**
;**	      up address collection.					**
;**									**
;** Ver 1.40: udpecho= will send udp echo instead of icmp echo packets. **
;**	      Flag=1 will continue sending despite of send errors.	**
;**	      Fixed bug limiting pdtbuild to 2047 hosts, now 4094.	**
;**	      Added test on no nameserver when nameservers needed.	**
;**	      Fixed sometimes inaccurate "active this run" in pdtbuild. **
;**									**
;** Ver 1.41: Added LongerTimeout= argument to run on slow links.	**
;**									**
;** Ver 1.42: Fixed IS_386 wrongly set for 8088/8086 (bug introduced in **
;**	      ver 1.35 caused hangs or bad checksum on PC XTs). 	**
;**									**
;** Ver 1.43: Try to handle the case with high speed CPUs overflowing	**
;**	      some network cards or packet drivers.			**
;**									**
;** Ver 1.44: Show in front of diff the packets dropped due to no bufs. **
;**	      Server mode now displays packets and load statistics.	**
;**	      With flag=32 the interval is in units of 0.1 ms.		**
;**	      With flag=64 udp= will send discard packets.		**
;**									**
;** Ver 1.45: Fixed display of junk characters if the time server IP	**
;**	      had all 12 digits in the "Clock set to ..." message.	**
;**									**
;** Ver 1.46: Added Flag=128 to suppress "End of pdclkset" message.	**
;**									**
;** Ver 1.50: Enhanced Flag= documentation. Flag=256 zero fills IP	**
;**	      numbers to fixed length suitable for sorting. Nicer	**
;**	      display when tablebuilding. The tables now shows the	**
;**	      number of ARP requests from each host so you can sort on	**
;**	      the most important hosts. Subdirectory for source code.	**
;**									**
;** Ver 1.51: Increased stacksize to fix some pdtbuild hangs, also	**
;**	      always check stack overflow. Make ";" equivalent to ","	**
;**	      (useful for BAT-file arguments, ":" is equiv to "=").	** 
;**	      Flag=512 will cause sends during packet driver upcalls	**
;**	      in server mode (to see if the driver can handle it).	**
;**									**
;** Ver 1.52: Count the number of out of sequence, repeated or lost	**
;**	      packets. Flag=1024: stop sending after above errors.	**
;**	      Change size default to -50, giving a 34-50 size sweep.	**
;**									**
;** Ver 1.53: Fixed so that undefined send errors dont print garbage.	**
;**									**
;** Ver 2.00: Increased number of full size buffers from 27 do 300+ by	**
;**	      converting all the code to use far addresses for buffers.	**
;**	      The above change needed for ping servers on a VERY loaded	**
;**	      network, where I've now seen up to 160 buffers in the	**
;**	      send queue waiting for collisions to finnish. Packet loss	**
;**	      computed differently during pinging to give a more stable	**
;**	      value at long delays. Ping throughput up by 10 - 20 % by	**
;**	      removing instructions and change register usage and	**
;**	      enhance the checksum routine. Lots of small changes. The	**
;**	      code change may have introduced bugs. There is definitely	**
;**	      one in tablebuilding. Flag=4096 enables IP sizes up to	**
;**	      4082 (for Token Ring). Fixed a bug that gave a not	**
;**	      completely correct port or protocol unreachable packet.	**
;**	      Added a min-size parameter for size sweeping.		**
;**	      Added a lot of useful debug code.				**
;**									**
;** ver 2.01: Found the tablebuilding bug. The source code restructured	**
;**	      to appear in a more logical order. DOS interrupt bottle-	**
;**	      necks replaced, giving a 40 % throughput increase! The	**
;**	      code is now 100% MAC hardware address length independent.	**
;**	      Interval may now have a decimal point and digit. Added	**
;**	      special handling for true SLIP and Token Ring (untested,	**
;**	      no source routing). Moved the EchoDisplay calls to	**
;**	      Somethig2Do, giving a more stable and accurate load	**
;**	      figure. Source quench code now use millisecond instead of	**
;**	      tick resolution, giving a more even load.			**
;**									**
;** ver 2.02: Made documentation changes for the above 2.x features.	**
;**									**
;** ver 2.03: Fixed server mode bug causing divide overflow or hangs.	**
;**									**
;** ver 2.04: Changed default echo interval to equal display interval,	**
;**	      giving better display rythm. Echo interval algorithm	**
;**	      changed to be more accurate and CPU speed independent. 	**
;**	      Fixed tablebuild bug causing display not always updated.	**
;**									**
;** ver 2.05: Changed buffer allocation to leave room for COMMAND.COM	**
;**	      so you can recall the previous command with the F3 key.	**
;**									**
;** ver 2.06: Fixed a hang that could occur after a long while running	**
;**	      ping client or server.					**
;**									**
;** ver 2.07: Ping display line was not advanced after other print.	**
;**									**
;*************************************************************************
;**		ACKNOWLEDGMENTS 					**
;*************************************************************************
;**									**
;** The checksum routine used is a modified NCSA Telnet version.	**
;** The dst algorithm was modelled after PCIP SETCLOCK (thanks Drew!),	**
;** but enhanced to use parameters from a table.			**
;** The dst algorithm table was derived from a comp.sources.unix 1989	**
;** posting by ado@ncifcrf.gov of localtime.c and related routines	**
;** and tables, and a later update (very useful data, thanks!). 	**
;** The master environment is found using Pat's code.			**
;** The millisecond timer is based on code from Dean Pentcheff. 	**
;** The DateTimeCalc routine is my own invention.			**
;** The packet driver interface routines were copied from the Crynwr	**
;** packet driver distribution, without which this project would not	**
;** have been possible (thanks Russ!).					**
;**									**
;** The small UDP/IP library was written by me, and can probably be	**
;** used in other small assembler applications. It is now fully RFC	**
;** compliant, except for a few small cases mentioned in the code. It	**
;** DOES handle IP type of service, fragment reassembly, source quench	**
;** throttling, sending port and protocol unreachables, multiple	**
;** default gateways, etc.						**
;**									**
;*************************************************************************
;**		WHERE TO GET IT FROM					**
;*************************************************************************
;**									**
;** Current version of PDCLKSET can be obtained by anonymous FTP from	**
;** ftp.lu.se:/pub/network/pdclkset/pdclkxxx.zip or from		**
;** msdos.ftp.sunet.se:pub/network/pdclkset/pdclkxxx.zip or from Novell **
;** server LUSTORFS/ARC:PUB\NETWORK\PDCLKSET\PDCLKxxx.ZIP		**
;** (Netware access only in Lund and around).				**
;** Major releases will also be available on the Simtel20 archive and	**
;** its mirror sites (like oak.oakland.edu, wuarchive.wustl.edu and	**
;** ftp.funet.fi) in the msdos.pktdrvr directory.			**
;**									**
;*									 *
;* Jan Engvald, Lund University Computing Center			 *
;* ____________________________________________________________________  *
;*   Address: Box 783		    E-mail: Jan.Engvald@ldc.lu.se	 *
;*	      S-220 07 LUND    Earn/Bitnet: xjeldc@seldc52		 *
;*	      SWEDEN	      (Span/Hepnet: Sweden::Gemini::xjeldc)	 *
;*    Office: Soelvegatan 18	    VAXPSI: psi%2403732202020::xjeldc	 *
;* Telephone: +46 46 107458	    (X.400: C=se; A=""; P=Sunet; O=lu;	 *
;*   Telefax: +46 46 138225		    OU=ldc; S=Engvald; G=Jan)	 *
;*     Telex: 33533 LUNIVER S						 *
;*									 *
;*************************************************************************

; Note: If you want to assemble this code yourself, you need Turbo ASM 
; (at least MASM 5.1 does not like comments on structure calls!).
; Also, some files from the Crynwr packet driver collection are needed.

;************************************************************************
;*		Compile time constants					*
;************************************************************************

		.lfcond  
PRGVERSION	equ	' v2.07'
TBLBUILD 	equ 	0
PINGCLIENT 	equ 	1
; DEBUG values above 5 degrade throughput a lot.
DEBUG 		equ 	0

MN		equ	60			; seconds in a minute
HR		equ	60*MN			; seconds in an hour

SUN		equ	0			; Sunday
SAT		equ	6			; Saturday
DAT		equ	0ffh			; Specific date follows

FEB2W		equ	31+2*7				; Feb 2nd week
MAR1W		equ	31+28+1*7			; Mar 1st week
MAR2W		equ	31+28+2*7			; Mar 2nd week
MAR3W		equ	31+28+3*7			; Mar 2rd week
MARLW		equ	31+28+31			; Mar last week
APR01		equ	31+28+31+1			; Apr 1
APR03		equ	31+28+31+3			; Apr 3
APR07		equ	31+28+31+7			; Apr 7
APR1W		equ	31+28+31+1*7			; Apr 1st week
APR2W		equ	31+28+31+2*7			; Apr 2nd week
APR14		equ	31+28+31+14			; Apr 14
APR18		equ	31+28+31+18			; Apr 18
APRNL		equ	31+28+31+30-7			; Apr next last week
APR23		equ	31+28+31+23			; Apr 23
APR26		equ	31+28+31+26			; Apr 26
MAY01		equ	31+28+31+30+1			; May 1
MAY2W		equ	31+28+31+30+2*7 		; May 2nd week
AUG28		equ	31+28+31+30+31+30+31+28 	; Aug 28
SEP01		equ	31+28+31+30+31+30+31+31+1	; Sep 1
SEP08		equ	31+28+31+30+31+30+31+31+8	; Sep 8
SEP12		equ	31+28+31+30+31+30+31+31+12	; Sep 12
SEP2W		equ	31+28+31+30+31+30+31+31+2*7	; Sep 2nd week
SEP17		equ	31+28+31+30+31+30+31+31+17	; Sep 17
SEP20		equ	31+28+31+30+31+30+31+31+20	; Sep 20
SEP3W		equ	31+28+31+30+31+30+31+31+3*7	; Sep 3rd week
SEP30		equ	31+28+31+30+31+30+31+31+30	; Sep 30
SEPLW		equ	31+28+31+30+31+30+31+31+30	; Sep last week
OCT01		equ	31+28+31+30+31+30+31+31+30+1	; Oct 1
OCT2W		equ	31+28+31+30+31+30+31+31+30+2*7	; Oct 2nd week
OCT24		equ	31+28+31+30+31+30+31+31+30+24	; Oct 18 - 24
OCT4W		equ	31+28+31+30+31+30+31+31+30+4*7	; Oct 4th week
OCT29		equ	31+28+31+30+31+30+31+31+30+29	; Oct 23 - 29
OCTLW		equ	31+28+31+30+31+30+31+31+30+31		; Oct last week
NOV13		equ	31+28+31+30+31+30+31+31+30+31+13	; Nov 5 - 13

AlgE		struc
AlgName 	db	"EUR "			;; Name of dst algorithm
AlgFromTime	dw	2*HR			;; local standard time dst start
AlgFromWeekDay	dw	SUN			;; weekday dst start
AlgFromWeek	dw	MARLW			;; last day-of-year dst start
AlgUntilTime	dw	2*HR			;; local standard time dst end
AlgUntilWeekDay dw	SUN			;; weekday dst end
AlgUntilWeek	dw	SEPLW			;; last day-of-year dst end
AlgAddAmount	dw	1*HR			;; dst advance amount
AlgEntryLen	equ	$-AlgName
AlgE		ends

AlgData 	struc
AUSA AlgE <"USA ", 2*HR,SUN,APR1W, 1*HR,SUN,OCTLW, HR>  ;; USA Canada Mexico
ACub AlgE <"CUB ", 0*HR,SUN,MAY2W,-1*HR,SUN,OCT2W, HR>  ;; Cuba
AChl AlgE <"CHIL", 0*HR,SUN,OCT2W,-1*HR,SUN,MAR2W, HR>  ;; Chile
ABrz AlgE <"BRZ ", 2*HR,SAT,OCT4W, 1*HR,SAT,FEB2W, HR>  ;; Brazil
AGBR AlgE <"GBR ", 1*HR,SUN,MARLW, 1*HR,SUN,OCT29, HR>  ;; United Kingdom
AWEu AlgE <"W_EU", 1*HR,SUN,MARLW, 1*HR,SUN,SEPLW, HR>  ;; West Europe
AMEu AlgE <"M_EU", 2*HR,SUN,MARLW, 2*HR,SUN,SEPLW, HR>  ;; Central Europe + SU
AEEu AlgE <"E_EU", 3*HR,SUN,MARLW, 3*HR,SUN,SEPLW, HR>  ;; East Europe
ALby AlgE <"LIBY", 2*HR,DAT,APR01, 1*HR,DAT,SEP30, HR>  ;; Libya
AEgy AlgE <"EGY ", 2*HR,DAT,MAY01, 1*HR,DAT,OCT01, HR>  ;; Egypt
ATur AlgE <"TURK", 1*HR,SUN,MARLW, 0*HR,SUN,SEPLW, HR>  ;; Turkey
AIra AlgE <"IRAN", 2*HR,SUN,MARLW, 1*HR,SUN,SEP3W, HR>  ;; Iran
APRC AlgE <"PRC ", 2*HR,SUN,APR2W, 2*HR,SUN,SEP2W, HR>  ;; People Rep of China
AROK AlgE <"ROK ", 2*HR,SUN,MAY2W, 2*HR,SUN,OCT2W, HR>  ;; Rep of Korea
AAus AlgE <"AUS ", 2*HR,SUN,OCTLW, 2*HR,SUN,MAR3W, HR>  ;; South Australia
ATas AlgE <"TASM", 2*HR,SUN,OCT24, 2*HR,SUN,MAR3W, HR>  ;; Tasmania
ANSW AlgE <"NSW ", 2*HR,SUN,OCTLW, 2*HR,SUN,MAR1W, HR>  ;; New South Wales
ALHI AlgE <"LHI ", 2*HR,SUN,OCTLW, 2*HR,SUN,MAR1W, 30*MN> ;; LHI (Australia) 
ANZe AlgE <"NZE ", 2*HR,SUN,OCTLW, 2*HR,SUN,MAR1W, HR>  ;; New Zealand

; All entries below this line are indexed by year modulo 4

APa0 AlgE <"PAC ", 2*HR,SUN,APR1W, 1*HR,SUN,NOV13, HR>  ;; Pacific presidential
APa1 AlgE <"PAC ", 2*HR,SUN,APR1W, 1*HR,SUN,OCTLW, HR>  ;; Pacific non-pres
APa2 AlgE <"PAC ", 2*HR,SUN,APR1W, 1*HR,SUN,OCTLW, HR>  ;; Pacific non-pres
APa3 AlgE <"PAC ", 2*HR,SUN,APR1W, 1*HR,SUN,OCTLW, HR>  ;; Pacific non-pres

; All entries above this line are cyclic and will last forever
; All entries below this line are non-cyclic, they only last 4 years

AIs0 AlgE <"ISR ", 0*HR,DAT,APR14,-1*HR,DAT,SEP08, HR>  ;; Israel 1996
AIs1 AlgE <"ISR ", 0*HR,DAT,APR18,-1*HR,DAT,SEP12, HR>  ;; Israel 1993
AIs2 AlgE <"ISR ", 0*HR,DAT,APR03,-1*HR,DAT,AUG28, HR>  ;; Israel 1994
AIs3 AlgE <"ISR ", 0*HR,DAT,APR23,-1*HR,DAT,SEP17, HR>  ;; Israel 1995

if 0    ; as years go by, replace entries above from below with same label
AIs1 AlgE <"ISR ", 0*HR,DAT,MAY04,-1*HR,DAT,SEP28, HR>  ;; Israel 1997
AIs2 AlgE <"ISR ", 0*HR,DAT,APR19,-1*HR,DAT,SEP13, HR>  ;; Israel 1998
AIs3 AlgE <"ISR ", 0*HR,DAT,APR11,-1*HR,DAT,SEP05, HR>  ;; Israel 1999
AIs0 AlgE <"ISR ", 0*HR,DAT,APR30,-1*HR,DAT,SEP24, HR>  ;; Israel 2000
AIs1 AlgE <"ISR ", 0*HR,DAT,APR15,-1*HR,DAT,SEP09, HR>  ;; Israel 2001
AIs2 AlgE <"ISR ", 0*HR,DAT,APR07,-1*HR,DAT,SEP01, HR>  ;; Israel 2002
AIs3 AlgE <"ISR ", 0*HR,DAT,APR27,-1*HR,DAT,SEP21, HR>  ;; Israel 2003
AIs0 AlgE <"ISR ", 0*HR,DAT,APR18,-1*HR,DAT,SEP12, HR>  ;; Israel 2004
AIs1 AlgE <"ISR ", 0*HR,DAT,MAY01,-1*HR,DAT,SEP25, HR>  ;; Israel 2005
AIs2 AlgE <"ISR ", 0*HR,DAT,APR23,-1*HR,DAT,SEP17, HR>  ;; Israel 2006
AIs3 AlgE <"ISR ", 0*HR,DAT,APR15,-1*HR,DAT,SEP09, HR>  ;; Israel 2007
AIs0 AlgE <"ISR ", 0*HR,DAT,APR27,-1*HR,DAT,SEP21, HR>  ;; Israel 2008
AIs1 AlgE <"ISR ", 0*HR,DAT,APR19,-1*HR,DAT,SEP13, HR>  ;; Israel 2009
endif
AlgData         ends

WARNYEAR        equ     1997                    ; acyclic data invalid year

;************************************************************************