QCOM.EXE   
       Revision 2.97
       February 1993
   
   
       ------------------------------------------   
   
   
   
       Copyright 1990-1993 by RTFM Software and Richard W. Turenne
       Winnipeg, Mb.  All Rights Reserved   
   
   
   
       All users are granted a limited license to try QCom for a reasonable  
       evaluation period to determine its' suitability.   
   
   
       QCom is USER SUPPORTED.  It is not Public Domain and is not free.   
       This means, if you decide to use this program, please show your   
       support by registering it with the author.   
   
   
       To add INCENTIVE, those who register will be shown how to utilize   
       the user defineable functions.  Users can pre-define other   
       external dos functions, or other external protocols, or batch files,  
       and access them with a single keystroke.  Additionally, they will be  
       able to eliminate the "nag" screen when ending QCom.   
   
   
   
   
   
       ------------------------------------------------------------------   
   
   
   
   
   
   
   
   
   
   
   
                                  -Page 1-
   
   
  SYSTEM REQUIREMENTS:   
   
     Minimum of one floppy drive, 256K or more memory, and a modem of   
     course.   
   
   
  INTRODUCTION to QCom:   
   
     QCOM is a compact communications program that attempts to pack in   
     maximum of function, form and ease of use into a small package.  It   
     was decided to primarily use external protocols for files transfers   
     because there are many available from which to choose.  And as the   
     technology of protocols progresses, it's a simple matter to keep your   
     communication software operating at the current state of the art.   
   
     Note: All references to DSZ also apply to GSZ by Omen Technology.   
   
     QCOM is tailored to use the shareware program DSZ by Omen Technology   
     to handle most file transfers.  When a file is to be transferred,   
     QCOM passes the proper commandline to DSZ which then handles all the   
     work of transferring and error checking.  It provides commonly used   
     Xmodem, Ymodem and Zmodem transfer methods.   
     (QCom can also be set up to use any other external protocol. See the   
     section on OTHER EXTERNAL PROTOCOLS.)   
   
     When the file transfer is finished, QCOM resumes control.   
     NOTE:   
     DSZ.COM  must be present in the default directory or in the DOS   
     path if you wish to transfer files.  DSZ or GSZ  may be obtained from   
     many local online sources.   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                  -Page 2-
   
  FIRST TIME SETUP AND CONFIGURATION:   
   
    Run the QCom Setup utility called QS.EXE.  Enter Com Port, screen   
    colors and select your modem from the list.  Pressing ENTER will   
    update the QCom configuration file.  Follow any instructions   
    relating to modem switches or jumpers.   
   
    Run QCOM.  Wait a few moments while the modem is being initialized.   
    An error message usually means the modem has not been properly   
    initialized.  Correct modem initialization is critical to all   
    operations that involve the modem.  If the string from QCom Setup   
    is incorrect, please advise the author so that corrections can be   
    made.   
    In the mean time, you may need to refer to your modem instruction   
    manual if you still have problems.  One way to check initialization   
    is to press ALT-M when at the terminal screen to reinitialize the   
    modem. If you get "ERROR" back from the modem then there is something in 
    the string that it doesn't understand. Refer to your modem manual to   
    remove any incorrect modem commands from the string.  Pressing ALT-O   
    when in QCom allows you to edit the modem string contained in the   
    configuration file.  Also see the Trouble Shooting section that   
    follows later.   
   
    All configuration data is stored in the text file called QCOM.CFG.   
    If you wish, you can edit the file with any ascii editor as long as a   
    few rules are adhered to:   
   
    a)The sequence and number of items in the file must not be altered.   
   
    b)Each line should be no longer than 80 characters.  Longer lines   
      are truncated to 80 characters.   
   
    c)Comments, if used, must be kept behind semicolons.   
   
    d)The editor must not insert any hidden formatting or control   
      characters into the text.  If in doubt about your editor, edit it   
      within QCom using ALT-O.   
   
    NOTE:   
    The "|" character will send a carriage return to the modem.  The   
    "~" is a half-second pause to allow the modem time to execute the   
    commands in the initialization string.  Some modems need more time   
    than others.  The pause is executed by QCom and the modem will not   
    actually receive the "~" character.   
    Function key definitions are shown in the last ten lines.  You can   
    configure your own "macros" here.  Control codes can be sent with   
    the use of the "^" character.   
    Example:           ^[ = an escape character   
                       ^M = a carriage return   
    Refer to any good ASCII chart for others.   
                                  -Page 3-
   
  COMMANDLINE PARAMETERS:   
   
    In addition to specifying a script,  the user can specify an   
    alternate configuration file and an alternate phone directory file.   
    This allows network users to have CFG and FON files tailored to   
    their individual needs.   
   
    Switches are:   
           /S = load and execute script file   
           /C = load alternate configuration file   
           /P = load alternate phone directory   
           /B = force monochrome  
    Usage is: QCOM [/Sfilename.SCR] [/Cfilename.CFG] [/Pfilename.FON] [/B]  
   
    Users may use the options in any sequence.  The switches (/S,/C,/P)   
    must NOT have a space preceding the filename.  When the commandline   
    options are not used, QCom defaults to QCom.CFG and QCom.FON.   
   
  TERMINAL EMULATION:   
   
    This version has built-in support for ANSI-BBS and straight TTY.   
    Pressing ALT-K will toggle between the two.   
   
  STATUS LINE EXPLANATION:   
   
    ----------------------------------------------------------------------   
    Alt-Z:Help SEC  Host system name     Online 05:55:55 Z COM1:2400N8   
    ----------------------------------------------------------------------   
        |       ||||         |                |       |     |       |   
        |       ||||         |                |       |     |       |   
    Commands    ||||         |                |       |     |       |   
    Script on -- |||         |                |       |     |       |   
    Echo On ----- ||         |                |       |     |       |   
    Capture On --- |         |                |       |     |       |   
    Alarm Off -----          |                |       |     |       |   
    Host name ---------------                 |       |     |       |   
    Carrier status ---------------------------        |     |       |   
    Time connected -----------------------------------      |       |   
    Transfer protocol --------------------------------------        |   
    Communication port, baud, parity and databits ------------------   
   
   
   
   
   
   
   
   
   
   
   
                                  -Page 4-
   
  FILE TRANSFER PROTOCOLS:   
   
    Transfer protocols are what DSZ uses as a method of flow-control and   
    error-checking when transferring files.  These protocols are   
    specified when adding to the Dialing Directory.  The Dialing   
    Directory is displayed when you press ALT-D.   
    The use of ZModem protocol is recommended if the host computer has   
    the option available.  QCom defaults to ZModem with crash recovery   
    and Moby Turbo enabled (z-rm).  This can be changed by bringing up   
    the configuration screen with ALT-O and editing the default ZModem   
    line.   
    When selecting XModem protocol, QCom defaults to using the built-in   
    XModem instead of DSZ's. This can be changed by editing the   
    appropriate line in QCom.CFG (press ALT-O in QCOM).   
   
    If it becomes necessary to change your transfer protocol while on-   
    line, you can do so by pressing ALT-T.  A box will pop up to allow   
    you to make the change.  The current protocol is displayed in the   
    right-hand box on the status line (see STATUS LINE EXPLANATION   
    below).  It is VERY important that the protocols at the receiving and   
    transmitting ends are the same, otherwise DSZ will give a "Time Out"   
    error message and abort without transferring anything.   
   
    Finding the required information on setting protocols in the DSZ   
    documentation can be challenging.  QCom gives the user a menu to   
    simplify selection and will send the command string that DSZ looks   
    for.  The following show the protocol commands QCom sends to DSZ.   
   
    Protocol:        DSZ Command string:   
    ZModem            "z -rm" (Can be changed in QCom.CFG)   
    YModem Batch      "b -cy"   
    YModem-G          "b -cgy"   
    XModem-CRC        "x -cy"   
    XModem-1K         "x -cky"   
    XModem-1K-G       "x -cgy"   
   
    The command that QCom gives to DSZ is the port and CONNECT baud rate   
    currently in use,  followed by an "s" or an "r" (depending on whether   
    the file is being sent or received) and the protocol string as in the   
    above  examples.   
    TIP: Other options can be added by using SET DSZOPT=options in the   
    autoexec.bat file.  See the DSZ docs for options.   
   
    The download path is added to the end of the  commandline when   
    downloading.  An unregistered copy of DSZ will ignore download paths.   
    The upload path precedes the filename specified by the user when the   
    upload command is issued.   
   
    TIP:  If you upload files from different sub directories, keep the   
    default upload path blank in the QCom.CFG file.  When prompted for   
    the file to upload, enter the path and filename together   
    (Eg. C:\QCOM\QCOM.ZIP").   
                                  -Page 5-
   
  FILE TRANSFER PROTOCOLS CONTINUED...   
   
    Another tip:  Put the line "SET DSZLOG =C:\QCOM\QCOM.LOG" in your   
    Autoexec.bat file and DSZ will keep a log of your file transfers in   
    QCOM.LOG (This assumes that you have installed QCom on drive C: in a   
    subdirectory \QCOM.  You may change the path and log filename as you   
    wish.).   
    File transfers may be aborted with ESC followed by several CTRL-   
    BREAK's.   
   
  OTHER EXTERNAL PROTOCOLS:   
   
    QCom can be set up to use most external protocols.  Non-registered   
    uses can jump to Dos (ALT-J) and manually execute the external prot-   
    ocol.  Registered users will be shown how to pass parameters to the   
    external protocols and execute them with a single keystroke.   
    Note: An unregistered copy of QCom is not "crippled".  The instruct-   
    ions for using this feature of QCom are provided to all those who   
    register.   
   
  SCREEN COLORS:   
   
    Screen colors can be changed by modifying values given in the   
    configuration file QCom.CFG.  The easiest way is to use QS.EXE, the   
    QCom Setup program.   
   
  VARIOUS FUNCTIONS:   
   
    ALT-A:   
         Toggles the sound functions on or off.   
    ALT-B:   
         Allows the user to scroll back up to 500 lines of received data.   
         Search capabilities are provided for finding particular text and   
         the whole buffer can be written to disk using the Save command,   
         "S" (the filename defaults to "QComBuff.Txt") or erase the buffer   
         with "E". "Q" is for quoting previously received text. When "Q" is  
         pressed another menu of choices is presented and one line of text   
         will be highlighted. This highlighted line can be moved through   
         the buffer with the cursor keys, Home, End, PgUp, or PgDn.  Lines   
         can be tagged or untagged by pressing "T" or the SPACE bar.  Once   
         text is selected, it can be save to disk with "F" or immediately   
         sent to the host with "S".  This last feature allows you to quote   
         lines from a message and return them to the host's editor when   
         answering that message online.  "U" will untag all tagged lines   
         as will sending or filing.   
    ALT-C:   
         Communication parameters can be modified here.  These changes   
         are in effect until changed again or until QCom ends.   
         Com Port must be set in QCOm.CFG. Port changes will not take   
         effect unless QCom is restarted.   
   
   
                                  -Page 6-
   
  VARIOUS FUNCTION CONTINUED...   
   
    ALT-D:   
         Displays the dialing directory.  Use the arrow keys to select   
         a number and ENTER to dial that number.  Other keys that are   
         PGUP, PGDN, HOME and END.  HOT TIP: Pressing ALT and a letter   
         will put the cursor on the first line beginning with that   
         letter.   
         Add a new entry with "A" or edit an existing one with "E".  To   
         delete an entry press "D".  You can dial the phone with a   
         manually entered number using "M".   
         Phone entries can be tagged or untagged with the Space bar.   
         This will cause QCom to continuously dial all tagged numbers   
         until a connection is made.  Dialing of tagged numbers will   
         commence when the Enter key is pressed.  Once a connection is   
         made and broken you will be returned to the Dialing Directory.   
         Continuous dialing will resume where it left off if Enter is   
         pressed again.   
    ALT-E:   
         Toggles local echo on or off.  This is used when the host does   
         not echo back the characters that you enter.  An "E" is   
         displayed in the left-hand box on the status line when local   
         echo is on.   
    ALT-F:  
         Toggles adding linefeeds to incoming and outgoing lines.  
    ALT-G:   
         Toggles output to printer on and off.  Allows all incoming text to  
         be sent to the printer.  Make sure the printer is online.   
    ALT-H:   
         Sends the hang-up string to the modem and toggles DTR.   
    ALT-I:   
         Will save the current screen image to a text file as specified   
         in the QCom.CFG file.  Default filename is QCOM.SCN which can   
         be changed by editing the QCom.CFG file (use ALT-O).   
    ALT-J:   
         Allows shelling out to DOS without ending QCOM.  External   
         programs can be executed while on-line.  The user could make   
         use of other external file transfer protocols here if desired.   
         Though there is a better way.  See registration section.   
    ALT-K:   
         Toggles between ANSI and TTY terminal emulation.   
    ALT-L:   
         Toggles the "capture" function.  If on, all incoming text will   
         be saved in a file named as specified in the QCom.CFG file.   
         Default is QCOM.CAP.  IF the file  does not exist in the   
         default directory, it will be created.  Otherwise data is   
         appended to an existing capture file.  A "C" is displayed in   
         the left-hand box on the status line when capture is on.   
    ALT-M:   
         Sends the modem initialization string to the modem.  This   
         string is automatically sent upon start-up (providing no   
         carrier is present).   
                                  -Page 7-
   
 VARIOUS FUNCTIONS Continued...   
   
    ALT-N:   
         Split-screen separates incoming and outgoing keystrokes   
         during a "chat" session.   
    ALT-O:   
         Brings up the QCOM.CFG file to the screen for editing.   
         Press F10 to save the file and to set the Communication   
         parameters as shown in the file.  Esc exits and makes no   
         changes.   
         If it were necessary to change baud or any other Communication   
         parameter while online, use ALT-O to edit and F10 to set   
         parameters.  Changing the port specified here will have no   
         effect unless QCom is  restarted.   
    ALT-P:   
         Sends the current password from an entry of the Dialing   
         directory when you have dialed and connected to that entry.   
    ALT-Q:   
         Load and execute a script.   
    ALT-R:   
         Re-dials the last phone number dialed when no entries are   
         "Tagged", or if entries are "Tagged", it will continue dialing   
         those.   
    ALT-S:   
         Toggles the Script Save function.  See the Script section for   
         more information on making and using scripts.   
    ALT-T:   
         Allows changing of the transfer protocol currently in effect.   
         This can be done while on-line.   
    ALT-V:   
         Allows the use of an external editor or file viewer.  The   
         editor (or file viewer) of choice is defined in the   
         configuration file.   
    ALT-U:   
         Will send a pure ascii text file to the host with no error-   
         checking.  Ascii transfer is used to send a text file to the   
         host PC.  For example, you might use it when sending a message   
         to an electronic mail service.  Instead of editing the message   
         on-line, you can prepare your message in advance.  Once on-   
         line, go into the message editing screen on the host and then   
         use ALT-U to upload your file.   
    ALT-W:   
         Wipes the screen clear.   
    ALT-X:   
         Ends QCOM.   
   
   
                                  -Page 8-
   
  VARIOUS FUNCTIONS Continued...   
   
    ALT-Y:   
        QCom becomes the host computer.  It will wait for any incoming   
        phone calls until ESC is pressed.  When a call is received, QCom   
        will answer the phone.  QCom sends the file HELLO.HOS 
         to the caller's PC.  You can edit this file to suit your own   
         needs using an ANSI "editor" like TheDraw.   
         After this message file is sent, the caller is shown the   
         menu contained in the file "MENU.HOS" 
    
         The caller can select one of the choices or the Host can enter   
         selections.   
         "Help"  sends a brief help screen, HELP.HOS to the user.   
         "Area"  allows the user to change to a different subdirectory.   
         When a caller selects the Area command, a file called AREAS.HOS   
         is displayed on the caller's screen.  This is intended to show   
         which "areas" (subdirectories in fact) the caller can have access    
         to. A sample AREAS.HOS file is included.  Users will want to edit  
         this file to suit their systems.  
         "Files" allows the user to list specified files in that   
         subdirctory.   
         "Chat"  will allow  a dialogue between each PC.  To end Chat   
         and return to the menu, the Host must press ESC.   
         "Upload"  will send a file to the Host using DSZ ZModem.   
         "Download" will send a file to the caller in a similar manner.   
         If the caller specifies the correct path and filename, he will   
         be able  to download a file from anywhere on the Host system.   
         "Proto" will allow the caller to select XModem, YModem or   
         ZModem protocols when transferring files.   
         "Goodbye" will send BYE.HOS and terminate the connection .   
         As Host, you can also terminate the call by pressing ALT-H to   
         hangup. QCom will then wait for the next caller.  ALT-X will   
         also terminate the call and in addition, end QCom.   
         A local Host mode test is available: Press ENTER when waiting   
         for incoming calls.  This allows preparation and preview  of   
         your own host welcome messages or help screens.   
   
     PGUP:   
         Uploads (sends) a file to the other system.  You will be   
         prompted to enter a filename to upload.  The file can be   
         preceded by a path only if NO upload path is specified in   
         QCOM.CFG.  If the host supports batch uploads then you can   
         take advantage of DSZ's capabilities; when prompted for a file   
         to upload enter the name of a file containing a list of the   
         files you wish to upload.  Precede the filename with an "@" .   
         Example: "@files.lst".  Or you can use QCom to create a list   
         file for you.  When prompted for a file to upload press ENTER   
         with any global file specification (*.* or *.zip). You will   


                                  -Page 9-  
  
 
  VARIOUS FUNCTIONS CONTINUED...    
         be shown a box containing filenames based on that specification.   
         From here simply use the cursor keys to select a files and Mark   
         them with "M".  When finished marking press ENTER and QCom will   
         create "Files.LST" and pass that to DSZ for you.   
   
     PGDN:   
         Downloads (receives) a file from the host computer.  If XModem   
         or YModem are the protocols in effect, you'll be prompted to   
         enter the filename to receive.  QCom tries to guess the   
         filename based on recently entered text and places its' guess   
         at the prompt.   
         If ZModem is in effect, entry of filenames is not required and   
         in fact, pressing PGDN is not required because QCom will call   
         DSZ automatically when it receives the Zmodem Receive string.   
     ALT-=:   
         Toggles "Doorway" mode.  This removes the status line when in   
         Doorway mode and gives full screen display for using remote   
         applications.   
         Allows you to make full use of all keys while online.  All   
         Alt-key combinations except ALT-= are sent out and their usual   
         functions are disabled in this mode.   For example, PgUp,   
         PgDn, Home, End and the cursor key codes are transmitted.  You   
         might make use of this when using a full-screen editor while   
         online or when using your PC as a dumb terminal on a non-DOS   
         system such as Unix.  Status line and all key functions are   
         restored when Doorway mode is turned off.   
     ALT-Minus:   
         Enables/disables debugging during script execution.  Status   
         line displays the next line of text which QCom is looking for.   
     Ctrl-END   
         Sends Break signal to host.  Used for terminating some mainframe   
         connections.   
     F1-F10:   
         Sends the text as listed in the last ten lines of QCom.CFG.   
         You can put your name, password, special key codes or whatever   
         you wish here. 80 characters max on each line.   
     Ctrl-F1   
         Displays the "Function Key Macros" as they appear in QCom.CFG.   
     Ctrl-F2   
         Displays the "Alt Key Macros" for registered users.   
   
   
   
   
   
   
   
   
   
                                  -Page 10-
   
   SCRIPTS:   
       Scripts are used for automating repetitive tasks such as dialing,   
       logging in to an online service, and transferring files or     
       electronic mail.  A script is generally made up of a series of    
       commands for QCom to execute at the appropriate time.  The script    
       can tell QCom to send text to the host or it can make QCom execute    
       one of its' internal functions.   
   
   MAKING A SCRIPT:   
      QCom has a built-in Script-save feature to simplify the creation of   
      scripts. To create a typical login script you would do the    
      following:   
      1.  From the Dialing Directory dial the number.   
      2.  When the host answers and immediately after the Dialing box   
          clears, press Alt-S to start the script saver.  It will prompt    
          you to enter the name of your script.  If, for example, you're    
          calling CompuServe, you could name it CIS.SCR.   
      3.  QCom will save each line of incoming text which prompts you for   
          input.  For example the host may prompt you...   
                   ENTER YOUR FULL NAME :   
          To which you respond by typing in your name and pressing ENTER   
          when the name is complete.  Always type entries in, don't use   
          Function key macros when saving a script. If/when prompted to   
          press "ANY" key always press ENTER.  QCom will store the host's   
          prompt, and the text you have entered in the script.   
          (Also Note: BBS software that has "HotKey" menu choices where    
          the user is not required to press ENTER after selecting a letter    
          is great BUT... when it comes to saving a script QCom will NOT    
          save the line unless you press ENTER.  So when saving a script    
          turn off the Hotkey feature at the BBS end.)   
      4.  QCom will also store any commands you give it such as ALT-L   
          to turn on the capture function.   
      5.  When you wish to stop saving a script press Alt-S again.   
      6.  To have this new script execute when you call this number again,   
          add the name of your script into that entry in the Dialing   
          Directory. The next time you dial that number the script will be   
          loaded and executed.   
   
      Sample script :   
      put a message on screen   
      ;ECHO ^M This is the start of my script! ^M   
   
      let's capture the session to file.txt   
      ;a-L file.txt   
   
      Do you want graphics (Enter)=no;^M   
      What is your full name?;John Doe^M   
   
      sends password from the Directory entry we just dialed   
      Password (Dots will echo)?;a-P   
      Scan Message Base Since 'Last Read' (Enter)=yes;^M   
      Press (Enter) to continue;^M   
                                  -Page 11-
   
   
   MAKING A SCRIPT Continued...   
   
      receiving (downloading) a file   
      min. left) Main Board Command?;d^M   
      Filename to Download (Enter)=none?;file.arc^M   
   
      downloads "file.arc"   
      ;D/L file.arc   
      Press (Enter) to continue;^M   
   
      goodbye   
      min. left) Main Board Command?;g^M   
   
      give hangup command   
      ;a-H Y   
   
      execute another script   
      ;a-Q MyBBS.SCR   
   
      The following is an example of a script that connects to   
      CompuServe through the DataPac network.   
   
      ;ECHO  Logging in to CompuServe.  Please wait...   
   
      send "..." when connected   
      ;...^M   
   
      send node id number when the word DATAPAC is received   
      DATAPAC;P 12345678^M   
   
      CompuServe Information Service   
      Host Name:;CIS^M   
   
      insert your user ID   
      User ID:;12345,6789^M   
   
      send password from dialing directory   
      Password:;a-P   
   
      check for mail or whatever   
      Enter choice!;5^M   
      etc, etc.   
   
      See the included file QCOM.SCR for more examples on scripting.   
   
      Note: When saving a script, QCom saves every line of incoming text on   
      which the user is prompted for input AND which is terminated with a   
      carriage return ( by pressing the ENTER key).  Any line that prompts   
      the user and does not require the ENTER key to be pressed, will NOT   
      be saved in the script.  Such lines would have to be manually typed   
      into the script with a text editor.   
                                  -Page 12-
   
   MAKING A SCRIPT Continued...   
   
      In order to use a script automatically, put the name of the   
      script file in the SCRIPT column in the Dialing Directory.   
      One way to create a new script is to capture a session and then   
      edit it to conform to the above format, using the semicolons to   
      separate incoming and outgoing text.  Any unnecessary text can be   
      deleted from the capture file (such as news bulletins, etc.).   
      Rename the file using ".SCR" as the extension in your script   
      filename.   
   
   COMMANDLINE SCRIPTS:   
   
      Commandline scripts allow you to start Qcom, dial a number, transfer   
      files, hangup and end Qcom automatically.   
   
      To create such a COMMANDLINE script, run Qcom, press ALT-S before   
      going into the Dialing Directory .  Enter the name of your script,    
      and proceed to step the program through the whole dialing and    
      connection procedure.  Qcom will save your commands as well as the    
      text coming in and going out.   
   
      To execute this script from the commandline use:   
   
      "QCom /SMyScript.scr"   
   
      The "/S" tells QCom that the following is the name of a script to   
      execute. You must use the full script filename.   
      When a script is executing you will see an upper case "S" on the   
      Status line.  To stop script execution at any time, press ESC.   
   
      Note:   
      When your script dials a directory entry that has another script   
      specified, the second script will be ignored.  You can, however,   
      call another script by using the ALT-Q command.   
      (eg. ";a-Q ANOTHER.SCR").   
   
   SCRIPT COMMANDS:   
   
      Most Script commands consist of shorthand for the keystrokes   
      you would use when manually running QCom.  The ALT-Key commands   
      that QCom understands can be entered into a script with  ";a-"   
      followed by the letter you wish to use. Eg. ALT-P would be ";a-p".   
      Upper or lower case will work.   
   
      Exceptions: ALT-- (ALT-Minus) and ALT-= cannot be saved or executed   
      in a script.   
   
   
   
   
   
                                  -Page 13-
   
   SCRIPT COMMANDS CONTINUED...   
   
      The following are script commands that may be manually added to   
      scripts.  These are NOT included in Saved scripts.   
   
      "ANY"     - used to send a given response to text that is received   
                repeatedly.   
                eg. ;ANY Press any key;^M   Whenever "Press any key" is   
                received, a carriage return will be sent. This will remain   
                in effect until the ANY command is used again in the script   
                to specify new incoming text.   
                eg. ANY   
                This effectively "turns off" a previous ANY command. QCom   
                will no longer respond to the previously specified incoming   
                text.   
   
     "DEBUG ON" -used in script debugging   
                The Status line shows which line of incoming text the    
                script is waiting for. This allows you to compare a script    
                line to actual received text to check for spelling errors    
                or typos in cases where a script is not working properly.   
                Pressing ALT-V during a debug session will load your script   
                into your editor so you can make corrections on the fly.   
   
     "DEBUG OFF" -disables the debug function.   
   
     "ECHO"     -prints text on the local screen.   
                eg. ";ECHO Please wait. Auto Logon in progress..."   
                Text can be colorized and positioned on screen   
                using ANSI escape codes.   
   
     "LOG"      - will save date, hostname, start time and duration   
                of calls in optional specified filename. If no log file   
                is specified, QCom defaults to "USAGE.LOG".   
                eg. ";LOG CIS.LOG"  could store a log of calls to   
                CompuServe. Also provided is a utility to total the   
                durations of calls, named QTT.EXE. Usage: QTT LogFile.   
   
     "WAIT"     - will pause the execution of a script for a specified   
                number of seconds.  Eg. ";WAIT 5"  will pause everything   
                for five seconds.  Do not pause for too long if you expect   
                to have incoming data during this time.  Hitting any key   
                will terminate a pause and continue the script.   
   
     "DOS"      Allows you to shell to Dos and execute batch files or   
                whatever.  Use the /WAIT switch after the commandline if   
                you wish to pause the display before returning to QCom.   
                eg:   
                ;DOS vampire.bat /WAIT   
   
   
   
                                  -Page 14-
  
  SCRIPT COMMANDS CONTINUED...   
   
      "ASK"     Used to get user input from the keyboard.  This will display  
                your "User Prompt" in a box and wait for user input.  When    
                the user presses Enter, QCom will compare the user's input    
                to the text in "Answer". If it is the same then the script    
                will go to the "Label". Otherwise the script will continue    
                with the next line. Use commas to separate the prompt,    
                answer and label.    
                Usage: ;ASK User Prompt ,Answer,Label    
                eg:   
                ;ASK Download your mail? (Y/N) ,Y,DownLoad Mail   
                ;GOTO No Download   
                :DownLoad Mail   
                ;...   
   
      "GOTO"    To branch to another part of the script.   
                eg:   
                ;GOTO Label 1   
                or...   
                When this text is received;GOTO Label 2   
   
      "CALL"    To go to another part of the script and execute until the    
                RET (Return) command is encountered. It returns to the line   
                following the Call. Calls can be nested 255 levels.   
                eg:   
                When this text is received;CALL Label 3   
                or...   
                ;Call Label 3   
                ;END   
                :Label 3   
                Look for this text;send something^M   
                ;RET   
   
      "RET"     As above, used to return from a CALL. A RET must not be    
                executed unless a CALL has been executed first. RET cannot    
                be used with GOTO.   
                Usage: ;RET   
   
      "T/O"     Timeout for incoming text.  A given timeout value will apply  
                to any script line waiting for incoming text which follows    
                the T/O command.    
                To enable timeout use: ;T/O Seconds   
                To disable timeout use: ;T/O 0   
      
        Example:   
                ;T/O 10   
                Wait for text for 10 seconds;Send if received before 10 secs  
                Otherwise wait for this for 10 seconds;...etc.   
                Disable timeout:   
                ;T/O 0    
                                  -Page 15-
     
  SCRIPT COMMANDS CONTINUED...   
       
      "ENQ"     Have QCom do something upon receiving an ENQ character (^E).  
      A typical use would be when transferring a file on Compuserve using   
      the QuickB protocol. The following example shows how to have QCom   
      shell out to OZBext (an external QuickB protocol) to transfer a file   
      on Com port 2 when the ENQ character is received.   
      Eg:  ENQ;DOS OZBext /c2 /x    
   
      Registered users may use port and file abbreviations, etc., where    
      appropriate, as per their instruction sheet.   
      After QCom receives this ENQ it stops looking for further ENQ's.   
       
      "END"    Used to stop script execution.   
            eg:   
            ;END   
            or...   
            When this text is received;END    

      "TAG" Used for tagging or marking Dialing Directory entries for 
            dialing.
            eg:
            ;TAG PCUG 
            QCom will tag or mark all Dialing Directory entries starting with  
            "PCUG". To tag only one of several entries with similar names it is 
            necessary to have something unique in the name you wish to tag.
            eg: ";TAG PCUG Node 1"

            Note : When entries have been tagged with the above TAG command,   
            use the DIAL command without a specified name.
            eg:
            ;TAG PCUG
            ;DIAL
            This will cause QCom to dial all tagged entries until a connection 
            is made.
    
       "UNTAG" QCom will untag all marked Dialing entries.
            eg:
            ;UNTAG
  
      The following are script commands that may be manually added to   
      scripts.  These ARE included in Saved scripts.   
   
      "DIAL"    -dials the entry specified. Eg. ";DIAL CompuServe"   
      "U/L"     -uploads the specified file Eg. ";U/L Myfile.Zip"   
      "D/L"     -downloads the specified file Eg. ";D/L Myfile.Zip"   
      "BREAK"   -sends a BREAK signal to the host Eg. ";BREAK"   





                                   -Page 16-

   
   Labels:   
      Like labels in batch files, a label is preceded by a colon and can   
      consist of one or more words or numbers.  No semi colon is used as   
      in other script lines.   
      eg:   
      :Label 1   
      :Label 2   
   
   SEMICOLONS:       
      In a QCom script, the semicolon is all important. It divides each   
      line into incoming and outgoing text. Lines beginning with a semi-   
      colon are commands that QCom will execute (such as an ALT-Key   
      command).   
      Also note that only the first semicolon is used as a divider.   
      Subsequent semicolons are treated as regular text.   
   
      Any line of text in a script with no semicolon or colon is ignored    
      by QCom and can be used as a comment line for clarification when    
      viewing or editing the script.   
   
      Script execution takes place only in the terminal screen. If your   
      script executes something like ALT-B (ScrollBack) or ALT-Z (Help),   
      manual input will be necessary to return to the terminal screen to   
      continue script execution.   
   
    FINAL NOTE ON SCRIPTS:   
      When saving a script, incoming phone noise may be saved during a   
      session and will have to be edited out before using the script.   
      It's wise to double-check a newly created script for any unwanted   
      characters.  Any pure text editor can be used to edit or create a   
      script file.   





















                                   -Page 17-

   
    TROUBLE SHOOTING:   
   
      Symptom:  "Cannot initialize Com Port x" error message. (x = 1 to 4)   
      Meaning of error message: Qcom cannot find the Com Port that is   
      specified in the configuration file (QCom.CFG).   
      Possible causes:   
      1. Error in configuration file.  The number specified there does not   
         match the Com Port used by the modem.   
      2. Hardware problem.  Two or more devices are configured for the same   
         Com port or the Com port specified is not installed.   
         Check that there is no conflict in hardware interrupt settings.   
         If two serial devices attempt to use the same Interrupt (IRQ)   
         setting chances are, neither will work. Typical settings would be:   
   
                           Com1 using IRQ 4, at I/O 3F8h   
                           Com2 using IRQ 3, at I/O 2F8h   
                           Com3 using IRQ 4, at I/O 3E8h   
                           Com4 using IRQ 3, at I/O 2E8h   
   
      3. Software conflict. A memory resident program that ties up the Com   
         port has been previously executed and has not been deinstalled.   
         Carbon Copy is an example of such a program.   
   
      Symptom: "Modem not responding"   
      Meaning of message: Modem did not respond with "OK" within the   
      alotted time.   
      Possible causes:  See the following:   
   
      Symptom: Modem does not dial out.  Modem does not receive some/all   
      commands sent by QCom.   
      Possible causes:   
      1. Baud rate specified in the configuration file is too high for the   
         modem.   
         Set the default baud rate to your modem's fastest speed.  Modem   
         will send back an "OK" when you initialize the modem (Alt-M) if   
         all is well.   
      2. External modem is not powered up or not connected properly.   
   
      3. Possible hardware conflicts with another installed serial device.   
         Internal modem has been improperly installed or configured.   
   
      4. Modem initialization or dialing prefix strings are incorrect.   
         Refer to the Modem instruction manual for the correct strings for   
         your modem.   
                                         
                                  -Page 18-
   
   TROUBLE SHOOTING Continued...   
   
      5. Modem is incorrectly configured.  Refer to modem manual and set   
         modem dip switches or NVRam for the following:   
         a) Modem must track the actual state of DCD (Carrier) and not be   
            forced.   
         b) Modem should track DTR and not be forced.   
         c) Modem MUST send back verbal result codes such as "OK" or   
            "CONNECT", etc.   
   
      6. See the following   
         Symptom:  QCom status line says "Online" even when not.   
         Cause:   
         Modem Carrier Detect line is forced on.  This MUST toggle on or    
         off depending on the actual Carrier state.  This is set with a    
         modem dip switch or a command sent in the initialization string.     
         Refer to the modem manual.  Edit the initialization string if    
         necessary and use Alt-M to manually send the string to the modem.    
 
         Or toggle the Carrier detect dip-switch if present.   
         Many modem factories typically set this to default to always on.   
         One result of this is QCom will prompt you whether you want to   
         initialize the modem at start-up which is an unnecessary annoyance   
         (the prompt is necessary in the instance where QCom is used as a   
         dumb terminal attached directly to another machine).   
   
   
         Symptom: Pressing Alt-M to re-initialize the modem gets back    
         "ERROR" from the modem.   
         Cause:   
         The modem initialization string (line six in the QCom.CFG file)   
         contains command(s) that the modem does not understand.  Or, the   
         command string is too lengthy.  Refer to the modem manual and    
         remove any command not found in the manual.  Long initialization    
         strings can be broken up into two sections with "^M~~~AT" inserted   
         about halfway.   
   
         Symptom: QCom reports "Unable to find DSZ.COM or DSZ.EXE"   
         Cause:   
         DSZ.COM or DSZ.EXE are not found in the default directory (the    
         same directory as QCom) or in the search path.  Put DSZ into    
         correct directory.   
          
         Symptom:Always get a fast busy signal after dialing. 
         Cause:  
         a) Call waiting string in Options is enabled when the feature 
         is not present on the phone line.  Disable the string by erasing 
         it or prefix it with a semicolon. 
         b) A pause character may need to be added after the string. Most   
         modems recognize a comma as a half second pause. eg:"*70,," 
   
                                      -Page 19-
   
   
    ONLINE SUPPORT BBS:   
   
         To obtain further help, or for the latest update of Qcom, you   
         can call the support BBS:   
   
         ************************************************   
         *   Programmer's Oasis, Ph.  1-204-478-3562.   *   
         ************************************************   
   
         
         When calling in, login as a new user with your full name and   
         password of your choice. After answering a few questions you   
         will be given the opportunity to go into the QCom area.   
         Once there you will have 30 minutes to send or receive messages   
         and download files.  Questions about QCom should be directed   
         to the author, not the Sysops.   
   
         Sysops Brian Lowe and Bernie Minuk are to be commended for   
         all their effort and enthusiasm in setting up and maintaining   
         this support area on their BBS.  Thanks guys, for doing an   
         outstanding job.   
   
      DISCLAIMER:   
   
      This software is provided "as is" without warranty either express or   
      implied.  The user assumes all responsibility in determining its'   
      usefulness and or fitness for any purpose, and assumes all risks and   
      liabilities including damages for loss of business profits, business   
      interruption, or loss of business information arising from the   
      operation of this software.   
   
   
   
   
   
   
   
   
   
   
   
   
    
  
 
  
 
  
 
  
 
                                  -Page 20-
  
 
                                        
 
                                        
 
             **************************************************  
 
                              QCOM REGISTRATION  
 
                                        
 
                 If you use QCom,  please register it.  This  
                software is the result of a great deal of time  
            and effort.  Please support its' continued development  
                          and the Shareware concept.  
 
                                        
       To add incentive, those who register will be shown how to utilize  
          the user defineable functions.  Users can pre-define other  
        external protocols, or DOS commands, and access them with a single  
                                  keystroke.  
                                         
 
              The one-time registration fee is a modest $20.00.  
              To receive a copy of the absolute latest version on  
                 disk, send an additional $5.00 to cover cost  
                 of disk, packaging and mailing.  Specify disk  
                    size desired and your current version.  
 
           A quick mailer is provided in the file called Register.  
                  
                        Send a check or money order to:  
                                     
                                RTFM  Software  
                                108 Egesz St.  
                                Winnipeg, Mb. Canada  
                                R2R 2E1  
                                    
             Your comments, questions, suggestions and bug reports  
                are always welcome whether or not you register.  
        Drop me a note, leave a message on CompuServe I.D. 72361,3117.  
      Or, leave a message on Programmer's Oasis BBS, Ph.  1-204-478-3562.  
 
             **************************************************  
 
                                        
                                    
                                      
                                       
                        
                           
                     
                                  -Page 21-