The introduction of a ROUTE_TO.CTL file.

This file allows you to take messages addressed to one system and
send them to another system.

The structure of the ROUTE_TO.CTL file is 3 fields per line.

[Addressed FROM] [Addressed TO] [Send TO]

The Addressed FROM and Addressed TO fields may contain parts of
an address or the entire address. The Send TO field must contain
the entire address.

e.g.

1314 1808 18087326909

Meaning: Any message that has an origin address starting with
1314 that has a destination address starting with 1808 and send
them to 18087326909.

This does basically the same thing that a Fidonet packer would
do using multple control verbs. ie... FORWARD-FOR xxxxxx and
ROUTE-TO xxxxx xxxxx xxxxxx, providing they are in the correct
positions and they're working correctly which most don't.

When routing or forwarding MATRIX mail to or For Fidonet mailers,
the Flash packer has an optional enhancement. A Btree index of
HTMS addresses pointing to assocated net/node addresses so the
flash packer will work with routed or forwarded Fidonet matrix
mail.

In order to engage the optional index, use the enclosed
BPINDEX.EXE program. It will create a FIdolist.BPL index file. If
this file exists and the flash packer is used, it will bundle
using the correct NET/NODE addresses.

BPINDEX requires ONE command line switch, your ZONE number. We
generally do NOT route or forward matrix mail for those outside
our Zone so there isn't any need to have them listed in the
index. If you just WANT them in, then enter a ZERO for the zone
number.

e.g. BPINDEX 1  <- Zone ONE
e.g. BPINDEX 2  <- Zone TWO
e.g. BPINDEX 3  <- Zone THREE
e.g. BPINDEX 0  <- ALL Zones


BPINDEX must be in the SAME directory as the Fidolist.Dat file.


Remember, BPINDEX is ONLY for Fidonet mailers. If your not
forwarding or routing FOR Fidonet mailers, it is NOT needed
nor used.

Changes in the Terminal section:

Added 2 additional protocols: Zmax and Ymodem-G.

Switch from DSZ to my own drivers. You will need Tmodem.exe, Zmodem.exe,
Xmodem.exe, Ymodem.exe, and Zmax.exe. Most of you already have them.

Changed VMS so that it only requests 200K of free memory for protocol
drivers instead of ALL memory. Will make no difference to those with EEMS
or LIM 4.00 but for those that don't have it, this will drastically speed
up the calls to the drivers.

Misc. Changes.

Added message area and inbound file area verification checks to assure
that both paths are accessible so the MicroSoft file functions don't
barf if for instants, a drive door is left open or something like that.

Changed from MCOMM's async_stop and async_restart to internal routines to
dis-engage and re-engage serial driver during shells or external program
calls. Async_stop and async_restart doesn't always work on all systems,
the new method will.