Introduction to Falken Serial I/O capabilities.

Falken's serial I/O capabilities are provided by an internal interrupt
handler.  It is not necessary (or smart) to load an external program to
control the serial ports.  Falken uses an 'interrupt-driven poll' method
to control the serial ports.  In short, this is what happens :

    Falken examines the hardware configuration, and determines the
    highest baud rate used by the system.  It then calculates how many
    times per second it must test the serial hardware to see if any
    of the modems need servicing.  The timer chip in the PC is then
    reprogrammed to interrupt Falken at that interval, and Falken
    queries the appropriate serial ports, looking for ports that
    require servicing (character received, transmit ready, DCD change,
    etc.).
    This method overcomes a very serious shortcoming in PC hardware
    design - there are only 2 IRQ vectors assigned to serial ports.
    If more than 2 serial devices are required, they must share these
    IRQ vectors.  If the devices that are sharing a vector are on
    different cards (2 or more internal modems, for instance), then
    interrupts can be lost.  So Falken does not use the normal serial
    I/O interrupts.  In fact, the IRQ setting of the serial device is
    irrelevant, and not used by Falken at all.

Falken's serial driver is Fossil compatible.  This means that the driver
conforms to most of the Fossil specification found in the FOSSIL.DOC file
included with this archive.  It supports a 'text' mode also.

In 'text' mode, Falkens internal Fossil drivers will :
    Echo incoming characters (keystrokes) back out to the port.
    Filter input according to an internal translation table.
    Characters to be echoed back to the port are held until the
        current output has completed.  An hex FF (0xff) character is
        used as an output separator.  If you start typing in the middle
        of a menu, for example, your keystrokes will not be echoed until
        the current transmission is completed.
    The 'flush output buffer' is more intelligent - allows the current
        output line to complete before flushing the output buffer.  In
        effect, it removes everything AFTER the next carriage return.
    On output, Line Feed characters are ignored, but a line feed is
        automatically transmitted after every carriage return.
    Backspace is echoed as '<BS><SPACE><BS>', so that a BS is destructive,
        but a BS will only be echoed if there are characters in the input
        buffer.
    Characters in the output buffer are not transmitted while there are
        characters in the input buffer.  This prevents the user's
        input from being intermixed with output text.

The net effect is a more fluid user interface.  Once the user's input
starts echoing out, it will not be interrupted by output from Falken.
Aborted output will not terminate in the middle of a line of text.
Output from Falken will not be interrupted by echoed keystrokes, until
the current 'record' is completed.

A door program that receives input from Falken via message queues does
not have to worry about echoing characters or cr/lf conversions, etc.
The line will still be in 'text' mode, since Falken is still in
control of the port.  This is not true if the door uses the port directly.

If a door program requests direct control of the serial port, the port
is placed into 'raw' mode.  All 'text' mode controls are disabled, and
the program is given a raw serial port which responds to Fossil calls.

To take direct control of the serial port, a door *MUST* inform Falken
that it wishes to do so.  Otherwise, both Falken and the door program
will be trying to obtain input and send output to the same port, and
very likely nothing will work right.  To gain control of the serial port,
simply send a message to Falken on your tasks queue, with message type '8'
like this :

    int m1;

    m1 = 8;
    send_md_msg(outq, &m1, 2);

As soon as Falken receives this message, it places the port into binary
mode (i.e. takes it out of text mode), and relinquishes all control of
the port.  When the door stops, Falken takes the port back.
The only real checking that Falken does while the door has control of
the port, is to check for Carrier Detect.  If DCD drops, Falken will
clean up the port and terminate the door.

See the file transfer protocols for examples of taking control of the
serial port.

Falken's built-in FOSSIL support provides the following standard FOSSIL
services to doors that have control of the serial port :

    Function 0  : Set Baud Rate (will not work if port is FIXED BAUD)
    Function 1  : Transmit Character with wait
    Function 2  : Receive Character with wait
    Function 3  : Status Request
    Function 4  : Initialize Port
    Function 5  : De-initialize Port
    Function 6  : Raise/Lower DTR
    Function 7  : Return System Timer Parameters
    Function 8  : Flush Output Buffer
    Function 9  : Purge Output Buffer
    Function A  : Purge Input Buffer
    Function B  : Transmit Character, no wait
    Function C  : Non-destructive 'peek' at input buffer
    Function F  : Flow Control
    Function 18 : Read Block
    Function 19 : Write Block
    Function 1A : Start/Stop Break Signal
    Function 1B : Get Driver Information

Functions 1, 2, and 8 specify that the Fossil driver will not return to
the caller until the condition is satisfied.  In this case, the Fossil
driver will use the Cswitch RELINQ() call to allow other tasks to run
until the condition is met.  Performance is not affected by using these
calls.

In addition, Falken provides additional FOSSIL services not defined in
FOSSIL.DOC.  Some of these services are reserved for Falken.  Services
available for doors tasks are :


    Function 41h : get address of I/O control structures
        Inputs :
            none

        Outputs :
            ax : segment address of i/o control structure array
            bx : offset address of i/o control structure array

        Note : This function is useful if you need to manipulate the
               flags and variables that the internal Fossil driver uses
               to control serial I/O.  In most cases, this direct
               manipulation is not needed, and can be dangerous to the
               system.  It is recommended that you use the other Fossil
               calls to control the serial port.



    Function 43h : Set buffer sizes
        Inputs :
            DX = Line Number
            AH = 43h
            BX = new input buffer size
            CX = new output buffer size

        Returns :
            AX :  0 if successful, -1 if error

        Note : This function is used to alter the Fossil's internal buffer
               sizes.  Falken allocates 4096 bytes of buffer space to each
               line.  Normally, the input and output buffers use only 512
               bytes each.  These buffers can be re-sized dynamically,
               provided the total buffer space does not exceed 4096 bytes.
               Sizes must be multiples of 16, i.e. 64, 128, 512, 2048, etc.
               This is mostly useful for file transfer protocols.  Upload
               protocols will allocate larger input buffers, while download
               protocols will allocate larger output buffers.


    Function 44h : Return total buffer space reserved for each line.
        Inputs :
            AH = 44h

        Returns :
            AX :  Total buffer space limit (Falken sets this to 4096)


    Function 49h : Put a character into the Fossil input buffer
        Inputs :
            AH = 49h
            DX = line number
            AL = character to be placed on the line's input buffer

        Outputs :
            none

        Note : This function places the specified character into the line's
               input buffer.  If the line is in text mode, the character will
               be echoed to the user, just as if it were typed by the user.
               If the sysop is monitoring this line, the character will
               be displayed in the monitor window, just as if it were typed
               by the user.


    Function 4ah : Return number of bytes available in output buffer
        Inputs :
            AH = 4ah
            DX = line number

        Outputs :
            AX = number of bytes available in output buffer.  This is the
                 number of bytes that can be sent to the Fossil driver
                 without data loss.  This value is equal to :
                 [output buffer size] - [bytes in output buffer]


    Function 4bh : Return number of bytes available in input buffer
        Inputs :
            AH = 4bh
            DX = line number

        Outputs :
            AX = number of bytes waiting in the Fossil input buffer