Falken V7.05 Changes from 6.69B
by Bill Bell

BBSCFG.H

   BBSCFG Structure:      (6272 bytes -> 8004 bytes)
        Totally changed to support 64 lines (plus console), and from 32->64
        library areas.  Expanded some more information.
        Each category has it's own download path, each library has one
        upload path.  Expanded from 8 to 20 categories per library.
        V7.05:
          Can now cut/paste in BBSCFG.EXE

STRUCTS.H

   Order of things pretty much stayed the same.  The size of the structure
   remained the same.

   1. Account Structure:  (620 bytes -> 620 bytes)
        Added the following:
           logoff_date, logoff_time, prev_logoff_date, prev_logoff_time
        Changed uploadflags to an array [2] and moved it.
        Changed dloadflags to an array [2].
        Acctnum now is variable length starting at "1". (not "0000001").
        Acctnum gets reused after running packfile for V7.0.
        V7.05:
           added use_credits 1=credit wont use the credits in menu.
           added account_type (any number, 6 mo, 3 mo, 1 year, etc
                for own use).
   2. User Structure:     (100 bytes -> 100 bytes)
        Changed "unsigned long ignore" to "unsigned char ignore[9]"
        to take into account 63 lines plus console.
        st_network was removed.
        V7.05:
           added busyflag for .busy can't receive or send .sends
   3. dloadrec Structure: (totally changed)
        Catagory starts at 1. No 0 anymore. From 8 to 20 Catagory areas.
        From 32 to 64 Library areas.
        In V6.69b : dl_acctid == '@s:\dir\' for CD_ROMS
        In V7.0 : download.exe does not work for "@", getting fixed.

DOORUTIL.C

   Minor changes throughout (bug fixes and more power!).
   workbuf is now "unsigned char workbuf[1300]", just define it as
   "extern unsigned char workbuf[]".

   Setting binary mode only works thru send_md_msg(0, ...). Other
   messages may only work thru queue 0 as well.
   V7.05:
      Added void message_out() because send_md_msg() looks like
        it can now fail.
      st_network added back in.
      setwatchdog() added to have Falken watch for Carrier!
      sendraw() added
      lprintf() added

DOORUTIL.H

   Now includes the fsubs prototypes.

FSUBSC.C/ FSUBS.OBJ

   f_getinfo takes void *buffer
   f_setbaud now takes unsigned int for baud rate.
   f_purgeout returns void
   f_writechar takes an integer for the char
   f_insertchar takes an integer for the char
   The input and output buffer is only 1024 bytes (from 2048).

   In the fsubs.asm there seems to be a new f_ovrunerrs() not
     in the .C versions.

TCB.H

   Minor changes in the struct tcb_rec structure (no sizeof change).
   New CSWITCH prototypes.  However not defined in lmtcc:
       ems_map_handle
       termtask
       ploadprg
       loadprg
       load_a_prog
     And ksignal() seems to went away (dunno what is did anyways).

LMTCC.C/lmtca.asm/smtca.asm

   Added recvmsg_nowait()