Fundamentals of FOSSIL implementation and use
                        Draft Version 3   March 7, 1987
                      Vincent E. Perriello, VEP Software
 

		 IFNA Address: Network 141 Node 491 (141/491)
     Usenet address: ...decvax!envore!vaxine!spark!141!491!Vince_Perriello






 






















 Copyright (C) 1987, VEP Software, Naugatuck, CT 06770. All rights reserved.
 
 This document may be freely used or copied by anyone interested in the data
 contained herein. No fees may be charged for distribution of this document.
 You will be held  accountable for all such charges,  and expected to either
 reimburse those persons or organizations so charged,  or to make a donation
 in the exact amount of those fees to the International FidoNet Association, 
 to  assist  them in their  efforts to  advance the  technology of  personal 
 computer telecommunications.


Fundamentals of FOSSIL implementation and use                         Page 1




 A. Objectives of this document

    This document is directed at implementors or intellectuals.  It is meant
    for use in implementing applications that can use FOSSIL drivers, or for
    details needed to implement a new FOSSIL. As such it won't always go out
    of its way to explain itself to the neophyte.

    This document will have served its purpose to you if you are able to use
    the data contained within to perform either of the above tasks.   If you
    feel that necessary data has been omitted please contact Vince Perriello
    at the above listed address so that the appropriate changes can be made.



 B. Historical perspective
 
    For those people who were not lucky enough to have an IBM PC or a system
    nearly completely compatible, the world has not been very friendly. With
    his implementation of the Generic Fido(tm) driver,  Tom Jennings made it
    possible for systems that had nothing in common with an IBM PC except an
    808x-class processor, and the ability to run MS-DOS Version 2 and above,
    to run his Fido(tm) software. That was a lot to ask, and a lot of people
    thought it was enough.

    But not everyone.  While Thom Henderson was debugging Version 4.0 of his
    SEAdog(tm) mail package,  an "extended" Generic driver was designed  (in
    cooperation with Bob Hartman)   as a quick kludge to help him get past a
    problem with certain UART chips.The new hook was quickly pounced upon by
    Vince Perriello,  who, with almost DAILY prodding (ouch! it still hurts)
    by Ken Kaplan,had been working with Henderson to get DEC Rainbow support
    into SEAdog. Vince then coded a driver to use this hook and - Voila! - 
    SEAdog 4.0 started working like a champ on the Rainbow.

    Then something WONDERFUL happened. Wynn Wagner started having a bad time
    getting the Greenleaf(tm) Communication Libraries to work in exactly the
    way he wanted them to. Enter Bob Hartman. Having already enjoyed success
    in the effort with Thom Henderson, he suggested to Wynn that with a very
    few extensions, the driver that SEAdog(tm) 4.0 liked could drive Opus as
    well. Then Vince called Wynn, Wynn called Bob, Bob called Vince, and the
    FOSSIL driver came into existence.

    FOSSIL, by the way, is an acronym that Vince dreamed up. It took a while
    for everyone to stomach it,but it now seems to be loved by all. It is an
    acronym for "Fido/Opus/SEAdog Standard Interface Layer". And the concept
    is catching on.   Henk Wevers is reportedly coding a terminal program in
    Turbo Pascal that uses FOSSIL services to do all the work.   This should
    mean that the result will play elsewhere.   And there are already FOSSIL
    implementations for the Tandy 2000, Sanyo 555, Z100 and others,   so the
    potential of a properly coded FOSSIL application is very great.


Fundamentals of FOSSIL implementation and use                         Page 2




 C. Basic principles of a FOSSIL driver

    1)  Interrupt 14H.

    The one basic rule that the driver depends upon,  is the ability for ANY
    target machine to allow the vector for INT 14H (absolute locations 50 to
    53 in segment 0) to be "stolen" by the driver. In a system where the INT
    14H vector is used already, it must be possible to replace the "builtin"
    functionality with that of a FOSSIL,  when an application that wants the
    use of a FOSSIL is to be run on the target machine.


    2)  How to install a FOSSIL driver in a system

    There's no hard and fast way to do this. The FOSSIL might be implemented
    as part of a device driver (like Ray Gwinn's X00.SYS) and therefore gets
    loaded using a line in CONFIG.SYS at bootup time.  It might be done as a
    TSR (terminate and stay resident) program, in which event you install it
    by running the program  (DECCOMM by Vince Perriello and Opus!Comm by Bob
    Hartman work this way, for example).


    3)  How an application can detect the presence of a FOSSIL

    The driver has a "signature" that can be used to determine whether it is 
    present in memory. At offset 6 in the INT 14H service routine is a word, 
    1954 hex,  followed by a byte that specifies the maximum function number 
    supported by the driver. This is to make it possible to determine when a
    driver is present and what level of functionality it provides. Also, the
    Init call (see below) returns a 1954 Hex in AX.  SEAdog(tm) looks at the
    signature and Opus just goes for the Init. Fido doesn't do either.


    4)  How to call a FOSSIL function

    The FOSSIL driver is entered by issuing a software Interrupt 14 Hex from
    the application  program. The code corresponding to the desired function 
    should be in 8-bit register AH. For calls that relate to communications,
    the port number will be passed from the application in register DX. When
    DX contains a zero (0) it signifies use of COM1, or whatever the "first"
    serial port on your machine is called. A one (1) in DX points the driver
    at COM2, and so on.


Fundamentals of FOSSIL implementation and use                         Page 3




D. Functions currently defined for FOSSILs



    AH = 0	Set baud rate 
		Input:	AL = baud rate code
			DX = port number

    This works the same as the  equivalent IBM PC BIOS call,  except that it
    ONLY selects a baud rate.  This is passed in the high order 3 bits of AL
    as follows:

		000 =  110 baud
		001 =  150  ''
		010 =  300  ''
		011 =  600  ''
		100 = 1200  ''
		101 = 2400  ''
		110 = 4800  ''
		111 = 9600  ''

    The low order 3 bits can be implemented or not by the FOSSIL, but in all
    cases, if the low order bits of AL are 00011,  the result should be that
    the communications device should be set to eight data bits, one stop bit
    and no parity. This setting is a  MINIMUM REQUIREMENT  of Fido, Opus and
    SEAdog.



    AH = 1	Transmit character 
		Input:	AL = character
			DX = port number
		Output: AX contains status bits (see function 3)

    AL contains the character to be sent.   If there is room in the transmit
    buffer the return will be immediate,  otherwise it will wait until there
    is room to store the character in the transmit buffer.  On return, AX is
    set as in a status request (see function 3).



    AH = 2	Receive a character 
		Input:	DX = port number
		Output:	AL = input character

    If there is a character  available in the  receive buffer,  returns with 
    the next character in AL.  It will wait until a character is received if
    none is available.


Fundamentals of FOSSIL implementation and use                         Page 4




    AH = 3	Request status
		Input:	DX = port number
		Output:	AX = status bit mask (see below)

    Returns with the line and modem status in AX.  Status bits returned are:

		In AH:
		Bit 0 =	RDA  - input data is available in buffer
		Bit 5 = THRE - room is available in output buffer
		Bit 6 = TSRE - output buffer is empty

		In AL:
		Bit 7 =	DCD  - carrier detect 

    This can be used by the application to determine  whether carrier detect
    (CD) is set,  signifying the presence/absence of a remote connection, as
    well as monitoring both the input and output buffer status.



    AH = 4	Initialize driver 
		Input:	DX = port number
		      ( BX = 4F50
			CX = ^C flag address --- optional )
		Output:	AX = 1954H if successful


    This is used to tell the driver to begin  operations,  and to check that
    the driver is installed. This function should be called before any other
    communications calls are made.  At this point all interrupts involved in
    supporting the comm port (specified in DX) should be set up for handling 
    by the FOSSIL, then enabled.  If BX contains 4F50 hex,  then the address 
    specified in DS:CX is that of a ^C flag byte in the application program,
    to be incremented when  ^C is detected in the keyboard service routines.
    This is an optional service and only need be supported on machines where
    the keyboard service can't (or won't) perform an INT 1B or INT 23 when a
    Control-C is entered.



    AH = 5	Deinitialize driver
		Input:	DX = port number

    This is used to tell the driver that comm port operations are ended. The
    function should be called  when no more comm port functions will be used
    on the port specified in DX.



    AH = 6	Raise/lower DTR
		Input:	DX = port number
			AL = DTR state to be set (1 = Raise, 0 = Lower)

    This function is used to control the DTR line to the modem.	AL = 0 means 
    lower DTR (disable the modem), and AL = 1 means to raise DTR (enable the 
    modem).  No other function (except Init) should alter DTR.


Fundamentals of FOSSIL implementation and use                         Page 5




    AH = 7	Return timer tick parameters
		Output:	AL = timer tick interrupt number
			AH = ticks per second on interrupt number in AL
			DX = approximate number of milliseconds per tick

    This is used to  determine the parameters of the timer tick on any given
    machine.  Three numbers are returned:

	AL =   Timer tick interrupt number
	AH =   Ticks per second on interrupt number shown in AL
	DX =   Milliseconds per tick (approximate)

    Applications can use this for critical timing  (granularity of less than
    one second) or to set up code  (such as a watchdog)  that is executed on
    every timer tick. See function 22  (add/delete function from timer tick)
    for the preferred way of actually installing such code.



    AH = 8	Flush output buffer
		Input:	DX = port number

    This is used to force any pending output.   It does not return until all 
    pending output has been sent.  You should use this call with care.  Flow
    control  (documented below)  can make your system hang on this call in a
    tight uninterruptible loop under the right circumstances.



    AH = 9	Purge output buffer
		Input:	DX = port number

    This is used to purge any pending output.   Any output data remaining in
    the output buffer (not transmitted yet) is discarded.  



    AH = 10	Purge input buffer
		Input:	DX = port number

    This is used to purge any pending input.   Any input data which is still
    in the buffer is discarded.



    AH = 11	Transmit no wait
		Input:	DX = port number
		Output:	AX = 1 if character was accepted and 0 if not.

    This is exactly the same as the "regular"  transmit call, except that if
    the driver is  unable to  buffer the character  (the buffer is full),  a
    value of zero (0) is returned in AX. If the driver accepts the character
    (room is available),  a one (1) is returned in AX.


Fundamentals of FOSSIL implementation and use                         Page 6




    AH = 12	Read no wait
		Input:	DX = port number
		Output:	AX = next character or FFFF if none available

    Return in  AX  the next character in the receive buffer.  If the receive 
    buffer is empty return FFFF.



    AH = 13	Keyboard read no wait
		Output:	AX = IBM-style keyboard scan code or FFFF if
			     no keyboard character available

    Return in  AX the next character  (non-destructive read ahead)  from the
    keyboard;  if nothing there  (in the type-ahead buffer),  return FFFF in
    AX.   Use IBM-style  function key mapping  in the high order byte.  Scan
    codes for non-"function" keys are not specifically required,  but may be
    included.



    AH = 14	Keyboard input with wait
		Output:	AX = IBM-style keyboard scan code

    Return in AX the next character from the keyboard;  wait if no character
    is available. Keyboard mapping should be the same as function 13.



    AH = 15	Enable or Disable flow control on transmit
		Input:	AL = bit mask describing requested flow control
			DX = port number

    This is used to stop output when the "other end" is overwhelmed, or when
    a BBS user wants to stop a screen.

    Two kinds of flow control are supported:

		Bit 0 = 1	XON/XOFF
		Bit 1 = 1	CTS/RTS

    Flow control is enabled, or disabled, by setting the appropriate bits in
    AL  for the types of flow control we want to ENABLE (value = 1),  and/or
    DISABLE  (value = 0),  and calling this function.  Bit 2 is reserved for
    DSR/DTR but is not currently supported in the DECCOMM implementation.

    Applications  using this  function  should set all bits  ON  in the high 
    nibble of AL as well.  There is a compatible  (but not identical) FOSSIL
    driver implementation that uses the  high nibble as a control mask.   If
    your application sets the high nibble to all ones,  it will always work,
    regardless of the method used by any given driver.


Fundamentals of FOSSIL implementation and use                         Page 7




    AH = 16	Extended Control-C / Control-K checking and transmit on/off
		Input:	AL = flags byte
			DX = port number
		Output:	AX = status (see below)

    This is used for BBS  operation,  primarily.  A bit mask is passed in AL
    with the following flags:

		Bit 0	enable/disable Control-C / Control-K checking
		Bit 1	disable/enable the transmitter

    The Enable (bit 0 = 1) and Disable (Bit 0 = 0) Control-C/Control-K check
    function is meant primarily for BBS use. When the checking is enabled, a
    Control-C or Control-K received  from the communications port will set a
    flag internal to the FOSSIL driver,  but will not be stored in the input
    buffer.  The next use of the function will return the value of this flag
    in register AX then clear the flag for the next occurrence. The returned
    value is used by the BBS  software to determine whether output should be
    halted or not.

    The Enable (Bit 1 = 1) and Disable (Bit 1 = 0) Transmitter function lets
    the application restrain the asynchronous driver from output in much the
    same way as XON/XOFF would.



    AH = 17	Set current cursor location.
		Input:	DH = row (line)
			DL = column

    This function looks exactly like like INT 10H, subfunction 2, on the IBM
    PC. The cursor location is passed in DX: row in DH and column in DL. The
    function treats the screen as a coordinate  system whose origin (0,0) is 
    the upper left hand corner of the screen.



    AH = 18	Read current cursor location.
		Output:	DH = row (line)
			DL = column

    Looks exactly like INT 10H,  subfunction 3,  on the IBM PC.  The current 
    cursor location  (using the same coordinate  system as  function 17)  is 
    passed back in DX.



    AH = 19	Single character ANSI write to screen.
		Input: AL = character to display

    The character in AL is sent to the screen by the fastest method possible
    that allows ANSI processing to occur (if available). This routine should
    not be used in such a way that DOS output  (which is not re-entrant) can 
    not be employed by some FOSSIL driver to perform the function  (in fact,
    on the IBM PC that is likely to be how it's done).  On some systems such
    as the DEC Rainbow this will be a very fast method of screen writing.


Fundamentals of FOSSIL implementation and use                         Page 8




    AH = 20	Enable or disable watchdog processing
		Input:	AL = 1 to enable or 0 to disable watchdog
			DX = port number

    When watchdog is enabled,   the state of the carrier detect (CD) line on
    the comm port specified in DX should be constantly monitored. Should the
    state of that line become FALSE (carrier lost), the system should be re-
    booted, to enable the BBS (or other application) to start up again.



    AH = 21	Write character to screen using BIOS support routines
		Input:	AL = character to display

    The character in AL is sent to the screen using  BIOS-level Input/Output 
    routines. This differs from function 19 in that DOS I/O CAN	NOT be used,
    as this function might be called from driver level.



    AH = 22	Insert or Delete a function from the timer tick chain
		Input:	AL    = 1 to add a function or 0 to delete one
			DS:DX = address of function
		Output:	AX    = FFFF if unsuccessful

    This function is used to allow a  central authority  to manage the timer
    interrupts, so that as code is loaded and unloaded, the integrity of the
    "chain" is not compromised.  Rather than using the traditional method of
    saving the old contents of the timer vector, storing the address of your
    routine there,  and executing a far call to the "old" routine when yours
    is done, instead you call this function. It manages a list of such entry
    points and calls them on a timer tick (interrupt) using a FAR call.  All
    the usual cautions about making DOS calls apply (that is, DON'T!).

    This makes it possible for a program to get in and out of the tick chain
    without having to know whether another program has also done so since it
    first insinuated itself.



    AH = 23	Reboot system
		Input:	AL = 0 for "cold boot" or 1 for "warm boot"

    Perform the old 3-finger salute.  Used in extreme emergency by code that
    can't seem to find a "clean" way out of the trouble it has gotten itself
    into.  Hopefully it won't happen while you're computing something in the
    other half of a DoubleDOS system. If your machine can make a distinction
    between a "cold" (power-up, self-test and boot) and a "warm" (just boot)
    bootstrap,  your FOSSIL should support the flag in AL. Otherwise just do
    whatever bootstrap is possible.


Fundamentals of FOSSIL implementation and use                         Page 9




E.  Validation Suite.

    Well, there is one, but it's involved.  Run FIDO_GEN V11w on your FOSSIL
    for about a week with  reasonable caller activity  in the message areas,
    file uploads and downloads,  and FidoNet(tm) mail.  Run SEAdog for a few
    days,  sending and receiving a reasonable  number of messages.  Then run
    Opus for the  rest of your natural life.  Why not?  It's a good package.
    Anyway,  some reasonable  compromise with the  above steps should ensure
    that your FOSSIL will work with most everything coded for one.



F.  Distribution.

    The good folks who  distribute Opus will be more than happy to take note
    of your new FOSSIL driver and to add it to their distribution.  And,  of
    course, you can upload it to any system you want, but your work will get
    more publicity in the Opus community than anywhere else.



G.  Technical Discussion.

    A FOSSIL echomail conference is in the process of starting up.   It will
    be coordinated by Vince Perriello at IFNA node 141/491.  Contact him for
    details on how to join. Keep in mind though, this conference is intended
    SPECIFICALLY  for implementors of  FOSSIL  software and not as a general
    Q&A conference,  for people who think  FOSSILs have something to do with
    paleontology.