You can have up to two serial ports on your I/O Card.  These 
serial ports support asychronous communication functions.
And, these ports can be set to COM1, COM2, COM3 or COM4.

The current release of PC or MS DOS recognizes COM1 and COM2.
Therefore, the current PC DOS (MS- DOS) only performs I/O  
functions COM1 and COM2.  Unfortunately, DOS can not recoginze
COM3 or COM4;i.e., input and output operations can not be    
performed by using COM3 or COM4.

Two new serial port utilities enable COM3 and COM4 to perform
the same functions as COM1 and COM2.  One is DEVCOM.SYS, a driver.
The other is CMODE.COM, a utility program.


1.   DEVCOM
	
     DEVCOM is a device driver that initializes two devices,
     COM3 and COM4, for serial ports on your I/O Card.  After
     DEVCOM has been executed, you can gain access to these
     serial ports by simply entering the names COM3 and COM4.

     Before starting DEVCOM, please set your I/O Card's serial
     ports to COM3 and COM4.  If the system fails to set these
     COM ports, the following message will appear on the screen:
 
     Can not find device COM n

     To execute DEVCOM, you must copy the DEVCOM utility onto
     your current working drive or DOS diskette.  The utility is     
     entitled, DEVCOM.SYS.  This device driver sets the COM
     parameters into the memory reserved for the operating system's
     data and gives you the interface between DOS and BIOS.  The
     DEVCOM.SYS utility must be set into your CONFIG.SYS device.
     If your boot diskette or current working drive has a            
     CONFIG.SYS device, please add the following command:
 
	DEVICE = DEVCOM.SYS

     If your boot diskette or current working drive does not have
     a CONFIG.SYS device, create one which includes the previous
     command.

     With your amended current working DOS diskette in the current
     working driver, reset the system.  You can reset the system by
     pressing the RESET buttom; simultaneously pressing CTRL, ALT
     and DEL; or turning the power off and on.  If COM3 or COM4 ports
     exist, then the following messages will appear on the screen:

	Device COM3 is installed.
	Parameters set to 2400, n, 8, 1
	Device COM4 is installed.
	Parameters set to 2400, n, 8, 1

     NOTE: A DEVCOM DEFAULT SETS COM3 AND COM4 COMMUNICATION
           PARAMETERS TO BAUD RATE 2400, NO PARITY, 8 DATA BITS 
           AND 1 STOP BIT.

     If COM3 and COM4 ports do not exist, then the following
     messages will appear on the screen:

	Can not find device COM3.
	Can not find device COM4.

     NOTE: WHEN USING PC/MS DOS VERSION 3.3+, THE DEVICE DRIVER ALONE IS
           SUFFICIENT AND THE DOS MODE COMMAND CAN BE USED TO SET ALL THE
           SERIAL PORT OPTIONS AS NORMAL, EXCEPT A BAUD RATE OF 19,200.
           HOWEVER A 19,200 BAUD RATE CAN BE SET USING THE CMODE.COM.


2.   CMODE COMMAND

     The utility programm, CMODE.COM, sets options for an
     asynchronous communications adapter.  The CMODE.COM also
     enables printer output to be routed to an asynchronous
     communications adapter or to another printer port. 


2.1  Setting Parameters

     The command format for setting the options of an asynchronous
     communications adapter is listed below.

	CMODE COMn:baud[,parity[,data bits[,stop bits[,p]]]]
          
     The variable "n" can be 1, 2, 3 or 4 designating the number 
     of the asynchronous communications adapter.

     The protocol parameters used to initialize the asynchronous
     communications adapter can be set by replacing the "[" symbols
     with specific characters.  These parameters and the specific 
     characters are listed below.

	Baud Rate: Enter 50, 75, 110, 134.5, 150, 300, 600, 1200,
                   1800, 2000, 2400, 3600, 4800, 7200, 9600, or 19200.

                   The default setting is 2400.

     NOTE: ONLY THE FIRST TWO CHARACTERS ARE REQUIRED, SUBSEQUENT
           CHARACTERS ARE IGNORED.  FOR EXAMPLE, IF THE COMMAND
           FORMAT WAS "CMODE COM3: 13,7", THE MODE OF OPERATION
           WOULD BE 134.5 BAUD RATE, EVEN PARITY AND STOPBIT
           PARAMETERS WOULD DEFAULT SINCE NO CHARACTERS WERE ENTERED.

	Parity:		Enter N (None), O (Odd), E (Even), M (Mark),
                        or S (Space).
                         
                        The default setting is E.

	Databits:	Enter 5, 6, 7 or 8.

			The default setting is 7.

	Stopbits:	Enter either 1 or 2.

			The default setting is 2 if the baud rate
                        is less than or equal to 110.

                        The default setting is 1 if the baud rate
                        is greater than 110.

     The "P" option indicates that the asynchronous adapter is 
     being used for a serial interface printer.  If you enter the 
     "P", time-out errors are continously retried.  You can stop
     the retry loop by pressing Ctrl-Break.  To stop the time-out
     errors from being continously retried when you have entered     
     "P", you must reinitialize the asynchronous adapter without
     entering the "P".


2.2  Routing Printer Output

     The command formats for directing parllel printer output to   
     an asynchronous communications adapter or to another printer
     are listed below.

	CMODE LPT#: = COMn

	CMODE LPT#: = LPT$

     There are three variables in this command format.  The variable
     "#" can be 1, 2, or 3 designating the printer port number.  The
     variable "n" can be 1, 2, 3 or 4 designating the asynchronous
     communications adapter.  And, the variable "$" can be 1, 2, or
     3 designating another printer port.

     All output direct to the printer LPT# is redirected to the
     asynchronous adapter n, or to another printer $.  Another format,
     CMODE LPT#: =LPT#, disables any redirection to the printer
     designated by the "#".

     Before you can use the CMODE to redirect the parallel printer
     output to a serial device, you must initialize the asynchronous
     communications adapter by using the CMODE COMn format described 
     in Section 2.1 Setting Parameters.  If that serial device is a
     printer, your seial initialization command should also include
     the "P" parameter.

             
     NOTE: WHEN USED IN THE CMODE COMn FORMAT WITH THE "P" OPTION, OR
           IN THE CMODE LPT#: = COMn OR CMODE LPT#: = LPT$, THE CMODE 
           COMMAND CAUSES THE PRINTER AND ASYNCHRONOUS COMMUNICATIONS
           ADAPTER INTERCEPT CODE TO BE MADE RESIDENT IN MEMORY.