Greetings from MEL's Diner BBS!       (714) 686-1522


IP is a serial interrupt and port verification program. Just run "ip" and the
program will check the RAM bios data area to see what port addresses your 
system is currently aware of. The program will then run a diagnostic routine
to discover any additional ports, and update the data area accordingly. In the
meantime, IP will also tell you which IRQ's are being used by what ports. 

NOTE: IP does not assume that address 0x3F8 is connected to IRQ3, 0x2F8 to 
IRQ4, etc... as several other serial port diagnostic utilities do. IP acually
enables the 8250's interrupts and does a functional check of the 8259 interrupt
controller chip and it's associated circuitry. In doing so, IP determines 
exactly which hardware ports are connected to which IRQ's.

IP will now take a command line switch (/n or /x). The /n (default) switch tells
IP to check standard IBM port addresses (3F8h,2F8h,3E8h,2E8h). The /x switch 
will allow IP to look for additional addresses which are sometimes used in non-
standard hardware schemes. The /x switch should be used with caution as some
non-standard hardware layouts will crash unexpectedly when one of these add-
itional port addresses are searched by IP. 

EXAMPLE:

Interrupt and Port Verifier (serial) - Version x.xx
Copyright (C) 1990-1991, AM Research Co.

Bios reports --> COM1:3F8 COM2:2F8  2 serial ports

PART#  BASE RD IE ID LC MC LS MS SP LSB MSB  IRQ (XT) IRQ (AT) INT  VECTOR
											 01234567 89ABCDEF
8250-B 3F8: 00 00 01 03 00 62 08 FF 030 000  00001000 00000000 0Ch 119C:032A
8250A  2F8: 0D 00 01 03 00 60 F0 00 030 000  00010000 00000000 0Bh 119C:02A2
16550A 3E8: 00 00 01 03 00 62 30 00 006 000  00000100 00000000 0Dh 119C:02FA

3 serial ports found!  Updating bios data area.


EXPLANATION:

The first info line after the copyright notice tells us that the system
bios data area (RAM) thinks that there are two serial port addresses in-
stalled in the computer under test. These addresses are found by the bios
POST routines when the system is first booted. Many older bios test routines
only check for COM1 and COM2 as the example shows.

After reading the bios, the program prints a list of each port address that
it found to contain a serial port. Each line will begin with the part number
of the UART chip which was found. After the part number the port address is
shown followed by the contents of the port's ten readable registers. The 
values displayed may make more sense if you check the 8250 data sheet for
register descriptions, etc. 

Following the register values is a list of 1's and 0's indicating which 
hardware IRQ the port in question is connected to. This is the place to look
if you are having a problem that you suspect is due to an IRQ conflict.
Generally speaking, it is ok for two ports to share the same IRQ as long as 
your work only uses one of the hardware devices at at time.

After the IRQ block is the interrupt number and vector of the ISR that will
be called to service the port if an interrupt is generated. Note that almost
all serial ports will have their interrupts turned OFF at the time you are
performing the test. The interrupt vector that is displayed will probably be 
changed by an application that enables the port's interrupts. 

It is very important for the operator to realize that IP is a diagnostic
utility which is meant to be used in checking/troubleshooting a newly modifed
or questionable computer. As such, IP may therefore interfere with the system's
operation as it actively enables and operates each port's interrupt circuitry. 

IP will probably NOT work properly if you have loaded any type of software that
activates the port's interrupts such as fossil drivers, etc. IP may very well
cause a crash if used with any type of multi-tasking software.

Finally, IP will modify the bios data area to report any additional ports it
discovers.

I would be quite interested in hearing from anyone with comments, suggestions,
crashing reports, etc...

As you might imagine, IP remains Copyright (C) 1990-1991, AM Research Co. 



Hope you enjoy using it.


												  bye for now...
													  
													  MEL



HISTORY

Version 1.22 - Fixed bug in the bios data area update routine. (It didn't
			   always update it!)

Version 1.21 - Fixed bug whereby NS16550's and NS16550A's wouldn't produce 
			   an interrupt if the fifo buffers were activated. Also added
			   NS16552 detection.

Version 1.20 - Added extended base addresses. Also protected system from the
			   isr test if interrupts are already activated.

Version 1.10 - Rewrote the isr. Works much better now.

Version 1.04 - Yet more bugs.

Version 1.03 - More minor bugs.

Version 1.02 - Minor bug fix.

Version 1.01 - First release.