Reprinted Article From The Oct 17, 1989 PC Magazine Advisor Column


           By: Lori Grunin                 Title: Beyond COM2


        LETTER:

        I've  been stumped by IBM's design limit for serial  ports.   I'd
        like  to add a COM3 and COM4 beyond the two already installed  in
        my 386 clone.  I put the new board in and properly set the  jump-
        ers,  but when I attempted to set the  communications  parameters
        via DOS's MODE command, I got "illegal device" error messages.

        I've looked for books to tell me how to get around this  problem,
        but to no avail.  Is there a software driver that I must  install
        to effect valid operation of these ports?

            Thomas Emery
            Goleta, California

        RESPONSE:

        IBM's original PC architecture supported only two COM ports,  and
        although compatible makers, and eventually IBM, added more serial
        capability, there are still no standard addresses or IRQ  (Inter-
        rupt Request) lines for the additional ports.

        The addresses for COM1 and COM2 are 3F8h and 2F8h,  respectively,
        with COM1 on IRQ4 and COM2 on IRQ3.  When you install more serial
        ports, COM3 usually uses 3E8h and IRQ4, while COM4 uses 2E8h  and
        IRQ3.   Unfortunately, some I/O card makers like to  blaze  their
        own  trails; IBM even added uncommon COM port addresses and  IRQs
        to the long list of PS/2 eccentricities.

        The  DOS MODE command doesn't work with serial ports  above  COM2
        because  DOS gets its I/O information from the BIOS, which  finds
        out  what's  installed where in your system during  the  Power-On
        Self-Test  (POST).   The POST checks only for the first  two  in-
        stalled ports.

        To  get  around this problem, communications  software  and  some
        serial  peripherals  (such  as mice)  will  occasionally  support
        higher COM ports by addressing them directly, rather than  making
        DOS function calls.  Of course, if your peripherals don't support
        these  extra  ports or you need to redirect data using  the  MODE
        command, that's where trouble arises.

        There  are a couple of public-domain utilities that allow you  to
        append  your COM port information to the BIOS, making  the  ports
        DOS-accessible.   COMSET (COMSET.ARC) and Port  Finder  (PF2.ARC)
        are available in the "general hardware" data library of the IBMHW
        forum  on Compuserve; Port Finder can also be obtained  from  its
        author,  mcTRONic Systems (7426 Cornwall Bridge Ln., Houston,  TX
        77041;(713)462-7687).
 





        Both  packages activate COM3 and COM4 (if they're  installed,  of
        course),  and  require DOS 3.3 or later.  They basically  do  two
        things: activate the extra ports by giving the BIOS the  address-
        es,  and provide utilities for swapping the addresses  among  the
        different  ports.   Address-swapping allows programs  that  don't
        support  COM3  and COM4 to access them.  Software  that  directly
        addresses the ports will usually be unaffected.

        Keep  in mind, however, that you probably won't be able  to  swap
        two ports that share an IRQ (such as COM1 and COM3) if you've got
        a  mouse  attached to one of them, because the  system  will  get
        confused when the interrupt triggers.

        Port Finder is the more flexible of the two.  In addition to  the
        aforementioned  features, it provides the same  capabilities  for
        LPT3,  including swapping among printer ports.   Furthermore,  it
        lets you easily restore all your original settings.

        Even if you think you've correctly configured the board, it can't
        hurt  to  double check a couple of things.  If you've got  a  bus
        mouse,  for instance, make sure that you're not stepping  on  its
        IRQ; although interrupt sharing is one of the touted features  of
        the PS/2, PCs can't do it very well.

        Also, don't leave any port holes-if you've got three, they should
        be COM1,COM2, and COM3, not COM1,COM2, and COM4. [END]
 





           Excerpt from July 1990 issue of "Vulcan's Computer Monthly"


                        10 Indispensable Online Utilities


        Commentary by Ron Albright


             Heaven  knows  that  the communication  voyager  has  enough
        problems  to deal with to find the jewels that  await  successful
        connections.   Incompatible  baud speeds, word length,  and  stop
        bits,  noisy  phone lines, busy signals, and  other  frustrations
        stand  in our way almost at every turn.  We battle  on,  however,
        knowing  that once we succeed, a wealth of information and  soft-
        ware awaits.

             Fortunately, there are several tools that every good  commu-
        nications  should  be aware of and keep in  their  armamentarium.
        This  article  will  examine 10 of these gems.   Each  handles  a
        specific problem the electronic journeyman faces, and  alleviates
        it to a large degree.  Here are my picks.


        PORT FINDER ...


             As you are probably well aware, setting up a PC for communi-
        cations is not a walk in the park.  The first battle you face  is
        getting  a modem to coexist with your current hardware.   If  you
        are  like me, and have more hardware hanging from  your  computer
        than  you can manage, you can run into problems right  there.   I
        for  example,  currently (it changes from week to  week)  have  a
        Logitech  ScanMan  Plus and Trackman connected  as  Bus-  devices
        (their own cards rather than using my serial ports), a voice mail
        board,  and an internal modem configured as COM3.  Since  the  PC
        handles  any hardware device through an "interrupt" ("IRQ"),  you
        can quickly run into conflicts that immobilize devices.  You  end
        up  doing  the "jumper shuffle," changing those  little  jumpers,
        replacing  the  boards, re-booting, and  crossing  your  fingers-
        hoping to find a montage that works.

             Well  with  "Port Finder" (mcTRONic Systems,  7426  Cornwall
        Bridge  Ln.,  Houston,  TX   77041;  (713)  462-7687;  Shareware,
        $13.95),  at  least some of the guesswork  is  eliminated.   PORT
        FINDER  is  a  very versatile program.  It   will   display  your
        computer    type, BIOS date, DOS version, display adapter   type,
        total  base   memory , extended memory, expanded memory  and  EMS
        version.    It will  detect  and  display  COM1 to COM4 and  LPT1
        to  LPT3  ports  that are  responding  with  the actual  HEX  ad-
        dress.   Because  PORT  FINDER displays  the  HEX port  addresses
        you  can also use PORT  FINDER  as  a diagnostic tool.   You  can
        swap   COM or LPT ports addresses instead  of  swapping   cables.
        On  AT systems Port Finder will check to see  if  a game port  is
        present and if so it will be added to the equipment list.
 





             If   you are using DOS 3.3 or higher  and have COM3   and/or
        COM4, PORT FINDER will  activate  both  COM3  and/or  COM4.   DOS
        will then recognize these ports and you will be able to  use  the
        DOS  MODE command.  Most system information type programs such as
        the  Norton  Utilities  System  Information   (SI)  program  will
        correctly   indicate  the number  of serial ports that  you  have
        including  the  COM3   and/or  COM4 ports   after  you  run  PORT
        FINDER.   Any other  programs that   operate through  DOS  should
        also  accept  COM3 and/or  COM4 after you run  PORT  FINDER   (if
        the  program does not allow you to enter COM3 or COM4   then  you
        will need to swap COM3 or COM4 with COM1 or COM2 before  you  run
        such  a program then select either COM1 or COM2 in said program).
        If  you   have  a new IBM PS/2 computer COM3  and/or   COM4  will
        already   be activated  .  You can use PORT FINDER to reset  both
        COM  and   LPT   port  addresses  in    case  you  forget    what
        addresses  have  been  swapped.

             PORT FINDER can also be used in a BATCH file to detect which
        COM  ports are  present. An  Errorlevel is  set for all  possible
        combinations.   An example batch file COMMTEST.BAT  is  included.
        Port  Finder will work under Microsoft Windows and a .PIF in  now
        included  with Port Finder.  Due to the fact that Desqview  moves
        the  COM and LPT port addresses to a nonstandard  location,  Port
        Finder will not be able to properly work when Desqview is loaded.

             For those, like me, who find themselves swapping hardware in
        and  out  of a machine with great regularity, Port Finder  is  an
        indispensable  tool  for managing your ports.   I  couldn't  live
        without it.


        PKZip ...                       TELEDISK ...

        PKware, Inc.                    Sydex
        7545 N. Port Washington Rd.     153 North Murphy Ave.
        Glendale, WI  53217             Sunnyvale, CA  94086
        414-352-3670                    408-739-4866
        Shareware, $47                  Shareware, $25

        LIST ...                        MSGVU ...

        Vernon Buerg                    Dave Briccetti and Associates
        139 White Oak Circle            P.O. Box 1713
        Pateluma, CA  94952             Lafayette, CA  94549
        $29.95                          Shareware, $30

        VDE ...                         Elsewhere ...

        Eric Meyer                      INTERLINK TECHNOLOGIES
        401 12th Ave SE - # 139         1222 5th Street
        Norman, OK  73071               Sarasota, FL  34236
        405-329-5777                    Updates $20
        Site Licenses $50
 





        ZMODEM ...                      Checkup ...

        Omen Technology Incorporated's  Levine & Associates
        17505-V                         9405 Bustleton Ave.
        Northwest Sauvie Island Road    P.O. Box 14546
        Portland,  Oregon  97231        Phila., PA  19115
        Shareware, $20                  215-333-8274
                                        $24.94


        Procomm 4.2 ...

        DataStorm Technologies
        P.O. Box 1471
        Columbia, MO  65205
 




        Reprinted From PC Computing January 1991, Prime Time Section


           Going Fishing For Shareware? Pack an Online Tackle Box


        by: Wendy Taylor


        . . .

           Some communications programs let you use only  COM1 or 2, Port
        Finder, a utility from  mcTRONic Systems  ($13.95;  7426 Cornwall
        Bridge Lane,  Houston,  Texas;  713-462-7687)  lets your software
        address   COM3 and 4   as well.    It  saves  you  the  hassle of
        reconfiguring your software or swapping cables.

        . . .
 



        Reprinted From The Power User's Tool Kit 1.0 - August 1990


          MicroWAREHOUSE Presents The Power Users's Tool Kit 1.0


       Compiled by: Rick Ayre

       . . .

       PORT FINDER

       James McDaniel's  Port Finder is one of my favorite Shareware pro-
       grams.  Couple  my love for  communications  with this easy to use
       program and its ability to solve port conflicts on  almost any PC,
       and you can see why.  This is one of those  programs that was ori-
       ginally written  because the  author  needed a tool,  and couldn't
       find it.  Today, I'm happy for all the frustration  that drove him
       to create Port Finder.  In this recent release, it not only sniffs
       out ports, both serial and parallel, but allows the initialization
       of com 3 and 4 if available.  It will also let you  swap any legal
       ports.  This version comes with a device driver that can be loaded
       into your config.sys file to configure your ports as you like.

       . . .

 



        Reprinted From The CPC Newsletter - New Canaan, CT - January 1991


                                The PC Chronicles


        by: Edward L. Kivell


        . . .

           One of the most useful shareware programs that I've run across
        in quite some time is Port Finder.    This is a Comm (serial) and
        LPT (parallel) port utility program.   It will activate Comm 3 or
        4 on  those computers  with those  ports and  DOS 3.3  or higher.
        Additionally,  it allows all possible Comm to Comm and LPT to LPT
        port swaps.  The program works flawlessly.  Through this program,
        I have been  able to activate Comm 3 on my PC and assign my fax /
        modem to that port.  By placing a single command in my "AUTOEXEC.
        BAT" file,  Comm 3  is turned  on without  my worrying  about it.
        Rather than pull  and switch serial cables because several serial
        devices have  to share  Comm 1 or 2,  you can use  Port Finder to
        swap  the  ports.  The shareware fee  is only $13.95 so you don't
        want to be without this utility.

        . . .

 



                Reprinted From PC SOURCES - FEBRUARY 1992 ISSUE


                                    FORUM

        By: Barry Brenesal

        . . .

        Port Finder  is one of those  utilities that you seldom need, but
        when  you do  , it's a  godsend.   It overcomes the  IBM's design
        limitations,  which  prevent  the  use of all but  COM1 and  COM2
        serial  ports.   If  these  ports  in  your  system  are  already
        assigned,  and your peripherals or  programs won't address higher
        ports directly,  Port Finder actvates  your COM3 and COM4  ports.
        It also  performs all  possible  COM  and  LPT  port  swaps,  and
        displays port addresses and basic system information.

        Port Finder: mcTRONic Systems, James D. McDaniel, 7426 Cornwall
        Bridge Ln., Houston, TX  77041, 713-462-7687.

        . . .

 



        Reprinted From PC Computing's Guide to SHAREWARE - (C) 1992 by ZD

                                    APPENDIX B

        By : Preston Gralla

        . . .

        If  you  have  a complicated  hardware setup,  you may  run  into
        problems  using your  COM ports.   For instance,  what do  you do
        when  you  need  to  use   COM3   for  communications,  and  your
        communications software can only use COM1 or COM2?  The answer is
        to get Port Finder, which will let you use COM3 and COM4.

        . . .

        Port Finder
        Registration fee: $
        mcTRONic Systems
        7426 ornwall Bridge Lane
        Houston, TX  77041
        (713) 462-7687
 


        *****************************************************************
         NOTICE  NOTICE  NOTICE  NOTICE  NOTICE  NOTICE  NOTICE  NOTICE
        *****************************************************************


        All  Port Finder  articles are  unmodified except for their price
        reference, which will be the  latest price including  shipping in
        the USA.    The prices  were changed  to avoid  confusion.   Most
        articles included information about other programs which has been
        left out here.  Only that portion about Port Finder is included.