ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 ºSTOP! ARRET! ALTO! HALT! STOP! ARRET! ALTO! HALT! STOP! ARRET! ALTO! HALT!º
 º                                                                          º
 º                    This program can harm your HARDWARE...!               º
 º                        YOU USE IT AT YOUR OWN RISK !!!                   º
 º                      ABSOLUTELY NO LIABILITY ACCEPTED !!!                º
 º                                                                          º
 ºThe program will not run without the appropriate parameters, so there is  º
 ºLITTLE risk that you will run it accidentally. But be very careful if you º
 ºcall it from a batch file...!                                             º
 º                                                                          º
 ºSTOP! ARRET! ALTO! HALT! STOP! ARRET! ALTO! HALT! STOP! ARRET! ALTO! HALT!º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
 
 
                              PORTS.EXE
                              ÄÄÄÄÄÄÄÄÄ

                         (Ver 1.3 - 19 Sep 91)



                     Copyright (c) and developed by

                              Jos‚ Campione
      2415 SouthVale Cr. U-25, Ottawa, Ont. K1B 4T9 (613) 523-4345.

                                   and

                          C. Robert Parkinson
           5 Ramsgate, Ottawa, Ont. K1V 8M4, (613) 523-7299.


               Program suggested by Micheline Johnson
          (who also worked out the details for example #4).

                                *  *  *

 NOTICE
 ÍÍÍÍÍÍ

     This program and every file distributed with it are copyright (c)
 by the authors, who retain authorship both of the pre-compiled and 
 compiled codes.  Their use and distribution are unrestricted, as long
 as nobody gets any richer in the process.  Although these programs 
 were developed to the best of the authors abilities, no guarantees
 can be given as to their performance.  By using them, the user
 accepts all risks and the authors decline all liability. 



 INTRODUCTION
 ÍÍÍÍÍÍÍÍÍÍÍÍ

     PORTS.EXE is a small utility to read and/or write a byte or 
 word value of an input/output (I/O) port.  This ability will enable 
 you to alter some of the defaults for your system operation.  In 
 particular, this program was designed to allow you to view and/or 
 alter the CMOS configuration values in 80286 and higher systems, 
 although it can be used for other purposes (see the WARNING below). 

     For those users who are not familiar with the Intel/Microsoft
 I/O port address structure, please read the BACKGROUND section below
 BEFORE you use this program.



 WARNING
 ÍÍÍÍÍÍÍ

     This utility can alter the basic operation of your system.
 DO NOT use it to write to the ports unless you thoroughly understand
 what you are doing.  In particular, DO NOT write to any port which
 is concerned with disk operations.  An incorrect value in another
 location may crash your system, but an improper value in these
 locations may corrupt your disk.  Be very careful to not get 
 confused between decimal and hexadecimal values.  

     Merely reading a port may also disrupt your system operation,
 although it will not harm any hardware.

     You have been warned!



 SYNTAX
 ÍÍÍÍÍÍ

     PORTS.EXE uses five possible first parameters.  The "u", "a"
 and "w" parameters, while they may be useful in other circumstances,
 were specifically created to deal with the CMOS RAM settings in 286
 and higher systems.  The parameters are:

         i = In (from port).
             Input/display a single byte from a port.

         o = Out (to port).
             Output/send a single byte to a port.

         u = Out/In (to port 1/from port 2).
             Output/send a single byte to a port, followed
             by an input/display from a second port.
             The optional parameter "#xxxx" (see below)
             permits a delay of xxxx milliseconds to be
             inserted between the two port accesses. 

         a = Out/Out (to port 1/to port 2).
             Output/send a single byte to a port, followed
             by an output/send of another byte to a second port.
             The optional parameter "#xxxx" (see below)
             permits a delay of xxxx milliseconds to be
             inserted between the two port accesses. 

         w = Word out (to port).
             Output/send a 2-byte word to a port.


     Usage:
     ÄÄÄÄÄ

         C:\> PORTS i $INWORD <!>

         C:\> PORTS o $OUTWORD <byte value> <!>

         C:\> PORTS u $OUTWORD <byte value> $INWORD <!>

         C:\> PORTS a $OUTWORD <byte value> $OUTWORD <byte value> <!>

         C:\> PORTS w $OUTWORD <word value> <!>


       Where:

       - INWORD and OUTWORD are port addresses.  These are not in the
         normal "segment:offset" form, but rather they are in terms of
         an "absolute" port address (e.g., "$061" for the speaker).
         The addresses can be entered as hex or decimal numbers,
         but hex addresses must be preceded by the "$" sign. (This is
         Pascal's way of indicating a hex number).

       - <byte value> or <word value> is the decimal or hex value
         that you wish written to the port.  Hex values must be
         preceded by the "$" sign.

       - The optional "#xxxx" parameter will only function with the
         first parameters "u" and "a", when making two successive
         calls to ports.  In the syntax for this parameter, "xxxx"
         represents any decimal number between (and including) 0 to
         9999.  A string  representing a number within this range
         will cause a delay of "xxxx" milliseconds between the first
         and the second port call.  Any string not representing a
         number within that range will cause this parameter to be
         ignored (i.e., no delay between the port calls).
         
       - The optional "!" parameter causes the display on the screen 
         of the value of the last input/output byte in decimal, hex 
         and binary formats.  It will also display the delay value
         if "#xxxx" was used.

       - Any positive integer below 65536 (0 to 65535 decimal, or 
         $0 to $FFFF hex) is a valid word.  Similarly, any positive
         integer below 256 (0 to 255 decimal, or $00 to $FF hex) is a
         valid byte.  When entering bytes or words, $DF is equivalent
         to $00DF and both are valid either as bytes or as words. 

       - Note that parameter "u" causes two successive calls. The 
         first one is similar to a call using parameter "o" and the 
         second one is similar to a call using parameter "i". 
         Similarly, parameter "a" makes two successive calls 
         equivalent to two separate calls using parameter "o".
         Our testing on several systems has determined that these two 
         successive calls (as, for example, those required to access 
         the CMOS) could not be carried out by two successive
         individual commands from the DOS prompt.  They require a
         special "single step" operation with a single call to PORTS.



 CMOS CONFIGURATION
 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

     For 80286 and higher systems, configuration information is held
 in battery-powered CMOS memory that retains the information even
 when the computer is switched off.  That information, originally
 entered through the software setup program, can be altered with
 PORTS.EXE.  However, to do so you must know the CMOS address and the
 desired value.  To display bytes in CMOS, use "PORTS u" (as in the 
 example below).  To change a CMOS value, using the example below,
 simply use "PORTS a" to output the CMOS address (byte) into port 70h
 and output the desired byte value into port 71h.


 Example:
 ÄÄÄÄÄÄÄ
                C:\>PORTS u $70 $14 $71 !

         This line causes the following display:

                Port byte = 35d, 0023h, 00100011b.
         
         Similarly, the same command line can be entered using decimal
         notation as:

                C:\>PORTS u 112 20 113 !

         which would have caused exactly the same display.

         This command outputs byte $14 (a CMOS address) to port $70
         and requests the input of the value currently held at that
         CMOS address from port $71, which in this case happens to
         contain byte $23.  In this example, the displayed byte
         is the equipment byte held in the CMOS.  You can interpret
         it as follows, remembering that bit 0 is the rightmost bit:

         Bits 6,7:      00 - 1 floppy drive
                        01 - 2 floppy drives

         Bits 4,5:      00 - No monitor, or EGA or better.
                        01 - 40 column, color.
                        10 - 80 column, color.
                        11 - monochrome.

         Bits 2,3:      (not used)  

         Bit  1  :      0  - math coprocessor not installed.
                        1  - math coprocessor installed.

         Bit 0   :      0  - No floppies installed.
                        1  - 1 or more floppies installed.



 ERRORLEVELS
 ÍÍÍÍÍÍÍÍÍÍÍ
 
     In all cases but one, the byte being addressed is returned as an
 ASCII value in the exit errorlevel.  The exception is when using the
 "w" parameter (out a 2-byte word to a port), when the returned
 errorlevel will be 0.  This exit errorlevel capability makes PORTS
 well suited for use in a batch file.  Use "PORTS i" with an
 errorlevel test to confirm that this is the proper value to alter,
 then use "PORTS u" with another errorlevel test to confirm that it
 has indeed been changed to the value that you desire, branching to
 an error routine in either case if the correct errorlevel is not
 returned.



 BACKGROUND
 ÍÍÍÍÍÍÍÍÍÍ

     The term "port" has two meanings, so this needs to be cleared
 up first.  From a user perspective, "port" is normally thought of
 as being a hardware connector.  The user is likely to consider that
 he has, for example, two serial ports, one parallel port and,
 perhaps, a mouse port and a game port.  However, to a programmer
 the term "port" implies an access point to facilitate data
 transfer, in other words, an input/output (I/O) address.  To
 contrast the two meanings, consider that one serial "port" has, in
 fact, eight separate but integral I/O "ports".  This document is
 concerned solely with the I/O address meaning of the word "port".

     Any Intel 80x8x processor has two separate address modes, using
 the same addressing pins.  The first mode addresses memory (i.e.,
 normal RAM/ROM addressing).  The second mode, I/O port addressing,
 while it uses some of the same numerical addresses as for RAM,
 actually sends/receives the information to or from support chips
 (e.g., the timer, the keyboard controller, etc.) or peripheral
 devices (e.g., the disk controller, the graphics adapter, etc.).
 All programming languages have built-in methods of differentiating
 between the two modes of addressing.

     As we said before, I/O address ports are used by DOS for data
 transfer.  The values in these locations govern that part of the
 system which is external to the processor itself.  Therefore, the
 ports allow direct access to the hardware.  Through ports you can
 access components on the mother board, on expansion cards or even
 devices external to the system proper, such as modems, printers,
 etc.  Each port will have a different meaning for each particular
 device and the use of any given port varies from chip to chip or
 device to device.  Before using PORTS, check your technical
 documentation for the motherboard, the expansion card or the device.

     Although we normally speak of the ports as one generic class,
 they are actually divided into two types, CPU ports and DOS ports.
 CPU ports (also known as "logical" ports) are directly accessible to
 the CPU and govern such things as the speaker, keyboard, timer, disk
 access, etc.  DOS ports are normally accessible to the processor
 only through the use of DOS "interrupts".  They control high-level
 data transfer via "serial" ports (e.g., COM1) and "parallel" ports
 (e.g., LPT1).  Understanding this difference is essential for those
 programmers who write at the hardware level.

     There are many differences in the port addressing schemes used
 by various Intel processors, although newer processors are always a
 superset of older ones.  These differences are necessarily also
 supported by the specific ROM BIOS for that system type.  Because of
 these differences, compatibility is normally attained by interacting
 with the ports only through the processor itself or through DOS/BIOS
 interrupts.  But sometimes, in order to achieve a specific purpose,
 direct access to the hardware cannot be avoided; PORTS.EXE can do
 this for you.

     Each port has a specific port number, or address.  In a 16-bit
 bus system (8086, 80286 and above) this allows 65,535 ports (0 to
 FFFFh). As of 1990, only port addresses 000h to 3FFh had been
 assigned.  In an XT system, because of the 8-bit external bus, the
 ports are limited to a maximum of 1,024.

     Five kinds of operations are usually performed on ports:

     1) input (receive from port) a byte;

     2) output (send to port) a byte;

     3) output (send to a port) a byte and input (receive) a byte
        from a second port in one single operation; 
 
     4) output (send to a port) a byte and output (send to the same
        or another port) another byte in one single operation; and
      
     5) output (send to a port) a word (two consecutive bytes in one
        single step). 

     This last "word" operation is necessary because many hardware
 functions are triggered immediately by any operation on the
 applicable port.  Any attempt to send two consecutive single-byte
 values to this port would necessarily fail.

     Some port operations require two successive bytes sent to the
 same port, but the hardware may require a small delay between these
 bytes.  PORTS can interpose this delay if required.

     Many ports are "bit-mapped", in that each bit has a specific
 function.  For example, port 14h is the so-called "equipment byte",
 since it specifies, in bit values, the elementary hardware
 configuration of your system.  Similarily, port 61h uses only the
 first two bits to control the speaker, the remaining six being used
 for unrelated purposes.  Changing bit-mapped ports with PORTS is a
 complex operation, requiring the conversion to and from binary
 values.  See Example #3 below.  To assist in this conversion, you
 may wish to use the PC Magazine utility CONVERT.COM.

     There are also many anomalies in the way in which ports respond.
 These are dependent upon the hardware being addressed, the system
 being used, the manufacturer's design whims, etc.  As these
 anomalies are very much system-specific, trial and error (hopefully
 not too much error!) is the only sure test.

     This small technical background is NOT designed to make you
 familiar with I/O ports and their usage.  Please consult any
 reliable programmer's handbook.



 EXAMPLES
 ÍÍÍÍÍÍÍÍ

 Example #1 - Controlling the Speaker
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

     Your computer's speaker is controlled by bits 0 and 1 of the
 bit-mapped byte found at port 61h.  If both bits are set to 1 you
 will hear a continuous tone in the same frequency as the infamous
 DOS beep.  To vary the tone, programs must use ports 42h and 43h to
 tell the system programmable timer chip how to vary the output
 frequency.  That's beyond what we want to demonstrate here; we're
 just going to show you how to output sound.

     The remaining bits 2 to 7 of the byte at port 61h are uses for
 other purposes, so don't disturb these.  This means that we have to
 first find the existing byte at that port.  Do that with this
 command:

           "PORTS o $061 !"

     Now take the binary byte on the screen (e.g., 01001000 or 48h)
 and change it so that bits 0 and 1 are set to 1 (e.g., 01001011 or
 4Bh).  Make certain that you do not alter the other 6 bits.  The
 easiest way to do this conversion is to use the CONVERT.COM utility
 from PC Magazine, but you can do it manually using the technique
 illustrated in Example #3.

     If we just output the changed byte to port 61h, we will get a
 continuous tone and we will then have to output the original byte
 to turn it off.  But we can use the PORTS "a" parameter to do both,
 inserting a variable delay so that we can tell that our ports call
 does work.  Using the example byte, this is the command:

           "PORTS a $061 $04B $061 $048 #500"
    
     Change the "#500" to vary the duration of the sound.



 Example #2 - Initializing the Printer
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

     Here is a simple example to reset a printer connected to your
 system to the printer's built-in default settings, assuming that it
 is a parallel port Centronics-compatible printer.  It also assumes
 that your printer is addressed through LPT1.  While this type of
 reinitialization can more easily be done using your printer's
 built-in "escape" sequences, this example merely illustrates one of
 the capabilities of PORTS.  The third of the LPT1 I/O port addresses
 is the one that controls the initialization (INIT) line to the
 printer.  To initialize the printer we have to drop the normal +5V
 signal on that INIT line to 0V, then restore it to +5V again.  To
 do this with a software routine, we have to determine that specific
 I/O address for our system, then send two sequential values to that
 port; one to set bit 2 to zero, then one to set bit 2 to 1.

     However, since the INIT line has to be held low (0V) for long
 enough for the printer to notice, we must either use two separate
 PORTS "o" calls or, preferably, use a PORTS "a" call to the same
 I/O address but with a delay ("#xxxx") between the two calls.  Here
 is the routine:

    - To find the specific I/O address for your system, we will use
      DEBUG.  However, you could use any other memory editor.  At the
      DEBUG "-" prompt, enter "d 0040:0008".  The values in the first
      two bytes are the first LPT1 I/O address.  On our test system,
      DEBUG gave "BC 03".  Remembering to reverse the order, we get
      an I/O address of "03BCh".  But we want the THIRD I/O address,
      so we add 2 (in hex) to that, giving us "03BEh" as the INIT
      port address.

    - Now, we have to drop bit 2 to 0, then raise it to 1 again.  So
      we output binary 11101000 (232) to the port.  Counting from 0
      on the right, you can see that bit 2 is indeed a 0.  To raise
      bit 2 to 1, we then output binary 11101100 (236) to the same
      port.

    - We're ready to try our test.  Execute the following PORTS
      command, remembering to substitute your own I/O port address if
      it differs from 03BEh:

        "PORTS a $03BE 232 $03BE 236 #50!"


     Experiment with different values for "#xxxx" to find the minimum
 delay that your printer requires.  On the test system, for example,
 a delay as small as 1 millisecond was acceptable.



 Example #3 - Setting Bright Text Background Colours
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

     Try this test if your system has a CGA card.  Only use it if you
 have a CGA card, as it may not work with other adapters.  If your
 VGA or SuperVGA adapter is 100% EGA compatible (e.g., the ATI VGA
 Wonder) this test will work.  PORTS does not check for the adapter
 type.

     You can modify the blinking bit that causes blinking characters
 on the screen, so that, instead of blinking, it will enable the use
 of bright background colors.

     Most CGA cards can be accessed through port 03D8h ($03D8). The 
 configuration word of the CGA card can be obtained from the BIOS (it
 is the word at address $0040:$0065).  Usually, this word contains the
 value $3029 (if you look into this address using DEBUG, remember that 
 DOS inverts the bytes in a word), which in binary is: 


                    3    0    2    9 h
                 0011 0000 0010 1001 b
                             ^

     To toggle blinking, bit 5 has to be reset (indicated with the
 caret). This can be done by "ANDing" 3029h with $DF:


                    3    0    2    9 h
                 0011 0000 0010 1001 b

         AND                  D    F h
                 0000 0000 1101 1111 b
                             ^
                 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    3    0    0    9 h
                 0011 0000 0000 1001 b



     So enter the following:

             C:\>PORTS !

     And you'll get the ports message with the blinking string
 "WARNING!".

     Then enter:

             C:\>PORTS w $0D38 $3009 !

     If everything went smoothly, you'll see that the blinking of
 "WARNING!" has ceased and that, instead, it is being displayed on
 a bright background color. 

     To change your display back to normal, enter:

             C:\>PORTS w $0D38 $3029 !

     Or replace $3029 with whatever word was originally found at
 address $0040:$0065 in your system. 



 Example #4 - Denying Access to Drives
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

     For 286/386/486 systems only.


       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º                   CAUTION                          º
       º                   ÄÄÄÄÄÄÄ                          º
       º  This procedure, if improperly done, can result    º
       º  in your having great difficulty accessing         º
       º  your computer system.                             º
       º                                                    º
       º  Improper inactivation of a hard drive can be      º
       º  rectified by booting from a floppy diskette       º
       º  and restoring the CMOS from the setup diskette.   º
       º                                                    º
       º  Improper inactivation of floppy drives is of      º
       º  more concern.  If you have provided for no way    º
       º  of restoring the CMOS from the hard drive, then   º
       º  you'll probably need to return to your dealer.    º
       º                                                    º
       º  UNDER NO CIRCUMSTANCES inactivate all floppy      º
       º  and hard drives.  Should you do so, even your     º
       º  dealer will be very unhappy.                      º
       º                                                    º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


     There are several password protection programs that permit the
 hiding or disabling of one or more storage devices.  One limitation
 of these programs is that they can usually be bypassed by booting
 with a system (bootable) diskette from the A: drive. 
 
     To overcome this security limitation, it is possible to switch
 off the A: and B: drives by appropriate editing of the CMOS RAM. 
 
     The retrieval and input of the CMOS configuration setup
 information from and to the CMOS EEPROM chip can be done by using
 the PC Magazine utilities CMOSGET and CMOSPUT.  In a manual
 operation, the byte file generated by CMOSGET can be edited using
 any good binary editor and then uploaded to the system using
 CMOSPUT.

     However, PORTS permits a more elegant and practical approach:


 1) Back up the complete hard drive that you wish to hide.

 
 2) Make a copy of the CMOS RAM, using "CMOSGET > CMOS.DAT".

 
 3) Make a bootable system diskette with the following programs (in
    addition to the two hidden system files) on it, which will
    permit everything to be put back to normal if there are any 
    problems:
 
             COMMAND.COM  
             CMOSPUT.COM 
             CMOS.DAT  
             PORTS.EXE  

 
 4) Note the contents of your CMOS RAM at address 10h (floppy
    drives), address 12h (hard drives) and at addresses 2E,2Fh
    (checksum).  An example of the contents might be:

      - at address 10h, the value 24h (1.2M and 1.4M floppy drives).

      - at address 12h, the value F0h (single hard drive type Fh).

      - at address 2E,2Fh, the checksum value 04D4h. 

 
 5) To switch off the floppy drives, address 10h has to be cleared
    (subtract 24h) and to switch off the hard drive, address 12h has
    to be cleared (subtract F0h).  Therefore, switching off the
    floppy drives requires a checksum of 04B0h.  If you are switching
    off the hard drive, a checksum of 03E4h is required.

 
 6) Put the following batch files on the hard drive:
 
      FLOFF.BAT
      ÄÄÄÄÄÄÄÄÄ
 
      ports a $70 $10 $71 $00 !
      ports a $70 $2E $71 $04 !
      ports a $70 $2F $71 $B0 !
 
    and 
 
      FLON.BAT
      ÄÄÄÄÄÄÄÄ
 
      ports a $70 $10 $71 $24 !
      ports a $70 $2E $71 $04 !
      ports a $70 $2F $71 $D4 !
 

 7) Put the following batch files on the bootable floppy diskette:
 
      HDOFF.BAT
      ÄÄÄÄÄÄÄÄÄ
 
      ports a $70 $12 $71 $00 !
      ports a $70 $2E $71 $03 !
      ports a $70 $2F $71 $E4 !

    and
 
      HDON.BAT
      ÄÄÄÄÄÄÄÄ

      ports a $70 $12 $71 $F0 !
      ports a $70 $2E $71 $04 !
      ports a $70 $2F $71 $D4 !
 
 
 8) In the above examples, the CMOS RAM port addresses are $70 and
    $71.  The parameters following $70 and $71 are the CMOS RAM
    internal address and the data to be written there, respectively.
    The "$" is the Pascal representation for hex numbers, used by
    PORTS.


 To Turn Off the Hard Drive
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 
 8) Run HDOFF from the bootable diskette in floppy drive A:.  To 
    test whether you have been successful in hiding the hard drive,
    do a boot, without the floppy diskette in drive A:.  If your
    efforts have been a success, the computer will now find no hard
    drive, and will give the prompt:

          "Insert BOOT diskette in drive A:"

    After booting from the floppy drive, any request to log on to
    the hard drive causes the display of the DOS error message:

          "Invalid drive specification".


 9) To return everything back to normal, run HDON from the floppy
    drive and reboot.


 To Turn Off the Floppy Drives
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 
 10) Run FLOFF from the hard drive, and reboot.  The computer will
     not even check the floppy drives to see if they contain
     diskettes.  Instead, it will boot straight from the hard drive.
     A request to log on to one of the floppy drives, regardless of
     the presence of a diskette in that drive, causes the display of
     the DOS error message:

          "Not ready reading drive A
           Abort, Retry, Fail ?" 
 

 11) To return everything back to normal, run FLON from the hard
     drive and reboot.
 
                               *  *  *