A Quick Reference


                           CONEX VERSION 7.0a

                         Wed  06-07-95 12:07:34


                  Copyright (C) 1991-95 Erhard Hilbig



CONEX (Latin connection) is used to communicate between IBM compatible
personal computer and a host or between two IBM PCs.

These are the highlights of the program:

 o  The IBM PC can be used as terminal via COM1 - COM4, via Interrupt 14,
    FOSSIL, DECNET LAT, FTP TCP/IP, B&W TCP/IP, 3COM (BAPI) at a host.

 o  COM parameters like baudrate (50-115200), parity, full/half duplex,
    xon/xoff or hardware handshake can be set in CONEX.

 o  Files can be transferred without protocol, e.g. to save a session to
    disk.

 o  Several DOS commands can be used inside CONEX such as "cd", "del"
    or a DOS shell can be entered.

 o  All incoming characters can be sent to a printer.

 o  You can transfer files to and from the host via ZMODEM or KERMIT
    protocol using long packets and sliding windows.

 o  Tektronix 4010/4014/4105 and DEC VT52 - VT320 can be emulated. The
    crosshair in GIN mode can be moved by a mouse.

 o  Graphical output can be displayed on a HPGL plotter or transferred to
    other programs.

 o  Supports screen modes with up to 50 lines and 132 columns.

 o  Up to 20-30 pages of screen output can be scrolled back to screen and
    edited.

 o  All keys including the numerical keypad and mouse buttons can be
    programmed.

 o  Incoming characters from the port can be remapped by the user.

 o  Supports a phonebook

 o  The configuration of CONEX can be saved to an ASCII file, which can
    be protected by a password or CONEX can be patched by itself.

 o  Several sessions, especially net sessions, can be opened concurrently.

 o  CONEX is completely written in assembler and therefore very quick
    and small. The only file necessary to run CONEX is "conex.exe".


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± How to start CONEX ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

Simply start CONEX version 7.0a with

                conex [<number>|<host>] [<port>] [options]

Parameters
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

<number> - enter session 0 - 9 (default: 0)

<host> - connect to host in a network

   Case 1: Session <host> has been defined previously with <Alt-I>
           --> change to this session

   Case 2: Session <host> is undefined
           --> select the lowest session with empty host name
               or session 0, if none available.
               port is determined automatically (can be set with <Alt-Y>)

<port> - telnet port number (default: 23)


Options
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

/i<filename> - Load different ini file (default: conex.ini)
/m0          - Terminal screen is monochrome, menus and status line are
               coloured.
/m1, /m      - All screens are monochrome (can be used by LCD screens)


=> <Alt-S> - Save all current parameters or Patch conex

   The parameters are normally written to the file "conex.ini" and are
   automatically read again when you start CONEX. If you select a
   different name as save file you will have to activate it with the command
   line option "/i<filename>".

   The following parameters are saved: port parameters (<Alt-I>), packet
   parameters (kermit mode <I>-command), VT320-emulation (<Alt-M>), graphics
   enabled (<Alt-G>), plot parameters (<Alt-P>), help page (<Alt-H>) and
   status line (<Alt-L>) in the different sessions 0 ... 9 and the
   keyboard macros. The save file is an ASCII file which can be altered
   by a normal editor, see "tech.ref" for more details. It can also be
   encrypted with a password especially to protect the keyboard macros.

   Replacing the ini-file by the exe-filename (normally "conex.exe") will
   save parameters to conex.exe itself. Afterwards the INI-file is not
   automatically read, lest you force CONEX to read it with the /i-option.
   Password protection is not supported then.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Port Parameters ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

=> <Alt-I> - Initialize connection

   The following parameters can be modified

   Host:       Name of the host to which you are connected. It is only
               important if you are working on a network with LAT,
               PC/TCP, BW/TCP or 3COM (BAPI). Changing this parameter
               will automatically close the old session.

   Port:       Com, interrupt 14, FOSSIL, LAT, PC/TCP, BW/TCP,
               3COM (BAPI)

   Bits/parity:7 space, 7 even, 7 odd, 7 mark, 8 odd, 8 even, 8 none

   Duplex:     half - all entered characters are immediately displayed.
               full - the host echoes all received characters.

   more ...:   This allows you to change more parameters which are less
               important. These are:

   Prompt:     You can enter part of the prompt of the connected machine
               here. When you enter "return" in "edit mode" all
               characters following this prompt are transmitted.

   Answer:     This string will be transmitted, if the host sends ENQ
               (decimal 5).


COM PORT, INT 14, FOSSIL
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   Portnumber: 1, 2, 3, 4
                  COM1 ... COM4 if they exist. COM3 and COM4 can only be
                  used if they are defined in BIOS, otherwise you have
                  to set IO-ports and interrupts for these ports in
                  conex.ini. (See tech.ref for more details)

   Baudrate:   50, 75, 150, 200, 300, 600, 1200, 1800, 2400, 3600, 4800,
               9600, 14400, 19200, 38400, 57600, 115200 bits/second
                  Shows the speed at which characters are transmitted.
                  Int14 and Fossil don't support all speeds, they are
                  mapped to similar ones.

   Stopbits:   1, 2 - Number of stop bits that follow the end of a
                  character on a serial line. Normally this has not much
                  influence on a transmission.

   Handshake:  none     - no handshake
               hardware - Characters are only transmitted if pins CTS or
                          DSR are set (not with Int14).
               xon/xoff - XOFF=^S stops transmission
                          XON=^Q starts transmission again

   CONEX accesses the hardware of com ports directly, because this is more
   flexible. Some networks offer a resident Interrupt 14 driver (Int14)
   to allow communication programs to use the network connection.

   FOSSIL (Fido/Opus/SEAdog Standard Interface Layer) drivers exist for
   a couple of communication boards.


PC/TCP and BW/TCP
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   Telnet port: Default port is 23, some hosts use different ports for
                special purposes.

   Telnet timeout: How long do we wait for an answer during initial
               connection in milliseconds? This value may be increased
               for long distance connections.


   LAT (Local Area Transport) is used to connect PC and host via
   DECNET. A resident program called "lat" must be loaded before using
   this option. LAT is contained in DECnet-DOS which is available from
   DEC (Digital Equipment Corporation). This software has been tested
   with DECnet-DOS version 2.1.

   With PC/TCP you can make a telnet connection on ethernet. The PC/TCP
   kernel ("ethdrv") from FTP Software Inc. must be loaded before, it is
   not public domain. The program has been tested with version 2.04, 2.05
   2.11 and 2.2. PC/TCP is a registered trademark of

      FTP software, Inc.                   anonymous file server
      26 Princess Street                   vax.ftp.com (128.127.2.100)
      Wakefield, MA 01880
      (617) 246-0900

   BW/TCP has the same features as PC/TCP. The internet number (e.g.
   128.127.2.100) can be entered directly in hostname or the internet
   name can be resolved with a host file. Its location and name can be
   changed in <Alt-Y>, otherwise the "conex.exe" directory is searched
   for the file "hosts". Hostname resolution with a name server is not
   supported.

   BW/TCP is a product from Beame & Whiteside Software Ltd.

      Beame & Whiteside Software Ltd       Tel + Fax:
      P.O. BOX 8130                        (416) 648 6556
      Dundos, Ontario
      CANADA
      L9H 5E7


3COM (BAPI)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   CONEX supports BAPI (Bridge Application Program Interface) from 3COM.
   You must enter a host name.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Modem connections ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

=> <Alt-D> - Dial phone number

   Enter several phone numbers, which must be separated with <F3>

                    <number1>³<number2>³<number3>...

   Dial telephone number <number1>, if it is occupied try next number
   <number2> ...
   The macro which dials phone numbers can be changed as virtual key
   þDIA in <Alt-K>.

   It is also possible to enter an alias in this command, which is
   looked up in the file "phone" in the "conex.exe" directory by
   default. Its path and name can be changed in <Alt-Y>. <Pageup> or
   <Pagedown> give a list of alias names.

   The ASCII file "phone" can be created with a normal editor and must
   look like this:

   <Aliasname1> blank <Phonenumber1> ...
   <Aliasname2> blank <Phonenumber2> ...
   ...

   - Blanks are not allowed within numbers and names.


=> <Alt-B> - send Break

   Will send a break over the serial line (short break), if <Alt-B> is
   pressed twice, the signals RTS and DTR are dropped for a short time
   (long break). These commands are normally used to interrupt the
   connection between host and pc/modem. In the networks NOVELL, DECNET
   or TELNET a break is sent according to network standards.



ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Sessions ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

=> <Alt-0> ... <Alt-9> - change to another session

   Up to 10 different network sessions can be opened concurrently
   depending on the limit of the resident network software. Port and
   kermit parameter can be set differently in each session, the screen
   is saved and restored, too. These sessions can be directly selected
   with <Alt-0> to <Alt-9>.


=> <Alt-N> - change to another session with host Name

   All sessions are listed and can be selected with the cursor keys.
   The following indicators are used:
           Arrow = open session in a network
           Block = current session


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Terminal Emulation ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

The pc can be used as a normal terminal. The following modes can be
selected with function keys:


=> <F7> - normal mode

   All input characters are immediately sent to the host.


=> <F8> - edit mode, scroll back

   In this mode the screen can be scrolled back and modified with the
   cursor keys (<Home>, <End>, <Left>, <Right>, <Up>, <Down>, <Page up>,
   <Page down>, <Del>, <Ins>, <Ctrl-End> = delete to end of line). You
   can scroll back up to 20-30 screen pages. You can enter this mode
   with <Shift-Cursor keys>, too.

   With <Return> the cursor line is sent to the host and CONEX is
   switched back to normal mode. If a prompt has been defined with
   <Alt-I> for this session it will be stripped off. With <Esc> or <F7>
   you return to normal mode without transmitting anything.


=> <Alt-M> - change eMulation, character set

   The following DEC terminals can be emulated: VT52, VT100, VT102,
   VT220, VT320. Actually VT100 - VT320 only differ in the response to
   the terminal identification, nearly all ESC sequences of a VT320
   terminal are interpreted and the keyboard is set up accordingly.

   The keyboard corresponds to a DEC terminal like this:

                       Dec VT 100/200/300 series

                             function keys
  ÚÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³     F6     ³     F7     ³    F8      ³    F9      ³    F10      ³
  ³ <Shift-F6> ³ <Shift-F7> ³ <Shift-F8> ³ <Shift-F9> ³ <Shift-F10> ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  ÚÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³     F11    ³     F12    ³    F13     ³    F14     ³    Help     ³
  ³  <Alt-F1>  ³  <Alt-F2>  ³  <Alt-F3>  ³  <Alt-F4>  ³  <Alt-F5>   ³
  ³            ³            ³            ³            ³    <F11>    ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  ÚÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³     Do     ³     F17    ³    F18     ³    F19     ³     F20     ³
  ³  <Alt-F6>  ³  <Alt-F7>  ³  <Alt-F8>  ³  <Alt-F9>  ³  <Alt-F10>  ³
  ³    <F12>   ³            ³            ³            ³             ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

             edit keys                         numerical keypad
 ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ¿   ÚÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿
 ³   Find   ³  Insert  ³  Remove    ³   ³ PF1  ³ PF2  ³ PF3  ³  PF4  ³
 ³          ³   Here   ³            ³   ³ <F1> ³ <F2> ³ <F3> ³ <F4>  ³
 ³   <End>  ³   <Ins>  ³  <Del>     ³   ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
 ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄ´   ³  7   ³  8   ³  9   ³   -   ³
 ³  Select  ³ Previous ³   Next     ³   ³ <7>  ³ <8>  ³ <9>  ³  <->  ³
 ³          ³ Screen   ³  Screen    ³   ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
 ³  <Home>  ³ <Pageup> ³ <Pagedown> ³   ³  4   ³  5   ³  6   ³   ,   ³
 ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÙ   ³ <4>  ³ <5>  ³ <6>  ³  <*>  ³
                                        ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
                                        ³  1   ³  2   ³  3   ³       ³
                                        ³ <1>  ³ <2>  ³ <3>  ³       ³
                                        ÃÄÄÄÄÄÄÁÄÄÄÄÄÄÅÄÄÄÄÄÄ´ Enter ³
                                        ³     0       ³  .   ³  <+>  ³
                                        ³    <0>      ³ <.>  ³       ³
                                        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ


   In 8 bit mode codes between 128-159 have special meanings and
   the above function keys send 8 bit codes. 8 bit can only be selected
   with VT220 or VT320.

   Character set 1 (characters 33-127) and character set 2 (characters
   160-255) can be selected from ASCII, UK, graphic, German, Finnish,
   PC-8, multinational and user. The user character sets are defined in
   CONEX.INI.

   The <Backspace> key can be defined to send ^H (default) or DEL.

   Characters which reach the right margin are either moved to the next
   line (default) or overwrite the last character in the line. This is
   called line wrapping.

   <Alt-M> always resets VT320 emulation to default values.


=> <Alt-L> - change status Line and Screen mode

   Status line: (1) Normal status line (default)
                (2) Empty status line
                (3) Status line with column numbers
                (4) No status line

   Clock type:  (1) No clock (default)
                (2) Current time in status line
                (3) Time passed since current session was opened

   Screen mode: (1) 25 lines and 80 columns (default)
                (2) 43 lines and 80 columns (EGA)
                    50 lines and 80 columns (VGA)
                (3) User screen mode:
                    You can set the screen to maximal 50 lines and 132
                    columns text mode (!) in user mode. Before this
                    screen mode can be selected, parameters must have
                    been set in "conex.ini".
                    See "tech.ref" for a detailed description of
                    conex.ini and possible screen modes on Super VGA
                    cards or read the description of your graphics card.

   The selection can be saved with <Alt-S>.


=> <Alt-H> - Help

   This gives a list of all possible commands in CONEX, the keyboard
   layout of VT320 keys, the modified keys and last not least my address.
   Keys which have been replaced by a single key are marked with an
   arrow.

   Pressing a function key or Alt-combination will execute this command,
   normal keys quit the help screen. <Alt-H> always returns to the last
   help page, it is also saved in conex.ini.


=> <F10> - quit CONEX

   Answer "hang up" if you want to close a connection over the COM port.
   (Signals DTR and RTS are dropped, which may cause a modem or host
   computer to disconnect the line.) Network connections are always
   closed.

   If you changed any important parameters you will be asked to save them.


=> <Ctrl-Backspace> = DEL, <Ctrl-Return> = LF

   An unknown fact is that DEL (127) and LF (10) can be produced this
   way. Another way is to redefine keys using <Alt-K> or define
   <Backspace> in <Alt-M>.


=> <Ctrl-Num Lock> or <Pause>

   Stop output to screen, any other key resumes output to screen again.
   This command is executed by the normal keyboard device driver.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± DOS Commands ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

DOS commands can be executed nearly at any time using the alternate keys.


=> <Alt-C> - Change to drive:directory

   The current drive and/or directory can be set here, e.g. "c:\conex".

   All files which are received in "transfer mode" are stored in the
   receive directory. If no directory is given the current one is taken.


=> <Alt-E> - Erase file

   Wild cards cannot be used when entering the filename, but you can
   switch to a selection menu with <Page up>/<Page down>.


=> <Alt-X> - eXecute DOS commands

   Any valid DOS commands can be executed. But if you want to enter the
   DOS shell completely give <Return>. You return to CONEX with "exit".
   This command saves part of the data in extended memory (XMS) or in a
   temporary file, if not available.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Graphic Screen ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

The program can switch automatically into graphic mode when it receives
a graphic command and behave as a tektronix 4010, 4014 (monochrome) or
4105 (colour). The following graphic cards are supported: hercules, CGA,
EGA and VGA. The graphic card is automatically detected on entry to
CONEX.

This mode is only used to view graphics, so it is not as comfortable as
normal text mode. Some keys like Alt combinations will not work any more
in this mode.


=> <F5> - enter graphic mode

   Switch into graphic mode manually. The last graphic picture will be
   restored.


=> <Alt-G> - enter Graphic mode automatically

   When a graphic command GS, FS, US or ESC ENQ, ESC FF, ESC SUB is
   received CONEX will automatically switch into graphic mode. You can
   switch back to normal by pressing <F7>.

   In GIN mode the crosshair can be moved using the cursor keys; the
   shift key speeds up this movement. If a Microsoft compatible mouse is
   connected and the mouse driver loaded you can move the crosshair with
   the mouse as well.


=> <Alt-P> - write a Plot file

   If you press <Alt-P> before you start a graphic, it will be written
   to a file in HPGL format and can be plotted on a HPGL compatible
   plotter later on. Pagewidth, margins and velocity of the pen can be
   selected as well. Plots use the original resolution of a Tektronix
   4014 screen.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Writing Macros ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

=> <Alt-K> - write macro

Enter key

   All keys can be programmed if they are detected by BIOS (Int 11h)
   calls. Press <F4> and the key you want to redefine. Simple ASCII
   characters must be entered without <F4>.

   There also exist some virtual keys þIN0 ..., which must be
   entered using <F4>, <I>, <N>, <0>.

   þIN0  When a new session # is opened the corresponding macro IN# is
   ...   automatically started. On com ports a new connection is
   þIN9  determined from the presence of DTR and CTS.

   þLMB  Macro executed when the left mouse button is pressed.
   þRMB  Macro executed when the right mouse button is pressed.
         These macros only work in graphic mode. (<F5>)

   þDIA  Dial macro
   þNUM  contains the number which is currently dialed in <Alt-D>

Macro

   You can enter all characters from 32 to 255 here, only "þ","®","³"
   and "¯" have special meanings and are interpreted differently.

   Function, Alt and Control keys must be entered by <F4><key>.
   The interpretation of these keys depends on the original definition.

   1) The key has an original definition within CONEX
      -> Always execute the original meaning not the redefined.

   2) The key has no predefined definition within CONEX
      -> Execute the user's redefinition or ignore it.

   Macros can be called from within macros up to a level of 5.

   A time delay will be added to each character or <CR> if you change
   "char delay" or "line delay" in menu <Alt-R>. Execution of a macro
   can be interrupted with <Ctrl-Break>.

   A memory region of 10000 bytes is reserved for keyboard macros.
   Variables and functions are described below.

Label

   <Alt-H> lists the labels of all defined user keys. During the
   execution of a macro this label is also displayed in the status line.
   Labels will be ignored if you replace a key by a single key.

Examples

   Define the key <Del> to send DEL=127:

   1) <Alt-K><F4><Del><Return>  ;enter key you want to program (=<DEL>)
   2) 4 * <Del>                 ;to delete original definition
   3) <Ctrl-Backspace><Return>  ;enter new definition (=decimal 127)


   Define the key <F12> to act as <F10><Return>:

   1) <Alt-K><F4><F12><Return>  ;enter key you want to program (=<F12>)
   2) 4 * <Del>                 ;to delete original definition
   3) <F4><F10><F4><Return>     ;enter new definition (= <F10><Return>)
      <Return>

Don't forget to save the definitions with <Alt-S>.


Variables and labels
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Numerical variables

   There are two sets of variables: system variables A-Z and normal
   variables a-z. Variables can contain integer values from 0 through
   65535. System variables are set to 0 at the beginning of a macro.

   The following system variables have special meanings in some
   commands:

   E - ®E ...¯: return value of last evaluate command
       ®J ...¯: jump to label according to variable E
   M - ®S ...¯: return maximal number of strings
   S - ®S ...¯: select string according to S
   W - ®W ...¯: return result of last W-command

                            ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Labels          ®: <label> ¯

   Marks a label in a macro.
   Labels may consist of any two characters. The following labels have a
   fixed meaning and should not be used as a label:

        <-  restart macro         << restart current level
        ->  exit macro            >> exit current level

    If macros are not nested labels <- << and -> >> will behave in the
    same way.

    e.g.        ®:AT¯   marks label "AT"



Functions
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Function keys <F1>="®", <F2>="¯", <F3>="³" can be used to enter special
characters in macros.


Evaluate        ®E <expression> [³ <result>] ¯

        <expression>    <a> op1 <b> op2 <c> ...         where

                        <a>, <b>, <c>   is a-z, A-Z, decimal number
                        op1, op2        is +, -, <, =, >

                        a+b Ä-> gives sum of a and b
                        a-b Ä-> gives difference of a and b

                        a<b    ÚÄ 0  if expression is false
                        a=b Ä->³
                        a>b    ÀÄ 1  if expression is true

        <result>      Variable, where the result is stored. The result
                      is always stored in system variable E.


        e.g.    ®E0³S¯      sets Select variable S=0
                ®EW+1<4³r¯  if W+1 < 4  then r=1
                            if W+1 >= 4 then r=0

                            ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Jump            ®J <label0> [³] [<label1> ³ <label2> ...] ¯

        ®J <label> ¯
        Jump to <label> at all events

        ®J <label0> ³ <label1> ³ <label2> ... ¯
        Jump to <label#> according to value in variable E=#.
        If <label#> does not exist the next command will be executed

        e.g.    ®JAT¯       jump to label AB (marked as ®:AT¯)
                ®J<-³AT¯    if E=0 then restart macro
                            if E=1 then jump to label "AT"
                              else ignore command

                            ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Select          ®S <string0> ³ <string1> ... ¯

        Select string depending on variable S. If S=0 transmit
        <string0>.
        Returns variable M = maximal value of S allowed

                            ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Wait            ®W [*] [#] [³ <string1> ³ <string2> ...] ¯

        Wait until the host sends <string1> or <string2> or ... If #
        contains a number, we wait only for # secs else we wait
        indefinitely.
        With * characters from the keyboard are processed.

        Returns Variable W: 0 = timeout occurred
                            1 = <string1> received
                            ...

        e.g.    ®W5¯        Wait 5 seconds
                ®W³word:¯   Wait until "word:" is received
                ®W5³word:¯  Wait until "word:" is received or 5 sec timeout
                ®W*³þCR.¯   Enter characters from keyboard until a
                            Carriage Return is received.


=> <Alt-Y> - configuration of CONEX

   page length
     If > 0 page numbers are printed at the top with <Ctrl-print screen>

   host name (BW)
     Name of host table, only used with BW/TCP

   phone list
     File which contains alias names and phone numbers. (default: phone)
     see <Alt-D> for a description

   default port
     When the program is started in a network with "conex <host>" and a
     session <host> has not been defined, this port is taken by default.
     When set to "automatic", the presence of network software LAT,
     PC/TCP, BW/TCP, Netbios and 3COM (BAPI) are checked in this sequence.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Transfer of Files without any Protocol ±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

=> <Alt-W> - Write file

   Use this command to save all incoming characters to a file either to
   remember what you were doing or to transfer files. The transfer may
   be interrupted with the <Alt-W>.


=> <Alt-R> - Read file

   The file is transferred to the host as it is. You can convert each
   end of line = CR,LF to a single CR during transmission, as it is
   entered manually. The transfer can be interrupted with <Ctrl-Break>.
   The file can be executed as a macro, i.e. keys þ... and macro
   commands ®...¯ are interpreted as macros entered with <Alt-K>.

   A time delay may be added to each character or end of line, it must be
   entered in computer ticks of 0.0549 seconds. (18 ticks = 1 second).
   This time delay also affects keyboard macros.


=> <Ctrl-Print Screen> - print incoming characters

   All incoming characters are transferred to the printer. If a page
   length is defined with <Alt-Y> the printed pages will be numbered.
   Pressing <Control-Print Screen> twice produces a form feed and page
   numbering begins anew.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Transfer of Files with Protocol ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

You need a protocol to safely transfer files to/from your pc on an
unreliable connection and to transfer binary files because control
characters may get lost.

Enter file transfer mode with <F9> and select the file transfer protocol
with <I>. The default protocol is ZMODEM, which I think is the most
popular protocol in mailboxes.


Zmodem
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

=> <I> -Init parameters

   Escape control chars - If you consistently get CRC errors probably
      some Control characters get lost during the transmission. Try to
      escape all control characters.

   Overwrite files - conditions when files are transmitted otherwise it
                   is skipped
      if shorter - the existing file must be shorter or older
      if <> CRC  - the existing file must have different length or checksum
      no, append - the transmitted file is appended to the existing file
      always     - the existing file is always overwritten
      if older   - the existing file must be older
      if <> date - the existing file must have a different date or
                   length
      never      - there must not exist a file with the same name

   File must exist - only transmit a file if it already exists on the
      host.

   File type
      binary - binary files are transmitted as they are
      ASCII  - files are converted, i.e. CR,LF in DOS files is
               converted to LF on a UNIX host
      recover - if a file transfer had been interrupted before only the
               missing part of the file is transferred.


=> <R> - Receive files

   To receive a file you must start the sending program on the host
   first, e.g. "sz test", before pressing <F9> <r> <CR>. The received file
   will be stored in the receive directory if it is defined by <Alt-C>
   else in the current directory.

=> <S> - Send files

   Multiple files separated with blanks and "wild cards" can be entered.
   If you want to select from a file list, press <page up>/<page down>
   and select with <Ins> or <Del>.


Kermit
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

You must start kermit on the host and enter "server", "receive" or
"send", then press <F9> to enter local kermit mode to start the file
transfer.


=> <I> -Init parameters

   ASCII/binary file type - Binary files (files with characters over 127)
      should be transferred with file type binary. The host must be
      set to this mode, too, normally with "set file_type binary".
      Sometimes binary files can also be transferred with "parity none",
      which is quicker.

   packet length - maximal length of a received or transmitted packet
        including packet number, type and checksum. (default 2000)
        Values above 94 will be ignored if the host does not support
        large packets.

   window size - Size of a window. (default 1) Values different from 1
        will be ignored if the host does not support windowing.

        - If you want to speed up the transmission rate

          enlarge packet size <-- reliable connection
          enlarge window size <-- unreliable connection

          Enlarging both packet and window size does not make much sense.

   type of checksum - CONEX supports 3 kinds of checksums, which consist
        of 1, 2 or 3 bytes. (default 1) It might be a good idea to
        select a more exact checksum with large packet sizes and
        unreliable connections.

   more... - Change more parameters, which are less important.


   padding character - characters sent before any packets to synchronize
        transmission. (normally not necessary)

   quote control character - control character are quoted with this
        character, Control-A is coded as '#A'. (default #)

   quote 8-bit character - characters whose 8th bit is set are quoted
        with this character, hex A8 is coded as &H. (default &)

   Repeating - repeated characters are compressed in a packet.

   repeat character - 8 characters 'HHHHHHHH' is shortened to 3
        characters ~'H, 8 is coded as '. (default ~)

   packet terminator - Every packet is terminated with this character.
        (default = CR)

   Max number of retries - number of trials to resend a packet, which
      has been refused by the host. (default 5)

   Time out in secs - If the PC did not answer for the specified time
      the last packet will be resend. (default 5)


=> <S> - Send files

   Multiple files separated with blanks and "wild cards" can be entered.
   If you want to select from a file list press <page up>/<page down>
   and select with <Ins> or <Del>.


=> <R> - Receive files

   This command is used to get files from the host. If this file already
   exists on the PC the old one will be renamed to ".bak". The received
   file will be stored in the receive directory if it is defined by
   <Alt-C> else in the current directory.

   If the sender has already been told the name of the file ("send
   foo") simply press return when asked for "receive file". It is also
   possible to enter "wild cards" which are understood by kermit on the
   host.


=> <O> - lOg packets to disk

   If log is on all sent and received packets will be written to the
   file "conex.log". This feature is mainly used to trace down any bugs.


=> <F> - Finish server on the host

   Kermit on the host is terminated and CONEX changes back to
   normal mode.


=> <L> - Logout on the host

   Like "finish" but terminate session, too.


=> cursor keys

   Scroll the messages at the bottom of the screen.


=> <C> - Change directory on the host

   This and the following commands will only work if kermit on the
   host supports generic commands.


=> <D> - list Directory on the host

=> <E> - Erase file on the host

=> <M> - send a short Message

=> <N> - reName file on the host

=> <Q> - Query server status

=> <T> - Type file

=> <U> - query disk Usage

=> <W> - Who is logged in


=> During a file transfer the following commands can be used.

   <Esc> - interrupts transmission completely. This should be the last
           resort if nothing else works.

   <^F>  - interrupts the transfer of current file, the transmission
           proceeds with the next file.

   <^G>  - interrupts file transfer completely.

   <CR>  - resend last packet if transmission stopped


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Error characters ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

Some characters, which are output to screen, have special meanings:

Blinking character  - Parity or Framing error: A bad character was received.
                      Alter bits/parity if all characters are blinking.

rubout (²)          - Overrun error at COM port. The UART chip lost some
                      of the incoming characters.

up arrow (dec 24)   - Sender timeout: Characters could not be sent out.
                      In a network environment the connection is
                      interrupted.

down arrow (dec 25) - Receiver timeout: Characters could not be received
                      from remote host. The connection is interrupted.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Tips and tricks ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

Packet drivers & NCSA telnet
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

CONEX cannot use packet drivers directly to communicate over ethernet,
but you can use "net14.exe" from the NCSA telnet package.

(1) Extract config.tel and net14.exe
(2) Enter your parameters in config.tel
(3) Execute "net14 conex"
(4) Select "port: Int14" with <Alt-I>
(5) Enter <Ctrl-B> "Hostname" <Ctrl-C>


Define original DEC VT100/VT220 keyboard layout
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Since <Numlock> is only internally used by the BIOS, it cannot normally
be redefined. But there exist resident programs, which redefine
<Numlock>, e.g. "NM", which redefines <Numlock> to <F1> and
<Shift-Numlock> to original <Numlock>. NM100 is available at simtel
msdos\kermit.

The <,>-key is missing on a IBM keyboard, it must be simulated with
<Shift-+> on the numerical keypad.


      Dec VT 100/200/300 series           PC AT extended keyboard

   ÚÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿      ÚÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿
   ³ PF1  ³ PF2  ³ PF3  ³  PF4  ³      ³ Num  ³  /   ³  *   ³   -   ³
   ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´      ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
   ³  7   ³  8   ³  9   ³   -   ³      ³  7   ³  8   ³  9   ³   +   ³
   ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´      ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄ´       ³
   ³  4   ³  5   ³  6   ³   ,   ³      ³  4   ³  5   ³  6   ³ Sht + ³
   ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´      ÃÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
   ³  1   ³  2   ³  3   ³       ³      ³  1   ³  2   ³  3   ³       ³
   ÃÄÄÄÄÄÄÁÄÄÄÄÄÄÅÄÄÄÄÄÄ´ Enter ³      ÃÄÄÄÄÄÄÁÄÄÄÄÄÄÅÄÄÄÄÄÄ´ Enter ³
   ³     0       ³  .   ³       ³      ³     0       ³  .   ³       ³
   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ

Redefine the keyboard as follows

directly in conex.ini            using <Alt-K>

key="þNK/",,"þF02"             <F4></>        -->  <F4><F2>
key="þNK*",,"þF03"             <F4><*>        -->  <F4><F3>
key="þNK-",,"þF04"             <F4><->        -->  <F4><F4>
key="þNK+",,"þNK-"             <F4><+>        -->  <F4><->
key="þ#N+",,"þNK*"             <F4><Shift-+>  -->  <F4><*>
key="þNKE",,"þNK+"             <F4><Enter>    -->  <F4><+>


The positions of the EDIT keys on a VT220 keyboard are not the same as
on the IBM keyboard.

         Dec VT 200/300 series                PC AT extended keyboard
   ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄ¿   ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄ¿
   ³   Find   ³  Insert  ³  Remove  ³   ³ Insert   ³  Home    ³  Page    ³
   ³          ³   Here   ³          ³   ³          ³          ³   Up     ³
   ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄ´   ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄ´
   ³  Select  ³ Previous ³   Next   ³   ³ Delete   ³   End    ³  Page    ³
   ³          ³ Screen   ³  Screen  ³   ³          ³          ³  Down    ³
   ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÙ   ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÙ

If this is what you want redefine them as follows

directly in conex.ini                 using <Alt-K>

key="þINS",,"þEND"              <F4><Insert>   -->  <F4><End>
key="þHOM",,"þINS"              <F4><Home>     -->  <F4><Insert>
key="þPUP",,"þDEL"              <F4><Page up>  -->  <F4><Delete>
key="þDEL",,"þHOM"              <F4><Delete>   -->  <F4><Home>
key="þEND",,"þPUP"              <F4><End>      -->  <F4><Page up>


Examples of useful macros
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Simple automatic login procedure (could be defined as þIN0):

         ®W³id:¯HilbigþCR.®W³rd:¯draculaþCR.

®W³id:¯         Wait for "userid:", actually we only wait for "id:"
HilbigþCR.      Enter userid "Hilbig". (Don't forget CR)
®W³rd:¯         Wait for "password:"
draculaþCR.     Enter password "dracula".

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

A more complicated automatic login procedure (could be defined as þIN0):

         ®W10³led³id:¯®EW<2¯®J³->¯HilbigþCR.®W*³term=¯vt100þCR.

®W10³led³id:¯   Wait for "[user]id:"
®EW<2¯®J³->¯    If the connection times out after 10 seconds or we
                receive "[fai]led" the macro will be aborted.
HilbigþCR.      The userid "Hilbig" is entered.
®W*³term=¯      Enter the password from the keyboard (W*). If the host
vt100þCR.       asks for the terminal "vt100" will be entered.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Problems ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

I usually repair bugs as soon as a I hear from them, but there are
certain features which I could not test myself:

(1) VT320 and Tektronix 4105 emulation are not yet complete. If you
    encounter any problems contact me, so I can enhance the
    implementation. Send me a file catched with <Alt-W>.

(2) Netbios has not been tested, because I don't have any Netbios
    connections. So if someone liked to do some testing contact
    me.

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Past history ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

6.0   1st Public Domain Version in comp.binaries.ibm.pc

6.1   Default COM3/4 Interrupt = 4 and 3
      COM3/4 Interrupt + IO address configurable
      Up to 4 LAT sessions
      ESC FF, ESC SUB, ESC ENQ automatically switch into graphic mode (Alt-G)
      Support extended keyboard (esp. F11, F12)
      Rotate interrupts configurable in conex.ini
      Format of CONEX.INI changed!!!
      Dial sequences are saved in CONEX.INI
      Start initial macro at 1st opening of a session (<Alt-K>, þIN#)
      Characters from port can be remapped (<Alt-M>, character set: user)
      Conex can be patched (<Alt-S>, file name: conex.exe)
      Support B&W TCP/IP (<Alt-P>)
      ESC stops macros only in normal or graphics mode
      Alphabetically sorted output in directory listing
      Alphabetically sorted output of macros in help screen
      Multinational supplement character set implemented
      ESC ENQ supported in graphics mode
      Hercules graphic screen increased to 720 X 360 pixels

6.2   Default setting changed to bits/parity: 8 none, emulation: VT320-7
      Single key replacement is shown with <Alt-H>
      Support sliding windows/long packets in kermit file transfer
      Default kermit packet size = 2000 bytes (long packet)
      "ESC [" switches back from graphic mode to text mode
      Cursor type changes according to insert/overwrite mode
      Numbers can be entered directly in windows
      <Shift-TAB> can be programmed
      Support printer command under VT... emulation
      Features from VT320 emulation
      Support UART 16550A FIFO
      Answerback message implemented (<Alt-I>, more=yes)
      Support line drawing patterns in Tek mode (ESC `, ..., ESC e)
      "ESC [ ? 38 h" switches into graphic mode
      Characters in Tektronix mode are transmitted to HPGL file
      Telnet port and timeout made configurable (<Alt-I>)

6.3   Support NETBIOS (not yet ready)
      Added character/line delay in <Alt-R>
      Initial connection errors reopen <Alt-I> window automatically
      "conex <host>" connects to host (port is automatically detected)
      <Alt-D> redefined: dial number
      Replaced commands in macro language ®D ¯ -> <Alt-D>
                                          ®R ¯ -> ®W ¯
      New commands in macro language ®: ¯, ®E ¯, ®J ¯, ®S ¯
      New keys programmable: NKE, NK/, ^NE
      "ESC 1", "ESC 2", "CAN", "ESC %!0" switch between VT320 and TEK mode
      BACKSPACE sends BS/DEL made configurable
      <Ctrl-Break> interrupts macros
      Added baudrate 14400
      Cursor can be positioned into 25th line (no status line)
      Display port/baudrate in status line if hostname is not specified
      Changed messages in "quit conex" <F10>
      Maximal length of host names increased to 32
      VT100 "delete screen" saves screen to scrollback buffer
      Scrollback buffer increased to 20-30 pages by compression
      Support 132 columns/50 lines on screen
      Left & right mouse button programmable in graphic mode
      3com (BAPI) supported
      User defined keys <Alt-K> disabled in EDIT mode
      Subset of Tektronix 4105 commands (enlarged on request)
      New kermit generic commands: Who's logged in + type file
      ESC sequence "cursor displayed/invisible" in VT320 supported
      New character sets PC-8, Finnish; characters 0-31, 128-159 definable
      Clock can be displayed in status line (<Alt-L>)
      COM port interrupts can be detected automatically
      Comments in conex.ini allowed
      New help screen with VT320 keyboard layout
      Graphic card definable in conex.ini

6.3b  New macro labels "<<"/">>" = restart/end current macro level
      Wrapping of lines can be configured with <Alt-M>

7.0   Graphics enabled as default
      ESC [ 3#,4# m sets ANSI colours directly (configurable)
      Read in macros directly from file <Alt-R>
      Packet length affects sending of packets, too
      Added ANSI and VT52 emulation
      conex/m# uses monochrome colours (eg. on LCD displays)
      <Ctrl-Spacebar> sends NULL
      <Alt-X> gives more memory (file/XMS)
      <Cursor up>/<Cursor down> don't move outside Scrollbuffer
      Reorganized screen in transfer mode (new colour!)
      Reorganized conex.ini to include keywords
      Support zmodem file transfer protocol
      On network errors open <Alt-I> or next session (configurable)
      Clock can display connect time
      FOSSIL support added <Alt-I>
      Convert CR,LF to CR during file input <Alt-R>

7.0a  Files "phone"/"hosts" looked up in directory of conex
      Receive file directory configurable <Alt-C>


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Future plans ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

o  FTP file transfer
o  direct access to packet drivers


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Distribution points ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

EMAIL
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The newest version is always available from me via email. Send me a
message.


ANONYMOUS FTP
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Look for the file on

 Simtel in directory </msdos/modem>
 garbo in directory </pc/connect>
 ftp.uni-koeln.de in directory </pc/msdos/commprogs>

or on our Novellserver

ftp nwftp.uni-paderborn.de    or    ftp 131.234.242.6
login: hrz/guest

in directory <\pub\comm>


MAILBOX
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

telephone number (+49) 5251/541334

per uucp       login:    nuucp
               password: nuucp

per fastlogin  login:    gast
               password: gast

in directory \archives\files\misc


COMPUSERVE
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
software:     <go ibmcom> comm programs get con70.zip (planned)
              Sorry, I did not succeed in uploading the program yet.
              They don't support zmodem and kermit did not work
              correctly.
mail to user: 100064,3655

Since I don't look up my mail at compuserve very often, it may take some
time till you get an answer. So better send me an Email from Compuserve.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Author ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        Erhard Hilbig
        Hochschulrechenzentrum
        Universitaet-Gesamthochschule Paderborn
        D-33095 Paderborn (Germany)

        Email:  zahilb@hrz.nw.uni-paderborn.de (preferred)
                zahilb@pbhrzt.uni-paderborn.de
        Phone: +49 5251/60-2433           Room: N2-316
        FAX:   +49 5251/60-2519


  This program has been developed by me and can be distributed freely,
  though I don't mind to get any donations. (Freeware) There is also a
  more detailed documentation in German available, which is written in
LaTeX. You can have it as LaTeX DVI file or as a print file, which must
                be output using "copy conex.lst prn/b".

    If you find any bugs or have an idea how to improve the program,
         send me a message! I love to get feedback from users.

 This software is provided "as is" without express or implied warranty.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³±±± Acknowledgements ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

                             Many thanks to

                 Jim Groeneveld and Martin B. Brilliant

   who tested my program and made lots of suggestions to improve it.