(tm)
                                      PC-VT


                                    VT100/102/52
                                         and
                                      4010/4014

                                  Terminal Emulator

                               (C) Copyright 1985-1990
                                  Mark C. DiVecchio
                          Athena Systems Development Group

                                    Version 10.0





















































                     PC-VT is dedicated to my mother and father
                       who, when they came to visit, could not
                     understand why I spent so much time tapping
                                 the keys of my PC.

                                                                      M.C.D.


















































          Forward


                  The PC-VT program and documentation were written  by Mark
          C. DiVecchio.

                  Many trademarks are used through out this  document. They
          are:

             -  PC-VT is a trademark of Mark C. DiVecchio.

             -  IBM,  IBM   PC,  IBM  AT  and  TopView  are  trademarks  of
                International Business Machines Corporation.

             -  DEC, VMS, VAX and  VT  are  trademarks of Digital Equipment
                Corporation.

             -  Smartmodem is a trademark of Hayes Microcomputer Products.

             -  UNIX is a trademark of AT&T Bell Laboratories, Inc.

             -  KERMIT is a trademark of Henson Associates, Inc.

             -  Tektronix is a trademark of Tektronix, Inc.

             -  The Everex Edge is a trademark of Everex Systems, Inc.

             -  Hercules is a trademark  of  Hercules  Computer Technology,
                Inc.

             -  DESQview is a trademark of Quarterdeck Office Systems.

                  For more details on the operation of a VT100 or  a VT102,
          refer to the VT100 and VT102 Video Terminal User Guides available
          from:

                            Digital Equipment Corporation
                                    PO Box CS2008
                                  Nashua, NH  03061
                          VT100 : Part No. EK-VT100-UG-003
                          VT102 : Part No. EK-VT102-UG-002
                                    (800)258-1710

                  For complete details on the  operation  of  the 4010/4014
          consult the "4014 and  4014-1  Computer  Display  Terminal User's
          Manual" distributed by:

                                   Tektronix, Inc.
                                     PO BOX 500
                                Beaverton, OR  97977
                                Part No. 070-1647-00.













                  For  details  on  the  Everex   Edge  Monochrome/Graphics
          Adapter Card which gives PC-VT its 132 column capability and high
          resolution 4014 emulation, you can contact Everex at:

                                Everex Systems, Inc.
                            47777 Warm Springs Boulevard
                                  Fremont, CA 94539

                  For  details  on the Hercules  monochrome  graphics  card
          which gives PC-VT its high  resolution  4014  emulation,  you can
          contact Hercules at:

                            Hercules Computer Technology
                                   2550 Ninth St.
                                 Berkeley, CA 94710

                  KERMIT was developed at  Columbia  University  Center for
          Computing  Activities  by   Frank da Cruz, Daphne Tzoar, and Bill
          Catchings and is included here  at no charge because imitation is
          the sincerest form  of  flattery. The supplement to this document
          contains a copy of the KERMIT manual.




                                     Conventions


                  Throughout this manual, hexadecimal numbers  are followed
          by the letter "H". All other numbers are decimal. Also, the Enter
          key on the keyboard  sends  a  carriage  return character - ASCII
          code  13.  A  carriage  return  function moves the cursor to  the
          beginning  of  the  current  line.  "ESC"  refers  to  the  ASCII
          character whose decimal value is 27.

                  The  word "frame" is used to mean what  you  see  on  the
          screen.  It  is  a  collection  of  words  and symbols  providing
          information. The word "display" is used to mean the screen itself
          or the act of causing characters to be shown on the screen.

                  For the latest news  about  PC-VT,  read  the file on the
          distribution diskette named READ.ME.


          THANKS


                  Your feedback helps  make  PC-VT a better and more useful
          program. If you have  any  ideas or comments, please send them to
          the address below.
















                                  Mark C. DiVecchio
                          ATHENA SYSTEMS DEVELOPMENT GROUP
                         9888 Carroll Center Road  Suite 113
                                 San Diego, CA 92126
                        (619) 549-4056  RBBS : (619) 549-3927


























































          PC-VT v10.0                                 VT100 & 4014 Emulator








                                      Chapter 1

                                    Introduction


                  PC-VT emulates DEC VT100, DEC VT102, DEC  VT52, Tektronix
          4010 and Tektronix 4014  terminals.  It runs on the IBM PC, PCXT,
          PCjr, and PCAT under DOS 2.x and 3.x. PC-VT  is  compatible  with
          both the DESQview and TopView multiprocessing software packages.


          1.1  General Terminal Emulation


                  Throughout this manual, host refers to  the  computer "on
          the other end of the line" with which PC-VT is communicating.

                  PC-VT performs these functions  which  make  it  a useful
          interface between a PC and a host computer:

             -   Communication over an RS232 port configured as either COM1
                or COM2 selectable from the SETUP frame.

             -  Communications support for all the  popular  baud  rate and
                data bit/parity bit combinations.

             -  On Line HELP by  pressing  the ALT-H key while in the VT100
                or 4014 communications, SETUP, DIALING, or MACRO frames.

             -  Full feature Upload and  Download  file  capability. ASCII,
                XMODEM (CRC capable), and KERMIT are  supported.  Path name
                support  is included. ASCII file upload includes  handshake
                capability to compensate for slow  host  systems.  User can
                set his preferred file  transfer  method  as the default in
                the SETUP B frame.

             -  Support for Hayes dialing commands and a  dialing directory
                with 10 entries. Each entry contains not only phone numbers
                and dialing commands but also a complete copy  of  the USER
                MEMORY file with which you  can  customize  PC-VT  for each
                host.  These customized  USER  MEMORIES  are  automatically
                loaded when PC-VT dials the phone number.

             -  ALT-F1 thru ALT-F10 are used as macro keys.

             -  DOS  functions  or  other  programs  can  be   run  without
                terminating  PC-VT   or   disconnecting   from   the  host.
                Especially  useful since PC-VT monitors the  communications


                                                                     Page 1






          Introduction                                          PC-VT v10.0


                line  and  saves  all  characters  received  while  you are
                running other  programs.  When  you  return  to  PC-VT, the
                received information is displayed.

             -  Use  of  the  environment  string  "PC-VT="  to   find  the
                parameter  files.

             -  Supports buffer  sizes  of  256  and  2048  characters. The
                smaller buffers give faster response to  interrupts  to the
                host while the larger size reduces XON/XOFF handshaking.

             -  Full Duplex with no EIA modem control. Only data leads have
                to be connected (FDX A mode). Suitable for use with  a null
                modem (direct) connection to  the  host  computer or with a
                modem which does not require modem control signals.

             -  Full receive parity checking.

             -  Capability to transmit a sustained Break.


          1.2  VT100/VT102/VT52


                  PC-VT  is  a  software emulator which makes  the  IBM  PC
          function  as a DEC VT102, VT100 or  VT52  video  terminal.  PC-VT
          defaults to VT102 emulation.

                  In  this  manual,  reference   to   the   VT100  emulator
          encompasses the VT100/VT102/VT52 emulator package.

                  PC-VT  emulates the majority of the documented  functions
          of the VT100. Because of either hardware limitations  of  the IBM
          PC  or limitations of DOS, some  functions  cannot  be  emulated.
          Other  functions  have been slightly  modified.  Throughout  this
          document, references are made to these changes and deletions. The
          vast majority of users will never notice these  hardware  and DOS
          mandated changes.

                  The VT user will  only  need to read Chapters 2 through 5
          of this manual. Chapter 6, SETUP frames, is only necessary if any
          of  the  selectable  features  need  to be changed  from  default
          settings. Chapter 7 describes the VT100 "USER MEMORY" which PC-VT
          emulates by creating and using a disk file.  The  Appendices give
          more sophisticated users a complete description  of  the internal
          workings of the VT mode of PC-VT.

                  The  following is a brief list  of  the  VT100  functions
          handled by PC-VT:

             -  Emulates  both  VT100 and VT102  terminals.  Emulates  VT52
                compatibility mode of the VT100.




          Page 2






          PC-VT v10.0                                 VT100 & 4014 Emulator


             -  Fast screen update for PC's with the color graphics display
                card. Known as  snow  update. A separate option is provided
                to select fast screen mode  (known as DMA) for screen saves
                and restores only and not for normal character display.

             -  Handles 8 foreground and 8  background  colors  on  a color
                monitor. User can set his color choices from the host.

             -  Selects either VMS or UNIX host. PC-VT supports EDT and EVE
                under VMS and VI under UNIX mode.

             -  Supports VMS 4.x Line Editing using the PC's Keypad.

             -  Copy the screen to a disk file at any time.

             -  NO SCROLL key XON/XOFF support. Can recall up to 8 previous
                screens of information and dump  all  of  those  screens to
                disk upon request.

             -  Ability to redefine  all  function and editing keys to send
                any text or Escape sequence of up to 50 characters.

             -  Connects a printer as LPT1 or LPT2 and includes local print
                screen operations.

             -  Capability to echo all displayed characters to LPT1 or LPT2
                as a hardcopy record of a terminal session.

             -  Screen blanking feature turns  off  the  CRT screen after 3
                minutes of inactivity.

             -  Special  ALT  key combinations provide  access  to  several
                special function procedures.

             -  SETUP A and  SETUP  B  frames  to  configure  PC-VT  to the
                operating environment.

             -  Both Numeric and Application Keypad modes.

             -  Full cursor control.

             -  Full XON/XOFF support for both transmit and receive.

             -  ON  LINE,  LED  "Lx" and KBD LOCKED lights are supported on
                line 25 of the PC's screen  as  a Status Line. (4 LED's are
                supported for both the VT100 and VT102 emulation.)

             -  132  column mode is supported if  you  have  installed  the
                Everex Edge card in your PC.

             -  Double width characters are  simulated  by  displaying them
                with a space between them so that 40 characters take up one
                entire 80 character line.



                                                                     Page 3






          Introduction                                          PC-VT v10.0


             -  Double height characters are simulated by clearing  the top
                half line to blanks and making the bottom half line  into a
                double width line.

                  The following functions are not handled by PC-VT in VT100
          mode:

             -  VT100 half duplex modes (HDX A and HDX B) and  special full
                duplex modes (FDX B and FDX C).

             -  Features  used only  in  these  unsupported  communications
                modes.

             -  VT100  Tests  and  Adjustments  Escape  sequences  are  not
                actually run on the PC.  PC-VT does respond with a terminal
                OK Device Status Report.

             -  Certain display attribute handling.  The  IBM  PC  does not
                handle reverse video (black on white) the same  way  as the
                VT100. It will look  the  same  on  the screen but changing
                from  one to the other mode will be  slower  and  will  not
                produce the expected results. Underline especially produces
                unusual results. The underscore attribute on PC's using the
                color graphics  display  card  is  displayed  with  bold or
                bold/blinking attributes selectable from the SETUP B frame.
                Look Appendix B for details of what combinations work.

             -  As mentioned  earlier,  functions  for  which  there  is no
                essential hardware such as Smooth Scroll  mode,  132 column
                mode, and Alternate Character ROM  modes  are  not handled.
                132  column  mode  will work if you install the Everex Edge
                card.

             -  Double height and double  width  characters  are simulated.
                The emulation is not exact.

             -  The line printer serves  as  a  capture device only. Escape
                sequences are not sent to the line printer.


          1.3  4010/4014


                  PC-VT includes a software emulator which makes the IBM PC
          function as a Tektronix 4010/4014 Computer Display Terminal.

                  In   this   manual,   reference   to  the  4014  emulator
          encompasses the Tektronix 4010/4014 emulator package.

                  PC-VT emulates the majority of the functions of the 4014.
          Because  of   either  hardware  limitations  of  the  IBM  PC  or
          limitations of DOS,  some  functions  cannot  be  emulated. Other
          functions have been slightly modified. The differences are listed
          below.


          Page 4






          PC-VT v10.0                                 VT100 & 4014 Emulator


                  The 4014 user normally only  needs to read Chapters 2 and
          11  to understand  the  operation of the 4014 emulator. Chapter 6
          is only necessary if any of the selectable features  need  to  be
          changed from the default settings.  PC-VT  defaults  to  the most
          commonly used  set  of  features.  The  Appendices  give detailed
          technical descriptions of the operation of PC-VT.

                  The 4014 emulator requires the IBM Color Graphics Adapter
          (CGA) (or equivalent),  the Everex Edge Monochrome/Color Graphics
          Adapter or the Hercules Graphics  Card  (or  equivalent).  If you
          have  both the IBM Monochrome and  IBM  Color  Graphics  Adapters
          along  with two displays, PC-VT will use both  of  them  in  4014
          mode.

          PC-VT handles the following 4014 functions :

             -  Emulates both Tektronix 4010 and 4014 terminals.

                Since the PC screen  is  not the same as the Tektronix 4014
                screen,  the following adjustment is made (high  resolution
                coordinates are shown in parentheses):

                For the 4010:
                X scale = Tekpoints 0-1023 are mapped into PC 0-639(720)
                Y scale = Tekpoints 0-779  are mapped into PC 0-199(348)
                          Y points 780-1023 map above the screen
                          but are still valid.

                For the 4014:
                X scale = Tekpoints 0-4095 are mapped into PC 0-639(720)
                Y scale = Tekpoints 0-3119 are mapped into PC 0-199(348)
                          Y points 3120-4095 map above the screen
                          but are still valid.

             -  Supports Alpha mode, Graph mode, Point  Plot  mode, Special
                Point Plot mode, Incremental Plot mode, and GIN mode.

             -  Handles  both  0-1023  (4010)  and 0-4096 (4014) coordinate
                spaces.

             -  Draws normal, dotted, dot-dashed, short-dash, and long-dash
                vectors.

             -  Supports  write thru mode by exclusive-ORing vectors  drawn
                in   that   mode   into   the  screen.  Therefore,  vectors
                continually drawn in  write  thru mode will appear to blink
                on the screen.

             -  Connects a printer as LPT1 or LPT2 and includes local print
                screen  operations.  The  IBM supplied GRAPHICS.COM program
                must have been run first as it is used for printing the CGA
                screen. The high resolution  screen  is  printed  by PC-VT,
                eliminating the need to run GRAPHICS.COM.



                                                                     Page 5






          Introduction                                          PC-VT v10.0


             -  Handles Page-Full and Autoprint operations.

             -  SCROLL LOCK key pauses vector drawing.

             -  Unlike a real 4014, PC-VT handles XON and XOFF like a VT100
                even in 4014 mode.  If  you  do  not want this handshaking,
                disable the XON/XOFF feature in the SETUP B frame.

          PC-VT can not handle the following items in 4014 mode:

             -  Margin  2  is  not  implemented.  Page  Full  condition  is
                selected when a line  feed  is output on the bottom line of
                the screen.

             -  The IBM PC does not display an Alpha cursor when the screen
                is in graphics mode.

             -  The alternate character set is not supported.

             -  PC-VT generates two character sets  when  using  either the
                IBM CGA, the Everex  Edge  or  the Hercules Graphics cards.
                The larger set is 8x8 dots and the smaller is 6x6 dots. The
                smaller set contains capital letters only.

             -  The IBM CGA supports 25 lines by 80 columns and 33 lines by
                106 columns. When using the  high  resolution  mode  of the
                Everex Edge or  Hercules  cards, PC-VT supports 43 lines by
                90 columns and 58 lines by 120 columns.

             -  Defocused  mode  is   not  supported.  Handled  as  regular
                vectors.

             -  Varying intensity vectors are not  supported.  Only  0% and
                100% intensity are supported.

             -  Special  Point  Plot  mode  responds  to  all  vectors with
                intensity  greater  than  0%   as   100%.   There   are  no
                intermediate intensity levels.


















          Page 6






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                      Chapter 2

                           Required Hardware and Software


                  PC-VT requires an IBM PC, PCXT, PCjr, or PCAT with either
          the  IBM  Monochrome  or  Color/Graphics  adapter,  an  80 column
          screen, 128K of memory (enough for DOS plus about 58K for the PC-
          VT program and about 23K for the HELP frame), one disk  drive and
          one RS-232 port. The RS-232 port can be jumpered as COM1 or COM2.
          A line printer, if present, is supported if it is connected  to a
          parallel  port  jumpered  as  either  LPT1 or LPT2. The DOS  MODE
          command can be used to route LPT1 or LPT2 output to a COM port if
          a  serial  printer  is attached. PC-VT operated under DOS 2.x, or
          3.x. PC-VT runs from either  floppy diskette or fixed disk. PC-VT
          is not copy protected.

                  To run the  4014  emulator, PC-VT requires either the IBM
          Color  Graphics  Adapter  and a color monitor,  the  Everex  Edge
          Monochrome/Color  Graphics Adapter and an IBM monochrome  monitor
          or the Hercules Graphics Card and an IBM monochrome monitor.

                  To use 132 columns in the VT emulator requires the Everex
          Edge  Monochrome/Color  Graphics Adapter and  an  IBM  monochrome
          monitor.

                  To use  the  Scroll  Buffer  feature,  PC-VT  requires an
          additional 88K of memory to hold the recalled screen information.
          To  run  the  KERMIT  file  transfer  module,  PC-VT requires  an
          additional 83K of memory.

                  The ANSI.SYS  device  driver  is  not  needed.  When it's
          loaded, it will not  interfere  with PC-VT but will slow down the
          program   operation.   PC-VT   will   not    recognize   keyboard
          redefinitions performed by ANSI.SYS.

                  PC-VT supports the  Hayes Smartmodem or compatible cards.
          Chapter 9 gives the details for their use. The modem card  can be
          configured as COM1  or  COM2.  If  an external modem is used, the
          RS-232 port in the IBM PC  can  also be configured either as COM1
          or COM2.









                                                                     Page 7






          Required Hardware and Software                        PC-VT v10.0


























































          Page 8






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                      Chapter 3

                            Installing and Starting PC-VT


          3.1  Installation


                  First, make  a  backup  of  the  diskette  containing the
          program and support files. Place  the original diskette in a safe
          place and use it only to make additional working copies of PC-VT.


          3.1.1  Floppy Diskette Installation


                  Insert the diskette into one of your diskette drives. Set
          the default diskette letter in DOS to that drive.

                  PC-VT  creates  and  uses three files on the disk to save
          default  parameters.  The  files  are PARAMS.DAT, DIALER.DAT, and
          MACRO.DAT. These files are automatically created  on  the default
          drive when you start the program for the first time.


          3.1.2  Fixed Disk Installation


                  Using PC-VT on the IBM  fixed disk is the most convenient
          way to use the program. There are no  special  requirements. Copy
          the program PC-VT.EXE and the file HELP.DAT to the fixed disk and
          using the SET command as described below. If you are going to run
          KERMIT file transfers, copy KERMIT.COM to the fixed disk.

                  PC-VT  creates  and  uses three files on the disk to save
          default  parameters.  The  files  are PARAMS.DAT, DIALER.DAT, and
          MACRO.DAT. These files are automatically created  in  the default
          directory  on the default drive. A better  way  to  handle  these
          files  is  to  specify an environment string  telling  PC-VT  the
          directory  to  store  these  three  files.  You  should copy  the
          KERMIT.COM into this directory as  well. You can specify the PATH
          command which DOS uses to locate the PC-VT  program  itself. With
          these two features, you can execute PC-VT without  regard  to the
          current default directory set on your fixed disk.

                  Use the DOS SET command as follows:

          SET PC-VT=d:path


                                                                     Page 9






          Installing and Starting PC-VT                         PC-VT v10.0


                  Where "d" is the drive letter and "path" is the pathname.
          The pathname can  be  any  string  acceptable  to  the  DOS CHDIR
          command. Some examples:

          SET PC-VT=              PC-VT uses the default
                                  directory on the default disk.

          SET PC-VT=C:            PC-VT uses the default
                                  directory on the C drive.

          SET PC-VT=A:\           PC-VT uses the root
                                  directory on the A drive.

          SET PC-VT=C:\PC-VT      PC-VT uses the directory
                                  named PC-VT on the C drive.

                  Again, if you  don't  bother with this option, PC-VT just
          uses the default directory on the default drive.

                  Here is an example of a command sequence used to load PC-
          VT onto a fixed disk. Put the diskette containing the program and
          support files into the A diskette drive. Replace the drive letter
          C in the example with the drive letter of your fixed disk.

          C:
          CD \
          MKDIR PC-VT
          SET PATH=C:\;C:\PC-VT
          SET PC-VT=C:\PC-VT
          COPY A:PC-VT.EXE C:\PC-VT/V
          COPY A:HELP.DAT C:\PC-VT/V
          COPY A:KERMIT.COM C:\PC-VT/V

                  Now you can  execute  PC-VT without regard to the current
          default directory.


          3.2  Starting PC-VT


                  If you have  a  modem which requires manual dialing, dial
          up the host computer and turn on the modem. Start the  program by
          typing PC-VT. PC-VT is preinitialized to communicate at 1200 baud
          with 8 data bits, no parity, and 1 stop bit  through  COM port 1.
          If these parameters are not correct for your installation you can
          change  them.   See  the  discussion  of  the  SETUP  frames  for
          instructions on how to change parameters.

                  As  PC-VT starts up, it initializes  the  COMx  port  and
          establishes the  connection to the modem. The screen displays the
          communications frame. Lines 1 through 24 emulate the VT100 screen
          which has 24 lines. Line 25 is a  Status  Line.  The  first thing
          that you  see  on  line  25 is the word "ON LINE" and the version
          number of PC-VT in the lower left.  This indicates that  PC-VT is


          Page 10






          PC-VT v10.0                                 VT100 & 4014 Emulator


          operating normally and is  ready  to  communicate.  If you have a
          Hayes or Hayes  compatible  modem, you can now automatically dial
          the host's number. Press CTRL-F9  to enter the DIALING frame. See
          Chapter  9  for  detailed instructions on how to use this dialing
          facility. Most host systems require  that  the  terminal initiate
          communications, so  press ENTER once or twice. Your host computer
          should now be responding. From this point on, PC-VT runs  your PC
          as a VT100 video terminal.

                  In addition to the items described above, the Status Line
          also shows the status of the  attached  modem if the cable to the
          modem carries all  signals  or  if  the  modem  is  an internally
          mounted unit. These three icons are displayed:

             -  DSR - Data Set Ready - the modem is ready to accept data.

             -  CD - Carrier Detect  -  the modem has detected a carrier on
                the phone line.

             -  CTS  -  Clear  To  Send  -  the  modem  has  established  a
                connection and is ready to send data to the host.

                  If  you  are  using a intelligent modem,  the  modem  may
          signal CD and CTS even when  not  connected to the host. There is
          usually a switch on the modem to switch these two lines  to their
          correct operation. Keep in mind  that  PC-VT  doesn't  care about
          these lines, it just displays them for your information.

                  The CD and DSR lines can  be  used by the dialer during a
          modem dial operation. See Chapter 9 for dialer details.

                  A  new  copy  of  Command.COM  can  be   started  without
          terminating PC-VT or breaking  the  host  connection. To do this,
          press ALT-F (hold down the ALT key and then press the F key). The
          contents of the communications frame  is saved by PC-VT. Then the
          screen clears and a DOS prompt appears on the screen. You can now
          execute all DOS commands  and  even  start  up other programs. Be
          careful, though, that you do not run a program that uses the same
          communications port or disk  files  as  being  used by PC-VT. The
          other program may leave the  communications  port  in  an unknown
          state and PC-VT may not be able to regain control of it. When you
          wish  to  return  to PC-VT, type "exit" at the Command.COM prompt
          and control returns to the PC-VT communications frame.

                  PC-VT uses the environment  string  "COMSPEC="  to locate
          the  command  processor.   Since   DOS   sets   this   string  up
          automatically, you don't have  to  concern  yourself with it. The
          most useful reason for getting back to DOS by this method instead
          of  terminating  PC-VT  is  that  PC-VT  remains  in  memory  and
          constantly monitors the communications port. Then when you return
          to  PC-VT  by  typing  "exit",  PC-VT  immediately  displays  all
          information which it received  and  saved  while you were running
          other  DOS programs. Of course, if you  terminate  PC-VT  to  run
          other  DOS  programs,  PC-VT  is  cleared  from  memory  and  the


                                                                    Page 11






          Installing and Starting PC-VT                         PC-VT v10.0


          communications port  is  no  longer  monitored.  All  information
          received on the port is lost.

                  PC-VT outputs both tones  and  clicks  on the internal PC
          speaker  to  indicate  attempted  illegal operations. PC-VT beeps
          under the following conditions:

            1.  when an undefined key is pressed on the keyboard,

            2.  when a control character of ASCII 7 (BEL) is received,

            3.  when margin bell has been selected in the SETUP B frame and
                the  cursor  enters  the 8th column from the right from the
                9th column from the right  under control of the keyboard or
                the host,

            4.  when the host tries  to  output to the line printer and the
                line printer is not ready,

            5.  when an attempt is made  to perform an illegal or undefined
                operation in the SETUP, DIALING or MACRO frames, or

            6.  when the modem has lost communications or  cannot transmit,
                PC-VT times out after trying to send a  character  for one-
                half second.

          PC-VT clicks under the following conditions:

            1.  when the keyboard has been locked by the host and a  key is
                typed or

            2.  when the user requests a BREAK to be sent to host.


          3.3  Command Line Options


                  When you start up PC-VT by typing the program name at the
          DOS  command  prompt,  you can follow the name with the following
          command line options. You must do  this  at least once if you are
          using  the  Everex  Edge or Hercules Graphics cards. To make your
          selections permanent once you have started PC-VT, go to the SETUP
          A frame  and  press  "S"  to  save  this information in your USER
          MEMORY on disk. Then when you next start PC-VT, the selected mode
          will be automatically started.


          /g             tells PC-VT not to display the opening  banner but
                         to go directly into the communications frame.

          /dn            tells PC-VT to  dial  the  number  in  the DIALING
                         frame corresponding to n, where n is a number from
                         1  to 10. PC-VT takes the  entry  in  the  DIALING
                         directory and dials the number during its start up


          Page 12






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         sequence.  This  lets you start  the  program  and
                         immediately  dial a number. The dialing entry  can
                         be a complete  logon  macro  as  described  in the
                         Chapter 9.

          /ln            tells PC-VT to load the SETUP data for the host in
                         the DIALING frame corresponding to n, where n is a
                         number from 1 to 10.  PC-VT takes the entry in the
                         DIALING directory and  loads the SETUP data during
                         its start up sequence.  This  lets  you  start the
                         program and have the SETUP data  for  a particular
                         host. This  is useful if you are already dialed in
                         to a host and  just  want to reset PC-VT or if you
                         are on a direct connection to a host.

          /c             tells PC-VT to  use the other communications port.
                         That is, if the default you have set is COM1, when
                         PC-VT starts, it uses COM2.

          /t             causes  PC-VT  to  immediately  go into 4014 mode.
                         Normally, PC-VT starts up in  VT100  mode  and you
                         must switch it to 4014 mode by pressing ALT-T.

          /b             tells PC-VT that you have both the  IBM monochrome
                         and IBM Color Graphics Adapter installed. That way
                         you can  use  the  monochrome  display  for  VT100
                         emulation  and  the  graphics  display   for  4014
                         emulation.  The  displays  are  not cleared as you
                         switch between emulators. To  let  PC-VT  make the
                         most of this mode, you  should  start  the program
                         from the monochrome display.

          /e             tells  PC-VT  that  you   have   an   Everex  Edge
                         Monochrome/Color Graphics Adapter Card with an IBM
                         monochrome monitor installed in your PC. With this
                         card, PC-VT  can  display  the  132  column  VT100
                         screen, the regular 80 column screen and  the 4014
                         high  resolution  graphic  screens  on   the  same
                         display. The display is automatically  switched as
                         you switch emulators. Caution : If you select this
                         option and you do  not  have  the Everex Edge card
                         installed,  the  results are  unpredictable.  This
                         mode  REQUIRES  the  IBM  monochrome   monitor  be
                         connected to the Edge card.

          /h             tells PC-VT that you have  either  an  Everex Edge
                         Monochrome/Color  Graphics  Adapter  or a Hercules
                         Graphics Card installed in your PC. PC-VT produces
                         4014 graphics using the  720  by  348  pixel modes
                         supported by these cards. You  don't  have  to use
                         this  option  if  you  have  already  used  the /e
                         option. Caution : If you  select  this  option and
                         you do not have  an  Everex  Edge or Hercules card
                         installed,  the  results are  unpredictable.  This


                                                                    Page 13






          Installing and Starting PC-VT                         PC-VT v10.0


                         mode  REQUIRES  the  IBM  monochrome   monitor  be
                         connected to the Edge card. 132 column mode is not
                         supported if you just  use  the  /h option and you
                         have the Everex  Edge  card  installed  -  in that
                         case, use the /e option.

          /i             tells PC-VT that you want to use what ever monitor
                         is attached to your system.  This  is  the default
                         and needs only be entered if you want  to  reset a
                         /h, /b, or /e option specified previously.














































          Page 14






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                      Chapter 4

                                   Stopping PC-VT


                  Since CTRL-C is a  valid  key for the VT100 and the 4014,
          PC-VT intercepts both that key  and CTRL-BREAK before DOS can use
          them  to  terminate  the program.  Even in the non communications
          frames, PC-VT cannot be  terminated  by  pressing CTRL-C or CTRL-
          BREAK.

                  Therefore,  to  terminate  PC-VT,  press CTRL-F8 from the
          communications frame.

                  The screen clears, control returns  to  DOS  and  the DOS
          prompt  appears.  The  host connection is not broken (DTR and RTS
          are   kept   active)   and   restarting    PC-VT   re-establishes
          communications.
































                                                                    Page 15






          Stopping PC-VT                                        PC-VT v10.0


























































          Page 16






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                      Chapter 5

                             VT100 Keyboard Assignments


                  Since the keyboard on the IBM  PC  is not the same as the
          VT100, certain keys have to be mapped. The basic keyboard  is the
          same of course. The keypad, cursor keys and certain other control
          keys are in different positions on the two  keyboards.  The other
          major difference is the lack of separate cursor keys  on  the  PC
          (the cursor keys and the keypad occupy the same  keys).  You  can
          also  make a custom keyboard mapping  described  in  the  section
          titled Keyboard Redefinition.


          5.1  Regular Key Mapping



          VT100           PC              Notes Key
                          Equivalent
                          Key


          DELETE

                         Backspace   The  backspace  key  on  the   IBM  PC
                         keyboard emulates the DELETE key on the  VT100. An
                         option on the SETUP  B  frame  lets you change the
                         IBM PC backspace key  to  send  an  ASCII 8 to the
                         host  instead  of  the  ASCII  127  per  the VT100
                         definition.

                         Del         When the keyboard is in numeric keypad
                         mode, the Del key sends  a  DEL  character  to the
                         host (ASCII 127).  In application keypad mode, the
                         keypad is redefined  to  work with one of the text
                         editors: EDT, EVE or VI.



          BACKSPACE

                         Shift-Tab   The  SHIFT-Tab  key  sends a backspace
                         character (ASCII 8) to the host.





                                                                    Page 17






          VT100 Keyboard Assignments                            PC-VT v10.0


                         Backspace   Alternate  method.  Use  the  SETUP  B
                         frame to change the IBM PC backspace key to send a
                         backspace (ASCII 8) to the host.

                         CTRL-H      The   CTRL-H   key  always   sends   a
                         backspace character (ASCII 8).



          LINEFEED

                         CTRL-J      This key combination sends a line feed
                         character to the host.



          CTRL-@

                         CTRL-@      This  key  combination  sends  a   NUL
                         character (ASCII  0) to the host. This is the same
                         as the VT100.



          NO SCROLL

                         SCROLL LOCK The SCROLL LOCK  key on IBM PC freezes
                         the display  and emulates the NO SCROLL key on the
                         VT100. PC-VT displays the word "SCR" on the status
                         line of  the display to remind you that the SCROLL
                         LOCK key has been depressed once.

                                     Depressing the key again resets SCROLL
                         LOCK and clears the  status  line  reminder. PC-VT
                         continues to accept characters from the host until
                         PC-VT's communications buffer fills at which point
                         PC-VT sends an XOFF.

                                     Pressing the Keypad + (plus) key dumps
                         the   screen   onto   a   disk  file.  The  screen
                         information is appended to the file if  it already
                         exists.  The  file is named  SCRNDUMP.DAT  and  is
                         created on the  default drive. Trailing spaces are
                         removed from  each  screen  line  as  the  data is
                         written to disk.

                                     The  Scroll  Buffer  section  in  this
                         chapter, describes PC-VT  features  activated when
                         you press the SCROLL LOCK key.



          ARROWS



          Page 18






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         Cursor Keys The  four  cursor  keys  on the IBM PC
                         keyboard emulate  the  four  cursor  keys  on  the
                         VT100.  NUM LOCK must be off  for  these  keys  to
                         function. If NUM LOCK is set, the keypad generates
                         the numeric characters shown on the keys.



          HERE IS

                         ALT-B       The ALT-B key emulates the HERE IS key
                         on the VT.  That  is,  the  answerback  message is
                         transmitted.



          ----

                         NUM LOCK    The  NUM  LOCK  key  places the IBM PC
                         keypad in numeric mode. The NUM LOCK key functions
                         locally in the  PC  only and does not transmit any
                         characters  to  the  host computer. PC-VT displays
                         the word "NUM"  on  the status line of the display
                         to  remind  you  that the NUM LOCK  key  has  been
                         depressed  once.  Depressing  the key again resets
                         NUM LOCK and clears the reminder.



          ----

                         CAPS LOCK   The CAPS LOCK key  places  the  IBM PC
                         keyboard  in  uppercase mode. The  CAPS  LOCK  key
                         functions locally in  the  PC  only  and  does not
                         transmit any characters  to the host computer. PC-
                         VT displays the  word  "CAP" on the status line of
                         the display to  remind  you that the CAPS LOCK key
                         has been depressed  once. Depressing the key again
                         resets CAPS LOCK and clears the reminder.

















                                                                    Page 19






          VT100 Keyboard Assignments                            PC-VT v10.0




          5.2  Keypad Mapping


                  In VT100 Numeric Keypad mode, F1 thru F4 on  the  IBM  PC
          keyboard emulate the PF1 thru PF4 keys on the VT100.

                  In VT100 Application Keypad  mode,  F1  thru F10 map onto
          the  VT100 keypad as follows (PC-VT  displays  the  Greek  letter
          alpha on the status line to indicate that Application Keypad mode
          is set. This mode is set and reset  only  by  an  escape sequence
          from the host computer.):

               IBM PC Key ..... VT100 Key

               F1 ................... PF1
               F2 ................... PF2
               F3 ..................... 7
               F4 ..................... 8
               F5 ..................... 4
               F6 ..................... 5
               F7 ..................... 1
               F8 ..................... 2
               F9 ..................... 0
               F10 .................... 0

               SHIFT-F1 ............. PF3
               SHIFT-F2 ............. PF4
               SHIFT-F3 ............... 9
               SHIFT-F4 ............... -
               SHIFT-F5 ............... 6
               SHIFT-F6 ............... ,
               SHIFT-F7 ............... 3
               SHIFT-F8 ........... ENTER
               SHIFT-F9 ............... .
               SHIFT-F10 .......... ENTER

                  This  assignment was closely follows the physical  layout
          of the keypad on the VT100. The VT100 has four columns of keys in
          the keypad. PC-VT emulates the two left columns with the function
          keys and emulates the two right columns with the shifted function
          keys.  Users  who  are  familiar  with the VT100 keypad and  have
          memorized the position of each  key  should  have  little trouble
          using this function key mapping. Note that the "0"  key  and  the
          ENTER  key are mapped onto two of the PC keys. This is because on
          the VT100, the "0" and ENTER keys are double width.

                  Note : NUM LOCK is handled locally in the IBM PC. For the
          keypad keys to work correctly when using PC-VT,  NUM  LOCK should
          not be set.





          Page 20






          PC-VT v10.0                                 VT100 & 4014 Emulator


                  Figure 1 shows this  mapping.  The name of the IBM PC key
          is in the upper left of each key and the emulated key or function
          is shown in the center of the key.





















































                                                                    Page 21






          VT100 Keyboard Assignments                            PC-VT v10.0


                          Figure 1 KEYPAD FUNCTION MAPPING


              FUNCTION KEYS                   SHIFTED FUNCTION KEYS


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F1        ³ ³F2        ³ ³F1        ³ ³F2        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³   PF1    ³ ³   PF2    ³ ³   PF3    ³ ³   PF4    ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F3        ³ ³F4        ³ ³F3        ³ ³F4        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³    7     ³ ³     8    ³ ³     9    ³ ³     -    ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F5        ³ ³F6        ³ ³F5        ³ ³F6        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³    4     ³ ³     5    ³ ³     6    ³ ³     ,    ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F7        ³ ³F8        ³ ³F7        ³ ³F8        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³    1     ³ ³     2    ³ ³     3    ³ ³          ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                     ³          ³
                                                     ³  ENTER   ³
              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
              ³F9           F10       ³ ³F9        ³ ³F10       ³
              ³                       ³ ³          ³ ³          ³
              ³         0             ³ ³     .    ³ ³          ³
              ³                       ³ ³          ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ












          Page 22






          PC-VT v10.0                                 VT100 & 4014 Emulator




          5.3  VMS Line Editing Keypad Mapping


                  In VT100 Numeric Keypad mode, which is the normal mode of
          operation, PC-VT supports the VMS line editing commands using the
          PC's Keypad. This mapping  is  in  effect  only in Numeric Keypad
          mode; in  Application Keypad mode, the selected text editor, EVE,
          EDT or VI, takes over the PC's keypad.

               IBM PC Key ............ Line Editing Function Performed

               Keypad + ................ Enter key on the VT100 Keypad
               Del key .................. Deletes the character to the
                                                    left of the cursor
               Up Arrow .................. Recall the previous command
               Down Arrow .................... Recall the next command
               Left Arrow ....................... Move the cursor left
               Right Arrow ..................... Move the cursor right
               Ins key  ............... Toggles Insert/Overstrike mode
               Home key ................ Moves the cursor to the start
                                                           of the line
               End key  .................. Moves the cursor to the end
                                                              the line
               PgUp key .................. Deletes characters from the
                                   beginning of the line to the cursor
               PgDn key ...................... Deletes the word at the
                                                                cursor

                  Figure 2 shows this  mapping.  The name of the IBM PC key
          is in the upper left of each key and the emulated key or function
          is then shown in the center of the key.























                                                                    Page 23






          VT100 Keyboard Assignments                            PC-VT v10.0


                    Figure 2 PC-VT SPECIAL VMS LINE EDIT MAPPING


                     PC KEYPAD KEYS as MAPPED into VMS Line Editing

          ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³7         ³ ³8         ³ ³9         ³ ³-[minus]  ³
                     ³CURSOR TO ³ ³ RECALL   ³ ³ DELETE   ³ ³          ³
                     ³  START   ³ ³ PREVIOUS ³ ³ BOL TO   ³ ³          ³
                     ³ OF LINE  ³ ³ COMMAND  ³ ³ CURSOR   ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³4         ³ ³5         ³ ³6         ³ ³+[plus]   ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ³  CURSOR  ³ ³          ³ ³  CURSOR  ³ ³          ³
                     ³   LEFT   ³ ³          ³ ³   RIGHT  ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
                     ³1         ³ ³2         ³ ³3         ³ ³          ³
                     ³ CURSOR   ³ ³ RECALL   ³ ³ DELETE   ³ ³  ENTER   ³
                     ³ TO END   ³ ³ NEXT     ³ ³ WORD     ³ ³          ³
                     ³ OF LINE  ³ ³ COMMAND  ³ ³          ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
          ³0                    ³ ³.[period]              ³ ³          ³
          ³   TOGGLE            ³ ³      DELETE           ³ ³          ³
          ³   INSERT/OVERSTRIKE ³ ³      CHARACTER        ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ



















          Page 24






          PC-VT v10.0                                 VT100 & 4014 Emulator




          5.4  EDT Keypad Mapping


                  In VT100 Application Keypad mode, which is set by the VMS
          EDT  text  editor,  the  following  keys  cause   special  escape
          sequences to be  transmitted.  Observe that some of these special
          keys transmit sequences that  require  two  or more keystrokes on
          the  VT100.  PC-VT  displays the Greek letter alpha on the status
          line to indicate that this mode is active.

                  Bits  in  the  SETUP frame select either VMS or UNIX mode
          and  select  EDT  or EVE keypad support for this special mapping.
          For  this  mapping,  VMS  mode  and EDT keypad support should  be
          selected.

               IBM PC Key ..................... EDT Function Performed

               Keypad + ................ Enter key on the VT100 Keypad
               Keypad - .. DEL L (delete line) key on the VT100 Keypad
               Del key ...................... DEL C (delete character)
               Backspace ................ Deletes the character to the
               or                      left of the cursor (DELETE key
               ALT-=                                     on the VT100)
               Ins key  .................................... OPEN LINE
               Home key .......................................... TOP
               End key  ....................................... BOTTOM
               PgUp key .................................. BACKUP SECT
               PgDn key ................................. ADVANCE SECT
               CTRL-Home key ............ Deletes the word to the left
               or                          of the cursor (LINEFEED key
               CTRL-J                                    on the VT100)
               CTRL-End key ............ ADVANCE DEL EOL - Erases from
                                                 the cursor to the end
                                                          of the line.
               CTRL-PgUp key ............................. BACKUP PAGE
               CTRL-PgDn key ............................ ADVANCE PAGE
               CTRL-Left Arrow key ....... BACKUP EOL - Move cursor to
                                                        the end of the
                                                        previous line.
               CTRL-Right Arrow key .... ADVANCE EOL - Move the cursor
                                                     to the end of the
                                                         current line.
               SHIFT-Tab ......................... Moves the cursor to
                                             the beginning of the line
                                         (BACKSPACE key on the VT100).

                  Figure 3 shows this  mapping.  The name of the IBM PC key
          is in the upper left of each key and the emulated key or function
          is then shown in the center of the key.





                                                                    Page 25






          VT100 Keyboard Assignments                            PC-VT v10.0


                       Figure 3 VT100 SPECIAL EDT KEY MAPPING


              FUNCTION KEYS                   SHIFTED FUNCTION KEYS

              For Functions in (), press GOLD Key First.
              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F1        ³ ³F2        ³ ³F1        ³ ³F2        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³  GOLD    ³ ³  HELP    ³ ³  FNDNXT  ³ ³   DEL L  ³
              ³          ³ ³          ³ ³  (FIND)  ³ ³  (UND L) ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F3        ³ ³F4        ³ ³F3        ³ ³F4        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³  PAGE    ³ ³  SECT    ³ ³ APPEND   ³ ³   DEL W  ³
              ³(COMMAND) ³ ³ (FILL)   ³ ³(REPLACE) ³ ³  (UND W) ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F5        ³ ³F6        ³ ³F5        ³ ³F6        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³ ADVANCE  ³ ³ BACKUP   ³ ³   CUT    ³ ³   DEL C  ³
              ³ (BOTTOM) ³ ³  (TOP)   ³ ³ (PASTE)  ³ ³  (UND C) ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F7        ³ ³F8        ³ ³F7        ³ ³F8        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³  WORD    ³ ³   EOL    ³ ³  CHAR    ³ ³          ³
              ³(CHNG C)  ³ ³ (DEL EOL)³ ³(SPECINS) ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³  ENTER   ³
                                                     ³  (SUBS)  ³
                                                     ³          ³
              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
              ³F9           F10       ³ ³F9        ³ ³F10       ³
              ³                       ³ ³          ³ ³          ³
              ³     LINE              ³ ³  SELECT  ³ ³          ³
              ³        (OPEN LINE)    ³ ³  (RESET) ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ












          Page 26






          PC-VT v10.0                                 VT100 & 4014 Emulator


                      VT100 SPECIAL EDT KEY MAPPING..continued


                     PC KEYPAD KEYS as MAPPED into EDT

          For Functions in (), press GOLD Key First.
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³7         ³ ³8         ³ ³9         ³ ³-[minus]  ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ³  TOP     ³ ³  CURSOR  ³ ³  BACKUP  ³ ³  DEL L   ³
                     ³          ³ ³    UP    ³ ³   SECT   ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³4         ³ ³5         ³ ³6         ³ ³+[plus]   ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ³  CURSOR  ³ ³          ³ ³  CURSOR  ³ ³          ³
                     ³   LEFT   ³ ³          ³ ³   RIGHT  ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
                     ³1         ³ ³2         ³ ³3         ³ ³          ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ³  BOTTOM  ³ ³  CURSOR  ³ ³ ADVANCE  ³ ³  ENTER   ³
                     ³          ³ ³   DOWN   ³ ³  SECT    ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
          ³0                    ³ ³.[period]              ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³   OPEN LINE         ³ ³         DEL C         ³ ³          ³
          ³     (LINE)          ³ ³        (UND C)        ³ ³          ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ




















                                                                    Page 27






          VT100 Keyboard Assignments                            PC-VT v10.0


                      VT100 SPECIAL EDT KEY MAPPING..continued


              PC KEYPAD KEYS as MAPPED into EDT - HOLD DOWN CTRL KEY


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³7         ³ ³8         ³ ³9         ³ ³-[minus]  ³
                     ³ DELETE TO³ ³          ³ ³  BACKUP  ³ ³          ³
                     ³ START OF ³ ³          ³ ³   PAGE   ³ ³          ³
                     ³ WORD     ³ ³          ³ ³          ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³4         ³ ³5         ³ ³6         ³ ³+[plus]   ³
                     ³ CURSOR TO³ ³          ³ ³ CURSOR TO³ ³          ³
                     ³ END OF   ³ ³          ³ ³ END OF   ³ ³          ³
                     ³ LAST LINE³ ³          ³ ³ LINE     ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
                     ³1         ³ ³2         ³ ³3         ³ ³          ³
                     ³ ERASE TO ³ ³          ³ ³ ADVANCE  ³ ³          ³
                     ³ END OF   ³ ³          ³ ³  PAGE    ³ ³          ³
                     ³ LINE     ³ ³          ³ ³          ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
          ³0                    ³ ³.[period]              ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ




















          Page 28






          PC-VT v10.0                                 VT100 & 4014 Emulator


              Figure 4 VT52 COMPATIBILITY MODE SPECIAL EDT KEY MAPPING


              FUNCTION KEYS                   SHIFTED FUNCTION KEYS

              For Functions in (), press GOLD Key First.
              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F1        ³ ³F2        ³ ³F1        ³ ³F2        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³  GOLD    ³ ³  HELP    ³ ³   DEL L  ³ ³  NOT     ³
              ³          ³ ³          ³ ³  (UND L) ³ ³  USED    ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F3        ³ ³F4        ³ ³F3        ³ ³F4        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³  PAGE    ³ ³  FNDNXT  ³ ³   DEL W  ³ ³  NOT     ³
              ³(COMMAND) ³ ³  (FIND)  ³ ³  (UND W) ³ ³  USED    ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F5        ³ ³F6        ³ ³F5        ³ ³F6        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³ ADVANCE  ³ ³ BACKUP   ³ ³   DEL C  ³ ³  NOT     ³
              ³ (BOTTOM) ³ ³  (TOP)   ³ ³  (UND C) ³ ³  USED    ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F7        ³ ³F8        ³ ³F7        ³ ³F8        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³  WORD    ³ ³   EOL    ³ ³  CUT     ³ ³          ³
              ³(CHNG C)  ³ ³ (DEL EOL)³ ³ (PASTE)  ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³  ENTER   ³
                                                     ³  (SUBS)  ³
                                                     ³          ³
              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
              ³F9           F10       ³ ³F9        ³ ³F10       ³
              ³                       ³ ³          ³ ³          ³
              ³      LINE             ³ ³  SELECT  ³ ³          ³
              ³        (OPEN LINE)    ³ ³  (RESET) ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ












                                                                    Page 29






          VT100 Keyboard Assignments                            PC-VT v10.0


             VT52 COMPATIBILITY MODE SPECIAL EDT KEY MAPPING..continued


                     PC KEYPAD KEYS as MAPPED into EDT

          For Functions in (), press GOLD Key First.
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³7         ³ ³8         ³ ³9         ³ ³-[minus]  ³
                     ³          ³ ³  CURSOR  ³ ³          ³ ³          ³
                     ³  TOP     ³ ³    UP    ³ ³  BACKUP  ³ ³  DEL L   ³
                     ³          ³ ³(REPLACE) ³ ³   SECT   ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³4         ³ ³5         ³ ³6         ³ ³+[plus]   ³
                     ³  CURSOR  ³ ³          ³ ³  CURSOR  ³ ³          ³
                     ³   LEFT   ³ ³          ³ ³   RIGHT  ³ ³          ³
                     ³ (APPEND) ³ ³          ³ ³ (SPECINS)³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
                     ³1         ³ ³2         ³ ³3         ³ ³          ³
                     ³          ³ ³  CURSOR  ³ ³          ³ ³          ³
                     ³  BOTTOM  ³ ³   DOWN   ³ ³ ADVANCE  ³ ³  ENTER   ³
                     ³          ³ ³  (SECT)  ³ ³  SECT    ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
          ³0                    ³ ³.[period]              ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³   OPEN LINE         ³ ³         DEL C         ³ ³          ³
          ³     (LINE)          ³ ³        (UND C)        ³ ³          ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ




















          Page 30






          PC-VT v10.0                                 VT100 & 4014 Emulator


             VT52 COMPATIBILITY MODE SPECIAL EDT KEY MAPPING..continued


              PC KEYPAD KEYS as MAPPED into EDT - HOLD DOWN CTRL KEY


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³7         ³ ³8         ³ ³9         ³ ³-[minus]  ³
                     ³ DELETE TO³ ³          ³ ³  BACKUP  ³ ³          ³
                     ³ START OF ³ ³          ³ ³   PAGE   ³ ³          ³
                     ³ WORD     ³ ³          ³ ³          ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³4         ³ ³5         ³ ³6         ³ ³+[plus]   ³
                     ³ CURSOR TO³ ³          ³ ³ CURSOR TO³ ³          ³
                     ³ END OF   ³ ³          ³ ³ END OF   ³ ³          ³
                     ³ LAST LINE³ ³          ³ ³ LINE     ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
                     ³1         ³ ³2         ³ ³3         ³ ³          ³
                     ³ ERASE TO ³ ³          ³ ³ ADVANCE  ³ ³          ³
                     ³ END OF   ³ ³          ³ ³  PAGE    ³ ³          ³
                     ³ LINE     ³ ³          ³ ³          ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
          ³0                    ³ ³.[period]              ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ




















                                                                    Page 31






          VT100 Keyboard Assignments                            PC-VT v10.0




          5.5  EVE Keypad Mapping


                  In VT100 Application Keypad mode, which is set by the VMS
          EVE  text  editor,  the  following  keys  cause   special  escape
          sequences to be  transmitted.  PC-VT  displays  the  Greek letter
          alpha on the status line to indicate that this mode is active.

                  Bits  in  the  SETUP frame select either VMS or UNIX mode
          and  select  EVE  or EVE keypad support for this special mapping.
          For  this  mapping,  VMS  mode  and EVE keypad support should  be
          selected.

               IBM PC Key ..................... EVE Function Performed

               Keypad + ........................................... Do
               Keypad - .......................... Moves the cursor to
                                             the beginning of the line
               Del key ........................................ Remove
               Backspace ................ Deletes the character to the
               or                      left of the cursor (DELETE key
               ALT-=                                     on the VT100)
               Ins key  .................................. Insert Here
               Home key ......................................... Find
               End key  ....................................... Select
               PgUp key .............................. Previous Screen
               PgDn key .................................. Next Screen
               CTRL-Home key .................................... Help
               CTRL-End key .......................... Forward/Reverse
               CTRL-PgUp key ...................................... Do
               CTRL-PgDn key .............................. Erase Word
               CTRL-Left Arrow key ................. Insert/Overstrike
               CTRL-Right Arrow key ..................... Move by Line
               SHIFT-Tab ......................... Moves the cursor to
                                             the beginning of the line
                                         (BACKSPACE key on the VT100).

                  Figure 5  shows this mapping. The name of the IBM  PC key
          is in the upper left of each key and the emulated key or function
          is then shown in the center of the key.














          Page 32






          PC-VT v10.0                                 VT100 & 4014 Emulator


                       Figure 5 PC-VT SPECIAL EVE KEY MAPPING


              FUNCTION KEYS                   SHIFTED FUNCTION KEYS


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F1        ³ ³F2        ³ ³F1        ³ ³F2        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³  FIND    ³ ³  HELP    ³ ³ FORWARD/ ³ ³   DO     ³
              ³          ³ ³          ³ ³  REVERSE ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F3        ³ ³F4        ³ ³F3        ³ ³F4        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³  SELECT  ³ ³  REMOVE  ³ ³ INSERT   ³ ³ MOVE BY  ³
              ³          ³ ³          ³ ³  HERE    ³ ³  LINE    ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F5        ³ ³F6        ³ ³F5        ³ ³F6        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³ not used ³ ³  CURSOR  ³ ³ not used ³ ³  ERASE   ³
              ³          ³ ³    UP    ³ ³          ³ ³   WORD   ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


              ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
              ³F7        ³ ³F8        ³ ³F7        ³ ³F8        ³
              ³          ³ ³          ³ ³          ³ ³          ³
              ³  CURSOR  ³ ³  CURSOR  ³ ³  CURSOR  ³ ³          ³
              ³   LEFT   ³ ³   DOWN   ³ ³   RIGHT  ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³  INSERT/ ³
                                                     ³OVERSTRIKE³
                                                     ³          ³
              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
              ³F9           F10       ³ ³F9        ³ ³F10       ³
              ³                       ³ ³          ³ ³          ³
              ³     NEXT              ³ ³ PREVIOUS ³ ³          ³
              ³     SCREEN            ³ ³  SCREEN  ³ ³          ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ












                                                                    Page 33






          VT100 Keyboard Assignments                            PC-VT v10.0


                      PC-VT SPECIAL EVE KEY MAPPING..continued


                     PC KEYPAD KEYS as MAPPED into EVE


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³7         ³ ³8         ³ ³9         ³ ³-[minus]  ³
                     ³          ³ ³          ³ ³          ³ ³ CURSOR TO³
                     ³  FIND    ³ ³  CURSOR  ³ ³ PREVIOUS ³ ³ START OF ³
                     ³          ³ ³    UP    ³ ³  SCREEN  ³ ³ LINE     ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³4         ³ ³5         ³ ³6         ³ ³+[plus]   ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ³  CURSOR  ³ ³          ³ ³  CURSOR  ³ ³          ³
                     ³   LEFT   ³ ³          ³ ³   RIGHT  ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
                     ³1         ³ ³2         ³ ³3         ³ ³          ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ³ SELECT   ³ ³  CURSOR  ³ ³   NEXT   ³ ³   DO     ³
                     ³          ³ ³   DOWN   ³ ³  SCREEN  ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
          ³0                    ³ ³.[period]              ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³   INSERT HERE       ³ ³      REMOVE           ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ




















          Page 34






          PC-VT v10.0                                 VT100 & 4014 Emulator


                      PC-VT SPECIAL EVE KEY MAPPING..continued


              PC KEYPAD KEYS as MAPPED into EVE - HOLD DOWN CTRL KEY


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³7         ³ ³8         ³ ³9         ³ ³-[minus]  ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ³   HELP   ³ ³          ³ ³    DO    ³ ³          ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³4         ³ ³5         ³ ³6         ³ ³+[plus]   ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ³ INSERT/  ³ ³          ³ ³ MOVE BY  ³ ³          ³
                     ³OVERSTRIKE³ ³          ³ ³  LINE    ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
                     ³1         ³ ³2         ³ ³3         ³ ³          ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ³ FORWARD/ ³ ³          ³ ³  ERASE   ³ ³          ³
                     ³ REVERSE  ³ ³          ³ ³   WORD   ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
          ³0                    ³ ³.[period]              ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ




















                                                                    Page 35






          VT100 Keyboard Assignments                            PC-VT v10.0




          5.6  VI Keypad Mapping


                  In VT100 Application Keypad mode,  which  is  set  by the
          UNIX  VI text editor, the following  keys  cause  special  escape
          sequences to  be transmitted. Some of these special keys transmit
          sequences that require two or more keystrokes on the VT100. PC-VT
          displays  the  Greek  letter alpha in the status line to indicate
          that this mode is active.

                  A bit in the SETUP frame selects either VMS or  UNIX mode
          for this special mapping. For this mapping, UNIX  mode  should be
          selected.

               IBM PC Key ...................... VI Function Performed

               Del key ............................ Delete a character
               ALT-= ......................... DELETE key on the VT100
               Ins key ........................... Go into Insert Mode
               Home key .................. Go to beginning of the file
               End key ......................... Go to end of the file
               PgUp key ........................... Scroll up the file
               PgDn key ......................... Scroll down the file
               CTRL-Home key ..................... Go to start of line
               CTRL-End key ........................ Go to end of line
               CTRL-PgUp key ................. Go to top of the screen
               CTRL-PgDn key .............. Go to bottom of the screen
               CTRL-Left Arrow key ............... Go to previous word
               CTRL-Right Arrow key .................. Go to next word

                  This VI keypad mapping  is  only  supported  in VT100/102
          mode not in VT52 compatibility mode.

                  Figure 6 shows this  mapping.  The name of the IBM PC key
          is in the upper left of each key and the emulated key or function
          is then shown in the center of the key.


















          Page 36






          PC-VT v10.0                                 VT100 & 4014 Emulator


                        Figure 6 VT100 SPECIAL VI KEY MAPPING


                      PC KEYPAD KEYS as MAPPED into VI
          ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³7         ³ ³8         ³ ³9         ³ ³-[minus]  ³
                     ³ GO TO    ³ ³  CURSOR  ³ ³  SCROLL  ³ ³          ³
                     ³ TOP      ³ ³    UP    ³ ³    UP    ³ ³          ³
                     ³ OF FILE  ³ ³          ³ ³          ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³4         ³ ³5         ³ ³6         ³ ³+[plus]   ³
                     ³ CURSOR   ³ ³          ³ ³ CURSOR   ³ ³          ³
                     ³ LEFT     ³ ³          ³ ³ RIGHT    ³ ³          ³
                     ³          ³ ³          ³ ³          ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
                     ³1         ³ ³2         ³ ³3         ³ ³          ³
                     ³ GO TO    ³ ³  CURSOR  ³ ³  SCROLL  ³ ³          ³
                     ³ END      ³ ³   DOWN   ³ ³   DOWN   ³ ³          ³
                     ³ OF FILE  ³ ³          ³ ³          ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
          ³0                    ³ ³.[period]              ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³   ENTER INSERT      ³ ³         DELETE        ³ ³          ³
          ³       MODE          ³ ³       A CHARACTER     ³ ³          ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ




















                                                                    Page 37






          VT100 Keyboard Assignments                            PC-VT v10.0


                       VT100 SPECIAL VI KEY MAPPING..continued


              PC KEYPAD KEYS as MAPPED into VI - HOLD DOWN CTRL KEY
          ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³7         ³ ³8         ³ ³9         ³ ³-[minus]  ³
                     ³ GO TO    ³ ³          ³ ³  GO TO   ³ ³          ³
                     ³ START OF ³ ³          ³ ³  TOP OF  ³ ³          ³
                     ³ LINE     ³ ³          ³ ³  SCREEN  ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ


                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿
                     ³4         ³ ³5         ³ ³6         ³ ³+[plus]   ³
                     ³ GO TO    ³ ³          ³ ³ GO TO    ³ ³          ³
                     ³ PREVIOUS ³ ³          ³ ³ NEXT     ³ ³          ³
                     ³ WORD     ³ ³          ³ ³ WORD     ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
                     ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
                     ³1         ³ ³2         ³ ³3         ³ ³          ³
                     ³ GO TO    ³ ³          ³ ³ GO TO    ³ ³          ³
                     ³ END OF   ³ ³          ³ ³ BOTTOM OF³ ³          ³
                     ³ LINE     ³ ³          ³ ³ SCREEN   ³ ³          ³
                     ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³          ³
                                                            ³          ³
                                                            ³          ³
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³          ³
          ³0                    ³ ³.[period]              ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ³                     ³ ³                       ³ ³          ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ




















          Page 38






          PC-VT v10.0                                 VT100 & 4014 Emulator




          5.7  Control Function Keys


           CTRL-F1:      PC-VT enters the SETUP frame. See Chapter 6.

          CTRL-F2:       Lets   you   change   the  default  directory  for
                         uploading and downloading files. See Chapter 8.

          CTRL-F3:       Receives a file (ASCII,  XMODEM,  or  KERMIT). See
                         Chapter 8.

          CTRL-F4:       Transmits  a file (ASCII, XMODEM, or KERMIT).  See
                         Chapter 8.

          CTRL-F5:       Prints  screen.  The  screen  is  printed  on  the
                         selected  printer (LPT1 or LPT2), if present.  The
                         printer is selected in the SETUP B frame.

                         Performs the  same function as receipt of a "ESC [
                         i" sequence. If the Print Termination Character is
                         set  in  the  SETUP  B  frame,  the  printer paper
                         advances to the top of  the  next  page  after the
                         screen is printed.

          CTRL-F6:       Echoes to selected printer (LPT1 or LPT2). Toggles
                         On/Off   echoing  to  the  selected  printer,   if
                         present. The printer is selected  in  the  SETUP B
                         frame.   Prints   all   characters   received   or
                         transmitted to/from the host. Characters displayed
                         on the status line (line 25) are never printed.

                         Performs the  same function as receipt of "ESC [ ?
                         5  i"  and  "ESC  [  ?  4  i"  sequences. A 'P' is
                         displayed in  column  42  of  the  status  line to
                         remind you that printer  echo  is  on.  A Formfeed
                         which is normally translated to a linefeed  by PC-
                         VT is  retained as a formfeed when printer echo is
                         on.

          CTRL-F7:       Sends a break to  the  host.  Confirmation  of the
                         operation is a click at the start of the break and
                         another click  at the end of the operation. If the
                         disconnect  character  feature  is selected in the
                         SETUP B frame, PC-VT sends an EOT character (ASCII
                         4) before it sends the break. A BREAK is a "space"
                         condition   on   the  line  for   at   least   275
                         milliseconds. To send  a long BREAK or disconnect,
                         press ALT-Q.

          CTRL-F8 or ALT-C :
                         Terminates PC-VT and returns to DOS.  Use  the ALT
                         key for PCjr's.


                                                                    Page 39






          VT100 Keyboard Assignments                            PC-VT v10.0


          CTRL-F9 or ALT-V :
                         Enters  the  DIALING  frame.  See  Chapter  9  for
                         instructions. The ALT key is for PCjr users.

          CTRL-F10 or ALT-O :
                         Enters  the  MACRO   frame.  See  Chapter  10  for
                         instructions. The ALT key is for PCjr users.


          5.8  ALT Keys


          ALT-F1 thru ALT-F10 :
                         Can be used as macro keys.

          ALT-B:         Emulates the HERE IS  key  on  the VT. PC-VT sends
                         the answerback message which is set in the SETUP B
                         frame.

          ALT-H:         Enters the HELP frame.  Once  you  are in the HELP
                         frame, use the PgDn key to look at  the  next HELP
                         page. Use the PgUp key  to  look  at  the previous
                         HELP page and use  the  Esc  key  to exit HELP and
                         return to  the  emulator.  HELP  works  from  most
                         frames  and is context sensitive. For example,  if
                         you need HELP within  the  SETUP  frames,  you get
                         SETUP information.

          ALT-K :        Starts  up  the KERMIT module.  See  the  attached
                         KERMIT document for details on its command set.

          ALT-F :        Starts  up  another  copy  of COMMAND.COM. This is
                         done without  terminating  PC-VT  or  breaking the
                         host  connection.   Once the  new  COMMAND.COM  is
                         started, you  can run any DOS function or other PC
                         program.  CAUTION : You should be careful that you
                         don't   run   a  program  that   uses   the   same
                         communications port as PC-VT is using.   The other
                         program may leave the port in an unexpected state.
                         PC-VT may not then be able to get  control  of the
                         port again.   Also be careful that you don't alter
                         any files which  PC-VT  may be using. To exit from
                         the new copy of COMMAND.COM and  return  to PC-VT,
                         type "exit" at the command prompt.

          ALT-Q :        Long BREAK or Disconnect. Causes PC-VT to drop the
                         RTS   and   DTR   lines   for   one-half   second.
                         Confirmation of the operation is  a  click  at the
                         start of the long BREAK along  with  another click
                         at the end of  the  operation.  If  the disconnect
                         character feature  is  selected  in  the  SETUP  B
                         frame,  PC-VT  sends an EOT  character  (ASCII  4)
                         before it sends the BREAK.



          Page 40






          PC-VT v10.0                                 VT100 & 4014 Emulator


          ALT-X :        Resets XOFF Flag. If PC-VT  has  received  an XOFF
                         character, PC-VT stops transmitting. If you type a
                         character,  PC-VT beeps and ignores the key.  This
                         is  part  of the VT100  definition.  If  something
                         happens  and  PC-VT receives an  XOFF  because  of
                         garbage on the  line,  you can reset the XOFF flag
                         by  pressing  ALT-X.   PC-VT  tells  you  when  it
                         receives the XOFF  by  displaying  an  'X'  on the
                         status line.

          ALT-Z :        Hangs  up  the  phone.  PC-VT  performs  the  same
                         functions as if you had entered the  DIALING frame
                         and pressed F5. That is, the Hayes compatible hang
                         up command is sent to the modem.


          5.9  Scroll Buffer


                  When  you  press  the SCROLL LOCK key, you can have PC-VT
          recall previous screens  of  information.  PC-VT  saves  the last
          eight 80 column screens or the last five 132 column screens.

                  To start this feature, set the Scroll Buffer selection in
          the SETUP B frame. This feature  needs  a lot of memory and PC-VT
          tries to get it from DOS. If PC-VT  can't  get  the  memory, this
          feature will not function even if selected.

                  You  can start this feature manually  as  well  from  the
          VT100 communications frame by pressing ALT-S. If you  do  set the
          bit in the  SETUP  B  frame,  then PC-VT attempts to allocate the
          Scrolling Buffer each time that it starts. The  DMA  feature must
          also be selected  in  the  SETUP  B frame since the Scroll Buffer
          directly accesses video memory.

                  To activate  the recall, press the SCROLL LOCK key. 'SCR'
          appears on the status line. At this point, you can scroll through
          the previous screens by pressing these keys:


          PgUp :         recalls  the  previous screens, one  screen  at  a
                         time.

          PgDn :         moves forward one screen at a time.

          Home :         recalls the oldest information in the buffer.

          Up Arrow :     recalls the previous screens one line at a time.

          Down Arrow :   once you go backward in the buffer, this key moves
                         forward one line at a time.

          End :          recalls  the  last active screen  but  remains  in
                         Scroll Buffer mode.


                                                                    Page 41






          VT100 Keyboard Assignments                            PC-VT v10.0


          SCROLL LOCK :  clears  the Scroll Lock, displays the last  active
                         screen, and resets the screen to normal operation.

          Shift PrtSc :  prints the screen on the  printer.  You  can print
                         any previous screen by using the movement keys and
                         then pressing this key.

          Keypad + (plus):
                         dumps the screen  onto  a  disk  file.  The screen
                         information is appended to the file if  it already
                         exists.  The  file is named  SCRNDUMP.DAT  and  is
                         created on the  default drive. Trailing spaces are
                         removed from  each  screen  line  as  the  data is
                         written to disk. You can dump any  previous screen
                         by using the movement keys and then  pressing this
                         key.

          Keypad - (minus) :
                         dumps the entire Scroll Buffer onto  a  disk file.
                         The  Scroll Buffer information is appended to  the
                         file if  it  already  exists.  The  file  is named
                         SCRNDUMP.DAT and is  created on the default drive.
                         Trailing spaces are  removed from each screen line
                         as the data is written to disk.

                  The scrolling stops at each end of the  buffer.  That is,
          once you reach the oldest line, pressing the Up Arrow or PgUp key
          does nothing.

                  The Scrolling  Buffer  is  cleared  whenever  you  switch
          between 80 and 132 column modes.


          5.10  Keyboard Redefinition


                  You can download new  definitions  for  all  function and
          editing keys  in both numeric keypad and application keypad modes
          for both the VT100 and VT52 emulators.

                  The escape sequence is:

          ESC [ Pt ; Pk ; "string" p

          sets extended key Pk in translation table Pt to the string given.
          The double quotes and  all  other  characters shown are required.
          The numbers Pt and Pk must be sent as ASCII characters  just like
          all other sequences.

                  An  error  code  is available with the "ESC [ ?  1  0  n"
          sequence. See the technical appendix.

                  The string can be  any  sequence  of ASCII characters. It
          cannot include a carriage return or escape character. If you need


          Page 42






          PC-VT v10.0                                 VT100 & 4014 Emulator


          to include a carriage return, use the tilde character '~'. If you
          need an  escape character, use the underline character '_'. PC-VT
          translates them when it processes the string.

                  Pt indicates the internal  table  which  is  changed. The
          tables are:

                         0       Reserved    to    indicate    Macro    Key
                         redefinition. See Chapter 10.
                         1 VT100 Numeric Keypad Mode.
                         2 VT52 Numeric Keypad Mode.
                         3 VT100 Application Keypad Mode if VMS and EDT are
                         selected in SETUP B.
                         4  VT100  Application   Keypad  Mode  if  UNIX  is
                         selected in SETUP B.
                         5 VT52 Application Keypad Mode.
                         6 VT100 Application Keypad Mode if VMS and EVE are
                         selected.
                         7-15 Reserved.

                  Pk indicates the  extended  function or editing key to be
          redefined. They are:

                         3 ......................................... CTRL-@
                         15 ..................................... SHIFT-Tab
                         16-25 .................... ALT-Q,W,E,R,T,Y,U,I,O,P
                         30-38 ...................... ALT-A,S,D,F,G,H,J,K,L
                         44-50 .......................... ALT-Z,X,C,V,B,N,M
                         59-68 ................................ F1 thru F10
                         71 .......................................... Home
                         72 ...................................... Up Arrow
                         73 .......................................... PgUp
                         74 .............................. Keypad Minus Key
                         75 .................................... Left Arrow
                         77 ................................... Right Arrow
                         78 ............................... Keypad Plus Key
                         79 ........................................... End
                         80 .................................... Down Arrow
                         81 .......................................... PgDn
                         82 ........................................... Ins
                         83 ........................................... Del
                         84-93 .......................... SHIFT-F1 thru F10
                         94-103 .......................... CTRL-F1 thru F10
                         104-113 .......................... ALT-F1 thru F10
                         115 .............................. CTRL-Left Arrow
                         116 ............................. CTRL-Right Arrow
                         117 ..................................... CTRL-End
                         118 .................................... CTRL-PgDn
                         119 .................................... CTRL-Home
                         120-129 ............................. ALT-1 thru 0
                         130 ................................... ALT-(dash)
                         131 .................................. ALT-(equal)
                         132 .................................... CTRL-PgUp



                                                                    Page 43






          VT100 Keyboard Assignments                            PC-VT v10.0


                  Remember that Application Keypad Mode is set and reset by
          the host computer. You can tell that it is selected because PC-VT
          displays the Greek letter alpha in the middle of the status line.
          Application Keypad Mode is usually set by editors,  such  as EDT,
          EVE and VI, and other programs,  such  as VMS Mail, which use the
          full screen capabilities of the VT100.

                  PC-VT can handle up  to  1000  characters of new strings.
          After that, additional redefinitions are ignored.  The  change is
          permanent until PC-VT is terminated and restarted.

                  Caution : if you redefine CTRL-F8, the user  will  not be
          able to terminate PC-VT without turning off the PC.

                  Examples (spaces for clarity only):

                         To set the Home key  in  the  Numeric  Keypad mode
                         table:

          ESC [ 1 ; 71 ; "run able~dir~set def [dir1.dir2]~logout~" p

                         To set  the  PgDn  key  in  the  VT100 Application
                         Keypad Mode VMS  table  to  produce  a  down arrow
                         sequence:

          ESC [ 3 ; 80 ; "_OB" p

                         To  set  the  ALT-H  key  to send the  PF2  Escape
                         sequence   followed   by   the  Keypad  Enter  key
                         sequence:

          ESC [ 3 ; 35 ; "_OQ_OM" p


                  This redefinition can also be done locally within the PC.
          Use  your  favorite  text editor and create a file which contains
          all of the redefinitions which you wish to make.  Then  start  up
          PC-VT. Use the "view a file" option of Transmit (Upload)  file to
          have PC-VT send the file to itself. PC-VT  interprets  the Escape
          sequences and redefines the keys. For more information on viewing
          a file, see the Chapter 8 section titled Viewing Files or look in
          the index under Viewing a File.

                  Here is an example of a file which when received by PC-VT
          will  cause the KEYPAD to map in a reasonable way for the VMS EVE
          editor. This mapping is the same as the mapping which you  get if
          you select EVE keypad support in the SETUP B frame.









          Page 44






          PC-VT v10.0                                 VT100 & 4014 Emulator


          Assign KEYPAD Keys for the EVE/TPU VMS Text Editor
          -------------------------------------------------
          (Home) = Find    <ESC>[3;71;"_OP"p
          (up arrow) = Up Arrow <ESC>[3;72;"_Ou"p
          (PgUp) = Prev Screen <ESC>[3;73;"_On"p
          (left arrow) = Left Arrow <ESC>[3;75;"_Oq"p
          (right arrow) = Right Arrow <ESC>[3;77;"_Os"p
          (End) = Select <ESC>[3;79;"_Ow"p
          (down arrow) = Down Arrow <ESC>[3;80;"_Or"p
          (PgDn) = Next Screen <ESC>[3;81;"_Op"p
          (Ins) = Insert Here <ESC>[3;82;"_Oy"p
          (Del) = Remove <ESC>[3;83;"_Ox"p
          (ctrl Home) = Help <ESC>[3;119;"_OQ"p
          (ctrl PgUp) = Do <ESC>[3;132;"_OS"p
          (ctrl right arrow) = Move by Line <ESC>[3;116;"_Om"p
          (ctrl End) = Forward/Reverse <ESC>[3;117;"_OR"p
          (ctrl PgDn) = Erase Word <ESC>[3;118;"_Ol"p
          (ctrl left arrow) = Insert Overstrike <ESC>[3;115;"_OM"p
          EOF

                  You must replace the word <ESC> with the escape character
          (ASCII 27).

                  Note: The Pt >  0  sequence can be used to reassign Macro
          Keys as well as any other key. If this is used, the user will not
          see the reassignment in the MACRO frame. You should use the  Pt =
          0 sequence for Macro key reassignment.





























                                                                    Page 45






          VT100 Keyboard Assignments                            PC-VT v10.0


























































          Page 46






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                      Chapter 6

                                    SETUP Frames


                  The SETUP frames are accessed  by  pressing  CTRL-F1 from
          the VT100 communications frame. SETUP  A  is  entered  first. The
          contents  of  the  communications  frame  are  preserved  and are
          restored when you exit SETUP.

                  The SETUP frames let you set program defaults used by all
          of the emulators within PC-VT.

                  PC-VT includes nine  frames  in which you can control the
          operation of the emulator.


          6.1  SETUP A




                  The SETUP A frame is used to perform the functions listed
          below. The bottom two lines of the frame represent the  tab stops
          which are set. The bottom line counts the columns  and  the  line
          above it shows  a "T" in each column where a tab is set. Here are
          the functions  available in SETUP A:


          Exit SETUP :   The ESC key or the CTRL-F1 key combination returns
                         PC-VT to the communications frame.  If unsolicited
                         terminal  parameter  reported  is enabled in VT100
                         emulation  mode,  the   terminal   parameters  are
                         reported.  This does not occur in VT102  emulation
                         mode.

          Reset :        The "0"  key  clears  the  tabs  and  features and
                         reloads them  from  the  USER  MEMORY  disk  file,
                         PARAMS.DAT,  on  the  default  drive.  PC-VT  then
                         returns to the communications frame.

          Set/Clear Tabs:
                         The "2" key sets  or  clears  a  tab at the column
                         position of the cursor. The left and right arrows,
                         the tab key, the space  bar, and the ENTER key can
                         be used to move the  cursor to the column in which
                         you want to set or clear the tab. A "T" appears to
                         indicate that a tab was  set or the "T" is blanked


                                                                    Page 47






          SETUP Frames                                          PC-VT v10.0


                         to indicate that  a  tab  was  cleared.  In either
                         case, the  character  is  highlighted  to indicate
                         that a change was made.

          Clear All Tabs:
                         The "3" key clears all tab stops. All  of  the "T"
                         tab stop indicators are cleared.

          Go to SETUP B :
                         The "5" key selects the SETUP B frame.

          Store into USER MEMORY:
                         The "S" key stores all currently set tab stops and
                         features selected by  SETUP  B onto a disk file on
                         the PC-DOS  default drive. The name of the file is
                         PARAMS.DAT.

          Reset :        The "R"  key  clears  the  tabs  and  features and
                         reloads them  from  the  USER  MEMORY  disk  file,
                         PARAMS.DAT, on the default drive. PC-VT remains in
                         the SETUP A frame.

          Select General Default:
                         The "D"  key clears any user set tabs and features
                         (from SETUP B) and resets  them  to  PC-VT defined
                         defaults.

          Select Tab Default:
                         The "T" key clears  any  user  set tabs and resets
                         them to every 8 columns as follows:

                         Columns 9, 17, 25, 33, 41, 49, 57, 65, and 73.

                         A  "T" appears in each of  these  columns  on  the
                         second line from  the  bottom of the SETUP A frame
                         to indicate that a tab is set.

          Incr/Decr Line Turnaround Character = xx (ASCII : y) :
                         This  character is used in conjunction with  ASCII
                         file upload.  When uploading, PC-VT can be told to
                         wait for this character (the =t option) to be sent
                         by the Host before PC-VT sends the next line.  For
                         our purposes, a line ends when  a  carriage return
                         (ASCII  13)  is  uploaded.  The value of xx is the
                         ASCII value  of the character, and y is the actual
                         ASCII  character.  The character is not  displayed
                         if  it  is  less than 32 or equal to 255.  The "L"
                         key  increments this value and the "K"  decrements
                         it.    You  must  execute  a "S - store into  USER
                         MEMORY" command to  save  the  new  value  of this
                         character on disk.  Otherwise, the next  time that
                         you  start PC-VT, the original value is  restored.
                         The  first time that PC-VT starts, this  character
                         is set to the dollar sign character, ASCII 36.


          Page 48






          PC-VT v10.0                                 VT100 & 4014 Emulator


          6.2  SETUP B


                  The SETUP B frame is used to perform the functions listed
          below. The bottom line of the frame represents the features which
          are  set  or  reset.  See  the  next  section  for details of the
          features.  The  number  of data bits  and  the  parity  type  are
          displayed. The COM port speed is displayed. The selected COM port
          is displayed.  LPTx is displayed to indicate the selected printer
          (either LPT1 or LPT2).

                  The currently selected host is displayed in the center of
          the screen. If  no  host  has  been selected in the DIALER frame,
          this field displays as  all  periods.  See  Chapter 9 for details
          about saving unique host setup information.

                  The default file transfer mode  is  displayed.  This mode
          will  be  used  whenever  a  file transfer is started without  an
          option.  Toggle  through  the  options  by  using  the  "x"  key.
          Permanently save the selected option by pressing "s" in the SETUP
          A frame to  save  the  USER  MEMORY  on disk. Modes which are not
          supported in both receive and transmit are set as follows:


                                  Receive                 Transmit
          Mode                    File                    File
          XMODEM                  XMODEM                  XMODEM
          XMODEM CRC              XMODEM CRC              XMODEM CRC
          ASCII (wait for LF)     ASCII (wait for LF)     ASCII
          ASCII (immediate)       ASCII (immediate)       ASCII
          ASCII (CTRL-Z)          ASCII                   ASCII (CTRL-Z)
          ASCII with Turnaround   ASCII                   ASCII with
          Turnaround
          View a File             ASCII                   View a File
          KERMIT                  KERMIT                  KERMIT

          See Chapter 8 for details on each of these modes.

                  The selected monitor  mode  is  displayed  to  show which
          monitor is being used by PC-VT. The monitor mode is selected when
          you first start up PC-VT and are saved  when  you  save  the USER
          MEMORY data on  disk.  Check  the  index  entry  on  Command Line
          Options for more information. Monitor modes are:

          Default:       PC-VT uses either the IBM  monochrome  or  the IBM
                         Color  Graphics  Adapter  whichever is the default
                         monitor when PC-VT is stated.

          Both:          PC-VT uses both  the  IBM  monochrome  or  the IBM
                         Color Graphics Adapters. The monochrome monitor is
                         used for VT emulation and the CGA is used for 4014
                         emulation.




                                                                    Page 49






          SETUP Frames                                          PC-VT v10.0


          Everex Edge:   PC-VT  uses  the  Everex  Edge card and monochrome
                         monitor  for both VT and 4014 Emulation.  Supports
                         132 column mode in the  VT emulator and 720 by 348
                         high resolution graphics in the 4014 emulator.

          Hercules:      PC-VT   uses   the   Hercules  Graphics  card  and
                         monochrome monitor for both VT and 4014 Emulation.
                         Supports 720 by 348  high  resolution  graphics in
                         the 4014 emulator.

                  Here are the functions available in the SETUP B frame:


          Exit SETUP :   The ESC key  or  CTRL-F1 exits SETUP B and returns
                         to  the  communications   frame.   If  unsolicited
                         terminal  parameter  reported  is enabled in VT100
                         emulation  mode,  the   terminal   parameters  are
                         reported.  This does not occur in VT102  emulation
                         mode.

          Go to SETUP A :
                         The "5" key selects the SETUP A frame.

          Toggle 1/0:    The "6"  key sets(1) or resets(0) a feature at the
                         column position of the cursor. The left  and right
                         arrows, the  tab key, the space bar, and the ENTER
                         key can be used to move the cursor  to  the column
                         in which you want to  set  or  clear  the feature.
                         Features displayed  with  an  "X"  are  set  to an
                         automatic default  and  cannot  be  changed. Other
                         features change from a "1" to a "0" or from  a "0"
                         to a "1" to indicate that the state of the feature
                         has  been  changed.  Features marked as "Reserved"
                         should not be toggled. The digit is highlighted to
                         indicate that a change was made. To preserve these
                         features in  your USER MEMORY disk file use the "S
                         - Store into  USER  MEMORY" command in the SETUP A
                         frame. Otherwise, the  old values will be reloaded
                         the next time PC-VT starts.

          COM Port Selection :
                         COM1 or COM2  can  be selected by flipping the 4th
                         bit  of  the  6th  group  of feature bits  on  the
                         bottom of the SETUP B frame. The word COM1 or COM2
                         displays next to  the  word MODEM on this frame to
                         indicate which RS232  port  is in use by PC-VT. To
                         change ports, just go to SETUP B frame, space over
                         to the 4th bit of the 6th group and then press the
                         "6" key. This causes the 1 or 0 in the feature bit
                         to  flip.  Then  return to the SETUP  A  frame  by
                         pressing "5" and store  the  new  value  into USER
                         MEMORY by pressing "S".




          Page 50






          PC-VT v10.0                                 VT100 & 4014 Emulator


          Modem Speed Control:
                         The "7" key causes PC-VT  to  display  the various
                         modem  speeds  supported. The  currently  selected
                         speed is displayed under the  MODEM  title  on the
                         screen.  Press  the  "7"  key repeatedly until the
                         speed  you  need  is  displayed.    The  new speed
                         selected is highlighted  to indicate that a change
                         was made. The supported speeds are:

                               100 baud                150 baud
                               300 baud                600 baud
                              1200 baud (default)     2400 baud
                              4800 baud               9600 baud

                         To  preserve  this speed selection  in  your  USER
                         MEMORY  disk file use the "S  -  Store  into  USER
                         MEMORY"  command in the SETUP A frame.  Otherwise,
                         the old  values will be reloaded the next time PC-
                         VT starts.

          Select Data/Parity Bits:
                         The "P" key causes PC-VT  to  display  the various
                         data  bits/parity  bits supported.  The  currently
                         selected  Data  bits/Parity  bits  combination  is
                         displayed  on  the  screen  under the MODEM title.
                         Press  the  "P"  key  repeatedly  until  the  data
                         bits/parity   bits   combination   you   need   is
                         displayed. The  new  selection  is  highlighted to
                         indicate  that  a  change  was made. The supported
                         combinations are:

                              7O ...... 7 data bits - odd parity
                              7E ...... 7 data bits - even parity
                              7N ...... 7 data bits - no parity
                              8O ...... 8 data bits - odd parity
                              8E ...... 8 data bits - even parity
                              8N ...... 8 data bits - no parity
                              (default)

                         The 7E setting is  the  best  for  UNIX and the 8N
                         setting is best for VMS.

                         To preserve these Data bit/Parity bit combinations
                         in your USER MEMORY disk file use the  "S  - Store
                         into USER  MEMORY" - command in the SETUP A frame.
                         Otherwise,  the  old  values  will be reloaded the
                         next time  PC-VT starts. If you are running a 212A
                         modem,  certain  of  the data bits/parity/stop bit
                         combinations are invalid. Check your  modem manual
                         for the valid combinations.

                         Note  that  actual  parity  checking is enabled by
                         setting  a feature in this frame. Parity  checking
                         defaults to off. See the next section.


                                                                    Page 51






          SETUP Frames                                          PC-VT v10.0


          Set Answerback Message:
                         The "A" key  permits  you to enter a message which
                         PC-VT  uses  to  respond  to  an  Enquire  control
                         character. Any character with an ASCII code from 0
                         to 127 can be entered in  this  message (Including
                         the use of the ALT key and the numbers on the PC's
                         keypad to enter  special characters). To enter the
                         message,  press "A".  PC-VT  displays  the  prompt
                         "A=". The prompt  is highlighted and blinking. You
                         may then type in the message. The  first character
                         typed  is  considered  a  delimiter by PC-VT. This
                         character must not be  present  in  the answerback
                         message itself and is  used  only  to  bracket the
                         message  since  control characters  like  carriage
                         return can be part of the  message.  Following the
                         message,  type the  delimiter  character  and  the
                         message is stored in memory.

                         If you make a  typing  mistake,  you must type the
                         delimiter  character  and  start the process over.
                         This is  because the backspace key does not act as
                         a text editor  but  is actually entered as part of
                         the answerback  message.  While  you  are entering
                         this message, non-displayable characters are shown
                         as  a  diamond.  The  message  is  highlighted  to
                         indicate that a change is being made.  To preserve
                         this message in your USER MEMORY disk file use the
                         "S  - Store into USER MEMORY"  -  command  in  the
                         SETUP A frame. Otherwise, the old message, if any,
                         will be reloaded the next time PC-VT starts.

                         The  default answerback message is null, that  is,
                         nothing  is transmitted in response to an  Enquire
                         control character.

                         The ALT-B key on the PC emulates the  HERE  IS key
                         on  the  VT  and causes this message to be sent to
                         the host.

          Change Default File Transfer Mode:
                         The "X"  key  lets  you  change  the  default file
                         transfer  mode.  Pressing  that  key   shows  each
                         possible mode. To  preserve this selection in your
                         USER MEMORY disk file use the "S - Store into USER
                         MEMORY" - command in the SETUP A frame. Otherwise,
                         the old transfer mode  will  be  set the next time
                         PC-VT starts.


          6.2.1  SETUP B Features and Defaults


                  The  SETUP  B  frame is used to select features of PC-VT.
          The  features are listed below along  with  their  defaults.  The


          Page 52






          PC-VT v10.0                                 VT100 & 4014 Emulator


          procedures for changing and saving these features  were described
          in the first part of this section. As you move the  cursor across
          the  bottom  of  the  frame   using  the  cursor  keys,  a  short
          description  of the meaning of the feature  and  its  values  are
          displayed.

                  A  default  of  (X)  indicates  that the feature  is  not
          supported or   is  reserved.  The  default  values  are  shown in
          parentheses.


          Group 1


          Scroll (X)     The design of  the  IBM PC does not support smooth
                         scroll.

          Auto Repeat (1)
                         0 = Disable autorepeat. PC-VT can only approximate
                         this function  since  it  is  handled  within  the
                         keyboard.  PC-VT clears the keyboard buffer  after
                         each  key  is read. This  effectively  clears  the
                         buffer of any auto repeated characters.

                         1 = Enable autorepeat.

          Screen Background (0)
                         0 = dark background

                         1 = light background

          Cursor (0)     0 = underline cursor

                         1 = block cursor


          Group 2


          Margin Bell (0)
                         Selects margin bell.
                         0 = Off

                         1 = On
                         If this feature  is  turned  on,  PC-VT  beeps the
                         speaker each time that the cursor  enters  the 8th
                         rightmost column  from  the  9th  rightmost column
                         under control of the keyboard  or  the  host. This
                         feature is best used when entering  text  from the
                         keyboard.  Any  other  use may cause unpredictable
                         results especially in full screen modes.





                                                                    Page 53






          SETUP Frames                                          PC-VT v10.0


          VMS Editor Support (0)
                         Selects  Keypad  mapping  for  VMS   editor.  Also
                         selectable from the host, see Appendix J.
                         0 = Keypad supports the EDT editor.

                         1 = Keypad supports the EVE editor.

          ANSI/VT52 (1)  Selects terminal mode.
                         0 = VT52 compatibility mode.

                         1  = ANSI mode. That is,  either  VT100  or  VT102
                         depending on the setting of the Terminal  Type bit
                         in Group 6 below.

          Auto XON/XOFF (1)
                         0 = XOFF is ignored. PC-VT's  buffer  may overflow
                         without warning or indication.

                         1  =  XOFF stops PC-VT  from  transmitting.  PC-VT
                         stops  transmitting characters  when  an  XOFF  is
                         received and transmits an  XOFF  when  75%  of its
                         receive buffer is  full (1536 characters). It then
                         transmits XON when the buffer has been  emptied to
                         10% full (204 characters). If the host ignores the
                         XOFF  character  and  continues  to   send,  PC-VT
                         displays a '#' character to indicate that data has
                         been lost.  When PC-VT receives an XOFF, an 'X' is
                         displayed in  column 41 of the status line. If you
                         try to type a character when the 'X' is displayed,
                         PC-VT beeps and rejects  it.  If  the 'X' comes on
                         because  of noise on the communications line,  you
                         can clear it by  pressing  the  ALT-X key. See the
                         ALT-X  key  definition in the  appendix  for  more
                         details.


          Group 3


          Character Set (0)
                         0 = Selects US Characters. The US character set is
                         selected as the default.

                         1 = Selects UK Characters. The UK character set is
                         selected as the default.
                         (Note that the only difference between the  two is
                         the SHIFT-3 character. In  the  US  set, it is the
                         "#" sign. In the UK set, it is the UK Pound sign.)

          Auto Wrap (0)  0 = Auto wrap  off.  If the cursor is at the right
                         margin  and  another  character is received, PC-VT
                         displays that character and all following received
                         characters   at   the   right   margin   position,
                         effectively writing over one another.


          Page 54






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         1 = Auto wrap on -  If  the cursor is at the right
                         margin  and  another  character is received, PC-VT
                         performs a  carriage  return  and  linefeed before
                         displaying that character. Be careful when you use
                         this feature. When performing full screen editing,
                         the host  may lose track of the cursor position if
                         you set autowrap  locally  in PC-VT and you do not
                         inform the host. In VMS, look at the  SET  TERM as
                         well as commands in the EDT editor.

          Linefeed / New Line (0)
                         0  =  LF/NL  off  -  Pressing ENTER sends  only  a
                         carriage return  to the host. The host must echo a
                         carriage return and linefeed to move the cursor to
                         the beginning of the next line.

                         1  =  LF/NL  on  -  Pressing  ENTER  sends both  a
                         carriage return and  a  linefeed  to  the  host. A
                         linefeed is processed just like a carriage return.

          Local Echo (0)
                         0 = Local echo off. - The host must echo  back all
                         typed characters in order for them to be displayed
                         on   the  screen.  Linefeed  characters  are   not
                         transmitted  during an ASCII file transfer.

                         1 = Local echo on -  PC-VT  automatically displays
                         all characters typed. The host need not  echo them
                         back. Linefeed characters  are  transmitted during
                         an ASCII file transfer.


          Group 4


          Print Termination Character (1)
                         0 = none - No control characters are  sent  to the
                         printer following a print screen operation.

                         1 = Form feed - A form feed is sent to the printer
                         following a print screen operation.

          Print Extent (1)
                         0 = Scrolling region -  A  print  screen operation
                         prints the scrolling region  as  set  by  the host
                         computer only.

                         1 =  Full screen - A print screen operation prints
                         the entire screen.

          Stop Bits (0)  0 = 1 stop bit is used by the RS232 interface.

                         1 = 2 stop bits are used by the RS232 interface.



                                                                    Page 55






          SETUP Frames                                          PC-VT v10.0


          Receive Parity (0)
                         0 = Parity on received data is not checked.

                         1 = Parity checking is enabled.  PC-VT  displays a
                         '!' character in place of the  character  with the
                         bad parity.


          Group 5


          Backspace (0)  0 = Send the  backspace  key as 7Fh (ASCII 127)  -
                         the VT100 DELETE key.

                         1  =  Send  the backspace key as 08h  - the IBM PC
                         standard. When you are doing this,  you  can still
                         send a DEL (ASCII 127) by  pressing  ALT-=. (Press
                         the ALT key and  the  equal  sign  key at the same
                         time.)

          Disconnect Character Enable (0)
                         0 = Terminal ignores the disconnect character.

                         1 = If PC-VT receives the  disconnect  character (
                         an EOT with an ASCII value of 4),  it  transmits a
                         sustained  Break and  disconnects  from  the  host
                         computer.

          Fast Screen (0)
                         0 =  Prevent  PC-VT  from  doing  direct  reads or
                         writes into video memory.  This  is  the  most DOS
                         compatible mode. It is also the slowest  mode. The
                         color graphics display adapter may not be  able to
                         keep up with 9600 baud  in this mode. Note that no
                         data will be  lost.  PC-VT will send XOFF and XON.
                         Must be set  to  0  for  TopView if you want to do
                         windowing.

                         1 = Permit PC-VT to  do  direct  reads  and writes
                         into   video  memory.   This   mode   will   cause
                         interference, or  "snow",  on  the  color graphics
                         display adapter but PC-VT should be  able  to keep
                         up with 9600 baud. For the  monochrome  card, this
                         setting has no effect.

          Operating System (1)
                         0 = The UNIX VI keypad mapping is selected for the
                         IBM PC keypad. Control-D is selected as the End of
                         File character for ASCII file upload.

                         1 = The VMS EDT keypad mapping is selected for the
                         IBM PC keypad. Control-Z is selected as the End of
                         File character for ASCII file upload.
                         See  Chapter  5  for  the  VT  keypad  mapping and


          Page 56






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         Chapter 8 for  ASCII file upload description. Also
                         selectable from the host, see Appendix J.


          Group 6


          Printer (0)    0 = LPT1 is selected.

                         1 = LPT2 is selected.

          Buffer Size (1)
                         0 = Use a 256 byte communications buffer.

                         1 = Use a 2048 byte communications buffer.
                         Use  of  the  larger  buffer causes fewer XON/XOFF
                         sequences  between  PC-VT and the  host.  It  also
                         slows the response to  CTRL-C,  CTRL-O  and CTRL-Y
                         commands. For some text editors which  do  not use
                         XON/XOFF, the larger buffer size works better.

          Terminal Type (0)
                         0 = PC-VT emulates a VT102.

                         1 = PC-VT emulates a VT100.

          COM Port (0)   0 = PC-VT uses COM1 as the communications port.

                         1 = PC-VT uses COM2 as the communications port.


          Group 7


          DMA (1)        0 = Prevents PC-VT from doing direct  memory reads
                         or writes  into  video  memory  while  saving  the
                         screen when you switch  into  the  SETUP  or other
                         auxiliary frame. The screen  will  still  be saved
                         but at the much slower pace of the  BIOS.  This is
                         the most DOS compatible mode. Must be set to 0 for
                         TopView if you want to do windowing.

                         1 = Permit PC-VT  to  use  direct memory reads and
                         writes  into video memory while saving the  screen
                         when you switch into the SETUP or  other auxiliary
                         frame. Permits operation of  Scroll  Buffer  - see
                         Group 10 below.

          Reserved (X)   Reserved for PC-VT.

          Clock (1)      0 = Do not display the clock and  MODEM  status on
                         the status line.




                                                                    Page 57






          SETUP Frames                                          PC-VT v10.0


                         1 = Display the time of day clock and MODEM status
                         on the status line.

          256 Char (0)   0 = If 8 bit data is selected for receive, the 8th
                         bit (high  order bit) is cleared to binary zero if
                         it is a binary one when  received.  PC-VT displays
                         characters only from the  first  128  ASCII codes.
                         (XMODEM always uses all 8 bits.)

                         1 = If 8 bit data is selected for receive, the 8th
                         bit is interpreted as the high order bit  of  an 8
                         bit  ASCII  character.  This permits 256 character
                         codes to be displayed on the screen. This is NOT a
                         VT function and  the  use of this option may cause
                         unpredictable results.


          Group 8


          CGA Underline (0)
                         0=Bold. PC-VT displays the underline  attribute as
                         bold on the Color Graphics Adapter.

                         1=Bold and Blinking. PC-VT displays  the underline
                         attribute as bold & blinking on the Color Graphics
                         Adapter.  The  monochrome  adapter  handles   this
                         attribute correctly as underline.

          Controls (0)   0=Interpret. PC-VT, when running as a VT emulator,
                         interprets and acts upon all escape sequences.

                         1=Display.   PC-VT   does   not  interpret  escape
                         sequences.  They are displayed on the screen  just
                         as  they  are received. The  escape  character  is
                         displayed as <ESC>.

          Columns (0)    0=80. PC-VT operates in normal 80 column mode.

                         1=132.  PC-VT  operates in 132  column  mode.  The
                         Everex Edge Monochrome/Color Graphics Adapter card
                         must  be  installed.  PC-VT  ignores   the  escape
                         sequence to go into  132  column  mode  unless you
                         have the card installed and you have started PC-VT
                         with the /e option on the command line.

          4014 Page Full (1)
                         0=Off

                         1=On. Causes a Page Full condition  to  occur when
                         the emulator linefeeds past the last  line  on the
                         screen. PC-VT beeps the speaker with  a  low pitch
                         tone and waits for the user to press  the  F2 key.
                         The  screen  is  cleared and displaying continues.


          Page 58






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         This must be  set  to  use  the  Autoprint feature
                         described below.


          Group 9


          4014 CR Effect (0)
                         0=CR only. PC-VT  transmits only a Carriage Return
                         code when the PC Enter key is pressed.

                         1=CR and  LF.  PC-VT  transmits  both  a  carriage
                         return and a  linefeed  code when the PC Enter key
                         is pressed.

          4014 LOY (1)   0=RUBOUT.  The RUBOUT  character  (ASCII  127)  is
                         ignored.

                         1=LOY. The RUBOUT character is  treated  as  a Low
                         Order Y coordinate address.

          4014 LF Effect (0)
                         0=LF only. PC-VT transmits  only  a  linefeed code
                         when the PC CTRL-J (linefeed) key is pressed.

                         1=LF and CR. PC-VT transmits both a linefeed and a
                         carriage  return  code  when  the  CTRL-J  key  is
                         pressed.

          4014 GIN Term. (1)
                         0=None. PC-VT only sends the  graphics coordinates
                         when GIN mode is terminated.

                         1=CR. PC-VT sends  a Carriage Return following the
                         graphics coordinates when GIN mode is terminated.


          Group 10 Shown as Group 0 on the frame.


          4014 Autoprint (0)
                         0=Off.

                         1=On. If the Page Full feature is set, a Page-Full
                         condition causes PC-VT to make a  hardcopy  of the
                         screen.  Completion of  the  hardcopy  clears  the
                         Page-Full condition and erases the screen.

          Scroll Buffer (0)
                         0=Do not attempt to allocate memory for the Scroll
                         Buffer. The Scroll Lock key  functions  as  the NO
                         SCROLL key on the VT100.  The  buffer  function is
                         disabled. Must be set to 0 for TopView if you want
                         to do windowing.


                                                                    Page 59






          SETUP Frames                                          PC-VT v10.0


                         1=Attempt  to  allocate  memory  for   the  Scroll
                         Buffer. Chapter 5  describes the operation of this
                         function.  This  feature  requires  that  the  DMA
                         feature be  selected  in  Group  7  above.  Scroll
                         Buffer directly accesses  video memory. Do not use
                         this feature if you already have a Scroll Lock key
                         handler installed.

          Screen Blanking (0)
                         0=Screen blanking is disabled.

                         1=PC-VT blanks the  VT emulator screen after three
                         minutes of inactivity. Receipt  of  data  from the
                         host or any key  press  turns  the screen back on.
                         Pressing the SHIFT key will turn  the  screen back
                         on without generating a character. This feature is
                         never active in 4014 mode. Do not use this feature
                         if  you  already have a  screen  blanking  program
                         installed.

          Reserved (X)   Reserved for PC-VT.



































          Page 60






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                      Chapter 7

                                 The PARAMS.DAT File


                  PC-VT maintains a USER MEMORY  file on disk. This file is
          used to save user selected features and tab stops.  The  file  is
          read  each  time  that  you  start  up  PC-VT  so  your  selected
          configuration is restored each time.


          7.1  Creation


                  The file is automatically created with default  values as
          defined  in  Chapter  6 if the file does not exist on the default
          drive.


          7.2  Location


                  A file  named  PARAMS.DAT  is  created  in  the directory
          pointed  to by  the 'PC-VT='string in  the  environment.  If  you
          haven't specified that string,  the  file  is  created on the DOS
          default drive. Chapter 3 on starting PC-VT describes  how  to use
          this string.


          7.3  Updating


                  The file is rewritten upon request while in  the  SETUP A
          frame by pressing "s".


          7.4  Error Messages


                  There are  several  messages  generated  by  PC-VT  while
          manipulating this file.


          "New USER MEMORY File Created":
                         PC-VT  could  not  find  PARAMS.DAT on the default
                         disk drive so  it  created a file with the default
                         feature selections and tab stops. PC-VT continues.



                                                                    Page 61






          The PARAMS.DAT File                                   PC-VT v10.0


          "Disk Directory Full":
                         PC-VT could not find space in the directory of the
                         default disk drive when  it  tried  to  create the
                         PARAMS.DAT file. PC-VT terminates.

          "Disk Full While Writing USER MEMORY File":
                         PC-VT ran out  of  space on the default disk drive
                         while   creating   the  PARAMS.DAT   file.   PC-VT
                         terminates.

          "Disk Swap Error - See User Manual":
                         PC-VT found a different  diskette  in  the default
                         drive from the time that the  directory  entry was
                         created and the file PARAMS.DAT was written. Since
                         the time between these two events  is  very small,
                         this error message  indicates a severe hardware or
                         system  failure.  PC-VT  terminates.  This   error
                         should never happen  if  PC-VT is run from a fixed
                         disk.

          "Error While Opening USER MEMORY File":
                         PC-VT  failed to successfully open the  PARAMS.DAT
                         file on the default disk. This usually  means that
                         the   disk  directory  has  been  damaged.   PC-VT
                         terminates.

          "USER MEMORY File Access Error":
                         An error  occurred  while  reading  the PARAMS.DAT
                         file from the default disk. Usually means that the
                         file  has  been  accidentally  overwritten.  PC-VT
                         terminates.

          "Can't find PARAMS.DAT.F1 to cancel,space to try again.":
                         This usually means that the default diskette drive
                         is  empty  or  the  door  is  open.   Correct  the
                         situation and hit the space key to continue. Press
                         F1 to terminate PC-VT.



















          Page 62






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                      Chapter 8

                          Transmitting and Receiving Files


                  PC-VT   has   complete   transmit  (upload)  and  receive
          (download) facilities. These facilities  are  accessed  using the
          CTRL-F4  and  CTRL-F3  keys, which are active whenever you are in
          either the VT100 or 4014  communications  frames.  PC-VT performs
          these functions on any ASCII character or binary file. The binary
          file  transfer  uses  the XMODEM protocol  and  must  be  over  a
          communications line set at 8 data bits, no parity, and 1 stop bit
          (PC-VT automatically switches the  communications  line  to 8-N-1
          before it starts an XMODEM transfer and restores  your  set value
          when  the  transfer  is complete). XMODEM can be used to transfer
          ASCII files for  greater  error  detection  capability.  Both the
          ASCII and XMODEM protocols are compatible with  computer bulletin
          board software such as RBBS or FIDO.

                  In  the descriptions which follow, the computer  referred
          to  as  the  host  is  assumed  to  be a VAX-11 running VMS.  All
          references  to an IBM PC filename include  a  drive  letter,  the
          path,  the  filename  and  the  file  extension,  for  example  -
          a:\usr\bin\file.ext. If no  drive  letter or path is given, PC-VT
          accesses  the  current  default  directory.  You  can  change the
          default drive and directory by  pressing  CTRL-F2.  See  the last
          section in this chapter for details.

                  The  file transfer mode can be set  when  you  enter  the
          filename to be transferred or it can be set in the SETUP B frame.
          In  that  frame,  press "x" until your desired mode is displayed.
          Then go  to  the  SETUP  A  frame  and  press  "s"  to  store the
          information into USER MEMORY on disk.

                  When you active any  of  the  functions described in this
          chapter from the VT emulator, PC-VT opens a window on  the screen
          in which the described interaction takes place. In  4014  mode, a
          window  is  not  opened but the interaction takes place as normal
          screen output.


          8.1  Transmitting ASCII Files (Uploading)


                  To transmit or upload an ASCII file to the host, the host
          must be  set  to  receive  the file and then PC-VT can be told to
          transmit it. The host  computer  can be told to execute a program
          which reads the terminal or more simply, you can use the VMS COPY


                                                                    Page 63






          Transmitting and Receiving Files                      PC-VT v10.0


          command.  Once  you  have started PC-VT and logged onto the host,
          you will see the "$" VMS command line  prompt.  You  use  the VMS
          COPY command as follows:

          COPY TT:  <filename>

          There must be space between the TT: and the filename.

          The  host  then  waits  for  characters to be transmitted by  the
          terminal. To request PC-VT to start uploading, press CTRL-F4. PC-
          VT prompts for the name  of  the  PC  file  to  upload.  Type the
          filename followed by "=a" and  then  press  ENTER.  Just pressing
          ENTER  cancels  the  transmit request. If PC-VT finds the file as
          specified, it transmits it to the host. If the file is not found,
          you will be prompted  again  for the filename. The "=a" option on
          the end of the filename indicates ASCII file transfer mode.

                  At  the end of the file, if you  have  selected  the  VMS
          operating system in  the  SETUP  frame,  PC-VT asks if you want a
          CTRL-Z  (ASCII  code  26) sent to the host. The CTRL-Z terminates
          the  VMS  COPY  command. An upper or lower case "y" must be typed
          followed by ENTER to send the CTRL-Z. If you  have  selected  the
          UNIX operating system and have done a CAT command, PC-VT  asks if
          you want a CTRL-D sent to the host.

                  PC-VT  normally  strips  all  Line Feed characters (ASCII
          code 10) before it transmits the file. All  other  characters are
          transmitted. If you have set Local Echo in the SETUP frame, PC-VT
          sends  the linefeed characters. This is the  only  case  when  it
          does. PC-VT detects  the  end  of  the  PC file by using the byte
          count in the directory entry for the file. PC-VT does not require
          that you have a CTRL-Z at the end of the PC file.

                  A very useful feature of  this routine is that it handles
          XOFF/XON characters received from the host during uploading. This
          prevents the host from losing data if it is busy. The  host sends
          an  XOFF  if  its buffer is filling.  PC-VT  automatically  stops
          transmitting until an XON  is  received  indicating that the host
          has emptied its buffer.  You  should be sure that this feature is
          enabled under your logon on the  VMS  system. To do this, use the
          VMS SET command as shown below:

          SET TERMINAL /HOSTSYNC

          This command should be put in your LOGIN.COM file unless your VMS
          system sets this feature as a default.

                  If  you  wish  to cancel the transmission  before  it  is
          complete, simply press CTRL-F4  at  any  time. PC-VT prompts with
          the CTRL-Z/CTRL-D message and then  terminate  the  upload. PC-VT
          ignores all other keys pressed during an upload.

                  If you don't request the transmission of a CTRL-Z/CTRL-D,
          you can press CTRL-F4  again  and send another file. The new file


          Page 64






          PC-VT v10.0                                 VT100 & 4014 Emulator


          transmitted  will  be  read  by  the  same  COPY command  entered
          earlier. You can use this function to append many  files  to  one
          another as you transmit them.

                  In addition, in VMS mode,  the host can cancel the upload
          if it needs to. If the host sends a CTRL-Z (ASCII 26) while PC-VT
          is  doing an ASCII file upload,  PC-VT  immediately  cancels  the
          upload. In UNIX mode, the host  can  also cancel the upload if it
          needs to. If  the  host  sends  a  CTRL-D while PC-VT is doing an
          ASCII file upload, PC-VT immediately cancels the upload.

                  There are  several  messages  generated  by  PC-VT  while
          transmitting a file:

          "Current default directory is ":
                         The current default directory is displayed.

          "Drive d: xxxxxx  bytes free":
                         The number of  free  bytes on the default drive is
                         displayed.

          "Default File Transfer Mode is ASCII
          Enter Name of the PC File to Transmit
          [d:][path][filename[.ext]][={a,z,x,c,k,t,v}]
          (Press ENTER to cancel upload and return to emulator):":


                         PC-VT is asking for  the  name  of  the PC file to
                         transmit.  Type the filename in  the  standard DOS
                         format  and  press  ENTER.  Pressing   just  ENTER
                         cancels the transmitting routine.  If  you  do not
                         specify a  drive  or  path,    PC-VT  accesses the
                         default  directory.  The default directory can  be
                         changed with the CTRL-F2 command.    See  the last
                         section in this chapter for details.

                         The "=a" and  "=z"  options  start  up  ASCII file
                         transfer. The "=a" option uses the byte count from
                         the  disk  directory  to  set  the  length  of the
                         transferred  file. The  "=z"  option  ignores  the
                         length  and  stops  transmitting  when a CTRL-Z is
                         encountered in the file.

                         The "=x" and  "=c"  options  start  up  the XMODEM
                         protocol. The "=t"  option starts up file transfer
                         with handshaking. These are both explained below.

                         The "=k" option starts up the KERMIT file transfer
                         program.

                         The "=v" option lets  you  look  at  a file on the
                         screen. See a later  section  in  this  chapter to
                         view a file.



                                                                    Page 65






          Transmitting and Receiving Files                      PC-VT v10.0


                         PC-VT DEFAULTS to XMODEM protocol  if  you  do not
                         enter an  option  and  have  not  selected  a file
                         transfer mode in the SETUP  B  frame.  The current
                         default is displayed as a reminder.

          "Transmitting xxx bytes (yyy blocks)":
                         PC-VT calculates the size of the file and displays
                         the   number   of  bytes  (and   blocks)   to   be
                         transmitted. There are 128 bytes in a  block which
                         corresponds to the XMODEM block size.

          "Should a CTRL-Z be transmitted? (y or n) :":
                         If you have selected the VMS  operating  system in
                         the SETUP frame and PC-VT detects the end of file,
                         it does not  transmit  a CTRL-Z to the host unless
                         you  respond  positively to this  query.  Type  an
                         upper or  lower case "y" followed by ENTER and PC-
                         VT   transmits a CTRL-Z. If  you  type  any  other
                         character   or   just   ENTER,   CTRL-Z   is   not
                         transmitted. With  this  feature,  CTRL-F4  can be
                         activated  again  and  several  PC  files  can  be
                         concatenated into one host file.

          "Should a CTRL-D be transmitted? (y or n) :":
                         If you have selected the UNIX operating  system in
                         the SETUP frame and PC-VT detects the end of file,
                         it does not  transmit  a CTRL-D to the host unless
                         you  respond  positively to this  query.  Type  an
                         upper or  lower case "y" followed by ENTER and PC-
                         VT transmits  a  CTRL-D.  If  you  type  any other
                         character   or   just   ENTER,   CTRL-D   is   not
                         transmitted. With  this  feature,  CTRL-F4  can be
                         activated  again  and  several  PC  files  can  be
                         concatenated into one host file.

          "Transmission Complete":
                         File uploading is complete.

          "Transmission Canceled":
                         CTRL-F4  was  pressed  during a file transmission.
                         The uploading is immediately canceled.

          "Filename is not in correct format":
                         The  filename entered in response to the  filename
                         inquiry is not  a  valid DOS filename. You may re-
                         enter the filename.

          "File not found as specified":
                         PC-VT could not find  the  file  on  the specified
                         disk.  Usually  caused  by  either the wrong drive
                         letter, directory or  a mistyped filename. You may
                         re-enter the filename.




          Page 66






          PC-VT v10.0                                 VT100 & 4014 Emulator



          8.1.1  Uploading with Handshake

                  If you append an "=t" on the end of the filename when you
          type itin, PC-VT uploads the ASCII file as described above except
          that the program waits for a turnaround character before it sends
          the next line. The  turnaround  character  is  set in the SETUP-A
          frame. This feature is useful if the host is not  buffered. PC-VT
          won't send any characters until the host has  processed  the last
          line transmitted and prompts for  another  line.  This turnaround
          character is sometimes  called  a bypass character. For a typical
          VAX system you may want to set this to a linefeed (ASCII 10) or a
          dollar sign (ASCII 36)  which  is the default value for PC-VT. In
          addition,  a  CTRL-Z/CTRL-D  is not transmitted at the end of the
          file.  This upload as well as the regular  ASCII  upload  can  be
          canceled by pressing CTRL-F4.

                  Pressing  the  space  bar  overrides  the  wait  for  the
          turnaround character. If the turnaround  character  is  missed or
          lost,  PC-VT  waits  forever. By pressing the space bar, you tell
          PC-VT to send the next line of the  file.  PC-VT  sends  the next
          line and waits again. Other keys are ignored while the  upload is
          in progress. (This lets you  set the turnaround character to some
          totally unused code and use the space bar to transmit one line at
          a time to the host.)

                  Operation is as follows: initiate the upload  by pressing
          CTRL-F4. Give PC-VT the  filename  with  the "=t" appended. PC-VT
          sends the first line of the  file  up to a carriage return (ASCII
          13).  PC-VT  then  waits  until  the  host  sends the  turnaround
          character. PC-VT then sends the next line of  the  file  up  to a
          carriage return and so  on.  Following the last line of the file,
          the keyboard is enabled again for you to type to the host.

                  Three dynamic features make this easier to use:

                The turnaround character can be changed in the middle of an
                uploaded file. To do  this,  as  you  are creating the file
                enter  an  ASCII  1  into  the  file  followed by  the  new
                turnaround character. The ASCII 1 (a CTRL-A)  signals PC-VT
                that the next character read from the file is be to  set as
                the new turnaround  character.  Neither the ASCII 1 nor the
                new  turnaround character is sent to  the  host.  This  new
                turnaround character  is visible in the SETUP A frame. This
                does mean that you  cannot  have an ASCII 1 in any uploaded
                text handshake file, but that should not be a problem since
                ASCII 1 is rarely used in a text file.

                An ASCII 2 (a CTRL-B) in the file signals PC-VT to wait for
                1 second before proceeding to the next character. This is a
                "pause" feature. You  can  have as many of these characters
                in  a row as you like to make up longer pauses. The ASCII 2
                is not sent to the host. This also means  that  you  cannot
                have an ASCII 2 in any upload text handshake file, but that


                                                                    Page 67






          Transmitting and Receiving Files                      PC-VT v10.0


                should not be a problem since  ASCII  2 is rarely used in a
                text file.

                An ASCII 20 (a  CTRL-T)  in the file signals PC-VT that the
                next character in the file is a binary value specifying the
                number  of  seconds  to  wait  after  the  receipt  of  the
                turnaround character before PC-VT sends the next  line. For
                example, to have PC-VT wait for 5 seconds before responding
                to each  turnaround character, enter a CTRL-T followed by a
                CTRL-E (ASCII 5) into the file. Once this value is  set, it
                remains set until you terminate PC-VT or you set it to some
                other value. Remember,  it  waits after the receipt of each
                turnaround character. Default value is zero seconds.

                  Scanning for these  three special control characters only
          takes place if you started the upload with the  "=t"  option.  If
          you started a  regular  upload (the "=a" option) these characters
          are uploaded just like all  others and the handshake is disabled.
          If, while you are setting up  your  files, you make a mistake and
          PC-VT is waiting  for  a turnaround character which never occurs,
          just press CTRL-F4 and PC-VT  returns  to  normal  keyboard input
          mode.


          8.1.2  Example of a Transmission Session


                  This  is  typical  of what you  would  see  and  type  to
          transmit a file to the host.

          $ copy tt: up.fil
          Press the CTRL-F4 key
          Current default directory is
          a:\usr\me\pcvt
          Drive a: 3435423 bytes free
          Default File Transfer Mode is ASCII
          Enter Name of the PC File to Transmit
          [d:][path][filename[.ext]][={a,z,x,c,k,t,v}]
          (Press ENTER to cancel upload and return to emulator)
          b:\mydire\pc.asc=a
          Transmitting 3543 bytes (28 blocks)
          Now the PC file named b:\mydire\pc.asc is transmitted,
          the file is displayed on the screen as it is
          echoed back from the host.
          Should a CTRL-Z be transmitted? (y or n) : y
          A CTRL-Z is sent to the host.
          Transmission complete
          ^Z
          The host file named up.fil is closed. The host COPY
          command is terminated.
          $





          Page 68






          PC-VT v10.0                                 VT100 & 4014 Emulator



          8.1.3  A Useful VAX .COM Upload File


                  This simplified  upload facility uploads a file from a PC
          disk file to a VAX system running VMS.

                  Create  a  file  on  the  VAX  system   named  "pcup.com"
          consisting of the following commands:

          $ on error then goto err1
          $ on control_y then goto ctrl
          $ if p1.eqs."" then inquire p1 "Enter Name of VAX File to " -
          $       "Contain Uploaded Data"
          $ if p1 .eqs. "" then goto ctrl
          $ set term/nobroad
          $ write sys$output "<ESC>[?22h"
          $ copy tt:  'p1'
          $ exit:
          $ set term/broad
          $ exit
          $ err1:
          $ write sys$output "A VAX error has occurred. Please try again."
          $ ctrl:
          $ write sys$output "Upload Canceled."
          $ goto exit

                  The symbol <ESC> is the  ESCAPE character 27. You have to
          use your host's text editor to replace the <ESC>  with  the  real
          ESCAPE character.

                  Once you have started PC-VT on the PC and you have logged
          onto a VAX, upload files from the PC to the VAX by:

            1.  Type this in response to the "$" VMS prompt:

                @pcup <filename>

            2.  If you did not enter the filename on the command  line, the
                facility asks you for the name of the VAX  file  which  you
                wish to create with the  uploaded  data  (include directory
                information if needed)

                dra1:[user1.dire.lev2]z.com

            3.  If you just press ENTER, the upload is canceled.

            4.  The facility asks you for the name of the PC file which you
                wish to upload (include disk drive letter if needed)

                zzzzz.com=a

            5.  If you just press ENTER, the upload is canceled.



                                                                    Page 69






          Transmitting and Receiving Files                      PC-VT v10.0


            6.  The rest is automatic. The data displays on the PC's screen
                as it is echoed. The upload is complete when  the  "$"  VMS
                prompt appears.

            7.  To abort the upload before it is complete, press:

                CTRL-F4

            8.  The VAX file contains whatever  data  was  uploaded  to the
                point where you aborted the  upload. You may see some extra
                characters  displayed  on  the  screen,  this  is  just the
                communications buffer emptying.

                  The  ESC [ ? 22 h sequence is  a  special  PC-VT  private
          sequence described in Appendix J.


          8.2  Transmitting Binary Files (Uploading)


                  PC-VT supports the XMODEM protocol  for  binary  or ASCII
          file  transfer.  Support  is  included  for  both  checksum error
          checking compatible with  RBBS  and  for  Cyclic  Redundancy Code
          (CRC) error checking.  This  transfer mode requires that the host
          computer be capable of handling this protocol.

                  To run XMODEM, start up  the host XMODEM program and then
          follow the instructions for transmitting ASCII files  but include
          "=x" after the filename("=c"  is  equivalent  for  transmit). The
          XMODEM module is automatically started and the  transfer proceeds
          without further intervention. The transfer is started in checksum
          mode; the receiver has the option of switching to CRC mode. PC-VT
          clicks the speaker with each block transmitted.

                  PC-VT automatically changes  the communications to 8 data
          bits, no parity, 1 stop bit (8-N-1) if you are not already set at
          that protocol. PC-VT then restores the protocol to your set value
          when the XMODEM transfer is complete.

                  To cancel  the transfer while it is progress, press CTRL-
          X. This may require a few seconds to take  effect  because  PC-VT
          must gracefully terminate the protocol.

                  Refer to  already  published  texts  for  details  on the
          XMODEM protocol.


          8.3  Receiving ASCII Files (Downloading)


                  To receive an ASCII  file,  PC-VT  must  be told to start
          receiving and then the host must be told to transmit. To activate
          Receive File, press CTRL-F3. This can be done at any time  in the
          communications frame. PC-VT asks for  the  filename  on  which to


          Page 70






          PC-VT v10.0                                 VT100 & 4014 Emulator


          write the received  characters.  Type in the filename followed by
          either  "=a"  or  "=A"  followed  by ENTER. Just  pressing  ENTER
          terminates the receive request. If the file already exists, PC-VT
          asks if you wish to overwrite it. If  you  type  "y"  followed by
          ENTER, PC-VT deletes the old file and starts to create another.

                  You  can  now  tell the host to type out a file and PC-VT
          writes  it  onto  the IBM PC disk. At the VMS dollar sign prompt,
          enter this command:

          TYPE <filename>

                  The option following the filename  tells  PC-VT  that you
          want to do an ASCII download. If you  use  the  "=A"  option, ALL
          further characters received from the  host except 00H and 7FH are
          written onto the disk file.

                  If You use the "=a" option, PC-VT waits until it receives
          a Line  Feed character, then ALL further characters received from
          the host except 00H and 7FH are written onto the disk file. PC-VT
          doesn't write out data to disk until a linefeed  is  received  in
          order  to  let  you to enter the VMS TYPE command.  This prevents
          the TYPE command from being written to the file.

                  To  terminate  Receive  File,  press CTRL-F3 again. PC-VT
          closes the disk file and resumes normal operation.

                  This mode is  also  called File Capture Mode. Since PC-VT
          cannot  tell   the  difference  between  a  file  and  any  other
          characters sent by the  host,  all  characters  (except - 00H and
          7FH)  received  go  onto  the  disk  file.  This includes  ESCAPE
          sequences and all VMS command language interaction. This can be a
          useful  feature  if  you  are  programming  with  some  of  these
          sequences  and  your  program  is  not  working  correctly. PC-VT
          preserves these  characters on disk for your inspection. Once the
          file  is  closed,  you must exit PC-VT and enter a text editor to
          strip off any unwanted characters from the file.

                  PC-VT puts an  End  of  File  indicator at the end of the
          disk file  before  it  closes  the file. For the IBM PC this is a
          CTRL-Z  character  (ASCII  code  26).  As  a  reminder, "RCV"  is
          displayed  on  the  Status Line while Receive File is active. The
          receipt  of  a  CTRL-Z in VMS mode  or  a  CTRL-D  in  UNIX  mode
          terminates  Receive File and closes the  received  file.  If  you
          terminate  PC-VT,  the  received  file  is closed as if a  CTRL-Z
          character was received.

                  Receive File terminates if it  runs out of disk space for
          the  downloaded  file.  The  last  block (up to  512  characters)
          received  is  lost  and no CTRL-Z  (End  of  File)  indicator  is
          written. The file, however, is closed.

                  There are  several  messages  generated  by  PC-VT  while
          receiving a file:


                                                                    Page 71






          Transmitting and Receiving Files                      PC-VT v10.0


          "Current default directory is ":
                         The current default directory is displayed.

          "Drive d: xxxxxx  bytes free":
                         The number of  free  bytes on the default drive is
                         displayed.

          "Default File Transfer Mode is ASCII
          Enter Name of the PC File to Receive
          [d:][path][filename[.ext]][={a,A,x,c,k}]
          (Press ENTER to cancel download and return to emulator):":

                         PC-VT is asking for  the  name  of  the PC file to
                         receive.  Type  the  filename  in the standard DOS
                         format  and  press  ENTER.  Pressing   just  ENTER
                         cancels the  receiving  routine.  If  you  do  not
                         specify  a  drive  or  path,  PC-VT  accesses  the
                         default  directory.  The  default directory can be
                         changed  with  the  CTRL-F2  command. See the last
                         section in this chapter for details.

                         The "=a" and  "=A"  options  start  up  ASCII file
                         transfer. The "=a" option waits  for  a  line feed
                         character, the other option does not.

                         The "=x" and  "=c"  options  start  up  the XMODEM
                         protocol.

                         The "=k" option starts up the KERMIT file transfer
                         program.

                         If you do  not  specify  a  option,  PC-VT assumes
                         XMODEM  protocol. The  currently  set  default  is
                         displayed as  a reminder. It can be changed in the
                         SETUP B frame.

          "Filename is not in correct format":
                         The  filename entered in response to the  filename
                         inquiry is not in the standard DOS format. You may
                         re-enter the filename.

          "Insert   diskette   with   received   file.   Press   ENTER   to
          continue....":
                         PC-VT found a different diskette in the disk drive
                         than  the one it  opened  the  download  file  on.
                         Replace  the  original  diskette  in the drive and
                         press the ENTER key. Pressing  any  other  key and
                         then pressing ENTER terminates the  file transfer.
                         The data on the diskette  may  not  be  correct or
                         complete.

          "File already exists. Do you want to overwrite it? (y or n)":
                         The filename which  you entered already exists. If
                         you  respond  with  a  lower  or  upper  case  "Y"


          Page 72






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         followed by the ENTER key, PC-VT deletes  the file
                         and  creates a new one with  the  same  name.  Any
                         other response preserves the file and receive file
                         is canceled.

          "File is being overwritten":
                         PC-VT confirms that the old file has  been deleted
                         and a new file is being created.

          "Invalid path/filename or directory full. Receive terminated":
                         PC-VT  could  not  create  the  file  because  the
                         directory on the  specified diskette was full, the
                         file  was  marked  read-only, or the path/filename
                         specified is invalid.

          "Disk full. Receive terminated":
                         PC-VT  ran  out  of space on the  disk.  The  file
                         already written is closed. A CTRL-Z is  not placed
                         at the end of the file. The last block (up  to 512
                         characters) received is lost.


          8.3.1  Example of a Receive Session


                  This is typical of what you would see and type to receive
          a file from the host. Comments are underlined.

          $
          Press the CTRL-F3 key
          Current default directory is
          a:
          Drive a: 32234  bytes free
          Default File Transfer Mode is ASCII
          Enter Name of the PC File to Receive
          [d:][path][filename[.ext]][={a,A,x,c,k}]
          (Press ENTER to cancel download and return to emulator)
          b:receive.txt=a
          RCV is displayed on the Status Line and any characters
          sent by the host are copied to the PC disk file.
          type host.dat
          The host file named host.dat is received by PC-VT
          and placed on the PC disk file named b:receive.txt.
          $
          Press the CTRL-F3 key
          The file is closed and RCV is cleared from the Status
          Line.


          8.3.2  A Useful VAX .COM Download File


                  This simplified Download facility downloads a file from a
          VAX system running VMS to a  PC  disk  file. Create a file on the


                                                                    Page 73






          Transmitting and Receiving Files                      PC-VT v10.0


          VAX  system  named   "pcdown.com"  consisting  of  the  following
          commands:

          $ on error then goto err2
          $ on control_y then goto ctrl
          $ if p1.eqs."" then inquire p1 "Enter Name of VAX File to
          Download"
          $ if p1 .eqs. "" then goto ctrl
          $ open for008 'p1'/error=err1
          $ close for008
          $ set term/nobroad
          $ write sys$output "<ESC>[?21h"
          $ copy 'p1' tt:
          $ write sys$output "^Z"
          $ exit:
          $ set term/broad
          $ exit
          $ err1:
          $ write sys$output "VAX File Not Found."
          $ ctrl:
          $ write sys$output "Download Canceled."
          $ goto exit
          $ err2:
          $ write sys$output "A VAX error has occurred, Please try again."
          $ goto ctrl

                  The symbol <ESC>  is  the ESCAPE character 27. The symbol
          ^Z is the CTRL-Z character 26.  You  have to use your host's text
          editor  to  replace  the <ESC> with the real ESCAPE character and
          the ^Z with a real CTRL-Z character.

                  Once you have started PC-VT on the PC and you have logged
          onto a VAX, download files from the VAX to the PC by:

            1.  Type this in response to the "$" VMS prompt:

                @pcdown <filename>

            2.  If you did not enter the filename on the command  line, the
                facility asks you for the name of the VAX  file  which  you
                wish to download (include directory information if needed)

                [upload]xmit.com

            3.  If you just press ENTER, the download is canceled.

            4.  The facility asks you for the name of the PC file which you
                wish to create with the downloaded data (include disk drive
                letter if needed)

                a:pcfile.dat=a

            5.  If you just press ENTER, the download is  canceled.  If the
                name you give for the PC file already exists, PC-VT asks if


          Page 74






          PC-VT v10.0                                 VT100 & 4014 Emulator


                you want to overwrite the file. If you answer "y",  all the
                new data  replaces  the  old  data  on  the PC file. If you
                answer "n" or just press ENTER, the download is canceled.

            6.  The rest is automatic. The data displays on the PC's screen
                while it is being downloaded. The download is complete when
                the "$" VMS prompt appears.

            7.  To abort the download before it is complete, press:

                CTRL-F3

            8.  The PC file contains  whatever  data  was downloaded to the
                point  where you aborted the download.  You  may  see  some
                extra output on the screen; this is just the communications
                buffer emptying.

                  The  ESC [ ? 21 h sequence is  a  special  PC-VT  private
          sequence described in Appendix J.


          8.4  Receiving Binary Files (Downloading)


                  PC-VT supports the XMODEM protocol  for  binary  or ASCII
          file  transfer.  Support  is  included  for  both  checksum error
          checking compatible with bulletin  boards  such  as RBBS and FIDO
          and for Cyclic Redundancy Code(CRC) error checking. This transfer
          mode requires that the host  computer be capable of handling this
          protocol.

                  To run XMODEM, start up  the host XMODEM program and then
          follow the instructions for  receiving  ASCII  files  but include
          "=x" after the filename  for  checksum mode or "=c" for CRC mode.
          The XMODEM  module  is  automatically  started  and  the transfer
          proceeds  without  further   intervention.  Since  PC-VT  is  the
          receiver, you have the option  of  selecting  the  error checking
          mode. Checksum mode detects all burst errors of less than  8 bits
          in length and 99.6% of all  burst  errors longer than 8 bits. CRC
          mode detects all single and double bit errors, all errors with an
          odd number of bits, all burst errors of  length  16  or  less and
          99.997% of all 17 bit and longer bursts. The CRC supported is the
          CCITT recommended x^16 + x^12 + x^5 + 1.

                  PC-VT automatically changes  the communications to 8 data
          bits, no parity, 1 stop bit (8-N-1) if you are not already set at
          that protocol. PC-VT restores the protocol to your set value when
          the XMODEM transfer is  complete.  PC-VT  clicks the speaker with
          each block received.

                  To cancel  the transfer while it is progress, press CTRL-
          X. This may require a few seconds to take  effect  because  PC-VT
          must gracefully terminate the protocol. PC-VT does not delete the



                                                                    Page 75






          Transmitting and Receiving Files                      PC-VT v10.0


          partial file already created on disk but closes it and  leaves it
          for you to examine and delete.

                  Refer to  already  published  texts  for  details  on the
          XMODEM protocol.


          8.5  Viewing Files


                  PC-VT lets you view files on the display  when  you press
          the CTRL-F4 (Transmit a file) key. Use the option "=v" at the end
          of the filename. PC-VT displays the file on the screen.

                  The  viewing  is  in the context of the emulator which is
          running. That is, if  the  VT100  emulator  is active, any Escape
          sequences read from the file are acted upon. The same is  true if
          the VT52 or 4014 emulator is running.

                  For example, you can use Receive file with "=A" option to
          capture a session with your  host computer. The Receive file with
          "=A" option  saves all received characters in the disk, including
          all  escape  sequences.  With the "=v" option, you can review the
          session  later  and  see the same cursor movement and full screen
          editing features as when you were on line to the host computer.

                  As  described  in  Chapter 5, you can use this feature to
          redefine any of PC-VT's extended function and editing keys.

                  An even more useful feature is to use the "=A"  option on
          Receive file to capture a 4014 plot for later playback.  Just use
          Transmit file with the "=v" option while in the 4014 emulator and
          you will see the plot again.


          8.6  KERMIT File Transfer


                  PC-VT supports the official release of KERMIT.  To access
          this  feature  press  ALT-K  from  the  communications  frame.  A
          supplement to this document is a reprint of a KERMIT  manual from
          Columbia University. That manual is a complete description of how
          to use KERMIT and is supplied at no charge. Of course,  your host
          computer must have its version of KERMIT running.

                  CTRL-F3 and CTRL-F4 let you  go  directly  to  KERMIT for
          receiving or transmitting one file at a time. When you  enter the
          filename  prompted for, put an "=k"  after  the  filename.  PC-VT
          constructs the necessary  commands  for KERMIT and then starts up
          the program. When  KERMIT  is finished transferring the file, the
          PC-VT communications frame is automatically restarted.





          Page 76






          PC-VT v10.0                                 VT100 & 4014 Emulator


          8.7  Changing the Default Directory


                  PC-VT supports  path  names  for  ASCII  and  XMODEM file
          transfers. PC-VT accesses  the  default drive and path unless you
          explicitly  enter  them.  You can change the  default  values  by
          pressing CTRL-F2 from the  communications  frame.  PC-VT displays
          the  current  default,  ask for the new default, and then display
          the complete new default path.  The input to this command follows
          the syntax for the CHDIR command to DOS. The amount of free space
          on the default drive is also displayed.

                  Here is what you would see and type:

          Current default directory is
          c:\level1
          Drive c: 34543  bytes free
          Enter new default directory
          [[d:][\][dirname][\dirname[...]]]
          level2
          Default directory is now
          c:\level1\level2
          Drive c: 34543  bytes free

                  When you type in  the  new  directory,  you can enter the
          change just as you would enter a change to the CHDIR command:

             -   a drive letter followed by a ":" changes  the  drive  only
                (since DOS remembers the  path  associated  with  each disk
                drive, the default directory  is  set  to whatever path had
                been active on the specified drive), e.g. c:

             -  a path name starting at the root, e.g. c:\mydir\nextdir

             -  the root, e.g. f:\

             -  a directory name starting at  the  current  directory, e.g.
                nextdir


          Error Message


          "Invalid directory entered - not changed":
                         You entered an invalid  disk  or  directory. PC-VT
                         did not change the default setting.










                                                                    Page 77






          Transmitting and Receiving Files                      PC-VT v10.0


























































          Page 78






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                      Chapter 9

                                    DIALING Frame


                  The DIALING frame is accessed  by  pressing  CTRL-F9 from
          the VT100 communications frame. The content of the communications
          frame is preserved and restored when you exit the DIALING frame.


          9.1  Dialing Instructions




                  The DIALING  frame  handles  Hayes  or  Hayes  compatible
          modems. The frame can hold 10 host names and phone  numbers. Each
          entry is broken into two fields. A name can be typed in columns 1
          to 20. This is for your information only. PC-VT does not use this
          information but it  is  stored  on  the  disk  file.  The dialing
          commands and phone number can be stored in columns 21 to  70. The
          "!" above column 21 is to remind you that,  when  dialing,  PC-VT
          sends  the data in columns 21 thru 70 to the modem as the dialing
          command.

                  Each  time  that  you save the DIALING frame using the F4
          key (see below),  PC-VT  saves the complete SETUP information for
          the host pointed to by the cursor. Then when you later  dial that
          host using the F1 key, PC-VT restores the SETUP information. This
          permits you to save  unique  SETUP information for each of the 10
          hosts. Be certain though, that when you press F4, that the cursor
          is on the line of the host in which you are interested.

                  When PC-VT starts up, it looks for a dialing directory on
          the default drive or the drive and directory pointed  to  by  the
          environment  string  'PC-VT='.  If it does not  find  one,  PC-VT
          creates a blank directory. The  name field is filled with dashes.
          The command field contains "ATDT" in the first  four  columns and
          is then filled with spaces. The SETUP information associated with
          each host is set to the default values.

                  The first thing that you need to do is enter the  name of
          the number's owner. You  can  use the cursor keys, the Enter key,
          the  Tab key, the Home key and the End key to position the cursor
          to any line. The "Ins" key inserts a space at the cursor position
          and the "Del" key  deletes  a  character  at the cursor position.
          Move the cursor to column 1 and type in the  name.  It should not
          go past column  20.    Then  to  enter the phone number, move the


                                                                    Page 79






          DIALING Frame                                         PC-VT v10.0


          cursor to column 24 using the TAB key and type in the number. The
          new directory can be saved by pressing the F4 key. The number can
          be dialed by pressing the F1 key.

                  Pressing any key while the dialer is running causes PC-VT
          to stop dialing and return to the communications frame.

                  Here is how each cursor  control  key  functions  in this
          frame:

          Left arrow :   moves the cursor one  column  to  the left. If the
                         cursor is  already in column 1, PC-VT beeps and no
                         action is taken. Use this key for a backspace then
                         enter a space to clear any character that may have
                         been mistyped.

          Right arrow :  moves the cursor  one  column to the right. If the
                         cursor is already in column 70, PC-VT beeps and no
                         action is taken.

          Up arrow :     moves  the cursor up one row.  If  the  cursor  is
                         already in the top  row  of  the  directory, PC-VT
                         beeps and no action is taken.

          Down arrow :   moves the cursor down  one  row.  If the cursor is
                         already in the bottom row of the  directory, PC-VT
                         beeps and no action is taken.

          Home :         moves the cursor to column 1 of the top row of the
                         directory.

          End :          moves the cursor to column  1 of the bottom row of
                         the directory.

          Enter :        moves  the  cursor  to column 1 of the next row of
                         the directory. If the  cursor  is  already  in the
                         bottom row of the directory, the  cursor  is moved
                         to column 1 of that row and PC-VT beeps.

          Tab :          moves the cursor to column 24 of the current row.

          Ins :          inserts a space at the cursor  position.  This key
                         operates  within either the name field (columns  1
                         thru 20) or the number field (columns 21 thru 70).
                         All characters from the  cursor  to  right  of the
                         field are moved one column to the  right. Anything
                         in the rightmost  column  of the field is lost. If
                         you press Ins within the  name  field,  the number
                         field is not affected.

          Del :          deletes  a character at the cursor position.  This
                         key operates within either the name field (columns
                         1 thru 20) or  the  number  field (columns 21 thru
                         70). All characters from the right  of  the cursor


          Page 80






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         to the rightmost column of the field are moved one
                         column to the  left.  A space is inserted into the
                         rightmost column of the field.  If  you  press Del
                         within the name field,  the  number  field  is not
                         affected.

                  In addition,  as a simple macro style logon facility, PC-
          VT does a little more work. If you enter the  tilde  key (the ~),
          PC-VT translates that into a carriage return (ASCII 13) when sent
          to  the modem. This permits you to send  multiple  lines  to  the
          modem. PC-VT translates  the  underscore,  '_',  into  the Escape
          character (ASCII 27).

                  PC-VT interprets several control characters in the dialer
          command line as special commands:


          CTRL-W :       causes  the  dialer   to  wait  5  seconds  before
                         continuing with the command. CTRL-W appears in the
                         directory as an underlined up-down arrow.

          CTRL-B :       causes   the  dialer  to  wait  1  second   before
                         continuing with the command. CTRL-B appears in the
                         directory as a Happy Face.

          CTRL-X :       stops the dialing at that  point  in  the command.
                         PC-VT  then,  as  usual,  sends its final carriage
                         return  to  the   modem.  CTRL-X  appears  in  the
                         directory as an up-arrow.

          CTRL-D :       causes the dialer to wait for  the  Carrier Detect
                         signal from the modem  before  continuing  to send
                         the dialer command. While  PC-VT  is  waiting, you
                         can  press  any  key and PC-VT goes on to the next
                         character in the command.  CTRL-D  appears  in the
                         directory as a diamond. Some modems require you to
                         set a  special  switch  in  the  modem  itself for
                         Carrier  Detect  to  operate correctly. Check your
                         modem manual.

          CTRL-F :       causes the dialer  to  wait for the Data Set Ready
                         signal from the modem  before  continuing  to send
                         the dialer command. While  PC-VT  is  waiting, you
                         can  press  any  key and PC-VT goes on to the next
                         character in the command.  CTRL-F  appears  in the
                         directory as a spade.

          CTRL-Q :       quotes the  next  character.  That  is,  the  next
                         character in the command  is  sent  to the host no
                         matter what it is.  This  is  used  if you need to
                         send one of the  control  characters  described in
                         this  section  which  PC-VT  normally  uses  as  a
                         special command.



                                                                    Page 81






          DIALING Frame                                         PC-VT v10.0


          CTRL-V :       causes the  dialer to send a BREAK signal. A BREAK
                         is a mark condition on the communications line for
                         approximately 300 milliseconds. CTRL-V appears  in
                         the directory as a small square block.

          CTRL-T :       causes the dialer to wait for the  character after
                         the CTRL-T in the command before it continues with
                         the command. Neither the CTRL-T nor the turnaround
                         character following is sent  to  the  modem. While
                         PC-VT is  waiting, you can press any key and PC-VT
                         goes on to  the  next  character  in  the command.
                         CTRL-T appears in the directory as a PI symbol.

          Only  your imagination limits you as to how  you  can  use  these
          dialer  commands.  You  can  have  PC-VT dial your host, wait  10
          seconds, enter your userid, wait  10 seconds, and then enter your
          password.

                  Special notes on the directory: You have complete control
          over the entire directory from columns 1 to 70. You can type over
          the  "ATDT"  command  and you can type any special modem commands
          like "," or ";".  You  can enter any key (including the Backspace
          key) except the control keys listed above into  the  command. You
          can  change  the  "ATDT" to any other modem command. For example,
          you can change the last line to "ATM2;"  and  when  you  move the
          cursor to that line and press F1, the modem is commanded  to turn
          on the speaker at  all  times. Just remember that PC-VT sends any
          character  in columns 21 to 70 to the modem when you press the F1
          key.  PC-VT  always  sends a carriage return right after it sends
          the last character in the number field. For users  of  the  PCjr,
          you can enter the CTRL-N command required by its internal modem.

                  In the examples below, the CTRL-F is shown as a ? and the
          CTRL-X is shown as a ^.

                  Here are some possible entries:


                              !
          Mark C DiVecchio    ATDT,,555-1212
          The computer        ATDT 1 - 506 - 555 - 1234,,,,,222* 432#
          Speaker on          ATM2;
          Full Logon          ATDT,555-1212~?~userid~password~^

                  In that last example,  the  modem  is  summoned, it is to
          wait  2 seconds for the dial tone (a  Hayes  modem  command),  it
          dials the number,  waits  for  Data  Set  Ready  to  indicate the
          connection is made, sends a single carriage return which wakes up
          the  host,  enters  the userid and then enters the password. Note
          the  final  CTRL-X.  This is needed to tell PC-VT not to send the
          spaces between the password and column 70 to the host  since they
          may be seen as part of the password.




          Page 82






          PC-VT v10.0                                 VT100 & 4014 Emulator


                  One other thing is done by this facility in order  to get
          around the buffer size within the modem. Spaces and dashes in the
          phone number are not sent to the modem. With several  modems, the
          buffers could overflow if all 50 characters in  the  phone number
          field were sent. PC-VT resumes sending spaces after it encounters
          the first tilde. This  means  that spaces can be included as part
          of the logon sequence.

          Here are the functions available in the DIALING frame:


          Exit DIALING :
                         The Esc key returns  PC-VT  to  the communications
                         frame.

          Dial :         The "F1"  key dials the number in the line pointed
                         to by the cursor. Before the dialing  takes place,
                         PC-VT restores the  SETUP information to the state
                         it was when you initially  saved  this  host phone
                         number. This permits you to save a specific set of
                         SETUP features with  each host phone number. PC-VT
                         then returns to the communications frame.

          Toggle DTR :   The "F2" key toggles the  DTR  signal  out  of the
                         serial port  to  the  opposite  state.  A  message
                         appears at the bottom of the screen indicating the
                         new state.

          Read Directory:
                         The   "F3"   key   clears  the  displayed  dialing
                         directory and  reloads  it  from  the  disk  file,
                         DIALER.DAT, on the default drive. PC-VT remains in
                         the DIALING frame. The SETUP information which was
                         saved with the selected host is restored.

          Store Directory:
                         The   "F4"   key   stores  the  displayed  dialing
                         directory into a  disk  file  on  the  DOS default
                         drive or the  drive  pointed  to  by  the "PC-VT="
                         string in the environment. The name of the file is
                         DIALER.DAT.  In  addition  to the directory, PC-VT
                         saves the SETUP information for  each  entry  in a
                         special spot in  the dialing directory. This means
                         that  when  you  later  dial  this  number,  PC-VT
                         reloads all of the SETUP  options  like  baud rate
                         and feature selections associated with  this host.
                         Be certain though, that you select  the  host with
                         the cursor. This selected host is the one which is
                         associated  with the current SETUP information.  A
                         message appears at  the  bottom  of  the  frame to
                         indicate  that  the new directory  is  written  to
                         disk.




                                                                    Page 83






          DIALING Frame                                         PC-VT v10.0


          Hang up:       The "F5" key sends the  command  to  the  modem to
                         hang up the phone. This procedure takes  about 2-3
                         seconds due  to  the  modem  protocol.  A  message
                         appears at the bottom of the  display  to indicate
                         that the phone line is  hung  up.  PC-VT  uses the
                         Hayes  commands  "+++"   and  "ATH0"  to  do  this
                         function.  This function can also be performed  by
                         pressing ALT-Z in the communications frame.

                  The current host is  shown  on the SETUP B frame. This is
          to remind you when you are updating the  SETUP  information which
          host's information you are modifying.


          9.2  Saving SETUP Information


                  As mentioned above, PC-VT saves a complete picture of the
          SETUP information with  each  of  the  10  hosts  in  the dialing
          directory.

                  Each  time  that  the  F4  key is pressed in the  DIALING
          frame,  PC-VT  saves  not only the 10 entry dialing directory but
          also saves the  current  SETUP information and associates it with
          the host pointed to by the cursor.

                  To update the SETUP  information  for  a  particular host
          follow these steps:


            1.  From the communication frame  press  CTRL-F9  to  enter the
                DIALING frame.

            2.  Use  the  up  and down arrow keys to move the cursor to the
                line of the host (the cursor can be anywhere on the line).

            3.  Press  the  F3  key  which  loads  any   SETUP  information
                previously associated with that host into PC-VT.

            4.  Press the Esc key to return to the communications frame.

            5.  Press the CTRL-F1 key to enter the SETUP frame.

            6.  Proceed to modify the SETUP information  as  appropriate to
                the host.

            7.  Press the Esc key to return to the communications frame.

            8.  At this point, you may call  the  host and be sure that the
                SETUP information set is correct.

            9.  Press the CTRL-F9 key to enter the DIALING frame.




          Page 84






          PC-VT v10.0                                 VT100 & 4014 Emulator


           10.  Make sure that the cursor is pointing to the  line  of  the
                host.

           11.  Press  the  F4  key  to  save  the  SETUP  information  and
                associate it with this host.

                  Now each time that  you  dial this host using the F1 key,
          PC-VT reloads the SETUP information before it starts to dial.


          9.3  Dialing From the DOS Command Line


                  You  can tell PC-VT to dial the  number  in  the  DIALING
          frame as soon at it starts  running.  Do this from the DOS prompt
          by starting PC-VT with:

                  pc-vt/dnn

          where  n  is  a  number  from  1  to 10.  The  number  picks  the
          corresponding entry in the dialing directory and dials the number
          during  the  PC-VT  start  up  sequence. This lets you start  the
          program and immediately dial a number. The dialing entry can be a
          complete logon macro as described above.


          9.4  The DIALER.DAT File


                  PC-VT maintains a dialing directory  file  on  disk. This
          file is used to record user defined phone numbers or  other modem
          commands.

                  The  file  consists  of 10 hosts. With each host there is
          stored  the  host  name, the phone numbers,  and  complete  setup
          information.

                  The host names and phone  numbers are read each time that
          you start up PC-VT  so  your  dialing  directory is restored each
          time. The setup information is read only if you specifically dial
          the host using the F1 key from the DIALING frame.


          9.4.1  Creation


                  The file is automatically created as  an  empty directory
          if  the  file does not exist on  the  default  drive  when  PC-VT
          starts.







                                                                    Page 85






          DIALING Frame                                         PC-VT v10.0



          9.4.2  Location


                  The file name is DIALER.DAT. The file is  created  in the
          directory pointed to  by   the 'PC-VT='string in the environment.
          If there is no such string in the environment the file is created
          on the DOS default drive. Chapter 3 on  starting  PC-VT describes
          how to use this string.


          9.4.3  Updating


                  The file is rewritten by pressing F4 while in the DIALING
          frame.


          9.5  Error Messages


                  There are  several  messages  generated  by  PC-VT  while
          manipulating this file.

           "New Dialing Directory Created":
                         PC-VT  could  not  find  DIALER.DAT on the default
                         disk drive  so  it  created  a  blank  file. PC-VT
                         continues.

          "Disk Directory Full":
                         PC-VT could not find space in the directory of the
                         default disk drive when  it  tried  to  create the
                         DIALER.DAT file. PC-VT terminates.

          "Disk Full While Writing Dialing Dir":
                         PC-VT ran out  of  space on the default disk drive
                         while   creating   the  DIALER.DAT   file.   PC-VT
                         terminates.

          "Disk Swap Error - See User Manual":
                         PC-VT found a different  diskette  in  the default
                         drive from the time that the disk  directory entry
                         was  created and the file DIALER.DAT was  written.
                         Since the time between these  two  events  is very
                         small,  this  error  message  indicates  a  severe
                         hardware or system failure. PC-VT terminates. This
                         error should never  happen  if PC-VT is run from a
                         fixed disk.

          "Error While Opening Dialing Directory":
                         PC-VT  failed to successfully open the  DIALER.DAT
                         file on the default disk. This usually  means that
                         the   disk  directory  has  been  damaged.   PC-VT
                         terminates.


          Page 86






          PC-VT v10.0                                 VT100 & 4014 Emulator


          "Dialing Directory Access Error":
                         An error  occurred  while  reading  the DIALER.DAT
                         file from the default disk. Usually means that the
                         file  has  been  accidentally  overwritten.  PC-VT
                         terminates.

          "Can't find DIALER.DAT. F1 to cancel, space to try again.":
                         This usually means that the default diskette drive
                         is  empty  or  the  door  is  open.   Correct  the
                         situation and hit the space bar to continue. Press
                         F1 to terminate PC-VT.

          "DIALER.DAT could not be written":
                         This   usually  means  that  the  disk  is   write
                         protected or you specified an illegal drive letter
                         in the "PC-VT=" environment string.

          "Data Terminal Ready (DTR) now a 0/1":
                         You have pressed  F2  and  PC-VT  has  changed the
                         state of the DTR line to the modem.




































                                                                    Page 87






          DIALING Frame                                         PC-VT v10.0


























































          Page 88






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Chapter 10

                                     MACRO Frame


          The MACRO frame is  used  to  update  the currently defined macro
          keys  and  is  accessed  by  pressing  CTRL-F10  from  the  VT100
          communications frame. The contents  of  the  communications frame
          are preserved and restored when you exit MACRO. A  macro  can  be
          sent  by  pressing  ALT-F1  thru   ALT-F10   directly   from  the
          communications frame. Only these 10  keys  are  supported  by the
          macro processor.

          Here are the functions available in the MACRO frame:


          Function                Key(s)

          Exit MACRO :   "Esc" returns PC-VT to the communications frame.

          Dial :         "F1" sends the macro in the line pointed to by the
                         cursor.  PC-VT then returns to the  communications
                         frame.  To  send   the  macro  directly  from  the
                         communications frame, press ALT-Fx right  from the
                         communications frame. There is  no  need  to press
                         CTRL-F10 first.

          Read Directory:
                         "F3"  clears the  displayed  macro  directory  and
                         reloads it from the disk file,  MACRO.DAT,  on the
                         default drive. PC-VT remains in the MACRO frame.

          Store Directory:
                         "F4"  stores the displayed macro directory  into a
                         disk file on the  DOS  default  drive or the drive
                         and directory specified  in the 'PC-VT=' string in
                         the  environment.  The  name   of   the   file  is
                         MACRO.DAT. A message appears at the bottom  of the
                         frame  to  indicate  that  the  new  directory  is
                         written to disk.


          10.1  Instructions for MACRO







                                                                    Page 89






          MACRO Frame                                           PC-VT v10.0


                  The MACRO frame is used  to create, update and save macro
          key  definitions.  The  frame can hold  10  macro  keys.  The  10
          definable  keys,  ALT-F1  thru ALT-F10, are listed on the left of
          the screen. The macro commands are stored in columns  21  to  70.
          The "!" above column 21 is  to  remind you that, when expanding a
          macro, PC-VT sends the data in columns 21 thru 70 to the modem as
          the macro command.

                  When PC-VT starts up, it looks for a  Macro  Directory on
          the default drive or the drive and directory pointed  to  by  the
          environment  string  'PC-VT='.  If it does not  find  one,  PC-VT
          creates a blank directory.


          10.1.1  Defining Macro Keys


                  You use the cursor keys, the Enter key, the Home  key and
          the End key to position the  cursor  to  any line.  The "Ins" key
          inserts a space at the cursor position and the "Del"  key deletes
          a character at the cursor position.

                  Here is how each of  cursor control keys functions in the
          macro frame:

          Left arrow :   moves the cursor one  column  to  the left. If the
                         cursor is already in column 21, the  speaker beeps
                         and  no  action  is  taken.  Use  this  key  as  a
                         backspace then press the space  bar  to  clear the
                         character.

          Right arrow :  moves the cursor  one  column to the right. If the
                         cursor is already in column 70, the  speaker beeps
                         and no action is taken.

          Up arrow :     moves  the cursor up one row.  If  the  cursor  is
                         already in  the  top  row  of  the  directory, the
                         speaker beeps and no action is taken.

          Down arrow :   moves the cursor down  one  row.  If the cursor is
                         already in the bottom row  of  the  directory, the
                         speaker beeps and no action is taken.

          Home :         moves  the  cursor  to column 21 of the top row of
                         the directory.

          End :          moves the cursor to column 21 of the bottom row of
                         the directory.

          Enter :        moves the cursor to column 21 of the  next  row of
                         the directory. If the  cursor  is  already  in the
                         bottom row of the directory, the  cursor  is moved
                         to column 21 of that row and the speaker beeps. If
                         you want to use the 'Enter' as part  of  the macro


          Page 90






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         definition, use the  tilde key '~'. PC-VT replaces
                         the tilde with a carriage return when the macro is
                         expanded.

          Ins :          inserts  a  space  at  the  cursor  position.  All
                         characters from the cursor to right  of  the field
                         are moved one column to the right. Anything in the
                         rightmost column of the field is lost.

          Del :          deletes a character at  the  cursor  position. All
                         characters from the right  of  the  cursor  to the
                         rightmost column of the field are moved one column
                         to  the  left.  A  space  is  inserted   into  the
                         rightmost column of the field.

                  Move the cursor to the first column of the key  which you
          want to define. Then enter the definition. Save the new directory
          by pressing F4.


          10.1.2  Sending Macros


          The macro can be sent by pressing the F1 key.  Once  you are back
          in  the  communications  frame,  you  can send the macro just  by
          pressing  the  ALT-Fx  key.  There  is no need to press  CTRL-F10
          first.

                  Pressing any key while  the  macro  is  being transmitted
          causes  PC-VT  to  stop  the   expansion   and   return   to  the
          communications frame.


                  Special notes on the macro directory:  You  have complete
          control over the entire  directory  from  columns  21 to 70. Just
          remember that PC-VT sends any character in columns 21  to  70  to
          the  Host  when  you  invoke  the  macro.  PC-VT  does not send a
          carriage return after it sends the last character in the line. If
          you want a carriage  return,  enter  the  tilde character. If you
          don't  put  in  a tilde, PC-VT sends whatever characters you have
          defined and then just goes back into keyboard input mode. You can
          type in additional characters or manually press the enter key.

                  In addition,  PC-VT does a little more work. As mentioned
          above, if you enter the tilde key (the ~), PC-VT  translates that
          into a carriage  return  (ASCII  13)  when sent to the Host. This
          permits  you  to  send  multiple  lines.  PC-VT   translates  the
          underscore, '_', into the Escape character (ASCII 27).

                  PC-VT interprets several  control characters in the macro
          command line as special commands:





                                                                    Page 91






          MACRO Frame                                           PC-VT v10.0


          CTRL-W :       causes   the  macro  to  wait  5  seconds   before
                         continuing with the command. CTRL-W appears in the
                         directory as an underlined up-down arrow.

          CTRL-B :       causes  the  macro  to   wait   1   second  before
                         continuing with the command. CTRL-B appears in the
                         directory as a Happy Face.

          CTRL-X :       stops the macro  at  that  point  in  the command.
                         CTRL-X appears in the  directory  as  an up-arrow.
                         PC-VT returns to keyboard input mode.

          CTRL-D :       causes the macro to wait  for  the  Carrier Detect
                         signal  from the modem before continuing to  send.
                         While PC-VT  is waiting, you can press any key and
                         PC-VT goes  on to the next character in the macro.
                         CTRL-D appears in the directory as a diamond. Some
                         modems require  you to set a special switch in the
                         modem   itself  for  Carrier  Detect  to   operate
                         correctly. Check your modem manual.

          CTRL-F :       causes the macro to  wait  for  the Data Set Ready
                         signal  from the modem before continuing to  send.
                         While PC-VT  is waiting, you can press any key and
                         PC-VT goes  on to the next character in the macro.
                         CTRL-F appears in the directory as a spade.

          CTRL-Q :       quotes the  next  character.  That  is,  the  next
                         character in the macro is be sent to  the  host no
                         matter what it is.  This  is  used  if you need to
                         send one of the  control  characters  described in
                         this  section  which  PC-VT  normally  uses  as  a
                         special command.

          CTRL-T :       causes the macro to wait for  the  character after
                         the CTRL-T in the command before it continues with
                         the command. Neither the CTRL-T nor the turnaround
                         character following is sent to the host. While PC-
                         VT is waiting, you can  press  any  key  and PC-VT
                         goes on to the next character in the macro. CTRL-T
                         appears in the directory as a PI symbol.

          Only your imagination limits you as to how you can use  this. You
          can have PC-VT enter a command, wait 10 seconds, enter an option,
          wait 6  seconds,  end  a  job and log you off the host. All other
          control characters  can  be  entered  into  the  macro definition
          including  backspace  and  CTRL-C. They are sent to the host when
          the macro is expanded.

                  In the examples below, the CTRL-W is shown as a ? and the
          CTRL-X is shown as a ^.

                  Here are some possible entries:



          Page 92






          PC-VT v10.0                                 VT100 & 4014 Emulator


                              !
          ALT-F1              run myjob~^
          ALT-F2              mail~?1~???~~~~ex~^
          ALT-F3              ATDT5551212~^
          ALT-F4              _[A^

                  It is always  wise  to  put  a  CTRL-X a the end of every
          macro  so  that  PC-VT knows exactly where to stop sending. PC-VT
          sends the spaces out to column 70 if you leave off the CTRL-X. In
          most cases this probably  won't  matter  but when trailing spaces
          are significant(like in a password), you need the CTRL-X.

                  You can also use the macro key definition to dial through
          a smart modem. Simply put the dialing command in as a macro. Then
          press the appropriate ALT-Fx key from the communications frame.


          10.2  Downloading Macro Keys


                  The 10 macro keys used by PC-VT can be set from  the host
          when  the  emulator  is in VT mode. Up to 50  characters  can  be
          specified in the same format as described above. Use the  tilde ~
          character  for  the  Enter  key.  You cannot include  the  Escape
          character in the string. If you want an Escape character, use the
          underline character, '_', in the  string  which  you  send. PC-VT
          converts  the  underline  to  an  Escape  character.  You  cannot
          download any  of the special CTRL characters which are acceptable
          to the macro processor when entered from the keyboard.

                  The Escape sequence is:


          ESC [ 0 ; Pk ; "string" p
                         Sets macro  key Pk to the string given. The double
                         quotes   and   all   other  characters  shown  are
                         required. The number  Pk  must  be  sent  as ASCII
                         characters just like all other sequences.

                         Example to set the ALT-F1 key:

          ESC [ 0 ; 1 ; "run able~dir~set def [dir1.dir2]~logout~" p

          ESC [ 0 ; Pk ; 0 ; Pk p
                         Clears the macro key Pk to a null string.

                         Example  to  clear  any definition associated with
                         the ALT-F4 key:

                         ESC [ 0 ; 4 ; 0 ; 4 p






                                                                    Page 93






          MACRO Frame                                           PC-VT v10.0


                         where Pk is:
                         1       ALT-F1
                         2       ALT-F2
                         3       ALT-F3
                         4       ALT-F4
                         5       ALT-F5
                         6       ALT-F6
                         7       ALT-F7
                         8       ALT-F8
                         9       ALT-F9
                         10      ALT-F10


          10.3  The MACRO.DAT File


                  PC-VT maintains a macro directory file on disk. This file
          is used to record user defined macro key definitions. The file is
          read each time that you start up PC-VT so your macro directory is
          restored each time.


          10.3.1  Creation


                  The MACRO.DAT file is automatically created  as  an empty
          directory if the file does not exist on the  default  drive  when
          PC-VT starts.


          10.3.2  Location


                  The  file  name  is MACRO.DAT. The file is created in the
          directory pointed to  by   the "PC-VT="string in the environment.
          If there is no such string in the environment the file is created
          on the DOS default drive. Chapter 3 on  starting  PC-VT describes
          how to use this string.


          10.3.3  Updating


                  The MACRO.DAT file is rewritten upon request while in the
          MACRO frame by pressing F4.


          10.4  Error Messages


                  Several error messages can be  generated  by  PC-VT while
          manipulating this file.




          Page 94






          PC-VT v10.0                                 VT100 & 4014 Emulator


          "New Macro Key File Created":
                         PC-VT could not find MACRO.DAT on the default disk
                         drive  so  it created an  empty  directory.  PC-VT
                         continues.

          "Disk Directory Full":
                         PC-VT could not find space in the directory of the
                         default disk drive when  it  tried  to  create the
                         MACRO.DAT file. PC-VT terminates.

          "Disk Full While Writing Macro Key File":
                         PC-VT ran out  of  space on the default disk drive
                         while   creating   the   MACRO.DAT   file.   PC-VT
                         terminates.

          "Disk Swap Error - See User Manual":
                         PC-VT found a different  diskette  in  the default
                         drive from the time that the disk  directory entry
                         was created and the  file  MACRO.DAT  was written.
                         Since the time between these  two  events  is very
                         small,  this  error  message  indicates  a  severe
                         hardware or system failure. PC-VT terminates. This
                         error should never  happen  if PC-VT is run from a
                         fixed disk.

          "Error While Opening Macro Key File":
                         PC-VT  failed  to  successfully open the MACRO.DAT
                         file on the default disk. This usually  means that
                         the   disk  directory  has  been  damaged.   PC-VT
                         terminates.

          "Macro Key File Access Error":
                         An error occurred while reading the MACRO.DAT file
                         from the default disk. Usually means that the file
                         has   been    accidentally    overwritten.   PC-VT
                         terminates.

          "Can't find MACRO.DAT. F1 to cancel, space to try again.":
                         This usually means that the default diskette drive
                         is  empty  or  the  door  is  open.   Correct  the
                         situation and hit the space key to continue. Press
                         F1 to terminate PC-VT.














                                                                    Page 95






          MACRO Frame                                           PC-VT v10.0


























































          Page 96






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Chapter 11

                                   4014 Emulation


                  The 4014 emulator requires either the IBM  Color Graphics
          Adapter, the Everex Edge Monochrome/Color  Graphics  Card  or the
          Hercules Graphics  Card. You start the emulator by pressing ALT-T
          from the VT100 Emulator or by starting PC-VT with the  /t command
          line option. You must have specified /e when you started PC-VT if
          you  have  the  Everex Edge card  installed  and  you  must  have
          specified /h if you have the Hercules Graphics Card installed.

                  If you don't have a graphics card in your  PC,  you  will
          see an error message at the bottom of the screen and  PC-VT stays
          in VT emulation mode.

                  When  the  4014  emulator starts up, you will see a short
          help message in the upper right of the screen and the rest of the
          screen will be  blank.  What  you  won't see is a cursor. Neither
          IBM's Color Graphics Adapter card,  Everex's  Edge  card,  or the
          Hercules card supplies a cursor when those boards are operated in
          graphics mode. This shouldn't  be  a problem in most cases as the
          last prompt indicates the cursor position.

                  The  F2  key  emulates the PAGE key on the 4014. Pressing
          that key clears the screen and places the invisible cursor at the
          upper  left of the screen. If you have  selected  the  Page  Full
          feature in the SETUP  B  frame, the speaker beeps when the screen
          fills with  text.  This  beep  is  lower  pitched beep so you can
          distinguish it from  other  beeps.  You  must press the F2 key to
          continue.

                  Terminal  Setup,   Dialing   Directory   and   Macro  key
          definition must be done from VT100 emulation mode.

                  Since the PC screen is not the same as the Tektronix 4014
          screen,  the    following  adjustment  is  made  (high resolution
          coordinates are shown in parentheses):

          For the 4010:
          X scale = Tekpoints 0-1023 are mapped into PC 0-639(720)
          Y scale = Tekpoints 0-779  are mapped into PC 0-199(348)
                    Y points 780-1023 map above the screen but are
                    still valid.





                                                                    Page 97






          4014 Emulation                                        PC-VT v10.0


          For the 4014:
          X scale = Tekpoints 0-4095 are mapped into PC 0-639(720)
          Y scale = Tekpoints 0-3119 are mapped into PC 0-199(348)
                    Y points 3120-4095 map above the screen but are
                    still valid.

                  Because of these adjustments, many Tekpoints  map  into a
          single dot on the PC's screen.

                  The other  adjustment that is made concerns the number of
          character positions  on the screen. The 4014 supports 4 character
          sets. PC-VT supports two character sets if you are using  the IBM
          Color Graphics Adapter - 25 lines  by  80 columns and 33 lines by
          106 columns. Because of  this,  the  exact character positions on
          some graphics output  from  the  host  may not appear in the same
          position  as  on a real 4014. The same is true if  you  have  the
          Everex Edge or Hercules card installed. The situation is a little
          better, though, as hardware  supports  43  lines of 90 characters
          and  58  lines  of 120 characters which more closely emulates the
          4014.

                  With all three graphics cards, the smaller  character set
          produces capital letters only.

                  Unlike a real 4014,  PC-VT  handles  XON  and XOFF like a
          VT100 even in 4014 mode. If you do not want this handshaking, you
          must disable the XON/XOFF feature in the SETUP B frame.


          11.1  4014 Options


                  Strap options on the 4014 are selectable from the SETUP B
          frame:


          Strap 1        Carriage Return effect  -  the ENTER key on the PC
                         can be set to send either a carriage  return  or a
                         carriage   return  and  a  linefeed.  Default   is
                         carriage return only.

          Strap 2        DEL Implies LOY -  PC-VT  can  be set to interpret
                         DEL  (ASCII 127) as a low order Y  code  or  as  a
                         RUBOUT. Defaults to low order Y code.

          Strap 3        Line Feed effect - the  CTRL-J  (linefeed)  key on
                         the PC can be set to send either just a  line feed
                         or a line  feed  and a carriage return. Default is
                         line feed only.

          Strap 4        GIN Terminator  -  A  single  carriage  return  is
                         normally sent  as  the  GIN  Terminator.  You  can
                         change this to no GIN terminator.



          Page 98






          PC-VT v10.0                                 VT100 & 4014 Emulator


          11.2  4014 Keyboard Mapping


                  All ASCII character keys on  the  IBM  PC's  keyboard map
          directly into the corresponding keys for the 4014. The 4014 has a
          very simple  keyboard layout. Most of the keyboard's special keys
          have no effect in this mode.


          11.2.1  Regular Key Mapping



          4014 Key          PC Equivalent Key                  Notes


          PAGE KEY

                         F2          acts as the PAGE key on the  4014. The
                         screen is cleared and the  cursor  is  returned to
                         the home position.



          RESET

                          CTRL-HOME  acts as the RESET key on the 4014. The
                         screen is cleared, the  cursor  is  homed  and all
                         options are reset.



          Arrow Keys

                          Arrow Keys The  PC's  arrow  keys  are  used  for
                         cursor movement. In  conjunction with the Ins key,
                         the arrow keys cause faster cursor movement. Press
                         and release the Ins key and PC-VT moves the cursor
                         in larger steps. Press  and  release  the  Ins key
                         again and PC-VT returns cursor movement to 1 pixel
                         steps.



          RUBOUT

                          Del        "Del"  emulates the RUBOUT key on  the
                         4014.



          BACKSPACE




                                                                    Page 99






          4014 Emulation                                        PC-VT v10.0


                          Backspace  The  backspace  key  sends a backspace
                         character  to  the host. The  character  sent  can
                         either be an ASCII 8  or an ASCII 127 depending on
                         the setting of the backspace character bit  in the
                         SETUP B frame.



          TTY LOCK

                          Caps Lock  The Caps Lock key acts as the TTY lock
                         key on the 4010.



          ----

                          Scroll LockThe 4014 does not a have a hold screen
                         function. With PC-VT you can press SCROLL  LOCK to
                         stop  vector  drawing.  Pressing SCROLL LOCK again
                         resumes drawing.




          11.2.2  Control Function Keys


                  Most CTRL-Fx keys operate the  same  manner  as  in VT100
          emulation mode:


          Key             Function

          F1             Returns to VT100 emulation.

          CTRL-F2        Changes  the default disk directory for  uploading
                         and downloading files. See Chapter 8.

          CTRL-F3        Receives a file (ASCII or XMODEM). See Chapter 8.

          CTRL-F4        Transmits a file (ASCII or XMODEM). See Chapter 8.

          CTRL-F5        Prints the screenon  the selected printer (LPT1 or
                         LPT2), if present. The printer is selected  in the
                         SETUP B frame.  If the Print Termination Character
                         is set in the SETUP B frame, the paper is moved to
                         the  top  of  the next page after  the  screen  is
                         printed.

          CTRL-F7        Sends a BREAK. To  send  a  sustained break to the
                         host, press CTRL-F7. Confirmation of the operation
                         is  a  click  at the start of the break along with
                         another click at the end of the operation.


          Page 100






          PC-VT v10.0                                 VT100 & 4014 Emulator


          CTRL-F8        Terminates  the program,  clears  the  screen  and
                         returns control to DOS.


          11.2.3  ALT Keys


          ALT-F1 thru ALT-F10 :
                          Can be used as macro keys.

          ALT-H:         Enters the HELP frame.  Once  you  are in the HELP
                         frame, use the PgDn key to look at  the  next HELP
                         page, use the PgUp key  to  look  at  the previous
                         HELP  page,  and  use the Esc key to exit HELP and
                         return to  the  emulator.  HELP  works  from  most
                         frames and is context sensitive. That  is,  if you
                         need HELP within the 4014 communication frame, you
                         get 4014 information.

          ALT-K :        Starts  up  the KERMIT module.  See  the  attached
                         KERMIT document for details on its command set.

          ALT-F :        Starts up another copy of  COMMAND.COM.    This is
                         done without  terminating  PC-VT  or  breaking the
                         host  connection.   Once the  new  COMMAND.COM  is
                         started, you  can run any DOS function or other PC
                         program.  You should be careful that you don't run
                         a  program that uses the same communications  port
                         as PC-VT is  using  since  the  other  program may
                         leave the  port in an unexpected state.  PC-VT may
                         not then be able to get control of the port again.
                         Also be careful that  you  don't  alter  any files
                         which PC-VT may be using.  To  exit  from  the new
                         copy  of  COMMAND.COM and return  to  PC-VT,  type
                         "exit" at the command prompt.

          ALT-Z :        Hangs   up  the  phone.PC-VT  performs  the   same
                         functions as if you had entered the  DIALING frame
                         and pressed F5. That is, the Hayes compatible hang
                         up command is sent to the modem.


          11.3  4014 Error Messages


          "4014 Graphics Emulation Requires the Color Graphics Adapter"

                         PC-VT  could  not find a  Color  Graphics  Adapter
                         card.  If  you  have  both  Monochrome  and  Color
                         Graphics  Adapter  cards  in  your system, you may
                         have left  off the /b option from the command line
                         when you started PC-VT.  If  you  have  the Everex
                         Edge card installed, you left off  the  /e option.



                                                                   Page 101






          4014 Emulation                                        PC-VT v10.0


                         If you have the Hercules card installed,  you left
                         off the /h option.






















































          Page 102






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Chapter 12

                                  PC-VT Status Line


                   When in the VT100 communications frame, PC-VT  uses line
          25  of  the  monitor as a status line. The VT100 only requires 24
          lines for proper operation.  The  4014  emulator does not display
          this  line.  The  meaning of each  of  the  fields  displayed  is
          summarized in this chapter.


          On Line        PC-VT is actively monitoring the COMx port.  It is
                         on line to a host only if you have established the
                         connection.

          Local          PC-VT  is performing some local function and  data
                         received on the COMx port  is  not  displayed. The
                         data is not lost  but  is  buffered  and displayed
                         when PC-VT returns  to  on line mode. Note that on
                         the  PCjr this may not be true.  If  the  PCjr  is
                         doing  a diskette operation, all other  interrupts
                         are masked off. If  data  is  received on the COMx
                         line, it is lost.

          Vx.x           The  version number of PC-VT. Please include  this
                         number if you write to us.

          KBD LOCKED     The  host  computer  has  locked the keyboard. The
                         host   is  also  responsible  for  unlocking   the
                         keyboard. PC-VT clicks the  speaker  if  a  key is
                         pressed when the keyboard is locked.

          CAP            The  Caps  Lock  key  has  been  depressed  on the
                         keyboard.

          NUM            The  Num  Lock  key  has  been  depressed  on  the
                         keyboard.

          SCR            The SCROLL LOCK  key  has  been  depressed  on the
                         keyboard. This key functions as the NO  SCROLL key
                         on the VT100.

          " "            The Greek letter alpha  is  displayed  to indicate
                         that  PC-VT is in VT100 Applications Keypad  mode.
                         This permits the PC's function and keypad  keys to
                         transmit special codes. See  chapter  5.  The host
                         controls entrance and exit to this mode.


                                                                   Page 103






          PC-VT Status Line                                     PC-VT v10.0


          X              Indicates that the host's buffer has filled up and
                         that the host is not accepting any more characters
                         from the PC. This  clears  automatically  when the
                         host's buffer has emptied.  Press  ALT-X  to clear
                         this flag in the cases  where  some  noise  on the
                         communications line happened to set it.

          P              Indicates that printer echo is turned  on  and all
                         characters displayed on  the screen are printed on
                         the  printer.  Characters  displayed on the status
                         line are never printed. Printer echo can be turned
                         on  by  the  host  via  an Escape sequence  or  by
                         pressing CTRL-F6 on the PC's keyboard.

          HH:MM:SS       Displays the time  of  day. This can be turned off
                         by resetting the CLOCK bit in the SETUP B frame.

          DSR            Indicates that the modem has raised  its  Data Set
                         Ready line. This indicator as well as the next two
                         modem status  indicators  can  be  turned  off  by
                         resetting the CLOCK bit in the SETUP B frame. Most
                         smart modems keep  this  line high at all times to
                         indicate that they  are ready to receive commands.
                         Note that PC-VT does not really care.  It displays
                         this only for information.

          CTS            Indicates that the modem has raised  its  Clear To
                         Send line. Some modems maintain this line  high at
                         all times.  There is usually a switch on the modem
                         which causes this  line to function normally. Note
                         that PC-VT does not really care. It  displays this
                         only for information.

          CD             Indicates that the modem  has  raised  its Carrier
                         Detect  line. Some modems maintain this line  high
                         at all times. There is  usually  a  switch  on the
                         modem which causes this line to function normally.
                         Note that PC-VT does not really care.  It displays
                         this only for information.

          L1L2L3L4       These represent the LED's on the  VT100.  All four
                         are used on the VT100  and the VT102, and none are
                         used on the VT52.













          Page 104






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Chapter 13

                                   Error Messages


                  This chapter  lists error messages which do not appear in
          other chapters or which deserve a more detailed explanation.

                  Error   messages   regarding   the   USER   MEMORY   file
          (PARAMS.DAT)  may  be  found  at  the end of Chapter 7.  Messages
          regarding file transfer  may  be  found  at the end of Chapter 8.
          Dialer messages are at  the  end of Chapter 9. Macro messages are
          at the end of Chapter 10.

                  PC-VT detects  all errors which occur while it is running
          in  order   to  notify  the  user  and  terminate  gracefully  if
          necessary.


          "PC-VT Requires DOS 2.0 or later.":
                         PC-VT  requires  DOS  2.0  or  later  in  order to
                         execute.

          "Sorry, not enough memory for HELP":
                         PC-VT  dynamically  allocates  memory for the HELP
                         data. This message  says that the Operating System
                         could not  allocate  PC-VT  the  additional memory
                         that it needed for the HELP frame.

          "Sorry, could not load the HELP file":
                         PC-VT could not  find  the  HELP.DAT  file  on the
                         default drive or the drive specified  by  the "PC-
                         VT="  environment  string. If you  are  running  a
                         diskette system, you  must have the PC-VT diskette
                         with the HELP.DAT file in the drive the first time
                         that you press ALT-H. This is when PC-VT reads the
                         file into memory. After  the  first  press  of the
                         HELP key, the file is kept in memory  so  that the
                         copy on the diskette is no longer needed.

          "File COMMAND.COM could not be found. Error xx":
                         You just pressed ALT-F to start up another copy of
                         COMMAND.COM and PC-VT could not locate it on disk.
                         This usually means that if you  are  running PC-VT
                         from a floppy  diskette, you must copy COMMAND.COM
                         to   that  floppy   diskette.   PC-VT   uses   the
                         environment  string  "COMSPEC="   to   locate  the
                         COMMAND.COM   program.   This   string   is    set


                                                                   Page 105






          Error Messages                                        PC-VT v10.0


                         automatically to the boot drive when you  start up
                         PC-VT. To check to see  if  it  is  set correctly,
                         type in the  "SET"  command  from  the  DOS prompt
                         after you terminate PC-VT by pressing CTRL-F8. The
                         error  number  is described in  the  DOS  Software
                         Technical  Reference  Manual.  Some  of  the  more
                         common errors are:

                         02      COMMAND.COM not found
                         03      Path given in the "COMSPEC="
                                 string is invalid
                         05      Access Denied

          "File KERMIT.COM could not be found. Error xx":
                         You just pressed ALT-K to start up  KERMIT.COM and
                         PC-VT could not locate it  on  disk.  This usually
                         means that  if you are running PC-VT from a floppy
                         diskette, you must  copy KERMIT.COM to that floppy
                         diskette. PC-VT looks for the program first in the
                         DOS  search path set by the environment  variable,
                         "PATH=". Then it  looks in the directory specified
                         by the  "PC-VT="  variable.  To  check  to  see if
                         either of these  variables are set correctly, type
                         in the "SET" command from the DOS prompt after you
                         terminate PC-VT  by  pressing  CTRL-F8.  The error
                         number is described  in the DOS Software Technical
                         Reference  Manual. Some of the more common  errors
                         are:

                         02      KERMIT.COM not found
                         03      Path given in the "PATH=" or
                                 "PC-VT=" strings is invalid
                         05      Access Denied

          "Disk not ready or Fixed Disk  error.  Abort or Retry (Press a or
          r) ?":          PC-VT just encountered a  disk  error.  The error
                         most likely was caused by  a door open on a floppy
                         diskette drive. Correct the situation and have PC-
                         VT retry the operation by  pressing  'r'.  To have
                         PC-VT  abort the  disk  operation  and  terminate,
                         press 'a'.

          "Fatal FAT Error. PC-VT Terminating. Press any key.":
                         PC-VT just found a  fatal  error  in the disk File
                         Allocation Table (FAT). PC-VT cannot  continue and
                         terminates as soon as you press any key.

          "PC-VT Requires an 80 Column Display":
                         The VT100 is an 80  column  device  so  PC-VT must
                         have an 80 column output device.

          "PC-VT Terminated...":
                         Indicates that PC-VT  successfully  terminated. It
                         closed the communications  buffer so that any data


          Page 106






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         received is lost. If you want to get  back  to DOS
                         without closing the  communications  buffer, press
                         ALT-F instead of CTRL-F8.

          "Found old versions of PARAMS.DAT and DIALER.DAT files."
          "Delete them and restart PC-VT"

                         Your diskette or  fixed  disk  has  copies  of the
                         PARAMS.DAT  and DIALER.DAT  files  from  an  older
                         version  of  PC-VT. The newer  versions  of  PC-VT
                         cannot use these files. Delete these two files and
                         then  restart  the  program.  PC-VT  automatically
                         recreates the files in their new format.

          "EVEREX EDGE card must be in monochrome mode"
          "use this command at the DOS prompt :"
          "SETMODE -amono -c80 -r25 -mmono"

                         You have told PC-VT  to  use  the Everex Edge card
                         for display output  and  the card is set for color
                         mode. In order for PC-VT  to use the card, it must
                         be in  monochrome mode. At the DOS prompt, type in
                         the command shown.

          "When using both monitors, start PC-VT from"
          " the Monochrome monitor"

                         You have told PC-VT to  use both the color and the
                         monochrome  displays.  PC-VT  must be started from
                         the monochrome display in this  case.  At  the DOS
                         prompt, enter the DOS command "mode mono".

























                                                                   Page 107






          Appendix 13                                           PC-VT v10.0


























































          Page 108






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Appendix A

                              VT100 Control Characters


                  These  appendices describe the internal operation of  PC-
          VT. They show the various control characters and escape sequences
          which PC-VT interprets as commands.  The  character  "ESC"  is an
          ASCII  control  character  with the decimal value  of  27.  These
          appendices can be skipped if your only use of PC-VT is  simply as
          a VT100 Video Terminal.

                  ASCII codes from 0 to  31 and 127 are control characters.
          PC-VT responds to these characters  as  listed  in  the following
          table.

          Name            Code            Function

          Null            0       This character is ignored. It can be
                                  used as a fill character. A fill
                                  character is sometimes used to take
                                  up space in a messages for timing
                                  reasons.

          End of Text     3       Not supported. PC-VT ignores this
                                  character.

          End of          4       This  character  can  be  selected  as  a
          Transmission disconnect character by the SETUP B
                                  frame. If selected, its receipt
                                  causes PC-VT to disconnect from the
                                  communications line by sending a Break.

          Enquire         5       Causes PC-VT to transmit its answerback
                                  message. The answerback back message is
                                  set in the SETUP B frame.

          Bell            7       Causes PC-VT to beep the IBM PC speaker.

          Backspace       8       Causes PC-VT to move the cursor back one
                                  column and delete the character there.
                                  If the cursor is already in column 1,
                                  this character is ignored.

          Horizontal Tab  9       Causes PC-VT to move the cursor to the
                                  next tab stop. If there are no tab stops
                                  between the current cursor position and
                                  column 80, the cursor is moved to column


                                                                   Page 109






          Appendix A                                            PC-VT v10.0


                                  80. The tab stops are set in
                                  the SETUP A frame.

          Line Feed       10      Causes the cursor to move down one
                                  line in the current column. If the
                                  cursor moves below the screen output
                                  area, the lines above the cursor move up
                                  one line, and a blank line is added to
                                  the bottom of the screen. The operation
                                  of this key is modified by the Line Feed/
                                  New Line feature selected in SETUP B.

          Vertical Tab    11      Handled as a line feed.

          Form Feed       12      Handled as a line feed except when being
                                  sent to a line printer via one of the
                                  print commands. It those cases, it is
                                  sent to the line printer as a Form
                                  Feed.

          Carriage Return 13      The cursor is moved back to the left
                                  margin. Cursor remains in the current
                                  line.

          Shift Out       14      Causes PC-VT to change its character set
                                  to the G0 character set. The G0 character
                                  set is selected by the Select Character
                                  Set escape sequence.

          Shift In        15      Causes PC-VT to change its character set
                                  to the G1 character set. The G1 character
                                  set is selected by the Select Character
                                  Set escape sequence.

          XON (Device     17      Causes  PC-VT  to  continue  or   restart
          Control 1) sending characters.

          XOFF (Device    19      Causes PC-VT to stop transmitting Control
          3) characters. It does not stop PC-VT
                                  from sending XON or XOFF.

          Cancel          24      Causes PC-VT to interrupt and cancel any
                                  in process escape control sequence.
                                  If received during the parsing of
                                  an escape sequence, it cancels the
                                  sequence without notification.

          Substitute      26      Handled as Cancel. If received during
                                  the parsing of an escape sequence, it
                                  cancels the sequence and displays an
                                  upsidedown question mark. It is also
                                  used as an End of File indicator
                                  during ASCII file transfers.



          Page 110






          PC-VT v10.0                                 VT100 & 4014 Emulator


          Escape          27      Indicates the start of a special escape
                                  control sequence. If received during
                                  the parsing of an escape sequence, it
                                  cancels the sequence without
                                  notification.

          Delete          127     This character is ignored when received.

                  All other control characters are ignored.















































                                                                   Page 111






          Appendix A                                            PC-VT v10.0


























































          Page 112






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Appendix B

                           VT100 Received Escape Sequences




                  PC-VT constantly monitors the communications line for the
          incoming escape sequences listed below. When  they  are received,
          PC-VT performs the function  as  shown.  The escape character and
          the characters which follow  it  and are part of the sequence are
          not displayed. When receiving (downloading) an ASCII  file, PC-VT
          copies  these  characters  to the PC disk file being created. The
          escape  character  is  shown below as  "ESC"  and  is  the  ASCII
          character with the value of 27.

                  Many  of  the  sequences  listed  are  extensions  to the
          standard VT100 and VT102  ANSI  escape  sequences.  Those include
          color support,  direct  control  of  PC-VT  using  private escape
          sequences, the 'Insert Character - ESC[Pn@' sequence,  the Device
          Status Report:Error sequence and keyboard redefinition sequences.


          Keypad Character Selection

          ESC =          Select  Alternate Keypad Mode - Sets the  keyboard
                         to transmit the  Alternate Keypad set of character
                         codes.

          ESC >          Select Numeric Keypad Mode - Sets the  keyboard to
                         transmit  the  Numeric  Keypad  set  of  character
                         codes.

          Select Character Sets

          ESC ( A        Select U.K. Character Set as G0 - The standard IBM
                         PC character  set is selected for ASCII codes 0 to
                         34 and 36 to 127. ASCII code 35 is replaced by the
                         extended character 156, the UK Pound sign.

          ESC ( B        Select U.S. Character Set as G0 - The standard IBM
                         PC character  set is selected for ASCII codes 0 to
                         127.

          ESC ( 0        Select Special Characters  and Line Drawing Set as
                         G0 - A  special  character and line drawing set is
                         selected. The  set  is  identical  to  the  IBM PC



                                                                   Page 113






          Appendix B                                            PC-VT v10.0


                         character set for ASCII codes 0 to 95. ASCII codes
                         96 to 127 are shown below.

          ESC ) A        Select U.K. Character Set as G1- The  standard IBM
                         PC character  set is selected for ASCII codes 0 to
                         34 and 36 to 127. ASCII code 35 is replaced by the
                         extended character 156, the UK Pound sign.

          ESC ) B        Select U.S. Character Set as G1 - The standard IBM
                         PC character  set is selected for ASCII codes 0 to
                         127.

          ESC ) 0        Select Special Characters  and Line Drawing Set as
                         G1 - A  special  character and line drawing set is
                         selected. The  set  is  identical  to  the  IBM PC
                         character set for ASCII codes 0 to 95. ASCII codes
                         96 to 127 are shown below.







































          Page 114






          PC-VT v10.0                                 VT100 & 4014 Emulator


          Special Character and Line Drawing Set

          ASCII Code      Character               IBM PC ASCII Code

          0 - 95          Same as the standard IBM PC character set.
          96              Diamond                           4
          97              Large Block                     219
          98              Horizontal Tab (right arrow)     26
          99              Formfeed (up triangle)           30
          100             Carriage Return (left arrow)     27
          101             Linefeed (up arrow)              24
          102             Degree Symbol                   248
          103             Plus/Minus Sign                 241
          104             New Line (down arrow)            25
          105             Vertical Tab (up/down arrow)     23
          106             Upper Right Corner              217
          107             Lower Right Corner              191
          108             Lower Left Corner               218
          109             Upper Left Corner               192
          110             Crossing Lines                  197
          111             Horizontal Line                 196
          112             Horizontal Line                 196
          113             Horizontal Line                 196
          114             Horizontal Line                 196
          115             Horizontal Line                 196
          116             Left T                          195
          117             Right T                         180
          118             Top T                           193
          119             Bottom T                        194
          120             Vertical Line                   179
          121             Less Than or Equal To           243
          122             Greater Than or Equal           242
          123             Pi Symbol                        20
          124             Not Equal Sign (squiggle)       247
          125             UK Pound Sign                   156
          126             Centered Dot                    250
          127             blank                            32


          Display Attributes

          ESC [ m        Select   Graphic   Rendition  -   Resets   Display
                         Attribute to default per SETUP B display.

          ESC [ 0 m      Same as "ESC [ m".

          ESC [ 1 m      Select Graphic Rendition - Sets  Display Attribute
                         to bold. PC-VT does not support  bold  and reverse
                         video concurrently.

          ESC [ 4 m      Select Graphic Rendition - Sets  Display Attribute
                         to  underline  (IBM  Monochrome Display only). For
                         the  Color  Graphics  Adapter, PC-VT displays this
                         attribute as bold or bold & blinking so that it is


                                                                   Page 115






          Appendix B                                            PC-VT v10.0


                         recognizable. The  attribute  is  selected  in the
                         SETUP B frame. PC-VT  does  not  support underline
                         and reverse video concurrently.

          ESC [ 5 m      Select Graphic Rendition - Sets  Display Attribute
                         to blink.

          ESC [ 7 m      Select Graphic Rendition - Sets  Display Attribute
                         to reverse video. PC-VT does not support underline
                         or bold and reverse video concurrently.

                         Bold does not appear when the screen is in reverse
                         video. This is a limitation  of  the  PC hardware.
                         Underline appears in  reverse video since the same
                         bits in the hardware attribute are used to control
                         those two modes.

                         The  other  modes   are  additive.  That  is,  The
                         sequence "ESC [ 7 m  ESC [ 5 m" produces blinking,
                         high intensity video. Then "ESC  [  m"  resets the
                         display to the default, usually white on black.

                         PC-VT supports multiple parameters for  the Select
                         Graphic Rendition sequence. For example, the three
                         sequences  in the previous paragraph can be  coded
                         as "ESC [ 7 ; 5 ; 1 m". Up to 14 parameters may be
                         specified.

                         Figure B.1 shows what you will see on a Monochrome
                         monitor.  With  the CGA monitor  the  results  are
                         similar depending on  what selection you have made
                         for underline in the SETUP B frame.
























          Page 116






          PC-VT v10.0                                 VT100 & 4014 Emulator




          ---------------------------------------------------------------------------

          Screen in White on Black Mode

          Attribute:
                  Under                                   Screen
          Normal  Line    Blink   Reverse Bold            Displays
          x                                               Normal Video
          x       x                                       Underline Normal Video
          x               x                               Blink Normal Video
          x       x       x                               Underline Blink Normal
          Video
                                  x                       Negative Video
                  x               x                       *Negative Video
                          x       x                       Blink Negative Video
                  x       x       x                       *Blink Negative Video

                                          x               Bold Video
                  x                       x               Underline Bold Video
                          x               x               Blink Bold Video
                  x       x               x               Underline Blink Bold Video
                                  x       x               *Negative Video
                  x               x       x               *Negative Video
                          x       x       x               *Blink Negative Video
                  x       x       x       x               *Blink Negative Video


          Asterisks indicate modes which are not exactly like the VT100.


                  Figure B.1 PC-VT Video Attribute Handling



          ---------------------------------------------------------------------------



















                                                                   Page 117






          Appendix B                                            PC-VT v10.0




          ---------------------------------------------------------------------------


          Screen in Black on White Mode
          Attribute:
                  Under                                   Screen
          Normal  Line    Blink   Reverse Bold            Displays
          x                                               Negative Video
          x       x                                       *Normal Video
          x               x                               Blink Negative Video
          x       x       x                               *Blink Normal Video
                                  x                       Normal Video
                  x               x                       *Normal Video
                          x       x                       Blink Normal Video
                  x       x       x                       *Blink Normal Video

                                          x               *Negative Video
                  x                       x               *Normal Video
                          x               x               *Blink Negative Video
                  x       x               x               *Blink Normal Video
                                  x       x               *Normal Bold Video
                  x               x       x               *Normal Bold Video
                          x       x       x               *Blink Bold Normal Video
                  x       x       x       x               *Blink Bold Normal Video


          Asterisks indicate modes which are not exactly like the VT100.

                  Figure B.1 (continued) PC-VT Video Attribute Handling



          ---------------------------------------------------------------------------





















          Page 118






          PC-VT v10.0                                 VT100 & 4014 Emulator



          Color

                         PC-VT  can  handle  color if you are  on  a  color
                         monitor.  The  color  must  be  set  by  the  host
                         computer.

          ESC [ Pc m     Select Graphic Rendition - Sets  Display Attribute
                         to  the  color  given by Pc as follows (Pc must be
                         sent as 1 or 2 ASCII characters):

                         8               Invisible
                         30              Black Foreground
                         31              Red Foreground
                         32              Green Foreground
                         33              Yellow Foreground
                         34              Blue Foreground
                         35              Magenta Foreground
                         36              Cyan Foreground
                         37              White Foreground
                         40              Black Background
                         41              Red Background
                         42              Green Background
                         43              Yellow Background
                         44              Blue Background
                         45              Magenta Background
                         46              Cyan Background
                         47              White Background


                         Example   to   set   red   characters  on  a  blue
                         background:

                         ESC [ 3 1 m ESC [ 4 4 m ESC [ 2 J ESC [7 H

                         Where ESC is the escape character ASCII 27.

                         Note that setting the colors does  not  affect the
                         current  contents of the display. Only  characters
                         displayed  following  the  color setting sequences
                         are in color. This is  consistent  with  the other
                         Select  Graphic Rendition sequences. To clear  the
                         screen to the new background color, use  the clear
                         screen  sequence  followed  by  the   home  cursor
                         sequence.  By just using the color sequences,  you
                         can  display portions of your output in  different
                         colors.

                         Certain   of   these  combinations,   like   black
                         foreground characters on a black background, won't
                         show anything on the display.

                         The  colors  which   you  select  become  the  new
                         temporary defaults for PC-VT. That is, if  you set


                                                                   Page 119






          Appendix B                                            PC-VT v10.0


                         up white on blue and  send the "ESC [ m" sequence,
                         the color is reset to the defaults which are white
                         on blue. If  you  want to return to standard white
                         characters on a black  background,  you  must send
                         "ESC [ 3 7 m ESC [ 4 0 m".

                         To make the selected colors permanent for the next
                         time  you  run  PC-VT, go to the SETUP A frame and
                         select the "s" store option.

          Scrolling Margin

          ESC [ Pt ; Pb r
                         Sets  top  and  bottom  scrolling  margins  -  The
                         scrolling region includes  display  lines starting
                         at Pt and ending at Pb inclusive. Pt  and  Pb must
                         be  between  1  and 24. Pb must be greater than or
                         equal to Pt. If Pt is omitted, it  defaults  to 1.
                         If Pb is omitted, it defaults to 24.

          Cursor Movement Commands

          ESC [ Pn A     Cursor Up  - Moves cursor up Pn lines. If omitted,
                         Pn is assumed to be 1. If the cursor is already at
                         the top of the screen, this  sequence  is ignored.
                         If Pn is  greater than the number of lines  to the
                         top of the screen, the  cursor is moved to the top
                         of the screen.

          ESC [ Pn B     Cursor Down  -  Moves  cursor  down  Pn  lines. If
                         omitted, Pn is assumed to be 1. If  the  cursor is
                         already at the bottom of the screen, this sequence
                         is ignored. If Pn is  greater than  the  number of
                         lines to the  bottom  of the screen, the cursor is
                         moved to the bottom of the screen.

          ESC [ Pn C     Cursor Right - Moves cursor right  Pn  columns. If
                         omitted, Pn is assumed to be 1. If  the  cursor is
                         already at the right margin  of  the  screen, this
                         sequence is ignored. If  Pn  is   greater than the
                         number of  columns  to  the  right  margin  of the
                         screen, the cursor is moved to the right margin of
                         the screen.

          ESC [ Pn D     Cursor Left - Moves  cursor  left  Pn  columns. If
                         omitted, Pn is assumed to be 1. If  the  cursor is
                         already at the left  margin  of  the  screen, this
                         sequence is ignored. If  Pn  is   greater than the
                         number  of  columns  to  the  left  margin  of the
                         screen, the  cursor is moved to the left margin of
                         the screen.





          Page 120






          PC-VT v10.0                                 VT100 & 4014 Emulator


          ESC [ Pl ; Pc H
                         Cursor  Position  -  Moves  the cursor to absolute
                         line given by  Pl and absolute column given by Pc.
                         Pl must be between 1 and 24. Pc must be  between 1
                         and 80. If omitted, Pl and Pc are assumed to be 1.

          ESC [ Pl ; Pc f
                         Same as "ESC [ Pl ; Pc H".

          ESC H          Cursor Position (Home) - Move  the  cursor  to the
                         top left  of the screen. Same as the sequence "ESC
                         [ 1 ; 1 H" or "ESC [ 1 ; 1 f".

          ESC [ f        Same as "ESC H".

          ESC D          Index - Moves the cursor down one line. The cursor
                         remains  in  the  same  column.  A  scroll  up  is
                         performed if the cursor moves below line 24.

          ESC M          Reverse Index  - Moves the cursor up one line. The
                         cursor remains in the same column.  A  scroll down
                         is performed if the cursor moves above line 1.

          ESC E          Next Line -  Moves  the cursor to the first column
                         of the  next line. A scroll up is performed if the
                         cursor moves below line 24.

          ESC 7          Save cursor - Saves  the  current  cursor position
                         (line,column),   display    character   attribute,
                         selected character set, and origin mode.

          ESC 8          Restore Cursor -  Restores the cursor position and
                         other  saved attributes to the values recorded  by
                         the last "ESC [  7"  sequence.  If the save cursor
                         escape sequence has  not been received since PC-VT
                         was started, no values are restored and the cursor
                         is moved to the top left margin.

          Line Attributes

          ESC # 3 and ESC # 4
                         Double  Height  Line,  Top  Half and Double Height
                         Line, Bottom  Half  -  These  two  sequences  must
                         always be used in pairs on adjacent  lines. Double
                         height lines are simulated  in  PC-VT  by blanking
                         the top line and converting the  bottom  line into
                         double width  by taking the left half of the line,
                         inserting  blanks  between   the   characters  and
                         placing them back down to occupy the  entire line.
                         Any characters on  the  right half of the line are
                         lost.

          ESC # 5        Single Width Line - Converts the current line into
                         a single  width  line.  PC-VT  simulates  this  by


                                                                   Page 121






          Appendix B                                            PC-VT v10.0


                         taking  every  other  character  from the line and
                         putting them down in  the  left  half of the line.
                         The right half of the line is blanked.

          ESC # 6        Double Width Line - Converts the current line into
                         simulated  double  width  characters by taking the
                         left half of the  line,  inserting  blanks between
                         the characters  and  placing  them  back  down  to
                         occupy  the  entire line. Any  characters  on  the
                         right  half  of  the  line  are  lost.  The cursor
                         remains in the  same character position unless the
                         cursor would  have  moved  off  the  right  of the
                         screen. In  that case, the cursor is placed at the
                         right margin.

          Tab Stops

          ESC H          Horizontal  Tab  Set  - Clear a tab  stop  at  the
                         column position occupied by the cursor.

          ESC [ g        Tabulation Clear  - Clears the tab, if any, at the
                         column position occupied by the cursor.

          ESC [ 0 g      Same as "ESC [ g".

          ESC [ 3 g      Tabulation Clear - Clears all tabs.

          Editing Functions

          ESC [ Pn @     Insert Character - Inserts Pn  characters starting
                         at the cursor  position. Character(s) to the right
                         of the cursor column move right.  Pn,  if omitted,
                         is assumed to be  1.  Character(s)  moved  off the
                         right of the display are lost.

          ESC [ Pn P     Delete Character - Deletes Pn  characters starting
                         at the cursor position. Characters to the right of
                         the   deleted  character(s)  move  left.  Pn,   if
                         omitted, is assumed to be 1.  Spaces  are inserted
                         at the right as needed.

          ESC [ Pn L     Insert Line - Inserts  Pn  lines  before  the line
                         containing cursor. The  current line and all lines
                         below it move down the display.  Lines  which move
                         below the bottom scrolling margin are lost. Pn, if
                         omitted, is assumed to be 1.

          ESC [ Pn M     Delete Line - Deletes  Pn  lines  starting  at the
                         line containing the  cursor and below. Lines below
                         the deleted lines move  up.  New  blank  lines are
                         created to fill the bottom of the  scrolling area.
                         If omitted, Pn is assumed to be 1.

          Erasing


          Page 122






          PC-VT v10.0                                 VT100 & 4014 Emulator


          ESC [ K        Erase In Line -  Erases  the  line occupied by the
                         cursor from the cursor to the end of the Line.

          ESC [ 0 K      Same as "ESC [ K".

          ESC [ 1 K      Erase In Line -  Erases  the  line occupied by the
                         cursor from  the  beginning  of  the  line  to the
                         cursor.

          ESC [ 2 K      Erase In Line - Erases the entire  line containing
                         the cursor.

          ESC [ J        Erase In Display  -  Erases  the  screen  from the
                         current cursor position to the bottom left  of the
                         display.

          ESC [ 0 J      Same as "ESC [ J".

          ESC [ 1 J      Erase In  Display - Erases the screen from the top
                         right  of  the   display  to  the  current  cursor
                         position.

          ESC [ 2 J      Erase In Display - Erases the entire screen.

          Print Commands

                         These commands are ignored if there is no printer
                         attached to the PC or if
                         the printer is not ready. LPT1 or LPT2 is selected
                         on the SETUP B frame. In
                         the normal VT100 definition, any formfeed
                         characters are translated to
                         linefeed characters before they are displayed. PC-
                         VT does not translate
                         formfeeds which are routed the printer.

                         If  a  printer  error  occurs, the escape sequence
                         "ESC [ ? 10 n"  returns the error code.

          ESC [ ? 5 i    Media Copy - Turn on  Auto  Print.  All characters
                         locally or echoed  by  the host are printed on the
                         selected  printer,  if   present,  as  soon  as  a
                         carriage return is  received. The character 'P' is
                         displayed in column 42 of the Status Line (line 25
                         ) of  the display to indicate that printer echo is
                         turned on.

          ESC [ ? 4 i    Media Copy - Turns off Auto Print.

          ESC [ 5 i      Media  Copy  -  Turns  on  Print  Controller.  All
                         characters received from the host are displayed on
                         the selected printer, if  present,  as  soon  as a
                         carriage return is received. Nothing  is displayed
                         on the screen.


                                                                   Page 123






          Appendix B                                            PC-VT v10.0


                         When Print Controller mode is on, escape sequences
                         are not sent to  the  printer.  This  is different
                         than the strict VT  printer  definition.  The next
                         sequence  when parsed, turns off Print  Controller
                         mode.

          ESC [ 4 i      Media  Copy  -   Turns  off  Print  Controller.  A
                         carriage return and linefeed should be sent to the
                         selected printer before transmitting this sequence
                         to be sure that the  printer is ready for the next
                         print sequence and that the print  carriage  is at
                         the left margin.

          ESC [ i        Media Copy - The  screen  as  defined by the print
                         extent  in  the  SETUP B frame is  copied  to  the
                         selected  printer, if present. A formfeed is  sent
                         to the selected printer at the  conclusion  of the
                         printing  if the Termination Character feature  is
                         set in the SETUP B frame.

          ESC [ ? 1 i    Media Copy - The  line  containing  the  cursor is
                         printed on the selected printer, if present.

          ESC [ ? 3 i    Special  Print  - A PC-VT  private  sequence.  The
                         contents  of the filename download buffer is  sent
                         to the printer. Underline characters are converted
                         to the  Escape  character  (ASCII  27).  Load  the
                         buffer  with the "ESC [ ? 2 4 h" and "ESC [ ? 2  4
                         l" sequences. See Appendix J.

          Reports

          ESC [ 5 n      Device Status Report, Hardware - The status of PC-
                         VT and hardware is reported with this response:

                         "ESC [ 0 n "        PC-VT is OK.

          ESC [ ? 10 n   Device Status Report, Error - The last error which
                         occurred  is  reported.  A private PC-VT sequence.
                         Format is:

                         "ESC [ ? x ; y n "      Last error  or  DOS return
                         code  which occurred is returned as  x.  If  x  is
                         zero, usually no error occurred.  Termination code
                         returned by a called program is  y.  This response
                         is available  for  printer  errors,  file transfer
                         errors  and  calling  of  COMMAND.COM.  Check  the
                         technical appendix for details.

          ESC [ ? 15 n   Device Status Report, Printer - The status  of the
                         selected printer is reported with these responses:





          Page 124






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         "ESC [ ? 13 n   "       No printer on system
                         "ESC [ ? 10 n   "       Printer ready
                         "ESC [ ? 11 n   "       Printer not ready.

          ESC [ 6 n      Device  Status  Report,  Cursor  Position   -  The
                         position of  the  cursor  is  reported  with  this
                         response:

                         "ESC [ Pl ; Pc R"       The cursor is currently at
                         line Pl and column Pc.

          ESC [ c        Device Attribute Report - PC-VT reports that it is
                         a VT102 or  VT100 Video Terminal compatible device
                         with the responses:

                         "ESC [ ? 6 c"           I am a VT102
                          or
                         "ESC [ ? 1 ; 2 c"       I am a VT100 with Advanced
                         Video Option (AVO)

                         The  response  depends   upon  the  state  of  the
                         Terminal Type  bit in the SETUP B frame. The VT100
                         terminal response includes the AVO indication even
                         though your hardware may not support 132 columns.

          ESC [ 0 x      Request  Terminal  Parameters  - PC-VT reports its
                         terminal   parameters   and   enables  unsolicited
                         reporting. When unsolicited reporting is  enabled,
                         PC-VT  reports  terminal  parameters when SETUP is
                         exited (in VT100 emulation mode only).

          ESC [ 1 x      Request  Terminal  Parameters  - PC-VT reports its
                         terminal  parameters   and   disables  unsolicited
                         reporting.

                         Terminal Parameters are reported as follows :
                         "ESC [ Ps ; Pp ; Pn ; Px ; Pr ; 1 ; x"          Where
                         :
                         Ps is  2 indicating that this sequence is a report
                         or 3 indicating that this sequence is a report and
                         that unsolicited reporting is disabled,
                         Pp is 1 indicating  no  parity,  4  indicating odd
                         parity or 5 indicating even parity,
                         Pn is 1 indicating 8 data bits or  2  indicating 7
                         data bits,
                         Px and Pr (both  identical)  indicating  COM1 port
                         speed as follows:









                                                                   Page 125






          Appendix B                                            PC-VT v10.0


                                 Value           Speed
                                 -----           -----
                                 16              100 baud
                                 32              150 baud
                                 48              300 baud
                                 64              1200 baud
                                 88              2400 baud
                                 104             4800 baud
                                 112             9600 baud

          ESC [ 0 c      Same as "ESC [ c".

          ESC Z          Same as "ESC [ c".

          Reset

          ESC c          Reset to Initial State -  PC-VT  is  reset  to its
                         initial state by reading the USER  MEMORY  file on
                         the default drive.  The program is then restarted.
                         If a host was selected,  either  from  the command
                         line or in the  DIALER  frame,  the SETUP data for
                         that host is  reloaded.  PC-VT sends an XON to the
                         host if XON/XOFF support is selected.

          Tests and Adjustments

          ESC[ ... y     PC-VT does  not run any local tests in response to
                         these  sequences. PC-VT  just  responds  with  the
                         terminal OK response  "ESC  [ 0 n". PC-VT sends an
                         XON to the host if XON/XOFF support is selected.

          Keyboard LED's

                         Four LED's are supported in both  VT100  and VT102
                         modes.

          ESC [ q        Load LED  (LED's  off)  -  The  emulated  LED's on
                         Status Line 25 of the display are turned off.

          ESC [ 0 q      Same as "ESC [ q".

          ESC [ 1 q      Load LED (L1 on) - The emulated LED  L1  on Status
                         Line 25 of the display is turned on.

          ESC [ 2 q      Load LED (L2 on) - The emulated LED  L2  on Status
                         Line 25 of the display is turned on.

          ESC [ 3 q      Load LED (L3 on) - The emulated LED  L3  on Status
                         Line 25 of the display is turned on.

          ESC [ 4 q      Load LED (L4 on) - The emulated LED  L4  on Status
                         Line 25 of the display is turned on.

          VT52 Compatible Mode


          Page 126






          PC-VT v10.0                                 VT100 & 4014 Emulator


          ESC <          Enter ANSI mode.

          ESC =          Enter alternate keypad mode.

          ESC >          Exit alternate keypad mode to numeric keypad mode.

          ESC F          Select special graphics character set.

          ESC G          Select US/UK character set.

          ESC A          Cursor up.

          ESC B          Cursor down.

          ESC C          Cursor right.

          ESC D          Cursor left.

          ESC H          Home cursor.

          ESC Y Pl Pc    Direct cursor address.

          ESC I          Reverse linefeed.

          ESC K          Erase to end of line.

          ESC J          Erase to end of screen.

          ESC ^          Enter auto print mode.

          ESC _          Exit auto print mode.

          ESC W          Enter printer controller mode.

          ESC X          Exit printer controller mode.

          ESC ]          Print screen.

          ESC V          Print current line.

          ESC Z          Identify what you are. PC-VT responds with  "ESC /
                         Z".

                         PC-VT   still  responds  to  DEC  private   escape
                         sequences while in VT52 compatibility mode.

          Set Mode

          ESC [ 2 h      Keyboard Action - The keyboard is locked. Pressing
                         any key causes PC-VT to  click.  The  message "KBD
                         LOCKED" is displayed  on  Status  Line  25  of the
                         screen.




                                                                   Page 127






          Appendix B                                            PC-VT v10.0


          ESC [ 4 h      Insert-replacement - Insert mode is  selected. Any
                         characters received cause the characters currently
                         on the screen  from  the  cursor  position  to the
                         right to be  moved  one position to the right. The
                         newly  received character is then inserted in  the
                         vacated space.

          ESC [ 12 h     Send-Receive Mode  -  Sets  host  echo. Characters
                         typed at the keyboard  are  not  locally displayed
                         unless they are sent back by the host.

          ESC [ 20 h     Linefeed /  New Line - Sets PC-VT to transmit both
                         a carriage return and linefeed when the  ENTER key
                         is pressed. Causes received linefeed, formfeed and
                         vertical tab characters to move the cursor  to the
                         left margin of the next line.

          ESC [ ? 1 h    Cursor Key -  Sets  the  cursor  keys  to generate
                         Application  Mode  functions.  For the VT102, this
                         sequence is valid only in Application Keypad mode.
                         For the VT100, it is valid anytime.

          ESC [ ? 5 h    Screen - Sets the screen  to  reverse  video mode.
                         The display attribute is set  to  black  on white.
                         The entire display is flipped to  black  on white.
                         All   characters received after this sequence  are
                         displayed in black on white.

          ESC [ ? 6 h    Origin - Sets the  home  position  to the top left
                         margin of the scrolling region set by the "Set top
                         and bottom margins" sequence "ESC [ Pt ; Pb r" .

          ESC [ ? 7 h    Autowrap - Sets autowrap on. When the  cursor gets
                         to the  right  margin  and  another  character  is
                         received, a carriage  return and linefeed are sent
                         to the display.

          ESC [ ? 8 h    Autorepeat -  Sets  autorepeat  on.  This  is  the
                         normal operation  of the IBM PC keyboard. If a key
                         is held down, it  starts  to  repeatedly  send its
                         code to the running program. This  is  the default
                         setting for PC-VT.

          ESC [ ? 18 h   Print Formfeed  On - PC-VT sends a formfeed to the
                         selected  printer  at the conclusion  of  a  print
                         screen operation. This is the default setting.

          ESC [ ? 19 h   Print Extent -  The  full screen is printed on the
                         selected printer  by  the  print  screen sequence.
                         This is the default setting.

          ESC [ ? 21 h   Receive File - Performs the same  function  as the
                         CTRL-F3 key on  the keyboard. PC-VT private. Error



          Page 128






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         code  is  available  with the "ESC  [  ?  1  0  n"
                         sequence. See Appendix J.

          ESC [ ? 22 h   Transmit File - Performs the same function  as the
                         CTRL-F4 key on  the keyboard. PC-VT private. Error
                         code  is  available  with the "ESC  [  ?  1  0  n"
                         sequence. See Appendix J.

          ESC [ ? 23 h   Special Sequence - This escape sequence causes PC-
                         VT to send a carriage return to the host. This was
                         implemented as a debug feature. PC-VT private. See
                         Appendix J.

          ESC [ ? 24 h   Set Buffer Load -  The  buffer  load  operation is
                         started. PC-VT private. See Appendix J.

          ESC [ ? 25 h   Change  Directory - Performs the same function  as
                         the CTRL-F2 key on  the  keyboard.  PC-VT private.
                         Error code is available  with  the "ESC [ ? 1 0 n"
                         sequence. See Appendix J

          ESC [ ? 26 h   Terminate PC-VT - Performs  the  same  function as
                         the CTRL-F8 key on  the  keyboard.  PC-VT private.
                         See Appendix J.

          ESC [ ? 27 h   Start Up Command.com  - Performs the same function
                         as the ALT-F key on the  keyboard.  PC-VT private.
                         Error code is available  with  the "ESC [ ? 1 0 n"
                         sequence. See Appendix J.

          ESC [ ? 28 h   Select EVE  editor  keypad  support.  Performs the
                         same function  as setting the EVE bit in the SETUP
                         B frame. PC-VT private. See Appendix J.

          ESC [ ? 29 h   Select VMS Operating System support.  Performs the
                         same function  as setting the VMS bit in the SETUP
                         B frame. PC-VT private. See Appendix J.

          ESC [ ? 38 h   Switch to the 4014 emulator. This  sequence  is an
                         extension based on the DEC VT240. The PC must have
                         an IBM Color Graphics Adapter, a Hercules Graphics
                         Card or  an Everex Edge Card or else this sequence
                         is ignored.

          Reset Mode

          ESC [ 2 l      Keyboard  Action - Unlocks the keyboard.  Pressing
                         any key causes the character  to  be  sent  to the
                         host. The "KBD LOCKED" message is cleared from the
                         Status Line.

          ESC [ 4 l      Insert-replacement - Selects replacement mode. Any
                         characters  received  overwrite  any characters on



                                                                   Page 129






          Appendix B                                            PC-VT v10.0


                         the screen at the  cursor  location.  This  is the
                         default setting.

          ESC [ 12 l     Send-Receive  Mode  -  Sets local echo. Characters
                         typed at the keyboard are locally displayed.

          ESC [ 20 l     Linefeed / New Line  -  Resets  PC-VT  to transmit
                         only   a carriage return when  the  ENTER  key  is
                         pressed.  Causes  received  linefeed, formfeed and
                         vertical tab characters to move cursor to the same
                         column of  the  next  line.  This  is  the default
                         setting.

          ESC [ ? 1 l    Cursor Key - Resets the  cursor  keys  to generate
                         ANSI (Cursor Mode)  control sequences. This is the
                         default  setting. For the VT102, this sequence  is
                         valid  only  in  Application  Keypad mode. For the
                         VT100, it is valid anytime.

          ESC [ ? 5 l    Screen - Resets the  screen  to  normal mode.  The
                         display attribute is changed  to  white  on black.
                         The entire display is flipped to  white  on black.
                         All   characters received after this sequence  are
                         displayed in white on black. This  is  the default
                         setting.

          ESC [ ? 6 l    Origin -  Resets the home position to the top left
                         of the screen. This is the default setting.

          ESC [ ? 7 l    Autowrap - Sets autowrap off. When the cursor gets
                         to the  right  margin  and  another  character  is
                         received,  the cursor remains at the right  margin
                         and   characters  overlay  one  another  until   a
                         carriage  return is  received.  This  the  default
                         setting.

          ESC [ ? 8 l    Autorepeat  - Sets autorepeat off. PC-VT can  only
                         simulate this function  since repeat is handled in
                         the keyboard by the 8048. When PC-VT receives this
                         escape sequence, it  clears the keyboard buffer of
                         any characters.

          ESC [ ? 18 l   Print Formfeed Off-  PC-VT performs a print screen
                         operation without a terminating formfeed.

          ESC [ ? 19 l   Print Extent - Only the  scrolling  region  of the
                         screen is printed on the selected  printer  by the
                         print screen sequence.

          ESC [ ? 24 l   Reset Buffer Load - The buffer  load  operation is
                         terminated. PC-VT private. See Appendix J.

          ESC [ ? 25 l   Send a formfeed to the printer. PC-VT private. See
                         Appendix J.


          Page 130






          PC-VT v10.0                                 VT100 & 4014 Emulator


          ESC [ ? 26 l   Start up HELP. Performs the  same  function  as if
                         the user had selected HELP from the  keyboard. PC-
                         VT private. See Appendix J.

          ESC [ ? 27 l   Start  up Command.COM. Performs the same  function
                         as if the user had select the DOS Gateway from the
                         keyboard. DOS is  entered in interactive mode. PC-
                         VT private. See Appendix J.

          ESC [ ? 28 l   Select EDT  editor  keypad  support.  Performs the
                         same function as  resetting  the  EVE  bit  in the
                         SETUP B frame. PC-VT private. See Appendix J.

          ESC [ ? 29 l   Select UNIX Operating System support. Performs the
                         same function as  resetting  the  VMS  bit  in the
                         SETUP B frame. PC-VT private. See Appendix J.

          Loading Macro Keys

                         This is a PC-VT extension which follows the format
                         of  the IBM ANSI.SYS keyboard redefinition.  PC-VT
                         can only redefine ALT-F1 thru ALT-F10.

          ESC [ 0 ; Pk ; "string" p
                         Sets macro key given  by  Pk  to the string inside
                         the double quotes. The double quotes and all other
                         characters shown are required. Pk must be  sent as
                         3  ASCII characters. Error Code is available  with
                         the "ESC [ ? 1 0 n" sequence.

                         Where Pk is:

                         104             ALT-F1
                         105             ALT-F2
                         106             ALT-F3
                         107             ALT-F4
                         108             ALT-F5
                         109             ALT-F6
                         110             ALT-F7
                         111             ALT-F8
                         112             ALT-F9
                         113             ALT-F10














                                                                   Page 131






          Appendix B                                            PC-VT v10.0


























































          Page 132






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Appendix C

                         VT100 Transmitted Escape Sequences


                  Control keys which do not have a defined  ASCII  code are
          translated into escape sequences for  transmission  to  the host.
          These keys are the cursor keys and the keypad keys. Both  sets of
          these keys can transmit  different  sequences.  The codes sent by
          the keypad keys are selected by the "Set Numeric Keypad" and "Set
          Application keypad" commands.  The  codes for the cursor keys are
          selected by the "Set  Cursor"  and  "Reset Cursor" mode commands.
          Note that setting numeric keypad mode resets the cursor mode. Set
          and reset cursor  mode  only function in application keypad mode.
          This VT100 defined numeric keypad mode has nothing to do with the
          PC NUM LOCK key. The NUM LOCK key  functions  locally  in  the PC
          only per the IBM documentation.


          VT100 Cursor Keys

          Key     Reset (Cursor) Mode
                                          Set (Application) mode

          Up      ESC [ A                 ESC O A Down
                  ESC [ B                 ESC O B Right
                  ESC [ C                 ESC O C Left
                  ESC [ D                 ESC O D






















                                                                   Page 133






          Appendix C                                            PC-VT v10.0


          VT100 Emulated Keypad Keys

          IBM PC          Emulated        ANSI Numeric    ANSI    Alternate
          Key VT100 Key Keypad Mode
                                                          Keypad Mode

          F10             0               0               ESC O p F7
                          1               1               ESC O q F8
                          2               2               ESC O r SHIFT-F7
                          3               3               ESC O s F5
                          4               4               ESC O t F6
                          5               5               ESC O u SHIFT-F5
                          6               6               ESC O v F3
                          7               7               ESC O w F4
                          8               8               ESC O x SHIFT-F3
                          9               9               ESC O y SHIFT-F4
                          -(minus)        -(minus)        ESC O m SHIFT-F6
                          ,(comma)        ,(comma)        ESC O l SHIFT-F9
                          .(period)       .(period)       ESC O n SHIFT-F8
                          Enter           Enter           ESC O M F1
                          PF1             ESC O P         ESC O P F2
                          PF2             ESC O Q         ESC O Q SHIFT-F1
                          PF3             ESC O R         ESC O R SHIFT-F2
                          PF4             ESC O S         ESC O S


          VT52 Cursor Keys

          Key     Reset (Cursor) Mode     Set (Application) mode

          Up      ESC A                   ESC A Down
                  ESC B                   ESC B Right
                  ESC C                   ESC C Left
                  ESC D                   ESC D






















          Page 134






          PC-VT v10.0                                 VT100 & 4014 Emulator


          VT52 Emulated Keypad Keys

          IBM PC          Emulated        ANSI Numeric    ANSI    Alternate
          Key VT100 Key Keypad Mode Keypad Mode

          F10             0               0               ESC ? p F7
                          1               1               ESC ? q F8
                          2               2               ESC ? r SHIFT-F7
                          3               3               ESC ? s F5
                          4               4               ESC ? t F6
                          5               5               ESC ? u SHIFT-F5
                          6               6               ESC ? v F3
                          7               7               ESC ? w F4
                          8               8               ESC ? x SHIFT-F3
                          9               9               ESC ? y SHIFT-F4
                          -(minus)        -(minus)        ESC ? m SHIFT-F6
                          ,(comma)        ,(comma)        ESC ? l SHIFT-F9
                          .(period)       .(period)       ESC ? n SHIFT-F8
                          Enter           Enter           ESC ? M F1
                          PF1             ESC P           ESC ? P F2
                          PF2             ESC Q           ESC ? Q SHIFT-F1
                          PF3             ESC R           ESC ? R SHIFT-F2
                          PF4             ESC S           ESC ? S

































                                                                   Page 135






          Appendix C                                            PC-VT v10.0


























































          Page 136






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Appendix D

                         VT100 Responses to Escape Sequences


                  PC-VT  responds to several control characters and  escape
          sequences. They are listed  here.  For  a complete description of
          all escape sequences see Appendix B.

          Elicitor                Response

          Enquire                 Answerback message.

          Device Status Report    PC-VT responds with emulator status.

          Cursor Status Report    Current cursor position is reported.

          Device Attributes       PC-VT identifies itself as either a or
                                  VT100,  a  VT102,  or  a  VT52  depending
          Identify Terminal on the bits set/reset in the SETUP B  or frame.
          What Are You

          Request Terminal        PC-VT responds with information regarding
          Parameters communications parameters


























                                                                   Page 137






          Appendix D                                            PC-VT v10.0


























































          Page 138






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Appendix E

                          VT100 Special ALT Key Definitions


                  PC-VT uses ALT-F to startup  the  DOS  Command Processor,
          ALT-Z to send a hangup command  to  the modem, ALT-H to start the
          HELP  facility,  and  ALT-X  to  clear  a  received XOFF  control
          character. You can tell if an XOFF has been received  because PC-
          VT displays an X on the status line.

                  Additionally,  several  special  ALT  key   commands  are
          available to the user  of  PC-VT. They were implemented to aid in
          the debug of this program. Most of these are  useful  only  under
          very special circumstances but some may be of general use. To use
          these  commands,  hold down the ALT key  and  at  the  same  time
          depress  the key listed. They work  only  in  the  communications
          frame and not in the SETUP, DIALING, or MACRO frames.  Other than
          the above mentioned keys, no  claims or guarantees are make about
          these keys and you use them at your own risk.

          ALT Key plus    Function


          C              Performs  the  same  function  as the CTRL-F8 key.
                         Terminates PC-VT. Mostly for PCjr users.

          E              Toggles Echo. This key toggles  the  state  of the
                         echo  flag.  If  the  host  is  not  echoing  back
                         characters,  you can press ALT-E and PC-VT  echoes
                         the characters to the display.

          F              Fork. This key sequence starts up another  copy of
                         Command.COM without terminating PC-VT or  breaking
                         the host connection.  Once the new  Command.COM is
                         started, you  can run any DOS function or other PC
                         program.  You should be careful that you don't run
                         a  program that uses the same communications  port
                         as PC-VT is using.    The  other program may leave
                         the port in an  unexpected  state.   PC-VT may not
                         then be able to get  control  of  the  port again.
                         Also be careful that  you  don't  alter  any files
                         which PC-VT may be using.  To  exit  from  the new
                         copy  of  Command.COM and return  to  PC-VT,  type
                         "exit" at the command prompt.

          G              Prints  current  line.  The  line  containing  the
                         cursor  is  printed on the  selected  printer,  if


                                                                   Page 139






          Appendix E                                            PC-VT v10.0


                         present. Performs the  same function as receipt of
                         a "ESC [ ? 1 i" sequence.

          H              HELP. Starts up the HELP  frame.  Check  the index
                         for more information on the ALT-H key and HELP.

          K              Starts up the KERMIT file transfer module.

          M              Toggles  "Ignore Nulls"  mode.  NUL(ASCII  0)  and
                         DEL(ASCII 127)  characters  are  not  normally put
                         into the  communications  buffer.  This  switch on
                         causes those characters to be  put  in  the buffer
                         just as all other characters. These characters are
                         eventually ignored  by  PC-VT,  the  difference is
                         that they  now take up I/O buffer space and cannot
                         be used as "filler" or timing characters.

          N              Toggles  "Ignore  ESCAPE"  mode.  Received  escape
                         sequences  are not acted upon. They are  displayed
                         as regular characters on  the  screen.  The escape
                         character itself is displayed as "<ESC>". Toggling
                         this  switch  at  the  wrong  time  may   lead  to
                         unpredictable    results.    Autowrap    is    set
                         automatically when this switch is set.

          O              Performs the same function  as  the  CTRL-F10 key.
                         Calls up the MACRO frame. Mostly for PCjr users.

          P              Sends a formfeed to  the  printer  if a printer is
                         attached.

          R              Restarts PC-VT. Clears COMx port and restarts from
                         the beginning. Selected features and tab stops are
                         not  changed. Host connection is not broken.  This
                         command is useful if you make the  host connection
                         after PC-VT is  started  and COMx port needs to be
                         initialized.   In   most  cases,   though,   PC-VT
                         initializes the port without the need for this.

          S              Initiates  the Scroll Buffer. When you press  this
                         key, PC-VT tries to allocate an additional  32K of
                         memory in which it keeps  the  last  5  screens of
                         information.   The  Scroll  Buffer  can  also   be
                         initiated by a feature selection  in  the  SETUP B
                         frame.

          V              Performs  the  same  function  as the CTRL-F9 key.
                         Calls up the DIALING frame. Mostly for PCjr users.

          X              Resets XOFF Flag. If PC-VT  has  received  an XOFF
                         character,  it does not transmit anything. If  you
                         type a character, PC-VT beeps and ignores  the key
                         you pressed. This is part of the VT100 definition.
                         If something happens and  PC-VT  receives  an XOFF


          Page 140






          PC-VT v10.0                                 VT100 & 4014 Emulator


                         because of garbage on the communications line, you
                         can reset the XOFF flag by pressing ALT-X.

          Z              Hangs  up  the  phone.  PC-VT  performs  the  same
                         functions as if you had entered the  DIALING frame
                         and pressed F5. That is, the Hayes compatible hang
                         up command is sent to the modem.

















































                                                                   Page 141






          Appendix E                                            PC-VT v10.0


                  The following ALT keys work only in Numeric Keypad mode (
          the  default mode).

          ALT Key plus    Function


          A              Turns on Print Only Mode. All characters sent from
                         the host are printed on the selected printer only.
                         Performs the  same function as receipt of a "ESC [
                         5 i" sequence.

          B              Transmits  the  answerback message.  Performs  the
                         same  function  as receipt of  a  Enquire  Control
                         Character (ASCII 5). Performs the same function as
                         the VT HERE IS key

          D              Turns off  Print  Only  Mode.  Performs  the  same
                         function as receipt of a "ESC [ 4 i" sequence.

          W              Reports   Terminal   Status.   Performs  the  same
                         function as receipt of a "ESC [ 5 n" sequence.

          Y              Reports Printer Status. Performs the same function
                         as receipt of a "ESC [ ? 15 n" sequence.

          U              Reports  Device  Attributes.  Performs  the   same
                         function as receipt of a "ESC [ c" sequence.

          H              Clears  Tab  Stop.  Performs  the same function as
                         receipt of a "ESC [  0 g" sequence. You should use
                         the SETUP A frame.

          J              Sets Tab  Stop.  Performs  the  same  function  as
                         receipt of  a "ESC H" sequence. You should use the
                         SETUP A frame.

          L              Clears  All Tab Stops. Performs the same  function
                         as receipt of a "ESC [ 3 g"  sequence.  You should
                         use the SETUP A frame.

















          Page 142






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Appendix F

                         4014 Received Character Processing


                  The next appendices describe  the  internal  operation of
          PC-VT in 4014 mode. They show the various  characters  and escape
          sequences which PC-VT interprets as commands. The character "ESC"
          is an ASCII control character with the decimal value of 27.

                  The  emulator  runs  in  4  basic modes -  Alpha,  Graph,
          Bypass/GIN  and  LCE.   The  control  characters  have  different
          meanings in each of those modes.


          F.1  Alpha Mode


                  Alpha mode is the default mode for the  emulator.  If you
          are using the IBM  Color  Graphics  Adapter, ASCII characters are
          displayed as either 25 lines of 80 characters or 33 lines  of 106
          characters.  If you are using the Everex  Edge  or  the  Hercules
          card,  characters   are  displayed  as  either  43  lines  of  90
          characters or  58 lines of 120 characters. Control characters are
          acted upon per the 4014 definition.

                  Use the following commands to enter Alpha mode:

          ESC FF         To clear the screen  and  move  the cursor to home
                         position.

          CR             To move the cursor to the left margin  in  the row
                         which contains the current graphic beam position.

          US             To enter Alpha mode  with  cursor  at  the current
                         Graphics beam position.

                  ASCII codes from 0  to  31  are control characters. PC-VT
          responds to these characters as listed in the following table.

          Name            Code    Function

            NUL           0       Ignored.
            SOH           1       Ignored.
            STX           2       Ignored.
            ETX           3       Ignored.
            EOT           4       Ignored.
            ENQ           5       Ignored.


                                                                   Page 143






          Appendix F                                            PC-VT v10.0


            ACK           6       Ignored.
            BEL           7       Causes PC-VT to beep the IBM PC speaker.
            BS            8       Causes PC-VT to move the cursor one space
                                  right. If the cursor is already in the
                                  rightmost  column,   this   character  is
          ignored.
                                  Characters backspaced over are NOT erased
                                  from the screen.
            HT            9       Causes PC-VT to move the cursor one space
                                  left. If the cursor is already in the
                                  leftmost column, HT causes an automatic
                                  linefeed and carriage return.
            LF            10      This causes the cursor to move down one
                                  line in the current column. If the
                                  cursor moves below the screen output
                                  area, the lines above the cursor move up
                                  one line, and a blank line is added to
                                  the bottom of the screen. The operation
                                  of this key is modified by the LF Effect
                                  feature selected in SETUP B.
            VT            11      This causes the cursor to move up one
                                  line in the current column. If the cursor
                                  is in the top line, VT wraps to the
                                  bottom line.
            FF            12      Ignored.
            CR            13      The cursor is moved back to the left
                                  margin. Cursor remains in the current
                                  line.
            SO            14      Ignored.
            SI            15      Ignored.
            DLE           16      Ignored.
            XON           16      Restart transmission, if stopped.
            DC2           18      Ignored.
            XOFF          19      Stop transmission until XON is Received.
            DC4           20      Ignored.
            NAK           21      Ignored.
            SYN           22      Ignored.
            ETB           23      Ignored.
            CAN           24      Ignored.
            EM            25      Ignored.
            SUB           26      Ignored.
            ESC           27      Sets LCE mode.
            FS            28      Sets Point Plot mode.
            GS            29      Sets Graph mode to do a dark (invisible)
                                  vector.
            RS            30      Sets Incremental Plot mode.
            US            31      Ignored.


                  ASCII  codes  from  32("  ")  to  126("~")  are taken  as
          displayable characters.

                  ASCII code 127(DEL) is ignored.



          Page 144






          PC-VT v10.0                                 VT100 & 4014 Emulator


                  To move the cursor to any desired position:

            1.  enter Graph mode with the GS command,

            2.  specify the graphics coordinates, and then

            3.  return to Alpha mode using the US command.

          For example,  to display the word PC-VT at coordinates (680,585),
          send:

          <GS>2i5H<US>PC-VT


          F.2  Graph Mode


                  Graph  mode  is  used to draw  vectors.  A  vector  is  a
          sequence  of  dots  on the screen. You enter Graph mode with a GS
          control character from Alpha mode. The first  coordinate received
          in  Graph  mode  does not cause any output to the screen. This is
          called a dark vector. It is  used  to MOVE to the beginning point
          of the  first vector to be drawn. Subsequent coordinates received
          DRAW a vector from the previous coordinate to the new coordinate.
          Vector drawing modes are set from LCE mode.

                  Use the following command to enter Graph mode:

          GS             Enter Graph mode with  the  beam  position  at the
                         lower  left  corner of the  current  Alpha  cursor
                         position.

                  Characters received are interpreted as coordinates. Up to
          5  characters  are  needed  to  form  a  single  coordinate.  The
          characters received must be in the following format and sequence:


                                  7 bit Character
          Byte    -------------------------------------------------
          Name    6       5       4       3       2       1       0
          ----    -------------------------------------------------
          HIY     0       1       ----- 5 MSB of Y Coordinate -----

          Extra   1       1       X       Y2      Y1      X2      X1

          LOY     1       1       ----- 5 LSB of Y Coordinate -----

          HIX     0       1       ----- 5 MSB of X Coordinate -----

          LOX     1       0       ----- 5 LSB of X Coordinate -----

            X = not used.




                                                                   Page 145






          Appendix F                                            PC-VT v10.0


                  The  extra byte is only used when  forming  12  bit  4014
          coordinates. In that case, the Y2  and  Y1 bits become the LSB of
          the  Y  coordinate  and  X2  and  X1  become the  LSB  of  the  X
          coordinate.

                  Note: MSB means Most Significant or Leftmost bits and LSB
          means Least Significant or Rightmost bits.


                  All  five  bytes do not need to  be  sent  for  each  new
          coordinate. PC-VT  remembers certain bytes. If those bytes do not
          change, they  do not have to be transmitted. Coordinate addresses
          may be shortened as follows:


          Bytes which             Bytes which must be sent
             change       HIY     Extra   LOY     HIX     LOX

             Hi Y         #                               #
             Extra                #       #               #
             Lo Y                         #               #
             Hi X                         #       #       #
             Lo X                                         #

                  The LOX byte must always be transmitted. As soon as PC-VT
          receives the LOX byte, it plots the point.

                  Here is an example of a typical move and draw sequence:



          ASCII           Binary                  Command
            GS (1Dh)      X  0  0  1  1  1  0  1  enter Graph mode

          First set of coordinates : move to (0,0)
            Space (20h)   X  0  1  0  0  0  0  0  HIY = 00000
            `  (60h)      X  1  1  0  0  0  0  0  LOY = 00000
            Space (20h)   X  0  1  0  0  0  0  0  HIX = 00000
            @  (40h)      X  1  0  0  0  0  0  0  LOX = 00000

          Second set of coordinates : draw to (512,512)
            0  (30h)      X  0  1  1  0  0  0  0  HIY = 10000
            `  (60h)      X  1  1  0  0  0  0  0  LOY = 00000
            0  (30h)      X  0  1  1  0  0  0  0  HIX = 10000
            @  (40h)      X  1  0  0  0  0  0  0  LOX = 00000

            US (1Fh)      X  0  0  1  1  1  1  1  enter Alpha mode

            X = parity bit - don't care)

                  ASCII codes from 0  to  31  are control characters. PC-VT
          responds to these characters as listed in the following table.

          Name            Code    Function


          Page 146






          PC-VT v10.0                                 VT100 & 4014 Emulator


            NUL           0       Ignored.
            SOH           1       Ignored.
            STX           2       Ignored.
            ETX           3       Ignored.
            EOT           4       Ignored.
            ENQ           5       Ignored.
            ACK           6       Ignored.
            BEL           7       Causes PC-VT to beep the IBM PC speaker.
            BS            8       Ignored.
            HT            9       Ignored.
            LF            10      Ignored.
            VT            11      Ignored.
            FF            12      Ignored.
            CR            13      Set Alpha mode.The cursor is moved
                                  back to the left margin.
            SO            14      Ignored.
            SI            15      Ignored.
            DLE           16      Ignored.
            XON           16      Restart transmission, if stopped.
            DC2           18      Ignored.
            XOFF          19      Stop transmission until XON is received.
            DC4           20      Ignored.
            NAK           21      Ignored.
            SYN           22      Ignored.
            ETB           23      Ignored.
            CAN           24      Ignored.
            EM            25      Ignored.
            SUB           26      Ignored.
            ESC           27      Sets LCE mode.
            FS            28      Sets Point Plot mode.
            GS            29      Do a dark (invisible) vector.
            RS            30      Sets Incremental Plot mode.
            US            31      Set Alpha mode.


                  ASCII codes 32(" ") thru 63("?") are taken as either HIGH
          X or HIGH Y graph coordinates.

                  ASCII codes 64("@") thru 95("_") are taken as LOW X graph
          coordinates.

                  ASCII codes  96("`") thru 126("~") are taken as LOY graph
          coordinates.

                  ASCII  code  127(DEL)  is  taken  as either a  LOY  graph
          coordinate or is ignored depending  on the setting the LOY option
          in the SETUP B frame.









                                                                   Page 147






          Appendix F                                            PC-VT v10.0


                                   Point Plot Mode


                  Point  plot   mode  is  a  submode  of  Graph  mode.  All
          characters are interpreted  exactly  the same as Graph mode. This
          only difference, is that instead  of drawing a vector, PC-VT only
          displays the end points.

                  Use the following command to enter Point Plot mode:

           FS            Enter Point Plot mode with  the  beam  position at
                         the lower left corner of the current  Alpha cursor
                         position.




                                Incremental Plot Mode


                  Incremental plot mode is a  submode  of  Graph  mode. The
          control characters 0 to 31 are handled as in Graph mode.  In this
          mode, the  drawing  beam  can  be  directly  controlled. Received
          characters shown below cause  the  beam  to  move in one Tekpoint
          increments. Since each dot on the PC's screen  may  cover several
          Tekpoints, it may take several movement commands to actually show
          a movement on the screen.

                  Use the following command to enter Incremental Plot mode:

          RS             Enter Incremental Plot mode with the beam position
                         at the lower  left  corner  of  the  current Alpha
                         cursor position.

                  Other characters are interpreted as follows:



          Character               Function
          space           Turns beam off
          A               Move beam one Tekpoint east
          B               Move beam one Tekpoint west
          D               Move beam one Tekpoint north
          E               Move beam one Tekpoint northeast
          F               Move beam one Tekpoint northwest
          H               Move beam one Tekpoint south
          I               Move beam one Tekpoint southeast
          J               Move beam one Tekpoint southwest
          P               Turns beam on







          Page 148






          PC-VT v10.0                                 VT100 & 4014 Emulator


                               Special Point Plot Mode


                  Special Point Plot mode functions  just  like  Point Plot
          mode except that the first character in the  point  coordinate is
          an intensity level. PC-VT supports only 0 and 100% intensity. The
          "@"  character indicates zero intensity (or  beam  off)  and  all
          other valid 4014 intensity codes produce 100% intensity.

                  Use the following command  to  enter  Special  Point Plot
          mode:

          ESC FS         Enter  Special  Point  Plot  mode  with  the  beam
                         position at the lower left corner  of  the current
                         Alpha cursor position.

                  The beam intensity set by this command  remains unchanged
          if you switch to Point Plot or Incremental Point Plot modes or if
          you switch back into Special Point Plot mode.




                                 Exiting Graph mode


                  There are several ways to exit Graph mode and enter Alpha
          mode. The character which you use determines the action taken:

          ESC FF         Erases the screen and moves the cursor to the home
                         position.

          CR             Moves the cursor to the left margin in the current
                         line.

          US             Leaves the cursor at its current position.

          ESC SUB        Switches to GIN mode  and  displays  the crosshair
                         cursor.

          FS             Switches to Point Plot mode.


          F.3  Bypass/GIN Mode


                  Use the following command to enter Bypass/GIN mode:

          ESC SUB        Enter Bypass/GIN mode with the crosshair displayed
                         at the last graph coordinate.

                  In  Bypass/GIN  mode,  the  host has requested coordinate
          information from PC-VT. PC-VT displays a  crosshair  pointer. You
          can  move  the  pointer  with  the  keypad  arrow keys.  You  can


                                                                   Page 149






          Appendix F                                            PC-VT v10.0


          terminate  GIN mode by pressing any ASCII key  or  the  host  can
          terminate it by sending ESC  ENQ. In both cases, PC-VT  sends the
          current  pointer  position  to  the  host.  The  format  of  this
          transmission is described in Appendix G.

                  ASCII codes from 0  to  31  are control characters. PC-VT
          responds to these characters as listed in the following table.

          Name    Code    Function

            NUL           0       Ignored.
            SOH           1       Ignored.
            STX           2       Ignored.
            ETX           3       Ignored.
            EOT           4       Ignored.
            ENQ           5       Ignored.
            ACK           6       Ignored.
            BEL           7       Causes PC-VT to beep the IBM PC speaker.
            BS            8       Ignored.
            HT            9       Ignored.
            LF            10      Causes the cursor to move down one
                                  line in the current column. If the
                                  cursor moves below the screen output
                                  area, the lines above the cursor move up
                                  one line, and a blank line is added to
                                  the bottom of the screen. The operation
                                  of this key is modified by the LF Effect
                                  feature selected in SETUP B.
            VT            11      Ignored.
            FF            12      Ignored.
            CR            13      Sets Alpha mode and moves the cursor
                                  back to the left margin.
            SO            14      Ignored.
            SI            15      Ignored.
            DLE           16      Ignored.
            XON           16      Restarts transmission, if stopped.
            DC2           18      Ignored.
            XOFF          19      Stops transmission until XON is received.
            DC4           20      Ignored.
            NAK           21      Ignored.
            SYN           22      Ignored.
            ETB           23      Ignored.
            CAN           24      Ignored.
            EM            25      Ignored.
            SUB           26      Ignored.
            ESC           27      Sets LCE mode.
            FS            28      Sets Point Plot mode.
            GS            29      Sets Graph mode and does a dark
                                  (invisible) vector.
            RS            30      Sets Incremental Plot mode.
            US            31      Set Alpha mode.


                  ASCII codes 32(" ") thru 127(DEL) are ignored.


          Page 150






          PC-VT v10.0                                 VT100 & 4014 Emulator


          F.4  LCE Mode


                  LCE  mode  arms  PC-VT  to  receive  a   special  control
          character. This is similar to,  bu simpler than, the VT100 escape
          sequences.

                  ASCII codes from 0  to  31  are control characters. PC-VT
          responds to these characters as listed in the following table.

          Name            Code    Function

            NUL           0       Remain in LCE mode.
            SOH           1       Ignored.
            STX           2       Ignored.
            ETX           3       Ignored.
            EOT           4       Ignored.
            ENQ           5       Returns terminal status.
            ACK           6       Ignored.
            BEL           7       Causes PC-VT to beep the IBM PC speaker.
            BS            8       Causes PC-VT to move the cursor one space
                                  right. If the cursor is already in the
                                  rightmost  column,   this   character  is
          ignored.
            HT            9       Causes PC-VT to move the cursor one space
                                  left. If the cursor is already in the
                                  leftmost column, HT causes an automatic
                                  linefeed and carriage return.
            LF            10      Remains  in  LCE mode. Causes  LF  to  be
          ignored
                                  until an invalid control character or
                                  BEL is received.
            VT            11      Causes the cursor to move up one
                                  line in the current column. If the cursor
                                  is in the top line, VT wraps to the
                                  bottom line.
            FF            12      Erases Screen and Homes cursor. (PAGE)
            CR            13      Remains  in  LCE mode. Causes  CR  to  be
          ignored
                                  until an invalid control character or
                                  BEL is received.
            SO            14      Ignored.
            SI            15      Ignored.
            DLE           16      Ignored.
            DC1           17      Ignored.
            DC2           18      Rings bell and waits for the user to
                                  press any ASCII key.
            DC3           19      Ignored.
            DC4           20      Returns to VT100 emulator mode.
            NAK           21      Ignored.
            SYN           22      Ignored.
            ETB           23      Makes a hardcopy of the screen on
                                  the attached printer.
            CAN           24      Sets Bypass mode.


                                                                   Page 151






          Appendix F                                            PC-VT v10.0


            EM            25      Ignored.
            SUB           26      Sets Bypass/GIN mode.
            ESC           27      Remains in LCE mode.
            FS            28      Sets Special Point Plot mode.
            GS            29      Sets Graph mode to do a dark
                                  (invisible) vector.
            RS            30      Sets Incremental Plot mode.
            US            31      Sets Alpha mode.


                  ASCII codes 32(" ") thru 55("7") are ignored.

                  ASCII codes 56("8")  thru 59(";") select character sizes.
          PC-VT  supports  two  character sizes when using the IBM CGA (the
          standard 25  line  by  80  column set and a 33 line by 106 column
          set) and two  character  sizes  when  using  the  Everex  Edge or
          Hercules card (these are 43 lines  by  90 columns and 58 lines by
          120 columns generated by PC-VT  software).  The  selection  is as
          follows:


          Set     ASCII code      IBM CGA         Everex or Hercules #1
                  56("8")         25 by 80        43 by 90  (default) #2
                  57("9")         25 by 80        43 by 90 #3
                  58(":")         33 by 106       58 by 120 Capital Letters
          #4 59(";") 33 by 106 58 by 120 Capital Letters

                  ASCII codes 60("<") thru 62(">") are ignored.

                  ASCII  code  63("?")  is interpreted as a LOY code if the
          LOY option is reset in the SETUP B frame.

                  ASCII codes 64("@") thru 95("_") are ignored.

                  ASCII codes  96("`")  thru  119("w")  set  drawing  modes
          depending on their bit patterns as follows:




















          Page 152






          PC-VT v10.0                                 VT100 & 4014 Emulator


          bit 7 is always off
                  0
          bits 6 and 5 are always on
                  11
          bits 4 and 3 specify beam mode:
                  00 Focused
                  01 Defocused (not supported)
                  10 Write-Thru
                  11 not used
          bits 2, 1, and 0 specify the beam form:
                  000 Solid
                  001 Dotted
                  010 Dot-Dashed
                  011 Short-Dashed
                  100 Long-Dash
                  101 Solid
                  110 Solid
                  111 Solid

                  Defocused drawing mode is not supported  and  if received
          results  in  normal  vectors.  Write-Thru  mode  is  simulated by
          writing  to  the  screen in Exclusive-OR mode. That is, each time
          that  a  Write-Thru  vector  is  received,  the  vector drawn  is
          alternately drawn and then erased. This appears to the user  as a
          blinking vector. As long as an even number of  draws  occur,  the
          vector is erased at the  end.  You  can  also  use  this  for any
          general type of drawing where exclusive-or is required.

                  Note : exclusive-or means  that  the  point which you are
          drawing is drawn only  if  it is different from the current value
          (ON or OFF) of the point on the screen.

                  Some typical sequences to select drawing modes are:


          ESC `           Focused Solid
          ESC a           Focused Dotted
          ESC b           Focused Dot-Dashed
          ESC c           Focused Short-Dashed
          ESC d           Focused Long-Dashed

          ESC p           Write-thru Solid
          ESC q           Write-thru Dotted
          ESC r           Write-thru Dot-Dashed
          ESC s           Write-thru Short-Dashed
          ESC t           Write-thru Long-Dashed

                  ASCII codes 120("x") thru 126("~") are ignored.

                  ASCII code  127(DEL) causes the emulator to remain in LCE
          mode.





                                                                   Page 153






          Appendix F                                            PC-VT v10.0


























































          Page 154






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Appendix G

                           4014 Received Escape Sequences




                  PC-VT constantly  monitors  the  communications  line for
          these incoming escape sequences. When  they  are  received, PC-VT
          performs  the function as shown. The  escape  character  and  the
          characters which follow it  and  are part of the sequence are not
          displayed.  When  receiving (downloading) an  ASCII  file,  PC-VT
          copies  these  characters  to the PC disk file being created. The
          escape  character  is  shown below as  "ESC"  and  is  the  ASCII
          character with the value of 27.

          ESC SO         Not supported.

          ESC SI         Not supported.

          ESC ENQ        Report   Terminal  Status.  See  Appendix  H   for
                         definition of the response.

          ESC ETB        Hardcopy.  The  screen  is  copied to the attached
                         printer. LPT1 or LPT2 can be selected in the SETUP
                         B frame.  The  IBM  supplied  program GRAPHICS.COM
                         must have been run  before  you  start up PC-VT in
                         order for the Hardcopy command to work.

          ESC CAN        Sets  Bypass condition. PC-VT does not respond  to
                         any data echoed back from the host.

          ESC FF         Selects  Alpha mode, erases the screen, homes  the
                         cursor and clears Bypass condition.

          ESC SUB        Sets  GIN mode. A crosshair pointer is  displayed.
                         You can position it  and  cause  PC-VT to send the
                         coordinates  of  that position to  the  host.  The
                         Appendix  H  shows  the  format of the coordinates
                         sent to the host.

          ESC FS         Sets Point Plot mode.

          ESC CR         Disables response to  carriage return until BEL or
                         an invalid control code is received.

          ESC LF         Disables  response  to linefeed until  BEL  or  an
                         invalid control code is received.


                                                                   Page 155






          Appendix G                                            PC-VT v10.0


          ESC DEL, ESC NUL, ESC CR, ESC LF, ESC ESC
                         These five sequences set  LCE  mode.  In addition,
                         ESC  CR  and  ESC  LF  affect  PC-VT  response  to
                         carriage return and linefeed.

          ESC ?          4014  terminals  have  a  "DEL implies LOY" option
                         which is  supported  in  SETUP  B  in  PC-VT. This
                         option allows the DEL control  character  to  be a
                         LOY value in coordinate specifications. Since this
                         usage  may  conflict  with some operating system's
                         usage  of  DEL,  4014  mode  accepts  this  escape
                         sequence as a substitute  for  the  LOY coordinate
                         value of DEL.

          ESC BEL, ESC BS, ESC HT, ESC VT, ESC GS, ESC RS, ESC US
                         These  sequences perform the same function as  the
                         second character without the escape character.

          ESC DC2        This  special escape sequence was added in  PC-VT.
                         Upon receipt, PC-VT sounds the PC's bell  and then
                         waits for the user  to  press  any ASCII key. This
                         pause can also be  done  using  the  standard 4014
                         commands by going back into Alpha mode and reading
                         the keyboard. This method  is  useful  if  you are
                         drawing a sequence of  graphs  which  the  user is
                         capturing for  later  review.  When  the  user  is
                         viewing  graphs  using  the  =v option of Transmit
                         File, this  sequence is the only way to have PC-VT
                         automatically pause between graphs.

          ESC DC4        This  special escape sequence was added in  PC-VT.
                         Upon  receipt,  PC-VT  switches  back  into  VT100
                         emulator mode.























          Page 156






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Appendix H

                         4014 Responses to Escape Sequences


                  PC-VT  responds to several control characters and  escape
          sequences. All sequences which return graphics coordinates always
          return 10 bit  coordinates  in  the  range of 0 to 1023 Tekpoints
          even if the host has been sending 12 bit coordinates.


          Elicitor                Response

          ESC ENQ

          Creates one of these GIN mode situations:

          GIN Mode 1 - Alpha Cursor / Graph Beam Position Report

          1. Causes terminal status and coordinates of lower left corner of
          the Alpha cursor to be sent to the computer if received while the
          terminal is in Alpha mode. Emulator remains in Alpha mode.


          Byte 1  X  0  1  0  0  0  0  1  Terminal status byte
          Byte 2  X  0  1  x9 x8 x7 x6 x5 HIX
          Byte 3  X  0  1  x4 x3 x2 x1 x0 LOX
          Byte 4  X  0  1  y9 y8 y7 y6 y5 HIY
          Byte 5  X  0  1  y4 y3 y2 y1 y0 LOY
          Byte 6  X  0  0  0  1  1  0  1  CR  (if selected by option)

          2. Causes terminal status and  coordinates of the display beam to
          be sent to  the  host  if  received while in Graph mode. Emulator
          remains in Graph mode.


          Byte 1  X  0  1  0  1  0  0  1  Terminal status byte
          Byte 2  X  0  1  x9 x8 x7 x6 x5 HIX
          Byte 3  X  0  1  x4 x3 x2 x1 x0 LOX
          Byte 4  X  0  1  y9 y8 y7 y6 y5 HIY
          Byte 5  X  0  1  y4 y3 y2 y1 y0 LOY
          Byte 6  X  0  0  0  1  1  0  1  CR  (if selected by option)

          PC-VT follows the cursor or beam position with the GIN terminator
          selected the SETUP B frame then return to Graph mode. Polling the
          terminal with ESC  ENQ  immediately following a hard copy request
          results in a terminal response after copying is completed.



                                                                   Page 157






          Appendix H                                            PC-VT v10.0


                  Where the terminal status byte is:


          Bit     Default         Meaning
                  Alpha Graph
           7      0     0         none but must be 0
           6      0     0         none but must be 0
           5      1     1         none but must be 1
           4      0     0         0 indicates hardcopy unit is available
           3      0     1         0=Alpha mode, 1=Graph mode is in effect
           2      0     0         0 indicates Graph mode exists
           1      0     0         0 indicates Margin 1 is in effect
           0      1     1         0 indicates an auxiliary unit is
                                    connected

          GIN Mode 2 - Immediate position report of crosshair pointer

          Requires an ESC SUB  first  to  display  the crosshair pointer in
          Graph  mode then a ESC ENQ. Sends the  current  position  of  the
          crosshair  pointer.  In  this case, return to  Alpha  mode  after
          transmission.


          Send:
          Byte 1  X  0  1  x9 x8 x7 x6 x5 HIX
          Byte 2  X  0  1  x4 x3 x2 x1 x0 LOX
          Byte 3  X  0  1  y9 y8 y7 y6 y5 HIY
          Byte 4  X  0  1  y4 y3 y2 y1 y0 LOY
          Byte 5  X  0  0  0  1  1  0  1  CR  (if selected by option)

          Elicitor                Response ESC SUB

          GIN Mode 3 - Interactive pointer position reporting

          ESC SUB displays the crosshair pointer in Graph mode. Hitting any
          keypad  arrow  key  causes the pointer to move. Hitting any ASCII
          key causes the program to send the following :

            1.  the ASCII code of the key pressed,

            2.  the current position of the crosshair pointer, and

            3.  GIN terminator as selected in the SETUP B frame.

          In this case, PC-VT returns to Alpha mode after transmission.


          Send:
          Byte 1  X  X  X  X  X  X  X  X  Key Pressed
          Byte 2  X  0  1  x9 x8 x7 x6 x5 HI X
          Byte 3  X  0  1  x4 x3 x2 x1 x0 LO X
          Byte 4  X  0  1  y9 y8 y7 y6 y5 HI Y
          Byte 5  X  0  1  y4 y3 y2 y1 y0 LO Y
          Byte 6  X  0  0  0  1  1  0  1  CR  (if selected by option)


          Page 158






          PC-VT v10.0                                 VT100 & 4014 Emulator


























































                                                                   Page 159






          Appendix I                                            PC-VT v10.0


          This mode  is  also  ended  by receipt of a CR, ESC FF,or ESC ENQ
          from the host or if the user presses  the  keyboard  PAGE  key or
          RESET key.






                                     Appendix I

                  4014 Special Shift, ALT and CTRL Key Definitions


                  In  4014 mode, PC-VT uses ALT-F  to  startup  the  PC-DOS
          command processor, ALT-Z to send a hangup command  to  the modem,
          and ALT-H to start the HELP facility.

                  Additionally,  several  special  Shift,  ALT and CTRL key
          commands  are  available   to   the  user  of  PC-VT.  They  were
          implemented to aid in the debug of this program.  Most  of  these
          are useful only under very  special circumstances but some may be
          of general use. To  use  these commands, hold down the Shift, ALT
          or CTRL key and at the same time  depress  the  key  listed. They
          work only in the 4014  communications frame. Other than the above
          mentioned keys, no claims or guarantees are made about these keys
          and you use them at your own risk.

          ALT Key plus    Function

          E              Sets local echo on.

          Y              Sets Point Plot mode.

          U              Sets LCE mode.

          I              Sets Special Point Plot mode.

          O              Sets Graph mode.

          P              Sends   a  formfeed  character  to  the   attached
                         printer.

          F              Starts up a second copy of COMMAND.COM.

          G              Sets Bypass/GIN mode.

          H              Starts up the HELP facility.

          J              Terminates Graph mode and goes to Alpha mode.

          K              Starts up the KERMIT file transfer program.

          L              Sends cursor position report.


          Page 160






          PC-VT v10.0                                 VT100 & 4014 Emulator


          Z              Hangs up the phone with a Hayes  compatible hangup
                         sequence.

          V              Returns  to  VT100  emulator  mode. Same effect as
                         pressing the F1 key.

          B              Sets Incremental Plot mode.

          N              Sets Alpha mode.

          M              Terminates Graph mode and sets Alpha mode.


          CTRL Key plus   Function

          @              Sends an ASCII 0 (NUL) character to the host.

          Shift Key plus  Function

          F1             Sets drawing mode to solid.

          F2             Sets drawing mode to dotted.

          F3             Sets drawing mode to dot-dashed.

          F4             Sets drawing mode to short-dash.

          F5             Sets drawing mode to long-dash.

          F6             Sets #1 character set.

          F7             Sets #2 character set.

          F8             Sets #3 character set.

          F9             Sets #4 character set.




















                                                                   Page 161






          Appendix I                                            PC-VT v10.0


























































          Page 162






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Appendix J

                               PC-VT Technical Details


                  This  appendix  describes  some  of  the  details  of the
          implementation of PC-VT for the user who wishes  to  interface to
          the program in some non-standard way.

                  PC-VT has been tested on DOS 2.0, 2.1, 3.0,  and  3.1  on
          the IBM PC, the IBM PCXT,  the  IBM  PCAT and the IBM PCjr. PC-VT
          has not been tested on any  compatible  nor has it been tested on
          any system with DOS "patches"  or auxiliary programs. It does not
          operate with DOS 1.0 or 1.1.


          J.1  Details




                               BIOS and DOS Calls Used


                  In general, PC-VT uses  BIOS  calls  instead of DOS calls
          where ever possible. BIOS calls used by PC-VT:

          10H     to handle the display of characters and control
                  sequences while communicating with the host.
          11H     to determine the type of monitor on the system
                  and to determine if a line printer is present.
          14H     to initialize the COM port.
          16H     to do keyboard input and to look at the
                  CAPS LOCK, NUM LOCK, and SCROLL LOCK key
                  status.
          17H     to get the printer status and to print
                  characters.
          1AH     to read the binary time of day clock.












                                                                   Page 163






          Appendix J                                            PC-VT v10.0


                  DOS calls used by PC-VT:

          21H     the general DOS utility call with AH equal to
                  09H     to display error messages on the screen.
                  19H     to get the current default drive.
                  1AH     to set Disk Transfer Addresses.
                  25H     to set the interrupt vectors for the
                          COM port, the critical error handler
                          and the CTRL-BREAK key.
                  2CH     to get the time of day.
                  2EH     to set VERIFY on.
                  30H     to determine the DOS version number.
                  33H     to set/clear BREAK checking.
                  3CH     to create a file with a path name.
                  3DH     to open a file with a path name.
                  3EH     to close a file with a path name.
                  3FH     to read from a file with a path name.
                  40H     to write to a file with a path name.
                  41H     to delete a file with a path name.
                  47H     to get the current default directory.
                  48H     to allocate memory for HELP and screen
                          saving.
                  4BH     to start up COMMAND.COM and KERMIT.COM.
                  4EH     to check for the presence of a file
                          with a path name.
                  54H     to determine the state of the VERIFY
                          switch.
          23H     to terminate the program and restore the
                  CTRL-BREAK address in DOS. This is the "normal"
                  way to terminate PC-VT.

                  An error in either DOS or the BIOS code causes  a problem
          with the cursor. When PC-VT starts, it cannot ascertain the shape
          of  the  cursor  due to this error. Although PC-VT is able to use
          either the underline or block cursor, it may not be able to reset
          the  cursor  to  the original size  upon  exit.  This  will  work
          correctly when IBM corrects the problem.

                  PC-VT does not "look"  into  DOS  directly for any reason
          with the exception of finding the COM1 and COM2 port address. PC-
          VT should be compatible with all future releases of DOS.




                                   COM Port Usage


                  In  order  to  get  the  highest speed out of the  RS-232
          ports, PC-VT  does direct input/output to those ports. PC-VT uses
          I/O  addresses  starting  at 3F8H for COM 1 and at 2F8H for COM2.
          PC-VT gets these addresses  from  DOS by looking at the two words
          starting at address 400 (segmented address 40:0) for the starting
          port addresses for  COM1  and COM2 respectively.Note that the IBM


          Page 164






          PC-VT v10.0                                 VT100 & 4014 Emulator


          PCjr does  not  assign  COM  ports like the PC. PC-VT has to do a
          little special work but it keeps them straight  (jr  switches the
          addresses if the internal modem is installed).

                  PC-VT sends a BREAK to the  host  by setting bit 6 of the
          RS-232 Port's Line Control Register for at least one-half second.
          The bit is then cleared.

                  PC-VT  handles  ASCII  characters  for codes greater than
          127.This works only when  the  COM port is initialized for 8 bits
          of data transfer. If  a  code greater than 127 is received, PC-VT
          can display the character  defined  in  the IBM documentation. In
          this  way,  PC-VT  is compatible with RBBS  systems  using  these
          extended  characters  while  maintaining  compatibility  with  VT
          terminals. The "256 char" bit must be set in the SETUP  frame for
          these extended characters to be displayed. Some hosts don't strip
          this  8th  bit  even when communicating with  plain  ASCII.  This
          causes  some  unusual  behavior.  Be  careful when you  use  this
          feature.

                  PC-VT also  does  direct  I/O  to  the  8259 Programmable
          Interrupt Controller  (PIC). It uses port address 21H for reading
          the interrupt source and address 20H for clearing that interrupt.




                                     Modem Usage


                  If you use an external modem or a  direct  connect, PC-VT
          does not require that all 25 lines of the DB-25 connector  on the
          COM port be connected.

                  Actually, only pin  2  (transmit  data),  pin  3 (receive
          data),  and  pin  7 (signal ground) need be connected. PC-VT does
          not  use  Clear  to Send (CTS), Data Set Ready (DSR) or any other
          modem status line.  This  is  the  FDX A mode of VT100 operation.
          Since  some  modems  require a basic handshake with the COM port,
          PC-VT sends Data Terminal Ready (DTR) and Ready to Send (RTS) out
          of the COM port. These 2 lines are not cleared when you terminate
          PC-VT,  permitting the connection to be maintained  while  you go
          back to DOS by terminating PC-VT. A better way to get into DOS is
          to  use  the  ALT-F  key  - this method keeps the  communications
          buffer actively monitoring  the  line.  Be  careful  because this
          means  that the phone does not hang  up  automatically  when  you
          terminate PC-VT. If you have a Hayes compatible modem, you should
          use  the  F5 function of the DIALING  frame  or  ALT-Z  from  the
          communications  frame  to  be sure. If your modem is manual, then
          you must physically hang up the phone.

                  Some installations require that the terminal drop  DTR as
          a  break  signal  to the host. PC-VT toggles the state of the DTR
          line when  you  press  F2.  It is initially set to a 1. The first


                                                                   Page 165






          Appendix J                                            PC-VT v10.0


          press of F2 clears it to a 0 and the next press sets it back to a
          1.

                  Receive parity checking, if set, checks not  only receive
          parity but also data overrun and framing errors. PC-VT puts a '!'
          in  the  buffer  when  a  character with bad parity is  received.
          Parity checking is normally off and can be enabled in the SETUP B
          frame.




                                Communications Buffer


                  The communications buffer in PC-VT is 2048  bytes long.To
          prevent buffer overflow, the  XON/XOFF  support  sends  XOFF when
          1536 characters are in the buffer (the 75% point of  the buffer).
          Then, XON  is  sent  when  the  buffer  backlog is reduced to 204
          characters (the 10% point of the buffer). If the host ignores the
          XOFF character transmitted, PC-VT  displays  a  '#'character when
          the buffer overflows. All characters received while the buffer is
          in the overflow condition are discarded.

                  The  buffer  size  can  be  reduced  to  256 bytes  by  a
          selection in the SETUP B frame. See the index for  "Buffer Size".
          The smaller buffer gives  you  faster  response to CTRL-C, CTRL-O
          and CTRL-Y but some programs which do not handle XON/XOFF may not
          work as well.




                                       VMS 4.0


                  Some users of PC-VT have  reported  problems  with XMODEM
          under VMS version 4.0. Due to some change  made  by  DEC  in that
          release,  an  additional  parameter must be set using the VMS SET
          TERM  command.  For  each TT line that to be used with PC-VT, you
          must permanently set the Alternate Type Ahead Buffer.

                  The VMS command to do this is:

          SET TERM /PERM/ALTYPEAHD

                  This specification takes effect at your next log in. This
          command may have to be  performed by your VMS system programmers.
          Contact your DEC representative for more information.







          Page 166






          PC-VT v10.0                                 VT100 & 4014 Emulator


                            "Snow" or Fast Screen Update


                  PC-VT  can  use  a "snow" screen update  with  the  color
          graphics  adapter.  Normally,  when you do a screen output to the
          color graphics adapter, the BIOS  waits  for  the  raster retrace
          before writing into  the  video memory. This would severely limit
          the baud rate to about 4800 baud. If you select the "snow" update
          option on the SETUP  B  frame,  PC-VT  writes directly into video
          memory  without  waiting  for  the  retrace  time.   This  causes
          conflicts between  the hardware reading the video memory in order
          to  display its contents and the writing of  new  data  into  the
          memory. The conflict appears  as  small  white  dots all over the
          screen. This is "snow". With  this feature on, PC-VT handles 9600
          baud. This is not an issue with the IBM  Monochrome  adapter  and
          Display as that video  memory  is dual-ported and can be read and
          written at the same time. PC-VT handles 9600 baud  with  the  IBM
          Monochrome adapter.

                  If you don't like the snow update feature but would still
          like  PC-VT to use direct memory access  (DMA)  when  saving  and
          restoring frames and when switching  to  reverse  video,  you can
          select the DMA option  in  the SETUP B frame. With this selected,
          normal output to the screen be snow-free. This  was  a compromise
          between full snow update and none at all.




                                       XMODEM


                  With XMODEM file transfer with  CRC  checking,  PC-VT has
          made a commitment to accurate  file transfer. In support of this,
          PC-VT sets the VERIFY switch on during its run. The VERIFY switch
          is restored to its initial value when PC-VT terminates.

                  When  running XMODEM,  PC-VT  automatically  changes  the
          communications to 8 data  bits,  no parity, 1 stop bit (8-N-1) if
          you are not already set at that protocol. PC-VT then restores the
          protocol to your value when the XMODEM transfer is complete.

                  Public  domain  programs are available  with  the  XMODEM
          program written for the  VAX  running VMS and the VAX running 4.2
          UNIX. Check with your local computer club.




                                        PCjr


                  A  comment on the operation of PC-VT  on  the  IBM  PCjr:
          There are some hardware differences which you should be aware of.


                                                                   Page 167






          Appendix J                                            PC-VT v10.0


          If  you  are  using  the  PCjr  internal  modem for  XMODEM  data
          transfer, don't forget that you must set the modem with a "^NF 4"
          command.  When  the  PCjr  is  doing  a  disk access,  all  other
          interrupts are turned off. This means that if data comes down the
          communications line, it is lost.  For  this  reason,  using ASCII
          file  transfer  for  receiving  a  file is not  recommended.  Use
          XMODEM. If you must receive a file using ASCII,  PC-VT  sends  an
          XOFF  while the PCjr is writing to disk and sends an XON once the
          machine  is ready to process interrupts  again.  Sending  a  file
          using the ASCII file transfer method works ok.  The  dialer works
          fine if you  change  the  modem  dialing command from ATDT to the
          characters  required  by  the  PCjr  modem  (you  need  the  PCjr
          Technical Reference Manual to  completely  understand  the PCjr's
          modem).

                  One other problem that some users have with PC-VT running
          on the PCjr is with the F8, F9, and F10 keys.  All  of  the other
          function keys work ok on the PCjr, and of course they all work ok
          on the PC and the AT. The problem  is  that  when  you want to do
          something like call up the DIALING frame, you have to press CTRL-
          F9. Some PCjr's ignore this key because BIOS never even sends the
          program an interrupt when  you  have pressed the key. If you have
          one  of  these  PCjrs, you have  one  alternative.  You  use  the
          Function Shift feature of the PCjr described on page 5-35  of the
          PCjr Technical Reference Manual:

                "Function Lock

               Concurrently pressing first the Fn key  and  Shift key,
               and then pressing the Esc key causes keys 2 thru  11 to
               shift to their 'Function' states and remain there until
               the same combination is pressed again."

                  When IBM refers to keys 2 thru 11 they  mean  the  number
          keys on the top row of the keyboard: 1 thru 0. To get CTRL-F8, go
          into the 'Function Lock' mode, then press the Ctrl key and  the 8
          key and then go back out of 'Function Lock' mode.

                  There are  three alternate keys which you can use instead
          of CTRL-F8,9,and 10.

          Instead of:             Use: CTRL-F8
                                  ALT-C CTRL-F9
                                  ALT-V CTRL-F10
                                  ALT-O


          J.2  HELP Customization


                  The HELP file  is  a  text  file which PC-VT reads into a
          segment of  dynamically  allocated  memory  when  the  user first
          presses ALT-H. Subsequent presses  of  the  HELP  key does not do
          disk reads. HELP is context sensitive; that is, the HELP  you get


          Page 168






          PC-VT v10.0                                 VT100 & 4014 Emulator


          is  related  to  the  part  of  PC-VT  which  you  are  currently
          executing.

                  The  text  file  can  be  thought of as broken down  into
          pages. The pages have a subject number assigned to them. When you
          ask for HELP in PC-VT, a subject number  is  passed  to  the HELP
          program. HELP then displays the pages which provide  HELP  on the
          subject. The subject numbers are:

                  '0'     display this page always
                  '1'     VMS specific page from Main Program
                  '2'     UNIX specific page from Main Program
                  '3'     PC-VT Main Program specific page
                  '4'     SETUP A specific page
                  '5'     DIALER specific page
                  '6'     MACRO specific page
                  '7'     SETUP B specific page
                  '8'     4014 specific page


                  The dollar sign  character  (ASCII 36) is the page break.
          It is followed by the  subject number. Therefore, the dollar sign
          cannot appear in any of the  HELP  text. There should be a CTRL-Z
          at the end of the file.

                  Each  time  that  the user presses PgUp or PgDn, the HELP
          information is scrolled either one page back or one page forward.
          Pressing the Esc key returns  you to whatever frame was displayed
          when you first asked for HELP.

                  The  HELP  information  displays  with   bold,  blinking,
          reverse video and underline  attributes.  If  for any reason, you
          want to change them, here is  how  they are coded in the HELP.DAT
          file.

                  The true video attribute  is  actually  put into the file
          preceded by a CTRL-Backspace character. The attributes are:

                          Normal     Intensified Blinking    Intensified
                                                             & Blinking
          White on Black  07h CTRL-G 0Fh CTRL-O  87h ALT-135 8Fh ALT-143
          Underline       01h CTRL-A 09h CTRL-I  81h ALT-130 89h ALT-137
          Black on White  70h P      78h x       F0h ALT-240 F8h ALT-248

                  So to get a normal video (white on black)  blink,  put  a
          CTRL-Backspace  followed  by  an 87h into the file. The ALT codes
          are generated by holding down the ALT key and pressing  the three
          digit keys on the keypad. Depending on which text editor you use,
          you may have to enter these codes in different ways.

                  So whenever PC-VT sees  a  CTRL-Backspace  (ASCII  127 or
          FFH) in  the  file,  it  reads  the  next character and uses that
          character as the attribute on the call to BIOS via interrupt 10h.
          It uses that attribute  until  you change it to some other value.


                                                                   Page 169






          Appendix J                                            PC-VT v10.0


          So  if  you want regular white on  black  again,  enter  a  CTRL-
          Backspace followed by a  CTRL-G.  With this, you can add color to
          the HELP screens also.

                  Of  course,  you  use  this   at  your  own  risk  -  its
          complicated.


          J.3  Miscellaneous


                  Since the IBM  PC  does  not  have  some  of  the special
          character and line drawing set characters, PC-VT makes use of the
          best available representation. See the description for the "ESC )
          0" sequence for the list of the selected representation.

                  The NUM LOCK key acts per the IBM documentation.

                  Undefined   or  illegal  escape  control  sequences   are
          ignored.

                  PC-VT controls the speaker to cause it to  beep  by doing
          direct I/O to addresses 42H,43H, and 61H.

                  The printer  serves  as  a  capture  device  only. Escape
          sequences are not sent to the printer. This is different than the
          VT100  attached printer. PC-VT has a  speical  sequence  to  send
          control  characters to the printer, look  at  the  section  below
          titled "Printer Support".

                  The  ALT-F  key  calls  up  another  copy  of COMMAND.COM
          leaving PC-VT in  memory  and asleep. The memory remains occupied
          and the interrupt driven communications buffer remains  active so
          that any characters which come down the line  are  buffered. Once
          you get the new DOS prompt,  you  can do almost anything that you
          can  do  from  the regular DOS prompt. When you wish to return to
          PC-VT, simply type the word: exit. PC-VT awakens and restores the
          screen. Any characters which have  come  down  the communications
          line while DOS was running are displayed but only if you  did not
          run  a  communications  program using the same COM port while you
          were in DOS.

                  In case the user executed  a  "BREAK  ON"  command, PC-VT
          resets  BREAK  checking  while  it  is running and  restores  the
          checking, if necessary, as it terminates.

                  PC-VT  uses  dynamic memory when  possible.  The  program
          permanently occupies about 58K bytes. For HELP, PC-VT grabs about
          23K bytes via DOS call 48H.  If  the memory is not available, the
          HELP key is ignored.  When  you  request  KERMIT, PC-VT starts up
          another copy  of COMMAND.COM and then EXECutes KERMIT.COM via DOS
          call 4BH. COMMAND.COM uses about 5K and KERMIT uses about 83K. If
          you have activated the Scroll Buffer, PC-VT allocates 32K for the
          buffer. If it  cannot  get  the  memory, the SCROLL LOCK key just


          Page 170






          PC-VT v10.0                                 VT100 & 4014 Emulator




          ---------------------------------------------------------------------------



                                      ÚÄÄÄÄÄÄÄÄÄÄ¿
                                      ³          ³
                                      ³          ³
                                      ³  KERMIT  ³
                        ÚÄÄÄÄÄÄÄÄÄÄ¿  ³          ³
                        ³          ³  ³   83K    ³  ÚÄÄÄÄÄÄÄÄÄÄ¿
                        ³  Scroll  ³  ³          ³  ³          ³
                        ³  Buffer  ³  ³          ³  ³          ³
                        ³          ³  ÃÄÄÄÄÄÄÄÄÄÄ´  ³  KERMIT  ³
                        ³   32K    ³  ³ Command  ³  ³          ³
                        ³          ³  ³   5K     ³  ³   83K    ³
                        ÃÄÄÄÄÄÄÄÄÄÄ´  ÃÄÄÄÄÄÄÄÄÄÄ´  ³          ³
                        ³  HELP    ³  ³  HELP    ³  ³          ³
                        ³          ³  ³          ³  ÃÄÄÄÄÄÄÄÄÄÄ´
                        ³   23K    ³  ³   23K    ³  ³ Command  ³
                        ³          ³  ³          ³  ³   5K     ³
          ÚÄÄÄÄÄÄÄÄÄÄ¿  ÃÄÄÄÄÄÄÄÄÄÄ´  ÃÄÄÄÄÄÄÄÄÄÄ´  ÃÄÄÄÄÄÄÄÄÄÄ´
          ³          ³  ³          ³  ³          ³  ³          ³
          ³          ³  ³          ³  ³          ³  ³          ³
          ³  PC-VT   ³  ³  PC-VT   ³  ³  PC-VT   ³  ³  PC-VT   ³
          ³          ³  ³          ³  ³          ³  ³          ³
          ³   58K    ³  ³   58K    ³  ³   58K    ³  ³   58K    ³
          ³          ³  ³          ³  ³          ³  ³          ³
          ÀÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÙ
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³                       DOS                          ³
          ³         The amount of memory used by DOS           ³
          ³ depends on its version and RAM resident software.  ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

                  Figure J.1 PC-VT Memory Configuration


          ---------------------------------------------------------------------------

          functions as a scroll lock and does not give you  recall ability.
          By  implementing  PC-VT  in this manner, it runs on machines with
          small memory sizes but if more memory is  available,  PC-VT makes
          full use of it.

                  Figure J.1 shows a few of the memory configurations which
          PC-VT can set up.

                  PC-VT  has a switch in the SETUP  frame  which  lets  you
          select  either a VMS host or a UNIX host. If VMS is selected, PC-
          VT sets up the editing keypad and function keys  for  either  the
          EDT or EVE editor and uses  CTRL-Z  as the End of File character.
          When the UNIX mode is selected, PC-VT sets up the  editing keypad


                                                                   Page 171






          Appendix J                                            PC-VT v10.0


          for the VI editor and uses CTRL-D as the End of File indicator to
          the host.

                  The  color  graphics  adapter  does not handle underlined
          characters. Since the VT100 has an attribute for underline, PC-VT
          handles this in a special way. On the color graphics adapter, PC-
          VT displays underlined text as bold  or  bold/blinking selectable
          from  the  SETUP  B frame. The IBM Monochrome Display can display
          the underline attribute.

                  Auto   repeat   is  handled  by   the   keyboard.   PC-VT
          approximates the  repeat off mode by clearing the keyboard buffer
          on  the receipt of the auto repeat off  escape  sequence  and  by
          clearing the keyboard buffer after reading each character. Repeat
          on mode is left entirely to the keyboard and the BIOS.


          J.4  DESQview and TopView


                  PC-VT is compatible with both DESQview and TopView. PC-VT
          normally  runs  in  the  foreground  only.  By  resetting certain
          features in the SETUP B frame, PC-VT also runs in the background.
          Running  PC-VT in the background lets  you  upload  and  download
          files  while you are doing other work. If you set up PC-VT to run
          in the background, it runs a little slower when you run it in the
          foreground and some features are not be available.


          DESQview


                  The minimum memory size is 58K. In order to use HELP, set
          the memory to  81K.  To  use  the Scroll Buffer, increase that by
          32K. Under DESQview, KERMIT  and  the  second copy of COMMAND.COM
          should be run as separate programs and not from PC-VT. To use the
          4014  emulator,  the  program  must  be  set  up  to  run in  the
          foreground only.

                  For  DESQview,  in  order  to  run  PC-VT  in either  the
          foreground or the background,:

             -  Set window position to 0,0,25,80,

             -  In the options list, set only the "close on  exit  to  DOS"
                option.

                  In  PC-VT's SETUP B frame, turn  Fast  Screen,  DMA,  and
          Scroll  Buffer off by setting their  feature  selection  bits  to
          zero.

                  To run PC-VT in the foreground only,:

             -  Set window position to 0,0,25,80,


          Page 172






          PC-VT v10.0                                 VT100 & 4014 Emulator


             -  In the options list, set  the  "write  directly  to screen"
                option and
                any others that you wish.

                  In PC-VT's SETUP B frame, you can select any options that
          you wish including Fast Screen,  DMA,  and  Scroll  Buffer. PC-VT
          suspends  when   you   switch   to   another   program   but  the
          communications line interrupt  handler still buffers any incoming
          characters.


          TopView


                  The minimum memory size is 58K. In order to use HELP, set
          the maximum size to  81K.  To use the Scroll Buffer, increase the
          maximum  by 32K. Under TopView, KERMIT and  the  second  copy  of
          COMMAND.COM should be run as separate programs and  not  from PC-
          VT. To use the 4014 emulator, the program must be  set  up to run
          in the foreground only.

                  For  TopView,  in  order  to  run  PC-VT  in  either  the
          foreground or the background:

          Set screen type to D,
          Set window size to 25 rows and 80 columns,
          Set pages to 1,
          Set offsets to 0,0,
          Set range of software interrupt vectors swapped to 0B low and 24
          high, and
          Answer n to the last four questions.

                  In  PC-VT's SETUP B frame, turn  Fast  Screen,  DMA,  and
          Scroll  Buffer off by setting their  feature  selection  bits  to
          zero.

                  To run PC-VT in the foreground only:

          Set screen type to D,
          Set window size to 25 rows and 80 columns,
          Set pages to 1,
          Set offsets to 0,0,
          Set range of software interrupt vectors swapped to 0B low and 24
          high,
          Answer y to the question about writing directly to the screen,
          and
          Answer n to the last three questions.

                  In PC-VT's SETUP B frame, you can select any options that
          you wish including Fast Screen,  DMA,  and  Scroll  Buffer. PC-VT
          suspends  when   you   switch   to   another   program   but  the
          communications line interrupt  handler still buffers any incoming
          characters.



                                                                   Page 173






          Appendix J                                            PC-VT v10.0


          J.5  PC-VT Private Escape Sequences


                  For those of you into such things, PC-VT contains several
          private escape sequences which cause it to do a few  things which
          normally can only be done by pressing keys on the  keyboard (i.e.
          done  by  the  user of the program).  The  distribution  diskette
          contains several *.COM files  which  use  some of these sequences
          and are provided as examples of this technique.




                         Automatic File Upload and Download


                  First are two private sequences  which  perform  the same
          effect as if the user had pressed:

          CTRL-F3         Receive File    ESC [ ? 2 1 h
          CTRL-F4         Transmit File   ESC [ ? 2 2 h

                  These would be useful  in  some  programed  file transfer
          routine which the user would only have to respond  to  a  program
          running  on  the  host.  It  would send down the escape  sequence
          without the user having to concern himself with it.

                  Any error condition which results from these commands can
          be accessed with the "ESC [ ? 1 0 n" report sequence described in
          more detail below.




                              Sending a Carriage Return


                  This private sequence, causes PC-VT  to  send  a carriage
          return (ASCII 13) to the host.

          Send CR         ESC [ ? 2 3 h




                           Filename Download from the Host
                                         and
                                  The Prearm Buffer


                  Another pair of escape codes does something a little more
          complicated. When you start  a  file  transfer, PC-VT always asks
          the user to type in the PC's filename. With these  two sequences,
          you a can set up PC-VT with a filename from the host. Then when a


          Page 174






          PC-VT v10.0                                 VT100 & 4014 Emulator


          file transfer is started, PC-VT  pulls this filename out and puts
          it in the keyboard buffer just  as  if  the user had typed it in.
          Start the prearm buffer load with the sequence:

          Start buffer    ESC [ ? 2 4 h

          Then send the filename  with  the  "=a",  "=A", "=x", "=c", "=t",
          "=v", or "=k" on the end. Since PC-VT's file  transfer  mode  can
          default to a mode selected by the user, the  host  should  ALWAYS
          send down the mode after the  equal  sign. You may put a carriage
          return at the end just as the user would type it in but it is not
          required. The  maximum buffer size is 80 characters including the
          carriage  return  but  DOS  legal  filenames are a maximum of  66
          characters. Excess characters are ignored. You cannot download an
          escape character into the buffer. Then end it with this:

          End buffer      ESC [ ? 2 4 l

          Now if you send down a start file receive sequence:

          Receive File    ESC [ ? 2 1 h

                  PC-VT uses  the filename which you sent. Since the buffer
          is loaded with a filename, PC-VT won't prompt the  user  for  the
          filename. If the downloaded  filename  already  exists on the PC,
          PC-VT renames the file  automatically  in  an  attempt to find an
          unused filename. PC-VT changes the last character of the filename
          to the digits '0' through '9' in sequence, looking for  an unused
          name. If it finds one, it informs the user and continues with the
          receive file command using that  name.  Otherwise  it  aborts the
          transfer and either a  CTRL-Y  or  CTRL-D character (depending on
          Operating System selection) to the host followed by a CTRL-X.

                  On file transmit, if the requested file is not found, PC-
          VT  aborts  the  transfer and send  either  a  CTRL-Y  or  CTRL-D
          character (depending on Operating System selection)  to  the host
          followed by a CTRL-X.

                  With this scheme, the user would not have to type  in the
          PC's filename. The host  computer  can send it down the line. You
          can  see  that  this  can  be  useful  for  some  type  of  batch
          upload/download.

                  Here is what this might look like:

          ESC [ ? 2 4 h a:FILENAME.TXT=x CR ESC [ ? 2 4 l
          ESC [ ? 2 2 h
          (spaces shown for clarity only) <now PC-VT transmits
          the file a:FILENAME.TXT using the XMODEM protocol>

                  This sequence can be sent by the C language code:

          printf("\033[?24h%s\r\033[?24l\n\033[?22h",filename);



                                                                   Page 175






          Appendix J                                            PC-VT v10.0


                  If you are using KERMIT file transfer, you  can  load the
          prearm  buffer with a filename just  as  described  above.  PC-VT
          constructs a command line which  it passes to KERMIT. The command
          line looks like:

          rec  filename           : for download a file
          send filename           : for upload a file

          KERMIT returns to PC-VT as soon as the command is complete.

                  In  addition,  you  can  load  the prearm buffer  with  a
          complete command line for  KERMIT.  To do this, send a pound sign
          '#' down as the first character in the buffer and end  the buffer
          with '=k' as usual. PC-VT then starts up KERMIT and passes it the
          prearm buffer minus the  '#'  and '=k'. For example, you may want
          to  start  up  KERMIT,  have  it  display  STATUS  and then GET a
          wildcarded filename. You can send:

          ESC [ ? 2 4 h # status,get ab*.d* CR ESC [ ? 2 4 l
          ESC [ ? 2 2 h
          (spaces shown for clarity only except the one
          between the "get" and the filename)
          <now PC-VT starts up KERMIT and passes it that command line>

                  If you load PC-VT's  prearm  buffer  with the string #=k,
          KERMIT starts up in interactive mode.

                  To start Kermit from the host, send "ESC [ ? 2 2 l". This
          way is a little quicker than loading the prearm buffer with '#=k'
          as described above.

                  The attachment to  this PC-VT document describing KERMIT,
          shows all of the commands which KERMIT executes. The interface to
          KERMIT  is very general. When new versions  of  the  program  are
          available from Columbia  University,  you  can  just  replace the
          version included on the PC-VT distribution diskette.

                  Any error condition which results from these commands can
          be accessed with the "ESC [ ? 1 0 n" report sequence described in
          more detail below.
















          Page 176






          PC-VT v10.0                                 VT100 & 4014 Emulator






                              Change Default Directory


                  This private  sequence  performs  the  same  function  as
          pressing CTRL-F2:

          Change Default Directory        ESC [ ? 2 5 h

          This causes PC-VT to ask for a new default  disk  directory.  The
          load prearm buffer sequence shown above can be used to set up PC-
          VT with a  directory  name.  If  an error is encountered when you
          download a directory name, the user is not informed but  an error
          code is available.

                  With  this scheme, you do not have to  type  in  the  new
          default directory. The host computer can send it  down  the line.
          You can see that this  can  be  useful  for  some  type  of batch
          upload/download.

                  Here is what this might look like:

          ESC [ ? 2 4 h a:\mydire\sub CR ESC [ ? 2 4 l
          ESC [ ? 2 5 h
          (spaces shown for clarity only)
          <now PC-VT changes the default directory to a:\mydir\sub>

                  This sequence can be sent by the C language code:

          printf("\033[?24h%s\r\033[?24l\n\033[?25h",directory);

                  Any error condition which results from  this  command can
          be accessed with the "ESC [ ? 1 0 n" report sequence described in
          more detail below.




                           Editor and OS Keyboard Support


                  These four  escape sequences let the host select the mode
          of keyboard  support. Sending these sequences has the same effect
          as if the user selected the corresponding options in the  SETUP B
          frame.

          Select EVE Keypad Support       ESC [ ? 2 8 h
          Select EDT Keypad Support       ESC [ ? 2 8 l
          Select VMS O/S Support          ESC [ ? 2 9 h
          Select UNIX O/S Support         ESC [ ? 2 9 l



                                                                   Page 177






          Appendix J                                            PC-VT v10.0


                              Terminate PC-VT Remotely


                  You can cause PC-VT to terminate by sending

          ESC [ ? 2 6 h

          This is the same pressing CTRL-F8 on the keyboard.




                                Start Up Command.COM


                  You  can   cause  PC-VT  to  start  up  another  copy  of
          Command.COM by sending either:

          ESC [ ? 2 7 h
          or
          ESC [ ? 2 7 l

                  This  is  the  same as pressing ALT-F on the keyboard. If
          Command.COM is started in  this  way,  it runs interactively. You
          must still type in the word "exit" to return to PC-VT.

                  The second escape sequence  causes  PC-VT  to  wait after
          Command.COM has completed before the  emulator  starts  up again.
          The user is prompted to press a key to continue.

                  You can also load the prearm buffer with a DOS command to
          be executed. Anything that you can normally type in  at  the  DOS
          prompt can be downloaded. In order for this to operate correctly,
          you must begin the command with "/c". This is  a  requirement  of
          DOS. You can execute any DOS internal command like  COPY  or  you
          can  execute  a  program like BASICA. DOS uses the current search
          path to find the program.

                  Here is what this might look like:

          ESC [ ? 2 4 h /cbasica myprog ESC [ ? 2 4 l
          ESC [ ? 2 7 h
          (spaces shown for clarity only except the
          ones in the DOS command itself) <now PC-VT executes
          the BASICA program named myprog>

                  or

          ESC [ ? 2 4 h /ccopy a:\dir\dir2\file1.dat e:\ableESC [ ? 2 4 l
          ESC [ ? 2 7 h
          (spaces shown for clarity only except the
          ones in the DOS command itself) <now PC-VT executes
          DOS COPY command with the two files given>



          Page 178






          PC-VT v10.0                                 VT100 & 4014 Emulator


                  Any error condition which results from  this  command can
          be accessed with the "ESC [ ? 1 0 n" report sequence described in
          more detail below.




                               Starting Help Remotely


                  You  can  cause  PC-VT  to  start up the HELP feature  by
          sending:

          ESC [ ? 2 6 l

                  This is the same as pressing ALT-H on the keyboard. Press
          the Esc key to return to PC-VT.

                  Any error condition which results from  this  command can
          be accessed with the "ESC [ ? 1 0 n" report sequence described in
          more detail below.




                              Ignoring Escape Sequences


                  You can cause PC-VT to start ignoring escape sequences by
          sending:

          ESC [ ? 2 3 l

          Once the host sends  this  sequence, you must reset the option in
          the SETUP B frame manually or terminate and restart PC-VT.




                                     Error Codes


                  A private escape sequence returns  the  last  error which
          PC-VT encountered. The sequence is:

          ESC [ ? 1 0 n

                  PC-VT responds with:

          ESC [ ? x x x ; y y y n

          where xxx is three ASCII  characters  which  represent  the error
          code/return  code  and  yyy  is  three  ASCII   characters  which



                                                                   Page 179






          Appendix J                                            PC-VT v10.0


          represent the termination code. Once  these  codes  are returned,
          PC-VT resets them to zero.

                  If you are going to use this feature,  you  should always
          read the code before you start in order to make  sure  that it is
          reset to zero.

                  The error/return and termination  codes  are  set  by the
          following actions from the host:

            1.  Any printer  action if the printer is unavailable, off line
                or runs out  of  paper.  The  error code is the status byte
                returned by the BIOS,

            2.  Receipt of the escape  sequence  which  redefines  the PC's
                keyboard.

            3.  Receipt of the escape sequence which invokes KERMIT,

            4.  Receipt of escape sequences which invoke any file transfer,

            5.  Receipt of the escape sequence which invokes HELP,

            6.  Receipt  of the escape sequence which invokes  COMMAND.COM,
                or

            7.  Receipt  of  the   escape  sequence  which  invokes  change
                directory.

                  Error codes which are returned as xxx are  in  most cases
          the  code  which DOS returns to PC-VT.  There  are  a  few  PC-VT
          extensions. The termination  code,  yyy, is zero. The error codes
          are:

                  ERROR
                  CODE
                  (xxx)   CONDITION
                  1       Invalid function
                  2       File not found
                  3       Path not found
                  4       Too many open files
                  5       Access denied
                  8       Insufficient memory
                  15      Invalid drive
                  100     Disk full
                  101     XMODEM error limit exceeded
                  102     Duplicate filename found during Receive file

                  Consult the DOS manual for other error codes.

                  The return code  is  produced  by  sequences  which start
          other  programs  such  as KERMIT and Command.COM. The code is the
          value which the called program returns in AL  when  it terminates



          Page 180






          PC-VT v10.0                                 VT100 & 4014 Emulator


          via  the  DOS  call  4Ch.  For  xxx  to be  a  return  code,  the
          termination code, yyy, must be greater than 100.

                  The termination code is also produced by  sequences which
          start other programs such as  KERMIT  and  Command.COM.  The code
          values are:

                  TERMINATION
                  CODE
                  (yyy)   CONDITION
                  000     xxx is an error code not a program return code.
                  100     Normal termination/yyy is a program return code.
                  101     Terminated by CTRL-BREAK. yyy is a program
                          return code.
                  102     Terminated by Critical Device Error. yyy is a
                          program return code.
                  103     Terminated by DOS call 31h. yyy is a program
                          return code.




                                       Colors


                  PC-VT  can handle color in VT100 mode if  you  are  on  a
          color monitor.  The color must be set by the host computer.  Here
          are the escape sequences and the colors which they invoke:

          ESC [ 8 m       Invisible
          ESC [ 3 0 m     Black Foreground
          ESC [ 3 1 m     Red Foreground
          ESC [ 3 2 m     Green Foreground
          ESC [ 3 3 m     Yellow Foreground
          ESC [ 3 4 m     Blue Foreground
          ESC [ 3 5 m     Magenta Foreground
          ESC [ 3 6 m     Cyan Foreground
          ESC [ 3 7 m     White Foreground
          ESC [ 4 0 m     Black Background
          ESC [ 4 1 m     Red Background
          ESC [ 4 2 m     Green Background
          ESC [ 4 3 m     Yellow Background
          ESC [ 4 4 m     Blue Background
          ESC [ 4 5 m     Magenta Background
          ESC [ 4 6 m     Cyan Background
          ESC [ 4 7 m     White Background

                  Example to set red characters on a blue background:

          ESC [ 3 1 m ESC [ 4 4 m ESC [ 2 J ESC [7 H

                  Where ESC is the  escape  character  ASCII 27. Certain of
          these combinations, like black foreground characters  on  a black
          background, won't show anything on the display.


                                                                   Page 181






          Appendix J                                            PC-VT v10.0


                  Note that  setting the colors does not affect the current
          contents of the display. Only characters displayed  following the
          color setting sequences are in color. This is consistent with the
          other Select  Graphic Rendition sequences. To clear the screen to
          the new  background color, use the clear screen sequence followed
          by the home cursor sequence. By just using  the  color sequences,
          you can make portions of your output display in different colors.

                  Once color is set, sending the "ESC [ m" (reset) sequence
          uses these colors for the default attributes. If you want to make
          these selections permanent for the  next time that you run PC-VT,
          go to the SETUP A frame and select the "s"  option  to store this
          information on disk. Because of this, if you want  to  return  to
          normal white on black operation, you must send the "ESC  [  3 7 ;
          40 m" sequence. Juset  sending  a reset does not restore white on
          black.

                  Since these sequences set the default attributes  for the
          program (until you terminate PC-VT), to run the PC-VT in  a color
          mode, have your host computer send down the appropriate sequences
          during your logon.




                                   Printer Support


                  To send a formfeed to the printer send "ESC [ ? 2 5 l" or
          press the ALT-P key on the keyboard.

                  Since PC-VT does not normally  send  escape  sequences to
          the printer, there is  a  special way to get control sequences to
          the  printer.  Use  the prearm buffer sequences above to fill the
          prearm buffer with the necessary controls. Then send the "ESC [ ?
          3 i" sequence.

                  Any  underline  characters  in  the buffer are translated
          into the escape  character  (ASCII  27)  before it is sent to the
          printer.

          ESC [ ? 2 4 h _124x ESC [ ? 2 4 l
          ESC [ ? 3 i
          (spaces shown for clarity only)

          The characters Escape, 1, 2, 4, and x are sent to the printer.










          Page 182






          PC-VT v10.0                                 VT100 & 4014 Emulator


                                 4010/4014 Emulation


                  A special sequence was added  in the 4014 emulator of PC-
          VT.  Upon  receipt  of  ESC  DC4, PC-VT switches back into  VT100
          emulator mode. The screen  is  cleared  unless  the /b option was
          used on the command line.




                                 Ignored Characters


                  PC-VT  normally  ignores  00h  and  7FH  while  in  VT100
          emulation mode.  To have PC-VT place them into the communications
          buffer  where they are still ignored later  but  take  up  buffer
          space send : "ESC [ 2 4 l".






































                                                                   Page 183






          Appendix J                                            PC-VT v10.0


























































          Page 184






          PC-VT v10.0                                 VT100 & 4014 Emulator








                                     Appendix K

                               User-Supported Software


                  This program and documentation are copyrighted by Mark C.
          DiVecchio.

                  Permission to copy:

                  Individuals, clubs and other non-profit organizations are
          granted permission by the author  to freely copy this program and
          documentation and share it with their members, so long as:

                No price is  charged  for  the  software  or documentation.
                However, a distribution cost may be charged for the cost of
                the diskette, so long as it is not more than $9 total.

                Club members are informed of the user-supported concept and
                encouraged to support it with their registration fees.

                The program and  documentation  are not modified in any way
                and are always distributed together.

                  Schools, universities, and other non-profit organizations
          are granted permission  by  the  author  to copy PC-VT for use on
          other computers and at  other  locations  in the organization, so
          long as:

                The full fee of $35 has been paid for the original  copy of
                the program.

                A usage fee of  $40  is  paid  for each additional building
                where PC-VT will be  used.  Within  each building for which
                the usage fee has been paid, PC-VT may be copied freely for
                use on any other computer  in  that  building.  Contact the
                author if you would like to make other arrangements.

                  Commercial users of this program are  required  to submit
          the registration fee. Commercial and  site  licenses  as  well as
          source code licenses (in MASM) are available. The site license is
          handled as a graduated per copy fee. Contact the author.








                                                                   Page 185






          Appendix K                                            PC-VT v10.0


          The User-Supported concept:

          User-Supported Software

                  If you are using this program and find it to be of value,
          your registration fee will be appreciated.  ($35 is suggested)

                  For a $55 registration  fee,  you  will receive a printed
          manual containing this complete document.

                  For California delivery, add 7.25% sales tax.

                                  Mark C. DiVecchio
                          Athena Systems Development Group
                         9888 Carroll Center Road  Suite 113
                                San Diego, CA  92126
           (616) 549-4056               RBBS : (619) 549-3927

                  Regardless of whether you pay the  registration  fee, you
          are encouraged to use, copy and share this program.

                  User-supported software is an experiment  in distributing
          computer programs, based on these beliefs:

                That the value and utility  of software is best assessed by
                the user on his/her own system.

                That the creation of  personal  computer  software  can and
                should be supported by the computing community.

                That copying of programs should be encouraged,  rather than
                restricted.

                  Anyone may request a copy of this  user-supported program
          by  sending  one  blank 1.2Mb formatted disk (without DOS) or two
          blank 360Kb formatted  disks  to  the  author of the program.  An
          addressed, postage-paid return mailer must accompany the disk (no
          exceptions, please). A copy of the program, with documentation on
          the  disk, will be sent by return mail.  The program will carry a
          notice  suggesting  the  payment  of  a registration fee  to  the
          program's author.  Paying  that  registration  fee  is completely
          voluntary on the part of each non-commercial user.

                  You may also get a  copy directly from the Athena Systems
          Development Group BBS at (619) 549-3927. Check this BBS for newer
          versions of the program as well.

                  Free  distribution of software and voluntary payment  for
          its use eliminates  costs  for  advertising  and  copy protection
          schemes.

                  Users obtain quality software at reduced  cost.  They can
          try it out  before buying, and do so at their own pace and in the



          Page 186






          PC-VT v10.0                                 VT100 & 4014 Emulator


          comfort  of their own home or office.   The  best  programs  will
          survive, based purely on their quality and usefulness.

                  Please join the experiment.

                  If you believe  in  these ideals, the registration fee is
          solicited to help make them work.

                  If you have read this far, and are considering submitting
          the fee, you get a free tip. When you start up  PC-VT,  put  a /g
          after the program  name  -  pc-vt/g  - and the 'send money' frame
          won't  be  displayed  but  you   will   go   directly   into  the
          communications frame.

                  The following invoice is  provided  for  those of you who
          wish an invoice for your tax records.








































                                                                   Page 187






          Appendix K                                            PC-VT v10.0



                                 --------------------
                                       INVOICE
                                 --------------------




                      Purchased from:
                           Mark C. DiVecchio
                           Athena Systems Development Group
                           9888 Carroll Center Road  Suite 113
                           San Diego, CA  92126

               DATE:     /     /                     Invoice No. 10.0
               --------------------------------------------------------------
                                                    PRICE     PRICE
               PRODUCT                    QTY       EACH      EXTENDED
               -------------------------  ---       -----     --------

               PC-VT Terminal Emulator
                  Registration Fee                  $35
                  v10.0

               PC-VT Terminal Emulator
                  Registration Fee
                  AND Printed Manual                $55
                  v10.0

               PC-VT Distribution Disk               $9
                  Includes Postage and
                  Handling

               Copy of PC-VT and Documentation      N/C
                  on your Preformatted 1.2Mb
                  Diskette Returned in your
                  Postage Paid Self Addressed
                  Mailer
                                       --------------------------------------
                                                  SUBTOTAL

               7.25% Sales Tax (CA Residents only)

                                       --------------------------------------
                                       PLEASE PAY THIS AMOUNT           TOTAL
                  -----------------------------------------------------------

                  Please make check payable to : Athena Systems Development
          Group.

                  You may retain this Invoice for your tax records.





          Page 188















                                          Index


                  ! - Parity Error            Answerback Message
                       Character 56              Setting 52
                  ! - Parity Error            Application Keypad
                       Character 166               Mode 20
                  # - Buffer Overflow         ASCII File Transfer
                       Character 166               with Handshake
                  132 Column Mode 13               67
                  4014                        Autoprint 59
                     Character Sets           Autorepeat
                       152                       Enabling 53
                     Coordinates 145          Autowrap
                     Terminal Status             Enabling 54
                       Byte 158
                  4014 Autoprint              B
                     Selecting 59             Backspace Key Code
                  4014 CR Effect                 Setting 56
                     Selecting 59             Beep 12
                  4014 Gin Termination        Bell 12
                     Selecting 59             BREAK
                  4014 Key                       Long 40
                     ARROW 99                 Buffer Size 166
                     BACKSPACE 99                Selecting 57
                     HOLD SCREEN 100          Bypass Character 67
                     NUL Character 161
                     PAGE KEY 99              C
                     RESET 99                 Cable
                     RUBOUT 99                   RS-232 Interface
                     Standard Keyboard             165
                       99                     CAPS LOCK 19, 100
                     To VT100 Mode 100        Capture Mode 71
                     TTY LOCK 100             Click 12, 103
                  4014 LF Effect              Color 181
                     Selecting 59                Permanently
                  4014 LOY                         Setting 182
                     Selecting 59                Selecting 119
                  4014 Page Full              COM Port
                     Selecting 58                Clearing 140
                  8 Bit ASCII                    Selecting 50, 57
                     Enabling 58              COM Port Addressing
                  8259 PIC 165                     165
                  8 Bit ASCII 165             Command Line Option
                                                 /c 13
                  A                              /d 12
                  Alpha character 20,            /e 13
                       36                        /g 12, 13












                     /h 13                    Emulator
                     /i 14                       Starting 4014
                     /l 13                         mode 129
                     /t 13                    Emulators
                  COMMAND.COM                    Changing from
                     Calling 40, 101               4014 to VT100
                  Command Line Option              100
                     /d 85                       Changing from
                  Communications                   4014 to VT100
                       Buffer Handling             156
                       166                    Error Codes 179
                  Crosshair Position          Error Messages 61
                       Report 158                Dialing Directory
                  CTRL-D Functions 64,             86
                       65, 71                    Macro Directory
                  CTRL-D Functions 66              94
                  CTRL-Z Functions 64,        Error Messages 105
                       65, 71                 ESC ? 156
                  CTRL-Z Functions 66         ESC CAN 155
                  Cursor Mode                 ESC DC2 156
                     Selecting 53             ESC DC4 156
                  Cursor Problem 164          ESC ENQ 157
                                              ESC ETB 155
                  D                           ESC FF 155
                  Default Directory           ESC SUB 155, 158
                     Changing 39, 77          Escape Sequences
                  Defaults                       Private 174
                     File Transfer            EVE Editor 32
                       Mode 49, 52, 63        Everex Edge 13
                  Del Character 17            Extra Byte 145
                  DEL implies LOY 147,
                       152                    F
                  DESQview 172                Fast Screen Update
                  Dialing Commands 81              167
                  Dialing Directory           File Capture Mode 71
                     Fetching 83              Fixed Disk 9
                     Saving 83                Frame
                  Dialing Facility 40            Communications 10
                  Dialing Key 79
                  DOS                         G
                     Gateway 101              GIN Mode 150
                  DOS Gateway 40
                  Drawing Mode                H
                     Defocused 153            Hang Up 41, 101
                     Setting 152              Hanging up the phone
                  Drawing Mode                     83
                     Write-Thru 153           HELP 40, 101, 140,
                  DTR                              168
                     Dropping 83              HERE IS 40
                                              High Resolution
                  E                                Graphics 13
                  Editor Selection            High Resolution
                       EDT/EVE 53                  Graphics 13
                  EDT Editor 25               Honk 97












                                              PCjr Function Keys
                  K                                168
                  KERMIT 76                   Prearm Buffer 175
                  Keyboard                    Printer
                     Redefinition 42
                  Keypad Support 20           Formfeed 182
                                                 Selecting 57
                  L                           Printer Echo
                  LCE Mode 151                   Selecting 39
                  Line Feed Characters        Printing the Screen
                       64                          39
                  Line Turnaround                4014 100, 155
                       Character 67
                  Linefeed Characters         R
                       55                     Receive a File
                  Local Echo                     =a option 72
                     Enabling 55, 139,           =c option 72
                       160                       =k option 72, 76
                  Logon Macros 81                =x option 72, 75
                  LPT                            Default Mode 49
                     Selecting 57             Receiving
                                                   (Downloading)
                  M                                Files 39
                  Macro Directory             Running Programs
                     Fetching 89                   from PC-VT 40,
                     Saving 89                     101
                  Macro Facility 40
                  Macro Keys 40, 89,          S
                       101                    Screen Background
                     Commands 91                 Selecting 53
                     Downloading 93           Screen Blanking 60
                  Margin Bell                 Screen Dump 18, 42
                     Enabling 53              SCRNDUMP.DAT 18, 42
                  Modem Parameters            Scroll Buffer 41,
                     Selecting 51                  170
                  Modem Speed                    Enabling 59
                     Selecting 50                Initiating 140
                  Monitor                     SCROLL LOCK 18, 100
                     Both 13                  SETUP
                     Default 14                  Defaults 53
                     Everex Edge 13              Key 39
                     Hercules Graphics           Saving 48
                       13                        Selecting
                                                   Defaults 48
                  N                              Selecting
                  NUM LOCK 19, 20                  Features 50
                                              SETUP Key 47
                  P                           Smart Macros 91
                  Page Full 58                Snow Screen Update
                  Parity Checking                  167
                     Enabling 56              Status Line 10, 18,
                  PC-VT= 9, 61, 86,                54, 103
                       90, 94                    Alpha character
                  PCjr 167                         103












                     CD 104                   Transmitting
                     CTS 104                       (Uploading)
                     DSR 104                       Files 39
                     KBD LOCKED 103
                     Local 103                U
                     Lx 104                   UK Character Set
                     On Line 103                 Selecting 54
                     P 104                    Underline Attribute
                     SCR 103                     Selecting 58
                     Vx.x 103
                     X 104                    V
                  Status Line                 Vectors
                     CAP 103                     Dark 145
                     NUM 103                  VI Editor 36
                  Stop Bits                   Viewing a file 76
                     Selecting 55             Viewing a file 65
                                              VMS 4.0 166
                  T                           VMS Line Editing 23
                  Tab Defaults                VT Key
                     Selecting 48                ARROWS 18
                  Tabs                           BACKSPACE 17
                     Clearing All 48             BREAK 39
                     Setting and                 DELETE 17
                       Clearing 47               HERE IS 19, 142
                  Tekpoints 97                   LINEFEED 18
                  Terminating PC-VT              NO SCROLL 18
                       15, 39                    NUL Character 18
                  Time of Day Clock              PF 20
                     Enabling 57                 SETUP 39
                  TopView 172                 VT100/VT102
                                                 Selecting 57
                  Transmit a File             VT52 Mode
                     =a option 65                Selecting 54
                     =c option 65
                     =k option 65             X
                     =t option 67             X Flag 40
                     =v option 65, 76         XMODEM 70, 75
                     =v option 76             XOFF-How to clear it
                     =x option 65                  40
                     =x option 70             XON/XOFF
                     =z option 65                Enabling 54
                     Default Mode 49




























                                      Contents





               Chapter 1  Introduction                               1
                  1.1  General Terminal Emulation  . . . . . . . . . 1
                  1.2  VT100/VT102/VT52  . . . . . . . . . . . . . . 2
                  1.3  4010/4014 . . . . . . . . . . . . . . . . . . 4

               Chapter 2  Required Hardware and Software             7

               Chapter 3  Installing and Starting PC-VT              9
                  3.1  Installation  . . . . . . . . . . . . . . . . 9
                     3.1.1  Floppy Diskette Installation . . . . . . 9
                     3.1.2  Fixed Disk Installation  . . . . . . . . 9
                  3.2  Starting PC-VT  . . . . . . . . . . . . . .  10
                  3.3  Command Line Options  . . . . . . . . . . .  12

               Chapter 4  Stopping PC-VT                            15

               Chapter 5  VT100 Keyboard Assignments                17
                  5.1  Regular Key Mapping . . . . . . . . . . . .  17
                  5.2  Keypad Mapping  . . . . . . . . . . . . . .  20
                  5.3  VMS Line Editing Keypad Mapping . . . . . .  23
                  5.4  EDT Keypad Mapping  . . . . . . . . . . . .  25
                  5.5  EVE Keypad Mapping  . . . . . . . . . . . .  32
                  5.6  VI Keypad Mapping . . . . . . . . . . . . .  36
                  5.7  Control Function Keys . . . . . . . . . . .  39
                  5.8  ALT Keys  . . . . . . . . . . . . . . . . .  40
                  5.9  Scroll Buffer . . . . . . . . . . . . . . .  41
                  5.10  Keyboard Redefinition  . . . . . . . . . .  42

               Chapter 6  SETUP Frames                              47
                  6.1  SETUP A . . . . . . . . . . . . . . . . . .  47
                  6.2  SETUP B . . . . . . . . . . . . . . . . . .  49
                     6.2.1  SETUP B Features and Defaults  . . . .  52

               Chapter 7  The PARAMS.DAT File                       61
                  7.1  Creation  . . . . . . . . . . . . . . . . .  61
                  7.2  Location  . . . . . . . . . . . . . . . . .  61
                  7.3  Updating  . . . . . . . . . . . . . . . . .  61
                  7.4  Error Messages  . . . . . . . . . . . . . .  61

               Chapter 8  Transmitting and Receiving Files          63
                  8.1  Transmitting ASCII Files (Uploading)  . . .  63
                     8.1.1  Uploading with Handshake . . . . . . .  67
                     8.1.2  Example of a Transmission Session  . .  68
                     8.1.3  A Useful VAX .COM Upload File  . . . .  69


                                          i









                  8.2  Transmitting Binary Files (Uploading) . . .  70
                  8.3  Receiving ASCII Files (Downloading) . . . .  70
                     8.3.1  Example of a Receive Session . . . . .  73
                     8.3.2  A Useful VAX .COM Download File  . . .  73
                  8.4  Receiving Binary Files (Downloading)  . . .  75
                  8.5  Viewing Files . . . . . . . . . . . . . . .  76
                  8.6  KERMIT File Transfer  . . . . . . . . . . .  76
                  8.7  Changing the Default Directory  . . . . . .  77

               Chapter 9  DIALING Frame                             79
                  9.1  Dialing Instructions  . . . . . . . . . . .  79
                  9.2  Saving SETUP Information  . . . . . . . . .  84
                  9.3  Dialing From the DOS Command Line . . . . .  85
                  9.4  The DIALER.DAT File . . . . . . . . . . . .  85
                     9.4.1  Creation . . . . . . . . . . . . . . .  85
                     9.4.2  Location . . . . . . . . . . . . . . .  86
                     9.4.3  Updating . . . . . . . . . . . . . . .  86
                  9.5  Error Messages  . . . . . . . . . . . . . .  86

               Chapter 10  MACRO Frame                              89
                  10.1  Instructions for MACRO . . . . . . . . . .  89
                     10.1.1  Defining Macro Keys . . . . . . . . .  90
                     10.1.2  Sending Macros  . . . . . . . . . . .  91
                  10.2  Downloading Macro Keys . . . . . . . . . .  93
                  10.3  The MACRO.DAT File . . . . . . . . . . . .  94
                     10.3.1  Creation  . . . . . . . . . . . . . .  94
                     10.3.2  Location  . . . . . . . . . . . . . .  94
                     10.3.3  Updating  . . . . . . . . . . . . . .  94
                  10.4  Error Messages . . . . . . . . . . . . . .  94

               Chapter 11  4014 Emulation                           97
                  11.1  4014 Options . . . . . . . . . . . . . . .  98
                  11.2  4014 Keyboard Mapping  . . . . . . . . . .  99
                     11.2.1  Regular Key Mapping . . . . . . . . .  99
                     11.2.2  Control Function Keys . . . . . . . . 100
                     11.2.3  ALT Keys  . . . . . . . . . . . . . . 101
                  11.3  4014 Error Messages  . . . . . . . . . . . 101

               Chapter 12  PC-VT Status Line                       103

               Chapter 13  Error Messages                          105

               Appendix A  VT100 Control Characters                109

               Appendix B  VT100 Received Escape Sequences         113

               Appendix C  VT100 Transmitted Escape Sequences      133

               Appendix D  VT100 Responses to Escape Sequences     137

               Appendix E  VT100 Special ALT Key Definitions       139

               Appendix F  4014 Received Character Processing      143
                  F.1  Alpha Mode  . . . . . . . . . . . . . . . . 143


                                          ii









                  F.2  Graph Mode  . . . . . . . . . . . . . . . . 145
                  F.3  Bypass/GIN Mode . . . . . . . . . . . . . . 149
                  F.4  LCE Mode  . . . . . . . . . . . . . . . . . 151

               Appendix G  4014 Received Escape Sequences          155

               Appendix H  4014 Responses to Escape Sequences      157

               Appendix I  4014 Special Shift, ALT and CTRL Key
                           Definitions                             160

               Appendix J  PC-VT Technical Details                 163
                  J.1  Details . . . . . . . . . . . . . . . . . . 163
                  J.2  HELP Customization  . . . . . . . . . . . . 168
                  J.3  Miscellaneous . . . . . . . . . . . . . . . 170
                  J.4  DESQview and TopView  . . . . . . . . . . . 172
                  J.5  PC-VT Private Escape Sequences  . . . . . . 174

               Appendix K  User-Supported Software                 185

               Index                                               189



































                                         iii