PCCOMM.DOC
				Version 1.1

	PCCOMM is an asynchronous communications program for the
   IBM-PC operating PC-DOS. It has the following features:

	1. Menu driven
	2. Interrupt operated in terminal mode
	3. Supports the Christensen protcol
	4. Optional H19 terminal emulation
        5. Online reconfiguration of communications parameters
	6. Optional local status line

	The initial configuration is determined from the values of
   the first few bytes in the program. DEBUG can be used to modify
   the parameters given below:


------------------                              ----------------------
Jump to Start -  |                              | Start -
    Don't Change |                              |    Don't Change
-----------------|                              |---------------------
                 |                              |
               -----                            -- 
     xxxx:0100 EB 0B F8 03 60 00 03-00 00 FF FF E8 7E 17 E8
                     ----- ----- -- -- -- -- --
-----------------------|     |   |   |  |  |  |  |----------------------------
Base Port -            |     |   |   |  |  |  |  | Local Status Line -
     F8 03 = COMM1     |     |   |   |  |  |  |  |         00 = Off
     F8 02 = COMM2     |     |   |   |  |  |  |  |         FF = On
------------------------     |   |   |  |  |  |  -----------------------------
-----------------------------|   |   |  |  |  |-------------------------------
Baud Rate -                  |   |   |  |  |  |    Backspace Conversion -
     80 01 =  300            |   |   |  |  |  |        00 = No Conversion
     60 00 = 1200            |   |   |  |  |  |        FF = Convert to Del/Rub
     0C 00 = 9600            |   |   |  |  |  |-------------------------------
-----------------------------|   |   |  |  |----------------------------------
---------------------------------|   |  |  |       Terminal type -
Word Length -                    |   |  |  |         00 = Glass Teletype
     02 = 7 bits                 |   |  |  |         FF = Heath/Zenith H19
     03 = 8 bits                 |   |  |  |----------------------------------
---------------------------------|   |  |-------------------------------------
-------------------------------------|  |	   Done -
Stop Bits -                          |  |            00 = None
     00 = One                        |  |            18 = Even
     04 = Two                        |  |            08 = Odd
-------------------------------------|  |--------------------------------------



												    				P. L. Kelley