PATSTACK - Stack Value Patching utility for SUPERK.COM

    There have been reports of strange things happening with SUPERK  when 
installed in various PC environments.  In order to keep the SuperK memory 
requirements  to  a  minimum,  I  have  set the Minimum and Maximum stack 
values at a bare minumum.  Testing has proven that this may very well  be 
the  cause  of the stange transfer results experienced by some users.  By 
providing a real time patching utility - as opposed to simply  increasing 
the  stack  values  -  you can experiment with different stack values and 
(hopefully) come up with the optimum compromise between  proper  transfer 
performance and memory requirements.  To this end, PATSTACK is being made 
available so that the user may patch the Minimum and Maximum stack values 
directly within SUPERK.COM. 

   You may also startup PATSTACK with two command line parameters:

                PATSTACK x y

       where x = the new Minimum Stack value 
             y = the new Maximum Stack value


    If  no  command line parameters are specified,  PATSTACK will display 
how the stack values are figured and what the current values are.  Simply 
enter the  new  values  and  PATSTACK  will  make  the  modifications  to 
SUPERK.COM.

    IN ALL CASES,  The Mimimum Stack value should be less than or equal to 
the Maximum Stack value. 

   It should be noted that SuperK memory requirements  will  increase  as 
the  values of the stack(s) increase and that the range of 512 to 2048 is 
checked prior to patching SUPERK.COM 

   PATSTACK will work on any version of SUPERK.COM