Termcap Compiler Version 1.01

	             Copyright (C) 1991 Rhys Weatherley

1. INTRODUCTION

The Termcap Compiler is a tool for creating new terminal emulations for use
with UW/PC (versions 2.00 and higher).  It takes source code in the form of an
abstract assembly code and compiles them into binary terminal descriptions that
UW/PC can use to provide new types of terminal emulations.  The standard UW/PC
terminal types are included as examples of the assembly code versions of the
terminal descriptions in the files VT52.CAP, ADM31.CAP and ANSI.CAP in the
source code archive UW-SRC.ZIP.

2. USING THE TERMCAP COMPILER.

The Termcap Compiler "TERMCC" accepts assembly code from the filename supplied
as an argument and writes the resultant compiled terminal description to the
supplied output file or a file with the same path and name as the input file,
but with a ".TRM" extension.  The full command syntax is:

	TERMCC infile[.CAP] [outfile[.TRM]]

3. USING NEW TERMINAL DESCRIPTIONS WITH UW/PC.

This section explains how you can add terminal descriptions you have written
and compiled to UW/PC so that it will use them during communications.  This
is also explained in "UW.DOC", but is repeated here for convenience.

In the configuration file "UW.CFG" for UW/PC the following configuration
options can be specified:

	emul (default adm31)

		The default terminal emulation type to use for windows.
		When a new window is created, it will use this emulation
		type.  This can be one of adm31, vt52, or ANSI or a string
		(e.g. "vt102"), signifying a currently loaded terminal
		description that will be searched for to become the
		default emulation.  The double quotes are optional.
		When the terminal description is searched for, case is
		ignored during compares.

	emul0 (defaults to whatever emul is set to)

		Set the terminal emulation type for protocol 0.  This is
		to rectify some problems with UNIX termcap entries that
		are missing the entry for ADM31 terminals, as discussed 
		above under "USING UW/PC".  It can be one of adm31, vt52
		or ansi or a string specifying a terminal type loaded
		with the "terminal" configuration option.

	terminal (no default)

		This can appear up to five times in the configuration file
		and each occurrence will load a terminal description into
		memory.  It's string value specifies a filename for a
		compiled terminal description.  The full pathname should be
		supplied.  For example, the following line could be added to
		the configuration file to add a "VT102" terminal emulation:

			terminal="c:\uw\vt102.trm"

		The standard VT52, ADM31 and ANSI terminal types can be
		replaced with new terminal descriptions by loading new
		files that have the VT52, ADM31 or ANSI terminal type
		specified.

4. THE ABSTRACT MACHINE.

UW/PC uses a small interpretive abstract machine to decode compiled terminal
descriptions on the fly while performing communications.  Its overhead is
small enough not to have a significant impact on the performance of UW/PC.
This abstract machine has a number of registers that can be accessed from
the assembly code described in the next section.

	accumulator	- This is the primary control register.  It holds
			  16 bit signed values.
	x register	- This is an auxillary register, primarily used for
			  cursor positioning during terminal emulation.  It
			  holds 16 bit signed values.
	y register	- This is an auxillary register, primarily used for
			  cursor positioning during terminal emulation.  It
			  holds 16 bit signed values.
	comparator	- After a comparison instruction, this register will
			  hold a value that is inspected during the conditional
			  jump instructions.  Its (16 bit) value cannot be
			  directly accessed.
	flags		- This is a 16 bit quantity that allows you to record
			  up to 16 single bit flags that may be useful for
			  recording such information as whether the terminal's
			  insertion mode is on or off, etc.
	saved x reg	- An auxillary register that can be used to save the
			  terminal's current X cursor co-ordinate.  It's value
			  cannot be directly accessed, except through the
			  "savexy", "restxy" and "getxy" instructions.
	saved y reg	- An auxillary register that can be used to save the
			  terminal's current Y cursor co-ordinate.  It's value
			  cannot be directly accessed, except through the
			  "savexy", "restxy" and "getxy" instructions.
	saved attribute	- An auxillary register that can be used to save the
			  terminal's current printing attribute.  It's value
			  cannot be directly accessed, except through the
			  "saveattr" and "restattr" instructions.
	argument array	- An array of eight 16-bit quantities that can be used
			  to store arguments to escape sequences for emulations
			  such as ANSI and VT102 which have variable numbers of
			  arguments for their escape sequences.
	number of args	- A 16-bit quantity that normally records how many
			  arguments are in the argument array.  It can also
			  be used as a loop counter.

5. ASSEMBLY INSTRUCTIONS.

This section describes the format of the assembly source file, and the various
instructions that can be used to create terminal descriptions.

The source file can contain comments that begin with "//" and continue to the
end of the line (like in C++), and it must begin with a "name" instruction,
although this is not checked by the compiler.  There is no fixed format for
the instructions except that labels cannot occur between an instruction's
name and its arguments.  Other than that, an instruction can appear in any
way with any amount of white space and comments surrounding its name and
arguments, and any number of instructions and labels can appear on the one
line or wrapped across lines.  Despite this, it is better to only place one
instruction on each line with an optional label preceding it, as shown in the
example terminal descriptions.

Labels consist of an alphanumeric identifier (that must not be an instruction
name) and a colon.  The two labels "start" and "keys" must be present in the
source file.  "start" indicates where the decoding for output to the terminal
screen begins, and "keys" indicates where the decoding of special keycodes
(for example terminal function keys) begins.  Without these labels, UW/PC
cannot process the terminal description properly.

There is one special escape sequence that EVERY terminal type MUST support:
"ESC |".  This will be used by UW/PC together with some of the upcoming
enhancements to UW/PC.  The handling for this escape sequence is to use
"getch" to retrieve the next character after the '|' and then to execute the
"client" instruction.  If a terminal description does not handle this escape
sequence in this way, then the special clients cannot be activated in
windows of that terminal type.

	add	- Adds the instruction's argument to the accumulator.
		  The argument can be numeric, "width" or "height".

	bell	- Ring the terminal bell.

	bs	- Move the cursor back one character.  The cursor will
		  not wrap around to the previous line if it is at the
		  start of the current line.

	bswrap	- Move the cursor back one character and wrap around to
		  the end of the previous line if necessary.  If the cursor
		  is in the top-left screen position, it won't be moved.

	clear	- Clear the entire screen to the current scrolling attribute.
		  The cursor is not moved from its current position.

	client	- This should be executed for the escape sequence ESC '|'.
		  UW/PC uses this for some of its specialised clients such
		  as the upcoming mail tool uwmail.

	clreol	- Clear to the end of the current line in the current
		  scrolling attribute.

	clreos	- Clear to the end of the screen from the current cursor
		  position in the current scrolling attribute.

	clrsol	- Clear to the start of the current line in the current
		  scrolling attribute.  The current cursor position is
		  not cleared.

	clrsos	- Clear to the start of the screen from the current
		  cursor position in the current scrolling attribute.
		  The current cursor position is not cleared.

	cmp	- Compares the instruction's argument to the accumulator.
		  The argument can be numeric, "width" or "height".  The
		  comparator will be set to reflect the result of the
		  comparison.

	cr	- Move the cursor to the start of the current line.

	dec	- Decrement the number of arguments and compare it with zero,
		  putting the result of the comparison into the comparator.

	delchar	- Delete the character at the current screen position,
		  moving all following characters left one place and
		  clearing the last position on the line in the current
		  scrolling attribute.

	delline	- Delete the current line and scroll the screen up.

	endkeys	- Marks the end of the key definition table.

	escape	- Unused at present - takes a numeric argument and specifies
		  and index to use in an "escape" table which isn't currently
		  implemented.  This is a convenient way to extend the
		  language without changing the TERMCC program - only the
		  main UW/PC program needs to be modified to recognise the
		  escape sequences.  It is suggested that you do not use
		  this because it may change in different versions of the
		  program, but is handy for "quick hacks".

	geta	- Gets an argument from the argument array.  This instruction's
		  first argument (1..8) specifies the argument to get and its
		  second argument specifies an 8-bit default value to use if
		  the argument in the argument array is not set.

	getarg	- Gets an argument from the remote host.  It is assumed to
		  be the ASCII representation of a number.  The number will
		  be placed into the next argument position and the
		  accumulator will return the character that follows the
		  number in the stream from the remote host.

	getch	- This instruction will wait until the next character is
		  received from the remote host, which it will place into
		  the accumulator, and then it will continue execution.

	getx	- Get the value of the X register and place it into the
		  accumulator.

	getxy	- Get the current cursor position and place it into the
		  X and Y registers.  This is mainly used to get a cursor
		  position prior to moving it about the screen.

	gety	- Get the value of the Y register and place it into the
		  accumulator.

        insblank - Insert a blank character without moving the cursor.

	inschar	- Insert the accumulator at the current screen position,
		  moving all present characters one position to the right.
		  If an insertion is performed at the right-most position,
		  then this instruction has the same effect as "send".

	insline	- Insert a new blank line before the current screen line.

	ja	- Jump to the label given as an argument if the result of
		  the last comparison using "cmp" was that the accumulator
		  was above (greater than) the comparison value.

	jae	- Jump to the label given as an argument if the result of
		  the last comparison using "cmp" was that the accumulator
		  was greater than or equal to the comparison value.

	jb	- Jump to the label given as an argument if the result of
		  the last comparison using "cmp" was that the accumulator
		  was below (less than) the comparison value.

	jbe	- Jump to the label given as an argument if the result of
		  the last comparison using "cmp" was that the accumulator
		  was less than or equal to the comparison value.

	je	- Jump to the label given as an argument if the result of
		  the last comparison using "cmp" was that the accumulator
		  was equal to the comparison value.

	jne	- Jump to the label given as an argument if the result of
		  the last comparison using "cmp" was that the accumulator
		  was not equal to the comparison value.

	jmp	- Jump unconditionally to the label given as an argument.

	jsr	- Jump to a subroutine at the label given as an argument.
		  Subroutines can only be nested up to 10 levels deep.  If
		  you go any deeper, it is not checked (for speed) and
		  strange things may occur.

	key	- Takes two arguments separated by a comma.  The first is
		  an IBM keyboard scan code indicating a key to be mapped
		  to the second argument which is a string of characters to
		  be sent to the remote host when that key is pressed.  Use
		  this to define the characters to send for arrow and function
		  keys in a terminal emulation.  It is assumed that the
		  label "keys" is followed by zero or more "key" instructions
		  and terminated with an "endkeys" instruction so that UW/PC
		  can find the key definitions.  No other instructions must
		  appear in the "keys" section otherwise strange things may
		  happen.

	load	- Loads the instruction's argument into the accumulator.
		  The argument can be numeric, "width" or "height".

	lf	- Move the cursor down one line on the screen, staying
		  in the same column.  At the bottom of the screen, the
		  screen is scrolled up one line.

	move	- Move the cursor to the position denoted by the X and Y
		  registers.  The screen origin is at (0,0).  If the
		  position is off-screen, the cursor is not moved.

	name	- Takes a string argument that specifies the name of the
		  terminal emulation.  This must be the first instruction
		  in the terminal description, but this is not checked.

	remote	- Send the value in the accumulator to the remote host.

	restattr - Restore the current printing attribute that was saved
		  by using "saveattr".

	resarr	- Resets the argument array.  All arguments will be marked
		  as "default value", the argument counter will be set
		  to zero, and the "shift" instruction value will be set
		  to zero.

	reset	- Takes a numeric argument which is a number between 0 and
		  15 that indicates a bit in the flags register to be reset.

	restxy	- Restore the current cursor position from the saved X and
		  Y registers.  The values may be saved by the "savexy"
		  instruction.

	ret	- Return from the current subroutine.  If you go up past
		  the first return address on the return stack then it
		  is not checked (for speed) and strange things may occur.

	saveattr - Save the current printing attribute so it can be later
		  restored using "restattr".

	savexy	- Save the current cursor position in the saved X and Y
		  registers.  The values may be restored by the "restxy"
		  instruction.

	scrldn	- Scroll the entire screen down one line, leaving the cursor
		  at its current position and filling the top line in
		  the scrolling attribute.

	scrlup	- Scroll the entire screen up one line, leaving the cursor
		  at its current position and filling the bottom line in
		  the scrolling attribute.

	send	- Send the accumulator to the screen.  When the cursor
		  reaches the right-hand side of the screen, it will
		  automatically wrap to the start of the next line, and
		  will scroll the screen as necessary.

	send52	- Send the accumulator to the screen.  When the cursor
		  reaches the right-hand side of the screen, it will
		  stay at that position until the next invocation of
		  "send" or "send52".  It got this name because this is
		  what the VT52 terminal type does.

	set	- Takes a numeric argument which is a number between 0 and
		  15 that indicates a bit in the flags register to be set.

	setattr	- Set the current printing attribute.  If a numeric
		  argument is supplied then the attribute is set from
		  the global attribute table (see below).  Otherwise,
		  the current accumulator value is used as the attribute.
		  The indexes into the global attribute table are:

		  	0 - Normal printing attribute.
			1 - Inverse printing attribute.
			2 - Highlighting attribute - usually "bold".
			3 - Normal attribute on the status line.
			4 - Highlighting attribute for the status line.

	setscrl	- Set the current scrolling attribute.  If a numeric
		  argument is supplied then the attribute is set from
		  the global attribute table (see above).  Otherwise,
		  the current accumulator value is used as the attribute.

	setc	- Set the number of arguments directly from the accumulator.
		  This is useful to use the number of arguments register as
		  a counter in loops, decrementing it with "dec" each time
		  through a loop.  The argument array is not modified, and
		  "geta" and "shift" can still be used to step through the
		  array to get the arguments.

	setx	- Places the value of the accumulator in the X register.

	sety	- Places the value of the accumulator in the Y register.

	shift	- Shift the arguments back one.  Using a "geta" instruction
		  after this instruction will get the "n + 1"th argument.
		  e.g. in "geta 1,1 shift geta 1,1", the second "geta"
		  instruction will get the argument following the first.
		  The "resarr" instruction will move everything back to the
		  start of the argument array.

	sub	- Subtracts the instruction's argument from the accumulator.
		  The argument can be numeric, "width" or "height".

	switch	- Extended comparison instruction that ends with "endsw".
		  Between "switch" and "endsw" are placed value and
		  jump label pairs.  For example:

			switch
			  0x00,start
			  '\r',crproc
			  '\n',lfproc
			  '\b',bsproc
			  '\t',tabproc
			  0x07,bellproc
			  0x1B,escproc
			endsw

		  The "switch" instruction will try to match each value
		  against the accumulator in turn, and will jump to the
		  associated label of the first matching value.  If no
		  values match, then execution will continue after the
		  "endsw" instruction.

	tab	- Move the cursor to the next tabstop.  Tabstops are
		  placed every 8 characters, and the cursor will wrap to
		  the start of the next line and will scroll the screen
		  as necessary.

	test	- Takes a numeric argument which is a number between 0 and
		  15 that indicates a bit in the flags register to be tested.
		  The comparator is set to a non-zero value if the flag bit
		  is set, and zero if it is reset.  The comparator can then
		  be tested with "je" (for reset) and "jne" (for set).

You should look at the standard VT52, ADM31 and ANSI terminal types that come
with the UW/PC source code for more information on how to write terminal
descriptions.  Please report any bugs or enhancements to the author.