.OP
		      Xmodem, CRC Xmodem, Wxmodem
			File Transfer Protocols

	  Please circulate this document anyway that you see
	  fit without alteration except on the page at the
	  end titled: "Notes and Comments".  It is requested
	  that anyone using these protocols within a commer-
	  cial product not charge for them as an option or
	  surcharge, but include XMODEM and its derivations
	  as part of the basic product.

					Peter Boswell
					June 20, 1986
					People/Link email: TOPPER
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 2
----------------------------------------------------------------------

			   TABLE OF CONTENTS


1.   PREFACE  . . . . . . . . . . . . . . . . . . . . . . . . . . .   3

2.   INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . . . .   5

3.   TERMINOLOGY  . . . . . . . . . . . . . . . . . . . . . . . . .   6

4.   XMODEM . . . . . . . . . . . . . . . . . . . . . . . . . . . .   7
     4.1. Xmodem Hardware Level Protocol  . . . . . . . . . . . . .   7
     4.2. Xmodem Initiation . . . . . . . . . . . . . . . . . . . .   7
     4.3. Xmodem Data Transmission  . . . . . . . . . . . . . . . .   8
     4.4. Xmodem Cancellation . . . . . . . . . . . . . . . . . . .   9
     4.5. Xmodem Error Recovery and Timing  . . . . . . . . . . . .   9

5.   CRC XMODEM . . . . . . . . . . . . . . . . . . . . . . . . . .  13
     5.1. CRC Calculation Rules . . . . . . . . . . . . . . . . . .  13
     5.2. CRC Xmodem Initiation . . . . . . . . . . . . . . . . . .  14

6.   WINDOWED XMODEM (WXMODEM)	. . . . . . . . . . . . . . . . . .  15
     6.2. Transparency and Flow Control Rules (Byte Level Rules)  .  16
     6.3. Initial Handshake Rules . . . . . . . . . . . . . . . . .  18
     6.4. Window Packet Transmission Rules  . . . . . . . . . . . .  18
     6.5. Notes for X.25 Hosts	. . . . . . . . . . . . . . . . . .  22

7.   APPENDIX A - CRC CALCULATION RULES . . . . . . . . . . . . . .  23
     7.1. IBM PC - 8088/8086 Data Structure . . . . . . . . . . . .  23
     7.2. BASIC Implementation of Bit Shift Method  . . . . . . . .  23
     7.3. BASIC Implementation of the Table Method  . . . . . . . .  26

8.   NOTES AND COMMENTS . . . . . . . . . . . . . . . . . . . . . .  28
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 3
----------------------------------------------------------------------

1.   PREFACE

In the years that have past since Xmodem was first developed as a file
transfer protocol, many thousands of people have been involved in
finding reasonable ways to move data via asynchronous telephone commun-
ications.  I appreciate the opportunity that I have had to meet and
learn from many of these people.  There is nothing in this document
that did not actually come from someone else.  Indeed, whether it is
WXMODEM, X.PC, Synchronous dial-up X.25, SNA, ZMODEM, Blast, Kermit or
any other protocol that becomes the dominant dial-up file transfer
protocol for personal and home computers is just not important.  What
is important is that the public domain have a high speed file transfer
protocol that is reasonably popular and  commonly available for many
types of personal computers, for bulletin boards and for services such
as People/Link, Delphi, CompuServe, GEnie and The Source.

Here are a few people that all of us should thank and I would espec-
ially like to recognize:

     Ward Christensen  Ward, a true pioneer in the microcomputer
     communications area, is the author of the original Checksum
     Xmodem protocol.  Thanks for reminding me to "keep it simple
     stupid".

     Chuck Forsberg  Chuck has edited perhaps the best work on
     Xmodem and has provided both YMODEM (1K Xmodem) and ZMODEM
     (Windowed YMODEM) to the public domain.  Thanks for showing
     me a protocol which would deal with the X-On/X-Off problem
     and reminding me that there is such a thing as a DLE char-
     acter.

     Richard (Scott) McGinnis  Scott is the architect, the moving
     force, for the People/Link software system.  His ideas,
     comments and encouragement have been wonderful.  Wait until
     you see his visual conference program for the IBM PC!
     Thanks for showing me how to use a DLE.

     Gene Plantz  Gene operates a major IBM PC bulletin board in
     the Chicago area and has been active in the National SYSOP
     Association.  Thanks for pushing me to do something about
     performance.

In a historical perspective, there seems to be a common pattern in all
computer systems development that can shed some light on where we stand
and how we got here.  The pattern is function first, then integrity and
finally performance.

Any kind of software must first do something worthwhile.  There is no
point in being error free, or inexpensive to operate if we do not want
the function.  Back in 1977, Ward Christensen had a need to move data
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 4
----------------------------------------------------------------------

between microcomputers.  Within a year it became obvious that the
function Xmodem provided met a real need to many microcomputer users.

Once we have a new function and we accept it, there is a normal desire
for the function to be correct.  No one can't count the times that new
software users have pointed out ... "that new function is super, but
the results are wrong".  The effort changes from providing new function
to providing integrity.  The development of CRC Xmodem is a clear
response to the integrity phase of a service as it reduced undetected
transmission errors by many orders of magnitude.

After the integrity has been accepted, people begin to look toward cost
and performance.  XMODEM entered this phase in 1984-1985.  Chuck
Forsberg's YMODEM is a major step in this effort providing larger
block sizes, batch mode and more.  His ZMODEM is a major step toward
making XMODEM derivative protocols work effectively with Public Data
Networks and most importantly, provides for restart of a file transfer
at the point of failure.  WXMODEM, presented here, is an alternate
solution to ZMODEM which is, hopefully, an easier solution to the most
important performance problems.

No one really knows where XMODEM and the file transfer function will go
in the coming years.  Perhaps X.PC from Tymnet, MNP from Microcom or
Synchronous X.25 will slowly push XMODEM, et. al, into history.  I
think this will happen, but not for maybe 5 to 10 years.  Perhaps when
50% of the households outgrow the Commodore 64, or when modem manufac-
turers can provide a $50 synchronous modem we will see the beginning of
the end for XMODEM, but not today.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 5
----------------------------------------------------------------------

2.   INTRODUCTION

XMODEM and its derivatives have become the primary method for file
transfer for personal computers.  Hopefully this document will help
people to understand these protocols and to implement them on their
own.  In particular, this document presents an additional XMODEM
derivation to the public domain: WXMODEM.

Why develop another file transfer protocol?

After working with bulletin boards, Public Data Networks such as Tymnet
and Telenet, and commercial host systems such as People/Link, Delphi,
CompuServe and others, a number of people came to believe that hobby-
ist, home and business users would benefit significantly from a new,
conceptually simple file transfer protocol which would provide improved
performance and fully support the public data networks such as Tymnet,
Telenet and Datapac.

But before WXMODEM can be presented, XMODEM and CRC XMODEM must be
described in detail.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 6
----------------------------------------------------------------------

3.   TERMINOLOGY

I've elected to use two special terms: transmitter and receiver.  The
transmitter is the computer/software which is transmitting data packets
and receiving acknowledgement characters.  The receiver is the com-
puter/software receiving the data packets and transmitting acknowledge-
ment characters.

Here is a table of special ASCII characters that are used throughout
this paper:

     Name      Decimal	      Hexadecimal    Description

     SOH	  01	       H001	     Start Of Header
     EOT	  04	       H004	     End Of Transmission
     ACK	  06	       H006	     Acknowledge (positive)
     DLE	  16	       H010	     Data Link Escape
     X-On (DC1)   17	       H011	     Transmit On
     X-Off(DC3)   19	       H013	     Transmit Off
     NAK	  21	       H015	     Negative Acknowledge
     SYN	  22	       H016	     Synchronous idle
     CAN	  24	       H018	     Cancel
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 7
----------------------------------------------------------------------

4.   XMODEM

Xmodem is a popular error recovery type protocol for transferring files
between computers via serial, asynchronous communications.   Before
learning more about Xmodem, it is important to hear what its author has
to say:

     "It was a quick hack I threw together, very unplanned (like
     everything I do), to satisfy a personal need to communicate
     with some other people.  ONLY the fact that it was done in
     8/77, and that I put it in the public domain immediately,
     made it become the standard that it is"....."People who
     suggest I make SIGNIFICANT changes to the protocol, such as
     'full duplex', 'multiple outstanding blocks', 'multiple
     destinations', etc etc don't understand that the incredible
     simplicity of the protocol is one of the reasons it survived
     to this day in as many machines and programs as it may be
     found in!"a

     4.1. Xmodem Hardware Level Protocol

     The protocol is Asynchronous, 8 data bits, no parity bit, one stop
     bit.  Modems which are commonly used are AT&T 103 (300 baud), AT&T
     212A (1200 baud) and CCITT V.22 (2400 baud).

     Typically, the data in a file is transmitted without change (if a
     7 bit machine, the left most, high order, bit is always zero)
     except that CP/M and MS/DOS operating systems want a ^Z (decimal
     26) to represent end-of-file.

     4.2. Xmodem Initiation

     Prior to entering the protocol, both the transmitting and receiv-
     ing computer must know where to get the data (what file is to be
     transmitted) and where to put the data (file to store the data or
     buffer area).  In Xmodem one side of the file transmission is
     always in charge (local computer), asking the other side (remote
     computer) to either transmit a file or to accept a file.  Through
     a dialog outside of Xmodem the local computer (your PC) first
     sends commands to the remote computer to select a file name
     to prepare to transmit or receive a file via XMODEM.  Once this is
     completed the remote computer enters the XMODEM protocol.	Now the
     local computer must be told what file to transmit or receive and
     it enters the XMODEM protocol, and hopefully data starts moving.


     a	  Ward Christensen, quoted from a message posted on CompuServe
	  in 1985.  Edited by Chuck Forsberg, "X/Ymodem Protocol
	  Reference", unpublished, 10/20/1985.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 8
----------------------------------------------------------------------

     Upon entering the Xmodem protocol, the transmitting computer waits
     between 10 seconds and a minute to receive an NAK character from
     the receiving computer.  The receiving computer is said to drive
     the protocol.  The transmitter may retry any number of times.  If
     any character other than a NAK or CAN is read by the transmitter,
     it is ignored.  The CAN character implies cancellation of the
     Xmodem file transfer and that the transmitter should leave the
     Xmodem protocol.  Once the receiver has sent a NAK, it will wait
     10 seconds for data to begin to arrive.  If none arrives in 10
     seconds, the receiver will send another NAK and continue to repeat
     10 times at which point the receiver will leave the Xmodem
     protocol (typically with a super cryptic error message such as
     "aborted", "NAK retry maximum exceeded").

     Transmitter			Receiver

     [wait for one minute]	   <	[NAK]

     [begin block transmission]    >

     4.3. Xmodem Data Transmission

     The transmitter takes the data, divides it into 128, 8 bit byte
     pieces and places it in an Xmodem Packet.

     The Xmodem Packet looks like this:

	  [SOH] [seq] [cmpl [seq] [128 data bytes] [csum]

	  SOH	    Start of header character (decimal 1).

	  seq	    one byte sequence number which starts at 1, and
		    increments by one until it reaches 255 and then
		    wraps around to zero.

	  cmpl seq  one byte 1's complement of seq.  This can be
		    calculated as cmpl = 255 - (255 and seq) or using
		    xor as cmpl = (255 and seq) xor 255.

	  data	    128, 8 bit bytes of data.  Note than when sending
		    CP/M and MS/DOS files a ^Z (decimal 26) must be
		    added to then end of the file.  If the last block
		    of data is less than 128 bytes, the Xmodem packet
		    must be padded with characters, usually ^Z's.

	  csum	    one byte sum of all of the data bytes where any
		    overflow or carry is discarded immediately.  For
		    example, if the first 3 bytes are 255, 5 and 6 the
		    checksum after the first 3 bytes will be 10.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 9
----------------------------------------------------------------------

     Once Xmodem Initiation has completed, the transmitter sends the
     first Xmodem packet and then waits.  After the receiver has the
     full packet, it will compare its own checksum calculation with the
     checksum that was sent by the transmitter.  If the checksums
     match, the receiver will send an ACK.  If the checksums are
     different, the receiver will send a NAK.

     After receiving an ACK the transmitter will send the next Xmodem
     packet.  If a NAK is received, the transmitter will resend the
     same XMODEM packet again.

     Once the transmitter has sent the last Xmodem packet and has
     received an ACK, the transmitter will send an EOT and then wait
     for a final ACK from the receiver before leaving the Xmodem
     protocol.	When the receiver sees an EOT instead of an SOH (the
     first character the next packet), the receiver transmits an ACK
     character, closes its files and leaves the Xmodem protocol.

     Let's look at a three block file transfer:

	  Transmitter				       Receiver

					<<<<<	       [NAK]
	  [SOH][001][255][...][csum]	>>>>>
					<<<<<	       [ACK]
	  [SOH][002][254][...][csum]	>>>>>
					<<<<<	       [ACK]
	  [SOH][003][253][...][csum]	>>>>>
					<<<<<	       [ACK]
	  [EOT] 			>>>>>
					<<<<<	       [ACK]

     Seems easy, right?  And it is, until something goes wrong.

     4.4. Xmodem Cancellation

     It has become a defacto standard that the receiver may cancel the
     file transfer by sending a CAN character and then leaving the
     protocol.	If the transmitter receives a CAN character when
     expecting either a NAK or ACK, the transmitter is to termin-
     ate and leave the protocol.  Likewise, if the receiver sees a CAN
     when expecting an SOH (start of packet) it should terminate the
     file transfer.  Many implementations now require two CAN char-
     acters before recognizing a cancel condition.

     4.5. Xmodem Error Recovery and Timing

     Error detection and recovery are the primary purposes of the
     Xmodem protocol.  The transmitter and receiver should continue to
     retry until 10 errors in a row have occurred.  Some of the common
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 10
----------------------------------------------------------------------

     error conditions are listed below:

	  4.5.1.    Complement Error

	  If the sequence number does not match the complement
	  sequence number, the packet must be discarded and a NAK
	  sent to the transmitter.

	  4.5.2.    Duplicate packet condition

	  If the sequence number is the same as the sequence
	  number of the last packet received, the packet should be
	  discarded and an ACK sent to the transmitter.

	  4.5.3.    Out of sequence error

	  If the sequence number matches the complement sequence
	  number and it is neither the expected sequence number
	  nor the last sequence number, the receiver should send
	  two CAN characters and leave the Xmodem protocol
	  (e. g. abort the file transfer).

	  4.5.4.    Receive timeout errors

	  When expecting data, if 10 seconds ever pass without
	  receipt of a character, the receiver should send another
	  NAK.	This should be repeated 10 times.  Some implement-
	  ations will timeout after 10 seconds waiting for the
	  first character of a packet, SOH, and then reduce the
	  timeout for characters in a packet.  The timeout should
	  not go below 5 seconds if the protocol is to be used
	  with public data networks.

	  4.5.5.    Transmit timeout errors

	  In the original protocol, the transmitter would wait 10
	  seconds for an ACK, NAK or CAN and then retransmit the
	  last Xmodem packet as if a NAK had been received.  Most
	  implementations either have the transmitter wait for a
	  very long time (30 seconds to a minute) and then
	  terminate the file transfer if an ACK, NAK or CAN has
	  not been receive or wait about 30 seconds and retransmit
	  the last packet.

	  4.5.6.    Packet synchronization errors

	  Since extraneous characters are frequently generated
	  when using asynchronous communications, the receiver
	  should not count on receiving exactly 132 characters for
	  each Xmodem packet.  One algorithm for re-synchroniz-
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 11
----------------------------------------------------------------------

	  ation goes as follows:

	       Assume that the checksum algorithm will cause re-trans-
	       mission of Xmodem packets which contain extraneous
	       characters.

	       If the character received when expecting the start of a
	       packet is not a SOH then ignore the character and
	       continue to search for a SOH.

	       Once a SOH is found, assume that the next two characters
	       will be a valid sequence number and complement.	If they
	       are complements then assume that the packet has begun.
	       If they are not complements, continue to search for a
	       SOH.

	       Send a NAK if a timeout occurs while attempting to
	       re-synchronize (e.g. continue to process timeouts as
	       described above).

	       If no re-synchronization occurs within 135 characters
	       then send a NAK character and retry receiving the
	       packet.

	  4.5.7.    False EOT condition

	  When the receiver sees an EOT (which was not sent by the
	  transmitter, but generated out of a communications error)
	  instead of a SOH character, the receiver assumes incorrectly
	  that the complete file has been transmitted.	This is
	  typically an unrecoverable error and it does occur especially
	  when the transmitting and receiving UARTs are clocked
	  slightly differently.  An algorithm to detect false EOT might
	  return a NAK for the first EOT received and only assume true
	  end of transmission after receiving two EOT's.

	       Transmitter		     Receiver

	       [last block .. ]    >>>>>
				   <<<<<     [ACK]
	       [EOT]		   >>>>>
				   <<<<<     [NAK]
	       [EOT]		   >>>>>
				   <<<<<     [ACK]

	  Just in case the transmitter was not prepared to resend the
	  EOT, it might be wise to set the timeout to about 3 seconds
	  and retransmit the NAK up to 3 times and then issue a warning
	  message but assume end of transmission.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 12
----------------------------------------------------------------------

	  4.5.8.    False CAN condition

	  Some Xmodem implementations will terminate on a single CAN
	  character.  Occasionally a CAN character will be generated by
	  a communications error and if this occurs and is seen by the
	  receiver between packets or is ever seen by the transmitter,
	  the file transfer will be incorrectly canceled.  Many
	  implementations now require two CAN characters in a row
	  before assuming that the file transfer is to be aborted.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 13
----------------------------------------------------------------------

5.   CRC XMODEM

CRC Xmodem is very similar to Checksum Xmodem.	The protocol initiation
has changed and the 8 bit checksum has been replaced by a 16 bit CRC.
Only theses changes are presented.

One of the earliest and most persistent problems with Xmodem were
transmission errors which were not caught by the checksum algorithm.
Assuming that there is no bias in asynchronous communications errors,
we would expect that 1 out of every 256 erroneous complete or oversized
Xmodem packets to have a valid checksum.  With the same assumption, if
the checksum were 16 bits, we would expect 1 out of every 65,536
erroneous complete or oversized packets would have a valid checksum.

     5.1. CRC Calculation Rules

     Considerable theoretical research has shown that a 16 bit cyclical
     redundancy check character (CRC/16) will detect a much higher
     percent of errors such that it would only allow 1 undetected
     bit in error for every 10^14 bits transmitted.  That's 1 un-
     detected error per 30 years of constant transmission at 1 mega-
     bit per second.  However, my personal experience indicates that
     something around 10^9 to 10^10 is more realistic.	Why such a vast
     improvement over the checksum algorithm?  It is caused by the
     unique properties that prime numbers have when being divided into
     integers.	Simply stated, if an integer is divided by a prime
     number, the remainder is unique.  The CRC/16 algorithm treats all
     1024 data bits in an Xmodem packet as an integer, multiples that
     integer by 2^16 and then divides that 1040 bit number by a 17 bit
     prime number.  The low order 16 bits of the remainder becomes the
     16 bit CRC.

     The 17 bit prime number in CRC Xmodem is 2^16 + 2^12 + 2^5 + 1 or
     65536 + 4096 + 32 + 1 = 69665.  So calculating the CRC is simple,
     just multiply the 128 byte data number by 65536, divide by 69665
     and the low order 16 bits of the remainder are the CRC.  The only
     problem is, I've never seen a computer which has instructions to
     support 130 byte integer arithmetic!  Fortunately for us, Seephan
     Satchell, Satchell Evaluations, published a specification a very
     efficient algorithm to calculate the CRC without either 130 byte
     arithmetic or bit manipulation.  Appendix A contains the source
     code, in IBM/PC BASIC, for the calculation of a CRC.

     Other methods of calculating CRC's for Xmodem involve bit level
     logic. a.


     a	  Chuck Forsberg, "X/Ymodem Protocol Reference", available on
	  many bulletin boards.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 14
----------------------------------------------------------------------

     5.2. CRC Xmodem Initiation

     The initiation of CRC Xmodem was designed to provide for automatic
     fall back to Checksum Xmodem if the transmitter does not support
     the CRC version.

     The receiver requests CRC Xmodem by sending the letter C (decimal
     67) instead of a NAK.  If the transmitter supports CRC Xmodem, it
     will begin transmission of the first Xmodem packet upon receipt of
     the C.  If the transmitter does not support CRC Xmodem, it will
     ignore the C.  The receiver should timeout after 3 seconds and
     repeat sending the C.  After 3 timeouts, the receiver should fall
     back to the checksum Xmodem protocol and send a NAK.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 15
----------------------------------------------------------------------

6.   WINDOWED XMODEM (WXMODEM)a

First, Xmodem provided the basic file transfer function, then CRC
Xmodem improved the data integrity, now we come to WXmodem which
provides better cost/performance.

     6.1. WXmodem Design Criteria

     A few people began discussing improvements to Xmodem with me in
     late 1985, over time we developed the following criteria:

	  6.1.1.    The protocol must be as similar as possible to the
		    XMODEM originally developed by Ward Christensen.
		    The popularity of XMODEM, I believe, is based on
		    its conceptual simplicity.	More software writers
		    are familiar with this protocol than any other.
		    More files are transferred everyday by this
		    protocol than any other asynchronous protocol.
		    Simplicity here implies a limited number of rules
		    for timing, error recovery and initiation.

	  6.1.2.    The protocol must overcome the propagation delay
		    that is characteristic of the public data net-
		    works.  While the cost of long distance communi-
		    cation is 50 to 90% less via the public data
		    networks than via the public voice networks, the
		    propagation delays inherent in public data networks
		    both reduces the cost savings and increases the
		    aggravation that occurs while watching a computer
		    slowly perform a file transfer.

	  6.1.3.    The protocol must overcome the flow control
		    problems which are characteristic in many public
		    data network situations.  Basically, in most
		    situations, the X-On and X-Off characters must
		    always be used for flow control and only for flow
		    control when using public data networks.

	  6.1.4.    The protocol should improve error recovery by
		    simplifying the manner in which a programmer can
		    determine the beginning of an XMODEM block.  Since
		    the Start of Header character (SOH) can appear in
		    the data or CRC, the programmer must use a rela-
		    tively sophisticated method to determine if a SOH
		    actually represents the beginning of a XMODEM
		    block.


     a	  This section assumes that the reader is already familiar with
	  Xmodem and CRC Xmodem presented above.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 16
----------------------------------------------------------------------


     6.2. Transparency and Flow Control Rules (Byte Level Rules)

     This protocol provides special public data network support for
     non-X.25 hosts and PC-Pursuit access to bulletin boards.  In order
     to accomplish this, the transmitter is not permitted to transmit
     the X-On and X-Off characters in the Xmodem packets.  The reason
     for this restriction is simple:

	  By the very nature of X.25 public data networks, without
	  flow control, buffer overruns and lost data are inevit-
	  able from time to time at any baud rate.

	  To avoid data loss public data networks must always
	  assume that any X-Off and X-On character is a flow
	  control character when supporting PC-Pursuit for
	  bulletin boards and when supporting non-X.25 host
	  systems.

     Since many non-X.25 hosts, bulletin boards and communications
     programs use X-On and X-Off as flow control characters, public
     data networks must support those X-Off and X-On requests at the
     point of connection where the X-Off is received by the public data
     network.  Otherwise, as many as several hundred characters backed
     up in the network would be transmitted by the public data network
     before the X-Off used for flow control reached the transmitter.
     The public data network has no way to know whether an X-On/X-Off
     protocol or Xmodem is operational at any point in time.  Therefore
     a Xmodem packet which contains an X-Off character and no succeed-
     ing X-On character will cause the public data network to stop
     forwarding the ACK or NAK.

     In addition, error recovery requires sophisticated programming for
     the receiver to determine the start of an XMODEM packet.  This
     protocol simplifies this task by dedicating a special character as
     an indicator that an XMODEM packet is about to begin.  The
     SYN (synch, decimal 22) character is used for this purpose.
     The presence of one or more SYN characters in a data stream always
     indicates that the next non SYN character is the beginning of an
     XMODEM packet (e.g. SOH).

     The method used here to handle these situations is through the
     insertion of the DLE character (H010, decimal 16, data link escape
     character) as an indicator that the character following the DLE is
     in fact a modified DLE, SYN, X-On, or X-Off character.

     Rules:

	  6.2.1.    Whenever an X-On, X-Off, SYN or DLE character is
		    about to be transmitted as any part of an actual
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 17
----------------------------------------------------------------------

		    XMODEM packet including the CRC, the transmitter
		    will transmit instead a DLE character followed by
		    the original character which has been modified by
		    exclusive or'ing it with 64 to its value. 1

	  6.2.2.    The inserted DLE characters are not counted in the
		    128 byte data length of the data portion of the
		    XMODEM packet.  Indeed, it would be possible to
		    have a packet which is physically 264 bytes in
		    length because the Xmodem block sequence number
		    (or its complement), all of the 128 data characters
		    and two CRC characters are all either X-On, X-Off,
		    SYN or DLE characters.

	  6.2.3.    Neither the DLE nor the adjusted characters are
		    used in the CRC calculation, rather the original
		    character is always used in the CRC calculation.


	  6.2.4.    When the receiver sees a DLE character, it does not
		    count it in the XMODEM block length calculation,
		    nor compute it in the CRC calculation but discards
		    it and then remembers to exclusive or the next
		    character with 64 and to verify that the result
		    character is either a DLE, SYN, X-On or X-Off (the
		    receiver will reject the packet unconditionally, if
		    not one of those four characters) and then include
		    the character as part of the packet.

	  6.2.5.    Prior to transmission of a XMODEM packet, the
		    transmitter will send one or more SYN characters
		    (recommend two) as a positive indicator to the
		    receiver of the beginning of a Xmodem packet.2

	  6.2.6.    Except for the character received after a DLE, the
		    receiver will test each incoming character to see
		    if it is a SYN character.  If it is, it will
		    discard the character and assume that the next
		    character will be another SYN or SOH.  If a SYN
		    character is received in the middle of a packet,
		    the receiver will NAK that packet.	The purpose of
		    the SYN character is to simplify recognition of the
		    beginning of a XMODEM packet by the receiver.  Once
		    an out of synch condition occurs on incoming
		    data, the receiver can just ignore every incoming
		    character until it sees a SYN.  Existing XMODEM
		    code which already properly deals with this
		    situation could just always discard any SYN
		    character at time of receipt with no further
		    action.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 18
----------------------------------------------------------------------


	  6.2.7.    The transmitter must support flow control char-
		    acters (X-On, and X-Off) during transmission of
		    packets.  Upon receipt of an X-Off it will wait 10
		    seconds for an X-On and will start transmission
		    again after 10 seconds or an X-On is received,
		    whichever occurs first.  Any extraneous X-On
		    characters received by the transmitter will be
		    ignored and discarded.  (Note that this does NOT
		    apply to X.25 host computers which use X.25 L2 and
		    L3 windows for flow control.)

     6.3. Initial Handshake Rules

     An initial handshake is provided to permit the receiver to
     indicate to the transmitter whether it can support checksum
Xmodem, CRC Xmodem, or Windowed Xmodem:

	  6.3.1.    WXMODEM - The receiver will send a character W
		    (decimal 87) and wait 3 seconds for the beginning
		    of a Xmodem packet.  This will be repeated 3 times
		    and then the receiver will drop down to CRC Xmodem.

	  6.3.2.    CRC XMODEM - The receiver will send a character C
		    (decimal 67) and wait 3 seconds for the beginning
		    of a Xmodem packet.  This will be repeated 3 times
		    and then the receiver will drop down to Checksum
		    Xmodem.

	  6.3.3.    Checksum XMODEM -  The receivers will send a NAK
		    and wait up to 3 seconds for the beginning of a
		    Xmodem packet.  This will be repeated 4 times and
		    if no valid SOH is received, the receiver will
		    abort the file transfer request.

     6.4. Window Packet Transmission Rules

     In order to overcome the propagation delays inherent with public
     data networks such as Tymnet, Telenet, Datapac, IPSS, Transpac and
     dozens more, the protocol must permit the transmitter to send more
     than one packet before receiving an acknowledgement from the
     receiver.	The number of packets that the transmitter will send
     before stopping transmission if an acknowledgement has not been
     received is called the "window".  WXmodem uses a window of 4
     packets for several reasons.  Most importantly, it uses a single
     set of timing rules which would deal reasonably well with a wide
     range of baud rates (that implied keeping the window fairly
     small).  Secondly, the window sequence number is directly related
     to the Xmodem packet sequence number which, hopefully, will
     simplify implementation of windowing.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 19
----------------------------------------------------------------------


     Rules:

	  6.4.1.    The window is always 4 Xmodem packets.  That is,
		    the transmitter will send 4 unacknowledged pack-
		    ets.  Transmission will not cease and the time out
		    interval will not begin until 4 unacknowledged
		    packets have been transmitted.  Note that the
		    window may be less than 4 Xmodem packets for short
		    files or at end-of-file.

	  6.4.2.    The receiver will transmit acknowledgements in the
		    form:

			 ACK[sequence]

		    The [sequence] field is an 8 bit number where the
		    high order or most significant 6 bits are always
		    zero and the low order or least significant 2 bits
		    are always the same as the low order 2 bits of the
		    XMODEM block sequence number of the XMODEM packet
		    being acknowledged (value in decimal may range
		    from 0 to 3).

	  6.4.3.    The receiver does not have to acknowledge every
		    packet, but must acknowledge at minimum every
		    fourth packet.  The transmitter will accept one
		    ACK[sequence] for multiple XMODEM packets.	For
		    example, after an unknown number of packets:

		    Transmitter 			    Receiver

		    ....
		    ....
		    ....
		    [Block Sequence Number H0FE]
		    [Block Sequence Number H0FF]	    ACK[H002]
		    [Block Sequence Number H000]	    ACK[H003]
		    [Block Sequence Number H001]
		    [Block Sequence Number H002]	    ACK[H001]
		    .....

		    Since some transmitters must close the window and
		    cease all communications before doing disk I/O to
		    read more data, it is suggested that acknowledge-
		    ments be sent for every packet (except when the
		    receiver can easily determine that another packet
		    is already being received at the point in time that
		    the ACK[sequence] is about to be sent).3
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 20
----------------------------------------------------------------------

	  6.4.4.    The receiver will reject a packet (request re-
		    transmission) by sending:

			 NAK[sequence]

		    Where [sequence] is then next window sequence
		    number (between H000 and H003) after the [sequence]
		    of the last good block.  The receiver will discard
		    up to 3 Xmodem packets received after the NAK is
		    transmitted until it receives the packet with the
		    sequence number that had previously been nak'ed by
		    the receiver.  The receiver will not send a second
		    NAK until another packet with the same sequence
		    number is received which is also invalid or a
		    timeout has occurred.

	  6.4.5.    When the transmitter receives a NAK[sequence], it
		    will complete transmission of any XMODEM block
		    currently being transmitted and then begin re-
		    transmission starting with the block which was
		    nak'ed.

	  6.4.6.    The receiver will discard duplicate packets but
		    count them in the window for purposes of deter-
		    mining the maximum receive window without an ACK in
		    response.  For example, if the receiver gets packet
		    sequence number 127 four times in a row, it must
		    send an ACK H003 even if the receiver has previous-
		    ly acked that block.

	  6.4.7.    The timeout intervals at various points in process-
		    ing are:

		    Waiting for a character on receive, start of packet
		    not yet recognized:      15 seconds

		    Waiting for a character on receive, start of packet
		    has been recognized:     15 seconds

		    Waiting for an Ack or Nak on transmit side after
		    the window has closed:   15 seconds4

		    Waiting for an X-On after receipt of an X-Off by
		    the transmitter:	     10 seconds

	  6.4.8.    When the transmitter times out waiting for an ACK
		    or NAK when the window is closed (e.g. four blocks
		    have been transmitted), the transmitter will
		    retransmit the last block transmitted and wait
		    again.  Only after 10 consecutive timeouts have
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 21
----------------------------------------------------------------------

		    occurred will the transmitter cancel the trans-
		    mission.

	  6.4.9.    Where possible, it is recommended that the receiver
		    return an ACK[sequence] for every packet or at
		    least 50% of the Xmodem packets.  When the receiver
		    must wait for the window to close (e.g. receive 4
		    Xmodem packets without an acknowledgement),
		    some performance benefit will be lost.

     If the receiver cannot overlap disk I/O and communications
     I/O, the receiver can temporarily stop transmission by either:

	  "Closing the window" (e.g. receiving 4 blocks without sending
	  an ACK[sequence]) performing the disk I/O and then sending an
	  ACK[sequence].

	  Transmitting an X-Off followed by an X-On when the receiver
	  is ready to resume accepting data.  Note that the receiver
	  should be prepared to accept data for about a 1/4 of a second
	  after the X-Off is sent to cover situations where satellite
	  propagation delay may occur.	One possible implementation
	  would let the computer user set the "X-Off delay time" so
	  that in the normal case the X-Off delay could be set to 25
	  milleseconds.  A sophisticated implementation might set the
	  initial X-Off delay at 250 milleseconds and then reduce it
	  based on experience during the file transfer.

	  Each approach has its advantages, but the X-Off approach will
	  provide the best performance in most cases especially when
	  using a public data network.	Note, however, that some
	  computers, notably the Commodore 64 and the IBM PC Jr cannot
	  receive communications data while writing to disk.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 22
----------------------------------------------------------------------

     6.5. Notes for X.25 Hosts

     Host computer systems which utilize the X.25 protocol
     (examples: People/Link, Delphi, CompuServe, The Source) to
     interface with the various public data networks may send special
     control packets which change the manner in which the network will
     communicate with the remote personal computer, bulletin board or
     terminal.	For the purposes of this paper, it is assumed that the
     X.25 host can already support CRC and/or Checksum Xmodem and
     present only the changes for WXMODEM.

	  6.5.1.    When an X.25 Host is the transmitter, it must be
		    sure to set the distant X.3 PAD parameters to
		    assure that the receiver can use X-Off/X-On for
		    flow control.  This is accomplished by sending a
		    Q-Bit command packet to set X.3 parameter 12 to a 1
		    prior to the initial handshake.  Note that if the
		    receiver cannot support WXMODEM, the X.25 Host must
		    send the appropriate Q-Bit packet to reset para-
		    meter 12 to a 0 before transmitting the first CRC
		    or Checksum Xmodem packet.

	  6.5.2.    When an X.25 Host is the receiver and in WXMODEM
		    mode, it must be sure to set the distant X.3 PAD
		    parameters to assure that the network will use
		    X-Off/X-On for flow control between the network and
		    the transmitter to prevent its buffers from
		    overflowing.  This is accomplished by sending a
		    Q-Bit command packet to set X.3 parameter 5 to a 1
		    prior to the initial handshake.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 23
----------------------------------------------------------------------

7.   APPENDIX A - CRC CALCULATION RULES

The purpose of this appendix is to give non-technical and non mathema-
tical software writers a cook book approach to calculating the CRC-16
used in Xmodem.  We have half accomplished that goal.  The BASIC code
in the examples below has been tested on an IBM PC and found to work
effectively even at 9600 with compiled Basic.  Some BASIC languages do
not offer an XOR function and others do not have MKI$ and CVI functions
which simplified the movement of data between data types.  Someday we
hope to provide a Commodore C-64/C-128 implementation which simulates
XOR, but not today!

My thanks go to Chuck Forsberg, Joe Noonan, John Byrns and Stephen
Satchell.  Without their help and public domain documents, this would
have never been possible.

     7.1. IBM PC - 8088/8086 Data Structure

     The Intel 8080 and upward has a feature, convenient only to some
     electrical engineer somewhere, which places 2 byte (16) bit
     integers in BYTE REVERSE order in memory.	That is, the least
     significant byte is placed in memory before the most significant
     byte for integer operations.  If A$ is one byte containing the
     number 52 and it is assigned to I% using the ASC function, the
     binary value (52) ends up in the first byte of I% and the second
     byte is zero.
			      Result

	  I%=0		      [x'0000']
	  I%=1		      [x'0100']
	  A$="A"	      [x'41']
	  I%=ASC(A$)	      [x'4100']
	  B$=MKI$(I%)	      [x'4100']  letter "A" then binary zero
	  I%=CVI(CHR$(0)+A$)  [x'0041']
	  A$=CHR$(65)	      [x'41']

     Once this is understood, many problems with these algorithms goes
     away.

     7.2. BASIC Implementation of Bit Shift Method

     The bit shift method here was converted from the "C" logic
     presented in Chuck Forsberg's "Xmodem/Ymodem" protocol reference
     and from an old IBM two page reference guide that Joe Noonan
     carries with him in his appointment calendar!
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 24
----------------------------------------------------------------------


     Chucks' "C" code:

/*
 * This function calculates the CRC used by the XMODEM/CRC Protocol
 * The first argument is a pointer to the message block.
 * The second argument is the number of bytes in the message block.
 * The function returns an integer which contains the CRC.
 * The low order 16 bits are the coefficients of the CRC.
 */
int calcrc(ptr, count)
char *ptr;
int count;
{
    int crc, i;

    crc = 0;
    while (--count >= 0) {
     crc = crc ^ (int)*ptr++ << 8;
     for (i = 0; i < 8; ++i)
	 if (crc & 0x8000)
	  crc = crc << 1 ^ 0x1021;
	 else
	  crc = crc << 1;
     }
    return (crc & 0xFFFF);
}
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 25
----------------------------------------------------------------------


     But in IBM PC BASIC, our implementation looks like:

100 DEFINT A-Z 'DEFAULT IS TWO BYTE INTEGERS
2000 REM * V$ CONTAINS 133 CHARACTER COMPLETE XMODEM PACKET
2010 REM * CRC$ IS TWO BYTE CRC WITH MOST SIGNIFICANT BYTE FIRST
2020 CRC$=CHR$(0)+CHR$(0)		       'START AT ZERO
2030 FOR I2=4 TO 131
2040   A$=MID$(V$,I2,1)
2050   GOSUB 4000
2060 NEXT I2
2070 REM * CRC$ CONTAINS CALCULATED CRC!

3000 IF CRC$=MID$(V$,132,2) THEN ....	 'IT'S GOOD!!!

4000 REM * CRC BITWISE CALCULATION (WHAT A JOKE!)
4010 CRCH1=ASC(LEFT$(CRC$,1)) XOR ASC(A$)
4020 CRCL1=ASC(RIGHT$(CRC$,1))
4030 FOR I3 = 0 TO 7
4040   CARRY=0 : IF CRCH1 > 127 THEN CARRY=-1  'IS HIGH BIT ON IN CRC?
4050   CRCH1=(CRCH1*2) AND 255		       'CRCH << 1 AND 255
4060   IF CRCL1>127 THEN CRCH1=CRCH1+1 'IF CRCL CARRIES THEN INCR CRCH
4070   CRCL1=(CRCL1*2) AND 255		       'CRCL << 1 AND 255
4080   IF CARRY=0 THEN GOTO 4105	       'IF HIGH BIT WAS ON,
4090   CRCH1=CRCH1 XOR 16		       'XOR WITH &H1021
4100   CRCL1=CRCL1 XOR 33
4110 NEXT I3
4130 CRC$=CHR$(CRCH1)+CHR$(CRCL1)
4140 RETURN 'WHEW


     That routine will execute 128 * 7 + 128 * 9 * 8 BASIC statements
     for each Xmodem packet or 10112 statements per Xmodem packet!  It
     will work for low baud rates in compiled BASIC, but just is too
     much for interpretive BASIC.
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 26
----------------------------------------------------------------------

     7.3. BASIC Implementation of the Table Method

     This method is based on routine M4 in Steven Satchell's paper,
     "Test of CRC Routines for CRC-CCITT", but has some very signifi-
     cant differences.	A table of 256 CRC's, originally calculated
     with the bit shift method is used to avoid performing the bit
     shift during communications.  The table contains the CRC's for
     each byte value from 0 to 255 when the original CRC is zero.  The
     result of this calculation is included in the DATA statements in
     the code.

     The comments are intended to show what is logically happening
     rather than physically.  Because of the "byte reverse" nature of
     integers in the 8088, a logical shift of 8 bits to the left is a
     physical shift of eight bits to the right!


200 DEFINT A-Z	'ALL INTEGERS
210 DIM CRCTB(256)

300 GOSUB 9000 'INITIALIZE CRC TABLES

6200 REM * CRC CALCULATION USING TABLE METHOD, V$=XMODEM PACKET
6210 CRC$=CHR$(0)+CHR$(0)		  'INITIALIZE TO ZERO
6220 FOR Q=4 TO 131
6230   CRCH1=ASC(LEFT$(CRC$,1)) 	  'CRC >> 8 AND 255
6240   CRCL2=CVI(CHR$(0)+RIGHT$(CRC$,1))  'CRC << 8 AND 255
6250   CRC1$=MKI$(CRCTB(CRCH1 XOR ASC(MID$(V$,Q,1))) XOR CRCL2)
6260   CRC$=RIGHT$(CRC1$,1)+LEFT$(CRC1$,1) 'SET IT BACK!
6270 NEXT Q
6280 IF CRC$ <> MID$(V$,N,2) THEN ....... 'GOTO ERROR ROUTINE
6290 REM * END OF CRC CALC

9000 FOR I%=0 TO 255 ' INITIALIZE CRC TABLE
9010   READ CRCTB(I%)
9020 NEXT I%
9025 RETURN
9030 DATA 0, 4129, 8258, 12387, 16516, 20645, 24774, 28903
9040 DATA -32504,-28375,-24246,-20117,-15988,-11859,-7730,-3601
9050 DATA 4657, 528, 12915, 8786, 21173, 17044, 29431, 25302
9060 DATA -27847,-31976,-19589,-23718,-11331,-15460,-3073,-7202
9070 DATA 9314, 13379, 1056, 5121, 25830, 29895, 17572, 21637
9080 DATA -23190,-19125,-31448,-27383,-6674,-2609,-14932,-10867
9090 DATA 13907, 9842, 5649, 1584, 30423, 26358, 22165, 18100
9100 DATA -18597,-22662,-26855,-30920,-2081,-6146,-10339,-14404
9110 DATA 18628, 22757, 26758, 30887, 2112, 6241, 10242, 14371
9120 DATA -13876,-9747,-5746,-1617,-30392,-26263,-22262,-18133
9130 DATA 23285, 19156, 31415, 27286, 6769, 2640, 14899, 10770
9140 DATA -9219,-13348,-1089,-5218,-25735,-29864,-17605,-21734
9150 DATA 27814, 31879, 19684, 23749, 11298, 15363, 3168, 7233
.PA
	  Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 27
----------------------------------------------------------------------

9160 DATA -4690,-625,-12820,-8755,-21206,-17141,-29336,-25271
9170 DATA 32407, 28342, 24277, 20212, 15891, 11826, 7761, 3696
9180 DATA -97,-4162,-8227,-12292,-16613,-20678,-24743,-28808
9190 DATA -28280,-32343,-20022,-24085,-12020,-16083,-3762,-7825
9200 DATA 4224, 161, 12482, 8419, 20484, 16421, 28742, 24679
9210 DATA -31815,-27752,-23557,-19494,-15555,-11492,-7297,-3234
9300 DATA 689, 4752, 8947, 13010, 16949, 21012, 25207, 29270
9310 DATA -18966,-23093,-27224,-31351,-2706,-6833,-10964,-15091
9320 DATA 13538, 9411, 5280, 1153, 29798, 25671, 21540, 17413
9330 DATA -22565,-18438,-30823,-26696,-6305,-2178,-14563,-10436
9340 DATA 9939, 14066, 1681, 5808, 26199, 30326, 17941, 22068
9350 DATA -9908,-13971,-1778,-5841,-26168,-30231,-18038,-22101
9360 DATA 22596, 18533, 30726, 26663, 6336, 2273, 14466, 10403
9370 DATA -13443,-9380,-5313,-1250,-29703,-25640,-21573,-17510
9380 DATA 19061, 23124, 27191, 31254, 2801, 6864, 10931, 14994
9390 DATA -722,-4849,-8852,-12979,-16982,-21109,-25112,-29239
9400 DATA 31782, 27655, 23652, 19525, 15522, 11395, 7392, 3265
9410 DATA -4321,-194,-12451,-8324,-20581,-16454,-28711,-24584
9420 DATA 28183, 32310, 20053, 24180, 11923, 16050, 3793, 7920


     This method uses 128 * 6 BASIC statements per Xmodem packet or a
     miserly 768 BASIC statements per packet.  And, if you want, the
     code can be tightened still more.	Unfortunately, any further
     tightening that we could see would eliminate most of the already
     limited readability of the code.
.PA
Xmodem, CRC Xmodem, WXmodem
June 20, 1986						      Page 28
----------------------------------------------------------------------

8.   NOTES AND COMMENTS

Please add your notes and comments here or send them to me and I'll get
them added to the current copy on People/Link.

1.   This was originally set up to ADD 32 to the character on transmit
     and SUBTRACT 32 on receive.  By using exclusive or with 64, the
     logic is the same on transmit and receive.

2.   The use of the SYN character was added at the request of several
     people who have coded Xmodem routines and have struggled valiantly
     to improve their error recovery routines.	Peter Boswell 6/10/86

3.   The suggestion that ACK[sequence] be sent for every block received
     was added. 	 Peter Boswell	     6/10/86

4.   The original value for the ACK/NAK timeout was 10 seconds.  This
     was changed to 15 seconds the situation where the receiver is
     operating at 300 baud and using X-Off to stop receipt of characters
     during disk I/O.  Peter Boswell, 6/10/86