Zmodem            Technical Reference Manual          Page 1

                                    Zmodem

         Zmodem   has  a built in communications manager  and  doesn't
         need  any  type of fossil, in fact you should make  sure  you
         turn  the  fossil  OFF if running it on a  BBS  that  uses  a
         fossil.

         Zmodem requires a number of command line switches:
                              -B, -P, {-R or -F}
         -@<filename>, Can be a text file listing the files to  Send.
                        One  filename  per line, unlimited  number  of
                        lines. This is to used in place of -F.
         -B<Baud Rate>
         -P<Port Number>
         -L<Serial Lock Rate>
         -R Receive files
         -UDrive:path,  directs that all files  received  should  be
                          stored on this drive and in this  directory.
                          This  switch  is primaryly  for  NON-OSIRIS,
                          NON-QT  systems. Osiris takes care  of  this
                          internally  and  this switch should  NOT  be
                          used.

         Example: -UC:\uploads
                  -UD:\files\temp
                  -UD:

         Do NOT end the path with a backslash "\"

         Illegal -U settings would be C:\
                                      C:\uploads\
                                      D:\files\temp\

         -F <Filenames>
         -K Keep interrupted transfers (Do not use if running on a BBS)
         -Nx, with x being the node number in use. For use on Osiris
               CBIS  systems only.  Zmodem will show the name  of  the
               caller as well as where he's from if this switch is used.

         -B,  supported baud rates 300 - 115,200 Baud.
              NOTE:  If  no -B switch is given, Zmodem  will  use  the
              current  baud  rate the serial port is set to.  This  is
              primaryly  a debugging aid. If you leave off the -B  and
              you are running a LOCKED serial port (high speed  modem)
              your  estimated  transfer  times,  cps,  and  efficiency
              ratings will be off.
         -S,  Handskaking Slow. Should ONLY be used if you are running
              a highspeed modem WITHOUT a 16550 Uart.
         -P,  Supported  Com  Ports, COM 1, COM  2, COM 3, and COM 4.
         -L,  Supported Locked Baud Rates, 300 - 115200 Baud.
         -F,  As  many as DOS allows. Full drive, path,  and  filename
              supported.


         Zmodem            Technical Reference Manual          Page 2

                   NOTE:   -R  -@ or -F  MUST be  the   last
                   parameter on the command line. As soon as
                   Zmodem encounters either one of these two
                   switches, it will begin to either Receive
                   or Send.


         Sample Osiris Command line (protocol control file)

         Send : -N*N -B*B -P*P -@*U
         RCV  : -N*N -B*B -P*P -R

         QT 2000 (protocol control file definitions)

         Send : -B*B -P*P -F *F
         RCV  : -K -B*B -P*P -R


                            Items to watch out for

         Zmodem  has it's own built in commucation driver.  Having  an
         ACTIVE   fossil  may  cause  system  lockups,  sessions   not
         starting,  and  other possiblities. Make sure  you  have  the
         fossil turned off if your running one.






























          Zmodem            Technical Reference Manual         Page  3

         Zmodem  may be freely used by Osiris Owners.  If you do NOT
         own Osiris, Zmodem must be purchased.

         The price is 15 dollars (US Currency).

                                   Mail to :
                              Micro TECH Systems
                             555 North Spring, #39
                           Cape Girardeau Mo. 63701

                               Revision History
                                   ver 8.10
         Added -S, Handshaking Slow. This causes RTS to DROP during
         disk writes. This should only be used *IF* you are running a
         high speed modem WITHOUT a 16550 Uart. Try running without the
         -S first, if you have a fast computer and you are not running
         a multi-tasker or on a Network, you may be able to slide by.

         The CORRECT solution is to install a 16550 Uart, priced at
         20.00's. If you're computer has the uart soldered to the
         mother board you will need to get a second serial card and
         install the 16550 on it. ver 8.00

         Added  the  ability to leave off the -B  switch  setting  for
         debugging purposes.
                                   ver 7.00

         Drastic  Speed  up in program speed. You may not  notice  any
         increase in transfer speed unless you happen to be running  a
         slower  computer attempting to push a highspeed modem  locked
         at 38400. Or running a multi-tasker such as Desqview.

                                   ver 6.00

         Command line switches and their respective values no longer
         have a space between the switch and the value.

         Old Method : -N *N -B *B -P *P -F *F
         New Method : -N*N -B*B -P*P -F *F

         Scrolling Batch effeciency window added.

                                   ver 4.00
         New display screen like the one in Tmodem.

         Only  Zmodem drivers  that support this feature will supply
         batch information. Zmodem.exe and DSZ are the only two that
         I know of  at this moment  that do. If  the sender  doesn't
         support batch information, the display will remain blank.

         Added EFFx.LOG for Osiris Systems.
          Zmodem            Technical Reference Manual         Page  4

                                   ver 3.00

         Allowing  Zmodem to be used on non-Osiris systems.

         If  OSIRIS=  is not set, Zmodem will assume an alien  BBS  or
         Terminal  program  and  switch  to  NON-COMPORT.DAT   status.
         Meaning  it'll  used the standard com  port  definitions  for
         COM1,  2, 3, and 4. Baring in mind that 3 and 4 have no  real
         standard.