BRKBOX    by     Tim Burmeister

V1.1 fixed snow when using IBM color card
     detects monochrome monitor automatically and changes display to all white
     removed time out error indicator - replaced with transmit indicator
     can use on second serial port

                              SYNTAX


BRKBOX       -for com1 will display graphic screen if you have a color monitor
BRKBOX=      -for com1 no graphic screen (good for batch files)
BRKBOX 2     -for com2 will display graphic screen if you have a color monitor
BRKBOX=2     -for com2 no graphic screen (good for batch files)

(if you have a monodisplay the graphics intro is not displayed)

                              ERROR BEEPS

STEADY TONE  error in the parameters you gave it
PULSED TONE  program is already installed

                              NOTES
Uses interupt 1C
uses less than 1k memory
writes screen only during vertical retrace
If the com port has not been initialized you wont see any display
              NO DISPLAY ????
Try putting your modem in ALB or if you dont have com2 port type brkbox 2 
and you will see the display (although it wont mean anything)


This program will display in the upper right hand side of display
the active (SPACE, CONTROL ON, POSITIVE VOLTAGE) RS232 signals. The DTE
generated signals are displayed in red, the DCE in green, also uart errors
are shown in white. ***** NOTE if you have a mono display everything is white

                      DISPLAY DEFINTIONS
TXD	TRANSMIT DATA
FRM    FRAMING ERROR
PAR	PARITY ERROR
OVR	OVERRUN ERROR
CD	Recieve Line Signal Detected --CARRIER DETECTED
RNG	RING INDICATOR
DSR	DATASET READY
CTS	CLEAR TO SEND
DTR	DATA TERMINAL READY
RTS	REQUEST TO SEND

This program installs itself in memory and the display can be toggled off and
on by depressing the ALT AND LEFT HAND SHIFT KEYS simultaeneously.

The display is turned on initialy (if you dont see anything put your modem
into analog or local loopback). Since this routine is active only about 18 
times per second it will not catch all error conditions that may occur
during a normal communications session.

IT HAS BEEN KNOWN TO CAUSE INTERFERENCE WITH COM PROGRAMS AT 9600 BAUD

   **********************************************************************
If the display is active while accessing a HALF-HEIGHT floppy drive
it causes data errors. If so toggle the display off while accessing
the floppy.If anyone has any info about this I would appreciate hearing from you.


I would like to hear your comments and suggesstions

                               Tim Burmeister