Comset Version 6.0 Documentation (c) 1989 Hank Volpe Computers

                  ___________________________________________    
    
                                  C O M S E T
    
                           Modem / Uart Setup Program
    
                        Version 6.0..release date 10/8/89
    
                       from Hank Volpe Computers (c) 1989
    
                  ___________________________________________
    
    
                                  Introduction
    
    Comset is a utility that is designed to setup a communications port 
    and a AT (Hayes) Compatible smartmodem. Many modems, especially 
    internals, do not have a method to reset the modem when it is 
    activated, nor does an adequate method exist to setup the serial port
    for use. 
    
    Comset will setup your serial port to any speed from 300 to 19200 bps 
    and then check to see if your modem is on-line. If it isn't, Comset 
    will perform a hardware reset to "wake" it up. Next a software reset 
    is performed by sending the command ATZ. If the reply OK is received, 
    you are informed that the modem is fine. If OK is not received, Comset 
    will attempt 3 times to reset the modem before informing you of an 
    error. If you have an external modem and it is off, Comset will abort 
    after setting up the serial port to the desired baud rate.
    
    
             Some of the features of Comset include the following ;
                      Level 1 options...Shareware Version
    
           ** User Selected baud rates from 300 to 19200 bps.
           ** User Selected Comm port assignments.
           ** Modem Status register testing.
           ** Redirectable output..can be sent to a file for logging.
              or used over any serial link.
           ** RTS/CTS DTR/DSR Handshake testing.
           ** Ability to setup the UART alone for dumb modems or
              other serial devices up to 19.2K Baud !!NEW !!

             Registered Users Have the following advanced features;

          ** User Selection of Comm ports 1 2 3 4.
          ** Log in of Comm ports 3 & 4 to DOS for use by other programs
             such as high level languages or applications.
          ** Batch file parameter passing and error reporting.
          ** Ability to send custom Hayes command strings to the modem
             using a simple ASCII text file !!NEW!! 






                                1

Comset Version 6.0 Documentation (c) 1989 Hank Volpe Computers
    
    
    
                                I. USING COMSET
                                ----------------
    
                    The usage syntax for Comset is simple. 
    
                             COMSET [speed] [port] U
                                       or
                             COMSET [speed] [port]
                                       or
                                    COMSET h
    
                      [speed] and [port] are user options
                      u tells Comset to set the UART only
                      h invokes runtime help for the user
    
    Comset is easy to use. Typing COMSET from the dos prompt will 
    automatically attempt to set up serial port COM1 to 2400 bps and 
    attempt to wake up its modem. Selecting a different speed involves
    only adding the speed after the word Comset...ie COMSET 1200 sets 
    serial port COM1 to 1200 bps instead of the default 2400. Trailing 
    zeros are not necessary, so you could also type COMSET 12 to set up 
    serial port COM1 to 1200 bps. If you wish to use a different serial 
    port, add that after the speed...ie COMSET 24 2 will set serial port 
    COM2 to 2400 bps. If you accidentally enter an invalid baud rate, the 
    default of 2400 bps will be used. If you accidentally enter an invalid 
    range of comm ports, the default of COM1 will be used. Defaults are 
    always used if the user does not supply speed and port.

    Typing  a U after any option instructs Comset to setup the  serial 
    port  only and not to look for a modem.  This is handy for setting 
    up  serial  printers or other dumb devices to speeds  higher  than 
    9600 baud.  Mode.com from dos will do the same,  but not at  19200 
    baud!.
    
    Typing COMSET h will bring up a runtime summary of features and other 
    helpful information.

    Ideally, Comset should be run out of your autoexec.bat file when you 
    first turn on your computer. Internal modem users can appreciate the 
    fact that probably 2 or 3 times out of a 100 their internal modem does 
    not "wake-up" properly when the computer is first turned on, and this 
    can hang-up some communications programs. Also, BBS sysops sometimes 
    experience problems with modems when stopping the BBS and trying to 
    use the modem to call out.  This is why Comset was written!

    









                                2

Comset Version 6.0 Documentation (c) 1989 Hank Volpe Computers

                          II. SERIAL PORT INFORMATION 
                          ---------------------------
    
    Comset supports all the industry standard Serial Port address 
    assignments for modems. The shareware version supports COM1 and COM2, 
    while the registered version adds COM3 and COM4 support also. Almost 
    all PC-modems allow you to use COM1-4, however only specific software 
    can use COM3 or COM4 on most machines.
    


    The full featured version of Comset not only will use COM3 or COM4 for
    itself, but it will log those ports into DOS for use by other programs
    such as high-level languages and applications (something that under
    normal conditions can't be done with an IBM-PC or most clones without
    special software).
    


    
                        III ERROR REPORTING INFORMATION
                        -------------------------------
    
            Comset checks your serial port in three distinct steps;
    
       1) Set the Serial Port computer UART to the desired baud rate
          and raise the DTR and RTS lines. If a serial port is not
          detected, Comset aborts and displays the message that there
          is no serial port with that COMM designation in your system.

       2) Check that DSR and CTS are returning from the modem, if not
          report an error and stop testing.
    
       3a)If steps 1 & 2 are successful, wake up the modem by sending
          the command string "ATZ". If OK is received, report all is 
          Normal and leave the RTS and DTR lines active.
    
        b)If the modem did not wake up, issue a more advanced hardware
          and software command string to reset and wake up the modem.
          Three attempts are made..if it fails, the RTS and DTR lines
          are turned off. This could happen if you tell Comset to
          test a serial port that does not have a compatible modem
          attached. In that case, a "failure" of this kind would be
          "normal" for your system.
    
    The Shareware version will report status to the screen. You can 
    redirect the output of Comset to a file if you wish to maintain a log 
    of each initialization. To do this, just use the command string
    
                      COMSET [speed] [port] >> comset.log

    Speed and port are optional. The >> symbol tells dos to make a file
    called comset.log and append it each time Comset is run.




                                3

Comset Version 6.0 Documentation (c) 1989 Hank Volpe Computers

                    IV FULL FEATURE USE AND ERROR REPORTING
                    ---------------------------------------
    
    Registered Users of Comset receive some advanced features, some of 
    which were described above in previous sections. An additional feature 
    of the registered version is that of error-code reporting. Error code 
    reporting simply stated passes "result-codes" from Comset to its 
    calling program. This allows you to write some advanced batch-file 
    procedures or to take specific actions.
    
    Running the registered copy, additional information is displayed 
    informing you of the Error code received. Also that error code can be 
    interpreted by Dos Batch files using the ERRORLEVEL function. Under 
    Normal conditions, a result code of 0 is returned to the calling 
    program. If something wrong is detected, an error code of 99 is 
    returned to the calling program.






    
    A simple use of this can be to start a communications program if the 
    modem is ok, but if not, default to some other action...an example 
    batch-file program looks like this;
     
    echo off
    comset 24 1
     IF ERRORLEVEL 99 goto stop
    echo passed
    goto exit
    :stop
    echo failed!
    :exit
    
    Other uses are left up to your imagination...you could flash up help 
    screens to the user like "HEY DUMMY...TURN ON THE MODEM!!!" or 
    something similar. Combined with redirecting the output to a logging 
    file, you could trace a history of failures or other actions.

   !!NEW FEATURE in VERSION 6...Custom Command File for  Regstered Users !!

    Also,  new  in the registered version of Comset is the ability  to 
    send custom setup strings to your modem from a simple text file.
    To use this feature, all you need to do is the following;

      1) Make a file with valid AT commands using edlin or any ASCII
         text editor and name the file Comset.cmd

      2) Place this file in the same directory that you are running
         comset out of. If you are running Comset from a path, then
         you must have a Comset.cmd file in the directory you are
         currently in for this feature to work. The reason for this
         is  so  that  you  could have multiple  comset.cmd  files  in 
         different directories for different uses.

                                4

Comset Version 6.0 Documentation (c) 1989 Hank Volpe Computers


    When  Comset starts,  it will look for Comset.cmd in  the  current 
    default directory,  and if it finds it,  it will send that command 
    string to the modem instead of the ATZ command. An example of such 
    a command set is the following;

    From dos, type edlin comset.cmd
    when edlin starts, type I for insert.
    Next, type AT M0 H1 then return
    Next, type control-Z
    Next, type e and the file will save.

    The next time you run comset, it will find the file comset.cmd and
    tell the modem to shut off the speaker and go off-hook.

    Any valid AT command set for your brand of modem can be sent.  The 
    only restriction is that all these commands fit on one line and
    the first two letters must be AT. 

    You  can  also redirect the output of this function to a  file  as 
    explained above.




                          V. REGISTRATION INFORMATION
                           --------------------------

    You can freely make copies and distribute Comset over BBS systems or 
    public domain libraries as long as no fee for Comset is charged 
    (except duplication costs) and as long as Comset.exe is distributed 
    along with this file Comset.doc. These may be archived together for 
    use on a bbs system.
    
    Comset is copyrighted by Hank Volpe and is not public domain software. 
    Shareware version users are granted a limited license for its use. No 
    warranties for Comset are stated or implied.
    
    
    Shareware authors continually provide computer users with low priced 
    software compared to the traditional retail approach. If you register
    Comset, you will be able to use all the features ( COM 1-4 support, 
    auto-log in of COM3 and 4 for Dos applications, advanced Error 
    reporting and batch file support).
    
    Registration is simple...and price is low. Comset is only $10, which 
    includes the latest version and free version updates. To register, 
    send $10 along with your name and address to;
    
    
                                   Hank Volpe
                               108 Broadmoor Dr.
                               Tonawanda NY 14150




                                5

Comset Version 6.0 Documentation (c) 1989 Hank Volpe Computers





                               VI. ERROR MESSAGES

     THERE IS NO COMx IN YOUR SYSTEM -
      Comset was instructed by the user to test a non-existent comm port.
      This could happen automatically if you don't have a COM1 in
      your system. If this is the case, use the line
      COMSET [speed] [port] to select your specific needs.



     MODEM NOT RESPONDING PROPERLY -
      The modem under test did not set up even after 3 extensive hardware
      and software attempts to do so. Either you have a non-compatible
      or non-intelligent modem, or you are using the wrong opening
      baud rate. Comset's defaults are 2400 bps and COM1. If you only
      have a 1200 or 300 bps modem, use the line
      COMSET [speed] [port] and use a lower speed. Valid speeds are
      300 bps,  1200 bps , 2400 bps [default], 4800 bps, 9600 bps
      and 19200 bps. Any other values default automatically to 2400 bps.
    
    
     MODEM APPEARS TO BE OFF OR DISCONNECTED -
     The hardware handshaking pairs RTS/CTS or DTR/DSR are not 
     communicating properly. This should NEVER happen on internal modems
     unless the CTS signal is not enabled. Internal Modems usually keep 
     this signal at a logic 1, so if you see this error, check your
     internal modem for proper strapping of the CTS and DSR signals.
    
     If you have an external modem,and the power for the modem is on, you 
     will see this error message if you do not have the CTS signal at a
     logic 1 or you have a defective or inadequate Serial Cable. Most
     external modems have Dip-switches on the back for setting the CTS 
     signal. Normally the CTS follows the Serial Ports RTS and the modem
     DSR (sometimes called MR) follows the Serial Ports DTR.
    
     In the case of an external modem you will see this error message
     everytime the modem has not been turned on. This is telling you
     that your serial port hardware is fine, just that your modem is
     off.
                           VII COMSET PROGRAM HISTORY
                           --------------------------
    
    Version 1 - Simple Assy program fixed at 300 bps. Two versions
                COM1 and COM2.
    
    Version 2 - Baud rate raised to 1200 bps.
    
    Version 3 - Baud rate raised to 2400 bps.
    
    Version 4 - COM1 / COM2 support in one program.
    


                                6

Comset Version 6.0 Documentation (c) 1989 Hank Volpe Computers

    Version 5 - Major rewrite, added interrupt support, hardware
                and software testing, COM 1-4 support, Multiple
                baud rate support, error checking and reporting,
                and support for high speed modems to 19200 bps.

    Version 6 - This version adds the U parameter to allow for testing
                and setup of dumb modems and other serial devices.
                The registered version adds the ability to send a 
                custom command string from a file named comset.cmd
                to the modem in place of the normal ATZ command


    Current Software release is Version 6.0 












































                                7