The following are settings for Telix 3.11 when using a Courier 14.4 HST
US Robotics modem when using an AT 286/12 computer

These settings have produced 1400 to 1550 cps on Exec PC and Rusty and
Edie's

Dip switch settings are as follows:
1,2,4,6,7,9,10: UP
All others: DOWN

Use Alt O in Telix to configure as follows:
(of course Com2 and ANSI-BBS may be others)

ÕÍµ Terminal options ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ 
³                                                                        ³ 
³ A - Baud 38400   Parity None    Data length 8    Stop bits 1           ³ 
³ B - COM2                                                               ³ 
³                                                                        ³ 
³ C - Default terminal type ........... ANSI-BBS                         ³ 
³ D - Status line ..................... Bottom                           ³ 
³ E - Local echo ...................... Off                              ³ 
³ F - Add Line Feeds after CRs ........ Off                              ³ 
³ G - Strip high bit (incoming data) .. Off                              ³ 
³ H - Received Backspace destructive .. On                               ³ 
³ I - XON/XOFF software flow control .. Off                              ³ 
³ J - CTS/RTS hardware flow control ... Off                              ³ 
³ K - DSR/DTR hardware flow control ... Off                              ³ 
³ L - Compuserve Quick B transfers .... On                               ³ 
³ M - Zmodem auto-downloads ........... On                               ³ 
³ N - Answerback string (ENQ) .........                                  ³ 
³                                                                        ³ 
³                                                                        ³ 
³ Change which setting?       (Return or Esc to exit)                    ³ 
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾ 


You may add &K0 to the Init string to turn off MNP compression
I use ATDP. You may be using ATDT, if you have touch tone.

ÕÍµ Modem and dialing parameter setup ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³                                                                            ³
³ A - Init string ......... AT &B1 &H1 X4 S0=0^M                             ³
³ B - Dialing prefix 1 .... ATDP                                             ³
³ C - Dialing prefix 2 .... ATDP                                             ³
³ D - Dialing prefix 3 .... ATDP                                             ³
³ E - Dialing suffix ...... ^M                                               ³
³ F - Connect string ...... CONNECT                                          ³
³ G - No connect strings .. NO CARRIER             BUSY                      ³
³                           VOICE                  NO DIAL TONE              ³
³ H - Hang-up string ...... ~~~+++~~~ATH0^M                                  ³
³ I - Auto answer string .. ATS0=1^M                                         ³
³ J - Dial cancel string .. ^M                                               ³
³                                                                            ³
³ K - Dial time ........... 50                                               ³
³ L - Redial pause ........ 5                                                ³
³ M - Auto baud detect .... Off                                              ³
³ N - Drop DTR to hangup .. On                                               ³
³                                                                            ³
³                                                                            ³
³ Change which setting?       (Return or Esc to exit)                        ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

Set the line rate to 38400.(some use 19200)


ÕÍµ Dialing Directory ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³               Name                    Number      Line Format     Script   
³  1  Exec PC(9600)                 1-414-963-3581  38400 Nù8ù1                ³
³  2  Rusty's(9600)                 1-216-726-0737  38400 Nù8ù1                ³


I have had good speeds with MNP on. Exec PC reports better speeds with MNP off
(&K0). I have not..

I got about 929 cps using Zmodem until I used these settings. Then they 
skipped to the coveted 1400 t0 1550 cps.

If you want to leave a message for me, leave one on Exec PC to Robert May.
I am still working with my new 14.4 USR HST and I would be interested in any
hints on further optimization.

Actually, I got no more than 929 cps until I used the settings I have
outlined above, despite using the settings I downloaded for the modem.

Good luck and enjoy your new found speed!!