>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>> 
LINE NOISE AND THE PROBLEMS IT CAUSES
>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>

Editors Note:
     The following dissertation is adapted from an article appearing on
     the MS-DOS Bulletin Board System of Triangle Park, N.C.
 
Many people ask why there are so many 'garbage' characters on their screens
and why file transfers are riddled with errors. These garbage characters are
really line noise and can be introduced in many different places. Pure noise
is a ASCII 255 (FF in hex), but most line noise is not 'pure'. It usually
comes in as something less than ASCII 255, like maybe an ASCII 251 (a
character that looks like this ' '). Ever see that one before?

One of the more common and familiar introduction points of line noise is in
the telephone company's system and even here there are several ways noise is
introduced. A signal is routed through multiple stations before it
eventually makes it to the other end. Older areas may have older, less
sophisticated equipment that is more apt to be affected by ambient noise.

This is one reason some people continue to have noise problems even after
hanging up and calling back multiple times.

Also, a given physical connection at one of these junctions may not be up to
snuff. If your particular bout of line noise is solved by hanging up and
calling back, then it's probable that you were previously connected through
an intermittent or 'dirty' connection. Some of these are trunk lines though
this is not usually the case.

It is possible that the problem is being caused at the communications PAD,
but not if the problem goes away when you call back and the line is clean
-or- if you are one of a very few users experiencing noise problems. You may
say that you are not having problems with other boards.....in which case the
problem is more than likely the route that your call takes to get here. You
may be going over micro-wave or through buried cable which for some reason
are sub-standard. No matter how many times you call, you will probably be
routed over the same path. Micro-wave problems are sometimes the hardest to
track down because they can cause intermittent problems. Some interference
only occurs during certain times of the day or week.

Another common noise introduction point is in your home. Most residential
homes have televisions, radios, microwave ovens, VCR's, and if you are
reading this, a micro-computer. All these devices radiate radio waves that
can (and often do) get into the phone lines and cause noise. Electric motors
and mechanical dimmer controls can introduce noise into the electrical
wiring in your house and cause problems. If your line noise problem does not
go away after repeated hanging up and calling back, then you may be
suffering from one of these household problems. If you are suffering from
this problem, you can take steps to eliminate it. First of all, turn off
EVERYTHING except the fridge (If it IS the fridge, then you're in trouble.
Can't live life with your icebox unplugged) and see if the noise persists.
If it goes away, then start turning things back on, checking the computer
each time until you see the noise start up again. It may be that a single
device is not bugging you but several devices plotting together to annoy
you. This elimination tournament may take awhile.

Another area to check is your wiring at the computer. Use noise supressors
on your power connections to both the PC and the modem (if external). Use a
shielded RS-232 cable to connect your modem to the PC.

Ribbon cables (especially long runs of it) are great antennas and will cause
problems.  Re-route the RS-232 cable so it does not run next to the PC power
supply or any other transformer.  Many 'clone' monitors do not have internal
metal shielding and can radiate lots of noise.  Make sure the cable does not
run near the monitor.  If you live near a freeway or highway, then
interference from CB radio can present a problem. Many interstate truckers
have 100+ watts of power (illegally) on their CB rigs and frequently have
sloppy amplifiers that can emit spurious radiation all over the radio
spectrum.

And now a little discussion about the modem itself. First of all, let's
clarify a commonly misused term - BAUD. The term "Baud" comes from a man's
name - J.M.E. Baudot (Pronounced: Baw-doe) a French Telegraphy expert. 1,200
and 2,400 Baud is NOT the same as 1,200 and 2,400 BPS (Bits Per Second).

The usage of "Baud" to describe line speed in terms of data through-put is
incorrect.  1,200 and 2,400 BPS modems both operate at 600 Baud. Basically,
without getting too technical, a Baud is a "blip" of information. 1,200 BPS
modems use four states per blip (or Baud) and 2,400 BPS modems use sixteen
states per blip. If you want more information on what Baud and BPS mean and
a full explanation of how data is actually represented and transferred by
the modem, please refer to PC Magazine Volume 6, Number 9 (May 12, 1987).

Modems operating at 2,400 BPS are much less tolerant of line noise than
are modems operating at 1,200 BPS. Conversely, modems capable of 2,400 BPS
operate better at 1,200 BPS than do 1,200 BPS only modems. If you are being
hopelessly attacked by noise at 2,400 BPS, trying calling back at 1,200 BPS.
It's very possible that the noise will be greatly reduced or disappear
altogether. I know, you didn't buy a 2,400 BPS modem just to retard it to
1,200 BPS. The brand of the modem plays a part in the immunity to line
noise.

Some modems can digest more noise (lower signal-to-noise radio) than others.
PC Magazine (same issue mentioned above) ran a test on 87 different modems.
You might check the results to see how your modem ranks. Most 2,400 BPS
modems operating at 1,200 BPS have approximately -8 to -10 db error
threshold while the same modem has about -16 to -20 db threshold operating
at 2,400 BPS.

For this reason, line quality is much more critical at 2,400 BPS operation.
One person who runs a bulletin board from their office has been plagued with
line noise problems at 2,400 BPS but very little noise at 1,200 BPS. The
culprit is the office's centralized telephone system.

Many office buildings have a given number of trunks that actually enter the
building while there may be many, many more extension within the building.
These types of telephone systems have their own controllers and line
assignment devices and are frequently not as high in quality as a hard-wired
commercial phone line. The acceptable signal-to-noise ratio in some of these
inter-office phone controllers are lower than necessary for reliable 2,400
BPS operation but not too low for 1,200 BPS.

If you get transmission errors while downloading or uploading a file,
don't fret it.  Use of Lotus Express (MS-DOS) or Desktop Express (Macintosh)
(message MCI Mailbox 218-0241 for additional information) incorporates an
error checking/correction mechanism that automatically detects and corrects
any errors that may occur during transmission.