MDM730

			 (NOTES ON HOW TO USE)

			  Copyright 1983,1984


			  Irvin M. Hoff W6FFC

			      22 Mar 1984


NOTE:  MDM730 SUPPORTS AUTO-DIALING AND AUTOMATIC CONTINUOUS REDIALING
       FOR THE FOLLOWING MODEMS:

		    SIGNALMAN ANCHOR MARK XII
		    HAYES SMARTMODEM 300 OR 1200 MODEMS
		    U. S. ROBOTICS 300/1200 MODEM
		    PMMI 103 S-100 PLUG-IN MODEM

	IT CAN STILL BE EASILY USED WITH OTHER EXTERNAL MODEMS
	ITH MANUAL DIALING SUCH AS THE BELL 212A, RACAL-VADIC,
	ETC.  IT SUPPORTS UP TO TWO LONG-DISTANCE DIALING SYSTEMS
	(SUCH AS 'MCI', 'SPRINT', 'TYMNET', ETC. FOR TOUCH-TONE
	DIALING SYSTEMS.


INTRODUCTION:
------------

     MDM730 enables a computer to communicate with another computer.
This is normally done by using standard telephone lines but with special
audio tones sending serial data.  Two common speeds are used, depending
on the facilities available -- 300 Baud or 1200 Baud.  A "modem" is used
which provides these audio tones.  This is an acronym for "modulator and
demodulator".  The one section (modulator) provides the audio tones for
sending over the telephone line and the other section (demodulator) then
converts those audio tones back to digital pulses the computer uses to
receive the incoming data.

     The modem itself is a hardware utility, usually costing around $75
to $200 for a typical 300 Baud device and from $250 to $800 for a system
offering 1200 Baud as well as 300 Baud.  Some of these (such as the PMMI
S-100 modem board) plug directly into the computer itself, while others
are totally independent of the computer and use an interconnect cable
(usually a RS-232 type) to control the external modem.	A Bell 212A is
an excellent example of this type modem.  Other examples would include
the Racal-Vadic, Hayes Smartmodem, U. S. Robotics, Signalman Anchor, etc.

     The program discussed in this guide allows each computer involved
to directly control its own modem, converting DC pulses into audio tones
which are sent to (or received from) the telephone line.  (The standard
1200 baud transmissions use "DPSK" (dibit phase shift keying) instead of
"AFSK" (audio frequency shift keying).

     For short distances, no modems are required as the computer can
provide the necessary digital voltages.  This discussion is centered
around systems intended for use over distances ranging from several
miles to literally around the world.



FEATURES:
--------

     A program to communicate with another computer can range from very
simple to very complex.  MDM730 is one of the more complex such programs
available today.  It started in 1977 as a relatively simple program.  It
was called MODEM at that time.	It was intended to be used primarily as
a means of exchanging programs with other people in other cities.  Since
that time a number of other (very useful) features have been added, in
addition to improved methods of program transfer.  A list of some of the
features offered by this particular program include:

  1)  Ability to talk with another computer via keyboard at each end.
	  (Called the "terminal mode".)
  2)  Ability to operate a remote mainframe computer such as TYM-SHAR,
	  or special data bank systems now commonplace.  This includes
	  "bulletin board" systems for receiving, sending or just read-
	  ing messges or other types of information.
  3)  Ability to upload (send) or download (receive) programs from other
	  computers whether TYM-SHAR, data banks, remote hobby systems
	  or just another individual in another location.
  4)  Ability to copy incoming information on a printer.  If the print-
	  er is too slow to copy the data directly, the extra characters
	  back into a large storage buffer until they can be printed.
  5)  Ability to copy incoming data into memory for automatic transfer
	  to a disk file.
  6)  Accomodates any computer clock speed up to 25.5 MHz. in 0.1 Mhz.
	  increments for uniform results.  (The clock speed is actually
	  of modest interest, it is only used for setting timing loops.)
  7)  Advanced type of error detection (CRC or Cyclic Redundancy Check)
	  using automatically generated high-speed lookup tables.
  8)  Ability to send any of 11 different pre-programmed function keys.
	  (These keys are very easy to reset, using a special external
	  program.)
  9)  Automatic disconnect from the telephone line when using CTL-N, or
	  "X" as an option during file transfer.  Two other disconnect
	  commands with the PMMI modem.
 10)  Additional features of special interest to those using the PMMI
	  103 S-100 plug-in modem, the U. S. Robotics 300/1200, the
	  Anchor Signalman Mark XII, the Hayes Smartmodem 300 or 1200
	  or other "Hayes-compatible" modems.  Those features basically
	  include automatic dialing and redialing (if requested) until
	  the other computer finally answers.
	
	       a) Automatic selection of a particular phone number from
		  a library of names and numbers.  (These phone numbers
		  can be very easily changed by using a special external
		  program.)
	       b) Automatic dialing for alternate long-distance systems
		  (where auto-dialing touch-tone modems are used).
	       c) Entry of a hand-typed number.  Although it might be as
		  simple to manually dial the number as hand-type it, it
		  can then be automatically redialed indefinitely.


USING THE PROGRAM THE FIRST TIME:
--------------------------------

     For now, we shall assume the program is ready to use on your equip-
ment.  (Normally the user must make some modest changes to the program
before it can be used.	This includes changing the port numbers and some
other personal options.  These will be covered later in the section that
describes how to adapt it to your equipment.)

     When the program is brought up is shows this display (if using the
PMMI modem):

	  MDM730 - (type M for Menu)
	  Version for PMMI S-100 modem starting at port: C0H

	  B>>COMMAND: x

       The cursor stops at point "x:" waiting for some sort of command.
Typing a "M" followed immediately by a RETURN, shows the first page of
a 4-page help guide.  If you do not have a PMMI modem, you would have
seen this (or a customized heading for your particular equipment):

	  MDM730 - (type M for Menu)
	  Version for Non-Pmmi modem

	  B>> COMMAND:

     In this case only a 3-page help guide is used, since the 4th page
is used to assist those with the PMMI modem.  It tells them a little
about changing from originate to answer mode, how to change Baud rates,
how to disconnect, etc.

     Several commands are similar to those already used for CP/M, such
as 'ERA', 'DIR' and the ability to change disk drives and user areas.
This adds tremendous flexibility while remaining in the modem command
mode.  To change disk drives, just say:

	  B>>COMMAND: A: <RET>

     and you are in the same user area on the A: drive.  You can also
say:
	  A>>COMMAND: A: 12 <RET>

     to change user areas.  When finished (using this example), say:

	  A12>>COMMAND: CPM  <RET>

     and you will go back to CP/M with the original driver and user area.

OPTIONS:
-------

     There are 6 primary options and 13 secondary options that may be
typed on the command line.  In additon there are over 35 commands ranging
from single character to three characters that can be used (such as DIR,
ERA, LOG, etc.)  Those are listed on the menu.	(The exact number varies
depending on whether you have the PMMI modem, etc.)


     Primary Options:	 E, L, M, R, S, T
	  E = Echo mode (special type of full duplex)
	  L = Local modem (no remote echo, half duplex)
	  M = Menu display showing features that are available
	  R = Receive a file from remote facility
	  S = Send a file to a remote facility
	  T = Terminal mode (full duplex, echo provived remotely)

     Secondary Options:  A, B, D, J, O, Q, R, S, V, X, 0, 1
	  A = Answer mode (used only by PMMI modems)
	  B = Batch mode -- allows automatic multiple file transfer
		(This is normally only used from modem-to-modem as
		no RCP/M system supports batch mode file transfers.)
	  D = Disconnect when done, stay in MDM730
	  J = Command mode when finished with a file transfer
	  O = Originate mode (used only by PMMI modems)
	  Q = Quiet mode, special purpose feature rarely used except if
		 operating through a "BYE" program.
	  R = Receive data shown on CRT during file transfer
	  S = Send data shown on CRT during file transfer
	  V = Visual inspection of an ASCII file being transferred.  Not
		 often used as most ASCII files are now "squeezed" for
		 minimum transfer time and disk space.
	  X = Exit to CP/M  when finished, disconnect from phone line
	  0 = Odd parity (PMMI modem)
	  1 = Even parity (PMMI modem)
	

     Although you can get the following information from the help guide
in MDM730 itself, showing it here will allow us to discuss the various
features in somewhat better detail.

     (*) INDICATES PMMI, ANCHOR, HAYES AND US ROBOTICS ALL APPLY.

-   -	-   -	-   -	-   -	-   -	-   -	-   -	-   -	-   -


THE HELP GUIDE, PAGE 1:
----------------------

		 Single Letter Commands

?  - Display current settings
^  - Function key intercept character, then (0-9)
M  - Display the menu
E  - Terminal mode with echo
L  - Terminal mode with local echo
T  - Terminal mode
	For copying text to disk use T (or E or L) FILENAME.TYP
	Start or Stop toggles described on subsequent screen.
R  - Receive CP/M file using Christensen Protocol
S  - Send CP/M file using Christensen Protocol
	COMMAND: R (or S) FILENAME.TYP
	R and S can use the following subcommands:
	   B  - Bulk transfer using wildcards (e.g., *.*)
	   D  -	Disconnect when done, return to command mode
	   Q  - Quiet mode (no messages to console)
	   V  - View <R> or <S> bytes on console
	   X  - When done, disconnect, go to CP/M

     The single letter commands may also be used on the
     command line when the program is initially executed.

Hit any KEY to CONTINUE

-   -	-   -	-   -	-   -	-   -	-   -	-   -	-   -	-   -


DISCUSSION OF HELP GUIDE PAGE 1:
-------------------------------

     There are basically three types of commands that may be used with
this program:
	     1)  Single-letter commands shown on page one.
	     2)  Three-letter commands shown on page 2, and
	     3)  Control-<char.> commands shown on page 3.

     Going down the list:

  ? - shows current parameters.  As these are closely tied in with some
	  of the other options, we shall show a typical example later
	  in this discussion.
  ^ - shows the function key intercept character.  This may be easily
	  changed using an external program.  (You may prefer 'escape'
	  or some seldom used control-character.)

	  NOTE:  typing this character while in the command mode will
		 display all the programmable function key definitions
		 with the exception of the log-on string which uses
		 CTL-L.

  M - shows the menu a page at a time.	You may abort after any page is
	  shown with a control-C.
  E - terminal mode with echo.	When talking with another terminal also
	  also using MDM730 (or a comparable program), one of you must
	  send an "echo-back" so you can both see what the other person
	  is typing.  This is needed for full-duplex operation.  Usually
	  the person originating the call will type "E" instead of "T".
	  However either may do this.  If "both" use the echo mode, the
	  program usually starts typing a string of feedback characters
	  since both computers are re-sending the same character over
	  and over.  You can stop this by just returning to command mode
	  (type control-E) and then retyping "T" rather than "E".
  L - terminal mode with local echo.  Shows what you are typing but does
	  not send an echo of the other person's typing back to him.  
          Can be used at both ends, in place of one person using "E".
          Both "E" and "L" are useful at times for some types of modems
          that do not use full-duplex, or for some main frame units that
          run half-duplex.  The combination of "T", "E" and "L" gives an
          excellent choice to use on various systems.  Normally the "T"
          mode is sufficient except when talking with another person and
          then the "E" mode at one end or "L" mode at both ends will
          provide normal results.  If the remote system does not supply
	  a LF after a CR, you can get that from the 'TLF' command.
  T - puts the program directly into "terminal mode", allowing it to
	  send from the keyboard to the other computer, and to copy any-
	  thing coming from the other computer with the exception of
	  file transfers (use "R" to receive those).
  R - used only for receiving files from the other computer.  These are
	  usually sent in binary form with either checksum verification
	  or more commonly, CRC (Cyclic Redundancy Checking).  If ready
	  to receive another file, you have several choices, depending
	  on the program used by the other computer.   After notifying
	  him you are ready (or will be very shortly), you can type:

	       B>>COMMAND: R HELLO.DOC <RET>

	  and when he starts to send, you will receive the program which
	  then goes directly to the disk.  You could also have said:

	       B>>COMMAND: RB <RET>

	  This is called the "Batch mode" and is an extremely useful way
	  to receive programs automatically, from another computer using
	  a similar program.  He will use the batch mode for sending the
	  programs and that automatically provides the file names at the
	  receiving end.  In this manner, large numbers of programs can
	  be transferred completely automatically, including full disks.
	  (Assuming you care to pay the toll calls for the time it will
	  take!)

	  NOTE:  The ideal way to receive batch mode would be:

	       B>>COMMAND: RB <RET>

		 since you may not know in advance how many programs he
		 will be sending.

	       NOTE:  While receiving a file, any errors will be shown
		      on the console CRT, indicating that portion of the
		      program is being repeated.  If the file finishes
		      transferring normally, it will have been received
		      error-free.  Those error notices are merely to let
		      the user know a momentary problem caused a resend.
		      The error messages indicate phone line quality.

  S - used only to end programs.  Similar to "R" but sends instead of
	  receives.  If the other system is ready to receive, you could
	  then type:

	       B>>COMMAND: S HELLO.DOC <RET>

	  It will tell you how many records are involved and how many
	  minutes and seconds it will take to send the program.  If the

ÿÿÁMÿÿÿÿÿSÿMÿËÿÃÿÿÿÿÿÿSÿMÁÿÿÿÿÿÃ\ÿÿÿÃMÿÿMÿÿMÿÿMÿÿÿMÿÿÍÿÌÿÿÿúÿóÿÿÿÿÁUÃÍÅÿÿÁUÿËÿÍSÿÿÿÿÁÿÿT€ÿ”êž€ žžº€í=ÿÿÿ#lÿ/-ÿ/=ÿÿüÿÿ/üÿÿ½ÿpbÿÿ/?½ÿkQÿq‘ÿQ›Kÿ››ÿ
Xÿÿÿxÿ›ÿ
»™ÿ»ÿÿxÿqÿÿÿÿÿ‘ÿÿÿQÿÿ‹
{Qq²F†VÒàÐ ’—Bv–ÆÂ&W6Væÿÿ|ÕÿõÿÿÿÿÕÿüÜÿüÿorrectly received at the other
	  computer.  If too many consecutive errors occur (normally set
	  at 10), the transfer is terminated.  The 'batch mode' may also
	  be used for sending:

	       B>>COMMAND: SB HELLO.*            (sending batch mode)

	  will send all files starting with HELLO, or can send just one
	  file, or can send several non-related files in this manner:

	       B>>COMMAND: SB HELLO.DOC XDIR.COM TERM.*

	  etc.	Be sure to put a space between the various files.  You
	  can include the 'X' option:

	       B>>COMMAND: SBX HELLO.* MDM730.LBR MDM730.AQM

	  When the file transfer is completed it disconnects from the
	  phone line and reverts to CP/M.  This allows you to be absent
	  when the file is finished, offering an advantage when sending
	  lengthy files.

-   -	-   -	-   -	-   -	-   -	-   -	-   -	-   -	-   -


THE HELP GUIDE, PAGE 2:
----------------------

		Three Letter Commands

CPM - Exit from this program to CP/M
DIR - List directory and space free (may specify drive)
ERA - Erase file (may specify drive)
LOG - Change default drive/user no. (specify drive/user)
      and reset disks.	e.g. LOG A0: or LOG B: (user # unchanged)
SPD - Set speed of file output in terminal mode
TIM - Select Baud rate 

		MD730C64

    MD730C64 is a version of Irv Hoff's MDM730 modified for
the Commodore 64.  If you are unfamiliar with MDM730, you can
get a detailed description from the file MDM730.DQC in the
library MDM730.LBR.  This version works with the Hayes 300 
Smartmodem, the VICmodem and probably any other modem that
connects to an RS-232 port.  With the Hayes, you can use the
auto dial features of the program.

    MD730C64 will work ONLY with a 44k (or smaller) Commodore
64 CP/M system.  The RS-232 buffers and a character translation
table are located in the "extra" 4k.  If you try to work with
a 48k system, the program will crash.

Please note the following:

   1. Ctl-W (not Ctl-T) is used to start an ASCII file transfer
      in terminal mode.
   2. The program is currently set for pulse dialing with a
      Haye's Smartmodem.  If you have touch tone dialing, patch
      location 105H to be an ASCII 'P'.  It is currently a 'T'.
   3. There is no cursor when you are in terminal mode.  (You'll
      get used to it - honest!)
   4. The program has been tested at 300 baud.  Because of
      the interaction between the two processors, it may need
      more work to run correctly at 1200.

    This is an initial release and I would sincerely appreciate
hearing from you if you use the program.  Modifying MDM730 for
this computer was painful because of the way the C-64 handles its
RS-232 port.  It has been thoroughly tested but it is
a very complex program and there may be problems remaining simply
because there are combinations of functions that I am not aware of.
Please let me know if you incover any.  I'd also like to hear from
you if you use it and don't have problems.  When I have enough
confidence in the program,  I'll release the source code for
the overlay.

				Walt Piotrowski
				RD1 Box 582
				Afton, NY 13730
				(607) 693-2809 (voice)
				Compuserve 72636,761
					or

			Leave a message on Charles Zalenski's
			RBBS (607) 797-6416 - Johnson City, NY