Modifying PC-Talk to run under MultiLink

PC-Talk uses the SOUND statement for timing purposes.  Unfortunately,
BASIC handles this by patching into the timer interrupt vector and
stepping up the rate of interrupts drastically... works in a single-
user system, but wreaks havoc under multitasking!

You can avoid this problem by locating all statements of the form

                          SOUND 32767,n

and replacing with a statement of the form

                      DELAY!=n:GOSUB 30000

where "n" is the specified number of timer ticks.

Then, add the following subroutine to the end of the program:

30000 DEF SEG=0
30010 TWBEG!=PEEK(&H46C)+256*PEEK(&H46D)
30020 TWCUR!=PEEK(&H46C)+256*PEEK(&H46D)
30030 IF TWCUR!<TWBEG! THEN TWCUR!=TWCUR!+65536
30040 IF TWCUR!<(TWBEG!+DELAY!) THEN 30020
30050 RETURN

While you're at it, it's a good idea to simply remove all other SOUND
and BEEP statements.  Cute little grunts and beeps are nice, but not
when they threaten to crash your system.
e
2110 DATA" Alt-S = Screendump   Alt-C = Clearsc
2115 DATA"  Alt-P =  communications Parameters
2120 DATA"  Alt-F =  set program deFaults
2125 DATA"  Alt-L =  change Logged drive
2130 DATA"  Alt-W =  set margin Width alarm
2135 DATA"  Alt-Z =  elapsed time/current call
2140 DATA"  Alt-X =  eXit to DOS
2145 DATA"Ctrl-End = send sustained Break signal
2150 '
2500 '
2505 Q$="":IF QL=0 THEN QL=255
2510 QI$=INKEY$:IF QI$="" THEN 2510
2515 IF QI$=CHR$(13) THEN RETURN
2520 IF QI$<>CHR$(8) THEN 2530 ELSE IF Q$="" THEN GOTO 2510
2525 IF QI$=CHR$(8) THEN GOSUB 2650:Q$=LEFT$(Q$,LEN(Q$)-1):GOTO 2510
2530 IF LEN(Q$)=QL THEN GOTO 2510
2535 IF LEN(QI$)=1 THEN 2545 ELSE IF QI$<>CHR$(0)+CHR$(3) THEN GOTO 2510 ELSE QI$=CHR$(0)
2545 IF ASC(QI$)>31 OR QI$=CHR$(27) THEN PRINT QI$; ELSE COLOR HI,BG:PRINT CHR$(ASC(QI$)+64);:COLOR FG,BG
2550 IF QI$=XCR$ THEN Q$=Q$+CHR$(13):GOTO 2510 ELSE Q$=Q$+QI$:GOTO 2510
2555 '
2560 FOR J=1 TO LEN(Q$):P=ASC(MID$(Q$,J,1)):IF P<97 OR P>122 THEN 2570
2565 MID$(Q$,J,1)=CHR$(P AND 95)
2570 NEXT:RETURN
2600 '
2605 MSG$=LEFT$(MSG$,78):ROW=CSRLIN:COL=POS(0):LOCATE 25,1:COLOR HI,BG:PRINT CHR$(16);:COLOR BG,FG:PRINT MSG$+SPACE$(78-LEN(MSG$));:COLOR FG,BG:LOCATE ROW,COL:RETURN
2650 '
2655 PRINT CHR$(29);" ";CHR$(29);:RETURN
2700 '
2705 CLOSE#2:IF RC THEN OPEN RCV$ FOR APPEND AS #2
2710 RETURN
2715 CLOSE#3:IF PR THEN OPEN PRNTPORT$ FOR OUTPUT AS #3
2720 IF TR THEN OPEN TRN$ AS #3 LEN=128:FIELD #3,128 AS X$
2725 RETURN
2800 '
2805 ROW=CSRLIN:COL=POS(0)
2810 EXIT=0:FOR I=1 TO 10:IF ALT$(I)<>"" THEN EXIT=-1:NEXT
2815 IF EXIT THEN EXIT=0:LOCATE ,,1:GOTO 1210
2820 IF MENU=0 THEN 2830
2825 LOCATE 25,1:PRINT" ";:COLOR BG,FG:PRINT"^PrtSc=prnt  Alt- T=tran R=recv V=view D=dial E=echo M=mesg X=exit <Home>=Help";:COLOR FG,BG:LOCATE ROW,COL:RETURN
2830 LOCATE 25,1:PRINT SPACE$(79);:LOCATE ROW,COL:RETURN
2835 '
3000 '
3010 IF RC THEN RC=0:RC$="":PRINT:PRINT"===RECEIPT OF FILE ";RCV$;" TERMINATED===":PRINT:GOSUB 2700:GOSUB 2800:IF MSG THEN PRINT#1,BL$;CR$;"===FILE RECEIVED===":GOTO 515 ELSE 515
3015 RC$="":PRINT:PRINT"===RECEIVE A FILE===":GOTO 3500
3020 IF RC$="X" THEN CLOSE#2:KILL RCV$:OPEN RCV$ AS #2 LEN=128:FIELD #2,128 AS X$:GOTO 3030
3025 IF MSG THEN PRINT#1,BL$;CR$;"===READY TO RECEIVE===
3030 MSG$=" Receiving "+RCVX$+"  (ALT-R to Terminate)":GOSUB 2600
3035 RC=-1:IF RC$="X" THEN 4500 ELSE 605
3040 '
3200 '
3210 IF TR THEN TR=0:TR$="":MSG1$="===TRANSMISSION OF FILE ":MSG2$=" TERMINATED===":PRINT:PRINT MSG1$;TRN$;MSG2$:GOSUB 2715:GOSUB 2800:IF MSG THEN PRINT#1,CR$;MSG1$;MSG2$,BL$:GOTO 515 ELSE 515
3215 IF TR THEN TR=0:TR$="":MSG1$="===END OF FILE":MSG2$="===":PRINT:PRINT MSG1$;" ";TRN$;MSG2$:GOSUB 2715:GOSUB 2800:IF MSG THEN PRINT#1,"65529 '";MSG1$;MSG2$;BL$:GOTO 515 ELSE 515
3220 TR$="":PRINT:PRINT"===TRANSMIT A FILE===":GOTO 3500
3225 CLOSE#3:OPEN TRN$ AS #3 LEN=128:FIELD #3,128 AS X$
3230 MSG$=" Transmitting "+TRNX$+" (ALT-T to terminate)":IF TR$="X" THEN MSG$=MSG$+"  # of blocks:" ELSE IF TR$="P" THEN MSG$=MSG$+"  percent remain:" ELSE MSG$=MSG$+"   min. remain:"
3235 GOSUB 2600:IF TR$="X" THEN ROW=CSRLIN:COL=POS(0):LOCATE 25,74:CNT!=FIX(LOF(3)/128):FLN!=LOF(3)/128:IF CNT!=FLN! THEN PRINT CNT!;:LOCATE ROW,COL ELSE PRINT CNT!+1;:LOCATE ROW,COL:GOTO 3245
3240 IF MSG THEN PRINT#1,CR$;"0 '===START OF FILE===";BL$
3245 TR=-1:FLN!=LOF(3):IF TR$<>"X" THEN 4000 ELSE 4700
3250 '
3400 '
3410 PRINT:PRINT"===VIEW A FILE===":GOTO 3500
3415 MSG$=" Viewing "+VEWX$+"  Hit <space> to continue  (Alt-V to terminate)":GOSUB 2600:PRINT:PRINT:PRINT
3420 WHILE NOT EOF(3):FOR I=1 TO 20:LINE INPUT#3,X$:J=LEN(X$):IF J<80 THEN PRINT X$ ELSE PRINT X$;:IF J>80 THEN I=I+FIX(J/80)
3425 NEXT
3430 Q$=INKEY$:IF Q$="" THEN 3430 ELSE IF Q$=" " THEN 3420 ELSE IF Q$=CHR$(0)+CHR$(47) THEN 3445 ELSE GOTO 3430
3435 WEND
3440 PRINT:PRINT"===END OF FILE ";VEW$;" ===":GOTO 3450
3445 PRINT:PRINT"===VIEWING OF FILE ";VEW$;" TERMINATED===
3450 GOSUB 2715:GOSUB 2800:GOTO 515
3455 '
3500 '
3510 EXIT=0:PRINT"   specification:";
3515 Q$=INKEY$:IF Q$="" THEN 3515 ELSE IF Q$=CR$ OR Q$=BS$ THEN FIL$="":PRINT:GOTO 3540
3520 IF LEN(Q$)>1 THEN Q=ASC(MID$(Q$,2,1)):IF Q>=59 AND Q<=68 THEN Q$=K$(Q-58) ELSE IF Q>=104 AND Q<=113 THEN Q$=K$(Q-93) ELSE IF Q>=84 AND Q<=103 THEN Q$=K$(Q-63) ELSE GOTO 3515
3525 IF Q$<>" " THEN PRINT Q$;:QL=128:GOSUB 2510:GOSUB 2555:FIL$=Q$:PRINT:LOCATE,,1:GOTO 3540
3530 IF EX=19 THEN FIL$=RCVX$ ELSE IF EX=20 THEN FIL$=TRNX$ ELSE IF EX=47 THEN FIL$=VEWX$
3535 Q$=FIL$:PRINT Q$;:QL=128:GOSUB 2510:GOSUB 2555:FIL$=Q$:PRINT:LOCATE,,1
3540 IF FIL$="" THEN PRINT"===CANCELLED===":GOTO 515
3545 IF LEFT$(FIL$,1)="?" THEN GOSUB 3625:GOTO 3510
3550 P=INSTR(FIL$,":"):IF P=0 THEN FIL$=DRIV$+FIL$
3555 IF EX=19 THEN RCVX$=FIL$ ELSE IF EX=20 THEN TRNX$=FIL$ ELSE IF EX=47 THEN VEWX$=FIL$
3560 P=INSTR(FIL$,"="):IF P=0 THEN IF EX<>20 OR PC$="" OR EXIT=-1 THEN 3595 ELSE EXIT=-1:Q$=FIL$+PC$:LOCATE CSRLIN-1,18:GOTO 3525
3565 Q$=RIGHT$(FIL$,LEN(FIL$)-P):FIL$=LEFT$(FIL$,P-1)
3570 IF Q$="B" THEN TR$="B"
3575 IF Q$="X" THEN IF EX=19 THEN RC$="X" ELSE IF EX=20 THEN TR$="X
3580 IF LEFT$(Q$,1)="P" THEN TR$="P":PROMPT$=RIGHT$(Q$,LEN(Q$)-1):DEL!=VAL(PROMPT$)
3585 IF TR$="B" OR TR$="X" OR RC$="X" THEN IF DTA$<>"8" THEN PRINT"*** You must communicate at 8 DATA BITS for binary or XMODEM ***":GOTO 5015
3590 IF TR$="X" OR RC$="X" THEN IF NS<>0 THEN PRINT"*** Stripping disabled for XMODEM ***":NS=0
3595 IF EX=19 THEN CLOSE#2:OPEN FIL$ FOR APPEND AS #2 ELSE CLOSE#3:OPEN FIL$ FOR INPUT AS #3
3600 PRINT STRING$(18+LEN(FIL$),61):IF EX=19 THEN RCV$=FIL$:GOTO 3020
3605 IF EX=20 THEN TRN$=FIL$:GOTO 3225
3610 IF EX=47 THEN VEW$=FIL$:GOTO 3415
3615 IF EX=21 THEN 3915
3620 '
3625 IF LEN(FIL$)=1 THEN FIL$=DRIV$+"*.*":GOTO 3640 ELSE FIL$=RIGHT$(FIL$,LEN(FIL$)-1):IF LEFT$(FIL$,1)=" " THEN FIL$=RIGHT$(FIL$,LEN(FIL$)-1)
3630 P=INSTR(FIL$,":"):IF P=0 THEN FIL$=DRIV$+FIL$
3635 IF LEN(FIL$)=P THEN FIL$=FIL$+"*.*
3640 PRINT:FILES FIL$:PRINT
3645 RETURN
3650 '
3800 '
3810 CLOSE#2:OPEN DUMP$ FOR APPEND AS #2:MSG$=" Appending to "+DUMP$+" at "+TIME$:GOSUB 2600 ' *ROD*
3815 FOR I=1 TO 24:Y$="":FOR J=1 TO 79:X=SCREEN(I,J):Y$=Y$+CHR$(X):NEXT J:PRINT#2,Y$:NEXT I:PRINT#2,STRING$(79,45);CR$;LF$;"===PC-TALK SCREENDUMP - ";DATE$;" at ";TIME$;"===";CR$;LF$;STRING$(79,61):CLOSE#2
3820 GOSUB 2705:GOSUB 2800:LOCATE ROW,COL:GOTO 515                     ' *ROD*
3825 '
3900 '
3910 PRINT:PRINT"===DELETE A FILE===":GOTO 3500
3915 PRINT"***The first 5 lines are:":FOR I=1 TO 5:IF NOT EOF(3) THEN LINE INPUT#3,X$:PRINT X$
3920 NEXT:PRINT"***ARE YOU SURE (y/n)?";:Q$=INPUT$(1):PRINT Q$:GOSUB 2555:IF Q$="Y" THEN CLOSE#3:KILL FIL$:PRINT" (deleted)":GOTO 3930
3925 PRINT" (not deleted)":PRINT GO$:GOTO 515
3930 PRINT GO$:GOTO 515
3935 '
4000 '
4010 IF TR$="B" THEN PRINT"(sending file as binary...)
4015 RATE!=VAL(BAU$)*6:CNT!=0:ROW=CSRLIN:COL=POS(0):GOTO 4060
4020 LOCATE 25,74:IF TR$<>"P" THEN PRINT USING"###.#";(FLN!-(CNT!*128))/RATE!; ELSE PRINT USING".##";(FLN!-CNT!*128)/FLN!;
4025 GET#3,CNT!:Y$=X$:LOCATE ROW,COL
4030 IF TR$="P" THEN GOSUB 4400:IF NOT ABORT THEN 4050 ELSE ABORT=0:GOTO 1500
4035 PRINT#1,Y$;:IF TR$="B" THEN 4050
4040 P=INSTR(1,Y$,LF$):IF P=0 THEN 4045 ELSE Y$=LEFT$(Y$,P-1)+RIGHT$(Y$,LEN(Y$)-P):GOTO 4040
4045 FOR I=1 TO 128:PRINT MID$(Y$,I,1);:NEXT
4050 ROW=CSRLIN:COL=POS(0):GOSUB 4070:B$=INKEY$:IF B$="" THEN 4060
4055 IF LEN(B$)>1 THEN 1500
4060 CNT!=CNT!+1:IF CNT!*128<FLN! THEN 4020 ELSE GET#3,CNT!:Y$=X$:GOTO 4200
4065 '
4070 IF EOF(1) THEN 4085 ELSE A$=INPUT$(LOC(1),#1)
4075 P=INSTR(1,A$,XF$):IF P<>0 THEN HLT=-1:COLOR HI,BG:PRINT"<<XOFF>>";:COLOR FG,BG
4080 IF HLT THEN P=INSTR(1,A$,XN$):IF P=0 THEN 4085 ELSE HLT=0:RETURN
4085 IF HLT THEN Q$=INKEY$:IF Q$<>"" THEN IF LEN(Q$)<>2 THEN 4070 ELSE IF ASC(RIGHT$(Q$,1))=24 THEN HLT=0:RETURN ELSE 4070 ELSE 4070
4090 RETURN
4200 '
4205 I=0:CNT!=(CNT!-1)*128
4210 I=I+1:CNT!=CNT!+1:IF I>255 THEN 4230 ELSE Z$=MID$(Y$,I,1)
4215 IF TR$="B" THEN IF CNT!<=FLN! THEN 4235 ELSE 4230
4220 IF Z$<>EF$ THEN 4235 ELSE 4230
4225 IF CNT!<=FLN! THEN 4235
4230 IF EOF(1) THEN 3215 ELSE DMMY$=INPUT$(LOC(1),#1):GOTO 4230
4235 IF TR$="P" THEN IF Z$=LF$ THEN 4210
4240 PRINT#1,Z$;:IF TR$="P" THEN IF Z$=CR$ THEN PRINT Z$;:GOSUB 4425:GOTO 4210
4245 IF TR$="B" OR Z$=LF$ THEN 4210
4250 PRINT Z$;:GOTO 4210
4400 '
4405 FOR I=1 TO LEN(Y$):Z$=MID$(Y$,I,1):IF Z$=LF$ THEN 4415 ELSE IF Z$<>CR$ THEN PRINT#1,Z$;:PRINT Z$;:GOTO 4415 ELSE PRINT #1," "+CR$;:PRINT CR$;:B$="":GOSUB 4420
4410 IF ABORT THEN RETURN
4415 NEXT:RETURN
4420 IF LEN(B$)>1 THEN ABORT=-1:RETURN
4425 IF (INP(LSR) AND 96)<>96 THEN 4425
4430 IF DEL!>0 THEN DELAY!=18*DEL!:GOSUB 30000:RETURN
4435 Z$="":WHILE NOT EOF(1):Z$=Z$+INPUT$(LOC(1),#1):WEND:PRINT Z$;:IF Z$="" THEN Z$=CHR$(0) ELSE IF LEN(Z$)>128 THEN Z$=""
4440 P=INSTR(Z$,PROMPT$):B$=INKEY$:IF P<>0 OR B$=" " THEN RETURN ELSE 4420
4445 '
4500 '
4510 PRINT"===RECEIVE FILE WITH XMODEM===":PRINT
4515 Y$="":BLK=1:SEC=1:CK=0:ECNT=0
4520 PRINT"***Holding for Start...":GOSUB 4975:PRINT#1,NAK$;
4525 GOSUB 4925:IF ABORT THEN 4645 ELSE 4535
4530 GOSUB 4905:IF Z$="" THEN 4545
4535 Y$=Y$+Z$:IF LEN(Y$)<=131 THEN 4530
4540 '
4545 IF LEN(Y$)=132 THEN LSET X$=MID$(Y$,4,128):N=132:GOTO 4580
4550 IF LEN(Y$)=131 THEN LSET X$=MID$(Y$,3,128):N=131:GOTO 4580
4555 IF LEN(Y$)>132 THEN PRINT"**Long  Block in #";BLK:GOTO 4615
4560 IF Y$=EOT$ THEN 4635
4565 IF Y$=CAN$ THEN 4640
4570 IF Y$="" THEN PRINT"***Timeout":GOSUB 4975:PRINT #1,NAK$:GOTO 4525
4575 PRINT"**Short Block in #";BLK:GOTO 4615
4580 IF (ASC(MID$(Y$,1,1)) AND ASC(MID$(Y$,2,1)) AND ASC(MID$(Y$,3,1)))<>0 THEN PRINT"**Error in SOH":Y$="":PRINT #1,NAK$:GOTO 4525
4585 IF ASC(MID$(Y$,2,1))=SEC-1 THEN PRINT"**Requesting Next Block":PRINT#1,ACK$:GOTO 4520
4590 IF SEC<>ASC(MID$(Y$,2,1)) THEN PRINT"**Block # Error in #";BLK:GOTO 4615
4595 IF (SEC XOR 255)<>ASC(MID$(Y$,3,1)) THEN PRINT"**Complement Error in #";BLK:GOTO 4615
4600 FOR I=1 TO 128:CK=CK+ASC(MID$(X$,I,1)):NEXT
4605 IF (CK AND 255)=(ASC(MID$(Y$,N,1))) THEN 4620
4610 PRINT"**Checksum Error in #";BLK:
4615 PRINT#1,NAK$;:ECNT=ECNT+1:IF ECNT<12 THEN 4625 ELSE 4645
4620 PRINT"Received Block #";BLK;:SEC=255 AND (SEC+1):PUT#2,BLK:BLK=BLK+1:PRINT#1,ACK$;:PRINT"- verified":ECNT=0
4625 Y$="":CK=0:GOSUB 4965:IF ABORT THEN 4645 ELSE 4530
4630 '
4635 PRINT"***End of File - verified":PRINT#1,ACK$;:GOTO 3010
4640 PRINT"***Cancelled by Transmitter":GOTO 3010
4645 PRINT"***Cancelled by Receiver":PRINT#1,CAN$;:GOSUB 4975:GOTO 3010
4650 '
4700 '
4710 PRINT"===TRANSMIT FILE WITH XMODEM===":PRINT
4715 SEC=0:BLK=0:CNT!=0:ECNT=0:EOT=0:ETT=0:GOSUB 4815
4720 PRINT"***Holding for Start...":GOSUB 4975:ABORT=0:SECZ=0:GOSUB 4985
4725 WHILE NOT EOF(1):Z$=INPUT$(1,#1)
4730 IF Z$=NAK$ THEN 4800
4735 IF Z$=CAN$ THEN 4855
4740 WEND:GOSUB 4965:IF ABORT THEN 4860
4745 GOSUB 4990:IF NOT TENSEC THEN 4725 ELSE GOSUB 4995:GOTO 4725
4750 '
4755 ABORT=0:SECZ=0:GOSUB 4985
4760 WHILE NOT EOF(1):Z$=INPUT$(LOC(1),#1)
4765 IF Z$=ACK$ THEN ECNT=0:PRINT "- verified ":IF NOT EOT THEN 4800 ELSE IF NOT ETT THEN 4845 ELSE 4850
4770 IF Z$=NAK$ THEN ECNT=ECNT+1:IF ECNT>12 THEN 4860 ELSE IF NOT EOT THEN 4805 ELSE 4845
4775 IF Z$=CAN$ THEN 4855
4780 WEND:GOSUB 4965:IF ABORT THEN 4860
4785 GOSUB 4990:IF NOT TENSEC THEN 4760
4790 GOSUB 4995:IF NOT ABORT THEN IF NOT EOT THEN 4805 ELSE 4845 ELSE 4860
4800 A$=Y$:PRINT"Sending Block #";BLK;:PRINT#1,A$;:IF CNT!<FLN! THEN GOSUB 4815:GOTO 4755 ELSE EOT=-1:GOTO 4755
4805 ECNT=ECNT+1:IF ECNT>12 THEN 4860 ELSE PRINT:PRINT"***Re-sending block...";:PRINT#1,A$;:GOTO 4755
4810 '
4815 BLK=BLK+1:CNT!=CNT!+128:GET#3,BLK:Y$=X$:IF CNT!<=FLN! THEN 4825
4820 Y$=MID$(Y$,1,128-(CNT!-FLN!))+STRING$(CNT!-FLN!,CHR$(0))
4825 CK=0:FOR I=1 TO LEN(Y$):CK=CK+ASC(MID$(Y$,I,1)):NEXT:CK=(CK AND 255)
4830 IF CK>256 THEN CK=CK-256:GOTO 4830
4835 SEC=(255 AND BLK):Y$=SOH$+CHR$(SEC)+CHR$(SEC XOR 255)+Y$+CHR$(CK):RETURN
4840 '
4845 PRINT#1,EOT$;:PRINT"***Sending End Marker ";:ETT =-1:GOTO 4755
4850 CLOSE #3:GOTO 3215
4855 PRINT:PRINT"***Cancelled by Receiver":CLOSE#3:GOTO 3210
4860 PRINT:PRINT"***Cancelled by Transmitter":CLOSE#3:PRINT#1,CAN$;:GOTO 3210
4865 '
4900 '
4905 Z$="":ZA=0
4910 IF NOT EOF(1) THEN Z$=INPUT$(LOC(1),#1):RETURN ELSE DELAY!=1:GOSUB 30000:ZA=ZA+1
4915 IF ZA>72 THEN RETURN ELSE 4910
4920 '
4925 ABORT=0:SECZ=0:GOSUB 4985
4930 GOSUB 4905:GOSUB 4965:IF ABORT THEN RETURN
4935 IF LEFT$(Z$,1)=SOH$ THEN RETURN
4940 IF LEFT$(Z$,1)=EOT$ THEN RETURN
4945 IF LEFT$(Z$,1)=CAN$ THEN RETURN
4950 GOSUB 4975:PRINT#1,NAK$;
4955 GOSUB 4990:IF NOT TENSEC THEN 4955 ELSE GOSUB 4995:GOTO 4930
4960 '
4965 B$=INKEY$:IF LEN(B$)<2 THEN RETURN ELSE Q$=MID$(B$,2,1):IF Q$=CHR$(19) OR Q$=CHR$(20) THEN ABORT=-1:RETURN ELSE RETURN
4970 '
4975 WHILE NOT EOF(1):Z$=INPUT$(LOC(1),#1):WEND:RETURN
4980 '
4985 SECX=60*VAL(MID$(TIME$,4,2))+VAL(MID$(TIME$,7,2)):RETURN
4990 TENSEC=0:SECY=60*VAL(MID$(TIME$,4,2))+VAL(MID$(TIME$,7,2)):IF SECY-SECX<10 THEN RETURN ELSE TENSEC=-1:RETURN
4995 IF SECZ<9 THEN GOSUB 4985:SECZ=SECZ+1:RETURN ELSE ABORT=-1:RETURN
4996 '
5000 '
5010 CLS:PRINT:PRINT"===COMMUNICATIONS PARAMETERS===
5015 PRINT:PRINT"Present parameters: ";:GOSUB 5100:PRINT"Options:
5020 PRINT"   1 -  300,E,7,1  (text)      2 -  300,N,8,1  (binary)
5025 PRINT"   3 - 1200,E,7,1  (text)      4 - 1200,N,8,1  (binary)
5030 PRINT SPACE$(15);"F - reset params to defaults
5035 PRINT SPACE$(15);"X - exit to terminal
5040 PRINT"Choose: ";
5045 Q$=INPUT$(1):GOSUB 2555
5050 IF Q$="X" THEN PRINT Q$:PRINT:PRINT"(Present parameters still in effect)":GOTO 5095
5055 IF Q$="F" THEN PRINT Q$:GOSUB 5815:PRINT:PRINT"Parameters reset to:";:GOSUB 5100:GOTO 5095
5060 Q=VAL(Q$):IF Q<1 OR Q>4 THEN GOTO 5045 ELSE PRINT Q
5065 BAU$="300":PAR$="E":DTA$="7":STP$="1
5070 IF Q=2 THEN PAR$="N":DTA$="8
5075 IF Q=3 THEN BAU$="1200
5080 IF Q=4 THEN BAU$="1200":PAR$="N":DTA$="8
5085 LOCATE ,,1:COMM$=COMMPORT$+BAU$+","+PAR$+","+DTA$+","+STP$+COMMINIT$:CLOSE#1:OPEN COMM$ AS #1
5090 PRINT:PRINT"New parameters are: ";:GOSUB 5100
5095 PRINT GO$:GOSUB 2800:GOTO 515
5100 COLOR BG,FG:PRINT MID$(COMM$,6,10);:COLOR FG,BG:PRINT:PRINT
5105 PRINT"Echo-";:IF ECH=-1 THEN PRINT"Y"; ELSE PRINT"N";
5110 PRINT" Mesg-";:IF MSG=-1 THEN PRINT"Y"; ELSE PRINT"N";
5115 PRINT" Strip-";:IF NS=0 THEN PRINT"N"; ELSE PRINT USING"#";NS;
5120 PRINT" Pace-";:IF PC$="" THEN PRINT"N" ELSE PRINT PC$
5125 IF NS=0 THEN PRINT:RETURN ELSE FOR I=1 TO NS:PRINT"Strip #";:PRINT USING"#";I;:PRINT" - /";:PRINT USING"###";ASC(S$(I));:PRINT"/";:IF R$(I)="" THEN PRINT"000"; ELSE PRINT USING"###";ASC(R$(I));
5130 PRINT"/":NEXT:PRINT:RETURN
5135 '
5200 '
5210 CLS:PRINT"===SET NEW DEFAULTS===":PRINT:COLOR BG,FG:PRINT" Present program defaults:";SPACE$(53);:COLOR FG,BG:EXIT=0
5215 FOR I=1 TO DFNUM:J=I+4:P=1:IF I>15 THEN J=I-11:P=32
5220 LOCATE J,P,0:PRINT DP$(I);:LOCATE J,P+16:IF D$(I)>=" " THEN PRINT D$(I); ELSE IF D$(I)="" THEN PRINT "''"; ELSE IF D$(I)=CHR$(0) THEN PRINT "0"; ELSE COLOR HI,BG:PRINT CHR$(ASC(D$(I))+64);:COLOR FG,BG
5225 IF I<15 THEN PRINT SPACE$(12-LEN(D$(I))); ELSE PRINT SPACE$(30-LEN(D$(I)));
5230 NEXT:LOCATE ,,1:IF EXIT THEN 5280
5235 LOCATE 21,1:COLOR BG,FG:PRINT" Enter ";ENT$;" to leave unchanged - <space>";ENT$;" for 'null' value - <ESC>";ENT$;" to quit ":COLOR FG,BG
5240 PRINT"*** Enter new values":ABORT=0:FOR I=1 TO DFNUM:J=I+4:P=1:IF I>15 THEN J=I-11:P=32
5245 IF ABORT THEN 5265
5250 IF D$(I)<>"" THEN LOCATE J,P+17+LEN(D$(I)) ELSE LOCATE J,P+19
5255 IF I>15 THEN QL=16 ELSE QL=4
5260 GOSUB 2500:IF Q$=CHR$(27) THEN GOSUB 2655:GOSUB 2655:ABORT=-1 ELSE IF Q$<>"" THEN D$(I)=Q$:IF D$(I)=" " THEN D$(I)=""
5265 NEXT
5270 GOSUB 5295:PRINT"*** New values ok (y/n)?";:Q$=INPUT$(1):PRINT Q$:GOSUB 2555:IF Q$="N" THEN GOSUB 5295:LOCATE 21,1:PRINT SPACE$(79);:LOCATE 21,1:PRINT"(default routine cancelled)":GOTO 5290
5275 EXIT=-1:GOSUB 5295:PRINT"*** Make these changes permanent (y/n)?";:Q$=INPUT$(1):PRINT Q$+" ...wait";:GOSUB 2555:IF Q$="Y" THEN GOSUB 5440:GOTO 5215 ELSE GOSUB 5600:GOTO 5215
5280 GOSUB 5815:CLOSE#1:OPEN COMM$ AS #1
5285 GOSUB 5295:LOCATE CSRLIN-1,1:PRINT SPACE$(79);:LOCATE CSRLIN,1
5290 COLOR FG,BG,BG:PRINT GO$:GOSUB 2800:GOTO 515
5295 LOCATE 22,1:PRINT SPACE$(79);:LOCATE 22,1:RETURN
5400 '
5405 RESTORE 5410:FOR I=1 TO DFNUM:READ DP$(I),D$(I):NEXT:GOSUB 5440:GOTO 300
5410 DATA Baud rate,300,Parity,E,Data bits,7,Stop bits,1,Echo,N,Messages,N
5415 DATA"Strip #1",0,Replace #1,0,"Strip #2",0,Replace #2,0,"Strip #3",0,Replace #3,0,Pacing p=,,Logged drive,"B:",Margin width,70
5420 DATA Screendump file,"B:SCRNDUMP.PCT",Redial delay,20,Connect prompt,CONNECT
5425 DATA Line 25 help,Y,Foreground,7,Background,0,High inten.,15
5430 DATA "Print port","LPT1:","Print init.",,"Print width",80
5435 DATA Comm. port,"COM1:",Comm. init.,",CS,DS",Modem init.,,C/R subst.,"}"
5440 CLOSE#1:OPEN FFIL$ FOR OUTPUT AS #1:WRITE#1,IFIL$:FOR I=1 TO DFNUM:WRITE#1,DP$(I),D$(I):NEXT:WRITE#1,IFIL$:GOSUB 5600:RETURN
5600 '
5605 BAU$=D$(1):PAR$=D$(2):DTA$=D$(3):STP$=D$(4)
5610 I=5:GOSUB 5805:IF D$(5)="Y" THEN DECH=-1 ELSE D$(5)="N":DECH=0
5615 I=6:GOSUB 5805:IF D$(6)="Y" THEN DMSG=-1 ELSE D$(6)="N":DMSG=0
5620 DNS=0:FOR J=1 TO 3:I=2*J+5:GOSUB 5810
5625 DS$(J)=CHR$(VAL(D$(I))):IF DS$(J)<>CHR$(0) THEN DNS=DNS+1 ELSE D$(I)