PackCom

                                   Display Version

                                         by

                                Jim Wright  (WB4ZJV)
































                                Documentation Manual

                                         by

                               Lloyd Phelps  (WD5HEH)







                                      OVERVIEW

          PackCom  is  a  program  written  for  PC's  and  compatibles  to
          facilitate  using  the PC with a TNC for communicating via packet
          radio.

          Any terminal emulation program  will  work  so  long  as  it  can
          address the serial port that the TNC is connected to, but PackCom
          is  unique in that it is written to make communicating via packet
          more enjoyable.   The help menus built into the program  make  it
          very  easy to use to the point of almost not needing a documenta-
          tion manual.

          If your PC has a color monitor,  PackCom can present you  with  a
          variety of colors, bells and whistles that you define for viewing
          the various packets that you send or receive.

          PackCom in its distribution form contains three files:

               PACKCOM.COM    The program.
               PACKCOM.000    Overlay file.
               PACKCOM.001    Overlay file.

          PackCom  will  create three additional files the first time it is
          run:

               PACKCOM.CNF    This  file  contains  the   program   default
                              parameters.   What communication port to use,
                              baud rate, parity, etc.

               PACKCOM.KEY    This file contains the macro key  definitions
                              that  you specify.   These macros can contain
                              such information as your QTH,  station equip-
                              ment, etc.

               PACKCOM.WRD    This  file  contains  key words to search for
                              and any special effects to perform  when  the
                              key word is found.







                                   GETTING STARTED

          To start the program, enter the command PACKCOM at the DOS prompt
          and press <ENTER>.  After the program loads you will be presented
          with the program logo containing the version number and  date  of
          release.   Next, press any key to clear the screen and get to the
          communications screen.

          Entering PACKCOM /V at the DOS  prompt  and  press  <ENTER>  will
          eliminate  the need for pressing a key at the PackCom logo screen
          to get to the communications screen.

          Entering PACKCOM /I at the DOS prompt will take  you  immediately
          to the operating defaults screen where you may view/change any of
          the  operating  parameters  before  actually running the program.
          Once changes have been made, if any,  you will be returned to the
          DOS prompt.

          The  communications screen is divided into two sections,  the top
          section is the Communications Buffer and  is  used  for  incoming
          packets  and  commands echoed by the TNC.   The bottom section is
          the Keyboard Buffer area.  Commands to the TNC and information to
          be transmitted is entered here and can be edited before  pressing
          <ENTER>.    Also,  previously  entered  lines can be recalled for
          editing and retransmission.

                                     HELP SCREEN

          Press ALT-H and a help screen will be displayed with the  various
          ALT-(key) commands and brief descriptions of their functions.

                                  PROGRAM DEFAULTS

          To view the communication port parameters,  press ALT-P.  Default
          settings are 1200 BAUD,  NO PARITY,  8 DATA BITS and 1 STOP  BIT.
          You  will be prompted to enter BAUD RATE,  PARITY,  DATA BITS and
          STOP BITS.   Pressing <ENTER> at the prompts will  leave  startup
          values unchanged.  Entering a new value and pressing <ENTER> will
          select  the  new  value.   Whether the values are changed or not,
          PackCom assumes you have changed the values  and  will  automati-
          cally save the parameters.   Set BAUD RATE, PARITY, DATA BITS and
          STOP BITS according to values needed  to  communicate  with  your
          TNC.

          Next press ALT-I to view/change operating defaults.

          Options 1 through 5 are changed using the ALT-P option.

          Option 6 is reserved for future use.

          Option 7 specifies the number of lines to maintain in the receive
          buffer.  Default is 250.

                                          1







          Option  8  specifies  whether  to  allow incoming bells (CTRL-G).
          Default is NO.

          Option 9 specifies whether to eliminate blank lines.   Default is
          NO.

          Option  10 specifies how often to display the date/time depending
          upon the setting of Option 11.

          Option 11 specifies whether to display time.  Default is YES.

          Option 12 allows you change display colors if you  have  a  color
          monitor.   Foreground color is CYAN.   Background color is BLACK.
          Reverse image foreground color is GREEN.    Reverse  image  back-
          ground  color is BLUE.   High intensity foreground color is LIGHT
          RED.  Border color is BLACK.

          Option 13 (forgotten) is reserved for future use.

          Option 14 specifies the amount of delay between characters  being
          sent to the TNC.   Default is 0.  Maximum delay is 32 seconds be-
          tween characters.

          Option 15 specifies the amount of delay after  sending  CR/LF  to
          the  TNC.    Default  is 0.   Maximum delay is 32 seconds between
          lines.

          Option 16 specifies the amount of memory in KBYTES to reserve for
          DOS programs.  Default is 30.

          Option 17 specifies the DOS program to execute.   The default  is
          COMMAND.COM.

          Option  18  specifies  whether  to  set  the TNC's date and time.
          Default is YES.

          Option 19 specifies the DRIVE/PATH to  PackCom's  overlay  files.
          Default is ".",  which specifies the drive/path where PackCom was
          started from.

          Option 20 speciies the SWITCH STREAM CHARACTER used.   Default is
          vertical bar (|).

          Options 7, 16, 18 and 19, if changed, require you to exit PackCom
          and restart the program for the changes to become effective.

                            SPECIAL EFFECTS CONFIGURATION

          Press ALT-A to bring up the Special Effects Configuration screen.

               1.   Configure Keyboard/Digi echo colors.


                                          2







               2.   Configure Non-Header colors.

               3.   Configure Key Words to search.

                    Example setup:

                    *** CONNECT     YELLOW  BLUE   ALARM
                    ZJV             YELLOW  BLUE   BELL
                    JIMZ            RED     BLACK  BELL
                    PACKCOM         RED     BLACK  BELL

               4.   Toggle  Key  Word beeps ON/OFF.   This parameter allows
                    you to turn off the beeps and  alarms  but  retain  the
                    special coloring.

               5.   Toggle  Key  Word  coloring  and  beeps  ON/OFF.   This
                    parameter controls both the special coloring and beeps.

                              FUNCTION KEY DEFINITIONS

          Press ALT-M to view/change/edit the function key definitons.    A
          total  of  40  definitions  can  be obtained from the 10 function
          keys.   F1  through  F10,  SHIFT-F1  through  SHIFT-F10,  CTRL-F1
          through CTRL-F10 and ALT-F1 through ALT-F10.





























                                          3

      section is the Communications Buffer and  is  used  for  incoming
          packets  and  commands echoed by the