PK232COM VERSION 1.45  PAGE 1


                     PK232COM Version 1.45 (c) 1987 by G3ZCZ

         
                  (C) Copyright 1987 - All Rights Reserved 

                               By Joe Kasser G3ZCZ
                                    POB 3419,
                                  Silver Spring,
                                 Md., 20901, USA.

        A Personal Packet Terminal Program for the TNC1, TNC2 and most of 
        all for the PK232.


             PK232COM is written and supported by Joe Kasser, G3ZCZ.

        The program is distributed as a Shareware product. You may freely 
        copy  and  share the product for non commercial  use,  with  your 
        friends,  associates  and other radio hams.  If you decide to use 
        the product, you are asked to become a registered user by sending  
        a QSL card and a contribution  to the author (suggested amount of 
        $35.00 or equivalent in foreign currency.

        The  contribution covers the cost of distribution of the  updated 
        disk,  and  supports  the continual development of "Software  for 
        Amateur  Radio".   Upon receipt of your  contribution,  you  will 
        receive  one  free update disk CUSTOMISED with YOUR CALLSIGN  (if 
        you write the type of TNC on the QSL card.), mail (electronic and 
        regular)  support,  and notice of further releases.   The  update 
        disk  will contain any new versions of the software on this  disk 
        plus  any  new  software,  accompanying the  series  of  articles 
        currently  being written on the applications of  data  processing 
        concepts of microcomputers to amateur radio.

        This  product may not be sold or distributed with another product 
        without the express written permission of Joe Kasser, G3ZCZ. 


        Joe  Kasser,  G3ZCZ  will only support unmodified copies of  this 
        software.   Your comments and suggestions for changes are however 
        welcome.   If  you  are  the first to suggest a  change  that  is 
        implemented,  you  will be sent a complimentary copy of the  disk 
        with the change incorporated.

        Potential Commercial Users please contact Joe Kasser directly for 
        details of Site licensing.











        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 2


                                    CONTENTS
                                  -------------
        1.0  INTRODUCTION

        1.1  PROGRAM HIGHLIGHTS
        1.1.1     MORSE/BAUDOT/AMTOR/ASCII
        1.1.2     PACKET RADIO

        2.0  CRT DISPLAY
             2.1  Status Display
             2.2  Incoming Text Display
             2.3  Outgoing Text Display
             2.4  Command/Status Display.
             2.5  Alarm Tones.

        3.0  Function keys.
             3.1  Function Keys
                       3.1.1    Capture to Disk Toggle
                       3.1.2    Transmit a file
                       3.1.3    CAllsign Sequence.
                       3.1.4    Brag tape
                       3.1.5    Call CQ
                       3.1.6    Change Communications Modes
                       3.1.7    Call/Connect 
                       3.1.8    Disconnect or Receive
                       3.1.9    Command Mode
                       3.1.10   Transmit Mode

             3.2  Alt Function keys
                       3.2.1    Exit or return to DOS.
                       3.2.2    Initialize the PK-232.
                       3.2.3    Connect Status
                       3.2.4    Set Terminal Mode
                                3.2.4.1   SOLO
                                3.2.4.2   TRAFFIC
                                3.2.4.3   CQ/BEACON
                                3.2.4.4   READ THE MAIL
                                3.2.4.5   Multiple Connect Modes.
                                          3.2.4.5.1 The Individual  Multi 
                                                     Connect Mode.
                                          3.2.4.5.2  The Conference Multi 
                                                     Connect Mode.
                                          3.2.4.5.3  Entering      the 
                                                     conference mode
                                          3.2.4.5.4  Connecting  in  the 
                                                     multi user mode
                                3.2.4.6   FEC 
                                3.2.4.7   ALISTEN 
                                3.2.4.8   ACHG 
                                3.2.4.9   ARQ 
                                3.2.4.10  Force LETTERS Case
                                3.2.4.11  Override Mailbox/Beacon.
                                3.2.4.12  Turn on Mailbox/Beacon.
                            
                       3.2.5    Monitor Channel Activity


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 3


                       3.2.6    Change Packet Connect / Contest / CQ text 
                                Message
                                3.2.6.1 Change Packet Connect Message
                                3.2.6.2 Change Contest Message
                                3.2.6.3 Change CQ text Message
                       3.2.7    Enter Call Sign
                       3.2.8    Not used. 
                       3.2.9    Activate Transmit Buffer
                       3.2.10   Help

             3.3  Shift Function Keys
                       3.3.1     Dir
                       3.3.2     Rename
                       3.3.3     List of Outgoing Messages to be sent.
                       3.3.4     Delete
                       3.3.5     List of messages that have been sent.
                       3.3.6     Mail Beacon Activate
                       3.3.7     Retry a call/connect request
                       3.3.8     Not used. 
                       3.3.9     Connected Indicator Reset. 
                       3.3.10    OVER function.

             3.4  Control Function Keys
                       3.4.1     Day Flag
                       3.4.2     CWID
                       3.4.3     Message Uploading 
                                3.4.3.1   Leaving a Note in your system.
                                3.4.3.2   Leaving  a message on an  other 
                                          PK232COM system [QSP].
                                3.4.3.3   Uploading  messages to  another 
                                          PK232COM system.
                       3.4.4     Show last few log entries. 
                       3.4.5     Automatic CQ Sender
                       3.4.6     SELCAL
                       3.4.7     Beacon  Activate  Toggle/CQ  Wait  Delay 
                                 Adjust.
                                3.4.7.1   Beacon Mode Toggle/On-Off
                                3.4.7.2   CQ Delay Time Adjust
                       3.4.8     Not used. 
                       3.4.9     Transmit Buffer Clear
                       3.4.10    Log QSO
             3.5  Shift/Baudrate Control keys
                       3.5.1     The RIGHT ARROW Key (Increase Baudrate).
                       3.5.2     The LEFT ARROW Key (Decrease Baudrate).
                       3.5.3     The UP ARROW Key (Change shift).
                       3.5.4     The DELETE Key (toggle USOS).

             3.6  Additional keys
                       3.6.1     The HOME Key.
                       3.6.2     The DOWN ARROW key.
                       3.6.3     The Alt A key (Alert Call Set/Toggle).
                       3.6.4     The Alt B key (BAUDOT/ASCII  baud  Rate 
                                               Set Key).
                       3.6.5     The Alt C key (Connect/Call).
                       3.6.6     The Alt D key (Display Inhibit).


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 4


                       3.6.7     The Alt F key (Digipeat Monitor Set/Toggle).
                       3.6.8     The Alt P key (Printer Toggle).
                       3.6.9     The Alt R key (Message Relay toggle).
                       3.6.10    The Alt S key (Sound Set/Toggle).
                       3.6.11    The Alt T key (Target Call Set/Toggle).
                       3.6.12    The Alt X key (Exit or return to DOS).
                       3.6.13    The PgUp key  (Scrolls back Incoming).
                       3.6.14    The Control Z key (AMTOR +?).

        4.0  PK232COM disk files
             4.1  PK232COM.COM
             4.2  PK232COM.RUN
             4.3  PK232COM.SYS
                  4.3.1     The callsign. 
                  4.3.2     The AMTOR SELCAL. 
                  4.3.3     The CQ Text.
                  4.3.4     The fourth and fifth lines (Band and Power).
                  4.3.5     The CQ Delay time.
                  4.3.6     The Message Relay Capability (QSP).
                  4.3.7     The Communications Port.
                  4.3.8     The TNC type.
                  4.3.9     The Terminal Baud Rate.
                  4.3.10    The QTC_Snatch flag
                  4.3.11    The remaining lines. 
             4.4  PK232COM.LOG
             4.5  PK232COM.DIR
             4.6  CONFIG.SYS
             4.7  *.MBX

        5.0  Initialization

        6.0  Running the Program

        7.0  Mailbox features (AMTOR/Packet Modes Only)
             7.1  Answering Machine.
             7.2  Mail Beacon (Annunciator).
             7.3  How to leave a message
             7.4  Remote File Downloading (Packet Mode Only).
             7.5  Remote Beacon shutdown.

        APPENDIX 0. UPDATES/REVISION HISTORY.

        APPENDIX 1. BUGS and anomalies.
                    A1.1 Command/Converse mode anomalies.
                    A1.2 Buffer messages in AMTOR Beacon CQ mode.
                    A1.3 FEC +? responses in AMTOR Beacon CQ mode.
                    A1.4 PK232COM versions 1.00 to 1.39. 
                    A1.5 Using a CGA card with a monochrome monitor.
                    A1.6 The Packet Conference Mode.
                    A1.7 Packet Conference Mode disconnects.
                    A1.8 Slow Screen Updating.
                    A1.9 Strange Events.





        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 5


        APPENDIX 2. MESSAGES IN A LOCAL AREA NETWORK

                    A2.1 LAN Protocol (G3ZCZ Version).
                    A2.2 Message Format.
                    A2.3 File downloading.
                    A2.4 Path Determination to a Dx station.

        APPENDIX 3  BASIC NC/L DICTIONARY

                    A3.1  :QBM: To download a file.
                    A3.2  :QMH: To request a call monitored list ('MH').
                    A3.3  :QSM: To request a repeat of a message.
                    A3.4  :QSP: To leave a message for another station.
                    A3.5  :QRT: To  shut  down  a  packet  mode  beacon 
                                station.
                    A3.6  :QRU: To upload messages. 
                    A3.7  :QNO: Error or function not present/active.
                    A3.8  :QJG: No more messages pending.
                    A3.9  :QRV: Ready for message.
                    A3.10 :QSL: Confirm receipt of message. 
                    A3.11 :QTC: Messsage list.
                    A3.12 :QYU: YAPP format file upload.
                    A3.13 :QYD: YAPP format file download.

        APPENDIX 4. USING OTHER TNC'S.

                    4.1 TNC2 (MFJ 1270)

                    A4.1.1     Default Commands.
                    A4.1.2     Program differences.

                    4.2 TNC1 (HD-4040)

                    A4.2.1     Default Commands.
                    A4.2.2     Program differences.

        APPENDIX 5. NOTES.

        APPENDIX 6. REGISTRATION FORM.


















        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 6


        1.0  INTRODUCTION

        PK232COM  is a Personal Digital Communications  Terminal  Program 
        for  a Packet Radio TNC.   while it takes advantage of the  extra 
        features  of the PK-232 which is made by  Advanced  Electronics 
        Applications Inc.  MANY OF THE PACKET RADIO FEATURES WILL WORK ON 
        A TNC1 AND MOST OF THESE FEATURES SHOULD WORK ON ANY TNC2.  It is 
        designed  to allow anyone to use and get the most out of the  PK-
        232  for  Morse,  ASCII,  BAUDOT,  AMTOR as well as Packet  Radio 
        communications  without having to keep the PK-232 or  other  TNC2 
        manual handy.   

        PK232COM  is  a sophisticated program.   In its  basic  state  it 
        allows  you to use the TNC in an optimal manner.   It  configures 
        the  TNC for you to maximise the communications efficiency in the 
        communications  mode of your choice.   That means,  for  example, 
        when  working  Packet on HF you need to program the  PK232  para-
        meters  to  different values than you would use on  VHF  to  make 
        maximum  use  of  the mode.   One significant difference  is  the 
        length of the packet itself,  for the longer it is,  the  greater 
        the  probability of QRM destroying it.  This program will  adjust 
        the packet parameters for you.

        Since  the  computer is now involved,  other features  have  been 
        added  to  simplify operation,  and several  features  have  been 
        automated.   All  these  operations are performed using  function 
        keys as documented below.   It will take a while to learn how  to 
        use  this program in a manner that suits you,  read this document 
        and  have  fun,  after all,  isn't that one of  the  purposes  of 
        Amateur Radio.

        This  documentation  file is not a manual.  It is  a  preliminary 
        document.   It  is written to remind you of what the program  can 
        do.   If  there is enough interest (registrations) I will  expand 
        it.   It  is  not  designed  to explain  the  theory  behind  the 
        different communications modes.   Read the PK232 Manual for  more 
        information.    This   program   is  designed  to  optimize   the 
        configuration  of  the PK232 in each communications mode  and  to 
        provide some smart terminal features. 

        1.1  PROGRAM HIGHLIGHTS

            1.1.1     MORSE/BAUDOT/AMTOR/ASCII
            Automatic  CQ caller.   Will call CQ repetetively and  signal 
            you when a reply is received. 
            
            SELCAL.

            Automatic capture to disk of all ingoing and outgoing text of 
            any QSO.

            AMTOR/PACKET  Selective  answering machine and MAILBOX  using 
            NC/L command dialog.




        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 7


            1.1.2     PACKET RADIO

            Automatic disk recording of all packet radio connects.  Auto-
            matic indication of Packet connects.  

            AMTOR/Packet  Local  Area  Network (LAN)  message  store  and 
            forward.   

            Capable of automatic connect attempts to download a QTC  from 
            an other station in the LAN.  

            Digipeat monitoring and capture. 

            Alert signal to let you know when a predetermined call  shows 
            up in a packet header on frequency.  

            Conference mode in multi- connect situations. 

            Path determination to Dx station via :QMH:. 

            Indicator  that a specific station designated as the 'target' 
            call   connected   in  Packet  mode,   or  linked  to   AMTOR 
            Beacon/Mailbox while you were away.

            Automatic  NET/ROM  path set up from  PK232COM.DIR  call/path 
            directory file.

            AMTOR/PACKET  Automatic  Answering  Machine  capability  with 
            display of message queue.

            Automatic  Beacon Mode CQ caller in Packet and AMTOR communi-
            cations modes.  

            Will  call  CQ repetitively and either work the  connect  and 
            keep  going  after disconnect or signal you when a  reply  is 
            received.

            Automatic logbook entries for Packet and Mailbox/Beacon  mode 
            AMTOR  Connects,  semi  automatic logbook entries  for  other 
            modes.  

            Log  file is compatible to that of the G3ZCZ CONTEST  program 
            can  be processed by the DBASE  Logbook Package of PC-HAM  by 
            G3ZCZ  for  indexed  listings,  tracking of  DXCC  and  other 
            AWARDS, etc.

            Contest  operation,  sends standard mesage and  automatically 
            increments QSO count.

            Automatic  optimized  configuration of the TNC for each  com-
            munications mode.

            FUNCTION KEY 'OVER' FEATURE

        Morse,  ASCII,  BAUDOT communication modes are HALF DUPLEX.   One  


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 8


        station  is transmitting at any time.   You thus have to use  the 
        Transmit/Converse  and Receive/Disconnect function keys  to  turn 
        the transmitter on and off respectively. 

        AMTOR  is also HALF DUPLEX but has some of the attributes of full 
        duplex.   In  this  mode  you  control  who  is  talking  through 
        software,  only one station can send data at a time,  but you can 
        type  characters in  to the buffer and they will  be  transmitted 
        automatically  when the other station turns the QSO over to  you.  
        Once   you  have  linked  with  someone,   you  do  not  use  the 
        Receive/Disconnect function UNTIL THE QSO IS OVER.  Both stations 
        are communicating automatically thanks to the TNC.   If you  want 
        the  other operator to respond type the +?  key sequence (or  use 
        shift function key 10).  

        Packet  Radio communications  on the other hand is a full  duplex 
        mode  of communications.   Once you have connected with  someone, 
        you  do not use the Receive/Disconnect function UNTIL THE QSO  IS 
        OVER.   Both  stations are communicating automatically thanks  to 
        the  TNC.   If you want the other operator to respond type the  > 
        key followed by the 'Enter' key,  better yet,  use shift function 
        key 10.  

        Note  that  Morse,  AMTOR,  ASCII and BAUDOT are  character  mode 
        communications  in  that each character you type is sent  as  you 
        type them.   In Packet Communications, the TNC stores them up and 
        sends out a burst or packet when you type the 'Enter' key or  you 
        type enough characters to fill up a packet.   Studies have  shown 
        that  the human attention span when sitting at the keyboard is of 
        the  order  of 2 seconds.  If you are in a keyboard  to  keyboard 
        packet radio connect,  remember this and don't forget to use  the  
        'Enter'  frequently,  especially  before you stop to think  about 
        what to send next.

        Any  Terminal  Node  Controller  (TNC)  is  a  complex  piece  of 
        equipment.   It can operate in a Command Mode,  in which you tell 
        it to do something,  or in a Converse Mode in which you are using 
        it  to talk to other stations.   Many people confuse the two when 
        first  getting on Packet.   If you monitor the channels you  will 
        recognize command mode TNC instructions on the air,  and when you 
        use  the  TNC you will receive the "?error" reply when  you  type 
        something  thinking  that you are in the Converse  Mode  but  are 
        really in the Command Mode.   PK232COM is designed to make Packet 
        operation simple using high level (Function key) commands.

        This Version has the following functions built in to it in a menu 
        driven format.

        Morse Code  20 wpm (CW).

        BAUDOT  with default of 45 WPM narrow shift (LSB).   You may  set 
        other  baud rates directly,  or use the left and right arrow keys 
        to change the baud rate (see below).




        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 9


        ASCII  with default 110 BAUDS narrow shift (LSB).   You  may  set 
        other  baud rates directly,  or use the left and right arrow keys 
        to change the baud rate (see below).

        Packet VHF or HF baud rates and shifts (LSB).

        AMTOR 100 BAUDS narrow shift (LSB).

        All  communications between the computer and the TNC normally use 
        COMM1  and operate in the 8 BIT NO PARITY and 1 stop  bit  RS-232 
        Serial Port configuration.  You CAN SEND FOREIGN LANGUAGE CHARAC-
        TERS  FROM  THE  KEYBOARD OR FILES.   If you want  to  limit  the 
        character  set  to the 7 bit ASCII set,  set the  TNC  parameters 
        accordingly.   The baud rate defaults to 1200, but you may set it 
        to 2400, 4800 or even 9600 if your CPU clock is fast enough.

        Access  to  the  TNC Command mode is provided in  case  the  user 
        wishes  to  override  any  of these defaults.

        IF YOU USE THIS PROGRAM, YOU STILL MUST READ THE TNC MANUAL.

        Note   that   AMTOR   and  PACKET  are  full  duplex   modes   of 
        communications.   When you connect with someone, there is no need 
        to use the transmit and receive function keys.   In fact you will 
        have  problems  if you do.   Do not disconnect until the  QSO  is 
        over.

        WARNING  ....   THIS PROGRAM OPERATES IN AN OPEN LOOP  MODE.   IT 
        REMEMBERS WHAT INSTRUCTIONS OR COMMANDS IT GAVE THE TNC.   IF FOR 
        SOME REASON,  THE TNC IS NOT SYNCHRONIZED TO THE PROGRAM YOU WILL 
        NOT GET CORRECT DISPLAYS ON THE SCREEN.

        2.0  CRT DISPLAY

        The CRT display contains four areas as follows.

        -------------------------------------------------
        |             STATUS DISPLAY                    |
        -------------------------------------------------
        |                                               |
        |                                               |
        |             INCOMING TEXT DISPLAY             |
        |                                               |
        |                                               |
        |                                               |
        -------------------------------------------------
        |             OUTGOING TEXT DISPLAY             |       
        |        ____________________________           |
        |       |____________________________|          |
        |                                               |
        -------------------------------------------------

             2.1  Status Display

             A  one  line display at the top of the  screen  showing  the 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 10


             status of the communications system.

             The  left side of the screen normally displays the  "capture 
             to  disk"  or  logging status,  the  center  of  the  screen 
             displays  status  information  depending  on  which  of  the 
             operational modes is active.

             2.2  Incoming Text Display

             The  center section of the screen displays data coming  back 
             from the TNC.   This consists of data received via the radio 
             communications link,  TNC status information and transmitted 
             data echoed back by the TNC.

             2.3  Outgoing Text Display

             The  lower area of the screen shows data being sent  to  the 
             TNC.   This consists of command data from the program to the 
             TNC, text typed by the user and files being transmitted.

             2.4  Command/Status Display.

             This  screen  located above the Outgoing Text Display  shows 
             the  command dialog between the program (PK232COM)  and  the 
             TNC.  If  you  want to see the dialog,  set the  TNC  'ECHO' 
             parameter to 'ON'.  The default should be 'OFF'.

             2.5  Alarm Tones.

             PK232COM  sounds a different number of alarm tones or chimes 
             according to the following events;

             1    Digipeat Detected. 
                  File Alarm Error.
             2    PK232COM :QTC:  message detected,  automatic QTC_Snatch 
                  connect request in progress.
                  Tones toggled back on.
             3    Alert Call heard in packet header.
             5    Somebody connected.

             The  alarm  tones  may be toggled ON/OFF  by  means  of  the 
             Alternate S key.

        3.0  Function keys.

        PK232COM  can be used as a simple Terminal Interface Program with 
        the  10  main function keys.   The control,  alternate and  shift 
        function keys provide advanced features.  You should first become 
        familiar with the function keys described in Section 3.1 and then 
        expand  your  use  of the program to  incorporate  the  remaining 
        expanded function keys.  Don't try to learn them all at once.






        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 11


        The operation of each of the function keys are explained below.

             3.1  Function Keys

                       3.1.1    Capture to Disk Toggle
                       This  key toggles the "capture to disk"  function.  
                       When  the  function is active,  all incoming  text 
                       (including 'Echo as sent' outgoing text) is stored 
                       on  a  disk  (floppy or hard)  in  a  file  called 
                       'PK232COM.RUN'.   If  this file does not exist the 
                       first time that PK232COM is loaded, it is created.  
                       From that time on,  successive activations  append 
                       new data to the contents of the file.

                       Each  time the function is activated  a  datestamp 
                       (or timetag) will be written to the file.

                       When  a  Packet station connects the  'capture  to 
                       disk'  function  will be  activated  automatically 
                       even  if  you  have  not  set  it  active.  Packet 
                       connects  will thus be recorded in their  entirety 
                       automatically  unless you turn off the 'Capture to 
                       disk' during the course of the QSO.  The  function 
                       will  be deactivated at disconnect time unless you 
                       have toggled it on.

                       You  may  later edit the file at your  convenience 
                       with your favorite word processor.

                       PK232COM  will automatically close the log capture 
                       file when you terminate the program and return  to 
                       DOS.

                       3.1.2    Transmit a file
                       This function allows you to transmit an ASCII file 
                       via  the PK-232.   You may abort the  transmission 
                       sequence  at  any  time by depressing any  of  the 
                       function keys,  the keys on or associated with the 
                       numerical pad, or the ESC key.  

                       During the file transfer,  the status window  will 
                       show the different states of the transmission.  It 
                       begins  with  a signal that the message  is  being 
                       sent.   If  the  text  is long and fills  the  TNC 
                       buffer,  you  will see a message 'QRX  TNC  BUFFER 
                       FULL'  possibly followed by  'TNC NOT RESPONDING'. 
                       This  latter message will seem to blink  periodic-
                       ally.   When  the TNC signals that it is ready  to 
                       accept  more  text,   the  message  sequence  will 
                       resume.

                       In the Packet Communications mode,  when the  file 
                       has been loaded into the TNC the computer will add 
                       the ^Z character to the outgoing text to signal to 
                       the  recipient that the file transmission is over.  


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 12



                       The  computer  will  signal you  (using  the  bell 
                       character,  when the file has been loaded into the 
                       TNC,   Note  that is not the same as the time that 
                       the TNC has transmitted the file,  because the TNC 
                       incorporates a character buffer.

                       3.1.3   Call Sign Sequence.
                       This  function  lets  you transmit  the  following 
                       sequence <other call) DE <your call>.  For example 
                       if  you are 4X6AA and you are working  G3ZCZ  then 
                       this function would transmit the sequence G3ZCZ de 
                       4X6AA.    You   use   this  at  the  start  of   a 
                       transmission in any mode except Packet.

                       3.1.4    Brag tape
                       This  function  allows you to transmit a  standard 
                       text file historically known as a "Brag Tape"  via 
                       the  TNC.   The  brag  tape file  must  be  called 
                       PK232COM.TXT,  and  should be created with a  word 
                       processor in the non-document mode.   Transmission 
                       of  the Brag Tape may aborted in a similar  manner 
                       to that of a regular file (see above).

                       3.1.5    Call CQ
                       You  use  this function key to call  CQ.   In  the 
                       Packet Communications mode,  the TNC will transmit 
                       a line of text along with the CQ packet.  The line 
                       of  text  is set up in the PK232COM.SYS file  des-
                       cribed in section 4.
                        
                       In the AMTOR communications mode, your SELCAL will 
                       be  transmitted along with the CQ call in the  FEC 
                       mode.

                       3.1.6    Change Communications Modes
                       This   function   allows   you   to   change   the 
                       communications  mode  of  the  PK-232.   Allowable 
                       modes are Morse code, BAUDOT, AMTOR standby, AMTOR 
                       Alisten,  ASCII, Packet and Signal.   In the Packet 
                       mode  you  can  choose VHF or HF  operation  in  a 
                       single step by entering the letters V or H.

                       When  you  select the AMTOR standby mode  you  are 
                       placed  into the 'standby receive' mode.   If  you 
                       want to read the mail on an existing AMTOR QSO  in 
                       progress,  select  the AMTOR Alisten or  chirpcopy 
                       mode.   If you are in AMTOR standby mode, you will 
                       not be able to see signals of the chirpcopy mode.

                       Use  the 'G' option to select the  'SIGNAL'  mode.  
                       Read   the   PK232  documentation   carefully   to 
                       understand  how this mode works.   Once the  PK232 
                       has identified the digital signal it is tuned  to, 
                       use the same function key a second time to  select 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 13


                       the relevant mode and set the baud rates and shift 
                       to display the data.

                       3.1.7    Call/Connect 
                       You  use this function to call a station heard  on 
                       the  band,  or to attempt a connect  with  another 
                       packet station.  You may also use it to call 'QRZ' 
                       or even 'TEST'.

                       In  AMTOR the call will be sent in the ARQ mode to 
                       the SELCAL of the desired station.

                       In the Packet Communications mode you can create a 
                       directory  file  and  keep  a list  of  names  and 
                       callsigns.   The computer will look up a name  and 
                       call the station by its callsign.   For example if 
                       you  put 
                                 Joe G3ZCZ
                       as a line in the file,  when you tell the computer 
                       to  connect  to  Joe,  it will try to  connect  to 
                       G3ZCZ.   If you enter 
                                 4X4HF  4X4HF V 4X1AA 4Z4ZB 4X4IL  
                       you  only  need  to type '4X4HF'  to  set  up  the 
                       correct  connect  path.   See section  4.5   which 
                       describes    the  PK232COM.DIR  file  for  further 
                       information.

                       You  can also use this function key to  automate a 
                       NET/ROM  path connection.   In the manual  NET/ROM 
                       path  setting up mode,  you would first connect to 
                       your local node,  then when you are connected with 
                       it,  connect  to the next node,  and so on through 
                       any  intermediate  nodes  within  the  whole  path 
                       before  you finally connect with your  destination 
                       station.   You may have digipeaters in any of  the 
                       paths.

                       For example if you wish to connect to K1HTV who is 
                       in  range  of  the  SSCT  node,  and  you  are  in 
                       Washington DC,  you would first have to connect to 
                       your   local   NET/ROM  node   (ELK),   then   the 
                       intermediate  nodes,  SNJ3,  NNJ,  WMA before  you 
                       could try to connect with K1HTV.

                       If  you put the following line in the PK232COM.DIR 
                       file

                       K1HTV ELK v WB4APR-5! SNJ3! NNJ! WMA! SCCT! K1HTV

                       the NET/ROM sequence will be automatic.

                       PK232COM will issue a 'disconnect' command to  the 
                       TNC  in  the  event the  NET/ROM  connect  attempt 
                       fails.   This function is designed for known paths 
                       not for general path determination.


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 14



                       In the Packet communications mode,  if you want to 
                       loop  back  through  someone else  enter  the  '/' 
                       character  followed by the call of the station you 
                       want  to  loop back through.   For  example  if  I 
                       (G3ZCZ)  want to loop back through 4X6AA,  I  just 
                       need to enter /4X6AA as the call to connect to and 
                       the  computer will tell the TNC to try to  connect 
                       to G3ZCZ via 4X6AA.

                       In  a  multi  connect situation the  program  will 
                       automatically select a free IO channel to try  the 
                       connect on.

                       3.1.8    Disconnect or Receive
                       This  function  key  returns the  station  to  the 
                       receive communications (PK232 command)  mode.   It 
                       may  also  be  used  to  abort  the  automatic  CQ 
                       sequence.   If  you use it to abort a CQ  sequence 
                       while the transmission is in progress,  flush  the 
                       PK232  transmit buffer using Control function  key 
                       9.

                       In  a  multi  connect situation the  program  will 
                       prompt   you  to  tell  it  which  IO  channel  to 
                       disconnect.

                       3.1.9    Command Mode
                       This  function puts the TNC into the command mode.  
                       At this time,  the program is transparent and acts 
                       as  a dumb terminal (except for  placing  incoming 
                       and  outgoing text in the relevant windows).   you 
                       use  this  mode  for overriding  any  of  the  TNC 
                       default conditions.   (SEE I TOLD YOU THAT YOU HAD 
                       TO READ THE TNC MANUAL).

                       3.1.10   Transmit Mode
                       This  function places the TNC into the transmit or 
                       converse mode.   The transmitter is turned on  and 
                       the  contents of the transmit buffer is  transmit-
                       ted.   In the non packet communications modes, the 
                       outgoing  characters will be echoed back from  the 
                       TNC  and  displayed in the INCOMING window on  the 
                       CRT as they are transmitted on the air.

             3.2  Alt Function keys

                       3.2.1    Exit or return to DOS.
                       Exits  the program and returns you to  DOS.   When 
                       you exit the program,  the TNC is put into the VHF 
                       default  mode in which it rejects calls  from  any 
                       other  stations.   (Read about the 'CFROM' command 
                       in  the  TNC manual).   you can thus if  you  wish 
                       leave  it powered,  and if you also leave the  VHF 
                       radio  powered  up,   you  will  be  active  as  a 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 15


                       digipeater,  but at the same time anyone trying to 
                       connect with you will receive a busy signal.   The 
                       MBX function (Reading the Mail) is also cleared at 
                       this time.

                       3.2.2    Initialize the PK-232.
                       Sets up the defaults for the PK-232 from the  file 
                       PK232COM.SYS.   If  you have put batteries in  the 
                       PK232,  you should normally only have to run  this 
                       function  when  you  first power up the  PK232  or 
                       change the batteries.

                       It will also set the date and time within the  TNC 
                       from the computer clock,  and,  when it has loaded 
                       the configuration file, will propmt you to set the 
                       PK232  Terminal  mode.   If you are using a  TNC2, 
                       select 'V'. 

                       3.2.3    Connect Status
                       When  you  are in the Packet communications  mode, 
                       this  function  lets  you see  the  state  of  the 
                       connection  in the Command Window.   It will  show 
                       you  if  there are any unacknowledged  packets  en 
                       route  to  the other station.   If you  have  been 
                       sending text, it is advisable to use this function 
                       before you disconnect, just to ensure that all the 
                       data  has  been received and acknowledged  by  the 
                       other party.   You may use this function in either 
                       the TNC Command or the TNC Converse mode.   If you 
                       use  it when in the Converse mode,  it will  leave 
                       you  in  the  command mode,  so  remember  to  use 
                       function key 10 to return to the converse mode.

                       In a multi connect situation, it will show you the 
                       status  on  all the IO channels (It uses  the  'C' 
                       TNC  command in the single user mode and the  'CS' 
                       TNC command in a multi user situation).

                       You may also use this function to reset the status 
                       window  display after a relink or any other  event 
                       which was not reflected in the status window.

                       3.2.4    Set Terminal Mode

                       This   key   allows  you  to  set   the   terminal 
                       configuration mode.  In Packet communications many 
                       stations  can  use the channel at the  same  time.  
                       Refer  to the "MONITOR' and 'MBX' commands in  the 
                       PK232 manual.  These modes give you some degree of 
                       control  as  to  how the  packets  from  different 
                       stations  are  displayed on ypur screen.   

                       In  the PACKET Communications mode,  the  function 
                       works in the following manner.



        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 16


                       You can set four Packet terminal modes as follows.

                            3.2.4.1   SOLO
                            In  this  mode,  you will only  see  messages 
                            addressed to you.  You will only get messages 
                            from  people  who  connect  to   you.   (This 
                            corresponds to 'MONITOR 0').

                            3.2.4.2   TRAFFIC
                            In this mode you will see most of the traffic 
                            on  channel.   you can use this mode to check 
                            that the TNC is working. (This corresponds to 
                            'MONITOR  4' or 'MONITOR ON').   

                            3.2.4.3   CQ/BEACON
                            In  This  mode,  you will see CQ  and  BEACON 
                            packets on the channel.  (This corresponds to 
                            'MONITOR  1').  This  mode only works on  the 
                            PK232.

                            3.2.4.4   READ THE MAIL
                            You  can  read  the mail on a  BBS  or  other 
                            station and get bulletins without  connecting 
                            to that station yourself.   You use this mode 
                            to do so.   you will be prompted for the call 
                            whose packets you wish to monitor.   Remember 
                            to  enter the call of the station sending the 
                            packets,  not  the call of the one  receiving 
                            them.   (This corresponds to 'MONITOR 0'  and 
                            'MBX' callsign).  This mode only works on the 
                            PK232.  

                            You  can  also use this function  to  monitor 
                            both sides (read the mail) on a QSO on a busy 
                            packet channel.

                            You  may  want  to  turn  the  Digipeat  Data 
                            Display mode off when reading the mail.

                       The  Packet  Terminal  mode of operation  will  be 
                       shown  in  the  Status window at the  top  of  the 
                       screen.

                       If  you  are reading the mail on  a  station,  the 
                       callsign of that station will be shown next to the 
                       word "MAIL".  

                       If  you  are connected to someone,  the call  (and 
                       path) will be shown prefixed by the "*>" sequence.

                       3.2.4.5 Multiple Connect Modes.

                       You  also use this function to go into and out  of 
                       the multiple connect mode.   The default condition 
                       is one connect at a time.   Should you opt for the 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 17


                       multiple connect mode, make sure you know what you 
                       are doing

                       When  you  enter  a  multiple  connect  mode,  the 
                       program will change the stream change character or 
                       the  CHSWITCH character (in the case of the  PK232 
                       from  a default $00) to the  '\'  (backslash).  At 
                       this  time  don't transmit raw directory files  in 
                       or you will see an error message.   You don't have 
                       to  be  in the command mode to  use  the  CHSWITCH 
                       character.   Read  all  about CHSWITCH in the  TNC 
                       manual.   When you return to the single user  mode 
                       the program will reset the stream character to the 
                       default $00.

                       When  you  are  in a  multiple  connect  mode,  an 
                       asterisk  will be shown in the status window  next 
                       to the word 'PACKET'.

                       PK232COM  supports  two  multiple  connect  modes, 
                       individual and conference.

                       An extract of an actual 'off the air' CRT  display 
                       (showing  received text only) in a multi user mode 
                       is  shown  below.   Note  each  line  of  text  as 
                       received  by the PK232 is prefixed (by the  PK232) 
                       with  the  IO channel number and callsign  of  the 
                       station its connected to .

        1:4X4IL: *** CONNECTED to 4X4IL via 4X4IC, 4X6JP
        0:4X4IC: joe do u read?
        2:4Z4ZB: *** CONNECTED to 4Z4ZB
        1:4X4IL: Look for me on PR via 4X6JP 73s and Shalom.
        2:4Z4ZB: GE JOE I WILL DIS THEN U CAN GO VIA THE REP....>
        1: *** DISCONNECTED: 4X4IL via 4X4IC, 4X6JP
        0:4X4IC: UNPROTO  CQ
        2:4Z4ZB: GO AHEAD BOYS...DE ALON..>
        0:4X4IC: 
        2: *** DISCONNECTED: 4Z4ZB

                                 3.2.4.5.1  The Individual Multi  Connect 
                                 Mode.
                                 This is the normal Multi Connect Mode as 
                                 described in the TNC manual.   Here  you  
                                 are  connected to up to 10 stations  and 
                                 will  send different traffic to each  of 
                                 them.    Each  time  you  wish  to  send 
                                 something  to a particular station,  you 
                                 must  select the IO channel the  station 
                                 is connected on before typeing the  text 
                                 or sending the file.

                                 You select the channel by typing the '\' 
                                 character followed by (in the PK232) the 
                                 channel number.   For example if you are 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 18


                                 connected  to G8BTB on IO channel 0  and 
                                 to  G3ZCZ on IO channel 1,  then to talk 
                                 to G8BTB you would type '\0' before  any 
                                 text, and similarly to send something to 
                                 G3ZCZ  you would type a '\1' before  the 
                                 text  you're going to send me.   If  you 
                                 are  not  using a PK232,  read  the  TNC 
                                 manual  to  determine if the IO  streams 
                                 are identified by numbers or by letters.  
                                 The  TNC2  standard  configuration  uses 
                                 letters.

                                 3.2.4.5.2  The Conference Multi  Connect 
                                 Mode.
                                 In  the  conference mode  on  the  other 
                                 hand,  everything  that you type at  the 
                                 keyboard  is transmitted to each station 
                                 that  you are connected with.   Thus  if 
                                 you are linked to two stations each line 
                                 will be packeted twice by the TNC.   You 
                                 don't  have to worry about  sending  the 
                                 wrong thing to the wrong person, as they 
                                 will all get the stuff. 

                                 In the conference mode, as the same text 
                                 is transmitted on all IO  channels,  the 
                                 throughput  will thus be  reduced,  slow 
                                 down  your  typing  speed or  use  short 
                                 packets.   Should you use function  keys 
                                 alt  3 or 5 to check the link status  or 
                                 call monitored list, you may not be able 
                                 to  get  back into the converse mode  if 
                                 you  have too many packets  outstanding. 
                                 If that happens,  wait a while and  then 
                                 try   to  set  the  converse  mode  with 
                                 function key 10.  You may have to try it 
                                 a few times,  depending on how good your 
                                 links are.

                                 DON'T   TRY  TO  SEND  A  FILE  IN   THE 
                                 CONFERENCE  MODE,  ITS NOT DESIGNED  FOR 
                                 IT. KEEP THE PACKETS SHORT. 

                                 3.2.4.5.3 Entering the conference mode.
                                 You enter this mode by selecting the '0' 
                                 option  in the terminal mode select menu 
                                 (Function key Alt 4).  You terminate the 
                                 mode by selecting the '1' option.

                                 3.2.4.5.4  Connecting in the multi  user 
                                 mode.
                                 You  connect in the usual  manner  using 
                                 function  key  7.   You MUST WAIT FOR  A 
                                 CONNECTION TO BE ESTABLISHED OR TIME OUT 
                                 before attempting to connect to the next 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 19


                                 station.  If you do not, you will get an 
                                 error message back from the TNC.

                       The conference mode will only work in the PK232 if 
                       DCDCONN  is  set to ON.   So if you  are  using  a 
                       PK232,  PK232COM will do it for you when you enter 
                       the  conference  terminal mode in case you  forgot 
                       or/and  haven't  set  the  PK232COM.SYS  file   to 
                       include  the line 'DCD ON',  At the same time  set 
                       PK232COM.SYS  default states to show the calls  of 
                       other  stations on each incoming line in the  muti 
                       connect modes.  (Read the TNC manual for how to do 
                       this).

                       The conference mode will only work in the TNC2  if 
                       DCDCONN  is jumpered so that Pin 8 of  the  RS-232 
                       Interface   changes  state  when  you  connect  to 
                       someone else.   If you get error messages and  see 
                       the  characters  '\J'  on your  screen,  then  the 
                       jumper probably isn't set.

                       The conference mode does not work on the TNC1.

                       In the conference mode, if any one of the stations 
                       disconnects,  the  TNC will return to the  command 
                       mode,  and  you must use function key 10 to return 
                       the  program to the converse mode before you  type 
                       another character of text.

                       After setting the terminal configuration mode,  it 
                       returns you to the TNC command mode.  

                       In  the  AMTOR  communications  mode  you  can  do 
                       several things as follows;

                            3.2.4.6   FEC 
                            Places  the  terminal into the  FEC  transmit 
                            mode.  This puts you on the air, anything you 
                            type will be transmitted.  

                            3.2.4.7   ALISTEN 
                            Read the Mail on a QSO.  Unfortunately,  when 
                            you  tune in a chirpy AMTOR QSO in the ARQ or 
                            standby  mode you won't get any copy  on  the 
                            QSO  in progress.   You can however read  the 
                            mail on one by entering the ALISTEN mode.  

                            3.2.4.8   ACHG 
                            Force a changeover or 'break in'.  If for any 
                            reason   you  want  to  interrupt  the  other 
                            station you send a 'BREAK' signal in software 
                            this way.

                            3.2.4.9   ARQ 
                            Return to the ARQ standby mode.  You must  be 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 20


                            in  this mode to receive signals from another 
                            station  who is calling you.  You may  do  it 
                            this  way or via the main Mode   Menu.   When 
                            you  tune for CQ calls,  they sound  somewhat 
                            like  fast RTTY with a ringing sound  similar 
                            to the connect alarm (but at a faster ringing 
                            rate) used by PK232COM.
                            
                            3.2.4.10   Force LETTERS Case
                            This  function lets you force the receiver to 
                            the  letters  case  if for  some  reason  you 
                            appear  to be in the numbers case.   It  will 
                            return you to the converse mode.

                            3.2.4.11  Override ROBOT Mailbox/Beacon
                            This  function  lets you override  the  ROBOT 
                            BEACON  and  chat  to  a  station  that   has 
                            linked  to  the  ROBOT.   Use  it  after  the 
                            message  in  PK232COM.TXT has been  sent,  ie 
                            when  the other station is sending a  message 
                            to you.

                            3.2.4.12  Turn on Mailbox/Beacon.
                            This  function  lets you turn on the  Mailbox 
                            during  a regular AMTOR QSO so that the other 
                            station  can  leave a message or  download  a 
                            file remotely.

                       3.2.5    Monitor Channel Activity
                       This  function  lets you see what calls the  PK232 
                       has  heard recently on the Packet  channels.   You 
                       can see up to 18, with the data and time they were 
                       last  logged  by the PK232.   If they  were  heard 
                       directly  an asterisk (*) will be listed  next  to 
                       the   call  sign.    If  they  were  heard   being 
                       re  transmitted via another station,  the asterisk 
                       (*) will not be shown.   Refer to the 'MH' command 
                       in  the  PK232 manual.   If you are using  a  TNC2 
                       refer to the MH command in the TNC manual for  the 
                       particulars of the display.

                       The  MH  list  shows up in a  special  window  and 
                       freezes until you depress any key.  While the list 
                       is  frozen,  PK232COM  is not monitoring  received 
                       data, so don't freeze it too long.

                       This function does not work on the TNC1.

                       3.2.6    Change Packet Connect/Contest Message

                            3.2.6.1   Change Packet Connect Message
                            This   function  allows  you  to  change  the 
                            message  that  will be  received  by  another 
                            packet station when it connects to you. Refer 
                            to the 'CTEXT' command in the TNC manual.


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 21



                            3.2.6.2 Change Contest Message
                            This function first toggles the contest mode.  
                            If  the  contest mode  is  active,  the  word 
                            'TEST' and the number of the next QSO will be 
                            displayed  in  the status  window.  When  the 
                            contest  mode  is toggled on,  this  function 
                            then  allows  you  to set  the  starting  QSO 
                            number  and  write  in the  non  changing  or 
                            standard message that will be transmitted  as 
                            part  of  an  exchange of messages  during  a 
                            contest.

                            The contest function is toggled off the  next 
                            time  you select this function,  or when  you 
                            change  the PK-232 Communications  mode  (ie. 
                            switch from Morse to BAUDOT).

                            Note  that while this does give you some semi 
                            automatic contest operation by using function 
                            keys,  there is no checking of callsigns  for 
                            duplicates  built  into the  program.   In  a 
                            contest,  you  enter the callsigns  and  call 
                            the other station in the normal manner,  then 
                            use   this  function  key  to  transmit   the 
                            exchange.  In Morse, and RTTY don't forget to 
                            use function key 10 to turn on the transmiter 
                            first.

                            3.2.6.3 Change CQ text Message
                            This  function  allows  you  to  change   the 
                            contents of the CQ text message string.  This 
                            is  the string that is transmitted along with 
                            the  CQ call.   The default value  is  loaded 
                            from the PK232COM.SYS file.

                       3.2.7    Enter Call Sign
                       This  key lets you enter the call of  any  station 
                       calling  you  into the program.  If you  type  the 
                       enter key in response to the prompt, you can later 
                       use  the  F3  (function key  3)  to  transmit  the 
                       sequence  "de  <yourcall>".  You may also use  the 
                       Shift F7 key to call that station in the non AMTOR 
                       modes.

                       In AMTOR,  you use it to enter the callsign of the 
                       station you want to or have called by means of the 
                       SELCAL.

                       You  should also use this to enter a callsign of a 
                       station  that called you,  if you were not  in  an 
                       autoCQ mode.

                       3.2.8    Not used. 
                       You  don't want to disconnect accidentally if  you 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 22


                       just depress function key 8 without the 'Alt' key.

                       3.2.9    Activate Transmit Buffer

                       The  use  of this key sets PK232COM to  the  "Type 
                       Ahead"  mode.   Any  characters then typed at  the 
                       keyboard  will  be placed into  the  TNC  transmit 
                       buffer.  The contents of the buffer will be trans-
                       mitted  over the air when the transmit function is 
                       invoked [FK10].  

                       This feature allows you to 'type-ahead' as you can 
                       enter text into the transmit buffer while  viewing 
                       incoming  words in the INPUT window in the screen.  
                       Any  characters  typed from the keyboard  will  be 
                       echoed in the OUTGOING window on the screen.

                       THIS FUNCTION IS NOT ACTIVE IN THE AMTOR or PACKET 
                       modes.   Packet is full duplex, while in AMTOR the 
                       PK-232 buffers the data until you receive the next 
                       +? sequence.

                       3.2.10   Help
                       The use of this key will activate the HELP menu in 
                       a  differnet  window on the screen.   This  window 
                       will remain on display until a character is  typed 
                       at the keyboard, or a character is received by the 
                       computer from the PK-232.

             3.3  Shift Function Keys

                       3.3.1     Dir
                       This  function  shows  you the  directory  of  the 
                       logged in (active) disk drive.

                       3.3.2     Rename
                       This  function allows you to rename a  file.   You 
                       could  for  example rename a document  file  to  a 
                       "callsign.OUT"  file so that someone will  receive 
                       it automatically next time they connect.

                       3.3.3     List of Outgoing Messages
                       This function shows you the outgoing messages that 
                       have not been sent. In other words, all files with 
                       the  file  extension  of '.OUT'.See  below  for  a 
                       description  of outgoing messages in your  "Packet 
                       Radio Answering Machine".

                       3.3.4     Delete
                       This function allows you to delete a file

                       3.3.5     List of messages that have been sent.
                       This  function  shows you the messages  that  have 
                       been  sent.   In other words,  all files with  the 
                       file extension of '.OLD'.


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 23



                       3.3.6     Mail Beacon Activate
                       Using this function will also load a 'Mail :' list 
                       into  your  Packet communications mode Beacon  and 
                       initiate  a  beacon transmission every 30  minutes 
                       (Refer  to the BTEXT command in the  TNC  manual).  
                       If  no  mail is pending then beacon  transmissions 
                       are  inhibited.   This conforms to good  operating 
                       practice on crowded Packet channels.

                       3.3.7     Retry
                       This  function allows you to retry a connect  that 
                       for some reason did not go through the first time.  
                       It save wear and tear on your fingers particularly 
                       if  the  desired connect path is via a  number  of 
                       digipeat  relays  or through a number  of  NET/ROM 
                       NODES.

                       In  the  non  packet  modes,   it  allows  you  to 
                       retransmit  a  call  to  another  station  without 
                       having to re-enter the call (FK7).

                       3.3.8     Not used. 
                       You  don't want to disconnect accidentally if  you 
                       just  depress  function key 8 without the  'Shift' 
                       key.

                       3.3.9 Connected Indicator Reset. 
                       You  use this function key to reset the PACKET and 
                       AMTOR   beacon  mode  "connect  has  taken   place 
                       indicator".  This is a flashing [C] display in the 
                       status window.   Whenever someone else connects or 
                       links  up to you this display will  be  activated.  
                       It  is  reset by this function key.   If  you  are 
                       monitoring  Packet traffic on a channel,  you  may 
                       not  notice  that a connect has  previously  taken 
                       place.   This  indicator  alerts you to check  the 
                       contents  of  the PK232COM.RUN disk file  for  any 
                       incoming messages.   The number shown with the 'C' 
                       is  the number of connects that have  taken  place 
                       since  the Indicator was last reset.   If a 'happy 
                       face'  is flashing along with the  connect  count, 
                       your    "target   station"   was   amongst   those 
                       connecting. 

                       3.3.10  OVER function.
                       In  the Packet communications mode  this  function 
                       sends  your  callsign followed by the >  and  Line 
                       feed  characters.   You  may  use this  to  signal 
                       'OVER' in a packet contact.

                       In  the  AMTOR communications mode  this  function 
                       sends  a  callsign sequence followed by  the  '+?' 
                       sequence  of  characters  which are  the  software 
                       'OVER' signal. 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 24



                       In   the   MORSE  and  RTTY  (Baudot  and   ASCII) 
                       communications  modes,   this  function  lets  you 
                       transmit  the following sequence <other  call)  DE 
                       <your  call> and returns you to the PK232  Command 
                       Mode.   For  example if you are 4X6AA and you  are 
                       working  G3ZCZ then this function  would  transmit 
                       the  sequence 'G3ZCZ de 4X6AA'.   You use this  at 
                       the  END  of  a transmission in  any  mode  except 
                       Packet.

                       If  you have typed something into the 'type  ahead 
                       buffer' then touch this function,  the contents of 
                       the  buffer  will will be transmitted followed  by 
                       the callsign sequence.

             3.4  Control Function Keys

                       3.4.1     Day Flag
                       This  function key puts the TNC into  the  command 
                       mode and loads the date into it from the computer. 
                       You  use  this to reset the TNC clock if it  isn't 
                       that stable,  or to flag a date and time into  the 
                       log file when in the non Packet modes. For example 
                       if you want to time tag a qso.

                       This function does not work on the TNC1.

                       3.4.2     CWID
                       This   function   key  is  used  to  send   a   CW 
                       identification  when  operating BAUDOT,  ASCII  or 
                       AMTOR.   You use this if your license requires you 
                       to  identify  in  morse code as  well  as  in  the 
                       operating mode.  In AMTOR, the CWID is sent in the 
                       FEC  mode.   

                       The  identification consists of the  sequence  'DE 
                       <your  callsign>'  where  your call sign  is  that 
                       entered into the PK232 as  'MYCALL'.

                       3.4.3     Message Upload
                       PK232COM  contains store and forward routines  for 
                       messages   in  a  Local  Area  Network  (LAN)   as 
                       described  in Appendix 2.   Use this  function  to 
                       upload a message to another system compatable with
                       PK232COM. 

                       When you invoke this function,  the computer  will 
                       ask  you  to tell it if you want to leave a  note, 
                       QSP or QRU.

                       3.4.3.1   Leaving a Note in your system.
                                 In all modes you can leave a brief  note 
                                 (message) for another station.  When you 
                                 invoke this function the header is writ-


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 25


                                 ten  to  the message file,  then as  you 
                                 enter the text it is stored on the  disk 
                                 in the usual format.

                                 WHILE WRITING YOUR NOTE,  ALL OTHER FUN-
                                 CTIONS  OF  PK232COM  ARE  INHIBITED  OR 
                                 LOCKED OUT.  THUS IF SOMEONE CONNECTS TO 
                                 YOU,  THE TNC WILL KNOW THT BUT PK232COM 
                                 WILL NOT.  BE WARNED !!!  

                                 After   you  have  left  the  note   and 
                                 received    the   'QSL'   message   from 
                                 PK232COM,  if  you  are  in  the  Packet 
                                 communications mode, push function key 8 
                                 or  function  key  shift 6 to  load  the 
                                 callsign  of  the  recipient  into   the 
                                 beacon.

                                 When you leave a note,  leave it for the 
                                 root  call,  for example to leave a note 
                                 for   KL7LF/KH3  leave  it  for   KL7LF, 
                                 similarly to leave a note for   WB8WKA-1 
                                 leave it for WB8WKA.   PK232COM is smart 
                                 enough to extract the root call from any 
                                 callsign it links/connects to.  

                       3.4.3.2    Leaving a message on an other  PK232COM 
                                 system [QSP].
                                 The  QSP  function lets  you  enter  the 
                                 callsign  of  the  station you  wish  to 
                                 leave a message for.   It will then send 
                                 the text sequence :QSP: <callsign>.  The 
                                 other PK232COM HOST station will  either 
                                 reply  :QNO:  followed  by a  number  or 
                                 :QRV:  <callsign>.   The  'QNO'  message 
                                 means  that  the other  computer  cannot 
                                 accept  the message,  the :QRV:  message 
                                 means that it is waiting for you to send 
                                 it.

                                 If you get the :QRV: reply, go ahead and 
                                 type the message,  or send the text file 
                                 containing the message.  If you type the 
                                 message,  use a control Z (^Z) character 
                                 and  carriage  return to  terminate  the 
                                 message.    (In  AMTOR,   PK232COM  will 
                                 translate  the  ^Z  to   :EOF:   +?   to 
                                 terminate  the message).   You will then 
                                 receive  either a :QSL:  frm  the  other 
                                 station  meaning  that  the  message  is 
                                 accepted,  or  a  :QNO:  followed  by  a 
                                 number  which means that something  went 
                                 wrong and the message was not stored.




        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 26


                       3.4.3.3    Uploading messages to another  PK232COM 
                                 system.
                                 The QRU function allows you to upload  a 
                                 number of messages to the other station.  
                                 You   use  it  when  you  have  messages 
                                 pending on your system and want to  pass 
                                 them  to a third computer for storage in 
                                 the  network,  while you take your  com-
                                 puter off-line.

                                 You  can only use this function  with  a 
                                 station  designated as a store and  for-
                                 ward mail box, for which you have set up 
                                 a  <callsign>.MBX file (see section  7).   
                                 This  function  may be triggered by  you 
                                 using   this  control  key  or  by   the 
                                 connecting  station sending you a  :QRU: 
                                 command.

                                 When the sequence is over,  the computer 
                                 sending  the messages will transmit  the 
                                 NC/L  command word :QJG:  to signal that 
                                 the  sequence is complete.   Should  you 
                                 receive it before you get any  messages, 
                                 then there weren't any pending. 

                                 If  you  want to download messages  from 
                                 another  PK232COM system,  connect to it 
                                 and type the sequence :QRU:  followed by 
                                 the 'Enter' character.  That system will 
                                 then  respond to you as if the  operator 
                                 there had initiated a QRU function.

                       Appendix  2 contains more information on  the  LAN 
                       capabilities of PK232COM.

                       3.4.4     Show last few log entries.
                       This function displays the log entries made during 
                       the  active  session.  If no QSO's have been  made 
                       since  the program was loaded the  display  window 
                       will be blank.   Up to 5 log entries will be disp-
                       layed in the window.   You use this function for a 
                       quick look at which stations have connected to you 
                       in your absence.

                       3.4.5     Automatic CQ Sender
                       This function will send a CQ sequence,  wait about 
                       a  minute  or so  and then repeat the CQ  sequence 
                       every  minute  or so until it receives  your  call 
                       back from someone else.   When it does so, it will 
                       alert you with a Connect Alarm signal and reset to 
                       the normal or listening mode.

                       When the Automatic CQ sequence is in operation, an 
                       indication  will  be shown in the  status  window.  


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 27


                       The display will be constant while the transmitter 
                       is  sending the CQ test,  and will blink while the 
                       receiver is listening for a reply.

                       The  time  delay  between calls is set  using  The 
                       Control Function key 7.

                       The  automatic CQ function will only work  in  the 
                       PK-232  non Packet modes if the 'EAS' mode is  set 
                       to  'ON'  per  the PK232COM.SYS  file.   In  other 
                       words,  you must be able to see the CQ text pop up 
                       in the outgoing window and then slowly echo in the 
                       incoming  window for the function  to  work.   The 
                       reason  for  this is that the "K K K" sequence  is 
                       used  to arm the software to look for  your  call-
                       sign.   If it wasn't,  the program would recognize 
                       your  call  being echoed to the screen  and  think 
                       that you had called yourself.

                       In AMTOR you will get the connect alarm only  when 
                       the  replying station transmits the '+?' character 
                       combination.

                       The  check for the detection of your callsign  and 
                       the connect alarm sequence only occur after a line 
                       feed character have been received.

                       Under most conditions in AMTOR,  many in RTTY, and 
                       some  in  MORSE,   PK232COM  will  recognize   the 
                       callsign  of  the  station answering your  CQ  and 
                       display  it in the status window.   In  the  event 
                       that  it fails completely,  the  sequence  '--?--' 
                       will  show  up in the status  window.   Since  the 
                       recognition  algorithm use just look for the first 
                       word following the 'DE ' sequence and assumes that 
                       it has the callsign,  be careful to check it  when 
                       operating under QRM conditions.   You can override 
                       the  automatic call selection with the Enter Call-
                       sign function key.

                       The  automatic  CQ sequence is cancelled  when  an 
                       incoming call is detected, you push the disconnect 
                       function  key,  or  if you  change  communications 
                       modes.

                       3.4.6     SELCAL
                       This  function  key toggles the SELCAL feature  on 
                       and off.   When the SELCAL is activated,  as shown 
                       in the status window,  the incoming text from  the 
                       PK232 is scanned.   When either the letters "ZCZC" 
                       or  'your  callsign' (as entered in line 1 of  the 
                       PK232COM.SYS file),  the capture-to-disk is turned 
                       on.   All  subsequent text will be stored  in  the 
                       PK232COM.RUN  disk  file until the letters  "NNNN" 
                       are received.  At that time the capture-to-disk is 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 28


                       turned off.

                       You   may   use  this  feature   when   monitoring 
                       commercial  RTTY  broadcasts  to record  news  and 
                       other  information,  or when calling CQ  to  start 
                       recording  all  incoming text and keep the QSO  on 
                       disk.

                       You may use the loggletoggle function to  override 
                       the automatic turnoff if you wish.

                       3.4.7     Beacon Toggle On/Off/CQ delay time set.
                       This  function toggles the beacon option  for  the 
                       automatic  CQ  caller  in  the  AMTOR  and  Packet 
                       communications modes.  When active and CQ is being 
                       called,  a  [B]  will be displayed in  the  status 
                       window.  In  this mode,  the Automatic CQ sequence 
                       will  resume after the AMTOR link is dropped or  a 
                       Packet Communications mode disconnect.    

                       In the beacon mode,  the last few logbook  entries 
                       will  be  displayed  in the logpage  window  which 
                       overlays the outgoing text window at the bottom of 
                       the screen.

                       In the Packet mode,  the CTEXT message is the only 
                       transmission from you that the other station  will 
                       receive, so make it good.

                       In the AMTOR Mailbox/Beacon mode,  the contents of 
                       the  PK232COM.TXT file will be transmitted to  the 
                       station who called you.   The capture-to-disk will 
                       then  be turned on to record one transmission from 
                       that station.   The QSO will then be logged to the 
                       logbook file.   Don't forget to check the  entries 
                       in case the computer made a mistake in recognizing 
                       the call sign of the other station.

                       THE BEACON MODE IS DESIGNED TO ENCOURAGE PEOPLE TO 
                       QSY OFF THE CROWDED PACKET HF CHANNELS. DO NOT USE 
                       IT  ON  A CROWDED HF CHANNEL OR ON AN  ACTIVE  VHF 
                       CHANNEL.  IF YOU DO, YOU WILL SOON FIND THAT OTHER 
                       STATIONS  HAVE  SET  THEIR TNC'S  TO  REJECT  YOUR 
                       PACKETS,  YOU WILL NOT WORK ANYBODY, YOU WILL JUST 
                       BA A SOURCE OF QRM AND WILL BE KNOWN AS SUCH.
                       
                       THE  MODE IS ALSO DESIGNED FOR ROBOT  BEACONS  FOR 
                       THE HIGHER FREQUENCIES.   FOR EXAMPLE IF YOU LEAVE 
                       IT  RUNNING  ON  10 METERS YOU NEVER KNOW  WHEN  A 
                       SHORT OPENING WILL ALLOW A QSO TO SOME PART OF THE 
                       WORLD.   A DX CONTACT YOU WOULD HAVE MISSED OTHER-
                       WISE.    DO NOT LEAVE IT RUNNING ON 20 METERS WHEN 
                       THE BAND IS OPEN.   YOU WILL JUST BE CAUSING  QRM.  
                       FURTHER  APPLICATIONS  ARE  IN  METEORSCATTER  AND 
                       OTHER "EXOTIC" MODES OF COMMUNICATIONS.


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 29



                       If  you  are using this mode in  a  special  event 
                       station  or  DX-pedition you may  type  characters 
                       into the transmit buffer,  while the other station 
                       is sending to you.   When he, she or even it turns 
                       it back to you, you will transmit those characters 
                       before the sign off sequence. 

                       In both the Packet and AMTOR communications modes, 
                       the  robot may be shut down by stations connecting 
                       to you and telling you to QRT.
                       3.4.7.1   Beacon Mode Toggle/On-Off
                                 This  function allows you to toggle  the 
                                 Beacon mode on and off.  

                       3.4.7.2   CQ Delay Time Adjust
                                 This  function allows you to change  the 
                                 time   that  the  program  waits  for  a 
                                 response  after  a  CQ  call  until  the 
                                 following  one  is   transmitted.    The 
                                 default   value   is  loaded  from   the 
                                 PK232COM.SYS  file.   You  may  want  to 
                                 experiment  since the actual  time  will 
                                 depend  on  the clock frequency  of  the 
                                 computer.   Make  it a small number such 
                                 as 4 or 6 when operating AMTOR or a  DX-
                                 pedition,  and  make it a larger  number 
                                 such  as  30 when operating  on  crowded 
                                 packet  channels.   The maximum  allowed 
                                 value is 255.

                       3.4.8     Not used. 
                       You  don't want to disconnect accidentally if  you 
                       just  depress  function key 8 without the  'Shift' 
                       key.

                       3.4.9     Transmit Buffer Clear
                       This  function is used if the PK232  continues  to 
                       transmit  the  characters you put into  the  'type 
                       ahead  buffer'  after  you have tried to  shut  it 
                       down.  

                       3.4.10    Logbook.
                       PK232COM  performs automatic logbook  entries  for 
                       Packet  and AMTOR Beacon mode Connects,  and  semi 
                       automatic  logbook entries for other  modes.   The 
                       Log  file  is  compatible to that of  the  CONTEST 
                       program  in  the G3ZCZ PC-HAM package and  can  be 
                       processed by the DBASE  Logbook Package of  PC-HAM 
                       by  G3ZCZ for indexed listings,  tracking of  DXCC 
                       and other AWARDS,  etc.  This is ideal for special 
                       event stations and DX-peditions, for the whole QSL 
                       process  and further statistical analyses of their 
                       operation has been automated.



        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 30


                       For this function to work,  the file  PK232COM.LOG 
                       must be present on the disk.  If it isn't, it will 
                       be  created for you.  After one logging  operation 
                       has occurred, edit out the initial text.  You must 
                       perform  this  editing operation before  appending 
                       the  contents of the logbook file to  the  logbook 
                       database of the PC-HAM LOGBOOK Package.   Edit the 
                       log  before appending it to the DBASE package,  as 
                       there  may be some null characters at the  end  of 
                       the  file which may be recognised as a blank entry 
                       by DBASE

                       It  is  also advisable not to let the each of  the 
                       files get too big.

                       When  an  AMTOR  beacon  mode  or  packet  connect 
                       occurs,  the connect is automatically logged.  The 
                       connect  path is placed in the comments section of 
                       the logbook entry.   In the non packet modes,  the 
                       log data entry is set up for you with default  599 
                       values for the reports exchanged.  You invoke this 
                       function to enter the data into the log.

                       When you invoke the function you will be presented 
                       with  the  following  typical  menu  in  the  menu 
                       window.

                                          LOG ENTRY
         DATE     TIME   CALL     BND  TX  RX  MODE  POWER S R   COMMENTS
        87/04/27 17:28             20  599     RTTY   10   - -
        Date,tIme,Call,Bnd,Tx,Rx,Mde,Pwr,qSl snt,cOmmnts or Logit (*) ?

                       You  should  reply with the capitalized  character 
                       associated with each item.   For example,  if  you 
                       want to change the Band,  enter the letter 'b', to 
                       change the cOments,  enter the letter 'o'.   Touch 
                       the  'ENTER'  key after you have made your  choice 
                       and enter the text when prompted.   You will  then 
                       be presented with an updated entry.

                       To  enter the data into the logbook,  use the  'l' 
                       key, to save the data but not make a log entry use 
                       the '*' character.   You would do that if you want 
                       to change the band or power information.

                       You  may use the 'qSl sent' entry to tag the  fact 
                       that you have written out a QSL card.

                       The band and power information are set up from the 
                       default  values  stored in the configuration  file 
                       PK232COM.SYS.   They  are displayed in the  status 
                       window.   If  you are using the logging  function, 
                       you  should change them when changing bands/powers 
                       and  quit  the  logging  function  with  the   '*' 
                       character so that you don't put a blank entry into 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 31


                       the logbook.

                       Note  that you can also use this function to enter 
                       the odd SSB contact into the logbook file.  If you 
                       do,  use  the  characters 'SSB' or 'FM' for  those 
                       voice modes to remain compatible with the rest  of 
                       the DBASE logbook package.

                       NOTE   Do  not use the comma character ',' in  the 
                       comments field.   If you examine the log entry you 
                       will see that all items are separated by  comma's.  
                       If  you use a comma character in the comments  you 
                       will  screw  up  the  transfer of  data  into  the 
                       logbook  package.   

                       The comments field in the logbook is restricted to 
                       a maximum of 10 characters.   If you try and enter 
                       more than 10, the surplus will be ignored.

                       When  you  examine the DBASE logbook file,  if  it 
                       looks funny or the data are in the  wrong,  place, 
                       then  you probably have the wrong number of  comma 
                       characters in some line.  Delete the .DBF file and 
                       re-edit the .LOG file, to make sure that there are  
                       the correct number of comma characters.   You will 
                       recognise the pattern readily enough.

             3.5  Shift/Baudrate Control keys
             
             The  following  keys are used to control the Shift (Wide  or 
             narrow) and the Radio link baudrate in the BAUDOT, ASCII and 
             PACKET communications modes.

                       3.5.1     RIGHT ARROW speeds up the baud rate.
                       3.5.2     LEFT ARROW slows down the baud rate.
                       3.5.3     UP  ARROW toggles the shift from Wide to 
                                 Narrow and back.
                       3.5.4     DELETE toggles the USOS function.

             In  the PACKET mode the baudrate may be changed between 300, 
             600, 1200 and 2400 bauds.  In the other modes all baud rates 
             supported by the PK232 may be selected.

             The  state  of each of the above functions are displayed  in 
             the  status  window at the top of the screen.   If  USOS  is 
             active,  'USOS' will be shown.  The shift is shown as 'W' or 
             'N'  for  wide or narrow respectively.

             3.6  Additional keys

                  3.6.1     The HOME Key

                       The home key will clear the window screen that the 
                       cursor  happens to be in at the time that the  key 
                       was depressed,  and will then position the  cursor 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 32


                       at the top left hand corner of that window.

                  3.6.2    The DOWN ARROW key 

                       The  DOWN  ARROW  key toggles the  Normal  Reverse 
                       Sideband  function  in  all  communications  modes 
                       except  MORSE.   The sideband is depicted  in  the 
                       status  window by the up and down arrows.   If the 
                       down  arrow  is showing,  you are  set  for  Lower 
                       Sideband (LSB) which is the normally used one.

                       If  you have reversed the sidebands a flashing  up 
                       arrow will be displayed.

                       If you set your transceiver to LSB you will be set 
                       correctly for all modes.  

                       For  CW operation you may set your rig to  the  CW 
                       position and ignore the sideband setting.   If you 
                       use FSK just set it so that it works for you.

                  3.6.3     The Alt A key (Alert toggle).

                       This  key toggles the Alert call function  on  and 
                       off.   If it is off, you are prompted for the call 
                       to  be monitored,  if it is on,  it is turned off.  
                       The toggle is set when you enter a  callsign,  and 
                       cleared  when you depress the 'Enter' key  instead 
                       of a callsign.

                       The  Alert  call  will be shown  flashing  in  the 
                       status window when in the disconnected state.

                       The   Alert  function  is  used  in   the   Packet 
                       communications  mode  when  disconnected  and  the 
                       terminal set for 'TRFC' or 'CQ/BEACON'.   PK232COM 
                       will  scan  the packet headers received  from  the 
                       TNC,  and,  when  it  sees a packet originated  or 
                       digipeated if the MRPT parameter in the TNC is set 
                       to 'ON', (the default state in PK232COM.SYS by the 
                       way) by the station whose call you have entered as 
                       the  'Alert' call,  it will sound an alarm at  the 
                       console.   

                       NOTE:  If the terminal is set for 'CQ/BEACON'  the 
                       Alert  will  only sound if the  specified  station 
                       transmits CQ or BEACON packets.

                  3.6.4     The Alt B key (Baudot/ASCII Baud rate set).

                       This   key   allows   you   to   set   a   desired 
                       communications  baud rate directly.   You will  be 
                       prompted  to  enter the desired  rate.   Use  this 
                       function to avoid having to shift through too many 
                       intermediate states,  if for example,  you want to 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 33


                       make a direct change from 45 to 100 bauds.

                  3.6.5    The Alt C key (connect request).

                       This key performs the same task as Function Key 7.  
                       The  Alt C key has been provided for those  people 
                       whose  fingers have learnt YAPP and don't wish  to 
                       be re-educated.

                  3.6.6    The Alt D key (display inhibit).

                       This key toggles the 'Display Inhibit' mode.   Use 
                       it  to  inhibit direct writing to the screen  when 
                       running  under  a multi-tasking  operating  system 
                       such as Doubledos.   It has been tested and  works 
                       under Doubledos Version 4.0.

                  3.6.7     The Alt F key (Digipeat monitor toggle)

                       This  key toggles the digipeat display function on 
                       and  off.   If  the Digipeat Display  Function  is 
                       active, any signals digipeated through you will be 
                       stored to the PK232COM.RUN file and a 'beep'  will 
                       be sounded for each packet being digipeated.   The 
                       status display window will also show a [D] at that 
                       time.   The  MDIGI  function is set 'ON' when  the 
                       Digipeat display function is 'ON', this means that 
                       digipeats  will show up while you are connected to 
                       someone.   The default state for the Digipeat Dis-
                       play Function is OFF.  

                  3.6.8     The Alt P key (printer toggle).

                       This key toggles the printer on and off.  When the 
                       printer  is turned on,  any incoming data will  be 
                       printed  in  real time.   If you intend  to  print 
                       files  received  at  1200  bauds  in  the   packet 
                       communications   mode,  use a print spooler or you 
                       may  loose  data.   The printer  is  automatically 
                       turned  off in the packet mode when  a  disconnect 
                       occurs.

                  3.6.9     The Alt R key (Message Relay toggle)

                       This  key  toggles the Store and  forward  Message 
                       Relay  Capability of your system on and  off.   If 
                       the  Message Relay Capability is  active  (toggled 
                       on),  any  one who connects can store a message in 
                       your  system  using the  ':QSP:  <callsign>'  NC/L 
                       function.  If  the Message Relay Capability is not 
                       active  (IE.  toggled off) anyone who attempts  to 
                       ':QSP: a message' will receive a ':QNO: 1' "error" 
                       message.   The  status display window will show  a 
                       [R]  when the Message Relay Capability is  active.  
                       The default state for the Message Relay Capability 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 34


                       is loaded from the PK232COM.SYS file.

                       When  the Store and forward capability is  active, 
                       the suffix 'R' will be added to the 
                                 '*** PK232COM 1.42' 
                       message  received  by  anyone connecting  to  your 
                       system   to  notify  them  that  they  can   store 
                       messages.   In this manner they don't have to  try 
                       to  leave a message and then get ':QNO:  1'  error 
                       message to find out if the feature is toggled off.

                  3.6.10   The Alt S key (Sound Set/Toggle).

                       This  key  toggles the sound on and off.   If  the 
                       sound  is  off,   a  flashing  indicator  will  be 
                       displayed in the Status Window.  When the sound is 
                       toggled on again, a chime will sound to verify the 
                       audio.

                  3.6.11     The Alt C key (Target Call set/toggle).

                       This  key toggles the Target call function on  and 
                       off.   If it is off, you are prompted for the call 
                       to  be monitored,  if it is on,  it is turned off.  
                       The toggle is set when you enter a  callsign,  and 
                       cleared  when you depress the 'Enter' key  instead 
                       of a callsign.

                       The  Target  call  will be shown flashing  in  the 
                       status window when in the disconnected state.

                       The  Target  call function is used in  the  Packet 
                       communications  mode when  disconnected.  PK232COM  
                       will monitor the stations connecting to you.  When 
                       it  sees  a connect by the station which you  have 
                       entered  as  the 'Target' call,  it will  set  the 
                       flashing  Connect Count display to show  a  'happy 
                       face'. 

                  3.6.12    The Alt X key (Exit or return to DOS).

                       This  function is the same as the Alternate  Func-
                       tion 1 key.  It exits the program and returns  you 
                       to DOS.  When you exit the program, the TNC is put 
                       into  the  VHF  default mode in which  it  rejects 
                       calls  from any other stations.   (Read about  the 
                       'CFROM' command in the TNC manual).   you can thus 
                       if  you  wish leave it powered,  and if  you  also 
                       leave the VHF radio powered up, you will be active 
                       as  a  digipeater,  but at the  same  time  anyone 
                       trying  to  connect with you will receive  a  busy 
                       signal.   The  MBX function (Reading the Mail)  is 
                       also cleared at this time.




        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 35


                  3.6.13    The PgUp key (Scrolls back incoming text).

                       This  key lets you repeat the display of  incoming 
                       text  which  has  scrolled  out  of  the  incoming 
                       window.   you  may print it or capture it to  disk 
                       during the repeat.  

                  3.6.14    The Control Z key.

                       This key is used in the Packet communications mode 
                       to  signal  the  end of a file  or  message,  when 
                       loading  messages into another PK232COM system  or 
                       into a BBS.   In the AMTOR communications mode, it 
                       is translated into the sequence ' :EOF: +? ' which 
                       can  be used as a fast break-in changeover  or  to 
                       terminate   a  message  being  stored  in  another 
                       PK232COM AMTOR mailbox. .cp7


        4.0  PK232COM disk files

        The following disk files are associated with the program.

             4.1  PK232COM.COM
             This is the program.  You activate it from DOS by typing the 
             word  PK232COM  followed by ENTER in the  normal  manner  of 
             invoking DOS commands.

             4.2  PK232COM.RUN
             This  is  the  file containing the captured  incoming  text.  
             This file contains incoming data from the TNC recorded while 
             the 'capture to disk' function was active.

             4.3  PK232COM.SYS
             This  file  contains the configuration information for  both 
             the program and the PK-232.  YOU MUST EDIT IT before you run 
             the  program  on  the air the first  time.   Use  your  word 
             processor in the NON-Document mode.    

             The contents of the file are as follows.

                  4.3.1     The first line. 

                       The first line  contains your callsign.  

                       Please  do  not use G8BTB.   Replace  G8BTB   with 
                       yours.   You  may  use / characters if  you  wish.  
                       This  is  the call sign that will be used  in  the 
                       non- Packet  modes.   You  may thus use  "portable 
                       designators"   such  as   G3ZCZ/A,   G3ZCZ/W3   or 
                       G3ZCZ/4X,  which you cannot do in Packet.   IF YOU 
                       DON'T CHANGE THE CALL SIGN,  YOU WILL GET AN ERROR 
                       MESSAGE AND THE PROGRAM WILL NOT RUN.

                       This is the call that will be monitored for in the 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 36


                       Digipeat monitoring mode.   In this mode which  is 
                       toggled  on and off by the Alt F key,  if  someone 
                       uses  you  as  a  digipeater  while  you  are  not 
                       connected to anyone else, the event will be logged 
                       to  disk.   This  mode  will  only  work  if  your 
                       callsign  as  stored  in  this  line  is  a  valid 
                       (uppercase only) packet callsign.  

                       For  example,  in the PK-232,  if the callsign  is 
                       G3ZCZ then the sequence >G3ZCZ> will be recognised 
                       as  a  digipeat and the event  logged.   Thus  for 
                       example  4X6AA*>G3ZCZ>4Z4ZB  would be logged as  a 
                       digipeat event.  

                       Now  if the callsign in this line is G3ZCZ/4X then 
                       the  event  will not be recognised as  a  digireat 
                       because  the  computer  would be  checking  for  a 
                       G3ZCZ/4X  in the packet header and it would  never 
                       see  G3ZCZ/4X.    This  option  is  inhibited  for 
                       reciprocal  callsign  operators due to  the  AX2.5 
                       protocol itself.  

                       If  you have a / character in your  callsign,  and 
                       use  the  base  call for  packet  identifying  the 
                       location  in the CQ text,  then the function  will 
                       work  if  you place the "portable location"  as  a 
                       suffix.   For example, if the call is G3ZCZ/4X and 
                       the  packet  identification  is  G3ZCZ,  then  the 
                       digipeat  monitor  will  work.  If  the  call  was 
                       entered  as  4X/G3ZCZ the digipeat  monitor  would 
                       check for 4X and would not appear to work.

                       Store  your callsign using UPPERCASE characters if 
                       you want this option to work (IE.  G3ZCZ).  If you 
                       use lower case (ie. g3zcz), the option will not be 
                       enabled as recognition will never take place.  The 
                       PK232 automatically converts case to upper case in 
                       the non packet communications modes.

                       If  you  are using an SSID (eg.  G3ZCZ-8)  in  the 
                       packet  communications mode,  you should enter the 
                       whole call INCLUDING the SSID.
                  4.3.2     The second line. 

                       The   second   line  contains  the  AMTOR   SELCAL 
                       configured  for your callsign.   You use it  again 
                       later to tell the PK232 what the SELCAL is.   This 
                       line just tells it to PK232COM.

                  4.3.3     The third line.

                       The   third  line  contains  the  line   of   text 
                       transmitted  by  the PK-232 in a CQ call  (in  any 
                       mode except for MORSE). Think of this message as a 
                       CQTEXT line.  Edit this line as well.


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 37



                  4.3.4     The fourth and fifth lines
                       The band and power information are set up from the 
                       default  values  stored in the configuration  file 
                       PK232COM.SYS.   They  are displayed in the  status 
                       window.   If  you operate on another band or  your 
                       transmitter  uses  a different power level  change 
                       the  default  values in the file to  reflect  your 
                       custom default state.

                       The  fourth  line contains the  band  information.  
                       The  default  value is 2 for 2  Meters.   Use  the 
                       Meter  value  for  the band to  keep  the  display 
                       correct.

                       The   fifth  line  contains  the  value  for   the 
                       transmitter power.  The default value is 10 for 10 
                       watts.

                  4.3.5     The sixth line
                       The  sixth line contains a number which tells  the 
                       program how long to wait before transmitting a  CQ 
                       call when in the beacon (automatic) mode.  A value 
                       of  4 corresponds to about 2 minutes.   This value 
                       of time will vary depending on the clock speed  of 
                       your  computer.   You may have to experiment  with 
                       different  values.   The default value is 0  which 
                       inhibits the beacon mode.

                  4.3.6     The seventh Line
                       The  seventh  line configures the  LAN  store  and 
                       forward  capacity of the system also known as  the 
                       Message Relay Capability.  If it is a '0' (default 
                       state)  your computer will not accept messages for 
                       forwarding.   If it is a '1', it will.  See Appen-
                       dix 2 for details about LANs.   

                       Remember,  if you configure your computer to store 
                       and forward messages,  you have a moral obligation 
                       to deliver them.

                       The  status of this function shows up as an [R] in 
                       your  status  display and in the  connect  message 
                       which  is transmitted to the other station at con-
                       nect  time,  as an 'R' suffix to the message  when 
                       active.

                  4.3.7     The eighth line
                       This  line  contains  the  default  Communications 
                       port.   The default value is 1.  You must leave it 
                       set  to 1.   THIS VERSION OF PK232COM CAN ONLY  BE 
                       USED WITH COMM1.

                  4.3.8     The ninth line (TNC type)
                       This  line  tells  the program which TNC  you  are 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 38


                       using.   The  PK232 command set is  slightly  dif-
                       ferent to those of TNC2 in the packet mode.   Thus 
                       the  command dialog has to be changed somewhat  to 
                       make the 'SOLO,  TRAFFIC, CQ/BEACON and MAIL' ter-
                       minal  modes  work correctly for different  TNC's.  
                       NOTE  that program does not check the TNC  in  the 
                       Non Packet modes, so for example if you try to set 
                       a  TNC2  to AMTOR,  PK232COM will send  the  PK232 
                       commands  to the TNC2 which should then return  an 
                       error message.

                       Valid TNC's are PK232 
                                       TNC1
                                       TNC2          (don't type the '.').
                       The  TNC2  used to test PK232COM 1.41 was  an  MFJ 
                       1270.

                  4.3.9     The Tenth line (Terminal Baud Rate).
                       This  line  tells PK232COM what baud rate the  TNC 
                       is set to. This is the baudrate on the RS-232 line 
                       between  the  TNC and the  computer.   Valid  baud 
                       rates for PK232COM are 1200,  2400, 4800 and 9600.  
                       If  you  specify  something  else  PK232COM   will 
                       default to 1200.

                       If the TNC does not use an interrupt driven serial 
                       port  you may experience problems when using  baud 
                       rates greater than 1200.  The PK-232 does not like 
                       baud  rates faster than 2400,  and  sometimes  not 
                       even that.  Use 1200 until you have tested and are 
                       sure that a faster one will work.

                       This  program  has been tested on a TNC2  using  a 
                       terminal  baud  rate  of  9600  bauds  and  worked 
                       correctly.

                  4.3.10  The QTC _Snatch or Automatic Connect  Attempt 
                          Flag.
                       If the value entered on this line is a 1, then the 
                       QTC_Snatch  Flag is enabled.   if the value on the 
                       line is a 0, then the flag is disabled.

                       If the QTC_Snatch flag is enabled,  PK232COM scans 
                       the contents of packets appearing in the  Inwindow 
                       on  the screen while the terminal is disconnected.  
                       Should   it  recognise  the  three  text   strings 
                       'PK232COM',   ':QTC:',  and 'your callsign' in the 
                       packet,  it  will then issue a connect request  to 
                       the callsign of the PK232COM station that  origin-
                       ated  the beacon transmission.   If the connect is 
                       made,  the other station will send you the message 
                       automatically which PK232COM will capture to disc.  
                       The  connect  will time out and  terminate  a  few 
                       minutes later.



        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 39


                       Hopefully  it will not try to connect to you if it 
                       hears  your beacon with your call in  it  (someone 
                       left you a message) via a digipeater.

                       The  normal connect request will be made DIRECT to 
                       the station.   A digipeat path will not be invoked 
                       as this feature is designed to trigger a  normally 
                       silent  station  standing  by  on  the  LAN  (good 
                       operating practice).   If you expect messages from 
                       stations  you  can only connect with via  a  digi-
                       peater,   place  the  path  in  your  PK232COM.DIR 
                       directory file.   It should be there anyhow if you 
                       connect to the station regulaly.   For example, if 
                       you  expect messages from 4Z4ZB whom you can  only 
                       work  if digipeated via 4X1AA then place an  entry 
                       like
                                     4Z4ZB   4Z4ZB V 4X1AA
                       in the PK232COM.DIR  file.

                  4.3.11    The remaining lines 
                       The  remaining lines contain commands to  the  PK-
                       232.  For  further information about them refer to 
                       the TNC manual.   The example in the  PK232COM.SYS 
                       file is as follows.

                       CONSTAMP ON
                       CHCALL ON
                       CHDOUBLE ON
                       CMSG ON
                       CTEXT SHALOM you have connected with G3ZCZ/4X
                       daystamp on
                       DCD ON
                       eas on
                       echo off
                       flow off
                       mycall G8BTB
                       MYALIAS JOE
                       MYSEL GBTB
                       newmode on
                       NUCR ON
                       nulf on
                       users 1
                       usos on

             If  you use a different TNC (other than the PK232) you  will 
             have to edit this command list.  

             4.4  PK232COM.LOG
             This  file  contains the log entries.   It will  be  created 
             automatically to intialize the logging function.  The format 
             of the logbook file is the same as that created by the G3ZCZ 
             CONTEST.BAS  program  and  both files  are  designed  to  be 
             appended  into the G3ZCZ LOGBOOK DATABASE package  presented 
             as part of the PC-HAM software package.  It should be edited 
             with a word processor in the non document mode to delete the 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 40


             first  line  and clean it up before the file is appended  to 
             the DBASE logging package data files.

             4.5  PK232COM.DIR
             This  is  a  directory file.  You use it  to  store  connect 
             NET/ROM   or   digipeat  paths  as  well  as   name/callsign 
             relationships.  

             Examples are
             Joe  G3ZCZ
             Alon 4Z4ZB V 4X6AA
             Milt 4X6AA
             LR   4X6LR
             hf-il 4x4hf v 4z4zb 4x4il
             hf-rj 4x4hf v 4z4zb 4z4rj

             You  create  this  file with your wordprocessor in  its  non 
             document mode.   You must leave AT LEAST one space character 
             between the first (key) word and the connect path.  When you 
             type in the key word,  the program does not care about upper 
             or  lower case.   If the program does not find the key word, 
             it will try to connect with whatever you typed in.

             If  you  already  have  a YAPP.DIR file just  rename  it  to 
             PK232COM.DIR.  

             An example of a PK232COM.DIR entry for a NET/ROM path is 

             K1HTV ELK v WB4APR-5! SNJ3! NNJ! WMA! SCCT! K1HTV

             where the '!' separates each stage of the link.

             Consider the manual sequence to make the connection.   K1HTV 
             is  the station the contact is being attempted with,  and he 
             is  located  within  range of the SCCT  NET/ROM  node.   The 
             station  attempting the connet is located in the  Washington 
             DC area one digipeat away from the ELK NET/ROM node.

             The  connection to the local node is performed  first.   the 
             operator has to type ' C ELK v WB4APR-5' to make that  link. 
             When  the  connect with the node is achieved,  the  operator 
             must type 'C SNJ3' to connect to the next node.   Each  time 
             the  connection  is  made,  the operator must  type  in  the 
             command to make the next one, until finally the last node is 
             reached and a connect request can be made to the destination 
             station  (either  direct or via  a  digipeater).   Sometimes 
             there  may be an intermediate non NET/ROM connection between 
             two stations somewhere in the path.

             This procedure is tedious and time consuming, because it may 
             take  several  seconds to complete each stage of  the  link.  
             PK232COM automates this sequence by scanning the line in the 
             PK232COM.DIR  file  associated  with the  key  callsign  and 
             transmitting each section of the line when it recognises the 
             'Connected  to ' reply from each NET/ROM node in  the  path.  


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 41


             When it finally gets to the destination it sounds a chime to 
             alert you that the connect has been achieved.

             If  for  any  reason the  connection  fails,  PK232COM  will 
             disconnect the link.

             The  format  of  the entry in the PK232COM.DIR  file  is  as 
             follows.

             K1HTV ELK v WB4APR-5! SNJ3! NNJ! WMA! SCCT! K1HTV

             The key word is K1HTV.   PK232COM then scans the line to see 
             if  there is a '!' in it.   If there is it knows that it  is 
             dealing  with  a  NET/ROM path.   It then tells the  TNC  to 
             connect  to the characters following the key word up to  the 
             '!'  sign to the TNC in the command mode.   In this case  it 
             tells the TNC to connect to ELK via WB4APR-5.  When the  TNC 
             sends back the connected message,  PK232COM tells the TNC to 
             try to connect to the next node in the path,  namely in this 
             example SNJ3.  The sequence continues each time a connection 
             is made until the link is complete.

             To  set  up  a directory entry just copy the  format  shown.  
             Place  a '!' sign after the uplink path and  different  node 
             segments. Do not place one after the downlink path.

             NOTE:  All  path entries in PK232COM.DIR must be on a single 
             line.

             4.6  CONFIG.SYS
             You  must have a CONFIG.SYS file on the boot disk if you are 
             going  to  use the disk logging features.   This  file  must 
             contain the line 
             FILES = 20
             See   the  DOS  manual  for  more  information  about   the 
             CONFIG.SYS file.

             4.7  *.MBX
             These  are the files associated with the stations  you  have 
             designated  as  store and forward mailboxes.   Thus  if  for 
             example  you  want  to  use 4Z4ZB as  a  store  and  forward 
             mailbox,  you  will have to create a file  called  4Z4ZB.MBX 
             using the non-document mode of your word processor.  In this 
             file  you will put a list of the call signs of the  stations 
             4Z4ZB  can  connect to reliably.   If for example  you  want 
             4Z4ZB to be able to store messages from you to 4X6AA, 4X6LR, 
             G3ZCZ, ON8IK, F0WN,and G8BTB, you would put those call signs 
             in the file, one call on a line as follows.

             4X6AA
             4X6LR
             G3ZCZ
             ON8IK
             F0WN
             G8BTB


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 42



             When the QRU function is invoked either by you using Control 
             Function key 3 or by 4Z4ZB connecting to you and sending you 
             the command :QRU:  ,  any messages addressed to any of those 
             stations  (EG.  G3ZCZ.OUT and ON8IK.OUT) will be transferred 
             from  you  to  4Z4ZB just as if you had  tried  to  QSP  the 
             messages  manually  or as if G3ZCZ or ON8IK   had  connected 
             directly to you.  The file names will be changed to *.OLD.

             You  must  create  one file for each  designated  store  and 
             forward station, ie. 4Z4ZB.MBX, G3ZCZ.MBX etc.

             5.0  Initialization

             5.1  Copy the files to a working disk.
             5.2  Edit PK232COM.SYS. If you are upgrading from a previous 
                  version  of PK232COM,  note that the new .SYS file  may 
                  not compatible with the old one.
             5.3  Copy the new PK232COM.SYS onto the old one.
             5.4  Put  the  working disk into the active drive  (the  one 
                  with the > prompt).
             5.5  Make sure that the file CONFIG.SYS exists and  contains 
                  the statement FILES=20.
             6.0 Running the Program

             6.1  Make sure that the PK-232 is connected to the computer.
             6.2  Make  sure that the DOS calendar date and time are  set 
                  to UTC.
             6.3  Run the program by typing the word PK232COM followed by 
                  the ENTER key.
             6.4  When  the program begins,  you will default  to  PACKET 
                  mode on VHF (Just like the PK-232 at switch on) in  the 
                  TRAFFIC terminal mode.  If the PK-232 is not set to the 
                  correct  baud rate and parity type the * characters  as 
                  explained in the PK-232 manual.    
             6.5  Initialize  the TNC using Alternate Function key 2.

             If  the PK232 does not have any batteries in it,  make  sure 
             that  the  RS-232 link between the TNC and the  computer  is 
             connected   then   load   and  run   PK232COM.    When   the 
             initialisation is over,  power up the TNC and type a few '*' 
             characters  as requested in the manual.   Once you  see  the 
             sign on message,  configure the TNC using Alternate function 
             key number 2.  To save you going through this rigmarole each 
             time  you power up the unit,  put some batteries in the TNC.  
             Use  good  quality  ones so that they don't  leak  over  the 
             circuit board.

        7.0 Mailbox features

             7.1 Answering Machine.

             The  program includes an AMTOR (Robot beacon CQ  mode  only) 
             and  PACKET mode   SMART "answering machine" facility.   You 
             can  leave messages on your disk (in the same  directory  as 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 43


             the  PK232COM.* files,  if you are using a hard  disk),  for 
             different  stations.  When someone connects to you,  if  you 
             left  a message for him,  he (or she or even it as the  case 
             may be) and only that station will receive it automatically.  
             No one else will normally be able to download that message. 

             7.2  Mail Beacon (Annunciator).

             To ensure that people know that you have left a message  for 
             them a 'MAIL for' list is loaded into your Packet Beacon and 
             transmitted  every 30 minutes (Refer to the BTEXT command in 
             the TNC manual) as  ':QTC:' followed by a list of calls.  If 
             no mail is pending then beacon transmissions are  inhibited.  
             This conforms to good operating practice on crowded channels 
             (at least inhibiting the beacon does).

             The  mail beacon in the AMTOR mode is transmitted as part of 
             the beacon autocq message.  It is automatically updated when 
             a message is transmitted.   If you don't set the beacon (see 
             below)  you  will not transmit a mail beacon  text  in  your 
             AMTOR CQ message.

             The  Mail  beacon text is set up either when  you  tell  the 
             computer to set it up using Shift function key 6 or when you 
             disconnect a packet QSO from another station.  

             In  this manner you may update the list while the program is 
             running,  for example by using Sidekick to write a  message, 
             or  preferably the NOTE function,  and then with a stroke of 
             Shift function key 6,  you will update the mail announcement 
             on your beacon.

             Any  station using PK232COM Version 1.42+ can be  configured 
             (default   state)   to  automatically  attempt   a   connect 
             (QTC_Snatch)  when  seeing their callsign in someone  else's 
             PK232COM :QTC: beacon mail message list.

             If  for some reason the message got lost  (eg.  because  the 
             link  was marginal),  :QSM:  in version 1.42+ will get you a 
             repeat of that message.

             7.3  How to leave a message

             You  can use the note function (Control function key  3)  or 
             type the message as a non-document file on Wordstar,  or  if 
             you  use another word processor,  you must leave the message 
             as an ASCII text file.  

             You  may also use the NOTE function built into the  program.   
             If you do,  the message will be given a header as if it came 
             in from someone else.   if you use a word processor to write 
             the  message,  you  will have to write in a header  or  show 
             somehow that the message is not 'live'.

             You  just  name  the message file as  the  callsign  of  the 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 44


             station  to whom you wish the message to be sent at  connect 
             time.  You must also give it the filetype of 'OUT'.

             For  example a message for G3ZCZ would be stored on the disk 
             as  a  file named 'G3ZCZ.OUT',  and similarly a  message  to 
             4X6AA would be stored on disk as '4X6AA.OUT'.  

             Once the message has been sent, an entry to that effect will 
             be made in the PK232COM.RUN  data capture file.  The message 
             file  will  then  be renamed and given  the  file  extension 
             '.OLD'.  At that time any previously existing mail file with 
             the  file extension '.OLD' will be deleted.   This stops the 
             addressee  receiving  the message on successive connects  if 
             you  can't delete it for some reason (you forget)  while  at 
             the same time, the message is still available to you in case 
             you need it.

             You  should use a utility program if you want the  calls  in 
             the  mail beacon sorted.   You may for example wish to  sort 
             them  alphanumerically or in the order of the date that they 
             were left in your answering machine.

             7.4  Remote File Downloading (Packet/AMTOR Modes Only).

             There  comes  a time when you want to leave a file  on  your 
             system  for someone to download later.   You can do this  by 
             using NC/L to control the transfer.  You must leave the file 
             in  a subdirectory called \PK232COM\FILES.   You must  first 
             create  it if it does not exist.   The station who wants the 
             message just asks for it using :QBM:  <filename>,  note they 
             do  not need to use the full subdirectory path.   They  must 
             however leave a single space character between :QBM: and the 
             filename.  In AMTOR the Mailbox must be turned on for remote 
             control functions.

             For example,  you have the latest ARRL DX bulletin,  and you 
             want to pass it on.  You could pass it to selected people by 
             copying  the file to individual messages with  the  filetype 
             '.OUT',  eg.  4X6AA.OUT,  4Z4ZB.OUT or even G3ZCZ.OUT if you 
             want me to get it, which wastes a lot of disk space.

             On  the  other hand you could tell people that the file  was 
             available  for  downloading,  either in  the  CTEXT  connect 
             message line which everyone gets when connecting to you,  or 
             in individual ('.OUT') messages.

             If  you  include   the  following  in  your  CTEXT   message 
                       "ARRLDX.015 now available"
             people will know that to download it, they just have to type 
             the  line ':QBM:  ARRLDX.015' (one space  character  between 
             :QBM:  and the file name) to get the file.   PK232COM is not 
             designed as a BBS,  however, if you copy the contents of the 
             \PK232COM\FILES subdirectory into a file called DIR (USE DIR 
             > DIR in DOS),  anyone can get a list of files the files you 
             have  stored  in it for downloading by  typeing  :QBM:  DIR.  


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 45


             Since they do not get the real directory,  just what was  in 
             it  at the time you copied it into the file 'DIR',  you  may 
             keep  "hidden"  files in this subdirectory.   You  may  thus 
             leave  a file for someone to download,  tell them by leaving 
             them a message (which they will get automatically when  they 
             connect)  and  no one else connecting will know that  it  is 
             there.
             
             When the QRU function is invoked either by you using Control 
             Function key 3 or by 4Z4ZB connecting to you and sending you 
             the  command :QRU:,  any messages addresses to any of  those 
             stations  (EG.  G3ZCZ.OUT and ON8IK.OUT) will be transferred 
             from  you  to  4Z4ZB just as if you had  tried  to  QSP  the 
             messages  manually or G3ZCZ or ON8IK  had connected to  you.  
             The file names will be changed from *.OUT to *.OLD.
             
             You  may only use the QRU function with stations  designated 
             as Store and Forward mailboxes.  Put a list of stations that 
             you can connect to reliably in your <callsign>.MBX file  and 
             send  it  to other stations in your LAN also using  PK232COM 
             Rev  1.36 or higher.   They will then be able to dump  their 
             mail  messages on you and you on them.  If they do the  same 
             and  send  you  their file,  then you will be able  to  send 
             messages via them for stations that they can work.

             While  QRU gives you the capability to bulk upload  messages 
             to  another station in your local area,  when you take  your 
             machine off line,  it may also be used to transfer  messages 
             between  two  LANs (such as the Baltimore and Washington  DC 
             Areas) via well sighted gateway digipeaters.

             7.5 Remote Beacon shutdown.

             I recognize that some stations may abuse the beacon facility 
             of  this  program.  I  have thus built into  the  program  a 
             'remote  shutdown' capability.   If someone running PK232COM 
             has their beacon timer set too often, connect to them in the 
             AMTOR   or  Packet Communications modes,  and tell  them  to 
             :QRT:  which will clear their beacon mode and take them  off 
             the air for a while at least.

             In  the  Packet communications mode,  the CQ beacon is  shut 
             down but the 30 minute mail beacon is not touched.   In  the 
             AMTOR communications mode,  the CQ delay time is set to 255. 
             The  Mailbox  will thus still be active in both  modes,  but 
             will not beacon on the air at the frequency it was set at.

        APPENDIX 0. UPDATES/REVISION HISTORY

        1.30 PACKET  MODE  Automatic Logging of  Connects.  Automatic  CQ 
             beacon added.  AMTOR Time shown in 'OVER' sequence. Callsign 
             sequence text added in ARQ call.  Automatic CQ beacon  added 
             with  logging  in  beacon  mode.    NON  PACKET  MODES  Semi 
             automatic logging added.   Call sequence changed to one line 
             except for CQ calls. Retry sequence works in all modes.


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 46



        1.31 Contest  Mode.  Function key 3 operation slightly  modified. 
             AMTOR  answering machine added.  Overwrite of status  window 
             fixed.

        1.32 Packet Mode Store and forward LAN :QSP: capability added.

        1.33 :QBM:   message/file   downloading  added  in  Packet  Mode. 
             Digipeat traffic mode logging added. File handle bug.

        1.34 File  handle  bug fixed,  logging/capture file  opens/closes 
             with  each  QSO.    Digipeat  detect  works  for  reciprocal 
             operators, ie >G3ZCZ>  for G3ZCZ/4X. Logbook file created if 
             non  existant.  Some changes in AMTOR beacon  signal  recog-
             nition algorithm. PK232COM.DIR directory added. 

        1.35 Digipeat   detect  now  stores  data  as  well  as   address 
             information on disk. 

        1.36 LAN :QRU:  store and forward added, code condensed.  Display 
             of  Multiple  connect  mode added.  Changes  in  NC/L  :QBM: 
             changed  to :QRV:  in message mode only.   Digipeat  logging 
             does not indicate times of logging on/off.

        1.37 AMTOR  now doesn't send Brag Tape in non beacon automatic CQ 
             mode.   Timeout added in PACKET Beacon mode to stop  station 
             connecting and holding system.

        1.38 V and H (direct Packet mode VHF/HF) added to function key 6. 
             Code  condensed  again.  AMTOR  ROBOT override  manual  mode 
             added. Packet loop back call added.

        1.39 CQ text change added to Alt F6.   AMTOR non beacon mode auto 
             CQ sends a callsign sequence and +?  when someone calls  in.  
             Note  feature added to Cont F3.  QRU echo's QSP  to  sending 
             terminal.   Printer toggle added.  RTTY 'RY' changed back to 
             single line in CQ mode.   AMTOR CQ works with EPROM  version 
             4/87.  Digipeat Display function now toggled on/off by Alt F 
             key (default is OFF).  CQ delay time now adjustable on-line. 
             Minor code changes within the program.

        1.40 Thirdpary  callsign  correct in 'QNO 1' response  situation. 
             Alt R key (Message Relay Capability toggle) added.  TNC type 
             line  added to PK232COM.SYS.   TNC2 code  added.  Additional 
             Baud rates added.   Internal code condensed. An active Store 
             and  forward  Relay status is indicated in  connect  message 
             '*** PK232COM 1.40' by the 'R' suffix. SIGNAL mode [G] added 
             to  function 6.  Digipeat display function also now controls 
             'MDIGI'.

        1.41 Packet  mode Baudrate,  shift reverses (change in 1.40)  now 
             done in command mode.  Delay added in Alternate function key 
             2 (TNC Initialise routine).  Commands transmitted in command 
             window, replies now show up in INwindow.



        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 47


        1.42 Path  determination  capability  (get  other  stations  'MH' 
             list), :QMH: added, multi user modes including conferencing, 
             code  compaction.  Packet  mode Alert  function  added.  '/' 
             character  added  in message header between date  and  time, 
             Terminal baud rate now 1200/2400/4800/9600,  Receive  buffer 
             expanded  from  128 bytes to  1K  bytes.  QTC_Snatch  added.  
             Packet mode Target call function added.  Outgoing text color 
             changed  to  light green (shows up better on mono  CRT  used 
             with  CGA).  Timetag  of logged events now  includes  dates.  
             :QSM:  for repeat of messages,  AMTOR Robot/Mail Beacon/Mail 
             headers  now without ?  marks.  Digipeat display and logging 
             function  (Alternate F key) now works for TNC2.  Alt B  key, 
             Direct Baudot/ASCII baud rate settup added.  Alt F5 or  'MH' 
             now has own window.  QTC_Snatch bug in TNC2.

        1.43 QTC_Snatch  bug fixed.  Target call function now also  works 
             properly  via  digipeater.  'DCD on' not sent to  non  PK232 
             TNC's.

        1.44 'MH'  window  module  code changed.  NET/ROM path  added  in 
             PK232COM.DIR   file.   TNC1 capability added.   Remote  TNC2 
             disconnect now returns you to command mode.

        1.45 TNC specific code modified.   PgUp key function added. AMTOR 
             function  key  8 now turns off transmitter and puts  you  in 
             ALIST   mode.   Mailbox   added  to   AMTOR   mode.    AMTOR 
             Robot/Mailbox  call recognition algorithm improved.   Target 
             call  changed  to Alternate T key.  Alt C key  now  same  as 
             Function key 7.   MH,  Help and DIR windows displays, freeze 
             until  key depressed.   Input buffer size increased  to  8K. 
             Check  added  on setting of CQ Delay.   Dialog condensed  to 
             save memory space.


        APPENDIX 1. ANOMALIES (and BUGS)

        A1.1 Since  the  Program  right  now has  no  way  to  check  the 
             command/converse mode status of the TNC, you may see various 
             cmd: and error messages from the TNC when using the function 
             key  commands.   Ignore them for now.   If you get an  error 
             message, try using the function key again.

        A1.2 In the AMTOR Beacon CQ mode,  if the other station drops the 
             link while you are recording the text, the program will time 
             out  before logging the QSO and restarting the CQ  sequence.  
             If  someone else calls in before the timeout  has  occurred, 
             the text from both stations should be captured to disk,  but 
             the  log  entry may not show both stations,  thus the  'LOG' 
             must be compared with the 'RUN' file for QSL purposes.

        A1.3 In the AMTOR Beacon CQ mode,  if another stations sends a +? 
             in  the  FEC  mode,  the  beacon will attempt  to  send  the 
             PK232COM.TXT file.  The PK232 however is not in the converse 
             mode at that time and will interpret the text of the file as 
             commands.   If  by some chance,  the text corresponds  to  a 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 48


             valid  command  the  PK232 will execute it and you  may  not 
             notice  that it did until you begin to wonder why nobody  is 
             replying to the beacon.   As such I recommend that the first 
             character  of  each line in the file PK232COM.TXT be  a  non 
             valid command character such as a number or a period (.)  or 
             another punctuation sign.

        A1.4 PK232COM versions 1.00 to 1.39 were written for a PK232 with 
             an Oct 1986 ROM.   There may be differences with later ROMs. 
             Version 1.39 works with the April 1987 ROM.

        A1.5 If you are using a CGA card with a monochrome  monitor,  the 
             text  you  type into the OUTWINDOW will be fainter than  the 
             incomming text.   This is because it is set to light  green.  
             If  you  are using a Hercules compatable card you  will  not 
             notice any difference.  

        A1.6 The  conference mode has been tested on a PK232 and a  SANYO 
             MBC-675  which  has a clock speed of 4.7MHz.   If  you  have 
             problems  with  intermittent selection of  IO  channels  try 
             slowing down your CPU clock.  There is a software delay loop 
             in  the program that is used to allow the TNC time to switch 
             IO streams after receipt of the stream change command.  This 
             delay is there because PK232COM tests for a connect on  each 
             channel before outputting any text, so that it does not send 
             unaddressed packets on non connected IO channels.

        A1.7 A  Packet conference Mode disconnect returns the TNC to  the 
             command  mode,  even if you remain connected to one or  more 
             other stations.

        A1.8 When using the non packet modes the 'long' time the software 
             takes  to rewrite the screens for each character means  that 
             there is a  delay in fiollowing the typing.  If this bothers 
             you,  set  EAS  OFF for manual operation (from  the  command 
             mode),  but don't forget to turn it on when using the autocq 
             mode.

        A1.9 Strange Events.
             If  the TNC does not use an interrupt driven serial port you 
             may  experience problems when using baud rates greater  than 
             1200.   The PK-232 does not like PK232COM to use RS-232 baud 
             rates faster than 2400,  and sometimes not even  that.   Use 
             1200  until  you have tested and are sure that a faster  one 
             will work.  

             IF  YOU  HAVE ANY STRANGE PROBLEMs AND ARE USING  an  RS-232 
             TERMINAL  BAUD RATE to the TNC WHICH IS GREATER  THAN  1200, 
             set  the  Terminal Baud Rate to 1200 and see if the  problem 
             goes away.

        As there are many different configurations of IBM PC  Compatables 
        and TNC's, I can't test all of them before releasing a version of 
        the program.   If a function does not work on your configuration, 
        after retrying it using 1200 bauds on the RS-232 line between the 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 49


        computer  and the TNC (see Section A1.9),  inhibit it and let  me 
        know  about  it.   It  will be made to  work  in  the  subsequent 
        release.

        APPENDIX 2. Local Area Network Capablity

        VHF  Packet  radio systems can be considered as part of  a  Local 
        Area  Network (LAN) in which messages can be left by one  station 
        in the computer belonging to a second station.  At HF the same is 
        true,  but  the area becomes greater.   The basic problem here is 
        that  people  can only send and receive messages to or  from  you 
        when you are on-line.   To compensate for this, BBS stations were 
        developed  which allowed both messages and bulletins to be stored 
        by anyone for later retrieval.

        PK232COM  allows you to store messages in your computer so as  to 
        use  it as an automatic answering machine.   Thus by storing  the 
        messages in a file called by the name of callsign,  with the file 
        extension  '.OUT',  anyone  connecting to the computer  will  get 
        their  message without having to request it.    PK232COM  Version 
        1.32 extends that concept to cover the eventuality of you wanting 
        to take your computer off-line for some reason.  You may now load 
        the  message  into any other computer you can  connect  to  using 
        elements  of  the Q code adapted to the High Level  Network  Com-
        munications  Language  (NC/L)  proposed in my book  Software  for 
        Amateur Radio,  (Book number 1560) published by TAB  Books,  Blue 
        Ridge Summit, Pa. 17214 USA.

        A2.1 LAN Protocol (G3ZCZ Version)

             The  protocol is as follows.  When connected to someone  who 
             has  their  computer configured as a host,  if you  want  to 
             store  a  message you send the following instruction to  the 
             other station :QSP: <callsign> where  <callsign> is the call 
             of the station that the message is for,  not the callsign of 
             the  host  station  in whose computer you  are  storing  the 
             message.  [Note  use  only  one space  character  after  the 
             :QSP:].   PK232COM  sends the  :QSP:  message  automatically 
             using Control Function Key 3.

             For  example  if  you want to store a message for  4Z4ZB  in 
             4X6AA's computer which is configured as a Store and  Forward 
             system,  you  would first connect to 4X6AA and then send the 
             message as
                        :QSP: 4Z4ZB .
             Better still use function key 3 to automate the sequence.

             The  computer at 4X6AA will respond either with a  statement 
             saying  that  it is ready for you to go  ahead,  or  send  a 
             message saying that it can't comply.  If it is ready you get 
             a positive reply which will take the form :QRV:   <callsign> 
             which if you know the Q code, means " I am ready to accept a 
             message for  <callsign>".

             At this time you may go ahead and send the message.   If you 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 50


             type  the  message at the keyboard,  you may  use  either  a 
             control  Z  (^Z) character or the character  sequence  :EOF: 
             followed  by a carriage return (the ENTER key) to  terminate 
             the  message.   If you have first written the message into a 
             text file you may then send it using function key 2  and the 
             termination sequence is automatic.

             Once  you  have  completed the  message,  the  other  (host) 
             computer  will  either  reply  that  the  message  has  been 
             successfully stored or give you an error message.

             If the message is stored and ready to be sent next time  the 
             addressee  connects  to  that computer,  you  will  see  the 
             message :QSL:  on your screen.  If something went wrong, you 
             will  get  back  a negative message taking  the  form  :QNO: 
             followed  by  a  number.   The  number  tells  you  why  the 
             operation failed.

        A2.2 Message Format

             The  message  is stored just as if you had left it  in  your 
             system  (except that a header is added identifying the  time 
             of reception and the call of the sending station).   It will 
             contain  a header showing the date and time it was  received 
             and  your  callsign.   Should  a message  for  that  station 
             already be in the system,  yours will be appended to it.  In 
             the  event  the your upload is aborted,  the amount of  text 
             received  before  the abort occurred will be stored  as  the 
             message.

             When you disconnect from the host station,  its mail  beacon 
             will be updated.

             Once  the  message  is loaded in the host,  it can  only  be 
             deleted  by  the operator of the  host  station.   When  the 
             addressee connects to the host and receives the message, the 
             file type will change from '.OUT' to '.OLD'.

        A2.3 File downloading

             See section 7.4 for the use of :QBM: for downloading text or 
             ASCII files from another PK232COM system.

        A2.4 Path Determination to a Dx station

             If  you  want  to establish a digipeat  path  to  a  station 
             somewhat out of your direct range, you need to know which of 
             the  stations that you can connect to can hear that  desired 
             DX  station.   If  you could get a call monitored (MH  list) 
             from the stations that you connect to,  you would be able to 
             see  if  the  station you are connected to  has  heard  your 
             desired DX station.   

             PK232COM  uses  the :QMH:  command to request such  a  list.  
             When   PK232COM  (Version 1.42+) receives a  :QMH:  command, 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 51


             it  drops  back  to the TNC command mode and issues  a  'MH' 
             command  to the TNC (except to a TNC1 which does not support 
             it).  It stores the list received in a temporary buffer, and 
             then  returns  to the converse mode and transmits  the  list 
             back to the station it is linked to.

             By  judicious use of :QMH:  you can determine paths to other 
             stations.   Note however,  that just because one station can 
             hear another station,  it does not mean that it can work it.  
             For  example,  the  station  you are connected  to  (running 
             PK232COM Version 1.42 or greater) may be using a power level 
             of  1 watt or so,  while the station 200 miles away that  it 
             heard was using 100 watts.   Test the path yourself,  or/and 
             leave a message asking how reliable the connect path between 
             those two stations is.

             If  you and a small group use a non standard packet  channel 
             for  inter-group communications,  you may also use the :QMH: 
             function to find out who the station you are connected with, 
             has heard recently, when you first sign on the LAN channel.

        APPENDIX 3     BASIC NC/L DICTIONARY
        Messages can be transferred into any other PK232COM computer  you 
        can connect with using elements of the Q code adapted to the High 
        Level  Network Communications Language (NC/L) proposed in my book 
        Software for Amateur Radio,  (Book number 1560) published by  TAB 
        Books, Blue Ridge Summit, Pa. 17214 USA.

        To  receive  a message,  do nothing,  you will receive your  mail 
        automatically  when  connecting/linking with a PK232COM  station.  
        You cannot normally read messages adressed to another person.

        A3.1  :QBM: To download a file, send
                    :QBM: filename.type
                    The filename.type is the file you want. For example 
                    :QBM: dir
                    :QBM: help
                    :QBM: pk232com.doc

        A3.2  :QMH: To  request  a  call monitored list ('MH')  from  the 
                    station  that you are connected with  using  PK232COM 
                    (1.42+), send
                    :QMH:

        A3.3  :QSM: To request a repeat of a message from a station using 
                    PK232COM (1.42+), send
                    :QSM:.
                    This  command  will  be valid as  long  as  the  host 
                    station  has  not deleted the <yourcall>.OLD file  on 
                    his  disk.   If  the file does not  exist,  you  will 
                    receive a :QNO: 2 'error' response.

        A3.4  :QSP: To leave a message, send
                    :QSP: callsign
                    the callsign is that of the station you wish to leave 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 52


                    a message for.

        A3.5  :QRT: To  shut  down an  AMTOR/Packet  mode  Mailbox/beacon 
                    station which is causing QRM,  link or connect to the 
                    station and send
                    :QRT:

        A3.6  :QRU: To  upload messages from one PK232COM (1.38+)  system 
                    to your computer, send 
                    :QRU:

        Computer responses

        A3.7  :QNO: 'NO' or error

                    QNO Error Values.
             The  following  error numbers are  associated  with  message 
             store and forward operations.

             ?    What you typed was not an NC/L command.
             1    Computer not configured as Store and Forward system.
             2    Requested ASCII file/ message (:QBM:) does not exist.
             3    You  made an error in the name of the callsign for whom 
                  the  message  is  intended  (It  must  be  at  least  3 
                  characters long).
             4    File creation error in host system.
             5    Error occurred during reception and storage of message. 
                  Could  be  that the computer ran out of  space  on  the 
                  disk,  or  something  else  went wrong in  storing  the 
                  message.
             6    :QRU:  You  are not authorised as a store  and  forward 
                  mailbox.
             7    :QRU: Error in opening <callsign>.MBX file.
             8    :QRU: Error in closing <callsign>.MBX file.
             9    :QRU:  Sequence   Error  in callsign of message to  go.  
                  The bad callsign will be shown after the error number.
             90   NC/L defined function not implemented in this release.
             99   PK232COM compatable program, but requested function has 
                  not been implemeted.

        A3.8  :QJG: The  QRU  sequence is complete.   There are  no  more 
                    messages pending.

        A3.9  :QRV: callsign 
                    The  computer is ready you to send the  message.  End 
                    the message with a control Z (^Z) character,  or  the 
                    sequence :EOF: .

        A3.10 :QSL: callsign 
                    Confirms receipt of message to that callsign.   It is 
                    also used to acknowledge receipt of a ':QRT:' comand.

        A3.11 :QTC: messsage list.
                    This  precedes a list of callsigns for whom  messages 
                    are  stored up on a computer.   It is used in  Packet 


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 53


                    Beacon  transmissions or AMTOR Beacon mode CQ  calls.  

                    If PK232COM receives :QTC:  it will respond with  the 
                    beacon text showing the mail queue.  

                    You can configure your version of PK232COM to issue a 
                    QTC_Snatch connect request to any other station using 
                    the  PK232COM beacon transmission to signal that  you 
                    have a message waiting.


             PROPOSED EXTENSIONS

        A3.12 :QYU:     YAPP format file upload.
        A3.13 :QYD:     YAPP format file download.

        APPENDIX 4. USING OTHER TNC'S.

        PK232COM  is  designed for the PK232.   However the  PACKET  mode 
        capabilities  can  be  used  on other  TNC's.   There  are  minor 
        differences in the command dialog between different  TNC's.   The 
        dialog  differences affecting the operation of PK232COM are built 
        into  the  program  and set when the TNC type is  read  from  the 
        PK232COM.SYS file at the program load time.  The non packet modes 
        will obviously result in error messages if attempted on a  packet 
        mode TNC.

        The   following  notes  apply  to  different  TNC's  or   digital 
        communications controllers.

        A4.1 TNC2 (MFJ 1270)

             A4.1.1     Default Commands.

             Edit  the  PK232COM.SYS file taking out the  PK232  specific 
             commands,  namely  anything  that is not mentioned  in  your 
             manual.   Add  in the default state for the TNC commands not 
             included  in the file and make sure that you set  AUTOLF  ON  
             and MCON ON.   If you are going to use the conference  mode, 
             set the multi user defaults to show the callsign in the text 
             header that the TNC sends to the computer.

             A4.1.2     Program differences.

             The following functions DO NOT WORK because the TNC does not 
             support them.

             All NON PACKET modes.
             Software controlled HF/VHF switching.
             Software controlled baudrate switching.
             MAIL Packet terminal mode (Alternate Function key 4). 
             CQ/BEACON Packet terminal mode (Alternate Function key 4).
             TNC Transmit Buffer flush (Control Function key 9).

        4.2 TNC1 (HD-4040)


        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 54



             A4.2.1     Default Commands.

             Delete or rename the PK232COM.SYS file.  Rename the TNC1.SYS 
             file to PK232COM.SYS and edit it using your wordprocessor in 
             its non document mode to customize it to your station.

             A4.2.2     Program differences.

             The following functions DO NOT WORK because the TNC does not 
             support them.

             All NON PACKET modes.
             Day/Time functions (Control function key 1).
             'MH' and remote :QMH: functions (Alternate Function key 5).
             MAIL Packet terminal mode (Alternate Function key 4). 
             CQ/BEACON Packet terminal mode (Alternate Function key 4).
             TNC Transmit Buffer flush (Control Function key 9).
             Conference and multi-connect modes.

        APPENDIX 5. NOTES

        I'm   always  interested  in  your  bug  reports,   comments  and 
        suggestions for changes.  In particular, what if any, binary file 
        transfer mode(s) should be supported.

                    For  the  latest  information on  Updates,  read  the 
                    UPDATE.* files on the distribution disk.





























        PK232COM.DOC (c) G3ZCZ 1987





        PK232COM VERSION 1.45  PAGE 55


        APPENDIX 6 REGISTRATION FORM.


        To: Joe Kasser G3ZCZ
             P O BOX 3419
             SILVER SPRING
             MD 20904.



        CALL ________________   TODAY'S DATE _____________

        NAME ______________________________________________

        ADDRESS ___________________________________________

                ___________________________________________

        CITY    ___________________________________________

        STATE   _________  POSTCODE  ______________________

        TNC TYPE _____________________

        I enclose a check for $35.00.  Please send me the latest  version 
        of PK232COM customised to my call and TNC,  and resister me as  a 
        user  of PK232COM.   I am currently using Shareware Version _____  
        which I obtained from  _________________________________________.

        The  first  10 lines of my current PK232COM.SYS file  are  listed 
        in the blank space below.

        Signature 


        Comments, likes, dislikes, wish list, etc.





















        PK232COM.DOC (c) G3ZCZ 1987