XMDM.EXE
			----------


This is a special implementation of the XMODEM protocol transfer. It runs
"beneath" Crosstalk, and is invoked via the Crosstalk "RUN" command.  It
will not run as a stand alone module.

HISTORY
=======

Because there is no "official" version of the XMODEM protocol, it is
impossible to create a universal implementation of XMODEM that will
work with all other XMODEM implementations.  Ward Christensen has been
quoted as saying that XMODEM was a "quick hack"; nevertheless, it has
made possible the BBS culture that exists today, and it is a very common
file transfer protocol.

If you are having difficulty using the XMODEM options in CROSSTALK with
a particular system, and changing CROSSTALK's PMode setting doesn't help,
use XMDM with CROSSTALK's RUN command.

This stand-alone version of XMODEM was developed as an add-on Crosstalk
command.  It uses CRC if the other side can support it, otherwise it uses
the usual 8-bit checksum.

USE
===

   1) While online to the remote system via Crosstalk in terminal mode,
      start the other end of the XMODEM transfer, just as you would do
      in preparation for using Crosstalk's RX or XX commands.

   2) Get to Crosstalk's COMMAND? prompt (via ESC or whatever key you've
      set up as the ATtention key).

   3) Use the Crosstalk RUN command to run XMDM to do the file transfer:

     	RU XMDM S foo 1			(send "foo" using port 1)
     	RU XMDM R xyz 1			(receive "xyz" using port 1)
     	RU XMDM R xmodem.c 2		(receive "xmodem.c" using port 2)
	
      You could, of course, set up a function key to type the "RU XMDM " part.

   4) As the transfer proceeds, you will see status messages on your screen.

   5) When the transfer is complete, you will be returned to Crosstalk.

NOTE: Do not - repeat DO NOT - attempt to run this as a stand-alone transfer
program (i.e. - outside of Crosstalk). It has some very touchy and difficult
code that was specially developed just to allow "re-using" the serial port
without actually opening it. This program wants to use the same baud rate and
data structure that Crosstalk has already set up. So it doesn't set these.
It just (CAREFULLY) massages the 8250 and 8259 so that while this program
is running it has full input AND output interrupt-driven access to the port,
without disturbing the environment (hardware/software) set up by Crosstalk.

If you run this without first having "opened" the serial port (by running
Crosstalk etc), then the 8250 will very likely go haywire.

Don't be tempted . . .      Just DON'T!

				- Joan Riff,  3 March 1985