FNTCLEAN Documentation
                                April 15, 1988

                           FONTVIEW and FNTCLEAN are
                              Copyright (c) 1988
                                      by
                         S.H. Moody & Associates, Inc.
                              1810 Fair Oaks Ave.
                           South Pasadena, CA 91030

                             All Rights Reserved.


          FNTCLEAN reads HP-specification LaserJet soft font files (either
     Portrait or Landscape), strips leading, trailing, or imbedded non-font
     descriptor strings from the file, and writes a new file containing a
     full 64 byte (40 hex) LaserJet II font descriptor header.  Its
     function is to clean up shareware fonts so that they can be read by
     other public domain or shareware programs such as FONTVIEW, or to
     remove escape code sequences which assign a font number, make a font
     permanent/temporary or designate the font as primary/secondary.  These
     types of printer commands should not be imbedded in the font itself;
     they should be sent separately before or after downloading the font as
     is done by Gary Elfring's DOWNLOAD utility, and by the utilities in
     HP's PCL package.


                                 W A R N I N G

          Although I have taken pains within FNTCLEAN to insure that the
     program will not overwrite your input file, it's best to back it up
     before using FNTCLEAN.  In addition, if you erase your original file
     in favor of using the new file produced by FNTCLEAN, you do so at your
     own risk.  In no event will S.H. Moody & Associates be liable to you
     for any damages, including any lost profits, lost savings, or other
     incidental or consequential damages arising out of your use or
     inability to use the program, or for any claim by any other party. 
     Finally, you should be aware that many commercial soft font suppliers
     forbid their licensees (the purchasers of the soft font) to modify
     their fonts in any way.  The output file created by FNTCLEAN may be
     considered a modification by these suppliers.


                                USING FNTCLEAN

          The syntax for running FNTCLEAN is:

                         FNTCLEAN INfile.ext OUTfile.ext

          where INfile.ext is the DOS path (if you are using DOS 2.0 or
     later) plus the name of the font file to be read, and OUTfile.ext is
     the name you choose for the "cleaned up" file which FNTCLEAN produces.

          The DOS path + filename + extension of the input file can not be
     the same as the path + filename + extension of the output file.  One
     technique I often use is to use the same filenames for both files, but
     designate a different path for the output.  For example, I might
     create a DOS path called CLEANFNT but locate the input file in the
     FONTS directory.  Then I can use FNTCLEAN as follows:

                    FNTCLEAN C:\FONTS\DEMO.SFP C:\CLEANFNT\DEMO.SFP



                            REGISTRATION
     
     If you find FONTVIEW or FNTCLEAN to be useful, you are requested
     to register these programs.
     
          If you register FONTVIEW and FNTCLEAN, you will receive the
     latest versions of the two programs on a diskette, PLUS, you will
     receive a copy of the program FONTFIX.  FONTFIX, which works on
     portrait soft fonts, is an extremely hard-working program.  It has
     all of the features of FNTCLEAN, plus: 
 
          1.   Displays the hexadecimal values and interpretation of all 64
               bytes of the font header. 
 
          2.   Displays the HP LaserJet escape sequence which completely
               identifies the font and can be used by your word processor
               or spreadsheet to designate the font for use, once it has
               been downloaded. 
 
          3.   Sorts its output file by ascending ASCII numbers.  Amazing-
               ly, I have viewed many font files which do not have their
               character data sorted in ASCII order.
 
          4.   Has a Command line option to move the Baseline for all
               characters Up or Down by a user-selected number of dots. 
 
          5.   Has a Command line option to set the font's "x-height"
               either manually (in dots), or have the program set the font
               x-height using data from the lower-case "x" character (ASCII
               120) if it is included in the font file. 
 
          6.   Goes through each character in a font on a bit (pixel)
               level, along the top, bottom, left and right edges,
               eliminating superfluous rows of dots which are all "off";
               then adjusts left offsets, top offsets, character widths and
               heights appropriately, and reconstitutes the character.  It
               then returns to the FONT header, and resets the cell width,
               cell height, and baseline distance such that these values
               are correct.  This results in a font which uses the minimum
               number of bytes to fully describe each character, thus
               minimizing download time, LaserJet memory requirements, and
               disk storage requirements.  Several shareware fonts do not
               make effective use of top offsets or left offsets.  If you
               display a font which is not left-justified on the graphics
               screen and which uses the same height and width for each
               character, it is likely that the size of the file can be
               reduced.  For example, the shareware font LARGEHLW.SFP was
               34,773 bytes long originally, but only 16,992 bytes long
               after processing by FONTFIX.  Naturally, the modified font
               performed identically on my LaserJet printer.


          You may register both FONTVIEW and FNTCLEAN by forwarding $15.00
     to:
 
 
                         S.H. Moody & Associates, Inc.
                              1810 Fair Oaks Ave.
                           South Pasadena, CA 91030