****************************************************************

                             COMMUNICATION INTERRUPTS

                                September 5th, 1987

                                   By Dale Loftis

       ****************************************************************

This archive should contain the following files:

        COMINT.C                Test program and queue routines.
        COMINT.PRJ              Turbo C project link list.
        INT3.ASM                COM 2 interrupt assembly language routines.
        INT4.ASM                COM 1 interrupt assembly language routines.

       ****************************************************************

After finding a need for RS232 interrupt routines and not being able to locate
anything suitable on any BB's, I decided to write these routines and put them
on the service for others.

The INT3 and INT4 routines are the real heart of the routines as they place
the incoming and outgoing characters in the proper places.

I have succesfully run programs using these routines up to 9600 baud on a AT
and had no problems with losing characters.

If you decide to alter these routines be aware that using INTerrupts to place
the characters in queues like these routines do,  it is imperative that you
act upon the characters by bumping the appropriate pointers depending on 
whether your transmitting or receiving.

       ****************************************************************

com1_set_interrupt(parameters);  initializes port and sets interrupt vector
com2_set_interrupt(parameters);  initializes port and sets interrupt vector

com1_restore_interrupt();   restores interrupt vector in disables interrupts
com2_restore_interrupt();   restores interrupt vector in disables interrupts

       ****************************************************************

The com_status() routine displays the status of the program as it runs on the
line 24 of the screen and is formatted as follows:

      aaaa - bbbb   cccc - dddd  ee  ff  gggg - hhhh  iiii - jjjj  kk  ll

where -
                                 RECEIVE
   aaaa =  *   COM 1 in  queue pointer   (count of characters received)
   bbbb =  *   COM 1 out queue pointer   (count of received chars acted upon)

                                TRANSMIT
   cccc =  *   COM 1 in  queue pointer   (count of chars to be transmitted)
   dddd =  *   COM 1 out queue pointer   (count of chars that were transmitted)

                               INT STATUS
    ee  =      COM 1 last interrupt status
                    00 = modem status interrupt
                    01 = xmit holding register empty interrupt
                    02 = data received interrupt
                    03 = reception error interrupt

                               PORT STATUS
    ff  =      COM 1 modem status register status
                    bit 7   1 = "data carrier detect"
                    bit 6   1 = "ring indicator"
                    bit 5   1 = "data set ready"
                    bit 4   1 = "clear to send"
                    bit 3   1 = change in "data carrier detect"
                    bit 2   1 = change in "ring indicator"
                    bit 1   1 = change in "data set ready"
                    bit 0   1 = change in "clear to send"

       ****************************************************************

                                RECEIVE
   gggg =  *   COM 2 in  queue pointer   (count of characters received)
   hhhh =  *   COM 2 out queue pointer   (count of received chars acted upon)

                                TRANSMIT
   iiii =  *   COM 2 in  queue pointer   (count of chars to be transmitted)
   jjjj =  *   COM 2 out queue pointer   (count of chars that were transmitted)

                               INT STATUS
    kk  =      COM 2 last interrupt status
                    00 = modem status interrupt
                    01 = xmit holding register empty interrupt
                    02 = data received interrupt
                    03 = reception error interrupt

                               PORT STATUS
    ll  =      COM 2 modem status register status
                    bit 7   1 = "data carrier detect"
                    bit 6   1 = "ring indicator"
                    bit 5   1 = "data set ready"
                    bit 4   1 = "clear to send"
                    bit 3   1 = change in "data carrier detect"
                    bit 2   1 = change in "ring indicator"
                    bit 1   1 = change in "data set ready"
                    bit 0   1 = change in "clear to send"

       ****************************************************************
        Items marked with a "*" are the actual offsets into the xmit and 
     receive queues and wrap back to zero when the queue sizes are reached.
       ****************************************************************

The variables com1_rs232_error and com2_rs232_error contain the status from a
reception error interrupt and is the line status register, formatted as:

                    bit 7   1 = time-out (off-line)
                    bit 6   1 = xmit shift register empty
                    bit 5   1 = xmit holding register empty
                    bit 4   1 = break detect
                    bit 3   1 = framing error (transmission is out of sync)
                    bit 2   1 = parity error
                    bit 1   1 = received data overrun (char not read in time)
                    bit 0   1 = byte of data has been received

       ****************************************************************