NAME
	g31.c, g32.c, g3.h - portable Core System graphics package

DESCRIPTION
	This is a portable implementation of the Core System graphics package
	intended for implementation on microcomputers with graphics
	approximately equivalent to the IBM PC.  The Core System is described
	in Computer Graphics vol 13, no 3 (Aug 79), reprints of which are
	available from the Association for Computing Machinery (item number
	428791).  You can call ACM at 1-800-526-0359, ext.  75, to order a
	copy.

	Three classes of upward compatible levels are specified for Core
	Systems; one class for output, one class for input, and one class
	concerning dimensionality.  This implementation has:

		Output level 1: basic output

			There are no retained segments or image transformations
			(not to be confused with viewing transformations, which
			are of course provided).  Of the text primitives, only
			text() is provided, and text is generated only in
			"string_precision" (CHARPLANE, CHARUP, CHARPATH, and
			CHARSPACE not implemented).  This means that strings
			are always displayed from left to right, and there are
			no tilted characters.

		Input level 1: no input

			A simple cursor key interface is provided.

		Dimension level 2: three dimensional

			All 2D and 3D viewing transformations are provided.

	Some inquiry and setting functions have not been implemented - for
	example, set_viewing_parameters(viewing_parameter_array).  Some viewing
	operation functions may still follow the definitions in the 1977 draft
	of the Core System.

	None of the "raster extensions" have been implemented.

USAGE
	A program using G3 consists of three layers of software.  First is the
	application software, which interacts with the user, reads data, and
	generates an image in "world coordinates" using calls to the output
	primitives.  Second is the Core System graphics package itself (files
	G31.C and G32.C) which converts the image from world coordinates
	(doubles) to screen coordinates (integers) and calls the third layer,
	which deals with the graphics hardware and is therefore machine
	dependent.

	One way to structure the application program is as follows:

		<read_data>
		<initialize>
		do	{<generate image>
			<get input from user>
			}
		while (not_finished);
		<terminate>

IMPLEMENTATION
	This package was written for the DeSmet C compiler.  G31 and G32 are
	entirely in C, and are not known to depend on the operating system. 
	The interface routines GPC and GZ are partly assembly language, which
	the DeSmet compiler permits to be intermingled with the C code.  They
	require MS-DOS 2.0 or higher (because of their use of the environment).

	This implementation was written with approximately these priorities:
	(1) correctness (freedom from visible glitches), (2) speed, and (3)
	functionality.

	This package requires a set of interface variables and functions for
	each machine.  I've written interfaces for the IBM PC and Z-100.  Each
	of these interfaces implements two separate graphics modes.  The user
	chooses between modes by setting the environment variable GRAPHICS to a
	number.  I chose that method so the application software would remain
	ignorant of the existence of multiple modes.  (This does mean that the
	application software should initialize the graphics before using any of
	the variables declared in G.H.) An alternative would be to put
	equivalent data into a configuration file.

	I'd be glad to work with anyone who wants to port the package onto
	other computers or other compilers, or to add the things I haven't
	implemented.  I'd especially like to see some of the raster extensions,
	like area fill and hidden line removal.  Note - the Core System package
	currently does not require the line erase function.  It will require
	that function if is extended to include retained segments.  If no line
	erase function is defined, the variable erase_line should be set to
	point to the line drawing routine.

AUTHOR
	Copyright (c) 1985 by James R.  Van Zandt (jrv@mitre-bedford)
	27 Spencer Dr., Nashua NH 03062, 603-888-2272.  Resale
	forbidden, copying for personal use encouraged.  Constructive
	comments welcome.