COMRING1 is a collection of Lattice "C" functions that set up COM1 to be
completely interrupt driven. When you want to transmit something, it is
placed in the transmit ring, and you immediately regain control to do 
other processing. In the meantime, the interrupt routine is sending data
from the transmit ring out the com port. Later on, you can check to see 
if the operation is done, or add more data to the xmit ring before the
previous xmit is finished. The receive function works similarily. When a
character is received, it is put into a ring. When you ask for a byte,
it is taken from the ring. This isn't quite true multi-tasking, but it's
close.

This version is a test version. As soon as I am sure it is solid, it will
be easy to do the same thing for COM2. Eventually I intend to write a
multiple user BBS program that will not require any special software
like Concurrent DOS or Topview.

Each function is described below. They were compiled using the small model.
Support for the other models will come later.


************************************************************************

c1setup (rcvlen, xmtlen)
	int	rcvlen, xmtlen

Allocates storage for transmit & receive ring. Enables all interrupts
and sets new interrupt vector. Returns 0 if all ok, or 1 if insufficient
storage for rings.

************************************************************************
c1bcnt(rbc, xbc)
	int	*rbc, *xbc

Sends the current byte counts of the receive & transmit rings.

************************************************************************

c1init (speed, parity, databits, stopbits)
	int	speed, parity, databits, stopbits;

Initializes the communications port. Return codes are:
  0 - all parameters valid
  1 - invalid speed (110,150,300,600,1200,2400,4800,9600)
  2 - invalid parity ('S','M','O','E','N')
  3 - invalid data bits ('5', '6', '7', '8')
  4 - invalid stop bits ('1', '2')

************************************************************************

c1mstat()
	int function that returns modem status. Refer to Technical
Reference manual for bit meanings.

************************************************************************

c1rbyte (rb, rstat)
	char *rb, *rstat

int function that gets a received byte and status from the receive ring.
Returns 0 if a character has been received, or 1 if the ring is empty.

************************************************************************

c1smc(dsw)
	int	dsw

Sets modem control (dtr, rts) on or off.

************************************************************************

c1xmitb(xchar)
	char	xchar

Inserts a character into the xmit ring.

************************************************************************

c1xmits(string)
	char 	*string

Int function that puts a string into the xmit ring. Returns 0 if entire
string was put in, or returns number of bytes that weren't put in because
the ring was full.

************************************************************************

c1xmitsw(string)
	char	*string

Same as c1smits, but waits for the xmit operation to finish.

************************************************************************

ckxfull()

Int function returns 0 if xmit ring is not full, returns 1 if it is full.

************************************************************************



If you have any problems, comments, suggestions etc. leave me (John Cantlin)
a message on the Consultants Exchange RBBS (714) 842-6348.