SCREDIT

                             The Screen Management System





                                     Version 1.02


                                   October 1, 1989



                                    USER'S MANUAL



                               Designed and Written by

                                    Tim Underwood







          Programs  and  Documentation  Copyright  (c)  1988, 1989  by  Tim
          Underwood.  All rights reserved.

          Published by:

                         Tim Underwood
                         1719 S. Shiloh
                         Wichita, KS  67207 USA
                         316-687-5762

          Electronic Mail to:

               Compuserve 73577,1554
               The Source Connection BBS (316)-687-0012 24hrs 300/1200 8N1


          PC-DOS, PC, PC XT, PC AT, and PS/2 are trademarks of IBM Corp.
          MS-DOS, OS/2, and Windows are trademarks of Microsoft Corp.
          TurboC is a trademark of Borland International.
































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood






                                  Table Of Contents

          Introduction  . . . . . . . . . . . . . . . . . . . . . . . .   i
               Registration Information . . . . . . . . . . . . . . . . iii
               SCREDIT License Agreement and Limited Warranty . . . . .  iv
               Technical Support  . . . . . . . . . . . . . . . . . . .  vi

          Installation  . . . . . . . . . . . . . . . . . . . . . . . .   1
               Installing the Program . . . . . . . . . . . . . . . . .   2

          Configuring SCREDIT . . . . . . . . . . . . . . . . . . . . .   3
               Starting SCREDIT . . . . . . . . . . . . . . . . . . . .   5
               SCREDIT Examples . . . . . . . . . . . . . . . . . . . .   6

          Technical Information . . . . . . . . . . . . . . . . . . . .   7

          Keyboard Actions within SCREDIT . . . . . . . . . . . . . . .   8

          Function Definitions  . . . . . . . . . . . . . . . . . . . .   9
               abort_screen . . . . . . . . . . . . . . . . . . . . . .  10
               attr . . . . . . . . . . . . . . . . . . . . . . . . . .  12
               background . . . . . . . . . . . . . . . . . . . . . . .  13
               bad_amount . . . . . . . . . . . . . . . . . . . . . . .  14
               bad_date . . . . . . . . . . . . . . . . . . . . . . . .  15
               bad_entry  . . . . . . . . . . . . . . . . . . . . . . .  16
               blank_status . . . . . . . . . . . . . . . . . . . . . .  17
               decimal_char . . . . . . . . . . . . . . . . . . . . . .  18
               disp_io_fields . . . . . . . . . . . . . . . . . . . . .  19
               disp_prompts . . . . . . . . . . . . . . . . . . . . . .  20
               display_status . . . . . . . . . . . . . . . . . . . . .  21
               drcr_symbol  . . . . . . . . . . . . . . . . . . . . . .  22
               edit_input_fields  . . . . . . . . . . . . . . . . . . .  23
               err_attrib . . . . . . . . . . . . . . . . . . . . . . .  25
               err_column . . . . . . . . . . . . . . . . . . . . . . .  26
               errmsg . . . . . . . . . . . . . . . . . . . . . . . . .  27
               error_window . . . . . . . . . . . . . . . . . . . . . .  28
               foreground . . . . . . . . . . . . . . . . . . . . . . .  29
               get_cursor_type  . . . . . . . . . . . . . . . . . . . .  30
               getkey . . . . . . . . . . . . . . . . . . . . . . . . .  31
               make_bar_menu  . . . . . . . . . . . . . . . . . . . . .  32
               make_pulldown_menu . . . . . . . . . . . . . . . . . . .  35
               make_window  . . . . . . . . . . . . . . . . . . . . . .  39
               money_symbol . . . . . . . . . . . . . . . . . . . . . .  41
               move_window  . . . . . . . . . . . . . . . . . . . . . .  42
               move_windows . . . . . . . . . . . . . . . . . . . . . .  43
               note . . . . . . . . . . . . . . . . . . . . . . . . . .  44
               num_decimals . . . . . . . . . . . . . . . . . . . . . .  45
               remove_bar_menu  . . . . . . . . . . . . . . . . . . . .  46
               remove_pulldown_menu . . . . . . . . . . . . . . . . . .  47
               remove_window  . . . . . . . . . . . . . . . . . . . . .  48
               req_error  . . . . . . . . . . . . . . . . . . . . . . .  49

     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood






               restore_status . . . . . . . . . . . . . . . . . . . . .  50
               save_status  . . . . . . . . . . . . . . . . . . . . . .  51
               setcursor  . . . . . . . . . . . . . . . . . . . . . . .  52
               stat_attrib  . . . . . . . . . . . . . . . . . . . . . .  53
               status_row . . . . . . . . . . . . . . . . . . . . . . .  54
               tf_error . . . . . . . . . . . . . . . . . . . . . . . .  55
               undisp_prompts . . . . . . . . . . . . . . . . . . . . .  56
               yn_error . . . . . . . . . . . . . . . . . . . . . . . .  57
               ynb_error  . . . . . . . . . . . . . . . . . . . . . . .  58











































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood






          Introduction

          SCREDIT is a screen design utility program  and library functions
          designed to  aid the  programmer  in creating  and maintaining  a
          consistent user interface for  programming.  SCREDIT itself is  a
          WYSIWIG editor to design your screen, create both the header file
          defining  the  data structure  for  the  screen, as  well  as the
          external  definitions  for  the  entry  points  to  the  screens.
          SCREDIT has libraries for TURBOC 2.0,  both small model and large
          model.

          "OK.  Great.  But  why should I  use SCREDIT instead  of X Corp's
          Screen Designer?".

          SCREDIT  is different  in  many  ways to  what  you find  in  the
          majority  of  commercial  software.   Most  screen  designers and
          screen builders operate in one of the following manners:

               1.   They create a screen image on the disk, with a separate
                    screen image for  each screen.  A  skeleton program may
                    be  optionally  created   that  saves  you  some   work
                    initially.   This results in three problems.   You have
                    lots of screen images on the disk.  This takes up a lot
                    of valuable space for  the user of your software.   You
                    also  have a  maintenance  problem with  your software.
                    You not only  have to distribute updated  programs, but
                    also updated screens. If the user doesn't update one of
                    the  screens,  the software  probably  won't  know, and
                    won't operate properly.  For  the software that creates
                    skeleton code, you have another  problem.  You probably
                    won't use the code  as is, you will 'tweak'  it here or
                    there.  This  will result in more work for you when you
                    want to update the  screen.  You must either  select to
                    create another skeleton  program, transferring any  and
                    all  changes you  made  to the  original  code to  this
                    skeleton code, or  you must change your  original code.
                    There  is also a performance  penalty that must be paid
                    each time a  screen is  'loaded' from the  disk.   This
                    also creates another problem, the use of  a file handle
                    or  FCB.    FCB's  have   been  discouraged  since  the
                    introduction of DOS 2.0.   Using FCB's also presents  a
                    performance problem.   They  are not  as fast  as using
                    file handles.  (Test  it yourself.  Open and  close the
                    same  file  1000 times  using both  an  FCB and  a file
                    handle, timing the  entire loop.  Handles are  about 10
                    times faster.)   Using a file  handle for this  process
                    also takes away one file handle  you could use for your
                    program.  Any medium to  large scale program will  need
                    as many handles  as it  can get.   This means that  you
                    must always  leave one or more handles available to the


     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      i






                    screen manager, or you  run the risk of not  being able
                    to open the screen file to load the screen.

               2.   They create screen libraries, each library holding  one
                    or  more screens.   A  skeleton program may  be created
                    also.   This  option results  in the  same problems  as
                    option 1; maintenance of not only the program, but also
                    its  associated   screen  libraries,   as  well  as   a
                    performance penalty loading the screen from the library
                    on  the disk.   You  may also  'lose' one or  more file
                    handles.

               3.   They are simply a library of routines that you must use
                    to build your screen,  one prompt field at a  time, one
                    I/O  field  at  a  time.     This  method  has  several
                    advantages over #1  and #2.   They don't use files,  so
                    there  isn't the  performance  penalty associated  with
                    loading the data from the disk,  and you don't lose any
                    file handles.  They also have  some problems.  All that
                    data going to build those  screens has to go somewhere,
                    namely in the Data Segment.   That means that a program
                    that may work  today, may  not be able  to be  enhanced
                    next  week, as  you  have  finally  used  up  the  Data
                    Segment.   You may  not even  be aware  of the  problem
                    until a user  calls you  and says, "An  'Out of  Stack'
                    message just appeared on my screen.  What do I do?", or
                    they  may experience strange behavior in their programs
                    because the  program has  run out  of stack, and  stack
                    checking is not enabled.  This means that you will have
                    to change the memory model of your program.  Even using
                    an Overlay Linker may not solve your problem.

          SCREDIT solves these problems.  SCREDIT generates object files to
          be linked into your  program.  This means that you  don't have to
          worry about sending  updated screens with your  updated programs,
          as SCREDIT's screens  are linked into your program.   There is no
          disk I/O performance penalty  to pay either.  Screen  changes may
          result  in  nothing   more  than   re-linking  your  program   to
          incorporate those  changes.   The  Data Segment  problem is  also
          resolved.  All of SCREDIT's screens, regardless of memory  model,
          are stored in  the Code Segment.  That means that even very large
          Small Memory model  programs may  be created simply  by using  an
          Overlay  Linker.   The  code required  to  drive SCREDIT  is very
          simple, and may be duplicated from  one source module to another,
          requiring simple changes to accommodate each screen.  It helps to
          create modular code.

          SCREDIT allows you to re-edit your original screen, directly from
          the object.  You won't have to create intermediate source to edit
          the screens.


     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     ii






          Registration Information

          SCREDIT is  a  copyrighted program  protected  by both  U.S.  and
          international  copyright law.    You  are  authorized to  use  it
          without charge for a  limited period of time  under the terms  of
          the SCREDIT license  agreement.  After this time is  up, you must
          register and pay for SCREDIT to continue using it.

          This method of distribution is known as shareware.  It allows you                                                  _________
          to determine whether SCREDIT meets your  needs before you pay for
          it.

          The  registration  fee  for a  single  copy  of  SCREDIT is  $50.
          Payment of this fee entitles you to:

               A disk with  the latest  version of  SCREDIT, registered  to
               you.

               An upgrade to the next version of SCREDIT, and reduced rates
               on future upgrades.

               Technical support via electronic mail.

          If you prefer, you may register for $35 and receive only the disk
          and notices of  future upgrades.   Network,  site, and  corporate
          licenses are also available.


























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                    iii






          SCREDIT License Agreement and Limited Warranty

          (1)  The SCREDIT program and all other programs and documentation
               distributed  or  shipped  with  it  are  copyrighted   works
               protected by U.S. and  international copyright law.  In  the
               rest  of  this  document,  this  collection of  programs  is
               referred to simply as "SCREDIT".   You are granted a license
               to  use  your  copy of  SCREDIT  only  under  the terms  and
               conditions specified in this license agreement.

          (2)  SCREDIT is a commercial  software package.  It is  not free,
               and it is  not in the public  domain.  It is  distributed as
               shareware, which means that before you pay for the  package,               _________
               you may  try it and  see if you  want to continue  using it.
               You may  use SCREDIT  free for a  trial period  of up  to 15
               days.   If you  wish to  continue using  SCREDIT after  that
               period, you must  pay the registration  fee.  If you  choose
               not to pay the registration fee, you must stop using SCREDIT
               and remove it from your computer,  though you are still free
               to keep copies and pass them along to others.

          (3)  You may use your copy of SCREDIT  on a single computer.  You
               may also install it on a computer  attached to a network, or
               remove it from  one computer and  install it on a  different
               one, provided there is no possibility  that a single copy of
               SCREDIT will  be used on more  than one computer  at a time.
               Network, site, and corporate licenses are available from Tim
               Underwood.

          (4)  You may copy SCREDIT  for backup purposes, and you  may give
               copies  of  the  unregistered version  of  SCREDIT  to other
               individuals, which  they may  also use  and  copy under  the
               terms  of this  agreement.   If  you  copy the  unregistered
               version of SCREDIT for  others, you must include all  of the
               files distributed with it.

          (5)  You may NOT give, sell, or  otherwise transfer copies of the
               registered version  of SCREDIT to  any other person  for any
               reason.    However,  you  may  transfer  ownership  of  your
               registered copy to another person, provided that when you do
               so, you stop using SCREDIT and remove it from your computer,
               and notify Tim Underwood of the new owner.

          (6)  SCREDIT  may  be distributed  by  user groups  or commercial
               libraries.  You may charge for distribution or mailing fees,
               not to exceed $5.   Only copies of the  unregistered version
               may  be  distributed,   and  all   files  included  in   the
               unregistered version must be on the distribution diskette.

          (7)  SCREDIT is a powerful program.  While all attempts have been
               made to build  in reasonable safeguards,  if you do not  use

     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     iv






               SCREDIT  properly  you  may destroy  files,  or  cause other
               damage to your computer software and  data.  You assume full
               responsibility  for  the  selection and  use  of  SCREDIT to
               achieve  your  intended  results;  in  no  event  shall  Tim
               Underwood be responsible  for any damages whatsoever  due to
               errors  in usage  or your  failure to  read, understand,  or
               follow  instructions  in the  documentation.   Tim Underwood
               limits his warranty  to replacement  of a defective  program
               diskette or manual.

          (8)  Like  all  useful  computer  software,  SCREDIT  may contain
               errors in programs  or documentation.   If you find such  an
               error or are  otherwise dissatisfied with a  registered copy
               of SCREDIT, you may return the entire package at any time up
               to 90 days after purchase for a full refund of your original
               registration fee; such  a refund shall  be your sole  remedy
               for any program error(s).  Tim Underwood shall not be liable
               for any other costs incurred by you due to such errors.

          (9)  If  you do not agree with these terms and conditions, you do
               not  have  permission from  the  copyright holder(s)  to use
               SCREDIT, and you must stop using  it and remove it from your
               computer.

          (10) You may not reverse-engineer, disassemble, modify, decompile
               or create derivative works of the product.   You acknowledge
               that  the  product   includes  certain  trade   secrets  and
               confidential information, all  of which  is the  copyrighted
               intellectual property of Tim Underwood.

          (11) Any  use  or  distribution of  SCREDIT  which  violates this
               license agreement will be considered a copyright  violation,
               and prosecuted to the full extend of the law.



















     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      v






          Technical Support

          Technical support for  SCREDIT is  available to registered  users
          ONLY!   If you are not a registered user, limited assistance will
          be  provided to help you get SCREDIT  installed if you contact me
          via electronic mail (see below).

          If you  are a registered user, you  can contact Tim Underwood for
          support at the following electronic addresses:

               Compuserve:
                    Easyplex to 73577,1554

               The Source Connection BBS:
                    (316)-687-0012  24hrs  300/1200  8N1
                    Leave a message to  Tim Underwood, or a comment  to the
                    'SYSOP'.

          Or via U.S. Mail at:

               Tim Underwood
               1719 S. Shiloh
               Wichita, KS.  67207

          Support via electronic mail  is strongly preferred, as  it allows
          correspondence at convenient  times regardless of time  zones and
          work schedules, and it provides a record of the communication.

























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     vi






          Installation

          SCREDIT  is  written for  the  IBM  PC, PC/XT,  PC/AT,  PS/2 (all
          models), and compatibles.  It requires  MS-DOS 2 or above (MS-DOS
          3 or  above is recommended),  and uses a  total of about  150K of
          memory.  Libraries are provided for TurboC 2.0.

          The following files are included on your distribution disk:

          SCREDIT.EXE    Screen Object file maintenance program.

          SCRDEMOS.LIB   Small  model library  of routines  for TurboC  2.0
                         (non-registered version only).

          SCRDEMOL.LIB   Large  model library  of routines  for  TurboC 2.0
                         (non-registered version only).

          SCRDEMO.H      Header file for SCREDIT  functions (non-registered
                         version only).

          GETKEY.H       Header  file  for  keyboard  input  functions  and
                         return codes.

          CURSOR.H       Header file for cursor functions.

          *MATHSTBS.OBJ  Small model  object to  'stub' out  floating point
                         routines called in the registered version.  May be
                         used when you do not desire to use floating point.

          *MATHSBTL.OBJ  Large  model object to  'stub' out  floating point
                         routines called in the registered version.  May be
                         used when you do not desire to use floating point.

          *SCREDITS.LIB  Small model  library of  routines  for TurboC  2.0
                         (registered version only).

          *SCREDITL.LIB  Large model  library  of routines  for TurboC  2.0
                         (registered version only).

          *SCRWIN.H      Header  file  for windowing  functions (registered
                         version only).

          *SCREDIT.H          Header file for SCREDIT functions (registered
                              version only).

          * These files  are included only  with the registered version  of
          SCREDIT.





     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      1






          Installing the Program

          You  should  make sure  that  you  have BUFFERS  command  in your
          CONFIG.SYS file set to 20 or above.

          To  do  this, edit  your CONFIG.SYS  file  and add  the following
          command:

               BUFFERS=20

          If you wish  to access SCREDIT from any place in your system, you
          should install it in  a directory that is currently in  your PATH
          environment variable, or the directory  that SCREDIT is installed
          in should be added to your PATH statement.  The libraries  should
          be accessible by TLINK.EXE  for linking into your programs.   The
          header files should be accessible by either TC.EXE or TCC.EXE for
          compiling your programs.



































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      2






          Configuring SCREDIT

          You may configure  SCREDIT by typing  in 'SCREDIT', after it  has
          been installed.   On the unregistered  version, press any key  to
          remove the initial title screen.

          Context sensitive help is available at  all points in the system.
          To get help, press the 'F1' key, and press 'ESC' to exit help.

          Select the 'Options'  option from the menu  bar by typing  'O' or
          moving the cursor to 'Options' and pressing ENTER.

          You  may now  set  the  default  directory, file  extension,  and
          printer  information.    The  information  is  saved  within  the
          SCREDIT.EXE file itself.





































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      3






          Compatibility Notes

          SCREDIT has been tested in  a variety of environments,  including
          8088, 8086, V20, 80286,  and 80386 processors.  SCREDIT  has been
          tested with a variety of monitors, including Monochrome, CGA, EGA
          and VGA.  It  has been tested with MS-DOS/PC-DOS 2.0 -  4.01.  If
          you find what appears to be a compatibility problem with SCREDIT,
          please contact Tim Underwood.  I will do my best to fix it, or if
          necessary I will refund your registration fee.

          SCREDIT.EXE reprograms the video parameters  to attain 26 or more
          lines of display for a status line, still allowing you to  use 25
          lines  to  create your  screens.   THE  LIBRARY FUNCTIONS  DO NOT
          REPROGRAM THE VIDEO PARAMETERS IN ANY WAY.

          CGA screens are reprogrammed to display 26 lines.
          EGA/VGA screens are reprogrammed to display 29 lines.

          Upon termination of SCREDIT, the display  will be returned to its
          normal video  status, and  the number  of lines  the display  was
          originally configured with prior to the execution of SCREDIT.































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      4






          Using SCREDIT

          This section briefly reviews SCREDIT  features, and provides some
          examples of how SCREDIT can help  you develop user interfaces for
          your programs.  It only covers a few of the many ways SCREDIT can
          be  used,  but  it  should  help  you start  thinking  about  the
          possibilities.

          Starting SCREDIT

          Start by typing  in 'SCREDIT'  and pressing ENTER.   General  key
          usage is as follows:

               To go back a level or abort an operation, press the ESC key.

               Menu  Selections  are  made through  either  'Bar'  menus or
               'Pulldown' menus.   You may  make your  selections on  these
               menus by either  pressing the first (highlighted)  letter of
               each option, or  by using the  cursor keys to highlight  the
               desired option and pressing ENTER.

               Context  sensitive  help  may be  obtained  at  any location
               throughout the system by pressing F1.

               For key usage during Editing/Creating a Screen Object, press
               F1 while editing.


























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      5






          SCREDIT Examples

          For examples on  using SCREDIT, refer  to the sample screens  and
          files.

               DISPLAY.C
               DISPLAY.H
               DISPLAY.SBJ    Examples  of  a  simple display-only  screen,
                              along with source and comments.

               INPUT.C
               INPUT.H
               INPUT.SBJ      Examples   of   a  user   interface,  showing
                              examples  of  input  fields, display  fields,
                              error messages, etc.

               WINDOW.C       Examples  of  windowing  interfaces,  showing
                              windows, bar-menus and pulldown menus.


































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      6






          Technical Information

          SCREDIT was developed using  TurboC 1.5 and  2.0.  In almost  all
          cases, functions  provided by  the  TC Libraries  has been  used.
          This  was  done to  simplify the  coding  and maintenance  of the
          product, as well as to help ensure that the code provided  was as
          compatible with TC  as possible,  as well as  small as  possible.
          (It should also  help in an  OS/2 or Windows compatible  compiler
          from Borland).

          Several  other  packages  will  replace  nearly  every   function
          available  within  a  compiler  with their  own  inventions.   As
          SCREDIT is not  intended at this  stage to go  beyond the IBM  PC
          compatible arena, I have  not considered this to be  important at
          this time.

          MATHSTB?.OBJ  objects  have  been   provided  in  the  registered
          version.  This is to stub out floating point routines used within
          the SCREDIT libraries  to implement floating point numbers.  (See
          the  compiler manual regarding compiling without floating point).
          This does mean, of course, that floating point numbers may not be
          displayed  or  input using  SCREDIT  if these  objects  have been
          linked in with your  .EXE.  If you inadvertently call  a floating
          point  routine and  these objects  are linked,  the program  will
          terminate with an error message indicating  that a floating point
          routine has been called, and is not supported.

          It  is  suggested  that  SCREDIT?.LIB  be  listed  first  in  the
          libraries to be  used for linking.   This should be done  in case
          you are using a linker that will not search through the libraries
          for unresolved externals.

          CARE  SHOULD  BE TAKEN  in attempting  to  use SCREDIT  in TSR's.
          SCREDIT itself should be completely compatible in TSR's, although
          not all of the functions provided in the TC libraries are able to
          be used in certain situations within TSR's.

          In replacing any of the TC library routines, you should implement
          all of the functionality that the  original routine had.  SCREDIT
          does  not  take  advantage  of  certain  quirks  of  the  library
          routines,  such  as  scrolling  within  the  active  window  when
          printing  in the  last  character position  using  cprintf.   The
          original functionality of the function must be maintained.









     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      7






          Keyboard Actions within SCREDIT

          Once  the  function edit_input_fields  has  been called,  it will                              _________________
          process the following keystrokes:

          Up Arrow       -  positions  the cursor  in  the first  character
                         position of the previous field.
          Down Arrow     - acts as a 'field exit' and positions  the cursor
                         in the first character of the next field.
          Left Arrow     -  moves the cursor left  one space, if the cursor
                         is on the first character position of a field, the
                         cursor will  go  to the  previous field.   If  the
                         field is an  OPTION field,  then this will  scroll
                         through  the  selections  available   within  this
                         field.
          Space Bar      -  if  the  current  field  is  an  OPTION  field,
                         pressing the  Space Bar will  act the same  as thr
                         Right Arrow  key in  an OPTION field.   Any  other
                         field simply generates a space.
          Right Arrow    - moves the cursor right  one space, if the cursor
                         is on the last character position of  a field, the
                         cursor will go to the next field.  If the field is
                         an OPTION field, then this will scroll through the
                         selections available within this field.
          Home           - moves the  cursor to the  first position of  the
                         first field on the screen.
          End            - moves the cursor to the first blank character at
                         the end of the current field.
          Backspace      -  if the  cursor is  not in  the first  character
                         position of a field, deletes  the character to the
                         left of  the cursor and moves the  cursor left one
                         space.
          Insert         - toggles insert mode.
          Delete         - deletes the  character above the  cursor, moving
                         all characters right of the cursor position to the
                         left one space.
          Tab            - acts as a 'field exit' to go to the next field.
          BackTab        - acts as  a 'field  exit' to go  to the  previous
                         field.
          Ctrl-Enter     -  clears  the  field   from  the  current  cursor
                         position to  the end of  the field, and  exits the
                         field to go to the next field.
          Esc            - exit the editing  process, all fields are  in an
                         indeterminate state.

          All other function keys (F1-F12, Ctrl, Alt, and Shift), the Enter
          key, and Paging keys will exit the editing process and return  to
          the  caller, with  the key used  to exit the  editing process, as
          well as the field at which the editing process was terminated.



     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      8






          Function Definitions

          The following pages describe the available functions in SCREDIT.

          Functions beginning with  '[*]' are  available in the  Registered
          Version of SCREDIT ONLY.














































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                      9







          [*]abort_screen


          Function       Defines the  function address of  the abort_screen
                         call.

          Syntax         extern void (*abort_screen)(int err);

          Prototype in   scredit.h

          Remarks        This  function  address is  pre-initialized  to an
                         internal  routine   that  is  called   whenever  a
                         critical  screen error  occurs.   This  routine is
                         called under the following conditions:

                         1    -   During  a   call  to   disp_prompts,  and
                              disp_prompts detects an invalid  screen.  The
                              abort_screen function is called with an error
                              of 1.

                         2    -  During  a  call  to  undisp_prompts,   and
                              undisp_prompts  detects  an  invalid  screen.
                              The abort  screen function is  called with an
                              error of 1.

                         3    - During a call to edit_input_fields, and the
                              offset passed  is not  an input  field.   The
                              abort screen function is called with an error
                              of 1.

                         4    - During a call to edit_input_fields, and the
                              offset  passed is  beyond the logical  end of
                              all  fields  within the  screen.    The abort
                              screen function is called with an error of 1.

                         5    - During  a call  to edit_input_fields,  when
                              the cursor is being moved  to the next field,
                              and it is  found to be beyond the logical end
                              of all fields  within the screen.   The abort
                              screen function is called with an error of 1.

                         The default  function pointed  to by  abort_screen
                         simply waits  for a  keystroke and  terminates the
                         program.


          Return value   void




     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     10






          See also       disp_prompts  (Pg  20),  undisp_prompts  (Pg  56),
                         edit_input_fields (Pg 23)

          Example        void (*abort_screen)(int err);

                         To call the  abort_screen function yourself, issue
                         the command:
                         (*abort_screen)(1);

                         To  replace the  abort_screen with  a function  of
                         your own, create a function  with the same calling
                         sequence as  the abort_screen definition,  and set
                         this address to the address  of your new function,
                         as follows:

                         extern void (*abort_screen)(int err);

                         void my_abort(int err)
                         {
                              switch(err) {
                                case 1: /* do error function 1 */
                                        break;
                                case 2: /* do error function 2 */
                                        break;
                                case 3: /* do error function 3 */
                                        break;
                                }
                         }

                         void main(void)
                         {
                              abort_screen = my_abort;
                         }



















     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     11







          attr


          Function       Creates a text foreground/background attribute

          Syntax         #define attr(fore,back) ((((back) << 4) | (fore)))

          Prototype in   scrwin.h

          Remarks        attr  is a  macro to  create foreground/background
                         attributes.   The color definitions in conio.h may
                         be used.

          Return value   A char or int value with the created attribute.

          See also       background (Pg 13), foreground (Pg 29)

          Example        #include  "conio.h"
                         #include  "scrwin.h"

                         int  c;

                         c = attr(BLUE, LIGHTGRAY);    /*     returns    an
                                                       attribute   with   a
                                                       BLUE  foreground and
                                                       a          LIGHTGRAY
                                                       background */
























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     12







          background


          Function       Returns the background color of an attribute.

          Syntax         #define  background(a)  (((a) & 0xF0) >> 4)

          Prototype in   scrwin.h

          Remarks        background  is a macro which will return a char or
                         int  value  of  the  background  color of  a  text
                         attribute.

          Return value   The background attribute color.

          See also       attr (Pg 12), foreground (Pg 29)

          Example        #include  "conio.h"
                         #include  "scrwin.h"

                         char      c;

                         c = background(attr(BLUE,LIGHTGRAY));   /* Returns
                                                                 LIGHTGRAY
                                                                 */


























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     13







          [*]bad_amount


          Function       Defines  the  default error  message  when a  user
                         enters  an  invalid numeric  amount  in  a numeric
                         field.

          Syntax         extern char *bad_amount;

          Prototype in   scredit.h

          Remarks        The  default  message is  "Invalid Amount".   This
                         message  may  be  changed by  the  program.   This
                         message will  appear anytime  the cursor  is in  a
                         Numeric field, and the user enters an amount which
                         cannot be converted from ASCII to numeric.

          Return value

          See also

          Example        extern char *bad_amount;
                         char *new_message={"Enter a Correct Number"};

                         bad_amount = new_message;


























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     14








          [*]bad_date


          Function       Defines  the default  error  message  when a  user
                         enters an invalid date amount in a date field.

          Syntax         extern char *bad_date;

          Prototype in   scredit.h

          Remarks        The  default  message  is "Invalid  Date".    This
                         message  may  be  changed by  the  program.   This
                         message will  appear anytime  the cursor  is in  a
                         Date  field,  and the  user  enters an  date which
                         cannot be decoded.

          Return value

          See also

          Example        extern char *bad_date;
                         char *new_message={"Enter a Valid Date"};

                         bad_date = new_message;


























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     15








          [*]bad_entry


          Function       Defines  the default  error  message  when a  user
                         enters something  in a field,  and SCREDIT  cannot
                         decode it properly.

          Syntax         extern char *bad_entry;

          Prototype in   scredit.h

          Remarks        The  default message  is  "Invalid Entry".    This
                         message  may  be  changed by  the  program.   This
                         message will  appear anytime  the cursor  is in  a
                         Date field,  and the  user enters  somehting in  a
                         field which SCREDIT cannot decode properly.

          Return value

          See also

          Example        extern char *bad_entry;
                         char *new_message={"Error Intrepreting Entry"};

                         bad_entry = new_message;

























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     16








          blank_status


          Function       Blanks the status line with the default colors

          Syntax         void blank_status(void)

          Prototype in   scredit.h

          Remarks        Blanks the  status  line with  the default  status
                         line attribute.

          Return value   void

          See also       stat_attrib   (Pg   53),   save_status   (Pg  51),
                         restore_status (Pg 50), note  (Pg 44), errmsg  (Pg
                         27)

          Example        void foo(void)      /*  Yes, you knew  'foo' would
                                             appear somewhere */
                         {
                              save_status();
                              blank_status();
                              .
                              .
                              .
                              restore_status();
                         }






















     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     17







          [*]decimal_char


          Function       Defines the default decimal symbol

          Syntax         extern char decimal_char;

          Prototype in   scredit.h

          Remarks        Defaults to '.'.  May be changed by the program.

          Return value

          See also

          Example        extern char decimal_char;

                         decimal_char = ','  /* decimal char is now a comma
                         */
































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     18







          disp_io_fields


          Function       Displays and converts  all the data in  I/O fields
                         in a screen.

          Syntax         void disp_io_fields(void far(*scrnptr)(), void
                         *struc_buf);

          Prototype in   scredit.h

          Remarks        This  call  will  display all  of  the  I/O fields
                         within the screen.  It  is automatically called by
                         edit_input_fields,  so  a  seperate  call to  this
                         routine is not necessary unless you simply wish to
                         display the data, or all of the I/O  fields on the
                         screen are display only.

          Return value   void

          See also       edit_input_fields (Pg 23)

          Example        struct sc_screendata {
                              char      name[31];
                              char      address1[31];
                              char      address2[31];
                              char      city[31];
                              char      state[3];
                              };

                         extern void sc_screen_inp(void);
                         extern void sc_screen_pmt(void);

                         void main(void)
                         {
                              struct sc_screendata  scr;

                              disp_prompts(sc_screen_pmt);
                              disp_io_fields(sc_screen_inp, &scr);
                              .
                              .
                              .
                              .
                              undisp_prompts(sc_screen_pmt);
                         }






     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     19







          disp_prompts


          Function       Displays static screen data

          Syntax         void disp_prompts(void far (*scrnptr)());

          Prototype in   scredit.h

          Remarks        This call displays  the static screen data.   Each
                         screen,  regardless of size, is really a 'window'.
                         The  window   is  created,  and   all  information
                         underneath   the   screen    is   saved.      When
                         undisp_prompts  is  called,  this   data  will  be
                         restored.  Any errors encountered during this call
                         will  display  an  error  message  and  will  call
                         abort_screen.

          Return value   void

          See also       undisp_prompts (Pg 56), abort_screen (Pg 10)

          Example        extern void sc_screen_pmt (void);

                         void main(void)
                         {
                              disp_prompts(sc_screen_pmt);
                              .
                              .
                              .
                              .
                              undisp_prompts(sc_screen_pmt);
                         }


















     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     20







          [*]display_status


          Function       Defines whether  or not  a status  line should  be
                         displayed.

          Syntax         extern char display_status;

          Prototype in   scredit.h

          Remarks        The  default  is  FALSE, no  status  line  will be
                         displayed.    By  setting this  value  to  TRUE, a
                         status  line   will  be   displayed.    Any   text
                         underneath a status line is always saved, and will
                         be restored.

          Return value

          See also       stat_attrib (Pg 53)

          Example        extern char display_status;

                         display_status = TRUE;




























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     21







          [*]drcr_symbol


          Function       Defines the default Debit/Credit symbol

          Syntax         extern char *drcr_symbol;

          Prototype in   scredit.h

          Remarks        The  default DR/CR symbol is "<>".   This is a two
                         character string.   When reassigning it,  only the
                         first two characters  of the string will  be used.
                         The first character is the  character that will be
                         displayed to the  left of  the number, the  second
                         character is the character  that will be displayed
                         to the  right of the  number.  If  a numeric field
                         uses this field  attribute, these characters  will
                         replace the negative sign in any numeric numbers.

          Return value

          See also

          Example        extern char *drcr_symbol;
                         char        *new_values={"[]"};

                         drcr_symbol = new_values;
























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     22







          edit_input_fields


          Function       Enters the screen to allow data entry

          Syntax         int edit_input_fields(void far (*flds)(), void
                         *struc_buf, void far **offset);

          Prototype in   scredit.h

          Remarks        Allows user entry of the data within the screen.

                         flds is the pointer to the screen,  defined in the
                         header file for the screen.

                         struc_buf is the address of the data structure.

                         offset  is  the  address of  a  data  pointer that
                         points  to the address of an input field where you
                         wish data entry to begin.

          Return value   int - The key the user pressed to exit the screen.
                         Possible exit  keys are: ENTER,  ESC, all Function
                         keys, PGUP, PGDN, etc.

                         offset is returned  with the address of  the field
                         that was active when the exit occurred.   This may
                         be used to  determine which field the user  was in
                         when a function key, etc., was pressed.

          See also       disp_io_fields (Pg 19)

          Example        extern void sc_screen_pmt(void);
                         extern void sc_screen_inp(void);

                         struct sc_screen {
                              int       customer_nbr;
                              char      name[31];
                              char      address1[31];
                              char      address2[31];
                              char                              long      balance;
                              };

                         void main(void)
                         {
                              struct sc_screen scr;
                              void far         *offset;
                              int              ret, exit;



     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     23






                              disp_prompts(sc_screen_pmt);

                              /* skip customer_nbr as it  is a display only
                              field */
                              offset = &scr.name;
                              do {
                                exit = FALSE;
                                ret    =   edit_input_fields(sc_screen_inp,
                              &scr,        &offset);
                                switch(ret) {
                                   case F1    :
                                        display_help_screen();
                                        continue;
                                   case PGDN  :
                                        display_page_two();
                                        continue;

                                   /* now do some testing of fields */
                                   case ENTER :

                                     if (scr.balance < 0L) {
                                        errmsg("Balance  must  be   greater
                                        than 0.00");
                                        /* place cursor in balance field */
                                        offset = &scr.balance;
                                        continue;      /* continue loop */
                                        }

                                   /* if all is OK,  then let fall into ESC
                                   case so that screen will be  cleared and
                                   exit will be set to drop out of loop */
                                   case ESC :
                                        undisp_prompts(sc_screen_pmt);
                                        exit = TRUE;
                                        break;
                                   }
                                } while (!exit);
                         }














     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     24







          [*]err_attrib


          Function       Defines the  default text  attribute  of an  error
                         message on the status line.

          Syntax         extern char err_attrib;

          Prototype in   scredit.h

          Remarks        The default attribute  of an error message  is RED
                         on LIGHTGRAY.   This value  may be changed  by the
                         program.

          Return value

          See also       errmsg (Pg 27)

          Example        extern char err_attrib;

                         /* error message is now YELLOW on BLACK */
                         err_attrib = attr(YELLOW,BLACK);





























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     25







          [*]err_column


          Function       Defines the default column of  an error message on
                         the status line.

          Syntax         extern char err_column;

          Prototype in   scredit.h

          Remarks        The default  value is  16.   errmsg and note  will
                         start  their  messages in  this column.   Messages
                         that are too long will be truncated.

          Return value

          See also       status_row (Pg 54), errmsg (Pg 27), note (Pg 44)

          Example        extern char err_column;

                         /* messages will start at column 1 */
                         err_column = 1;





























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     26







          errmsg


          Function       Displays an error message on the status line.

          Syntax         void errmsg(char *msg);

          Prototype in   scredit.h

          Remarks        Displays an error message on the status line using
                         the err_attrib text attribute.

          Return value   void

          See also       err_attrib (Pg 25), note (Pg 44), blank_status (Pg
                         14), save_status (Pg 51), restore_status (Pg 50)

          Example        int funcx(void)
                         {
                              /* Please tone down error messages */
                              errmsg("PRESS THE RIGHT KEY DUMMY!!");
                         }

                         void funcy(int value, char *buf)
                         {
                              char      msg[80];

                              sprintf(msg,  "%s is  at %d%  over capacity",
                              buf, value);
                              errmsg(msg);
                         }




















     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     27







          [*]error_window


          Function       Displays an error message window

          Syntax         void error_window(char *msg);

          Prototype in   scrwin.h

          Remarks        Displays an error window, with  the message, and a
                         prompt  for the user to press  the ESC key to exit
                         the error window.

          Return value   void

          See also

          Example        error_window("Must enter 'Y' or 'N');

































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     28







          foreground


          Function       Returns the foreground color of an attribute

          Syntax         #define foreground(a)  ((a) & 0x0F)

          Prototype in   scrwin.h

          Remarks        foreground  is a macro which will return a char or
                         int value corresponding to the foreground color of
                         a text attribute.

          Return value   The foreground attribute color.

          See also       attr (Pg 12), background (Pg 13)

          Example        #include  "conio.h"
                         #include  "scrwin.h"

                         char      c;

                         /* Returns RED */
                         c = foreground(attr(RED,LIGHTGRAY));



























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     29







          get_cursor_type


          Function       Returns the current cursor type

          Syntax         unsigned int get_cursor_type(void);

          Prototype in   cursor.h

          Remarks        Returns the current cursor shape.

          Return value   unsigned int corresponding to the current cursor.

          See also       setcursor (Pg 52)

          Example        {
                              unsigned int   old_cursor;

                              old_cursor = get_cursor_type();

                         }






























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     30







          getkey


          Function       Keyboard interface, using BIOS services

          Syntax         int getkey(int type);

          Prototype in   getkey.h

          Remarks        Gets a keystroke from BIOS.

                         type may be one of the following:

                         0    - wait for keystroke.   The keystroke will be
                              returned as  an integer.   If  the  key is  a
                              character between 0 and 255,  then 0 thru 255
                              will be returned.  All  other key returns are
                              defined in getkey.h

                         1    - test for keystroke availability.  Returns 0
                              if   no  keystroke  is  available,  otherwise
                              returns the keystroke.  The keystroke is left
                              in the keyboard buffer.

                         2    - get current shift flags.

          Return value   int

          See also

          Example        {
                              int  key;

                              key = getkey(0); /* wait for keystroke */
                         }
















     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     31







          make_bar_menu


          Function       Creates a bar menu

          Syntax         int make_bar_menu(POPBAR far *bar_buf);

          Prototype in   scrwin.h

          Remarks        make_bar_menu creates a bar-type menu  on row 1 of
                         the  screen.  It allows  the use of both 'hotkeys'
                         as  well  as arrow  keys  in conjunction  with the
                         ENTER key.

                         bar_buf  is the  address  of  a POPBAR  structure.
                         Before  the  first  call  to  make_bar_menu,  this
                         structure should be initialized as follows:

                         init indicates whether or not  the window has been
                         initialized.   Before  calling  make_bar_menu,  it
                         should be set to UNINIT.

                         attrib is the  foreground/background color of  the
                         entire bar.

                         norm_attrib  is the foreground/background color of
                         each selection on the bar menu.

                         hilit_attrib is the foreground/background color of
                         a hilited selection.

                         lnorm_attrib is  the normal  foreground/background
                         color of the 'hot' letter of the selection.

                         lhilit_attrib  is the foreground/background of the
                         'hot' letter when  it is  in a hilited  selection.
                         'Hot'  letters  are  the  first  letter  of   each
                         selection passed in **selections.

                         hotactive indicates  whether or not  'hotkeys' are
                         active.  If set to TRUE, 'hotkeys' will be active,
                         if FALSE, 'hotkeys' will not be active.  'Hotkeys'
                         allow  selection  of  a  menu  item  by  the  user
                         pressing the corresponding letter for a menu item.
                         This will be matched  against the internally built
                         'hot' letters.

                         **selections is a  pointer to  an array of  string
                         pointers.  The  array member after the  last valid


     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     32






                         selection must be  NULL.  The 'hotkeys'  are built
                         from  the  first  UPPERCASE  letter  within   each
                         selection.

                         You  do  not  have to  remove  the  bar  menu when
                         executing  the  function   a  user  has  selected.
                         make_bar_menu, if called again,  will already know
                         that a  bar menu exists,  and will not  create one
                         again.

          Return value   -1  indicates  that the  window  for the  bar menu
                         could not be created.  ESC (defined in 'getkey.h')
                         will be returned  if the  user pressed the  Escape
                         key to  exit the bar menu.  A return code of 0 - n
                         indicates   the   selection    the   user    made,
                         corresponding to the selection they made.

          See also       remove_bar_menu (Pg 46)

          Example        **selections may be built in one of two ways:

                         {
                         char      *selections[]={"A", "B", "C",  "D", "E",
                                   ""};  /* note that a NULL string follows
                                   the last valid selection */
                         }

                         or:

                         {
                         char      *selections[10];
                         int       x;

                         setmem(selections, sizeof(selections), 0);
                         for (x = 0; x < num_strings; x++)
                           selections[x] = &string;
                         }

                         {
                              POPBAR    x;
                              int       ret;

                              x.init = UNINIT;
                              x.attrib = attr(BLACK, CYAN);
                              x.norm_attrib = attr(BLACK,CYAN);
                              x.hilit_attrib = attr(BLACK,LIGHTGRAY);
                              x.lnorm_attrib = attr(RED,CYAN);
                              x.lhilit_attrib = attr(RED,LIGHTGRAY);
                              x.hot_active = TRUE;
                              x.selections = menu;
                              do {

     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     33






                                   ret = make_bar_menu(&x);

                                   switch(ret) {
                                     case  -1    :  return;   /*  an  error
                                   occured */
                                     case ESC : remove_bar_menu(&x);
                                                return;
                                     case 0   : /* user selected "A" */
                                                break;
                                     case 1   : /* user selected "B" */
                                                break;
                                     case 2   : /* user selected "C" */
                                                break;
                                     case 3   : /* user selected "D" */
                                                break;
                                     case 4   : /* user selected "E" */
                                                break;
                                     }  /* end of switch */
                              } while (ret != ESC);
                         }
































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     34







          make_pulldown_menu


          Function       Creates a pulldown-type menu window

          Syntax         int make_pulldown_menu(PULLDOWN far *pull);

          Prototype in   scrwin.h

          Remarks        make_pulldown_menu creates a pulldown-type menu on
                         a  selected  row and  column  of the  screen.   It
                         allows the use of both  'hotkeys' as well as arrow
                         keys in conjunction with the  ENTER key.  It  also
                         optionally  allows  the  use  of an  'enumeration'
                         function that allows selections  to be selected by
                         a number.

                         pull is  the  address  of  a  PULLDOWN  structure.
                         Before the first  call to make_pulldown_menu, this
                         structure should be initialized as follows:

                         init indicates whether or not  the window has been
                         initialized.   Before  calling  make_bar_menu,  it
                         should be set to UNINIT.

                         row  is the row desired for  display, it must be 2
                         or greater.

                         col is the column desired for the display.

                         attrib is  the foreground/background color  of the
                         entire pulldown menu.

                         norm_attrib  is the foreground/background color of
                         each selection on the pulldown menu.

                         hilit_attrib is the foreground/background color of
                         a hilited selection.

                         lnorm_attrib is  the normal  foreground/background
                         color of the 'hot' letter of the selection.

                         lhilit_attrib  is the foreground/background of the
                         'hot' letter when  it is  in a hilited  selection.
                         'Hot'  letters  are  the   first  letter  of  each
                         selection passed in **selections.

                         bdr_type  selects   the   border   type   desired:
                         No_Border, Single_Border, Double_Border.


     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     35







                         enumerate is a value indicating whether selections
                         should be enumerated.  No_Enumerate indicates that
                         enumeration should not  be used.   Enum_0_Relative
                         indicates  that enumeration  should  be used,  the
                         first    selection    being    0,     then    1-9.
                         Enum_1_Relative indicates that  enumeration should
                         be used,  the first selections being 1-9, followed
                         by 0.

                         passkey is a  boolean type.   If set to TRUE,  the
                         users keystrokes  will be normally  processed, and
                         after  the  processing occurs,  the  key the  user
                         pressed  will  be  returned  back to  the  calling
                         function.  This  allows action  upon keys such  as
                         F1-F10, PGUP, PGDN, etc.

                         hotactive indicates  whether or not  'hotkeys' are
                         active.  If set to TRUE, 'hotkeys' will be active,
                         if FALSE, 'hotkeys' will not be active.  'Hotkeys'
                         allow  selection  of  a  menu  item  by  the  user
                         pressing the corresponding letter for a menu item.
                         This will be matched against the  internally built
                         'hot' letters.

                         title is a string indicating what the title of the
                         pulldown menu should be.  Strings may be passed in
                         the calling  sequence.   To prevent  a title  from
                         being displayed, pass a NULL string ("").

                         **selections is a  pointer to  an array of  string
                         pointers.  The  array member after the  last valid
                         selection must  be NULL.   The  'hotkeys' will  be
                         built  from  the first  UPPERCASE  letter in  each
                         string.

                         You  do not have to  remove the pulldown menu when
                         executing  the  function  a  user  has   selected.
                         make_pulldown_menu, if called again,  will already
                         know that  a pulldown  menu exists,  and will  not
                         create one again.

          Return value   -3 will be  returned if  the row is  less than  2.
                         Pulldown menus may only be created on lines 2-n.

                         -3 will also  be returned if you have selected the
                         enumerate option, and have passed  in more than 10
                         selections.  -3 may also be returned  if the total
                         number of rows is greater than  25 rows, of if the
                         total number of columns is greater than 80.


     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     36






                         In any of the above cases, an error message window
                         will be displayed indicating what the error is.

                         -1  will  be  returned  if   there  was  an  error
                         allocating  memory   to  save   the  screen   text
                         underneath the  pulldown menu.    ESC (defined  in
                         'getkey.h') will be  returned if the user  pressed
                         the Escape key  to exit  the bar menu.   A  return
                         code of  0 -  n indicates the  selection the  user
                         made, corresponding to the selection they made.


          See also       remove_pulldown_menu (Pg 47)

          Example        **selections may be built in one of two ways:

                         char      *title = {"Test"};
                         {
                         char      *selections[]={"One",   "Two",  "tHree",
                                   "Four", "fIve", ""};
                                   /* note that  a NULL string follows  the
                                   last valid selection */
                         }

                         or:
                         {

                         char      *selections[10];
                         int       x;

                         setmem(selections, sizeof(selections), 0);
                         for (x = 0; x < num_strings; x++)
                           selections[x] = &string;
                         }

                         {
                              PULLDOWN  x;
                              int       ret;

                              x.init = UNINIT;
                              x.row = 2;
                              x.col = 2;
                              x.attrib = attr(BLACK,CYAN);
                              x.norm_attrib = attr(BLACK,CYAN);
                              x.hilit_attrib = attr(BLACK,LIGHTGRAY);
                              x.lnorm_attrib = attr(RED,CYAN);
                              x.lhilit_attrib = attr(RED,LIGHTGRAY);
                              x.bdr_type = Single_Border;
                              x.e_value = No_Enumerate;
                              x.passkey = FALSE;
                              x.hot_active = TRUE;

     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     37






                              x.title = title;
                              x.selections = selections;
                              do {
                                   ret = make_pulldown_menu(&x);

                                   switch(ret) {
                                     case -3  :
                                     case  -1    :  return;   /*  an  error
                                   occured */
                                     case ESC : remove_pulldown_menu(&x);
                                                return;
                                     case 0   : /* user selected "One" */
                                                break;
                                     case 1   : /* user selected "Two" */
                                                break;
                                     case 2   : /* user selected "tHree" */
                                                break;
                                     case 3   : /* user selected "Four" */
                                                break;
                                     case 4   : /* user selected "fIve" */
                                                break;
                                     }  /* end of switch */
                              } while (ret != ESC);
                         }




























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     38







          make_window


          Function       Creates a text window.

          Syntax         WINDO far *make_window(WINDO far *win_buf);

          Prototype in   scrwin.h

          Remarks        make_window creates  a text window on  the screen.
                         If the coordinates  are invalid, make_window  will
                         return NULL.

                         Before  calling  make_window,  the  window  buffer
                         should be initialized as follows:

                         init indicates whether or not  the window has been
                         initialized.   Before  calling  make_bar_menu,  it
                         should be set to UNINIT.

                         row  and  col  are  the  upper   left-hand  corner
                         coordinates fo the window.

                         num_cols and num_rows are  the number of printable
                         columns and rows the window should be built with.

                         txt_attr  is  the   default  foreground/background
                         color  of the window.  When the window is created,
                         the area will  be filled with  blanks set to  this
                         color attribute.   Any characters  printed in  the
                         window will have this attribute, unless changed.

                         bdr_attr is the foreground/background attribute of
                         the border.

                         bdr_type is  the type  of border  desired.   Valid
                         selections  are   No_Border,  Single_Border,   and
                         Double_Border.  If No_Border is selected, then the
                         entire window area  is available for display.   If
                         either Single_Border or Double_Border is selected,
                         the printable area  of the window will  be created
                         at  the coordinates specified,  for the  number of
                         rows and  columns specified.   For  example, if  a
                         window is created with No_Border at coordinates 1,
                         1, 25, 80, then the entire screen may  be used for
                         display.  If a window is created at coordinates 2,
                         2, 10, 40,  with either a Single or Double border,
                         then the border will  be displayed at  coordinates
                         1, 1,  11,  41, giving  you  the entire  area  you


     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     39






                         specified for display.  This  means that using the
                         function gotoxy(1,1)  will position the  cursor at
                         the upper-left hand corner of  the window, not the
                         border.

                         title is  an optional  title for  the window.  The
                         title will be centered  above the window.   If the
                         title string  is too long,  then no title  will be
                         displayed.  If you  do not wish to print  a title,
                         then a NULL string should be passed ("").

                         Any  text  underneath  the area  the  window  will
                         occupy,  will be saved within the WINDO structure,
                         and   will   be   automatically    restored   when
                         remove_window is called.

          Return Value   If   the  window   is  already   created,  or   is
                         successfully  creaated, a  pointer  to the  window
                         structure  will  be returned,  as  if it  had been
                         successfully created.  If make_window is unable to
                         allocate  an  area for  the  saved portion  of the
                         screen, NULL will be returned.

          See Also       remove_window (Pg 48)

          Example        {
                              WINDO     x;
                              int       ret;

                              x.init = UNINIT;
                              x.row = 2;
                              x.col = 2;
                              x.num_rows = 5;
                              x.num_cols = 20;
                              x.txt_attr = attr(BLACK,CYAN);
                              x.bdr_type = Single_Border;
                              x.bdr_attr = attr(BLACK,LIGHTGRAY);
                              strcpy(x.title, "Test Window");
                              if (make_window(&x) == NULL)
                                   return;

                              .
                              .
                              .
                              .
                              remove_window(&x);
                         }





     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     40







          [*]money_symbol


          Function       Defines the default monetary symbol

          Syntax         extern char money_symbol;

          Prototype in   scredit.h

          Remarks        Default monetary  symbol is  the dollar  sign '$'.
                         The default may be changed by the program.

          Return value

          See also

          Example        extern char money_symbol;

                         /* change to British pounds */
                         money_symbol = 156;































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     41







          [*]move_window


          Function       Moves the active window on the screen

          Syntax         void move_window(WINDO *win, int direction)

          Prototype in   scrwin.h

          Remarks        Allows movement of the window on the screen.  Text
                         is automatically  saved and  restored when  moving
                         the window.   The direction  should be one  of the
                         defined  values in  getkey.h, _LEFT,  _RIGHT, _UP,
                         _DOWN.   Movement is  automatically restricted  to
                         the physical size of the screen.

          Return value   void

          See also       move_windows (Pg 43)

          Example        move_window(&win,  _UP);  /*  moves window one row
                         up */





























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     42







          [*]move_windows


          Function       Defines whether or  not windows are allowed  to be
                         moved by the user.

          Syntax         extern char move_windows;

          Prototype in   scredit.h

          Remarks        The default value is FALSE.  Setting this value to
                         TRUE allows the user to move windows around on the
                         screen by  pressing the Scroll-Lock key, and using
                         the  cursor  keys to  move  the window.    Text is
                         automatically saved  and  restored.    The  window
                         position, once moved, is not remembered,  only the
                         original position  established by  the program  is
                         remembered.

          Return value

          See also       move_window (Pg 42)

          Example        extern char move_windows;

                         move_windows = TRUE;

























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     43







          note


          Function       Displays a 'note' message on the status line.

          Syntax         void note(char *msg);

          Prototype in   scredit.h

          Remarks        note displays a  message on the status  line using
                         the stat_attrib text attribute.

          Return value   void

          See also       stat_attrib  (Pg   53),   save_status   (Pg   51),
                         blank_status  (Pg  14),  restore_status  (Pg  50),
                         errmsg (Pg 27)

          Example        void x(void)
                         {
                              note("This   process  will   take   about  10
                              miniutes.");
                         }

                         void y(int time_value)
                         {
                              char      buf[80];

                              sprintf(buf, "This process will take about %d
                                minutes", time_value);
                              note(buf);
                         }



















     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     44







          [*]num_decimals


          Function       Default value  of  number  of  decimal  places  in
                         monetary field types.

          Syntax         extern char num_decimals;

          Prototype in   scredit.h

          Remarks        Defines  the default  number of decimal  places in
                         monetary field types.   The  default is 2  decimal
                         places.  May be changed by the program.

          Return value

          See also

          Example        extern char num_decimals;

                         num_decimals = 4;   /* all decimal  places are now
                         four */





























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     45







          remove_bar_menu


          Function       Removes a bar menu

          Syntax         void remove_bar_menu(&menu)

          Prototype in   scrwin.h

          Remarks        Removes the bar  menu, and restores any  text that
                         was previously underneath the bar menu.

          Return value   void

          See also       make_bar_menu (Pg 32)

          Example        #include  "scrwin.h"

                         POPBAR    menu={UNINIT};

                         {
                              ret = make_bar_menu(&menu, attr(BLACK,CYAN),
                              attr(BLACK,CYAN), attr(BLACK,LIGHTGRAY),
                              attr(RED,CYAN), attr(RED,LIGHTGRAY), TRUE,
                              selections);

                              remove_bar_menu(&menu);

                         }






















     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     46







          remove_pulldown_menu


          Function       Removes a pulldown menu

          Syntax         void remove_pulldown_menu(&pulldown);

          Prototype in   scrwin.h

          Remarks        Removes a  pulldown menu, and restores  the screen
                         text underneath the pulldown menu.

          Return value   void

          See also       make_pulldown_menu (Pg 35)

          Example        #include  "scrwin.h"

                         PULLDOWN  menu={UNINIT};

                         {
                              ret = make_pulldown_menu(&menu,
                              attr(BLACK,CYAN), attr(BLACK,CYAN),
                              attr(BLACK,LIGHTGRAY), attr(RED,CYAN),
                              attr(RED,LIGHTGRAY), Single_Border, FALSE,
                              TRUE, selections);

                              remove_pulldown_menu(&menu);

                         }





















     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     47







          remove_window


          Function       Removes a created window using make_window

          Syntax         void remove_window(&win);

          Prototype in   scrwin.h

          Remarks        remove_window will remove  the window specified in
                         the WINDO pointer.  All text underneath the window
                         will be  automatically  restored,  and  the  WINDO
                         structure will be reset to an UNINIT state.

          Return value   void

          See also       make_window (Pg 39)

          Example        #include  "scrwin.h"

                         WINDO     win={UNINIT};

                         {
                              make_window(1, 1, 25, 80, attr(WHITE,BLACK),
                              No_Border, attr(YELLOW,BLACK), "Window",
                              &win);

                              remove_window(&win);

                         }





















     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     48







          [*]req_error


          Function       Defines  the default  error  message for  required
                         entry fields.

          Syntax         extern char *rq_error;

          Prototype in   scredit.h

          Remarks        The default message is "Entry is required for this
                         field".   This message  will appear  in any  field
                         that requires a non-blank or non-zero value.

          Return value

          See also

          Example        extern char *rq_error;
                         char      *required={"Must not be blank or 0"};

                         rq_error = requried;





























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     49







          restore_status


          Function       Restores the saved text from the status line

          Syntax         void restore_status(void)

          Prototype in   scredit.h

          Remarks        Restores  text  previously  saved  by  a  call  to
                         save_status, to the status line area.

          Return value   void

          See also       save_status (Pg  51), blank_status  (Pg 14),  note
                         (Pg 44), errmsg (Pg 27)

          Example        int main(void)
                         {
                              save_status(); /* saves  data on status  line
                              */
                              .
                              .
                              .
                              .
                              restore_status();   /*  restores  data   from
                                                  save_status() */
                         }























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     50







          save_status


          Function       Saves the text underneath the status line.

          Syntax         void save_status(void);

          Prototype in   scredit.h

          Remarks        This  function  saves   the  text  and  attributes
                         underneath the status line, for later restoration.
                         The data is saved in a buffer internal to SCREDIT.

          Return value   void

          See also       restore_status (Pg 50), blank_status (Pg 14), note
                         (Pg 44), errmsg (Pg 27)

          Example        void save_status(void);

                         int my_func(void)
                         {
                              save_status();  /* save status line data */
                         }



























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     51







          setcursor


          Function       Sets the cursor type

          Syntax         void setcursor(unsigned int cursor_type);

          Prototype in   cursor.h

          Remarks        Sets the cursor on, off or to a block shape.

          Return value   void

          See also       get_cursor_type (Pg 30)

          Example        setcursor(blk_cursor); /*  sets  cursor  to  block
                         shape */


































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     52







          [*]stat_attrib


          Function       Defines the default  text attribute of  the status
                         line

          Syntax         extern char stat_attrib;

          Prototype in   scredit.h

          Remarks        The default attribute is BLUE  on LIGHTGRAY.  This
                         color may be changed by the program.

          Return value

          See also

          Example        extern char stat_attrib;

                         /* changes to BLACK on LIGHTGRAY */
                         stat_attrib = attr(BLACK,LIGHTGRAY);






























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     53







          [*]status_row


          Function       Defines the default row of the status line.

          Syntax         extern char status_row;

          Prototype in   scredit.h

          Remarks        The  default row  of the  status  line is  row 25.
                         This may be changed to any value 1-25.  The status
                         line uses an entire row.

          Return value

          See also       display_status (Pg 21), stat_attrib (Pg 53)

          Example        extern char status_row;

                         status_row =  1;  /* sets the status row on line 1
                         */






























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     54







          [*]tf_error


          Function       Defines  the default  message to be  displayed for
                         boolean TRUE/FALSE fields.

          Syntax         extern char *tf_error;

          Prototype in   scredit.h

          Remarks        The default message  is "Must  enter 'T' or  'F'".
                         This may be changed by  the program.  This message
                         is displayed anytime the cursor is in a TRUE/FALSE
                         boolean  field and the  user enters anything other
                         than 'T' or 'F'.

          Return value

          See also       yn_error (Pg 57), ynb_error (Pg 58), req_error (Pg
                         49)

          Example        extern char *tf_error;
                         char *new_message={"Enter (T)rue or (F)alse"};

                         tf_error = new_message;


























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     55







          undisp_prompts


          Function       Removes a screen, and restores screen underneath

          Syntax         void undisp_prompts(void far (*scrnptr)());

          Prototype in   scredit.h

          Remarks        Removes a  screen from  the display,  and restores
                         the saved screen data underneath the screen.

          Return value   void

          See also       disp_prompts (Pg 20)

          Example        extern void sc_screen_pmt (void);

                         void main(void)
                         {
                              disp_prompts(sc_screen_pmt);
                              .
                              .
                              .
                              .
                              undisp_prompts(sc_screen_pmt);
                         }
























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     56







          [*]yn_error


          Function       Defines the default  message for a  boolean YES/NO
                         field.

          Syntax         extern char *yn_error;

          Prototype in   scredit.h

          Remarks        The default message  is "Must  enter 'Y' or  'N'".
                         This may be changed by  the program.  This message
                         appears anytime the  user is  in a YES/NO  boolean
                         field and presses any other key than 'Y' or 'N'.

          Return value

          See also       ynb_error (Pg 58), tf_error (Pg 55), req_error (Pg
                         49)

          Example        extern char *yn_error;
                         char *new_error={"Press 'Y' or 'N'"};

                         yn_error = new_error;



























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     57







          [*]ynb_error


          Function       Defines   the   default   error  message   for   a
                         YES/NO/BLANK boolean field.

          Syntax         extern char *ynb_error;

          Prototype in   scredit.h

          Remarks        The  default message is "Must  enter 'Y' or 'N' or
                         Blank".    This  message  may  be changed  by  the
                         program.   This  message will  appear  anytime the
                         cursor is in  a YES/NO/BLANK input field,  and the
                         user presses  any other  key then  'Y',  'N' or  a
                         blank.

          Return value

          See also       yn_error (Pg 57)

          Example        extern char *ynb_error;
                         char *new_message={"Please press 'Y', 'N', or
                              leave Blank"};

                         ynb_error = new_message;

























     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     58






                                        Notes



















































     SCREDIT Function Reference Guide
     Copyright (c) 1987, 1988, 1989 by Tim Underwood                     59