NAME
                setdtr -- set state of data terminal ready flag
                setrts -- set state of ready to send flag

        SYNOPSIS
                void setdtr(port, mode);
                void setrts(port, mode);
                int port;        0, 1, 2, or 3 (for COM1-COM4)
                int mode;        TRUE to set flag, FALSE to clear flag


        DESCRIPTION
        These are assembly language functions which provide direct
        access to the serial communications chips for the fastest
        access possible.  Each function sets a particular
        communications output bit to the condition stated by "mode".
        The port parameter may be specified as integers 0-3, or
        SER1 to SER4 as defined in <smdefs.h>.



        EXAMPLE

            int sport;        /* serial port */

            sport = SER2;     /* let it point to COM2 */
            setdtr(sport, YES);  /* take the modem offhook */










        This function is found in SMTCx.LIB for the Turbo-C Compiler