Turbo C profiler (TCPROF version 1.5)
                        Copyright (C) 1988 Andre Nancoz
                              all rights reserved





                               Contents



          INTRODUCTION                                               1
             Overview  . . . . . . . . . . . . . . . . . . . . . . . 1
             History . . . . . . . . . . . . . . . . . . . . . . . . 1
             Copyright information . . . . . . . . . . . . . . . . . 1
             Trademark information . . . . . . . . . . . . . . . . . 1
             System requirements . . . . . . . . . . . . . . . . . . 2
             Compilation and execution requirements  . . . . . . . . 2
             Restrictions and caveats  . . . . . . . . . . . . . . . 2

          USING THE PROFILER                                         4
             Executing the profiler  . . . . . . . . . . . . . . . . 4
             Profiler options  . . . . . . . . . . . . . . . . . . . 4

          INPUT/OUTPUT                                               6
             File usage  . . . . . . . . . . . . . . . . . . . . . . 6
             Report content  . . . . . . . . . . . . . . . . . . . . 6

          MEMORY USAGE                                               9
             Lines within functions  . . . . . . . . . . . . . . . . 9
             Functions only  . . . . . . . . . . . . . . . . . . . . 9

          ERROR MESSAGES                                            10

          APPENDIX A                                                11
             LISTING 1..............................................11
             EXAMPLE 1..............................................12
             EXAMPLE 2..............................................13

          APPENDIX B                                                14
             Registered user information . . . . . . . . . . . . . .14
             Registered user features  . . . . . . . . . . . . . . .14

          APPENDIX C                                                17
             PROBLEM REPORT/SUGGESTIONS  . . . . . . . . . . . . . .17
             REGISTERED USER ORDER FORM  . . . . . . . . . . . . . .18






















                                       i




                             INTRODUCTION


     Overview

          TCPROF will show you where the most time is being spent in a
          program  written with Borlands' Turbo C.  The output report
          indicates the percentage of time (numerically and
          graphically) spent in each function and line of your program.
          Several options allow you to vary the amount of information
          shown on the report.  No changes to your source code are
          required in order to run the profiler.  The hardware timer is
          read but not modified.

          This program is distributed at no charge and is designed for
          users who have an occasional need or curiosity about the
          efficiency of their programs.  A registered user version of
          this program (TCPROFRU) is available which allows more
          extensive tailoring of the output and can reduce the amount
          of overhead and size of the report (See Appendix B for more
          information).


     History

          Version 1.0   First release.

          Version 1.5   Update for Turbo C release 2.0.  Timing logic
                        change to increase consistency.


     Copyright information

                Turbo C profiler program TCPROF and documentation
                       Copyright (C) 1988 by Andre Nancoz
                               all rights reserved

          The Turbo C profiler is not public domain software.  TCPROF
          and it's accompanying documentation may be distributed freely
          provided no fee is charged and it is not part of a package
          for which a charge is made.  Furthermore, the program and
          documentation must be distributed with no modifications.

          TCPROF is distributed as-is with no expressed or implied
          warranties.


     Trademark information

          Turbo C is a trademark of Borland International Inc.
          IBM-PC is a trademark of International Business Machines
          Corporation.
          MS-DOS is a trademark of Microsoft Corporation.








October 4, 1988                                                 INTRODUCTION - 1




     System requirements

          IBM-PC and true compatibles.
          MS-DOS version 3.0 or above.
          Minimum memory required is 39K above that required for the
          program being profiled.  Additional memory may be required
          depending on the program being profiled.  See the section on
          memory usage for more information.


     Compilation and execution requirements

          In order to run a program under the profiler the program must
          be compiled with, at least, the following options:

          TCC command line;
            -y generate line numbers in .obj file.
            -M full link map.

          TLINK command line;
            /m or /s to generate a link map.
            /l output line numbers in link map.

          Integrated Development Environment;
            O/C/Code generation/Line numbers..On
            O/L/Map file..Publics or Detailed

          NOTE:  Line numbers and map options are required even if the
          functions only option is used.

          When running the profiler the .EXE and the .MAP file must be
          available using the standard DOS search path, i.e. the
          current directory of the current drive is checked first.  If
          not found, each directory in the environment PATH is checked.


     Restrictions and caveats

          Timer
          If your program steals the timer interrupt it must chain to
          the previous owner of the interrupt.  The profiler does NOT
          modify the timer rate but does read the timer chip.  If your
          program modifies the timer rate the profiler may still
          operate correctly.

          Single Step and Interrupt 3
          If your program uses these, the profiler will not work
          correctly.  It may be reboot time.

          longjmp
          Likely to mess up timing.

          Static functions
          All line numbers for a function defined as static will be
          included with the last non-static function.  This will likely
          cause the warning message regarding inaccurate timing.  The
          profiler keeps track of entrances to and exits from




                                                                INTRODUCTION - 2




          functions.  Since static function addresses do not appear in
          the link map the profiler does not have an accurate
          indication of where the static function began or where the
          previous non-static function ended.

          Assembler
          Assembler modules should be assembled without the line number
          option(TASM /ZD).  The profilers' timing resolution cannot
          handle interrupts at each machine instruction.

          Unlike previous versions of Turbo C, version 2.0 passes the
          line number option on to TASM when inline assembler is used.
          When a single machine instruction is generated for a line of
          C source it is likely that they will be reported as 0% due to
          the profilers timing resolution.  Some functions such as
          enable(), disable(), etc. will cause the same problem.  Use
          of the emit() function to output one instruction per line
          will also cause the problem.

          If you are using previous versions of Turbo C, use of the asm
          keyword within a C module will cause no line numbers to be in
          the map, TCC invokes MASM without the line number option.
          Therefore, functions which contain the asm keyword should be
          compiled in a separate module from functions which you wish
          to time.

          TSRs
          I have tested the profiler with several TSRs with no
          problems.  The timing may be different for the same program
          depending on which TSRs are loaded.  Therefore, in order to
          compare results of two profiler runs, the same environment
          should be used for each run.  Of course activating a TSR
          during a profiler run would disturb the timing.

          Bugs
          This program is not a debugger and expects a reasonably
          behaved program.  The profiler may be useful in detecting
          some problems such as loops or functions executing the wrong
          number of times or not executing at all, etc.






















                                                                INTRODUCTION - 3




                          USING THE PROFILER


     Executing the profiler

          TCPROF [prof options] program-name [program-name options]
            The brackets [] denote optional information, they are
            not entered.

          If the program-name is not entered, help information is
          displayed.

          Program-name options are passed to program-name in the same
          manner as if the program was executed stand-alone.  The
          argv[0] parameter contains program-names' full path.  The
          profiler report is written to stdout, any redirection applies
          to both program-name and the profiler report.  The profiler
          uses stderr for error messages which cause it to abort the
          run, also for a few messages to the console when stdout is
          redirected.


     Profiler options

          Profiler options may be entered in upper or lower case.  The
          leading character may be either a - or a /.  All profiler
          options must precede the name of the program to be profiled.

          -F            Profile by function.  The default is a detailed
                        report by line number within function.  Using
                        this option creates an output report with only
                        one line per function and substantially reduces
                        the profiler overhead when your program is
                        running.


          -Cnn          Print only lines whose execution count is equal
                        to or greater than nn. The default value is 0.
                        This option only influences the amount of
                        report output.  The option has no effect if the
                        -F option is chosen.  The nn is interpreted as
                        an unsigned long integer.

          -Lnn          Number of lines per page.  The default is 25.
                        If nn is omitted, 0 or an invalid number, the
                        default is 58 (a good value for 8.5 inch
                        printed output).  This option does not change
                        the "pause between each page" output action,
                        which is controlled by whether or not stdout
                        has been redirected.

          -Snn          This option controls an internal memory
                        allocation parameter.  Entry to a function
                        requires a word on an internal stack, the word
                        is released at function exit.  The value
                        specified is the number of words to allocate.
                        The maximum is 32751 minus the number of




                                                          USING THE PROFILER - 4




                        functions profiled.  It should only be required
                        if your program uses recursion.   The default
                        value is 10.  If the warning message "Timing
                        may be inaccurate" occurs then this parameter
                        should be used.  It should be set to the
                        maximum level of recursions that can occur at
                        any one time.






















































                                                          USING THE PROFILER - 5




                             INPUT/OUTPUT


     File usage

          When the program to be profiled is run only the standard
          Turbo C start up files are open.  The spawn function passes
          these files to the program to be run.  The profiler uses
          stdout and stderr before and after running your program.  Any
          redirection applies to both the profiler and the program
          being profiled.  Delimiter lines are written by the profiler
          to stdout before and after running your program.

          Besides the program to be profiled, the .MAP file must be
          available for read only access, this file is not open while
          your program is running.  All file are located via the
          standard DOS path search.


     Report content

          The profile report is written to stdout with a default of 25
          lines to the page, the L option can be used to change the
          default.  If stdout has not been redirected the output will
          pause at the end of each page and you may either display the
          next page or cancel the remaining output, a clear screen is
          issued between each page.  When output has been redirected,
          no pause or clear screen occurs between pages.

          Appendix A contains a listing and two reports of a small test
          program.  The first report is by line number.  This report
          exhibits very high profiler overhead since majority of time
          is spent within loops which generate a small number of
          machine instructions per line of C code.  In more realistic
          programs overhead is in the 30% range.  The second report is
          the same program but it was run with the functions only
          option.

          Only functions which are compiled with the line number option
          "on" are shown on the report.  The time for functions
          compiled without line numbers are included in the lines of
          your program from where they are called.  As a consequence,
          all the time for the system run time library functions (such
          as printf) will be included in the lines from which they are
          called.  In the test program line 23 took 1 percent of the
          main functions' time, this includes the time it took to
          execute the printf function (with redirection to disk).  On
          the other hand, the time for line 19 only includes the time
          to call and return from test_func, since test_func line
          numbers are included in the map.

          The first page of output contains general information about
          the program being profiled.  In reality this may be many
          pages of output since it contains the stdout of the program
          being profiled.  The options section on this page shows all
          the profiler options which were in effect during this
          execution.




                                                                INPUT/OUTPUT - 6




          Prior to running your program, the .MAP file is analyzed and
          a table is built in memory.  After this is done the amount of
          memory available to run your program is printed.

          The "parameters" line contains the argv[0] to be passed to
          your program, subsequent line(s) contain argv[1] to argv[n]
          parameters each enclosed in quotes.  A line is then output to
          delimit the stdout of your program from that of the profiler,
          it contains the full path and name of the program to be
          executed.  If stdout has not been redirected the profiler
          will pause with a message allowing you to cancel execution or
          run the profile, optionally you may clear the screen prior to
          running your program.

          After returning from your program, a line is output giving
          the return code and the calculated time your program would
          have taken if the profiler had not been used.  This time is
          the basis for the percentage calculations made in the body of
          the report.  The next line contains the start date, time, end
          time and the percentage of the elapsed time spent within the
          profiler.

          The body of the report starts on the next page.  In Appendix
          A, example 1 is lines within functions, example 2 is a
          functions only report.

          Whenever a new module is encountered in the .MAP file a line
          is output with the module name.  When the beginning of a
          function is identified a line is output with the name, the
          percentage of time the function executed as compared to your
          programs total time from page 1 and a graphic representation
          of the percentage.  In addition, for a functions only report
          the count column contains the number of times the function
          was executed, for a lines within function report this count
          appears on the first line within the function.

          The line number report has additional information.  The first
          column contains the starting address of the line, the line
          number, the number of times the line was executed, the time
          taken by the line as a percentage of the programs' time, the
          time taken by the line as a percentage of the functions' time
          and a graphic representation of the percentages.

          Each column in the graph represents approximately 2.5%.  Four
          characters are used within the graph, asterisks, periods,
          equal signs and dashes.  The asterisks are used for function
          lines only, no other characters appear on these graph lines.
          Even though a report by lines is requested, if a function is
          not executed only the function line will appear on the
          report.  The period only appears in the first column of the
          graph, it is used when a line was executed at least once but
          the time was less than 2.5%.  The end of the equal signs
          represents the lines' time compared to the total time.  The
          end of the dashes represents the lines' time compared to the
          functions' time.






                                                                INPUT/OUTPUT - 7




          For the lines within functions report, the format of the
          source file can affect the report.  The listing in Appendix A
          contains some examples which will be referred to in the
          following discussion.  The source for lines 33 and 34, and
          line 39 are essentially the same and generate identical
          machine instructions.  On the other hand, the report is
          different for these two instruction sequences due to the map
          output.  The compiler generates the initialization code of
          the "for loop" and outputs the line address for the .MAP
          file.  Since the calculation is contained on the same line
          nothing is output to the .MAP file for it.  Therefore, line
          39 reports that the line was executed only once and all the
          time for the loop is included with line 39.  In the case of
          lines 33 and 34, the compiler outputs the line 33 address for
          the initialization code and the line 34 address for the
          calculation which shows 19999 executions of the expression.
          In version 2 of Turbo C other loop constructs (while, do) are
          now generated similarly, so that lines 21 and 37 are now
          reported in the same manner as line 39.

          All times for the last line of a function are reported with
          the line which called the function.  Therefore for best
          results, the closing bracket of a function should appear on a
          separate line.  The count for the last line of a function is
          correct.

          The difference in times between lines 21 and 39 indicate the
          efficiencies of register variables.  In the main function two
          dummy variables were allocated as registers so that the other
          variables, which are used in line 21, could not be
          automatically assigned by the compiler to registers.  In
          test_func the variables for the loop were allocated to
          registers.

          In version 2.0 of Turbo C the compiler outputs line numbers
          to the .MAP file for floating point instructions.  Therefore,
          these lines are now reported correctly.

          If you are using version 1.5 of Turbo C, lines 41 and 42
          exhibit a problem when using floating point.  If the first
          machine instruction to be generated on a line is for a
          floating point operation the compiler does not output a line
          number for the .MAP file.  Therefore, line 42 does not appear
          in the report and all the time for line 42 is reported in
          line 41.  If you need to see one or more floating point lines
          separately the only option would be to precede each statement
          with a non-floating point statement, such as an increment of
          a dummy integer variable (better yet, upgrade to version 2,
          it's worth it).
            Example:  dummy++; r = a * b;  /* on one line */











                                                                INPUT/OUTPUT - 8




                             MEMORY USAGE


     Lines within functions

          "Memory required" =
          16 * "number of lines mapped" +
          2  * ("number of functions within the line map" +
                "value of -S option") +
          13 * "number of modules within the line map" +
          "your program requirements" + 39k


     Functions only

          "Memory required" =
          16 * "number of functions within the line map" * 2 +
          2  * ("number of functions within the line map" +
                "value of -S option") +
          13 * "number of modules within the line map" +
          "your program requirements" + 39k








































                                                                MEMORY USAGE - 9




                            ERROR MESSAGES


          Return
          Code    Message

          35      DOS version must be 3.0 or later.

          36      Parameter invalid in response file.

          37      File not found (.exe and .map required).

          38      Invalid map file, no line numbers.
                  In the chapter "INTRODUCTION" see section "Compiler
                  and execution requirements".

          39      Insufficient memory.

          40      Logic.
                  This message is accompanied by other information.  If
                  it should occur please notify me, giving the full
                  message displayed, details of your system and compile
                  options used on the program being profiled.

          41      Not a Turbo C program.

          42      Invalid map file, no public values found.
                  Refer to the section "Compiler and execution
                  requirements".

          43      NOTE:  Timing inaccurate, see -S in documentation.
                  Refer to the section "Profiler options".

          44      NOTE:  Timing inaccurate, see caveats in
                  documentation.
                  See the discussion on static functions under
                  "Restrictions and caveats".

          99      Parameter display or error.

                  All return codes below 35 are identical to the errno
                  values used by Turbo C.



















                                                             ERROR MESSAGES - 10




                                   APPENDIX A


                             ---------------------------------
                                   LISTING 1
                             ---------------------------------

           1  #include <stdio.h>
           2  #include <stdlib.h>
           3
           4
           5
           6
           7  /*      Prototype Definitions      */
           8  void test_func(void);
           9  /* End Prototypes  */
          10
          11  #define LOOP_CNT 20000
          12
          13  main()
          14  {
          15  register int reg_si, reg_di; /* dummy variables to use up regs */
          16  int a = 10;
          17  int i = LOOP_CNT;
          18
          19    test_func();
          20
          21    while (--i) a = a * a / a;
          22
          23    printf("Proftest executed");
          24    return (0);
          25  }                  /*     end of main     */
          26
          27  void test_func(void)
          28  {
          29  register unsigned int i;
          30  register unsigned int a = 10;
          31  float b, c;
          32
          33    for (i = LOOP_CNT; --i;)
          34      a = a * a / a;
          35
          36    i = LOOP_CNT;
          37    while (--i) a = a * a / a;
          38
          39    for (i = LOOP_CNT; --i;) a = a * a / a;
          40
          41    for (i = 50, b = 10.0; i > 0; i--)
          42      c = b * b / b;
          43  }                /* end of test_func */











                                                                 APPENDIX A - 11




                            ----------------------------------
                                   EXAMPLE 1
                            ----------------------------------

                         Turbo C Profiler (TCPROF V1.5)                    1

PROFILER OPTIONS:
  Minimum line count printed(-C) 0:  Lines per page(-L) 58
  Internal stack size(-S) 10 default

Analyzing C:\C\PROFTEST.MAP
18 lines in 2 functions in 1 module will be profiled

Building profile table
Memory available 437432 bytes

Parameters:  C:\C\PROFTEST.EXE

***** STDOUT FOR C:\C\PROFTEST.EXE *****
Proftest executed

*** End of Program Output  Return code 0  Time mm:ss 0:03 ***
Start 9-25-1988 16:41:26.67  End 16:41:42.22  Profiler overhead 84%

   --------   Example 1 Page 1:   tcprof -L proftest >proftest.ex1   --------





PROFTEST.EXE             Turbo C Profiler (TCPROF V1.5)                    2
Func/Addr   Line   Count      %Tot %Fun...1...2...3...4...5...6...7...8...9...

MODULE PROFTEST

main                           36      ***************
0000:01FA   13     1            0    0 .
0000:0202   16     1            0    0 .
0000:0207   17     1            0    0 .
0000:020C   19     1            0    0 .
0000:020F   21     1           36   99 ==============--------------------------
0000:0229   23     1            0    1 .
0000:0232   24     1            0    0 .
0000:0236   25     1            0    0 .

test_func                      64      *************************
0000:023C   27     1            0    0 .
0000:0244   30     1            0    0 .
0000:0247   33     1            0    0 .
0000:024C   34     19999       21   33 ========-----
0000:025D   36     1            0    0 .
0000:0260   37     1           18   28 =======----
0000:0273   39     1           18   28 =======----
0000:0289   41     1            0    0 .
0000:0299   42     50           7   11 ===-
0000:02B6   44     1            0    0 .





                                                                 APPENDIX A - 12




*** End of profile report for C:\C\PROFTEST.EXE ***

   --------   Example 1 Page 2:   tcprof -L proftest >proftest.ex1   --------

                       ----------------------------------
                                   EXAMPLE 2
                       ----------------------------------

                         Turbo C Profiler (TCPROF V1.5)                    1

PROFILER OPTIONS:
  FUNCTIONS ONLY(-F):  Lines per page(-L) 58
  Internal stack size(-S) 10 default

Analyzing C:\C\PROFTEST.MAP
2 functions in 1 module will be profiled

Building profile table
Memory available 437656 bytes

Parameters:  C:\C\PROFTEST.EXE

***** STDOUT FOR C:\C\PROFTEST.EXE *****
Proftest executed

*** End of Program Output  Return code 0  Time mm:ss 0:03 ***
Start 9-25-1988 16:42:58.56  End 16:43:02.08  Profiler overhead 12%

   -------   Example 2 Page 1:   tcprof -L -F proftest >proftest.ex2  -------

PROFTEST.EXE             Turbo C Profiler (TCPROF V1.5)                    2
Func/Addr   Line   Count      %Tot %Fun...1...2...3...4...5...6...7...8...9...

MODULE PROFTEST

main               1           38      ***************
test_func          1           62      *************************

*** End of profile report for C:\C\PROFTEST.EXE ***

   -------   Example 2 Page 2:   tcprof -L -F proftest >proftest.ex2  -------




















                                                                 APPENDIX A - 13




                              APPENDIX B


     Registered user information

          A registered users version of this program, TCPROFRU, is
          available for $20.00 ($25.00 for 3 1/2" diskettes).  Please
          use the order form at the end of this document.

          The registered user version has additional options which
          allow you to tailor the amount of information gathered by the
          program.  On larger programs this reduces the overhead of the
          profile runs and the size of the report.


     Registered user features

          -A[-]func-nm  Alter the treatment of the named function.

                        If the profiler is being run in the default
                        mode of lines by function, each function named
                        by this option will NOT have line numbers
                        traced.  A single line, as for a functions only
                        report, is output for each named function.

                        If the functions only option is "on" (-F) then
                        the named functions will have line number
                        tracing on.

                        For either case above, if a minus sign precedes
                        the named function it will not be traced and
                        all times for the function will be included in
                        the lines or functions that call it.

                        Multiple A options may be used.  The function
                        name is case sensitive.

                          Ex:  tcprofru -F -Afn1 -A-fn2 tstprg
                        Functions only plus fn1 lines and no trace on
                        fn2.

          -M[-]mod-nm   Alter the treatment of all functions in the
                        named module.

                        Depending on the status of the F switch the
                        treatment of all functions within the named
                        module will be modified.  This is a shorthand
                        method of altering(A[]) the treatment of all
                        the functions in a module.

                        Multiple M options may be used.  The module
                        name is not case sensitive.

                          Ex:  tcprofru -Mmod1 -M-mod2 testprog
                        Profile functions only in mod1, no profile of
                        functions in mod2, all other functions are
                        profiled by line.




                                                                 APPENDIX B - 14




          -F[-][+]      Alter the treatment of all functions in the
                        program.

                        The -F- option causes all functions to be
                        skipped except those specified by A or M
                        options.  The functions included by a -A or -M
                        option are profiled by line unless the name is
                        preceded by a -, in which case a single line
                        per function is reported.  This is convenient
                        when only a few functions in a large program
                        needs to be profiled.

                        The -F+ option resets the default, profile by
                        line.  It would be used if a response file (-@
                        option) contains a -F option and you wish to
                        override it. The last -F option encountered on
                        the command line is the one in effect for all
                        functions.

                        The interaction between the -F, -M and -A
                        options result in 27 possibilities.  The table
                        below is taken from the help screen of
                        TCPROFRU.

          -F[-][+]     |     No or +     |       Yes       |      with -     |
          -M[-]module  |  N  |  Y  |  -  |  N  |  Y  |  -  |  N  |  Y  |  -  |
          -A[-]function|N Y -|N Y -|N Y -|N Y -|N Y -|N Y -|N Y -|N Y -|N Y -|
              resulting L F S F L S S L F F L S L F S S L F S L F L F S F L S
                profile: L = lines; F = function; S = skip, add time to caller

                        The second, third and fourth columns are
                        interpreted as follows:  N means that the
                        option not used for a particular module or
                        function.  Y means that the option was used for
                        a particular module or function.  The - means
                        that a particular module or function was
                        preceded by a minus.

                          Ex: tcprofru -M-module1 -Amod1fn2
                        Refering to the preceding table:  The
                        "resulting profile" line gives the effect for a
                        particular function.  the effect on functions
                        mod1fn1 and mod1fn2 in module1 is:  No -F
                        option therefore, select -F column 1; -M-
                        specified for module1 therefore, select -M
                        column 3; for mod1fn1 -A was not specified
                        therefore, select -A column 7 which results in
                        this function not appearing in the report and
                        its time being added to the caller.  On the
                        other hand, mod1fn2 is specified by a -A option
                        which selects -A column 8 and results in each
                        line of the function being profiled.









                                                                 APPENDIX B - 15




                          Ex:  tcprofru -F- -Afn1 -M-mod2 tstprg
                        The -F- option turns off profiling of all
                        functions in the program.  The -A and -M
                        options then modify this action as follows:
                        Profile by lines function fn1, one line per
                        function will be profiled for the functions in
                        module mod2, all other function times are
                        included with the caller's.


          -PnnF&|T      Only print lines whose percentage exceeds nn.

                        F = Line's percentage of function:  T = Line's
                        percentage of total. If both are specified the
                        line is printed if either percentage exceeds
                        the nn value.  If both are to be the same
                        percentage it may be specified as P20FT.

                          Ex:  tcprofru -P50F -p10t tstprg
                        Only print lines, which are 50% or more of the
                        function or are 10% or more of the total.

          -I[-]         Include C source in the report.

                        This option interleaves the C source code with
                        the report.  For each C module encountered in
                        the .MAP file a standard DOS path search is
                        made.  If the source code is found it is
                        printed with the report.  The -I- option can be
                        used to override a -I specified in a response
                        file (-@ option).

          -@file-name   Merge the named file with the command line
                        options.

                        When the @ option is encountered on the command
                        line the file is opened and each line within
                        the file is treated as one profiler command
                        line parameter.  The response file cannot be
                        used to specify the program to be profiled or
                        it's options.  The options must be in the same
                        sequence as they would appear on the command
                        line.  An @ option may not be contained within
                        the file.  Multiple @ options may be used on
                        the command line.

                          Ex: tcprofru -@op.dat -Aadd_fn tstprg














                                                                 APPENDIX B - 16




                              APPENDIX C


     PROBLEM REPORT/SUGGESTIONS

                                                     TCPROF version 1.5
          From:  Name:             ___________________________________

                 Company:          ___________________________________

                 Address:          ___________________________________

                 City, State, Zip: ___________________________________

          Received program from: _____________________________________

          Hardware:          _________________________________________

          Operating system:  ________________________  version: ______

          Resident programs: _________________________________________

                            __________________________________________

          Error message (if problem report):

             _________________________________________________________

          Description of error or suggestions:
















          If appropriate and available, printed output of the profile
          report and a listing of the program or a fragment
          illustrating the problem would be helpful.

          Mail to:
                              Mr. Andre Nancoz
                              349 Quincy Ave.
                              Bronx, NY 10465





     REGISTERED USER ORDER FORM

          Mail to:
                              Mr. Andre Nancoz
                              349 Quincy Ave.
                              Bronx, NY 10465

            ..........................................................

            Order for TC profiler registered users version (TCPROFRU):

          Name:             __________________________________________

          Company:          __________________________________________

          Address:          __________________________________________

          City, State, Zip: __________________________________________


          Received TCPROF program from:

            __________________________________________________________


          Hardware:          _________________________________________


          Operating system:  ________________________  version: ______

          Send:

             ___ copies of 5 1/4" DSDD at $20.00 each ________

             ___ copies of 3 1/2" DSDD at $25.00 each ________

                                     Total enclosed. $________
            Checks only.  U. S. funds.  NO COD.