VID_SCRN.DOC
    Jerry Joplin [70441,2627] CIS
    Version 1.0  23-Nov-1987
 
    VID_SCRN.ASM is the assembly language source to a set of very fast
video manipulation routines providing direct access to video memory
while maintaining Microsoft Windows and DESQview __good_screen_behavior__
compatibility. Also provided is VID_SCRN.LIB which contains the assembled
object module.
 
    i)   Many of the included functions directly access video memory, yet
         remain Microsoft Windows and DESQview compatible by checking
         to see if a virtual screen buffer has been established for
         the current process.  This enables programs written using
         these techniques to run under these operating environments
         in a well behaved window.
    ii)  Some functions are especially useful for an application
         running under a control program, but all the functions will
         perform identical operations when a control program is not
         present.
    iii) Snow suppression is used when non-monochrome real video memory
         is accessed.
    iv)  Absolutely no error checking is done on any of the functions
         in order to provide maximum throughput.
    v)   The functions have been designed to work with the small and
         tiny models only.  They also work fine with MSC V4.0 and 5.0
    vi)  I dont ask for any compensation for this library of routines
         but would like to see any improvements or enhancements that
         may come from them.
    vii) Included functions -
 
               vid_puts            ;Write string w/attr
               vid_readc           ;Read char/attr
 
               vid_memread         ;Video memory block read
               vid_memwrite        ;Video memory block write
 
               vid_putc            ;Write character w/attr
 
               vid_begin           ;Begin a video update
               vid_update          ;End a video update
               vid_buffc           ;Write a char/attr in an update
 
               vid_clearbox        ;Clear a window
               vid_scrollbox       ;Scroll a window
               vid_drawbox         ;Draw a box around a window
               vid_setbox          ;Set a box character set
 
               vid_setpage         ;Set the active video page
               vid_setmode         ;Set the video mode
               vid_poscurs         ;Position the cursor
 
Released into the public domain by the author. Windows is a registered
trademark of Microsoft Corporation.  DESQview is a registered trademark
of Quarterdeck.


/***********************************************************************/
 
function vid_puts
 
 
    int vid_puts(string,row,col,attr)
    char *string;
    int row;
    int col;
    int attr;
 
         Parameter descriptions
              string - pointer to a null terminated character string
              row    - row at which to display string
              col    - column at which to display string
              attr   - video attribute for the displayed string
 
         Summary
              This function displays a null terminated string to
              a row and column on the video screen with the
              specified attribute.
 
         Return values
              none
 
         Example
              /*
              Display a string at top left corner of screen
              in reverse video
              */
 
              #define REVERSE 0x0070
              vid_puts("Hello world",0,0,REVERSE);
 
 
         Notes for use under a control program
              If a control program is present the string is written
              to the process virtual screen.  A request is then sent to
              update the altered positions of the virtual screen onto
              the real screen.  Since several characters lying in a
              contigious block of video memory can be included in one
              real screen update request, this function is very fast.
 


/***********************************************************************/
 
function vid_readc
 
 
    unsigned vid_readc(row,col)
    int row;
    int col;
 
         Parameter descriptions
              row    - row from which to read a character/attribute
              col    - column from which to read a character/attribute
 
         Summary
              This function reads a character and its attribute
              from a row and column on the video screen.
 
         Return values
              Unsigned integer containing the character read from the
              screen in the low byte of the word, and the attribute
              in the high byte of the word.
 
         Example
              /*
              Read character/attr from the top left corner of screen
              */
 
              #define REVERSE 0x0070
              unsigned char_attr;
              char_attr = vid_readc(0,0);
              if ( (char_attr & 0x00ff) == 'H') {
                  ....
                  }
              if ( (char_attr >> 8) == REVERSE) {
                  ....
                  }
 
         Notes for use under a control program
              If a control program is present the char/attr is read
              straight from the process virtual screen.
 


/***********************************************************************/
 
function vid_memread
 
 
    int vid_memread(buffer,row,col,count)
    void *buffer;
    int row;
    int col;
    int count;
 
         Parameter descriptions
              buffer - near pointer to a buffer of size (count * 2)
                       where the block will be stored
              row    - row at which to start the video block read
              col    - column at which to start the video block read
              count  - number of CHARACTER positions to read
 
         Summary
              This function reads a block of memory from the video
              screen.  Each word of memory will contain both the
              attribute and the character values for (count) positions
              in the memory block.
 
         Return values
              none
 
         Example
              /*
              Save 20 characters and attributes from the top left
              corner of the screen
              */
 
              void *buffer;
 
              void = malloc( 20 * 2);
              vid_memread(buffer,0,0,20);
 
         Notes for use under a control program
              If a control program is present the block is read
              straight from the process virtual screen.
 


/***********************************************************************/
 
function vid_memwrite
 
 
    int vid_memwrite(buffer,row,col,count)
    void *buffer;
    int row;
    int col;
    int count;
 
         Parameter descriptions
              buffer - near pointer to a buffer of size (count * 2)
                       which will be transfered to video memory
              row    - row at which to start the video block write
              col    - column at which to start the video block write
              count  - number of CHARACTER positions to write
 
         Summary
              This function writes a block of video memory from a saved
              buffer.  Each word of memory should contain both the
              attribute and the character values for (count) positions
              in the memory block.  The buffer is generally created
              using a call to vid_memread.
 
         Return values
              none
 
         Example
              /*
              Save 20 characters and attributes from the top left
              corner of the screen then write the same block of
              memory to row 1 column 5 of the screen
              */
 
              void *buffer;
 
              void = malloc( 20 * 2);
              vid_memread(buffer,0,0,20);
              vid_memwrite(buffer,1,5,20);
 
 
         Notes for use under a control program
              If a control program is present the block is written
              to the process virtual screen.  A request is then
              sent to update the altered positions of the virtual
              screen onto the real screen.  All positions written to
              the screen will lie in a contigious block of video memory
              making this function very fast.
 


/***********************************************************************/
 
function vid_putc
 
 
    int vid_putc(chr,row,col,attr)
    char chr;
    int row;
    int col;
    int attr;
 
         Parameter descriptions
              chr    - character to display
              row    - row at which to display chr
              col    - column at which to display chr
              attr   - video attribute for the displayed chr
 
         Summary
              This function displays a character to a row and
              column on the video screen with the specified attribute.
 
         Return values
              none
 
         Example
              /*
              Display a 'H' to the top left corner of screen
              in reverse video
              */
 
              #define REVERSE 0x0070
              vid_putc('H',0,0,REVERSE);
 
 
         Notes for use under a control program
              If a control program is present the character is written
              to the process virtual screen.  A request is then sent to
              update the altered position of the virtual screen onto
              the real screen.  There is a small amount of overhead
              for updating the character onto the real screen. Thus
              this function probably shouldn't be used if more chars
              are going to be displayed that will lie in a contigious
              block of video memory OR if they are clustered together
              in a small block of contigious video memory.
 


/***********************************************************************/
 
function vid_begin
 
 
    int vid_begin()
 
         Parameter descriptions
              none
 
         Summary
              This function is used to mark the begining of
              a video update.  It is especially useful under
              environments running Microsoft Windows or DESQview
              and has no effect if neither is detected.
 
         Return values
              none
 
         Example
              /*
              See vid_update
              */
 
 
         Notes for use under a control program
              This is especially designed for environments running
              Microsoft Windows or DESQview. It can be used in
              conjuction with vid_buffc, and vid_update to obtain
              high performance displays under these control programs.
              See example under vid_update.


/***********************************************************************/
 
function vid_buffc
 
 
    int vid_buffc(chr,row,col,attr)
    char chr;
    int row;
    int col;
    int attr;
 
         Parameter descriptions
              chr    - character to write to video buffer
              row    - row at which to place  chr
              col    - column at which to place chr
              attr   - video attribute for the buffered chr
 
         Summary
              This function places a character with attribute to
              a row and column on the video buffer. It is especially
              useful under environments running Microsoft Windows or
              DESQview.  Otherwise the function is functionally
              equivalent to to vid_putc since the location of the
              video buffer is the real video screen.
 
         Return values
              none
 
         Example
              /*
              See vid_update
              */
 
         Notes for use under a control program
              This is especially designed for environments running
              Microsoft Windows or DESQview. It can be used in
              conjuction with vid_begin, and vid_update to obtain
              high performance displays under these control programs.
              See example under vid_update.
 


/***********************************************************************/
 
function vid_update
 
 
    int vid_update()
 
         Parameter descriptions
              none
 
         Summary
              This function is used to mark the end of a video
              update and to transfer all the changed positions of
              the process video buffer to the real video screen.
              It is especially useful under environments running
              Microsoft Windows or DESQview and has no effect if
              neither is detected.
 
         Return values
              none
 
         Example
              /*
              Case 1 : vid_begin, vid_buffc, and vid_update are
              used to build a portion of the video screen that is
              a closely contigious portion of video memory.  This is
              comparared to a slower usage of vid_putc to achieve
              the same output.
              */
 
              /* display message at the top left corner of screen   */
              #define REVERSE 0x0070
              vid_puts("Hello world",0,0,REVERSE);
 
              vid_begin();                   /* Mark start of update */
              vid_buffc('J',0,0,REVERSE);    /* Change               */
              vid_buffc('B',0,6,REVERSE);    /*        "Hello world" */
              vid_buffc('w',0,8,REVERSE);    /* to                   */
              vid_buffc(' ',0,10,REVERSE);   /*        "Jello Bowl " */
              vid_update();                  /* Move Jello Bowl to   */
                                             /* the real video screen*/
                                             /* The control program, */
                                             /* if present, will move*/
                                             /* 10 characters on the */
                                             /* call to vid_update.  */
 
 
              /* redisplay original message at the top left corner   */
              #define REVERSE 0x0070
              vid_puts("Hello world",0,0,REVERSE);
 
              vid_putc('J',0,0,REVERSE);    /* Change               */
              vid_putc('B',0,6,REVERSE);    /*        "Hello world" */
              vid_putc('w',0,8,REVERSE);    /* to                   */
              vid_putc(' ',0,10,REVERSE);   /*         "Jello Bowl "*/
                                            /* This is slower than  */
                                            /* above use since each */
                                            /* character is updated */
                                            /* to the real screen as*/
                                            /* it is written.       */
 
 
              /*
              Case 2 : vid_begin, vid_buffc, and vid_update are
              used to build a portion of the video screen that is
              not in a closely contigious portion of video memory.
              This is comparared to a faster usage of vid_putc to
              achieve the same output.
              */
 
              /* define normal attribute */
              #define NORM      7
              /* define the characters of the corners of a box */
              #define UPLEFT    218
              #define UPRIGHT   191
              #define LOWLEFT   217
              #define LOWRIGHT  192
 
              /* display the corners of a box characters */
 
              vid_begin();                   /* Mark start of update */
              vid_buffc(UPLEFT,0,0,NORM);    /* Buffer upper left,   */
              vid_buffc(UPRIGHT,0,19,NORM);  /*  upper right,        */
              vid_buffc(LOWLEFT,19,0,NORM);  /*  lower left          */
              vid_buffc(LOWRIGHT,19,19,NORM);/*  and lower right.    */
              vid_update();                  /* Move the chracters to*/
                                             /* the real video screen*/
                                             /* The control program, */
                                             /* if present, will move*/
                                             /* (20 * 20) = 400 words*/
                                             /* at call to vid_update*/
                                             /* This causes noticable*/
                                             /* flicker under Windows*/
 
 
              /* redisplay the corners of a box using vid_putc */
              vid_buffc(UPLEFT,0,0,NORM);    /* Display upper left,  */
              vid_buffc(UPRIGHT,0,19,NORM);  /*  upper right,        */
              vid_buffc(LOWLEFT,19,0,NORM);  /*  lower left          */
              vid_buffc(LOWRIGHT,19,19,NORM);/*  and lower right.    */
                                             /* Here the screen is   */
                                             /* updated 4 times but  */
                                             /* the control program, */
                                             /* if present, will only*/
                                             /* move 4 words to the  */
                                             /* real screen.         */
 
 
         Notes for use under a control program
              This is especially designed for environments running
              Microsoft Windows or DESQview. It can be used in
              conjuction with vid_begin, and vid_buffc to obtain
              high performance displays under these control programs.
 


/***********************************************************************/
 
function vid_clearbox
 
 
    int vid_clearbox(toprow,leftcol,lowrow,rightcol,attr)
    int toprow;
    int leftcol;
    int lowrow;
    int rightcol;
    int attr;
 
         Parameter descriptions
              toprow   - top row of the window to be cleared
              leftcol  - left column of the window to be cleared
              lowrow   - bottom row of the window to be cleared
              rightcol - right column of the window to be cleared
              attr     - video attribute of the cleared area
 
         Summary
              This function clears a window of the video screen
              and sets it to a specified video attribute.
 
         Return values
              none
 
         Example
              /*
              Clear the entire 80 X 25 screen and set it to
              a normal video attribute
              */
 
              #define NORM 7
              vid_clearbox(0,0,24,79,NORM);
 
 
         Notes for use under a control program
              No special action is taken if a control program is
              present since this calls on the BIOS scroll box
              video function to clear the area of the screen and
              both Windows and DESQview do an excellant job of
              intercepting this call and performing it quickly.
 
 


/***********************************************************************/
 
function vid_scrollbox
 
 
    int vid_scrollbox(toprow,leftcol,lowrow,rightcol,attr,direct,lines)
    int toprow;
    int leftcol;
    int lowrow;
    int rightcol;
    int attr;
    int direct;
    int lines;
 
         Parameter descriptions
              toprow   - top row of the window to be scrolled
              leftcol  - left column of the window to be scrolled
              lowrow   - bottom row of the window to be scrolled
              rightcol - right column of the window to be scrolled
              attr     - video attribute for new lines
              direct   - direction of the scroll
                            0 = scroll up
                            1 = scroll down
              lines    - number of lines to scroll
 
 
         Summary
              This function scrolls a window of the video screen
              a certain number of lines in a specified direction,
              setting the new lines from the scroll to an attribute.
              If the number of lines is given as 0 then this becomes
              a functional equivalent to vid_clearbox.
 
         Return values
              none
 
         Example
              /*
              Scroll a box down by 3 lines setting the new lines
              in the top of the window to normal video attributes
              */
 
              #define NORM     7
              #define TOP      0
              #define LEFT     0
              #define BOTTOM   19
              #define RIGHT    50
              vid_clearbox(TOP,LEFT,BOTTOM,RIGHT,NORM,1,3);
 
 
         Notes for use under a control program
              No special action is taken if a control program is
              present since this calls on the BIOS scroll box
              video function to scroll the area of the screen and
              both Windows and DESQview do an excellant job of
              intercepting this call and performing it quickly.
 
 
 


/***********************************************************************/
 
function vid_drawbox
 
 
    int vid_drawbox(toprow,leftcol,lowrow,rightcol,attr,boxset)
    int toprow;
    int leftcol;
    int lowrow;
    int rightcol;
    int attr;
    int boxset;
 
         Parameter descriptions
              toprow   - top row of the box
              leftcol  - left column of the box
              lowrow   - bottom row of the box
              rightcol - right column of the box
              attr     - video attribute for characters of the box
              boxset   - character set to use for the box
                         use vid_setbox to establish a character set
                         default boxsets are set as
                            1 = single line box
                            2 = double line box
                         up to 8 box sets can be created ( 0 thru 7 )
 
         Summary
              This function draws a border around a specified window
              of the video screen.  The characters to use for the
              border are specified as a box set number from 0 to 7.
              These characters can be set using vid_setbox.
 
         Return values
              none
 
         Example
              /*
              Draw a double line box around a window setting the box
              characters to reverse video
              */
 
              #define REVERSE  0x70
              #define TOP      0
              #define LEFT     0
              #define BOTTOM   19
              #define RIGHT    50
              vid_drawbox(TOP,LEFT,BOTTOM,RIGHT,REVERSE,2);
 
 
         Notes for use under a control program
              This function calls upon vs_begin, vs_buffc, and
              vs_update to draw the top and bottom lines of the
              box.  The right and left edges of the box are drawn
              using vs_putc.
 


/***********************************************************************/
 
function vid_setbox
 
 
    int vid_setbox(set,topleft,top,topright,right,lowright,low,lowleft,left)
    int set;
    int topleft;
    int top;
    int topright;
    int right;
    int lowright;
    int low;
    int lowleft;
    int left;
 
         Parameter descriptions
              set      - number of the boxset to establish
                         must be a value from 0 to 7 .
                         two default boxsets are initialized :
                            1 = single line box
                            2 = double line box
              topleft  - the character for the top left corner
              top      - the character for the top side
              topright - the character for the top right corner
              right    - the character for the right side
              lowright - the character for the bottom right corner
              low      - the character for the bottom side
              lowleft  - the character for the bottom left corner
              left     - the character for the left side
 
         Summary
              This function establishes a character set to use for
              drawing a border around a specified window of the video
              screen using vid_drawbox.
 
         Return values
              none
 
         Example
              /*
              Establish box set 0  with the top and bottom lines
              as double line characters and the sides of the box as
              single line characters. Then draw the box around a window
              in reverse video.
              */
 
              #define REVERSE  0x70
              #define NORMAL   0x07
              #define TOP      0
              #define LEFT     0
              #define BOTTOM   19
              #define RIGHT    59
              vid_setbox(0,213,205,184,179,190,205,212,179);
              vid_clearbox(TOP,LEFT,BOTTOM,RIGHT,NORMAL);
              vid_drawbox(TOP,LEFT,BOTTOM,RIGHT,REVERSE,0);
 
 
         Notes for use under a control program
              This function doesn't actually perform any video
              screen IO.
 


/***********************************************************************/
 
function vid_poscurs
 
 
    int vid_poscurs(row,col)
    int row;
    int col;
 
         Parameter descriptions
              row    - row to position cursor
              col    - column to position cursor
 
         Summary
              This function sets the cursor to row and
              column on the video screen.
 
         Return values
              none
 
         Example
              /*
              Hide the cursor by positioning it to row 25 column 0
              */
 
              vid_poscurs(25,0);
 
 
         Notes for use under a control program
              No special action is taken if a control program is
              present since this calls on the BIOS set cursor position
              video function, which both Windows and DESQview
              intercept nicely.
 


/***********************************************************************/
 
function vid_setpage
 
 
    int vid_setpage(vidpage)
    int vidpage;
 
         Parameter descriptions
              vidpage - video page
 
         Summary
              This function sets the current video page.  The only
              supported page in this library is page 0.  The function
              is only provided to make sure the video page has been
              initialized to zero.
 
         Return values
              none
 
         Example
              /*
              Initialize the video page to 0
              */
 
              vid_setpage(0);
 
 
         Notes for use under a control program
              No special action is taken if a control program is
              present since this calls on the BIOS set video page
              video function, which both Windows and DESQview
              intercept nicely.
 
 


/***********************************************************************/
 
function vid_setmode
 
 
    int vid_setmode(vidmode)
    int vidmode;
 
         Parameter descriptions
              vidmode - video mode
 
         Summary
              This function establishes the current video mode.
              The following modes are supported in this library
                   2       80  X 25   blank and white text
                   3       80  X 25   color text
                   7       80  X 25   monochrome text
 
         Return values
              none
 
         Example
              /*
              Set the video mode to 80 X 25 color text
              */
 
              vid_setmode(3);
 
 
         Notes for use under a control program
              No special action is taken if a control program is
              present since this calls on the BIOS set video mode
              video function, which both Windows and DESQview
              intercept nicely.
 
/***********************************************************************/