December 14, 1985

                          TURBODBG.DOC

OVERVIEW

TURBODBG is a source code debugger for use in debugging Turbo 
Pascal (tm) Programs on the IBM-PC (tm).  When used in 
conjunction with TURBO.COM, it allows you to:

     1.  View your source code while debugging.
     2.  Trace the operation of your program statement by 
         statement.
     3.  Insert breakpoints in your program by procedure/function 
         name or by statement number.
     4.  Examine (and change) global variables in your program, 
         including strings, array variables, and records.


SYSTEM REQUIREMENTS

     1.  Turbo Pascal IBM-PC Version 3.00B or 3.01A.
     2.  Approximately 64k or so more memory than would normally 
         be required to run your program in the Turbo memory 
         mode.


OPERATION

To use TURBODBG, include the file DBG??.COM (the ?? is a two 
digit revision number) on the disk (or in the directory) with 
TURBO.COM, TURBO.MSG, and your program file.  At the DOS prompt, 
call for DBG??.  After a brief sign on message, TURBODBG will 
load TURBO.COM and transfer control to it.  (The message 
'Incorrect TURBO.COM version!' indicates that TURBODBG and your 
version of TURBO.COM are incompatible.)

At this point, all of the commands and features of Turbo Pascal 
should operate as they always have with the exception of the Run 
command.  The only special requirement for programs to be 
debugged is that the {$U+} compiler directive not be used.  When 
the Run command is executed, TURBODBG will regain control and the 
debugging screen will appear.

The debugging screen is divided into two parts.  The lower 
section is the command and data section.  The '*' is a prompt for 
one of the commands described later.  The top part of the screen 
displays the program source code text which at this point will be 
centered at the first executable statement of your program.

Within the text part of the display, the current statement (the 
next one to be executed) will be highlighted.  The left margin 


                           1











contains the statement number of the first statement occurring on 
that particular line.  Statement numbers are consecutive numbers 
and are used to refer to individual statements in the commands 
described later.  Since there may be more than one statement on a 
line, the statement number in the margin is that of the first 
statement on the line.  The first character of each statement is 
highlighted.  Note also that there may be no statements on a 
given line so those lines will have no numbers.

Dividing the two portions of the debugging screen is a line which 
at this point will probably display 'Memory'.  This indicates 
that the text file being observed is in memory.  Later, when 
viewing a portion of the program source code which is in an 
'include' file, the name of the 'include' file will appear here.


SPECIAL KEYS FOR VIEWING TEXT

The following keys may be used to change the text being 
displayed:

     Pg Up
     Pg Dn  Move the display up or down one page.

     ^Pg Up
     ^Pg Dn Move to the start or end of the current file.

     Up arrow
     Down arrow  Scroll up or down one line.

     F10 key  Toggle between the debug screen and the screen
              of the program under test.

In addition, the text being displayed may be changed using the 
View command described later.


COMMAND EDITOR

When entering commands, the following keys may used to edit the 
command:  (They perform the same functions as they do in the 
Turbo Pascal editor.)

     ^A,^S,^D,^F,^G,^T,^H,LFARW,RTARW,^LFARW,^RTARW,
     Ins, Del, Backspace

The Insert mode (default) is indicated by a slightly fatter 
cursor while the cursor is normal in the Overwrite mode.

In addition, the F3 function key causes the last command entered 
(having more than three characters) to be redisplayed.  This may 



                           2











be used to make minor changes to a previous command or to correct 
a syntax error.

Note that commands are not acted upon until the Enter key is hit.  
(The cursor does not have to be at the line end to enter the 
command.)


COMMAND PARAMETERS

Commands consist of one or two letters (only one letter commands 
presently exist) which may be followed by one or more parameters.  
A non alphabetic character must follow the command to delimit it 
from a following parameter.  The parameters which may be used 
are:

  <Symbol>
     A Pascal source code symbol representing a 
     procedure/function name, variable, or constant as 
     appropriate.  The special symbol 'RTN' may be used to refer 
     to the return point of a procedure/function.

  <Statement>
     A statement number as displayed in the left margin of the 
     text display.


COMMANDS

G    (Go)

  Format:
     G [<parameter> [<parameter..]]

  The Go command starts execution of the program under test.  
  Execution will continue until a breakpoint is reached, the 
  program terminates, or the <control Break> key is hit.

  One or more breakpoints may be entered with the Go command.  
  These breakpoints are called temporary breakpoints as they are 
  in effect only until the first stopping point is reached.  Any 
  temporary breakpoint would then have to reentered with the next 
  Go command if desired.

  The program under test may be interrupted using the <control 
  Break> key.  Note that <control C> does not perform the same 
  function but rather performs its normal Turbo Pascal function 
  (as defined by the {$C } compiler directive.






                           3











  Examples:

     G   Start execution with no temporary breakpoints. (There 
         might be some permanent breakpoints, however.)

     G 345 PROC1 RTN
         Start execution with temporary breakpoints at statement 
         345, at the start of procedure PROC1, and at the return 
         point of the current procedure/function.  In addition, 
         there might be other permanent breakpoints in effect.

T    (Trace)

  Format:
     T

  Execute the current statement.  Only one statement is executed.


N    (Next)

  Format:
     N

  Execute the current statement in its entirety.

  The difference between the Trace and the Next command is that 
  if the current statement is a procedure or function call, Next 
  will completely execute the procedure/function whereas Trace 
  will Trace through the procedure/function.


P    (Permanent breakpoint)

  Format:
     [-]P [<parameter>]

  The P command is used to specify permanent breakpoints.  Unlike 
  temporary breakpoints, permanent breakpoints remain in effect 
  until removed (using a '-' preceding the P command).  

  If no parameter is entered, the breakpoints in effect are 
  listed.

  Examples:

     P        List all permanent breakpoints.
    -P        Delete all permanent breakpoints.
     P 345    Install a breakpoints at statement 345.
    -P PROC1  Remove a breakpoint at procedure PROC1.




                           4











V    (View text)

  Format:
     V [<parameter>]

  The View command may be used to change the text being observed 
  in the text window.  If no parameter is entered, the text will 
  be centered around the current statement (the one to be 
  executed next).

  Examples:

     V InitScreens   View text at procedure InitScreens.
     V 545           View text around statement 545.
     V Rtn           Find out where this procedure/function was
                     called from.


E    (Examine/change variable or constant)

  Format:
     E <symbol>

  The Examine/change command allows the the value of global 
  variables and constants to be displayed.  In addition, for 
  variables, a new value may be entered.  Note that Turbo Pascal 
  'typed constants' are actually initialized variables and these 
  may also be changed.  

  After a variable value has been output in response to the 
  Examine/change command, a new value may be entered followed by 
  the Enter key.  For byte and integer types, a hex value may be 
  specified by preceding it with a '$'.  Hitting the Enter key 
  only retains the old variable value.  

  8 bit variables (byte, char, boolean) are displayed in decimal, 
  hex, and character (if printable).  In the case of boolean, 0 
  is false, and 1 is true.

  Integer variables are displayed as both decimal and hex.

  Real variables are displayed in 'E' format and also decimal 
  format if within a reasonable range.

  Pointer variables are displayed with the phrase 'Points to:' 
  followed by an address and symbolic name if appropriate.  If 
  the pointer variable is followed by '^', the contents of the 
  pointed to variable are displayed.

  String variables are displayed as a string within quotes.  When 
  specifying a change to a string variable, enclose the new 
  string in quotes.  A null string is specified by two quotes 


                           5











  enclosing nothing.  Individual characters of a string may be 
  displayed and changed by treating the string as an array.

  Non numerical scaler variables are displayed numerically.  For 
  instance, a variable defined as

    Var   Color   :(red,green,blue,orange);

  would be be given a value of 2 if it contained blue.  However, 
  note that:

     E BLUE

  could be used to verify that blue was represented by 2.

  Sets cannot be examined.

  Examples:

     E RealArray[4,3]
     E InString
     E PersonRecord[12].ID.Lastname
     E PT^.Index1
     E START^.NEXT^.NEXT^.NEXT^.VALUE[10][3]


Q    (Quit)

  Format:
     Q

  The Quit command when entered in TURBODBG returns control to 
  Turbo Pascal without running the program under test to 
  completion.


HINTS

It is possible to insert breakpoints in the source code using 
INLINE($CC).  These breakpoints cannot be removed by TURBODBG 
but may be useful for conditional breaks.  For instance:

  IF I=49 THEN INLINE($CC);

To get around the fact that local variables are not visible, the 
CONST's and VAR's may be moved temporarily to a global area.  
Turbo Pascal allows them to be moved just above the 
procedure/function definition.  Of course this only works if the 
procedure/function is not used recursively and if there is no 
symbol name conflict.




                           6











RESTRICTIONS, PROBLEMS, BUGS

The following are current limits.  These may be easily changed by 
changing a constant and recompiling.

  Permanent and temporary breakpoints are limited to 3 each.
  Maximum number of include files = 6.
  Maximum include file size = 32k.
  Maximum number of statements = 2000.
  Maximum allowable symbol table size = 5k.
  Maximum symbol length = 28.

When changing a string using Examine/change, there currently is 
no protection against entering one that is too long.  Use care.

Only global procedure/functions, variables, and constants are 
known to TURBODBG currently.  Procedure/function dummy variables 
and function values may be added in the future.  It may not be 
practical to make local variables and procedure/function symbols 
accessible.

Presently symbolic constants cannot be used as subscripts in the 
Examine/change command.  For instance, if

 Var   Opcode  :ARRAY[MOV..CMP] OF BYTE;

it is presently necessary to specify OPCODE[0] rather than 
OPCODE[MOV] when using the Examine/change command.

The <control Break> program interrupt does not perform properly 
when the program under test is waiting for keyboard input.

A simple screen switch is currently used.  This limits debugging 
to text only programs.

There is a problem when compiling to a disk COM file.  Turbo 
often takes a short cut and transfers directly from memory to 
disk without recompiling.  However, the memory file has been 
altered by TURBODBG and the resulting COM file is corrupted.  It 
is best at this stage to compile to disk only without the 
debugger.

At this stage, TURBODBG is experimental.  Please report any 
problems, comments, suggestions, and especially if it doesn't 
work with your IBM-PC version 3.00B or 3.01A TURBO.COM to me at 
Compuserve ID 76327,53.
                                             
                                        Dave Baldwin

     IBM-PC is a trademark of International Business Machines 
     Corporation.
     Turbo Pascal is a trademark of Borland International Inc.


                           7




utrademark of Borland International Inc.


                           7